CLECs who require Access facilities out of Tariff/Guidebook that carry trunks out of ICA: CLECs who purchase “Access” T1 circuits from AT&T out of “Tariff/Guidebook’ for underlining facilities that support their CLEC Interconnection network (trunk groups): Meet-Point [MD] trunk groups [Interlata/IXC traffic] Ancillary trunk groups [911, Choke/Mass Calling, OS/DA traffic]

NOTE: The ‘CLEC Start-Up Steps for Access Services out of Tariff/Guidebook’ must be ‘Complete’ prior to submitting the Standalone T1 Access ASR to the appropriate Service.

NOTE: For 911 services-- These guidelines are for only T1 facilities that will support 911 trunks (DS0s) at an AT&T 911 Selective Router/SECLOC (i.e., HLWDCA01CT9, FTWOTXED1ED, ROCHMIMNDS0). They are NOT for Meet Point Billed (MPB) T1s that may be used for 911 services at a non-AT&T switch/central office (i.e., BRSWCAXH1ED). Those Multi-EC ASRs should be treated BAU (business as usual) for MPB T1 facility out of Access Tariff/Guidebook between AT&T and another ILEC, due to the MPB T1 facility is not for 911 services at an AT&T Selective Router/SECLOC (i.e., Facility ACTL in AT&T territory and SECLOC in ILEC territory.)

| Key ASR Fields | Value/Comments |
| --- | --- |
| CC | Blank |
| Proj | If associated with a NIS/Forecast, indicate the Project ID assigned by NIT Lead/Project Mgr., as designated on the Project Notifier [PN] Blank if not associated with a PN via the NIS/Forecast process |
| REQTYP | SD |
| PIU | 100 |
| LTP [applicable to Switch Access only, not applicable to Special Access] | Applicable LTP value: End Office = HA (riding T3 CFA), GF (No T3 CFA) Tandem = JA (riding T3 CFA), KF (No T3 CFA) |
| SPEC | T1s that carry 911 Trunks only: E911FAC |
| REMARKS | The Remarks for the Access T1 ASR should indicate the following: Type of Trunk Group the T1 facility will support (Meet-Point [MD], Choke/Mass Calling, 911, OS/DA) Example: T1 for CLEC Meet-Point (MD) TG T1 for CLEC Choke/Mass Calling TG Specific for 911: Example: T1 for CLEC 911 TG at BLISILBIDS0 T1 for CLEC 911 TG at KSCYKCJO1ED T1 for CLEC 911 TG at HLWDCA01CT9 NOTE: If CLEC is not requesting diverse T1 facilities for 911, please note in Remarks: ‘Electing not to request diversity from AT&T’. |
| NC | Refer to the Carrier Coding Guides for the applicable NC value: NOTE: 3rd character of NC = “E” (B8ZS/T1ZF) 3rd character of NC = “-“ (SF/AMI) WEST Region [CA/NV] for CLEC 911 T1s only: HCEM (B8ZS-CO Mux DS1 to Analog Voice) HC-M (SF/AMI-CO Mux DS1 to Analog Voice) [T1s in West Region connect to a 911 Hub/Mux location refer to additional info below under SECLOC] |
| NCI | Refer to the Carrier Coding Guides for the applicable NCI value: NOTE: NCI of the higher-level facility the T1 will ride |
| SECLOC | Applicable 11-character AT&T Tandem/Switch CLLI T1s for CLEC 911 Trunk Groups only: Southwest [MO, OK, KS, AR] & Midwest [IL, IN, MI, OH, WI] Regions: T1s are typically a connection directly to the 911 Selective Router switch SECLOC = 11-character 911 Selective Router switch CLLI NOTE: AT&T will design to the Master Location of the 911 Selective Router switch, will be provided on FOC [Firm Order Confirmation] West [CA, NV] Region: T1s are a connection to the 911 Hub/Mux location, refer to the Selective Router Table document (columns ‘J’ and ‘K’) posted to CLEC online for the 911 Hub/Mux (11 or 8 character CLLI) used in the SECLOC Field, examples: SECLOC = BKFDCA12K02 SECLOC = AUBNCA01 |

Once FOC is received and RID has passed on the ‘Access T1’ ASR, the ‘Trunk-only’ ASR can be submitted.

*Note: This document is intended to be a guide only. For a complete list of requirements, refer to the Access Service Ordering Guidelines (ASOG) and Carrier Coding Guide (CCG).