AT&T 12-State Data Validation File

User Guide

Version: 3.9

Issue Date: December 1, 2014

Table of Contents

Revision History for Data Validation Files	3

Chapter 1	6

Overview of Data Validation Files	6

Chapter 2	7

Access to the Files:	7

Chapter 3	8

Description of Files	8

Chapter 4	11

File Layout Records	11

AT&T Midwest Region	11

FILE NAME ---SAG File	12

FILE NAME ---Feature Availability File	15

FILE NAME --- Directory Names	18

FILE NAME ---Class of Service	19

FILE NAME --- USOC/FIDS	22

FILE NAME ---Community Name File	27

FILE NAME ---PIC/LPIC	29

AT&T West Region	32

FILE NAME ---SAG File	33

FILE NAME ---Feature Availability File	35

FILE NAME --- Directory Names	45

FILE NAME ---Class of Service	46

FILE NAME --- USOC/FIDS	50

FILE NAME ---Community Name File	53

FILE NAME --- Yellow Page Headings	54

FILE NAME ---PIC/LPIC	55

FILE NAME ---   North Alternate Community Name File	56

FILE NAME ---  South Alternate Community Name File	57

AT&T Southwest Region	58

FILE NAME ---SAG File	59

FILE NAME ---Feature Availability File	61

FILE NAME --- Directory Names	63

FILE NAME ---Class of Service	64

FILE NAME ---USOC/FIDS	68

FILE NAME ---Community Name File	71

FILE NAME --- Yellow Page Headings	72

# Revision History for Data Validation Files

| Revision # | Change | Date |
| --- | --- | --- |
| 1.0 | New Document | 3/01/02 |
| 1.1 | Update to AIT Yellow Page Heading Layout Records | 3/21/02 |
| 1.2 | Update to AIT PIC/LPIC Layout Record to support Type of Service | 5/29/02 |
| 1.3 | Update to add CONNECTICUT file layout records | 7/7/02 |
| 1.4 | Update to add CONNECTICUT feature availability file | 8/13/02 |
| 1.5 | Update to add the CONNECTICUT SAG file layout record. Also to add Alternate Community PB/NB only file record layout | 9/24/02 |
| 1.6 | Update to correct and add new fields and characteristics to the USOC and CLS file for all regions | 10/25/02 |
| 1.7 | Update to correct the field length for the LSR field and add max character length for the comma fields USOC and CLS file for all regions Update to show the breakdown of the SWBT Feature files by state and what the file name equates to. | 11/20/02 |
| 1.8 | Updated to change the TOS field for the CLS and USOC files from 2 to 4. Also to show the new Type of service that is applicable for LSOG 6. The PB.NB Alternate community files were added to the CD and were sent out as 2 separate files North and South. Update is to show both files. | 6/14/03. |
| 1.9 | Update to change the USOC/FID files for all regions to add a COS field. Also to show the Alternate Community in the West as North and South. To change the Branding to the new SBC branding | 8/20/03 |
| 2.0 | Update to add the ACNADES (Carrier Name) field to the PIC / LPIC Data Validation file for all regions. Add header information to the Midwest Feature File to indicate State Wide and Switch Specific features, | 10/30/03 |
| 2.1 | Update to change the Branding for CONNECTICUT from SBC CONNECTICUT to SBC Connecticut | 03/13/04 |
| 2.2 | Update to correct the file layout for the Midwest Feature file | 04/05/04 |
| 2.3 | Update to change the PIC/LPIC file layout for the East and the West adding new field, Carrier Authorization. Also to change the Midwest PIC/LPIC file from one file to one for each state. Updates will be effective with the July file updates—available in August | 6/11/04 |
| 2.4 | Update to the West (California and Nevada) region Feature Availability file to add 4 features and to add a note. Page 43 | 11/02/04 |
| 2.5 | Update to better define the definitions for the Community Name and the Directory Name file for all regions. Changes made to Chapter 3 | 12/14/04 |
| 2.6 | Update to SBC Midwest Directory Name file to change the layout | 01/27/05 |
| 2.7 | Update to the East Directory Name, the East Community Name and the West PIC / LPIC file | 03/02/05 |
| 2.8 | Update to the East, West, and Southwest Feature Availability file. Update to the West PIC / LPIC file | 9/22/05 |
| 2.9 | Update to the West Feature Availability File. Feature 126 line 269. | 3/17/06 |
| 3.0 | Update entire user guide to reflect the branding changes to AT&T. Added Table of Contents | 5/30/06 |
| 3.1 | Updated the Midwest Directory Name file to reflect the new file layout which will be effective with the 1/25/07 updates | 12/11/06 |
| 3.2 | Updated the East Directory Name file to reflect the new file layout which will be effective with the 3/29/07 updates Changed AT&T CONNECTICUT to AT&T Connecticut. | 01/25/07 |
| 3.3 | Updates to the Midwest, Southwest and West Community Name files. Effective with the April 26, 2007 updates | 3/23/07 |
| 3.4 | Updates to the West Feature Availability and Yellow Page Heading file. Changes effective with the June 28, 2007 updates. | 5/17/07 |
| 3.5 | Updates to the East and Southwest PIC / LPIC files and to the Midwest Yellow Page Heading Files. Changes effective with the November 29, 2007 updates. Adding double quotes and changing the file layouts. | October 1, 2007 |
| 3.6 | Chapter 4 – File Layout Records AT&T West Region – Directory Names – Changes to the File format | September 1, 2009 |
| 3.7 | Chapter 4 – File Layout Records Yellow Pages Headings (AT&T West Region) Page 56 Record Section Structure 4 Code – Changed Data_Type to AN (ALPHA/NUMERICS) Changed cover sheet to reflect Version 3.7 and Issue Date | June 17th, 2011 |
| 3.8 | Cover Sheet updated to Version 3.8 and new Issue Date Page 82/83 SAG File – AT&T Southwest Region – Added new note at end of record layout to provide link to SAGA Information Guide | March 17th, 2012 |
| 3.9 | Added Telecordia disclaimer to Chapter 1 As part of SNET Transfer to Frontier Communications, removed all references to AT&T East Region, Connecticut, etc. This included all AT&T East Region file information. Chapter 2, removed all references to CONNECT: DIRECT and CD-ROM. | December 1st, 2014 |

# Chapter 1

## Overview of Data Validation Files

This user guide will help you learn what you need to know about obtaining Data Validation Files.

Data Validation files are files containing information that can be used to populate a database, or in place of performing pre-order transactions.  The record layout structure of each file will be consistent throughout all AT&T 12-State Regions.  Variances in population of the data in such files will depend on the availability of that data in source back-end systems. The file layout records for these documents are contained in Chapter 4.

The following data validation files will be available throughout all AT&T 12-State Region:

- SAG – Street Address Guide

- Feature Availability/Service Availability by Switch

- Directory Names

- Class of Service Codes

- USOC (Universal Service Order Code)

- Community Names

- Yellow Page Headings

- PIC/LPIC (InterLATA/IntraLATA)

- Alternate Community Name, North and South,  AT&T West Region Only

The Data Validation files will be updated on a monthly basis.

Note:

Telcordia® and Common Language® are registered trademarks and iconectiv, CLCI, CLEI, CLFI, CLLI, USOC, FID, NC, NCI and NC/NCI, are trademarks of Telcordia Technologies, Inc. The Common Language codes identified herein are the proprietary information of Telcordia Technologies, Inc. dba as iconectiv ("iconectiv") and are licensed to AT&T Services Inc. The Common Language codes are provided herein solely for the purpose of this document  and may not be reproduced, stored, or used for any other purpose without the express, written consent of iconectiv.

# Chapter 2

## Access to the Files:

Data Validation files will be available through the following mediums:

- Pre-Ordering Graphical User Interface (GUI)  - Verigate

- CLEC Online

The data validation files can be obtained by downloading via the pre-order GUI (Verigate) or the file layout records through CLEC on-line.

CLEC On-line requires access to the CLEC Web Site via the Internet. The Data Validation files can be accessed via the CLEC Online Website at https://clec.att.com/ . Click on CLEC Handbook, then select a region from the drop-down box at the top of the page. From the Handbook main menu, select Ordering and then Data Validation Files.

Pre-ordering Graphical User Interface (Verigate) requires access to the AT&T 12-State web toolbar.  Toolbar access is obtained via the block id request form.

Due to the large size of the tables in some of the Data Validation files, it is recommended that users open the files into a database type application that supports large table extractions.

# Chapter 3

## Description of Files

Address Validation

Provides information to ensure that addresses submitted on Service Orders are valid

Feature Availability

Provides information to identify desired features and prefixes that are available for the requested area by a particular Central Office or switch

Directory Names

Identifies directory names and subsections for purposes of ordering foreign listings.

Class of Service

Provides information about classes of service and Uniform Service Order Codes (USOCs).  Codes which determine the type of service, customers will have, i.e. Residential, Business.

USOCs / FIDS

Provides USOCs and FIDs that are used to indicate the types of new or changed products and services when requesting due dates and submitting orders. A three or five character alphabetical, numerical, or alphanumeric code that identifies a specific item of service or equipment on the service order and on the Customer Service Information Report.

Community Names

Provides a list of community names in full and/or abbreviated format.  Consult regional business rules in the CLEC Handbook for instructions on which form to use when submitting orders.

Yellow Page Headings

The Yellow Page Headings data specifies the acceptable heading codes and verbiage for directory listings orders.

PIC / LPIC

Pre-subscribed Interexchange Carrier (PIC) or Local Pre-subscribed Intraexchange Carrier (LPIC). The Interexchange & Intraexchange  Customer (IC) that an End User (EU) has selected to provide "Dial 1+" functionality for Interstate and/or Intrastate calling within a particular switch.

Alternate Community Name ---North.   Northern California and Nevada

Provides a list of the Community Names or the prestige name for a listed address and the Alternate Community Name or the postal address or the service address.

Alternate Community Name ---South.	Southern California

Provides a list of the Community Names or the prestige name for a listed address and the Alternate Community Name or the postal address or the service address.

# Chapter 4

## File Layout Records

### AT&T Midwest Region

|  | AT&T Midwest Region |
| --- | --- |
| SAG | Flat |
| Feature Availability | Comma Delimited |
| Directory Names | Comma Delimited |
| Class of Service | Comma Delimited |
| USOC/FID | Comma Delimited |
| Community Name | Comma Delimited |
| Yellow Page Headings | Comma Delimited |
| PIC/LPIC | Comma Delimited |

FILE NAME ---SAG File 	(AT&T Midwest Region)

Detail Record Layout

| Field Name | Data Length | Data Type | Position | Comments |
| --- | --- | --- | --- | --- |
| Street Name | 40 | A/N | 1 – 40 | Street Name of the address |
| Directional | 3 | A/N | 41 – 43 | Direction in which the street runs (N, E, S, W, NE, SW, NW, SE) |
| Low Address Range | 15 | A/N | 44 – 58 | The numeric or alpha/numeric characters that are the lowest valid value for the street name within zip code, exchange or central office boundaries. |
| High Address Range | 15 | A/N | 59 – 73 | The numeric or alpha/numeric characters that are the highest valid value for the street name within zip code, exchange or central office boundaries. |
| Odd Even Indicator | 1 | A/N | 74 | Indicates whether the address range is only the even or odd side of the street. This field is only applicable when a boundary runs down the middle of a street. |
| NPA | 3 | A/N | 75 – 77 | Number Plan Area (area code) for a telephone number. |
| Exchange | 4 | A/N | 78 – 81 | The serving exchange that serves the customer. |
| Central Office (NNX) | 3 | A/N | 82 – 84 | The standard central office code. |
| State Code | 2 | A/N | 85 – 86 | Abbreviation of the State. |
| Zip Code | 5 | A/N | 87 – 91 | The 5-digit zip code. |
| Rate info- Rate Band | 1 | A/N | 92 | Shows rate band entries for both Residential and Business |
| Rate info- Access Area | 1 | A/N | 93 | Area within a rate band in which additional charges apply |
| Community Name | 20 | A/N | 94 - 113 | The name of the city or community in which the street address is physically located. |
| Remarks- Remark 1 | 72 | A/N | 114 – 185 | Can occur 0 – 4 times. This is text which provides additional information about an address which may impact customer negotiations. |
| Remarks- Remark 2 | 72 | A/N | 186 – 257 | Second Remark. |
| Remarks- Remark 3 | 72 | A/N | 258 – 329 | Third Remark. |
| Remarks- Remark 4 | 72 | A/N | 330 – 401 | Fourth Remark. |

(Record Size will be 401 bytes)

FILE NAME ---Feature Availability File 	(AT&T Midwest Region)

Contains information for each Central Office (represented by NPA-NNX).  In situations where a Central Office is serviced by more than one switch, the file contains information about which switch provides each feature.  This contains all currently available class features.

Header Record Layout

| Field Name | Data Length | Max Char Length | Data Type | Comments |
| --- | --- | --- | --- | --- |
| STATE-WIDE FEATURES | 19 | 24 | A/S | Header –State Wide Features (State-Wide Features will appear before the Switch-Specific Features for each state) |
| SWITCH-SPECIFIC FEATURES | 24 | 24 | A/S | Header – Switch Specific Features |

Note:   All the USOCS under the Statewide Features header are available state wide in all switch types.  The USOCS/FEATURES that appear under the Switch specific header are available only in the switches indicated.

| Field Name | Data Length | Max Char Length | Data Type | Comments |
| --- | --- | --- | --- | --- |
| State (state_cd) | 2-4 | 4 | A/N | Valid Values: IL, IN, MI, OH, WI |
| Comma Delimiter | 1 | 1 | S | , |
| Exk NPA (exk_npa) | 3 | 3 | A/N | This is field to uniquely identify the CLLI code. For the State-Wide Features, this value will be empty. |
| Comma Delimiter | 1 | 1 | S | , |
| Exk NNN (exk_nnn) | 3 | 3 | A/N | This field to uniquely identify the CLLI code. For the State-Wide Features, this value will be empty. |
| Comma Delimiter | 1 | 1 | S | , |
| LST (CLLI) Local Service Termination | 11 | 11 | A/N/S | Common Language Location Identifier (CLLI) - uniquely identifies the switch. For the State-Wide Features, this value will be empty. |
| Comma Delimiter | 1 | 1 | S | , |
| Switch Type | 1-10 | 10 | A/N | Switch ID designates the type of switch. Example, DMS, 5ESS, SIEMENS For the State-Wide Features, this value will be empty. |
| Comma Delimiter | 1 | 1 | S | , |
| Remote Access Call Forwarding (RACF)Indicator | 1 | 1 | A/N/S | Indicates whether or not Remote Access Call Forwarding (RACF) is available for the Central Office. X = Available Blank = Not Available For the State-Wide Features, this value will be empty. |
| Comma Delimiter | 1 | 1 | S | , |
| USOC Table Feature USOC (cofa_usoc) (feature_exception_usoc) | 3-10 | 10 | A/N/S | Feature USOC offered by the central office (NNX). |
| Comma Delimiter | 1 | 1 | S | , |
| Feature DES (English Description) | 1-50 | 50 | A/N/S | Text Description of the Feature / USOC |
| Comma Delimiter | 1 | 1 | S | , |
| Market Segment A = RESALE B = UNE There will be only one Market Segment per row. If a USOC has more than one Market Segment, a duplicate line will appear on the data validation file and show the second Market Segment value. | 1 | 1 | A/N | A = Loop ( B ) B = Loop with NP ( B ) C = NP ( B ) E = Resale (A ) F = Unbundled Local ( B ) Switching (Port) J = Directory Services ( A, B ) K = Resale Private Line ( A ) M = Loop with Port ( B ) P = Resale Centrex/Plexar ( B ) R = Digital Trunking Resale ( B ) S = Digital Trunking Loop with Port ( B ) T = DID/PBX Resale ( A ) U = DID/PBX Port ( B ) V = Centrex/Plexar Port ( B ) W = DID/PBX Loop with Port ( B ) X = Centrex/Plexar Loop with Port ( B ) Y= ISDN PRI Loop with Port ( B ) Z = ISDN PRI Resale ( A ) 2 = ISDN PRI with Port ( B ) 3 = Digital Trunking with Port (B) |
| Comma Delimiter | 1 | 1 | S | , |
| ** TOS (Type of Service) Example: 1 or 2 or 1,2 1=Business, 2=Residence | 1-4 | 4 | N/S | 1st Character 1 = Business ( 1 ) 2 = Residence ( 2 ) 3 = Government (Federal) ( 1 ) 4 = Coin ( 1 ) 5 = Home Office ( 2 ) |

FILE NAME --- Directory Names 	( AT&T Midwest Region)

Provide a list of Directory Names, the towns and communities served by that directory.

| Field_Name | Data_Length | Maximum Character Length | Data_Type | Comments |
| --- | --- | --- | --- | --- |
| State | 2-4 | 4 | AN | Valid Values: IL, IN, MI, OH, WI |
| Comma Delimiter | 1 | 1 | S | , |
| Directory Name | 1-50 | 50 | AN | Name of the directory, example Lake County |
| Comma Delimiter | 1 | 1 | S | , |
| Directory Subsection | 1-150 | 150 | ANS | Name of the directory subsection, example Libertyville |
| Comma Delimiter | 1 | 1 | S | , |
| Directory Identifier (DIRIDL) | 1-4 | 4 | A | LIWL |
| Comma Delimiter | 1 | 1 | S | , |
| Directory Section | 1-3 | 3 | AS | B |

FILE NAME ---Class of Service(CLS) 	(AT&T Midwest Region)

Provide a list of the Class of Service and an English Description

| Field_Name | Data_Length | Max Char Length | Data_Type | Comments or Example of Data, not format |
| --- | --- | --- | --- | --- |
| REGION | 2-5 | 5 | ANS | AT&T Midwest, AT&T Connecticut, AT&T Southwest, AT&T West |
| comma delimiter | 1 | 1 | S | , |
| STATE | 2-4 | 4 | AN | CT, IL, TX, OK, CA |
| comma delimiter | 1 | 1 | S | , |
| USOC | 2-10 | 10 | ANS | AEV, 1FB, FPSVE, AS3DL |
| comma delimiter | 1 | 1 | S | , |
| USOC_DESC | 1- 350 | 350 | ANS | Text Description to 350 Char |
| comma delimiter | 1 | 1 | S | , |
| PRODUCT_FAMILY | 1-50 | 50 | AN | COIN, ISDN DIRECT |
| comma delimiter | 1 | 1 | S | , |
| STATUS | 1 | 1 | AN | Y, G, R, B |
| comma delimiter | 1 | 1 | S | , |
| TOS (Type of Service) | 4 | 100 | ANS | 1st Character 1 = Business 2 = Residence 3 = Government (Federal) 4 = Coin 5 = Home Office 2nd Character C = Coin E = Centrex H = BRI-ISDN J = PBX-trunk K = PRI-ISDN P = Data Voice split line R = Data voice shared line 1 = Circuit Analog 2 = Circuit Digital less then 1.5 Mbps 3 = Circuit Digital greater than 1.5 Mbps 4 = Switch 56/Dial Up Data 5 = Both DID/PBX 6 = DID 7 = Centrex based / BRI-ISDN 8 = POTS - = Not Applicable 3rd Character* M = Measured Rate F = Flat Rate G = Message Per Minute POTS - = Not Applicable 4th Character* F = Foreign Exchange Service G = Semi Public P = Prison Inmate R = Remote Call Forwarding S = 800 Service W = WATS Y = Digital Trunk Z = Wholesale Number Retention - = Not Applicable |
| comma delimiter | 1 | 1 | S | , |
| PROV_METHOD (Market Segment) | 1 | 60 | ANS | A,B,C,E,F,J,K,M,P,R,S,T,U,V,W,X,Y,Z,2,3 |
| comma delimiter | 1 | 1 | S | , |
| FID | 2--10 | 200 | ANS | C /HTG |
| comma delimiter | 1 | 1 | S | , |
| LSR_FIELD | 2-10 | 350 | ANS | R ECCKT |
| comma delimiter | 1 | 1 | S | , |
| SPEC_IND | 1 | 1 | AN | U, L, F |
| comma delimiter | 1 | 1 | S | , |
| ACCT LINE_FEATURE | 1 | 1 | A | L, A, B |
| comma delimiter | 1 | 1 | S | , |
| CONDITIONS | 1-1000 | 1000 | ANS |  |
| comma delimiter | 1 | 1 | S | , |
| COMMENTS | 1-1000 | 1000 | ANS |  |

STATUS:  Indicate the STATUS of the USOC in this column.

Valid Entries:

Y= Valid for ordering on an LSR

N = Not a Valid Code—Cannot enter on an LST for any Wholesale or Retail order.

G = Grandfathered - can enter on a migration request only.

R = Retail Only - cannot enter on an LSR

B = Billing Only - cannot enter on an LSR - MOG or a Service Rep can populate on service orders.

P = Provisioning Only - Can enter on a migration LSR if present on an existing account, but not on a new activity - This will

be completed internally by AT&T 12-State.

TOS (Type of Service)	* 3rd and 4th characters are only completed if available.  If not available, the values will not be populated.

SPEC IND Indicate in this column the SPECial INDicators

Valid Entries:

U == USOC

L = Line Assignable USOC

F = FID

ACCOUNT LINE FEATURE: Indicate Account Feature, Line Feature or Both in this column

Valid Entries:

L = Line Feature (Res/Bus)

A = Account Feature

B = Both Line and Account Feature

FILE NAME --- USOC/FIDS 	(AT&T Midwest Region)

Provide a list of the USOC/FIDS for each region down to the state level.

| Field_Name | Data_Length | Max Char Length | Data_Type | Comments or Example of Data, not format |
| --- | --- | --- | --- | --- |
| REGION | 2-5 | 5 | ANS | AT&T Midwest, AT&T Connecticut, AT&T Southwest, AT&T West |
| comma delimiter | 1 | 1 | S | , |
| STATE | 2-4 | 4 | AN | CT, IL, TX, OK, CA |
| comma delimiter | 1 | 1 | S | , |
| USOC | 2-10 | 10 | ANS | AEV, 1FB, FPSVE, AS3DL |
| comma delimiter | 1 | 1 | S | , |
| USOC_DESC | 1-350 | 350 | ANS | Text Description to 350 Char |
| comma delimiter | 1 | 1 | S | , |
| Class of Service Indicator | 1 | 1 | A | Y = Yes , N = No |
| comma delimiter | 1 | 1 | S | , |
| PRODUCT_FAMILY | 1-50 | 50 | AN | COIN, ISDN DIRECT |
| comma delimiter | 1 | 1 | S | , |
| STATUS | 1 | 1 | AN | Y, G, R, B |
| comma delimiter | 1 | 1 | S | , |
| TOS (Type of Service) | 4 | 100 | ANS | 1st Character 1 = Business 2 = Residence 3 = Government (Federal) 4 = Coin 5 = Home Office 2nd Character C = Coin E = Centrex H = BRI-ISDN J = PBX-trunk K = PRI-ISDN P = Data Voice split line R = Data voice shared line 1 = Circuit Analog 2 = Circuit Digital less then 1.5 Mbps 3 = Circuit Digital greater than 1.5 Mbps 4 = Switch 56/Dial Up Data 5 = Both DID/PBX 6 = DID 7 = Centrex based / BRI-ISDN 8 = POTS - = Not Applicable 3rd Character* M = Measured Rate F = Flat Rate G = Message Per Minute POTS - = Not Applicable 4th Character* F = Foreign Exchange Service G = Semi Public P = Prison Inmate R = Remote Call Forwarding S = 800 Service W = WATS Y = Digital Trunk Z = Wholesale Number Retention - = Not Applicable |
| comma delimiter | 1 | 1 | S | , |
| PROV_METHOD (Market Segment) | 1 | 60 |  | A,B,C,E,F,J,K,M,P,R,S,T,U,V,W,X,Y,Z,2,3 |
| comma delimiter | 1 | 1 | S | , |
| FID | 2-10 | 200 | ANS | C /HTG |
| comma delimiter | 1 | 1 | S | , |
| LSR_FIELD | 2-10 | 350 |  | R ECCKT |
| comma delimiter | 1 | 1 | S | , |
| SPEC_IND | 1 | 1 | A | U, L, F |
| comma delimiter | 1 | 1 | S | , |
| ACCT LINE_FEATURE | 1 | 1 | A | L, A, B |
| comma delimiter | 1 | 1 | S | , |
| CONDITIONS | 1-1000 | 1000 | ANS |  |
| comma delimiter | 1 | 1 | S | , |
| COMMENTS | 1-1000 | 1000 | ANS |  |

STATUS:  Indicate the STATUS of the USOC in this column.

Valid Entries:

Y= Valid for ordering on an LSR

N = Not a Valid Code—Cannot enter on an LST for any Wholesale or Retail order.

G = Grandfathered - can enter on a migration request only.

R = Retail Only - cannot enter on an LSR

B = Billing Only - cannot enter on an LSR - MOG or a Service Rep can populate on service orders.

P = Provisioning Only - Can enter on a migration LSR if present on an existing account, but not on a new activity - This will

be completed internally by AT&T 12-State.

TOS (Type of Service)	* 3rd and 4th characters are only completed if available.  If not available, the values will not be populated.

SPEC IND Indicate in this column the SPECial INDicators

Valid Entries:

U == USOC

L = Line Assignable USOC

F = FID

ACCOUNT LINE FEATURE: Indicate Account Feature, Line Feature or Both in this column

Valid Entries:

L = Line Feature (Res/Bus)

A = Account Feature

B = Both Line and Account Feature

FILE NAME ---Community Name File 	(AT&T Midwest Region)

Provide a list of Community Names and the abbreviations

| Field_Name | Data_Length | Maximum Char Length | Data_Type | Comments |
| --- | --- | --- | --- | --- |
| State | 2 | 2 | A | IL |
| Comma Delimiter | 1 | 1 | S | , |
| Community Name Full Spelling | 1-45 | 45 | ANS | Addieville, |
| Comma Delimiter | 1 | S | 46 | , |
| Community Name Abbreviation | 1-25 | 25 | ANS | Addieville, |

FILE NAME --- Yellow Page Headings 	(AT&T Midwest Region)

| Field_Name | Data_Length | Maximum Char Length | Data_Type | Comments |
| --- | --- | --- | --- | --- |
| State | 2 | 2 | AN | IL, IN, MI, OH, WI |
| Comma Delimiter | 1 | 1 | S | , |
| Yellow Page Code | 6 | 6 | AN | 000025 |
| Comma Delimiter | 1 | 1 | S | , |
| Yellow Page Heading Text | 1-76 | 76 | AN | ALLOYS |
| Comma Delimiter | 1 | 1 | S | , |
| Yellow Page Heading Abbreviation | 1-40 | 40 | AN | alloys |
| Comma Delimiter | 1 | 1 | S | , |
| Directory Type Code | 1 | 1 | AN | B=Bus to Bus, C=Consumer, D=Both (Dual) |
| Comma Delimiter | 1 | 1 | S | , |
| Standard Industrial Classification (SIC) | 4 | 4 | AN | 5051 |

Note:  Each individual piece of Data with in the Yellow Page Heading Text and the Yellow Page Heading Abbreviation fields will be surrounded by double quotes “ “.      The double quotes will add 2 bytes to the field length of 40 characters

FILE NAME ---PIC/LPIC 	(AT&T Midwest Region)

Provides a list of the valid interlata and intralata carriers for NPA, Exchange, and Central Office.

| Field Name | Data Length | Data Type | Position | Comments |
| --- | --- | --- | --- | --- |
| State | 2 | A/N | 1 – 2 | Valid Values: IL, IN, MI, OH, WI |
| Comma Delimiter | 1 | S | 3 | , |
| NPA | 3 | A/N | 4 – 6 | Number Plan Area (area code) for a telephone number. |
| Comma Delimiter | 1 | S | 7 | , |
| Exchange | 4 | A/N | 8 – 11 | Four-letter abbreviation of the Exchange that represents a geographic grouping of Central Office prefixes. |
| Comma Delimiter | 1 | S | 12 | , |
| Central Office | 3 | A/N | 13 – 15 | High level generic central office that represents central offices in the same wire center. |
| Comma Delimiter | 1 | S | 16 | , |
| Exk NPA | 3 | A/N | 17 – 19 | This is a new field to uniquely identify the CLLI code. |
| Comma Delimiter | 1 | S | 20 | , |
| Exk NNN | 3 | A/N | 21 – 23 | This is a new field to uniquely identify the CLLI code. |
| Comma Delimiter | 1 | S | 24 | , |
| CLLI Code | 11 | A/N | 25 – 35 | This is a new field for the PIC/LPIC file. Common Language Location Identifier (CLLI)- uniquely identifies the switch. |
| Comma Delimiter | 1 | S | 36 | , |
| Exchange PIC Table- Occurs n times PIC | 4 | A/N | 37 – 40 | The ACNA (Access Customer Name Abbreviation) identifying the carrier |
| Comma Delimiter | 1 | S | 41 | , |
| PICX | 5 | A/N | 42 – 46 | The Carrier Identification Code (CIC) of the carrier E = Interlata A = Intralata B = Both |
| Comma Delimiter | 1 | S | 47 | , |
| PIC Type | 1 | A/N | 48 | Identifies the type of long distance service the carrier is providing |
| Comma Delimiter | 1 | S | 49 | , |
| Type of Service | 1 | A/N | 50 | R = Residence B = Business |
| Comma Delimiter | 1 | S | 51 | , |
| ACNADES | 35 | A/N/S | 52 - 86 | Carrier Name |
| Comma Delimiter | 1 | S | 87 | , |

(Record Size will vary depending on occurrences of the PIC table)

File Name		Description

ILCARR.TXT		PIC / LPIC by Switch Illinois

INCARR.TXT	PIC / LPIC by Switch Indiana

MICARR.TXT	PIC / LPIC by Switch Michigan

OHCARR.TXT	PIC / LPIC by Switch Ohio

WICARR.TXT	PIC / LPIC by Switch Wisconsin

Note	Codes in the ACNA Description Column for the AT&T Midwest Region:

DNA* - "DO NOT ACCEPT" RESTRICTION

- Identifies carriers that have advised the AT&T Midwest Region that they do not wish to be selected by end users under any circumstances.

- Any carrier designated by DNA* is not PIC-able.

- Users must contact the carrier and the carrier will submit the order.

DNO* - "DO NOT OFFER" RESTRICTION

- The prefix means do not offer when reading the list of available carriers.

- The prefix DNO* is added in front of the carrier's name. (DNO* Joe's Phone)

B* - "PREFERS BUSINESS CUSTOMER ONLY" RESTRICTION

- When reading the list of available carriers to a residential customer, those with a B* prefix should not be included.  If a residential customer asks for a B* restricted carrier, explain that the requested carrier prefers business customers only.  Offer to give the carrier's telephone number to the customer.

- If the residential customer claims that they have already spoken with the restricted carrier, and the carrier agreed to sign them up as a new customer, then the B* carrier may be selected.

R* - “PREFERS RESIDENCE CUSTOMER ONLY" RESTRICTION

- When reading the list of available carriers to a business customer, those with an R* prefix should not be included.  If a business customer asks for an R* restricted carrier, explain that the requested carrier prefers residence customers only.  Offer to give the carrier's telephone number to the customer.

- If the business customer claims that they have already spoken with the restricted carrier, and the carrier agreed to sign them up as a new customer, then the R* carrier may be selected.

### AT&T West Region

|  | AT&T West Region |
| --- | --- |
| SAG | Flat |
| Feature Availability | Comma Delimited |
| Directory Names | Comma Delimited |
| Class of Service | Comma Delimited |
| USOC/FID | Comma Delimited |
| Community Name | Comma Delimited |
| Yellow Page Headings | Comma Delimited |
| PIC/LPIC | Comma Delimited |
| North Alternate Community Name | Comma Delimited |
| South Alternate Community Name | Comma Delimited |

FILE NAME ---SAG File 	(AT&T West Region)

Header Record Layout

| Field Name | Data Length | Data Type | Position | Comments |
| --- | --- | --- | --- | --- |
| HDR1 | 3 | ANS | 1-3 | Header indicator |
| Date-Time | 14 | ANS | 4-17 | Date and time the file was created |
| Filler | 233 | ANS | 18-250 |  |

Detail Record Layout

| Field Name | Data Length | Data Type | Position | Comments |
| --- | --- | --- | --- | --- |
| Addr type | 1 | ANS | 1 | Type of range record |
| Community-req | 1 | ANS | 2 | Address range indicator |
| Directional | 2 | ANS | 3-4 | E, W, S, N, SW, NE, SE, NW |
| Street name | 50 | ANS | 5-54 | Street name |
| Low range | 8 | ANS | 55-62 | Low street range |
| High range | 8 | ANS | 63-70 | High street range |
| Odd-even | 1 | ANS | 71 | Odd or Even street ranges |
| Community | 32 | ANS | 72-103 | Community name |
| Exch-code | 4 | ANS | 104-107 | Exchange code |
| State | 2 | ANS | 108-109 | Abbreviation of the state |
| SAGA | 4 | ANS | 110-113 | Street Address Guide Area |
| TTA | 3 | ANS | 114-116 | Terminating Telephone area |
| Tax-code | 6 | ANS | 117-122 | Tax type levied on phone service |
| ALT-ind | 1 | ANS | 123 | Primary or alternate address range |
| GSG | 4 | ANS | 124-127 | Geographic Segment |
| ZIP-Code | 5 | ANS | 128-132 | Postal Zone |
| Rate-Zone | 5 | ANS | 133-137 | Rate zone type |
| Wire Center | 8 | ANS | 138-145 | 8 character wirecenter name e.g. SNFCCA11 |
| NPA | 3 | ANS | 146-148 | Number Plan Area |
| Tax-ind | 1 | ANS | 149 | Tax code region |
| ESN | 3 | ANS | 150-152 | Emergency Service Number (not applicable AT&T California) |
| ADNC | 4 | ANS | 153-156 | Address Name Code |
| Num-Srt | 10 | ANS | 157-166 | Street Name, only if it’s numeric |
| PD | 9 | ANS | 167-175 | Plant Installation District |
| Filler | 75 | ANS | 176-250 |  |

(Record Size will be 250 bytes)

FILE NAME ---Feature Availability File 	(AT&T West Region)

| Field_Name | Data_Length | Data_Type | Position | Comments |
| --- | --- | --- | --- | --- |
| NPA | 3 | AN | 1-3 |  |
| Comma Delimiter | 1 | S | 4 | , |
| NXX | 3 | AN | 5-7 |  |
| Comma Delimiter | 1 | S | 8 | , |
| CLLI | 11 | AN | 9 -19 | The 5th and 6th characters of the CLLI code is the state code (CA or NV). |
| Comma Delimiter | 1 | S | 20 | , |
| Switch Type | 1-10 | 10 | AN | DMS |
| Comma Delimiter | 1 | 1 | S | , |
| 800 (Inward WATS) | 1 | AN | 21 | X or Blank |
| Comma Delimiter | 1 | S | 22 | , |
| 976 Call Blocking (ICSB) | 1 | AN | 23 | X or Blank |
| Comma Delimiter | 1 | S | 24 | , |
| Internet Service Provider | 1 | AN | 25 | X or Blank |
| Comma Delimiter | 1 | S | 26 | , |
| Coin Capability | 1 | AN | 27 | X or Blank |
| Comma Delimiter | 1 | S | 28 | , |
| Customer Owned Pay Telephone | 1 | AN | 29 | X or Blank |
| Comma Delimiter | 1 | S | 30 | , |
| Direct Inward Dialing | 1 | AN | 31 | X or Blank |
| Comma Delimiter | 1 | S | 32 | , |
| Poll Star (DLC) | 1 | AN | 33 | X or Blank |
| Comma Delimiter | 1 | S | 34 | , |
| Virtual Message Wait Indicator | 1 | AN | 35 | X or Blank |
| Comma Delimiter | 1 | S | 36 | , |
| Limited Disconnect Program | 1 | AN | 37 | X or Blank |
| Comma Delimiter | 1 | S | 38 | , |
| Measured/Metro Service Indicator | 1 | AN | 39 | X or Blank |
| Comma Delimiter | 1 | S | 40 | , |
| 976 Call Blocking (Res Option 2/3) | 1 | AN | 41 | X or Blank |
| Comma Delimiter | 1 | S | 42 | , |
| Call Waiting with Delayed Call Forwarding | 1 | AN | 43 | X or Blank |
| Comma Delimiter | 1 | S | 44 | , |
| Direct Connect Shared | 1 | AN | 45 | X or Blank |
| Comma Delimiter | 1 | S | 46 | , |
| Plain Old Telephone Service (POTS) | 1 | AN | 47 | X or Blank |
| Comma Delimiter | 1 | S | 48 | , |
| Universal WATS | 1 | AN | 49 | X or Blank |
| Comma Delimiter | 1 | S | 50 | , |
| Remote Call Forwarding | 1 | AN | 51 | X or Blank |
| Comma Delimiter | 1 | S | 52 | , |
| Number Retention Service | 1 | AN | 53 | X or Blank |
| Comma Delimiter | 1 | S | 54 | , |
| Service Area Wide Area Telephone Service | 1 | AN | 55 | X or Blank |
| Comma Delimiter | 1 | S | 56 | , |
| Single Line Remote Call Forwarding (IMCF) | 1 | AN | 57 | X or Blank |
| Comma Delimiter | 1 | S | 58 | , |
| WATS (Wide Area Telephone Service) | 1 | AN | 59 | X or Blank |
| Comma Delimiter | 1 | S | 60 | , |
| Custom Virtual Network | 1 | AN | 61 | X or Blank |
| Comma Delimiter | 1 | S | 62 | , |
| 3 Way Calling | 1 | AN | 63 | X or Blank |
| Comma Delimiter | 1 | S | 64 | , |
| Busy Call Forwarding Intraswitch | 1 | AN | 65 | X or Blank |
| Comma Delimiter | 1 | S | 66 | , |
| Busy Call Forwarding Extended | 1 | AN | 67 | X or Blank |
| Comma Delimiter | 1 | S | 68 | , |
| Caller ID Complete Blocking with Cancel per call | 1 | AN | 69 | X or Blank |
| Comma Delimiter | 1 | S | 70 | , |
| Cancel Call Waiting | 1 | AN | 71 | X or Blank |
| Comma Delimiter | 1 | S | 72 | , |
| Call Forwarding | 1 | AN | 73 | X or Blank |
| Comma Delimiter | 1 | S | 74 | , |
| Caller ID | 1 | AN | 75 | X or Blank |
| Comma Delimiter | 1 | S | 76 | , |
| Call Return | 1 | AN | 77 | X or Blank |
| Comma Delimiter | 1 | S | 78 | , |
| Call Trace | 1 | AN | 79 | X or Blank |
| Comma Delimiter | 1 | S | 80 | , |
| Call Waiting | 1 | AN | 81 | X or Blank |
| Comma Delimiter | 1 | S | 82 | , |
| Delayed Call Forwarding Intraswitch | 1 | AN | 83 | X or Blank |
| Comma Delimiter | 1 | S | 84 | , |
| Remote Access to Call Forwarding | 1 | AN | 85 | X or Blank |
| Comma Delimiter | 1 | S | 86 | , |
| Intercom Plus | 1 | AN | 87 | X or Blank |
| Comma Delimiter | 1 | S | 88 | , |
| Priority Ringing | 1 | AN | 89 | X or Blank |
| Comma Delimiter | 1 | S | 90 | , |
| Repeat Dialing | 1 | AN | 91 | X or Blank |
| Comma Delimiter | 1 | S | 92 | , |
| Select Call Forwarding | 1 | AN | 93 | X or Blank |
| Comma Delimiter | 1 | S | 94 | , |
| Speed Calling 8 | 1 | AN | 95 | X or Blank |
| Comma Delimiter | 1 | S | 96 | , |
| Speed Calling 30 | 1 | AN | 97 | X or Blank |
| Comma Delimiter | 1 | S | 98 | , |
| Caller ID Complete Blocking without Cancel per call | 1 | AN | 99 | X or Blank |
| Comma Delimiter | 1 | S | 100 | , |
| Basic Features CMSTRI | 1 | AN | 101 | X or Blank |
| Comma Delimiter | 1 | S | 102 | , |
| DNCF | 1 | AN | 103 | X or Blank |
| Comma Delimiter | 1 | S | 104 | , |
| PORT | 1 | AN | 105 | X or Blank |
| Comma Delimiter | 1 | S | 106 | , |
| Basic Features CMSTRII | 1 | AN | 107 | X or Blank |
| Comma Delimiter | 1 | S | 108 | , |
| 800 Inward WATS | 1 | AN | 109 | X or Blank |
| Comma Delimiter | 1 | S | 110 | , |
| Additional Call Pickup | 1 | AN | 111 | X or Blank |
| Comma Delimiter | 1 | S | 112 | , |
| Busy / Delayed Call Forwarding - Busy All | 1 | AN | 113 | X or Blank |
| Comma Delimiter | 1 | S | 114 | , |
| Call Waiting with Cancel Call Waiting | 1 | AN | 115 | X or Blank |
| Comma Delimiter | 1 | S | 116 | , |
| Call Forwarding | 1 | AN | 117 | X or Blank |
| Comma Delimiter | 1 | S | 118 | , |
| Area Wide Centrex | 1 | AN | 119 | X or Blank |
| Comma Delimiter | 1 | S | 120 | , |
| Call Selection | 1 | AN | 121 | X or Blank |
| Comma Delimiter | 1 | S | 122 | , |
| Call Waiting with Delay Call Forwarding | 1 | AN | 123 | X or Blank |
| Comma Delimiter | 1 | S | 124 | , |
| Busy / Delayed Call Forwarding - Delay Out Only | 1 | AN | 125 | X or Blank |
| Comma Delimiter | 1 | S | 126 | , |
| Anonymous Call Reject | 1 | AN | 127 | X or Blank |
| Comma Delimiter | 1 | S | 128 | , |
| Distinctive Ringing | 1 | AN | 129 | X or Blank |
| Comma Delimiter | 1 | S | 130 | , |
| Speed Calling | 1 | AN | 131 | X or Blank |
| Comma Delimiter | 1 | S | 132 | , |
| WATS (Wide Area Telephone Service) | 1 | AN | 133 | X or Blank |
| Comma Delimiter | 1 | S | 134 | , |
| Message Screening | 1 | AN | 135 | X or Blank |
| Comma Delimiter | 1 | S | 136 | , |
| Account Codes | 1 | AN | 137 | X or Blank |
| Comma Delimiter | 1 | S | 138 | , |
| Call-in-One (for TMC) | 1 | AN | 139 | X or Blank |
| Comma Delimiter | 1 | S | 140 | , |
| Call Waiting Indicator | 1 | AN | 141 | X or Blank |
| Comma Delimiter | 1 | S | 142 | , |
| Call-in-One (for 50+) | 1 | AN | 143 | X or Blank |
| Comma Delimiter | 1 | S | 144 | , |
| Call-in-One (for Unisys 100) | 1 | AN | 145 | X or Blank |
| Comma Delimiter | 1 | S | 146 | , |
| Basic CENTEX Service | 1 | AN | 147 | X or Blank |
| Comma Delimiter | 1 | S | 148 | , |
| 976 Call Blocking (ICSB) | 1 | AN | 149 | X or Blank |
| Comma Delimiter | 1 | S | 150 | , |
| Automatic Callback | 1 | AN | 151 | X or Blank |
| Comma Delimiter | 1 | S | 152 | , |
| Customer Dialed Account Recording | 1 | AN | 153 | X or Blank |
| Comma Delimiter | 1 | S | 154 | , |
| Call Forwarding Busy / Don't Answer Expanded | 1 | AN | 155 | X or Blank |
| Comma Delimiter | 1 | S | 156 | , |
| Call Forwarding over Private Facilities | 1 | AN | 157 | X or Blank |
| Comma Delimiter | 1 | S | 158 | , |
| Call Forwarding Reminder Ring | 1 | AN | 159 | X or Blank |
| Comma Delimiter | 1 | S | 160 | , |
| Conference Call | 1 | AN | 161 | X or Blank |
| Comma Delimiter | 1 | S | 162 | , |
| Cenpath | 1 | AN | 163 | X or Blank |
| Comma Delimiter | 1 | S | 164 | , |
| Direct Digital Interface | 1 | AN | 165 | X or Blank |
| Comma Delimiter | 1 | S | 166 | , |
| Electronic Telephone Feature Pkg / Business Set | 1 | AN | 167 | X or Blank |
| Comma Delimiter | 1 | S | 168 | , |
| Station Message Detail Recording Premise | 1 | AN | 169 | X or Blank |
| Comma Delimiter | 1 | S | 170 | , |
| Prompted Repeat Dialing | 1 | AN | 171 | X or Blank |
| Comma Delimiter | 1 | S | 172 | , |
| Additional D Channel Packet Device | 1 | AN | 173 | X or Blank |
| Comma Delimiter | 1 | S | 174 | , |
| B Channel Packet Service | 1 | AN | 175 | X or Blank |
| Comma Delimiter | 1 | S | 176 | , |
| Centrex IS (Centrex Basic Rate ISDN) | 1 | AN | 177 | X or Blank |
| Comma Delimiter | 1 | S | 178 | , |
| Home ISDN | 1 | AN | 179 | X or Blank |
| Comma Delimiter | 1 | S | 180 | , |
| Primary Rate ISDN | 1 | AN | 181 | X or Blank |
| Comma Delimiter | 1 | S | 182 | , |
| Access to Switched Data 56kbs Network | 1 | AN | 183 | X or Blank |
| Comma Delimiter | 1 | S | 184 | , |
| Privacy Manager | 1 | AN | 185 | X or Blank |
| Comma Delimiter | 1 | S | 186 | , |
| Quick Dial Tone | 1 | AN | 187 | X or Blank |
| Comma Delimiter | 1 | S | 188 | , |
| Universal WATS | 1 | AN | 189 | X or Blank |
| Comma Delimiter | 1 | S | 190 | , |
| Direct Connect | 1 | AN | 191 | X or Blank |
| Comma Delimiter | 1 | S | 192 | , |
| Call Transfer Disconnect | 1 | AN | 193 | X or Blank |
| Comma Delimiter | 1 | S | 194 | , |
| Talking Call Waiting | 1 | AN | 195 | X or Blank |
| Comma Delimiter | 1 | S | 196 | , |
| Busy / Delayed Call Forwarding | 1 | AN | 197 | X or Blank |
| Comma Delimiter | 1 | S | 198 | , |
| Datapath 56Kb Line | 1 | AN | 199 | X or Blank |
| Comma Delimiter | 1 | S | 200 | , |
| DPX 56Kb Line | 1 | AN | 201 | X or Blank |
| Comma Delimiter | 1 | S | 202 | , |
| OCUDP Local 56Kb Line | 1 | AN | 203 | X or Blank |
| Comma Delimiter | 1 | S | 204 | , |
| OCUDP Foreign Exchange | 1 | AN | 205 | X or Blank |
| Comma Delimiter | 1 | S | 206 | , |
| Call Forwarding Intragroup | 1 | AN | 207 | X or Blank |
| Comma Delimiter | 1 | S | 208 | , |
| Call Forwarding Intraswitch | 1 | AN | 209 | X or Blank |
| Comma Delimiter | 1 | S | 210 | , |
| Call Forwarding Interswitch | 1 | AN | 211 | X or Blank |
| Comma Delimiter | 1 | S | 212 | , |
| Forwarded Call Information | 1 | AN | 213 | X or Blank |
| Comma Delimiter | 1 | S | 214 | , |
| Message Waiting Indicator | 1 | AN | 215 | X or Blank |
| Comma Delimiter | 1 | S | 216 | , |
| Answering Supervision | 1 | AN | 217 | X or Blank |
| Comma Delimiter | 1 | S | 218 | , |
| Warmline | 1 | AN | 219 | X or Blank |
| Comma Delimiter | 1 | S | 220 | , |
| Busy Call Forwarding Interswitch | 1 | AN | 221 | X or Blank |
| Comma Delimiter | 1 | S | 222 | , |
| Delayed Call Forwarding Interswitch | 1 | AN | 223 | X or Blank |
| Comma Delimiter | 1 | S | 224 | , |
| Call Screen | 1 | AN | 225 | X or Blank |
| Comma Delimiter | 1 | S | 226 | , |
| Constellation + | 1 | AN | 227 | X or Blank |
| Comma Delimiter | 1 | S | 228 | , |
| Flexible Hi-Cap | 1 | AN | 229 | X or Blank |
| Comma Delimiter | 1 | S | 230 | , |
| Packet Internetworking | 1 | AN | 231 | X or Blank |
| Comma Delimiter | 1 | S | 232 | , |
| Digital Data Over Voice Advanced Digital Network | 1 | AN | 233 | X or Blank |
| Comma Delimiter | 1 | S | 234 | , |
| Public Packet Switching Asynchronous | 1 | AN | 235 | X or Blank |
| Comma Delimiter | 1 | S | 236 | , |
| Public Packet Switching Synchronous | 1 | AN | 237 | X or Blank |
| Comma Delimiter | 1 | S | 238 | , |
| Switched Multi-Megabit Data Service | 1 | AN | 239 | X or Blank |
| Comma Delimiter | 1 | S | 240 | , |
| Call Forwarding Intraswitch | 1 | AN | 241 | X or Blank |
| Comma Delimiter | 1 | S | 242 | , |
| Call Forwarding Interswitch | 1 | AN | 243 | X or Blank |
| Comma Delimiter | 1 | S | 244 | , |
| Call Forwarding Intergroup | 1 | AN | 245 | X or Blank |
| Comma Delimiter | 1 | S | 246 | , |
| Business Voice Mail - Series 100 | 1 | AN | 247 | X or Blank |
| Comma Delimiter | 1 | S | 248 | , |
| Business Voice Mail - Series 50 | 1 | AN | 249 | X or Blank |
| Comma Delimiter | 1 | S | 250 | , |
| The Message Center | 1 | AN | 251 | X or Blank |
| Comma Delimiter | 1 | S | 252 | , |
| Switched Digital Service IS (1mb/1ml Basic Rate ISDN) | 1 | AN | 253 | X or Blank |
| Comma Delimiter | 1 | S | 254 | , |
| National ISDN One | 1 | AN | 255 | X or Blank |
| Comma Delimiter | 1 | S | 256 | , |
| Access to Switched Data 64kbs Network | 1 | AN | 257 | X or Blank |
| Comma Delimiter | 1 | S | 258 | , |
| Internet Caller ID | 1 | AN | 259 | X or Blank |
| Comma Delimiter | 1 | S | 260 | , |
| Abbreviated Toll free Calling | 1 | AN | 261 | X or Blank |
| Comma Delimiter | 1 | S | 262 | , |
| Unified Communications - Consumer | 1 | AN | 263 | '-', 'L' or 'X' |
| Comma Delimiter | 1 | S | 264 | , |
| Unified Communications – Business | 1 | AN | 265 | '-', 'L' or 'X' |
| Comma Delimiter | 1 | S | 266 | , |
| Unified Communications – Business Plus | 1 | AN | 267 | '-', 'L' or 'X' |
| Comma Delimiter | 1 | S | 266 | , |
| Centrex IP | 1 | AN | 267 | X or Blank |
| “internal use only” | 1 | AN | 269 | X or Blank |
| Comma Delimiter | 1 | S | 270 | , |
| Unified Messaging DID Voice Mail | 1 | AN | 271 | '-', 'L' or 'X' |

Note:  All the blank spaces after line 271, Feature  127, Unified Messaging DID Voice Mail , are reserved for future use and will be updated as the features are added to the file.

The characters having the following meaning:

'-' (dash) – The Feature is not available.

'X'  – The feature is available and a toll call is not required to utilize the service.

'L' – The feature is available and a toll call is required to utilize the service.

FILE NAME --- Directory Names 	(AT&T West Region)

Provide a list of Directory Names and associated DIRIDL Values

| Field_Name | Data_Length | Maximum Char. Length | Data Type | Comments |
| --- | --- | --- | --- | --- |
| State | 2-4 | 4 | AN | CA, NV |
| Comma Delimiter | 1 | 1 | S | , |
| Directory Name | 1-50 | 50 | AN |  |
| Comma Delimiter | 1 | 1 | S | , |
| Directory ID (DIRIDL) | 2-3 | 3 | A | Examples AA – Airport Area CPT – Compton |
| Comma Delimiter | 1 | 1 | S | , |
| Directory Subsection (Towns & Community Name | 1-45 | 45 | ANS | NOT USED IN THE WEST; Null Value |
| Comma Delimiter | 1 | 1 | S | , |
| There will be no header, footer, error record, etc. |  |  |  |  |

Updated: September 1, 2009 for new file format

FILE NAME ---Class of Service 	(CLS) 	(AT&T West Region)

Provide a list of the Class of Service and an English Description

| Field_Name | Data_Length | Max Char Length | Data_Type | Comments or Example of Data, not format |
| --- | --- | --- | --- | --- |
| REGION | 2-5 | 5 | ANS | AT&T Midwest Region, AT&T Connecticut, AT&T Southwest Region, AT&T West Region |
| comma delimiter | 1 | 1 | S | , |
| STATE | 2-4 | 4 | AN | CT, IL, TX, OK, CA |
| comma delimiter | 1 | 1 | S | , |
| USOC | 2-10 | 10 | ANS | AEV, 1FB, FPSVE, AS3DL |
| comma delimiter | 1 | 1 | S | , |
| USOC_DESC | 1- 350 | 350 | ANS | Text Description to 350 Char |
| comma delimiter | 1 | 1 | S | , |
| PRODUCT_FAMILY | 1-50 | 50 | AN | COIN, ISDN DIRECT |
| comma delimiter | 1 | 1 | S | , |
| STATUS | 1 | 1 | AN | Y, G, R, B |
| comma delimiter | 1 | 1 | S | , |
| TOS (Type of Service) | 4 | 100 | ANS | 1st Character 1 = Business 2 = Residence 3 = Government (Federal) 4 = Coin 5 = Home Office 2nd Character C = Coin E = Centrex H = BRI-ISDN J = PBX-trunk K = PRI-ISDN P = Data Voice split line R = Data voice shared line 1 = Circuit Analog 2 = Circuit Digital less then 1.5 Mbps 3 = Circuit Digital greater than 1.5 Mbps 4 = Switch 56/Dial Up Data 5 = Both DID/PBX 6 = DID 7 = Centrex based / BRI-ISDN 8 = POTS - = Not Applicable 3rd Character* M = Measured Rate F = Flat Rate G = Message Per Minute POTS - = Not Applicable 4th Character* F = Foreign Exchange Service G = Semi Public P = Prison Inmate R = Remote Call Forwarding S = 800 Service W = WATS Y = Digital Trunk Z = Wholesale Number Retention - = Not Applicable |
| comma delimiter | 1 | 1 | S | , |
| PROV_METHOD (Market Segment) | 1 | 60 | ANS | A,B,C,E,F,J,K,M,P,R,S,T,U,V,W,X,Y,Z,2,3 |
| comma delimiter | 1 | 1 | S | , |
| FID | 2--10 | 200 | ANS | C /HTG |
| comma delimiter | 1 | 1 | S | , |
| LSR_FIELD | 2-10 | 350 | ANS | R ECCKT |
| comma delimiter | 1 | 1 | S | , |
| SPEC_IND | 1 | 1 | AN | U, L, F |
| comma delimiter | 1 | 1 | S | , |
| ACCT LINE_FEATURE | 1 | 1 | A | L, A, B |
| comma delimiter | 1 | 1 | S | , |
| CONDITIONS | 1-1000 | 1000 | ANS |  |
| comma delimiter | 1 | 1 | S | , |
| COMMENTS | 1-1000 | 1000 | ANS |  |

STATUS:  Indicate the STATUS of the USOC in this column.

Valid Entries:

Y= Valid for ordering on an LSR

N = Not a Valid Code—Cannot enter on an LST for any Wholesale or Retail order.

G = Grandfathered - can enter on a migration request only.

R = Retail Only - cannot enter on an LSR

B = Billing Only - cannot enter on an LSR - MOG or a Service Rep can populate on service orders.

P = Provisioning Only - Can enter on a migration LSR if present on an existing account, but not on a new activity - This will

be completed internally by AT&T 12-State.

SPEC IND Indicate in this column the SPECial INDicators

Valid Entries:

U == USOC

L = Line Assignable USOC

F = FID

TOS (Type of Service)	* 3rd and 4th characters are only completed if available.  If not available, the values will not be populated.

ACCOUNT LINE FEATURE: Indicate Account Feature, Line Feature or Both in this column

Valid Entries:

L = Line Feature (Res/Bus)

A = Account Feature

B = Both Line and Account Feature

FILE NAME --- USOC/FIDS 	(AT&T West Region)

Provide a list of the USOC/FIDS for each region down to the state level.

| Field_Name | Data_Length | Max Char Length | Data_Type | Comments or Example of Data, not format |
| --- | --- | --- | --- | --- |
| REGION | 2-5 | 5 | ANS | AT&T Midwest Region, AT&T Connecticut, AT&T Southwest Region, AT&T West Region |
| comma delimiter | 1 | 1 | S | , |
| STATE | 2-4 | 4 | AN | CT, IL, TX, OK, CA |
| comma delimiter | 1 | 1 | S | , |
| USOC | 2-10 | 10 | ANS | AEV, 1FB, FPSVE, AS3DL |
| comma delimiter | 1 | 1 | S | , |
| USOC_DESC | 1- 350 | 350 | ANS | Text Description to 350 Char |
| comma delimiter | 1 | 1 | S | , |
| Class of Service Indicator | 1 | 1 | A | Y = Yes , N = No |
| comma delimiter | 1 | 1 | S | , |
| PRODUCT_FAMILY | 1-50 | 50 | AN | COIN, ISDN DIRECT |
| comma delimiter | 1 | 1 | S | , |
| STATUS | 1 | 1 | AN | Y, G, R, B |
| comma delimiter | 1 | 1 | S | , |
| TOS (Type of Service) | 4 | 100 | ANS | 1st Character 1 = Business 2 = Residence 3 = Government (Federal) 4 = Coin 5 = Home Office 2nd Character C = Coin E = Centrex H = BRI-ISDN J = PBX-trunk K = PRI-ISDN P = Data Voice split line R = Data voice shared line 1 = Circuit Analog 2 = Circuit Digital less then 1.5 Mbps 3 = Circuit Digital greater than 1.5 Mbps 4 = Switch 56/Dial Up Data 5 = Both DID/PBX 6 = DID 7 = Centrex based / BRI-ISDN 8 = POTS - = Not Applicable 3rd Character* M = Measured Rate F = Flat Rate G = Message Per Minute POTS - = Not Applicable 4th Character* F = Foreign Exchange Service G = Semi Public P = Prison Inmate R = Remote Call Forwarding S = 800 Service W = WATS Y = Digital Trunk Z = Wholesale Number Retention - = Not Applicable |
| comma delimiter | 1 | 1 | S | , |
| PROV_METHOD (Market Segment) | 1 | 60 | ANS | A,B,C,E,F,J,K,M,P,R,S,T,U,V,W,X,Y,Z,2,3 |
| comma delimiter | 1 | 1 | S | , |
| FID | 2--10 | 200 | ANS | C /HTG |
| comma delimiter | 1 | 1 | S | , |
| LSR_FIELD | 2-10 | 350 | ANS | R ECCKT |
| comma delimiter | 1 | 1 | S | , |
| SPEC_IND | 1 | 1 | AN | U, L, F |
| comma delimiter | 1 | 1 | S | , |
| ACCT LINE_FEATURE | 1 | 1 | A | L, A, B |
| comma delimiter | 1 | 1 | S | , |
| CONDITIONS | 1-1000 | 1000 | ANS |  |
| comma delimiter | 1 | 1 | S | , |
| COMMENTS | 1-1000 | 1000 | ANS |  |

STATUS:  Indicate the STATUS of the USOC in this column.

Valid Entries:

Y= Valid for ordering on an LSR

N = Not a Valid Code—Cannot enter on an LST for any Wholesale or Retail order.

G = Grandfathered - can enter on a migration request only.

R = Retail Only - cannot enter on an LSR

B = Billing Only - cannot enter on an LSR - MOG or a Service Rep can populate on service orders.

P = Provisioning Only - Can enter on a migration LSR if present on an existing account, but not on a new activity - This will

be completed internally by AT&T 12-State.

SPEC IND Indicate in this column the SPECial INDicators

Valid Entries:

U == USOC

L = Line Assignable USOC

F = FID

TOS (Type of Service)	* 3rd and 4th characters are only completed if available.  If not available, the values will not be populated.

ACCOUNT LINE FEATURE: Indicate Account Feature, Line Feature or Both in this column

Valid Entries:

L = Line Feature (Res/Bus)

A = Account Feature

B = Both Line and Account Feature

FILE NAME ---Community Name File 	(AT&T West Region)

Provide a list of Community Names and the abbreviations.

| Field_Name | Data_Length | Maximum Char Length | Data_Type | Comments |
| --- | --- | --- | --- | --- |
| State | 2 | 2 | A | CA |
| Comma Delimiter | 1 | 1 | S | , |
| Community Name Full Spelling | 1-45 | 45 | ANS | AETNA SPRINGS |
| Comma Delimiter | 1 | S | 46 | , |
| Community Name Abbreviation | 1-25 | 25 | ANS | AETNA SPGS |

FILE NAME --- Yellow Page Headings 	(AT&T West Region)

Header Section:

| Header_Field_Name | Data_Length | Max_Char_Length | Data_Type | Comments/Example of Data/Not Format |
| --- | --- | --- | --- | --- |
| File Name | 8 | 8 | A | WESTHEAD |
| Application Name | 3 | 3 | A | CSS |
| Effective Date | 8 | 8 | N | Format: MMDDYYYY Actual: 01102007 |

Record Section:

| Field_Name | Data_Length | Max Char Length | Data_Type | Comments or Example of Data, not format |
| --- | --- | --- | --- | --- |
| Yellow Page Code | 6 | 6 | N | 107788 |
| Comma Delimiter | 1 | 1 | S | , |
| Yellow Page Heading Name | 1-100 | 100 | ANS | Chiropractic-Doctors of Chiropractic (D.C.) |
| Comma Delimiter | 1 | 1 | S | , |
| Yellow Page Heading Abbreviation | 1-32 | 32 | ANS | Chiro Drs Of Chiro (D.C.) |
| Comma Delimiter | 1 | 1 | S | , |
| Heading Type Code | 1 | 1 | A | B=Bus to Bus, C=Consumer, D=Both |
| Comma Delimiter | 1 | 1 | S | , |
| Standard Industrial Classification (SIC) | 4 | 4 | N | 8041 |
| Comma Delimiter | 1 | S | S | , |
| Structure 4 Code | 4 | 4 | AN | EDLZ |

Trailer Section:

| Trailer_Field_Name | Data_Length | Max_Char_Length | Data_Type | Comments/Example of Data/Not Format |
| --- | --- | --- | --- | --- |
| Record Count | 7 | 7 | N | Fixed length with leading zeros. Average Number of Yellow Page Headings are in the 8,500’s and the file is always a full replace. |

FILE NAME ---PIC/LPIC 	(AT&T West Region)

Produce a file containing a list of the PIC (InterLATA Pre Subscription Indicator Code) and LPIC (IntraLATA Pre Subscription Indicator Code) codes.

| Field_Name | Data_Length | Max Character Length | Data_Type | Comments |
| --- | --- | --- | --- | --- |
| State | 2 | 2 | A | CA, NV |
| Comma Delimiter | 1 | 1 | S | , |
| PIC (CIC code) | 1-4 | 4 | N |  |
| Comma Delimiter | 1 | 1 | S | , |
| LPIC (CIC code) | 1-4 | 4 | N |  |
| Comma Delimiter | 1 | 1 | S | , |
| ACNA | 1-3 | 3 | AN |  |
| Comma Delimiter | 1 | 1 | S |  |
| ACNADES | 1-35 | 35 | A/N/S | Carrier Name |
| Comma Delimiter | 1 | 1 | S | , |
| LST (Local Service Termination )-(CLLI) | 1-11 | 11 | AN |  |
| Comma Delimiter | 1 | 1 | S | , |
| TOS (Type of Service) | 1 | 1 | A | R= Residence |
|  |  |  |  | B=Business |
|  |  |  |  | C=Coin |
| Comma Delimiter | 1 | 1 | S | , |
| Carrier Authorization | 1-30 | 30 | AS | Y = YES N = NO |

FILE NAME ---   North Alternate Community Name File 	(AT&T West Region)

Provide a list of Community Names and the alternate Community names.

| Field_Name | Data_Length | Max Char Length | Data_Type | Comments |
| --- | --- | --- | --- | --- |
| SAGA | 1–12 | 12 | A | BAY |
| Comma Delimiter | 1 | 1 | S | , |
| Community Name | 1-32 | 32 | AS | Crystal |
| Comma Delimiter | 1 | 1 | S | , |
| Alternate Community Name | 1-32 | 32 | AS | AMARGOSA VLY |
| Comma Delimiter | 1 | 1 | S | , |
| NPA | 3 | 3 | N | 775 |
| Comma Delimiter | 1 | 1 | S | , |
| ZIP | 5 | 5 | N | 89041 |

Definitions:

Community Name is the prestige name for a listed address.

Alternate Community Name is the postal address or the service address.

FILE NAME ---  South Alternate Community Name File 	(AT&T West Region)

Provide a list of Community Names and the alternate Community names.

| Field_Name | Data_Length | Max Char Length | Data_Type | Comments |
| --- | --- | --- | --- | --- |
| SAGA | 1–12 | 12 | A | LAN |
| Comma Delimiter | 1 | 1 | S | , |
| Community Name | 1-32 | 32 | AS | Crystal |
| Comma Delimiter | 1 | 1 | S | , |
| Alternate Community Name | 1-32 | 32 | AS | AMARGOSA VLY |
| Comma Delimiter | 1 | 1 | S | , |
| NPA | 3 | 3 | N | 775 |
| Comma Delimiter | 1 | 1 | S | , |
| ZIP | 5 | 5 | N | 89041 |

Definitions:

Community Name is the prestige name for a listed address.

Alternate Community Name is the postal address or the service address.

### AT&T Southwest Region

|  | AT&T Southwest Region |
| --- | --- |
| SAG | Flat |
| Feature Availability | Comma Delimited |
| Directory Names | Comma Delimited |
| Class of Service | Comma Delimited |
| USOC/FID | Comma Delimited |
| Community Name | Comma Delimited |
| Yellow Page Headings | Comma Delimited |
| PIC/LPIC | Comma Delimited |

FILE NAME ---SAG File 	(AT&T Southwest Region)

Header Record Layout

| Field Name | Data Length | Data Type | Position | Comments |
| --- | --- | --- | --- | --- |
| HDR1 | 3 | ANS | 1-3 | Header indicator |
| Date-Time | 14 | ANS | 4-17 | Date and time the file was created |
| Filler | 233 | ANS | 18-250 |  |

Detail Record Layout

| Field Name | Data Length | Data Type | Position | Comments |
| --- | --- | --- | --- | --- |
| Addr type | 1 | ANS | 1 | Type of range record |
| Community-req | 1 | ANS | 2 | Address range indicator |
| Directional | 2 | ANS | 3-4 | E, W, S, N, SW, NE, SE, NW |
| Street name | 50 | ANS | 5-54 | Street name |
| Low range | 8 | ANS | 55-62 | Low street range |
| High range | 8 | ANS | 63-70 | High street range |
| Odd-even | 1 | ANS | 71 | Odd or Even street ranges |
| Community | 32 | ANS | 72-103 | Community name |
| Exch-code | 4 | ANS | 104-107 | Exchange code |
| State | 2 | ANS | 108-109 | Abbreviation of the state |
| SAGA | 4 | ANS | 110-113 | Street Address Guide Area |
| TTA | 3 | ANS | 114-116 | Terminating Telephone area |
| Tax-code | 6 | ANS | 117-122 | Tax type levied on phone service |
| ALT-ind | 1 | ANS | 123 | Primary or alternate address range |
| GSG | 4 | ANS | 124-127 | Geographic Segment |
| ZIP-Code | 5 | ANS | 128-132 | Postal Zone |
| Rate-Zone | 5 | ANS | 133-137 | Rate zone type |
| Wire Center | 8 | ANS | 138-145 | 8 character wirecenter name e.g. SNFCCA11 |
| NPA | 3 | ANS | 146-148 | Number Plan Area |
| Tax-ind | 1 | ANS | 149 | Tax code region |
| ESN | 3 | ANS | 150-152 | Emergency Service Number (not applicable AT&T California) |
| ADNC | 4 | ANS | 153-156 | Address Name Code |
| Num-Srt | 10 | ANS | 157-166 | Street Name, only if it’s numeric |
| PD | 9 | ANS | 167-175 | Plant Installation District |
| Filler | 75 | ANS | 176-250 |  |

(Record Size will be 250 bytes)

For the SAGA Field, values may change at any given time. For the most current values that are returned, the SAGA Information Guide should be referenced that is available on CLEC Online. To access the SAGA Information Guide, which is on CLEC online web site at https://clec.att.com/clec, use the following steps:

- Select CLEC HANDBOOK

- Select Handbook State (Top of screen)

- Select Guides / Tech Pubs

- Address Information

- SAG Information Guide

FILE NAME ---Feature Availability File 	(AT&T Southwest Region)

Provides a list of the wholesale features that are available in each switch in USOC format with the English description.

| Field_Name | Data_Length | Max Char Length | Data_Type | Comments |
| --- | --- | --- | --- | --- |
| Header | 1-45 | 45 | AN | EASE AVAILABLE PRODS and date and time the file was created. |

| Field_Name | Data_Length | Max Char Length | Data_Type | Comments |
| --- | --- | --- | --- | --- |
| State | 2-4 | 4 | AN | MO |
| Comma Delimiter | 1 | 1 | S | , |
| LST (CLLI) Local Service Termination | 1-11 | 11 | ANS | STLSMO01DSA |
| Comma Delimiter | 1 | 1 | S | , |
| FEATURE (USOC) | 3-6 | 6 | ANS | ESM |
| Comma Delimiter | 1 | 1 | S | , |
| FEATURE DES (English Description) | 1-50 | 50 | ANS | Call Forwarding |
| Comma Delimiter | 1 | 1 | S | , |
| MS (Market Segment) Indicator | 1 | 1 | A | R=Resale |
| Comma Delimiter | 1 | 1 | S | , |
| SWITCH TYPE | 1-10 | 10 | AN | DMH |
| Comma Delimiter | 1 | 1 | S | , |
| TOS (Type of Service) | 1 | 1 | N | B=Bus, R=Res |

The AT&T Southwest Region feature files, due to their size, will be broken down by state when accessed via any of the interfaces,  Direct Connect (NDM), GUI (Verigate), or the CLEC online web site.

The Feature file names and their description will appear as listed below.

File Name		Description

HCOFEAT.TXT	Feature Availability by Switch Arkansas

LCOFEAT.TXT	Feature Availability by Switch Kansas

CCOFEAT.TXT	Feature Availability by Switch Missouri

RCOFEAT.TXT 	Feature Availability by Switch Oklahoma

TCOFEAT.TXT 	Feature Availability by Switch Dallas Texas

NCOFEAT.TXT 	Feature Availability by Switch Houston Texas

XCOFEAT.TXT 	Feature Availability by Switch San Antonio Texas

FILE NAME --- Directory Names 	( AT&T Southwest Region)

Provide a list of Directory Names, the towns and communities served by that directory.

| Field Name | Data Length | Max Char Length | Data Type | Comments |
| --- | --- | --- | --- | --- |
| State | 2-4 | 4 | AN | AR |
| Comma Delimiter | 1 | 1 | S | , |
| Directory Name | 1-35 | 35 | AN | BATESVILLE |
| Comma Delimiter | 1 | 1 | S | , |
| Directory Subsection (Towns & Communities) | 1-25 | 25 | ANS | Cave City |
| Comma Delimiter | 1 | 1 | S | , |
| YPIMA Code | 1-6 | 6 | N | 004052 |

FILE NAME ---Class of Service (CLS)  (AT&T Southwest Region)

Provide a list of the Class of Service and an English Description

| Field_Name | Data_Length | Max Char Length | Data_Type | Comments or Example of Data, not format |
| --- | --- | --- | --- | --- |
| REGION | 2-5 | 5 | ANS | AT&T Midwest Region, AT&T Connecticut, AT&T Southwest Region, AT&T West Region |
| comma delimiter | 1 | 1 | S | , |
| STATE | 2-4 | 4 | AN | CT, IL, TX, OK, CA |
| comma delimiter | 1 | 1 | S | , |
| USOC | 2-10 | 10 | ANS | AEV, 1FB, FPSVE, AS3DL |
| comma delimiter | 1 | 1 | S | , |
| USOC_DESC | 1- 350 | 350 | ANS | Text Description to 350 Char |
| comma delimiter | 1 | 1 | S | , |
| PRODUCT_FAMILY | 1-50 | 50 | AN | COIN, ISDN DIRECT |
| comma delimiter | 1 | 1 | S | , |
| STATUS | 1 | 1 | AN | Y, G, R, B |
| comma delimiter | 1 | 1 | S | , |
| TOS (Type of Service) | 4 | 100 | ANS | 1st Character 1 = Business 2 = Residence 3 = Government (Federal) 4 = Coin 5 = Home Office 2nd Character C = Coin E = Centrex H = BRI-ISDN J = PBX-trunk K = PRI-ISDN P = Data Voice split line R = Data voice shared line 1 = Circuit Analog 2 = Circuit Digital less then 1.5 Mbps 3 = Circuit Digital greater than 1.5 Mbps 4 = Switch 56/Dial Up Data 5 = Both DID/PBX 6 = DID 7 = Centrex based / BRI-ISDN 8 = POTS - = Not Applicable 3rd Character* M = Measured Rate F = Flat Rate G = Message Per Minute POTS - = Not Applicable 4th Character* F = Foreign Exchange Service G = Semi Public P = Prison Inmate R = Remote Call Forwarding S = 800 Service W = WATS Y = Digital Trunk Z = Wholesale Number Retention - = Not Applicable |
| comma delimiter | 1 | 1 | S | , |
| PROV_METHOD (Market Segment) | 1 | 60 | ANS | A,B,C,E,F,J,K,M,P,R,S,T,U,V,W,X,Y,Z,2,3 |
| comma delimiter | 1 | 1 | S | , |
| FID | 2--10 | 200 | ANS | C /HTG |
| comma delimiter | 1 | 1 | S | , |
| LSR_FIELD | 2-10 | 350 | ANS | R ECCKT |
| comma delimiter | 1 | 1 | S | , |
| SPEC_IND | 1 | 1 | AN | U, L, F |
| comma delimiter | 1 | 1 | S | , |
| ACCT LINE_FEATURE | 1 | 1 | A | L, A, B |
| comma delimiter | 1 | 1 | S | , |
| CONDITIONS | 1-1000 | 1000 | ANS |  |
| comma delimiter | 1 | 1 | S | , |
| COMMENTS | 1-1000 | 1000 | ANS |  |

STATUS:  Indicate the STATUS of the USOC in this column.

Valid Entries:

Y= Valid for ordering on an LSR

N = Not a Valid Code—cannot enter on an LST for any Wholesale or Retail order.

G = Grandfathered - can enter on a migration request only.

R = Retail Only - cannot enter on an LSR

B = Billing Only - cannot enter on an LSR - MOG or a Service Rep can populate on service orders.

P = Provisioning Only - Can enter on a migration LSR if present on an existing account, but not on a new activity - This will

be completed internally by AT&T 12-State.

SPEC IND Indicate in this column the SPECial INDicators

Valid Entries:

U == USOC

L = Line Assignable USOC

F = FID

TOS (Type of Service)	* 3rd and 4th characters are only completed if available.  If not available, the values will not be populated.

ACCOUNT LINE FEATURE: Indicate Account Feature, Line Feature or Both in this column

Valid Entries:

L = Line Feature (Res/Bus)

A = Account Feature

B = Both Line and Account Feature

FILE NAME ---USOC/FIDS  (AT&T Southwest Region)

Provide a list of the USOC/FIDS for each region down to the state level.

| Field_Name | Data_Length | Max Char Length | Data_Type | Comments or Example of Data, not format |
| --- | --- | --- | --- | --- |
| REGION | 2-5 | 5 | ANS | AT&T Midwest Region, AT&T Connecticut, AT&T Southwest Region, AT&T West Region |
| comma delimiter | 1 | 1 | S | , |
| STATE | 2-4 | 4 | AN | CT, IL, TX, OK, CA |
| comma delimiter | 1 | 1 | S | , |
| USOC | 2-10 | 10 | ANS | AEV, 1FB, FPSVE, AS3DL |
| comma delimiter | 1 | 1 | S | , |
| USOC_DESC | 1- 350 | 350 | ANS | Text Description to 350 Char |
| comma delimiter | 1 | 1 | S | , |
| Class of Service Indicator | 1 | 1 | A | Y = Yes , N = No |
| comma delimiter | 1 | 1 | S | , |
| PRODUCT_FAMILY | 1-50 | 50 | AN | COIN, ISDN DIRECT |
| comma delimiter | 1 | 1 | S | , |
| STATUS | 1 | 1 | AN | Y, G, R, B |
| comma delimiter | 1 | 1 | S | , |
| TOS (Type of Service) | 2 | 100 | ANS | 1st Character 1 = Business 2 = Residence 3 = Government (Federal) 4 = Coin 5 = Home Office 2nd Character C = Coin E = Centrex H = BRI-ISDN J = PBX-trunk K = PRI-ISDN P = Data Voice split line R = Data voice shared line 1 = Circuit Analog 2 = Circuit Digital less then 1.5 Mbps 3 = Circuit Digital greater than 1.5 Mbps 4 = Switch 56/Dial Up Data 5 = Both DID/PBX 6 = DID 7 = Centrex based / BRI-ISDN 8 = POTS - = Not Applicable 3rd Character* M = Measured Rate F = Flat Rate G = Message Per Minute POTS - = Not Applicable 4th Character* F = Foreign Exchange Service G = Semi Public P = Prison Inmate R = Remote Call Forwarding S = 800 Service W = WATS Y = Digital Trunk Z = Wholesale Number Retention - = Not Applicable |
| comma delimiter | 1 | 1 | S | , |
| PROV_METHOD (Market Segment) | 1 | 60 | ANS | A,B,C,E,F,J,K,M,P,R,S,T,U,V,W,X,Y,Z,2,3 |
| comma delimiter | 1 | 1 | S | , |
| FID | 2--10 | 200 | ANS | C /HTG |
| comma delimiter | 1 | 1 | S | , |
| LSR_FIELD | 2-10 | 350 | ANS | R ECCKT |
| comma delimiter | 1 | 1 | S | , |
| SPEC_IND | 1 | 1 | AN | U, L, F |
| comma delimiter | 1 | 1 | S | , |
| ACCT LINE_FEATURE | 1 | 1 | A | L, A, B |
| comma delimiter | 1 | 1 | S | , |
| CONDITIONS | 1-1000 | 1000 | ANS |  |
| comma delimiter | 1 | 1 | S | , |
| COMMENTS | 1-1000 | 1000 | ANS |  |

STATUS:  Indicate the STATUS of the USOC in this column.

Valid Entries:

Y= Valid for ordering on an LSR

N = Not a Valid Code—Cannot enter on an LST for any Wholesale or Retail order.

G = Grandfathered - can enter on a migration request only.

R = Retail Only - cannot enter on an LSR

B = Billing Only - cannot enter on an LSR - MOG or a Service Rep can populate on service orders.

P = Provisioning Only - Can enter on a migration LSR if present on an existing account, but not on a new activity - This will

be completed internally by AT&T 12-State.

SPEC IND Indicate in this column the SPECial INDicators

Valid Entries:

U == USOC

L = Line Assignable USOC

F = FID

TOS (Type of Service)	* 3rd and 4th characters are only completed if available.  If not available, the values will not be populated.

ACCOUNT LINE FEATURE: Indicate Account Feature, Line Feature or Both in this column

Valid Entries:

L = Line Feature (Res/Bus)

A = Account Feature

B = Both Line and Account Feature

FILE NAME ---Community Name File 	(AT&T Southwest Region)

Provide a list of Community Names and the abbreviations

| Field_Name | Data_Length | Maximum Char Length | Data_Type | Comments |
| --- | --- | --- | --- | --- |
| State | 2 | 2 | A | AR |
| Comma Delimiter | 1 | 1 | S | , |
| Community Name Full Spelling | 1-45 | 45 | A | Aberdeen |
| Comma Delimiter | 1 | 1 | S | , |
| Community Name Abbreviation | 1-25 | 25 | A | Aberdeen |

FILE NAME --- Yellow Page Headings 	(AT&T Southwest Region)

Provide a list of the yellow page headings for the region/state selected.

| Field_Name | Data_Length | Data_Type | Position | Comments |
| --- | --- | --- | --- | --- |
| State | 2-4 | AN | 1-4 |  |
| Comma Delimiter | 1 | S | 5 | , |
| Yellow Page Code | 4-8 | AN | 6-13 | SECURE |
| Comma Delimiter | 1 | S | 14 | , |
| Standard Industrial Classification (SIC) | 4-6 | N | 15-20 | Blank |
| Comma Delimiter | 1 | S | 21 | , |
| Yellow Page Heading Text | 1-200 | ANS | 22-221 | Blank |
| Comma Delimiter | 1 | S | 222 | , |
| Yellow Page Heading Abbreviation | 40 | ANS | 223-262 | Blank |
| Comma Delimiter | 1 | S | 263 | , |
| Directory Type Code | 1 | ANS | 264 | Blank |

FILE NAME ---PIC/LPIC 	(AT&T Southwest Region)

Produce a file containing a list of the PIC (InterLATA Pre Subscription Indicator Code) and LPIC (IntraLATA Pre Subscription Indicator Code) codes.

| Field_Name | Data_Length | Maximum Char Length | Data_Type | Comments |
| --- | --- | --- | --- | --- |
| State | 2-4 | 4 | AN | MO |
| Comma Delimiter | 1 | 1 | S | , |
| PIC (CIC code) | 4 | 4 | N | 1234 |
| Comma Delimiter | 1 | 1 | S | , |
| LPIC (CIC code) | 4 | 4 | N | 5678 |
| Comma Delimiter | 1 | 1 | S | , |
| ACNA | 3 | 3 | AN | CCC |
| Comma Delimiter | 1 | 1 | S | , |
| ACNADES | 1-35 | 35 | A/N/S | Carrier Name |
| Comma Delimiter | 1 | 1 | S | , |
| LST (Local Service Termination )-(CLLI) | 1-11 | 11 | ANS | ADRNMOAXRS0 |
| Comma Delimiter | 1 | 1 | S | , |
| TOS (Type of Service) | 1 | 1 | AN | Blank |

Note:  Each individual piece of Data with in the ACNADES field will be surrounded by double quotes “ “.

The double quotes will add 2 bytes to the field length of 35 characters