CLCI S/S– Serial Number Format Service Codes and Modifiers

Standard Definition:

| Prefix | . | Service Code | Modifier | . | Serial Number | . | Suffix | . | Company Assigning Circuit Identification | . | Segment |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 2 |  | 3 | 4 | 5 | 6 |  | 7 | 8 | 9 | 10 | 11 | 12 |  | 13 | 14 | 15 |  | 16 | 17 | 18 | 19 |  | 20 | 21 | 22 |

- Character positions 1 and 2 – Prefix ~ These two positions are locally assigned by AT&T and represent locally assigned logic including exchanges/regions, etc. (Not addressed in this document).

- Character positions 3 and 4 – Service Code ~ these two positions comprise a two-character alphanumeric field called the Service Code.  This code describes specific services provided to a customer.  Functionality identified with a service code may include the following:

  - *Jurisdiction (Access Vs Non-Access)	* Transmission Parameters	* Digital Services

  - * Types of Facilities		* Analog Services		* Optical Services

  - *Bandwidth Services		*Technology (as a service)

- Character positions 5 and 6 – Modifiers ~ these two positions have been combined to make a single two-character data field.  The Modifier provides additional information that pertains to the jurisdiction and technical optional features, e.g., channelized service, Clear Channel Capability (CCC) (CCC), or a Parameter only offering.   Modifiers are Flexible, with the definitions not applicable to all Service Codes.

- Characters 7-15 (Locally assigned and not covered in this Document as part of CL)

- Characters 16-19 (Company code uses IAC or EC codes per the CLCI S/S BR and Not covered in this Document)

- Characters 20-22 (Locally assigned and not covered in this Document as part of CL)

Sample CLCI S/S Circuit ID = 04/DHXO/987653//SW

- SPECIAL NOTE: The codes listed in this TAB are the codes that AT&T plans to use on a going forward basis.  Customers are encouraged to utilize these codes.  Many codes that are still reflected in the Tariffs or M&Ps are no longer nationally recognized as valid.  There may be a “Lag” time or “Advance” time between the documentation in the CCGs and when all other M&Ps and system changes or Client Notifications can be / are made.  AT&T is committed to the use of valid Nationally Standard COMMON LANGUAGE® (CL) codes when possible.  Due to needs of the business, we may at times utilize non-standard coding.  We regret any inconvenience this may cause our Customers and Business Partners.  Our goal is fully to continue to work towards a consistent use of nationally standard CL codes possible, while continuing to meet AT&T's overall business needs.  Additionally, due to different implementation dates for various products, some codes contained in this document may reflect products with future implementation dates.  Please see Product Announcements, Accessible Letters, or your Account Manager for actual product availability.

- AT&T West region has limited its use of the Non-Access Private Line CLCI S/S codes because of the Standard Serving Arrangement (SSA) effort in the ‘90s.   Many of these services are identified with Access Service codes found in TAB 11.   Throughout this document, if there is a “#” in the left-hand column with the Service Code and Modifier, this indicates the non-Access code is not used in AT&T’s West region (probably covered in the Access arena).

- In the past the 5th position modifier of “R” was used erroneously.    The “R” should be replaced with one of the other valid codes found in this TAB.   Questions from external clients may be directed to your Account Managers, and for internal AT&T employees please contact the AT&T Operations Inc. CL Coordinator, (Diane Fletcher (df1685@att.com) or (770-650-5841)

- Due to complex coding rules, the entire CLCI S/S Circuit ID should be read for uniqueness when assigning or tracking a circuit.

- All modifiers listed in TABs 11 and 12 are intrastate in jurisdiction unless otherwise noted within the modifier definition.

- A Temporary Addendum has been added to the end of this TAB to include the appropriate Standard CLCI S/S coding used by Domestic Legacy AT&T (cT). We will gradually be incorporating standardized CL Coding used by Legacy AT&T as we continue with the merger integration process and implement combined projects.

Private Line services:

##### Valid Service Code and Modifier Combinations

| Service Code and Modifier | Service Code Description | Modifier Descriptions |
| --- | --- | --- |
| ADXS # (Not valid in Southeast) | Attendant - Provides interconnection between an AT&T Centrex switch and a customer’s attendant equipment. | Customer/provider interface. |
| ADXZ # (Not valid in Southeast) | Attendant - Provides interconnection between an AT&T Centrex switch and a customer’s attendant equipment. | Official company service (OCS). |
| AFXX (Only in Southwest and West) | Commercial Audio (Full Time) - A program-grade circuit used in the transmission of audio signals for full-time radio broadcasting. | No further parameters. |
| AGXU (Not valid in Southeast) | Digital Subscriber Line (DSL) – Convertible subscriber rates. | Unbundled. |
| AIXS # (Not valid in Southeast) | Automatic Identified Outward Dialing - Provides a connection from a Centrex or PBX to a switching machine to identify outward dialed calls by the line number of an originating station. | Customer/provider interface. |
| ANXZ # (Not valid in Southeast) | Announcement Services - A voice-grade circuit between a central office and a recorded announcement or voice messaging system. It is used to provide access from the switched message network. The sponsor can be other than the telephone company. | Official company service (OCS). |
| BAPX # (Not valid in Southeast) | Protective Alarm (DC Interface at Customer Premises) - Provides a channel for an alarm system. The alarm points may be arranged in series or parallel configurations. | Parameter only offering under an intrastate restructured private line (RPL) tariff. |
| CLXS # (Not valid in Southeast) | CENTREX CO Line - Provides a direct connection from a Centrex unit located on a telephone company premises to a station located on the customer premises. | Customer/provider interface. |
| CLXZ # (Not valid in Southeast) | CENTREX CO Line - Provides a direct connection from a Centrex unit located on a telephone company premises to a station located on the customer premises. | Official company service (OCS). |
| CUXM (Not valid in Southeast) | Metro Ethernet Virtual Connections (EVC/OVC) - Identifies a Metro Ethernet Virtual Connection or an Operator Virtual Connection (An association of two or more Physical Ethernet Access Links). | Multipoint-to-Multipoint (Future Offering). |
| CUXP (Not valid in Southeast) | Metro Ethernet Virtual Connections (EVC/OVC) - Identifies a Metro Ethernet Virtual Connection or an Operator Virtual Connection (An association of two or more Physical Ethernet Access Links). | Point-to-Point. |
| CSXG | Channel Service - Provides a channel which has the capacity of transmitting up to 30 baud. The channel does Not have access to the switched message network. | Enhanced 911 (E911). |
| DCJX # (Not valid in Southeast) | Digital Data 64Kbps - Provides for the transmission of digital transport at a rate of 64Kbps (can be used for ISDN “B” Channels) | Channelized service with customer control. |
| DCJZ # (Not valid in Southeast) | Digital Data 64Kbps - Provides for the transmission of digital transport at a rate of 64Kbps (can be used for ISDN “B” Channels). | Channelized service with customer control. Official company service (OCS). |
| DCXU (Not valid in Southeast) | Digital Data 64Kbps - Provides for the transmission of digital transport at a rate of 64Kbps (can be used for ISDN “B” Channels). | Unbundled. |
| DCXX # | Digital Data 64Kbps - Provides for the transmission of digital transport at a rate of 64Kbps (can be used for ISDN “B” Channels). | No further parameters. |
| DDXS (Only in Southwest) | Direct Dial – Alternative Design – A voice-grade circuit between a Centrex PBX, or system providing similar functions and a central office. It is used for completion of direct-in-dial traffic. This service code will be used for the alternate design parameters. | Customer/provider interface. |
| DDXU # (Not valid in Southeast) | Direct Dial – Alternative Design – A voice-grade circuit between a Centrex PBX, or system providing similar functions and a central office. It is used for completion of direct-in-dial traffic. This service code will be used for the alternate design parameters. | Unbundled. |
| DDXX # (Not valid in Southeast) | Direct Dial – Alternative Design – A voice-grade circuit between a Centrex PBX, or system providing similar functions and a central office. It is used for completion of direct-in-dial traffic. This service code will be used for the alternate design parameters. | No further parameters. |
| DHMX (Only in Southeast) | Digital Service - Provides for two points of private-line digital transport transmission operating at a speed of 1.544 Mbps. | Channeled service. |
| DHXB (Only in Midwest) | Digital Service - Provides for two points of private-line digital transport transmission operating at a speed of 1.544 Mbps. | Rebundled. Note: Limited offering please verify availability in your region via the Product announcements. |
| DHXE # | Digital Service - Provides for two points of private-line digital transport transmission operating at a speed of 1.544 Mbps. | Customer reconfigurable. |
| DHXO | Digital Service - Provides for two points of private-line digital transport transmission operating at a speed of 1.544 Mbps. | Enhanced 911 (E911). |
| DHXS # (Not valid in Southeast) | Digital Service - Provides for two points of private-line digital transport transmission operating at a speed of 1.544 Mbps. | Customer/provider interface. |
| DHXU (Only in Midwest) | Digital Service - Provides for two points of private-line digital transport transmission operating at a speed of 1.544 Mbps. | Unbundled. |
| DHXX # | Digital Service - Provides for two points of private-line digital transport transmission operating at a speed of 1.544 Mbps. | No further parameters. |
| DHXZ | Digital Service - Provides for two points of private-line digital transport transmission operating at a speed of 1.544 Mbps. | Official company service (OCS). |
| DHZS (Not valid in Southeast) | Digital Service - Provides for two points of private-line digital transport transmission operating at a speed of 1.544 Mbps. | Clear Channel Capability (CCC) Customer/provider interface. |
| DHZX | Digital Service - Provides for two points of private-line digital transport transmission operating at a speed of 1.544 mbps. | Clear Channel Capability (CCC) |
| DHZZ (Not valid in Southeast) | Digital Service - Provides for two points of private-line digital transport transmission operating at a speed of 1.544 Mbps. | Clear Channel Capability (CCC) Official company service (OCS). |
| DIXS # (Not valid in Southeast) | Direct-In-Dial - A voice-grade circuit between a Centrex, PBX or system providing similar functions and a central office. It is used for completion of direct-in-dial traffic. | Customer/provider interface. |
| DIXU # (Not valid in Southeast) | Direct-In-Dial - A voice-grade circuit between a Centrex, PBX or system providing similar functions and a central office. It is used for completion of direct-in-dial traffic. | Unbundled. |
| DIXZ # (Not valid in Southeast) | Direct-In-Dial – A voice-grade circuit between a Centrex, PBX or system providing similar functions and a central office. It is used for completion of direct-in-dial traffic. | Official company service (OCS). |
| DKXS # (Not valid in Southeast) | Data Link - A voice-frequency signaling path used to transfer switching commands and other network data between controls and/or switch units. Examples would be signaling links and may also include modem pooling. | Customer/provider interface. |
| DMXS # (Not valid in Southeast) | Digital Data - 19.2 Kbps - Provides for two or more points of private-line digital transmission operating at a synchronous data speed of 19.2 Kbps. No alternate voice or voice coordination is provided with this service. | Customer/provider interface. |
| DMXZ # (Not valid in Southeast) | Digital Data - 19.2 Kbps - Provides for two or more points of private-line digital transmission operating at a synchronous data speed of 19.2 Kbps. No alternate voice or voice coordination is provided with this service. | Official company service (OCS). |
| DNXS # (Not valid in Southeast) | Direct-Out-Dial – Alternate Design | Customer/provider interface. |
| DNXU # (Not valid in Southeast) | Direct-Out-Dial – Alternate Design | Unbundled. |
| DOXS # (Not valid in Southeast) | Direct-Out-Dial - A voice-grade circuit between a Centrex, PBX or system providing similar functions and a central office. It is used for direct station access to the message network. | Customer/provider interface. |
| DOXZ # (Not valid in Southeast) | Direct-Out-Dial - A voice-grade circuit between a Centrex, PBX or system providing similar functions and a central office. It is used for direct station access to the message network. | Official company service (OCS). |
| DPXS # (Not valid in Southeast) | Digital Data - 2.4 Kbps - Provides for two or more points of private-line digital transmission operating at a synchronous data speed of 2.4 Kbps. No alternate voice or voice coordination is provided with this service. | Customer/provider interface. |
| DPXX (Only in West) | Digital Data - 2.4 Kbps - Provides for two or more points of private-line digital transmission operating at a synchronous data speed of 2.4 Kbps. No alternate voice or voice coordination is provided with this service. | No further parameters required. |
| DPXZ # (Not valid in Southeast) | Digital Data - 2.4 Kbps - Provides for two or more points of private-line digital transmission operating at a synchronous data speed of 2.4 Kbps. No alternate voice or voice coordination is provided with this service. | Official company service (OCS). |
| DQXS # (Not valid in Southeast) | Digital Data - 4.8 Kbps - Provides for two or more points of private-line digital transmission operating at a synchronous data speed of 4.8 Kbps. No alternate voice or voice coordination is provided with this service. | Customer/provider interface. |
| DQXZ # (Not valid in Southeast) | Digital Data - 4.8 Kbps - Provides for two or more points of private-line digital transmission operating at a synchronous data speed of 4.8 Kbps. No alternate voice or voice coordination is provided with this service. | Official company service (OCS). |
| DRXG | Digital Data - 9.6 Kbps - Provides for two or more points of private-line digital transmission operating at a synchronous data speed of 9.6 Kbps. No alternate voice or voice coordination is provided with this service. | Enhanced 911 (E911). |
| DRXS # (Not valid in Southeast) | Digital Data - 9.6 Kbps - Provides for two or more points of private-line digital transmission operating at a synchronous data speed of 9.6 Kbps. No alternate voice or voice coordination is provided with this service. | Customer/provider interface. |
| DRXZ # (Not valid in Southeast) | Digital Data - 9.6 Kbps - Provides for two or more points of private-line digital transmission operating at a synchronous data speed of 9.6 Kbps. No alternate voice or voice coordination is provided with this service. | Official company service (OCS). |
| DWXE # (Not valid in Southeast) | Digital Data - 56 Kbps - Provides for two or more points of private-line digital transmission operating at a synchronous data speed of 56 Kbps. No alternate voice or voice coordination is provided with this service. | Customer reconfigurable. |
| DWXS # (Not valid in Southeast) | Digital Data - 56 Kbps - Provides for two or more points of private-line digital transmission operating at a synchronous data speed of 56 Kbps. No alternate voice or voice coordination is provided with this service. | Customer/provider interface. |
| DWXZ # (Not valid in Southeast) | Digital Data - 56 Kbps - Provides for two or more points of private-line digital transmission operating at a synchronous data speed of 56 Kbps. No alternate voice or voice coordination is provided with this service. | Official company service (OCS). |
| DZJX # (Not valid in Southeast) | 64 Kbps on the 'D' Channel - Provides for digital packets of 64 Kbps on the ISDN "D" channel. | Channelized service with customer control. |
| DZJZ # (Not valid in Southeast) | 64 Kbps on the 'D' Channel - Provides for digital packets of 64 Kbps on the ISDN "D" channel. | Channelized service with customer control. Official company service (OCS). |
| DZXU (Not valid in Southeast) | 64 Kbps on the 'D' Channel - Provides for digital packets of 64 Kbps on the ISDN "D" channel. | Unbundled. |
| EBXB | Electronic Business Service –Provides a connection between a CO and an electronic business set located at a customer premises. | Enhanced 911 (E911). |
| EBXS # (Not valid in Southeast) | Electronic Business Service –Provides a connection between a CO and an electronic business set located at a customer premises. | Customer/provider interface. |
| EBXU (Only in Midwest) | Electronic Business Service –Provides a connection between a CO and an electronic business set located at a customer premises. | Unbundled. |
| EBXZ # (Not valid in Southeast) | Electronic Business Service –Provides a connection between a CO and an electronic business set located at a customer premises. | Official company service (OCS). |
| EIXS # | E911 Tandem Interconnection - A dedicated trunk providing interconnection between tandems for the routing of E911 calls to the proper E911 emergency reporting entity. | Customer/provider interface. |
| EIXX (Not valid in Southeast) | E911 Tandem Interconnection - A dedicated trunk providing interconnection between tandems for the routing of e911 calls to the proper e911 emergency reporting entity. | No further parameters. |
| ELXS # | Emergency Reporting Line - A voice-grade circuit between reporting station(s) and a central location. It is used for emergency reporting and has no access to the switched message network. | Customer/provider interface. |
| EMGD | Emergency Reporting Center Trunk - A voice-grade circuit between a central office and an emergency reporting center (e.g., 911, E911). | Interstate: The interstate usage is more than 10% interstate as determined by the "PIU" FID, or Feature Group A services, the "UTNT' FID initially indicated more than 10% interstate usage. Enhanced 911 (E911). |
| EMXS | Emergency Reporting Center Trunk - A voice-grade circuit between a central office and an emergency reporting center (e.g., 911, E911). | Customer/provider interface. |
| EMXX (Valid in Southeast, Southwest, West) | Emergency Reporting Center Trunk - A voice-grade circuit between a central office and an emergency reporting center (e.g., 911, E911). | No further parameters. |
| EMXZ # | Emergency Reporting Center Trunk - A voice-grade circuit between a central office and an emergency reporting center (e.g., 911, E911). | Official company service (OCS). |
| EPXS (Not valid in Southeast) | Emergency Private Switch Trunk - Service between a customer premises and a local exchange carrier (LEC) e911 system. The circuit carrier station dialed 911 calls, and Annie information from the customer equipment (switching system) to the LEC e911 system interface. | Customer/provider interface. |
| EQXX # (Not valid in Southeast) | Equipment Only (Network Element) Assignment- This assignment provides for the assignment of equipment-only network elements that must be identified in circuit id format as part of the provisioning process. This application includes stand-alone equipment located at a station or on the customer premises side of the network interface (NI). (Note: The NI will be located between the customer term. equip. and its connection to network elements). | No further parameters. |
| EQXZ # (Not valid in Southeast) | Equipment Only (Network Element) Assignment- This assignment provides for the assignment of equipment-only network elements that must be identified in circuit id format as part of the provisioning process. This application includes stand-alone equipment located at a station or on the customer premises side of the network interface (NI). (Note: The NI will be located between the customer terminal equipment and its connection to network elements). | Official company service (OCS). |
| EVXS | Enhanced Emergency Reporting Trunk - A trunk circuit between a local central office and the central office serving an emergency reporting center (e.g., E911). | Customer/provider interface. |
| EVXZ (Not valid in Southeast) | Enhanced Emergency Reporting Trunk - A trunk circuit between a local central office and the central office serving an emergency reporting center (e.g., E911). | Official company service (OCS). |
| FCXG | Frame Relay - 320 Kbps - Circuit providing frame relay service at a digital rate of 320 Kbps. | Enhanced 911 (E911). |
| FDXE (Only in Southeast) | Private Line Data - A voice-grade service for data transmission between two or more stations without access to the switched message network. Voice transmission may be provided on an alternate or simultaneous basis. | Customer reconfigurable. |
| FDXG | Private Line Data - A voice-grade service for data transmission between two or more stations without access to the switched message network. Voice transmission may be provided on an alternate or simultaneous basis. | Enhanced 911 (E911). |
| FDXS # (Not valid in Southeast) | Private Line Data - A voice-grade service for data transmission between two or more stations without access to the switched message network. Voice transmission may be provided on an alternate or simultaneous basis. | Customer/provider interface. |
| FDXX (Only in the Southeast) | Private Line Data - A voice-grade service for data transmission between two or more stations without access to the switched message network. Voice transmission may be provided on an alternate or simultaneous basis. | No further parameters. |
| FDXZ | Private Line Data - A voice-grade service for data transmission between two or more stations without access to the switched message network. Voice transmission may be provided on an alternate or simultaneous basis. | Official company service (OCS). |
| FDX5 (Not valid in Southeast) | Private Line Data - A voice-grade service for data transmission between two or more stations without access to the switched message network. Voice transmission may be provided on an alternate or simultaneous basis. | Packet Switch and Official company service (OCS). Note: This is for internal usage only. The “5” is a National standard for Companies to use strictly for internal purposes. This is Not valid external to AT&T. |
| FEXG | Frame Relay - 448 Kbps - Circuit providing frame relay service at a digital rate of 448 Kbps. | Enhanced 911 (E911). |
| FFXG | Frame Relay - 576 Kbps Circuit providing frame relay service at a digital rate of 576 Kbps. | Enhanced 911 (E911). |
| FHXG | Frame Relay - 704 Kbps - Circuit providing frame relay service at a digital rate of 704 Kbps. | Enhanced 911 (E911). |
| FJXG | Frame Relay - 832 Kbps - Circuit providing frame relay service at a digital rate of 832 Kbps. | Enhanced 911 (E911). |
| FKXG | Frame Relay - 960 Kbps - Circuit providing frame relay service at a digital rate of 960 Kbps. | Enhanced 911 (E911). |
| FLZS # (Not valid in Southeast) | Fractional T-1 | Clear Channel Capability (CCC), Customer/provider interface. |
| FMXG | Frame Relay - 1024 Kbps - Circuit providing frame relay service at a digital rate of 1024 Kbps. | Enhanced 911 (E911). |
| FNXG | Frame Relay - 1088 Kbps - Circuit providing frame relay service at a digital rate of 1088 Kbps. | Enhanced 911 (E911). |
| FOXG | Frame Relay - 1152 Kbps - Circuit providing frame relay service at a digital rate of 1152 Kbps. | Enhanced 911 (E911). |
| FPXG | Frame Relay - 1216 Kbps - Circuit providing frame relay service at a digital rate of 1216 Kbps. | Enhanced 911 (E911). |
| FQXG | Frame Relay - 1280 Kbps - Circuit providing frame relay service at a digital rate of 1280 Kbps. | Enhanced 911 (E911). |
| FTXS # (Not valid in Southeast) | Foreign Exchange Trunk - A voice-grade circuit between a remote central office and a Centrex, PBX, ACD, or turret. | Customer/provider interface. |
| FTXU # (Not valid in Southeast) | Foreign Exchange Trunk - A voice-grade circuit between a remote central office and a Centrex, PBX, ACD, or turret. | Unbundled. |
| FUXG | Frame Relay – 1344 Kbps - Circuit providing frame relay service at a digital rate of 1344 Kbps. | Enhanced 911 (E911). |
| FXXG | Foreign Exchange Line - A voice-grade circuit between a remote central office and a station. | Enhanced 911 (E911). |
| FXXS # (Not valid in Southeast) | Foreign Exchange Line - A voice-grade circuit between a remote central office and a station. | Customer/provider interface. |
| FXXU # (Not valid in Southeast) | Foreign Exchange Line - A voice-grade circuit between a remote central office and a station. | Unbundled. |
| FXXX # | Foreign Exchange Line - A voice-grade circuit between a remote central office and a station. | No further parameters. |
| FYXG | Frame Relay – 1408 Kbps - Circuit providing frame relay service at a digital rate of 1408 Kbps. | Enhanced 911 (E911). |
| FZXG | Frame Relay – 1472 Kbps - Circuit providing frame relay service at a digital rate of 1472 Kbps. | Enhanced 911 (E911). |
| HBXS # (Not valid in Southeast) | Non- DDS Digital Data - 19.2 Kbps - Provides for two or more points of private-line digital data transmission Not associated with DDS at 19.2 Kbps. | Customer/provider interface. |
| HBXW | Non- DDS Digital Data - 19.2 Kbps - Provides for two or more points of private-line digital data transmission Not associated with DDS at 19.2 Kbps | Enhanced 911 (E911). |
| HBXZ # (Not valid in Southeast) | Non- DDS Digital Data - 19.2 Kbps - Provides for two or more points of private-line digital data transmission Not associated with DDS at 19.2 Kbps | Official company service (OCS). |
| HIXE # | Digital Service - 44.736 Mbps or Higher - Provides for two or more points of digital transmission at a speed of 44.736 Mbps or higher. | Customer reconfigurable. |
| HIXS # (Not valid in Southeast) | Digital Service - 44.736 Mbps or Higher - Provides for two or more points of digital transmission at a speed of 44.736 Mbps or higher. | Customer/provider interface. |
| HIXW | Digital Service - 44.736 Mbps or Higher - Provides for two or more points of digital transmission at a speed of 44.736 Mbps or higher. | Enhanced 911 (E911). |
| HIXZ # (Not valid in Southeast) | Digital Service - 44.736 Mbps or Higher - Provides for two or more points of digital transmission at a speed of 44.736 Mbps or higher. | Official company service (OCS). |
| HIZZ (Only in Midwest) | Digital Service - 44.736 Mbps or Higher - Provides for two or more points of digital transmission at a speed of 44.736 Mbps or higher. | Clear Channel Capability (CCC) Official company service (OCS). |
| HPXG | Non- DDS Digital Data - 2.4 Kbps - Provides for two or more points of private-line digital transmission Not associated with DDS at 2.4 Kbps. | Enhanced 911 (E911). |
| HPXS # (Not valid in Southeast) | Non- DDS Digital Data - 2.4 Kbps - Provides for two or more points of private-line digital transmission Not associated with DDS at 2.4 Kbps. | Customer/provider interface. |
| HPXZ # (Not valid in Southeast) | Non- DDS Digital Data - 2.4 Kbps - Provides for two or more points of private-line digital transmission Not associated with DDS at 2.4 Kbps. | Official company service (OCS). |
| HQXS # (Not valid in Southeast) | Non- DDS Digital Data - 4.8 Kbps - Provides for two or more points of private-line digital transmission Not associated with DDS at 4.8 Kbps. | Customer/provider interface. |
| HQXZ # (Not valid in Southeast) | Non- DDS Digital Data - 4.8 Kbps - Provides for two or more points of private-line digital transmission Not associated with DDS at 4.8 Kbps. | Official company service (OCS). |
| HRXS # (Not valid in Southeast) | Non- DDS Digital Data - 9.6 Kbps - Provides for two or more points of private-line digital transmission Not associated with DDS at 9.6 Kbps. | Customer/provider interface. |
| HRXW | Non- DDS Digital Data - 9.6 Kbps - Provides for two or more points of private-line digital transmission Not associated with DDS at 9.6 Kbps. | Enhanced 911 (E911). |
| HRXZ # (Not valid in Southeast) | Non- DDS Digital Data - 9.6 Kbps - Provides for two or more points of private-line digital transmission Not associated with DDS at 9.6 Kbps. | Official company service (OCS). |
| HWXS # (Not valid in Southeast) | Non- DDS Digital Data - 56 Kbps - Provides for two or more points of private-line digital transmission Not associated with DDS at 56 Kbps. | Customer/provider interface. |
| HWXW | Non- DDS Digital Data - 56 Kbps - Provides for two or more points of private-line digital transmission Not associated with DDS at 56 Kbps. | Enhanced 911 (E911). |
| HWXX (Only in the Southeast) | Non- DDS Digital Data - 56 Kbps - Provides for two or more points of private-line digital transmission Not associated with DDS at 56Kbps. | No further parameters. |
| HWXZ # (Not valid in Southeast) | Non- DDS Digital Data - 56 Kbps - Provides for two or more points of private-line digital transmission Not associated with DDS at 56 Kbps. | Official company service (OCS). |
| HYXS # (Not valid in Southeast) | Non- DDS Digital Data - 64 Kbps - Provides for two or more points of private-line digital transport Not associated with DDS at 64 Kbps. | Customer/provider interface. |
| HYXX (Valid in Southeast and Southwest) | Non- DDS Digital Data - 64 Kbps - Provides for two or more points of private-line digital transport Not associated with DDS at 64 Kbps. | No further parameters. |
| HYXZ # (Not valid in Southeast) | Non- DDS Digital Data - 64 Kbps - Provides for two or more points of private-line digital transport Not associated with DDS at 64 Kbps. | Official company service (OCS). |
| IBJR (Not valid in Southeast) | ISDN Basic Access Line | Channelized service with customer control. Service restoration. (Used for E911) |
| IBJZ (Not valid in Southeast) | ISDN Basic Access Line | Channelized service with customer control. Official company service (OCS). |
| IBMU (Not valid in Southeast) | ISDN Basic Access Line - Provides basic access for ISDN service between an end user's interface and a Telco switch. | Channeled service. Unbundled. |
| IBMZ (Not valid in Southeast) | ISDN Basic Access Line – Provides basic access for ISDN service between an end user's interface and a Telco switch. | Channeled service. Official company service (OCS). |
| IBXE (Southeast only) | ISDN Basic Access Line – Provides basic access for ISDN service between an end user’s interface and a Telco switch. | Customer reconfigurable. |
| IBXH (Not valid in Southeast) | ISDN Basic Access Line - Provides basic access for ISDN service between an end user's interface and a Telco switch. | Enhanced 911 (E911). |
| IBXN (SE only) | ISDN Basic Access Line- Provides basic access for ISDN service between an end user’s interface and a Telco switch. | Packet switched network. |
| IBXU (Not valid in Southeast) | ISDN Basic Access Line - Provides basic access for ISDN service between an end user's interface and a Telco switch. | Unbundled. |
| IBXX | ISDN Basic Access Line - Provides basic access for ISDN service between an end user's interface and a Telco switch. | No further parameters. |
| IBXZ | ISDN Basic Access Line - Provides basic access for ISDN service between an end user’s interface and a Telco switch. | Official company service (OCS). |
| IBZX (Not valid in Southeast) | ISDN Basic Access Line | Clear Channel Capability (CCC). |
| IBZZ (Not valid in Southeast) | ISDN Basic Access Line | Clear Channel Capability (CCC). Official company service (OCS). |
| IDXX # (Not valid in Southeast) | Derived Services - Provides for two or more points of digital or analog service which allows the deriving of two or more channels of any combination of voice and/or data services. | No further parameters. |
| IPXE (Valid only in Southeast) | ISDN Primary Access Line | Customer reconfigurable. |
| IPXL (Valid only in Southeast) | ISDN Primary Access Line | Customer surveillance. |
| IPXX (Valid only in Southeast) | ISDN Primary Access Line | No further parameters. |
| IPXZ (Valid only in Southeast) | ISDN Primary Access Line | Official company service (OCS). |
| IPZX (Valid only in Southeast) | ISDN Primary Access Line | Clear Channel Capability (CCC). |
| ITXZ # (Not valid in Southeast) | Intertandem Tie Trunk - Connects two tandem PBXs or Centrex(s) in a PBX tie trunk network. An Intertandem tie trunk may be connected to other tie trunks at both ends. | Official company service (OCS). |
| LAXS (Southwest only) | Local Area Data Channel (LADC) - A metallic channel for data only transmission over limited distances. Examples include LADC and 3002-type data channels with b-type conditioning. | Customer/provider interface. |
| LAXZ (Southwest only) | Local Area Data Channel (LADC) - A metallic channel for data-only transmission over limited distances. Examples include LADC and 3002-type data channels with b-type conditioning. | Official company service (OCS). |
| LIXN (Not valid in Southeast) | LAN Connection Operating at 4 Mbps (TOKEN RING) | Packet switched network. |
| LMXS # (Not valid in Southeast) | Transparent LAN Service - Provides two-point LAN access service for interconnecting LANs (e.g., token ring or Ethernet) | Customer/provider interface. |
| LMXZ (Valid Southwest, Midwest) | Transparent LAN Service - Provides two-point LAN access service for interconnecting LANs (e.g., token ring or Ethernet) | Official company service (OCS). |
| LOXE (Valid Southeast only) | Ethernet connection operating at 10 Mbps | Customer reconfigurable. |
| LOXF | Ethernet connection operating at 10 Mbps | Enhanced 911 (E911) |
| LOXL (Valid Southeast only) | Ethernet connection operating at 10 Mbps | Customer surveillance. |
| LOXX (Valid Southeast only) | Ethernet connection operating at 10 Mbps | No further parameters. |
| LSXS # (Not valid in Southeast) | Local Service - Provides residential, business or coin service (pots) requires the assignment of equipment and/or facilities that are inventoried in the trunk bureau records, and which may provide enhanced features. | Customer/provider interface. |
| LSXU (Valid Midwest only) | Local Service - Provides residential, business or coin service (pots) requires the assignment of equipment and/or facilities that are inventoried in the trunk bureau records, and which may provide enhanced features. | Unbundled. |
| LUHN (Valid Southeast only) | Ethernet connection operating at 1 Gbps | Redundant protection facility. User to Network interface (UNI) Switch Termination per MEF 10.1 |
| LUHX | Ethernet Connection Operating at 1 Gbps. | Redundant protection facility. |
| LUXF | Ethernet connection operating at 1 Gbps | Enhanced 911 (E911). |
| LUXM | Ethernet connection operating at 1 Gbps | Network Monitoring. |
| LUXN | Ethernet connection operating at 1 Gbps | User to Network interface (UNI) Switch Termination per MEF 10.1 |
| LUXQ | Ethernet connection operating at 1 Gbps | User to Network interface (UNI) Switch Termination per MEF 10.1 w/Enhanced 911 (E911) |
| LUXX | Ethernet connection operating at 1 Gbps | No further parameters. |
| LUXZ | Ethernet connection operating at 1 Gbps | Official company service (OCS). |
| LVHN (Valid Southeast only) | Ethernet connection operating at 100 Mbps | Redundant protection facility. User to Network interface (UNI) Switch Termination per MEF 10.1 |
| LVXE (Valid Southeast only) | Ethernet connection operating at 100 Mbps | Customer reconfigurable. |
| LVXF | Ethernet connection operating at 100 Mbps | Enhanced 911 (E911) |
| LVXL (Valid Southeast only) | Ethernet connection operating at 100 Mbps | Customer surveillance. |
| LVXM | Ethernet connection operating at 100 Mbps | Network Monitoring. |
| LVXN | Ethernet connection operating at 100 Mbps | User to Network interface (UNI) Switch Termination per MEF 10.1 |
| LVXQ | Ethernet connection operating at 100 Mbps | User to Network interface (UNI) Switch Termination per MEF 10.1 w/Enhanced 911 (E911) |
| LVXS (Not valid in Southeast) | Ethernet connection operating at 100 Mbps | Customer/provider interface. |
| LVXX | Ethernet connection operating at 100 Mbps | No further parameters. |
| LVXZ | Ethernet connection operating at 100 Mbps | Official company service (OCS). |
| LZHX | Ethernet Connection Operating at 10 Gbps. | Redundant Protection facility. |
| LZXF | Ethernet connection operating at 10 Gbps | Enhanced 911 (E911) |
| LZXQ | Ethernet connection operating at 10 Gbps | User to Network interface (UNI) Switch Termination per MEF 10.1 w/Enhanced 911 (E911) |
| LZXS (Not valid in Southeast) | Ethernet connection operating at 10 Gbps | Customer/provider interface. |
| LZXX | Ethernet connection operating at 10 Gbps | No further parameters. |
| LZXZ | Ethernet connection operating at 10 Gbps | Official company service (OCS). |
| L1HN (Valid Southeast only) | Rate adjustable Ethernet - 1 Gbps | Redundant protection facility. User to Network interface (UNI) Switch Termination per MEF 10.1 |
| L1XE (Valid Southeast only) | Rate adjustable Ethernet - 1 Gbps | Customer reconfigurable. |
| L1XF | Rate adjustable Ethernet - 1 Gbps | Enhanced 911 (E911) |
| L1XL (Valid Southeast only) | Rate adjustable Ethernet - 1 Gbps | Customer surveillance. |
| L1XN | Rate adjustable Ethernet - 1 Gbps | User to Network interface (UNI) Switch Termination per MEF 10.1 |
| L1XQ | Rate adjustable Ethernet - 1 Gbps | User to Network interface (UNI) Switch Termination per MEF 10.1 w/Enhanced 911 (E911) |
| L1XS (Not valid in Southeast) | Rate adjustable Ethernet - 1 Gbps | Customer/provider interface. |
| L1XX | Rate adjustable Ethernet - 1 Gbps | No further parameters. |
| L1XZ | Rate adjustable Ethernet - 1 Gbps | Official company service (OCS). |
| L1YX (Not valid in Southeast) | Rate adjustable Ethernet - 1 Gbps | Interstate jurisdiction. |
| L2HN | Rate adjustable 100 Mbps Fast Ethernet. | Redundant protection facility. User to Network interface (UNI) Switch Termination per MEF 10.1 |
| L2XF | Rate adjustable 100 Mbps Fast Ethernet. | Enhanced 911 (E911) |
| L2XN | Rate adjustable 100 Mbps Fast Ethernet. | User to Network interface (UNI) Switch Termination per MEF 10.1 |
| L2XQ | Rate adjustable 100 Mbps Fast Ethernet. | User to Network interface (UNI) Switch Termination per MEF 10.1 w/Enhanced 911 (E911) |
| L2XX | Rate adjustable 100 Mbps Fast Ethernet. | No further parameters. |
| L3XF | Rate adjustable 10 Mbps Ethernet. | Enhanced 911 (E911) |
| L3XN | Rate adjustable 10 Mbps Ethernet. | User to Network interface (UNI) Switch Termination per MEF 10.1 |
| L3XQ | Rate adjustable 10 Mbps Ethernet. | User to Network interface (UNI) Switch Termination per MEF 10.1 w/Enhanced 911 (E911) |
| L3XX | Rate adjustable 10 Mbps Ethernet | No further parameters |
| L4XB | Rate adjustable 10 Gbps Ethernet | Bundled Network Capacity (physically routed circuits to allow for customer-initiated bundling). |
| L4XF | Rate adjustable 10 Gbps Ethernet | Enhanced 911 (E911). |
| L4XN | Rate adjustable 10 Gbps Ethernet | Packet Switched Network |
| L4XQ | Rate adjustable 10 Gbps Ethernet | Packet Switched Network w/Enhanced 911 (E911). |
| L4XS | Rate adjustable 10 Gbps Ethernet | Customer/provider interface. |
| L4XX | Rate adjustable 10 Gbps Ethernet | No Further Parameters. |
| L4XZ | Rate adjustable 10 Gbps Ethernet | Official company service (OCS). |
| L4YB | Rate adjustable 10 Gbps Ethernet | Interstate jurisdiction. Bundled Network Capacity (physically routed circuits to allow for customer-initiated bundling). |
| L4YS | Rate adjustable 10 Gbps Ethernet | Interstate jurisdiction. Customer/provider interface. |
| L4YX | Rate adjustable 10 Gbps Ethernet | Interstate jurisdiction. |
| L7XX | Ethernet connection operating at 40 Gbps. | No further parameters required |
| L8HX | Ethernet connection operating at 100 Gbps | Redundant protection facility |
| L8XX | Ethernet connection operating at 100 Gbps | No further parameters required |
| L9XS (Not valid in Southeast) | Rate Adjustable Ethernet - Identifies Ethernet service where the physical interface (UNI, ENNI) can be 10 Mbps, 100 Mbps, 1 Gbps, 10 Gbps, 40 Gbps, and 100 Gbps. The actual speed of the service will be anywhere from 1 Mbps up to 100 Gbps. Note: This code is not to be used for adjustments between fixed rates i.e., 10Mbps to 100Mbps. | Customer/provider interface. |
| L9XX | Rate Adjustable Ethernet - Identifies Ethernet service where the physical interface (UNI, ENNI) can be 10 Mbps, 100 Mbps, 1 Gbps, 10 Gbps, 40 Gbps, and 100 Gbps. The actual speed of the service will be anywhere from 1 Mbps up to 100 Gbps. Note: This code is Not to be used for adjustments between fixed rates i.e., 10 Mbps to 100 Mbps. | No further parameters. |
| L9XZ | Rate Adjustable Ethernet - Identifies Ethernet service where the physical interface (UNI, ENNI) can be 10 Mbps, 100 Mbps, 1 Gbps, 10 Gbps, 40 Gbps, and 100 Gbps. The actual speed of the service will be anywhere from 1 Mbps up to 100 Gbps. Note: This code is Not to be used for adjustments between fixed rates i.e., 10 Mbps to 100 Mbps. | Official company service (OCS). |
| MCXX | Multi-Service Broadband | No further parameters. |
| MDXX | SONET - STS1 Signal | No further parameters. |
| MEXS (Not valid in Southeast) | SONET-STS3 Signal -A circuit carrying SONET services at the electrical digital rate of an STS3 or STS3C signal (155.520 Mbps). | Customer/provider interface. |
| MEXZ (Not valid in Southeast) | SONET-STS3 Signal - A circuit carrying SONET services at the electrical digital rate of an STS3 or STS3C signal (155.520 Mbps). | Official company service (OCS). |
| MGAE (Valid only in Southeast) | SONET - OC3 Signal - A circuit carrying SONET services at the optical digital rate of an OC3 signal (155.520 Mbps). | Point to point. Customer reconfigurable. |
| MGAX (Valid only in Southeast) | SONET - OC3 Signal - A circuit carrying SONET services at the optical digital rate of an OC3 signal (155.520 Mbps). | Point to point. |
| MGCX (Valid only in Southeast) | SONET - OC3 Signal - A circuit carrying SONET services at the optical digital rate of an OC3 signal (155.520 Mbps). | Concatenated. |
| MGXB (Valid only in the Midwest) | SONET - OC3 Signal - A circuit carrying SONET services at the optical digital rate of an OC3 signal (155.520 Mbps). | No further parameters required. Rebundled. Note: Limited offering please verify availability in your region via Product Announcements. |
| MGXS (Not valid in Southeast) | SONET - OC3 Signal - A circuit carrying SONET services at the optical digital rate of an OC3 signal (155.520 Mbps). | Customer/provider interface. |
| MGXT (Valid only in Southeast) | SONET - OC3 Signal - A circuit carrying SONET services at the optical digital rate of an OC3 signal (155.520 Mbps). | Service is transported over non-SONET infrastructure (overhead remains transparent to provider) |
| MGXU # (Not valid in Southeast) | SONET - OC3 Signal -A circuit carrying SONET services at the optical digital rate of an OC3 signal (155.520 Mbps). | Unbundled. |
| MGXX (Valid only in Southeast) | SONET - OC3 Signal - A circuit carrying SONET services at the optical digital rate of an OC3 signal (155.520 Mbps). | No further parameters required. |
| MGXZ (Not valid in Southeast) | SONET - OC3 Signal - A circuit carrying SONET services at the optical digital rate of an OC3 signal (155.520 Mbps). | Official company service (OCS). |
| MHXB (Valid only in Midwest) | SONET - OC12 Signal - A circuit carrying SONET services at the optical digital rate of an OC12 signal (622.080 Mbps). | No further parameters required. Rebundled. Note: Limited offering please verify availability in your region via Product Announcements. |
| MHXS (Not valid in Southeast) | SONET - OC12 Signal - A circuit carrying SONET services at the optical digital rate of an OC12 signal (622.080 Mbps). | Customer/provider interface. |
| MHXT (Valid only in Southeast) | SONET - OC12 Signal - A circuit carrying SONET services at the optical digital rate of an OC12 signal (622.080 Mbps). | Service is transported over non-SONET infrastructure (overhead remains transparent to provider) |
| MHXU # (Not valid in Southeast) | SONET - OC12 Signal - A circuit carrying SONET services at the optical digital rate of an OC12 signal (622.080 Mbps). | Unbundled. |
| MHXZ (Not valid in Southeast) | SONET - OC12 Signal - A circuit carrying SONET services at the optical digital rate of an OC12 signal (622.080 Mbps). | Official company service (OCS). |
| MJXS (Not valid in Southeast) | SONET - OC48 Signal - A circuit carrying SONET services at the optical digital rate of an OC48 signal (2488.320 Mbps). | Customer/provider interface. |
| MJXT (Valid Southeast only) | SONET - OC48 Signal - A circuit carrying SONET services at the optical digital rate of an OC48 signal (2488.320 Mbps). | Service is transported over non-SONET infrastructure (overhead remains transparent to provider) |
| MJXU # (Not valid in Southeast) | SONET - OC48 Signal - A circuit carrying SONET services at the optical digital rate of an OC48 signal (2488.320 Mbps). | Unbundled. |
| MJXZ (Not valid in Southeast) | SONET - OC48 Signal - A circuit carrying SONET services at the optical digital rate of an OC48 signal (2488.320 Mbps). | Official company service (OCS). |
| MKXS (Not valid in Southeast) | SONET - OC192 Signal - A circuit carrying SONET services at the optical digital rate of an OC192 signal (9953.280 Mbps). | Customer/provider interface. |
| MKXT (Valid only in Southeast) | SONET - OC192 Signal - A circuit carrying SONET services at the optical digital rate of an OC192 signal (9953.280 Mbps). | Service is transported over non-SONET infrastructure (overhead remains transparent to provider) |
| MKXU # (Not valid in Southeast) | SONET - OC192 Signal - A circuit carrying SONET services at the optical digital rate of an OC192 signal (9953.280 Mbps). | Unbundled. |
| MKXZ (Not valid in Southeast) | SONET - OC192 Signal - A circuit carrying SONET services at the optical digital rate of an OC192 signal (9953.280 Mbps). | Official company service (OCS). |
| MNXS (Not valid in Southeast) | Optical Data Transport Service - This service code identifies an optical data transport, which includes a variety of fiber-based services (i.e., ESCON, Gig-E, SONET, FICON, Fibre channel, FDDI). | Customer/provider interface. |
| MNXX | Optical Data Transport Service - This service code identifies an optical data transport, which includes a variety of fiber-based services (i.e., ESCON, Gig-E, SONET, FICON, Fibre channel, FDDI). | No further parameters. |
| MNXZ | Optical Data Transport Service - This service code identifies an optical data transport, which includes a variety of fiber-based services (i.e., ESCON, Gig-E, SONET, FICON, Fibre channel, FDDI). | Official company service (OCS). |
| MOXS (Not valid in Southeast) | SONET - Flexible Rate. | Customer/provider interface. |
| MOXZ (Not valid in Southeast) | SONET - Flexible Rate. | Official company service (OCS). |
| MTXS (Not valid in Southeast) | Wired Music - Provides for the transmission of either speech or music between two or more locations. | Customer/provider interface. |
| MTXZ (Not valid in Southeast) | Wired Music - Provides for the transmission of either speech or music between two or more locations. | Official company service (OCS). |
| NDXS # (Not valid in Southeast) | Network Data Link - Provides a direct connection for a modem or equivalent on the customer's premises to the central office. This central office may or may not, for telephone company reasons be its customary central office. This service has access to the switched-message network. | Customer/provider interface. |
| NDXZ # (Not valid in Southeast) | Network Data Link - Provides a direct connection for a modem or equivalent on the customer's premises to the central office. This central office may or may not, for telephone company reasons be its customary central office. This service has access to the switched-message network. | Official company service (OCS). |
| OPXS # (Not valid in Southeast) | Off Premises Extension | Customer/provider interface. |
| OSXG | Off Premises PBX Station Line | Enhanced 911 (E911). |
| OSXS (Not valid in Southeast) | Off Premises PBX Station Line | Customer/provider interface. |
| PAPX # (Not valid in Southeast) | Protective Alarm (AC Interface at Customer Premises) | Parameter only offering under an intrastate restructured private line (RPL) tariff. |
| PCXS # (Not valid in Southeast) | Switched Digital Access Line - Provides access for switched digital data transmission operating at synchronous data speeds such as 56 Kbps. Alternate analog voice service may be provided (e.g., public switched digital system). | Customer/provider interface. |
| PCXZ # (Not valid in Southeast) | Switched Digital Access Line - Provides access for switched digital data transmission operating at synchronous data speeds such as 56 Kbps. Alternate analog voice service may be provided (e.g., public switched digital system). | Official company service (OCS). |
| PGXS # (Not valid in Southeast) | Paging | Customer/provider interface. |
| PLPS # (Not valid in Southeast) | Private Line - Voice | Parameter only offering under an intrastate restructured private line (RPL) tariff. Customer/provider interface. |
| PLXB (Valid Midwest only) | Private Line - Voice | No further parameters required. Rebundled. Note: Limited offering please verify availability in your region via the Product Announcements. |
| PLXS # (Not valid in Southeast) | Private Line - Voice | Customer/provider interface. |
| PLXZ # (Not valid in Southeast) | Private Line - Voice | Official company service (OCS). |
| QEXX (Valid Southeast only) | Frame Relay - 56 Kbps | No further parameters. |
| QEXZ (Valid Southeast only) | Frame Relay - 56 Kbps | Official company service (OCS). |
| QGXE (Valid Southeast only) | Frame Relay - 1.544 Mbps | Customer reconfigurable. |
| QGXX (Valid Southeast only) | Frame Relay - 1.544 Mbps | No further parameters. |
| QGXZ (Valid Southeast only) | Frame Relay - 1.544 Mbps | Official company service (OCS). |
| QIXE (Valid Southeast only) | Frame Relay - 44.736 Mbps | Customer reconfigurable. |
| QIXX (Valid Southeast only) | Frame Relay - 44.736 Mbps | No further parameters. |
| QIXZ (Valid Southeast only) | Frame Relay - 44.736 Mbps | Official company service (OCS). |
| QJXX (Valid Southeast only) | Frame Relay - 384 Kbps | No further parameters. |
| QJXZ (Valid Southeast only) | Frame Relay - 384 Kbps | Official company service (OCS). |
| QKXX (Valid Southeast only) | Frame Relay - 64 Kbps | No further parameters. |
| QKXZ (Valid Southeast only) | Frame Relay - 64 Kbps | Official company service (OCS). |
| QLXX (Valid Southeast only) | Frame Relay - 128 Kbps | No further parameters. |
| QLXZ (Valid Southeast only) | Frame Relay - 128 Kbps | Official company service (OCS). |
| RTXS # (Not valid in Southeast) | RADIO LAND LINE ~ A channel used to provide access to non-broadcast radio transceivers. | Customer/provider interface. |
| RTXX | Radio Land Line - A channel used to provide access to non-broadcast radio transceivers. | No further parameters. |
| RTXZ # (Not valid in Southeast) | Radio Land Line - A channel used to provide access to non-broadcast radio transceivers. | Official company service (OCS). |
| SQXS (Not valid in Southeast) | Equipment Only (Customer Premises) Assignment | Customer/provider interface. |
| SQXZ (Not valid in Southeast) | Equipment Only (Customer Premises) Assignment | Official company service (OCS). |
| SVXS # (Non-standard) (Not valid in Southeast) | Generic code to be used for generating WORD document for NMA when no design is required but WORD document is needed for tracking or billing. (NOT FOR USE EXTERNAL TO AT&T) | Customer/provider interface. |
| TAXS # (Not valid in Southeast) | Tandem Tie Trunk | Customer/provider interface. |
| TAXX # | Tandem Tie Trunk | No further parameters |
| TAXZ # | Tandem Tie Trunk | Official company service (OCS). |
| TCPS # (Not valid in Southeast) | Control/Remote Metering Telegraph Grade | Parameter only offering under an intrastate restructured private line (RPL) tariff. Customer/provider interface. |
| TCXZ (Not valid in Southeast) | Control/Remote Metering Telegraph Grade | Official company service (OCS). |
| TGXS # (Not valid in Southeast) | Central Office – Trunk Side Termination | Customer/provider interface. |
| TGXU # (Not valid in Southeast) | Central Office – Trunk Side Termination | Unbundled. |
| TIXX # (Not valid in Southeast) | Central Office – Trunk Side Termination – Alternate Design | No further parameters. |
| TIXZ (Not valid in Southeast) | Central Office – Trunk Side Termination – Alternate Design | Official company service (OCS). |
| TJXS # (Not valid in Southeast) | Local PBX Trunk – Alternate Design | Customer/provider interface. |
| TJXZ # (Not valid in Southeast) | Local PBX Trunk – Alternate Design | Official company service (OCS). |
| TKXS (Not valid in Southeast) | Local PBX Trunk | Customer/provider interface. |
| TKXU (Not valid in Southeast) | Local PBX Trunk | Unbundled. |
| TKXZ (Not valid in Southeast) | Local PBX Trunk | Official company service (OCS). |
| TLXB (Valid Midwest only) | Non-Tandem Tie Trunk | No further parameters required. Rebundled. Note: Limited offering please verify availability in your region via Product Announcements. |
| TLXS (Not valid in Southeast) | Non-Tandem Tie Trunk | Customer/provider interface. |
| TLXZ (Not valid in Southeast) | Non-Tandem Tie Trunk | Official company service (OCS). |
| TXXG (Valid Southeast, Southwest only) | Dedicated Facility without Equipment | UNE with test access. |
| TXXU (Not valid in Southeast) | Dedicated Facility without Equipment | Unbundled. |
| TXXZ (Not valid in Southeast) | Dedicated Facility without Equipment | Official company service (OCS). |
| TYXG (Valid Southeast, Southwest only) | Dedicated Facility with Equipment | UNE with test access. |
| TYXU (Valid Midwest only) | Dedicated Facility with Equipment | Unbundled. |
| UBXU # (Not valid in Southeast) | Basic Rate ISDN (BRI) Non-Access | Unbundled. |
| UBXZ (Valid Southwest only) | Basic Rate ISDN (BRI) Non-Access | Official company service (OCS). |
| UBYU # (Not valid in Southeast) | Basic Rate ISDN (BRI) Non-Access | Interstate: Unbundled. |
| UCXS (Not valid in Southeast) | Voice Line Non-Access | Customer/provider interface. |
| UCXU (Valid Midwest only) | Voice Line Non-Access | Unbundled. |
| UCXZ (Not valid in Southeast) | Voice Line Non-Access | Official company service (OCS). |
| UDXS (Not valid in Southeast) | Voice Trunk Non-Access | Customer/provider interface. |
| UDXU (Not valid in Southeast) | Voice Trunk Non-Access | Unbundled. |
| UDXX (Valid West only) | Voice Trunk Non-Access | No further parameters. |
| UDXZ (Not valid in Southeast) | Voice Trunk Non-Access | Official company service (OCS). |
| UGXG | Analog Data Non-Access (Long definition for clarity = A voice-grade transmission channel (300-3000 Hz) suitable for use as a basic-data circuit. Optional data conditioning may be added to the basic channel.) | Enhanced 911 (E911). |
| UGXR | Analog Data Non-Access (Long definition for clarity = A voice-grade transmission channel (300-3000 Hz) suitable for use as a basic-data circuit. Optional data conditioning may be added to the basic channel.) | Service restoration. (Used for E911). |
| UGXS (Not valid in Southeast) | Analog Data Non-Access (Long definition for clarity = A voice-grade transmission channel (300-3000 Hz) suitable for use as a basic-data circuit. Optional data conditioning may be added to the basic channel.) | Customer/provider interface. |
| UGXU (Valid Midwest, West only) | Analog Data Non-Access (Long definition for clarity = A voice-grade transmission channel (300-3000 Hz) suitable for use as a basic-data circuit. Optional data conditioning may be added to the basic channel.) | Unbundled. |
| UGXZ (Not valid in Southeast) | Analog Data Non-Access (Long definition for clarity = A voice-grade transmission channel (300-3000 Hz) suitable for use as a basic-data circuit. Optional data conditioning may be added to the basic channel.) | Official company service (OCS). |
| UTXX | OTN - OTU-1 Signal. | No further parameters required. |
| UVHX | OTN - OTU-2 Signal. | Redundant protection facility. |
| UWHX | OTN - OTU-3 Signal. | Redundant protection facility. |
| UWXX | OTN - OTU-3 Signal. | No further parameters required. |
| UXHX | OTN - OTU-4 Signal. | Redundant protection facility. |
| UXXX | OTN - OTU-4 Signal. | No further parameters required. |
| VRXS (Not valid in Southeast) | Non-commercial Television | Customer/provider interface. |
| VSXS (Not valid in Southeast) | Video Service | Customer/provider interface. |
| VUXX | Component Serial Digital Video-Compressed (Requires a DS3 Transport) | No further parameters required. |
| VUXZ | Component Serial Digital Video-Compressed (Requires a DS3 Transport) | Official company service (OCS) |
| VUYX | Component Serial Digital Video-Compressed (Requires a DS3 Transport) | Interstate jurisdiction. |
| VVXS | Component Serial Digital Video-Uncompressed (i.e., 270 Mbps) | Customer/provider interface. |
| VVXZ | Component Serial Digital Video-Uncompressed (i.e., 270 Mbps) | Official company service (OCS). |
| WCHX (Valid Southeast only) | Wavelength Channel (DWDM) | Redundant protection facility. |
| WCXS (Not valid in Southeast) | Wavelength Channel (DWDM) | Customer/provider interface. |
| WCXX (Valid Southeast only) | Wavelength Channel (DWDM) | No further parameters. |
| WCXZ | Wavelength Channel (DWDM) | Official company service (OCS). |
| WIXS # (Not valid in Southeast) | WATS Service Trunk | Customer/provider interface. |
| WOXS # (Not valid in Southeast) | WATS Line (Out) | Customer/provider interface. |
| WSXS # (Not valid in Southeast) | WATS Trunk (Out) | Customer/provider interface. |
| WXXS # (Not valid in Southeast) | WATS Service Line | Customer/provider interface. |
| ZAXZ # (Not valid in Southeast) | Alarm Circuits | Official company service (OCS). |
| ZBXZ # (Not valid in Southeast) | Digital Sampling Circuits | Official company service (OCS). |
| ZCXZ # (Not valid in Southeast) | Call and Talk Circuits | Official company service (OCS). |
| ZEXZ # (Not valid in Southeast) | Emergency Patching Circuits | Official company service (OCS). |
| ZFXZ # (Not valid in Southeast) | Order Circuits - Facility are used for voice communications between normally unattended locations and maintenance centers. | Official company service (OCS). |
| ZMXZ # (Not valid in Southeast) | Measurement and Recording Circuits | Official company service (OCS). |
| ZPXZ # (Not valid in Southeast) | Test Circuits, Plant Service Center | Official company service (OCS). |
| ZQXZ # (Not valid in Southeast) | Quality Control and Management Circuits | Official company service (OCS). |
| ZSXZ # (Not valid in Southeast) | Switching, Control and Transfer Circuits | Official company service (OCS). |
| ZTXZ | Test Circuits – Central Office | Official company service (OCS). |
| ZVXZ # (Not valid in Southeast) | Order Circuits – Service | Official company service (OCS). |

The following is a list of Private Line service codes that may need to be processed through AT&T systems for other companies.  These codes should not be used to represent services sold by AT&T (except the “Q” series in the Southeast region), however, other companies (e.g., Verizon West) may use them as their primary circuit designation.  In such cases, the circuit may be physically transported through AT&T territory, and we should carry their circuit designation in our system.

| CLCI S/S Code | Description |
| --- | --- |
| QE | A circuit providing Frame Relay service at the digital rate of 56 Kbps. Used in Southeast Region. In AT&T West region we would use CLCI “XH” with a 4th character Modifier of “S”. In all other regions we would use CLCI Service Code, “DW” with a 4th character Modifier of “S”. |
| QG | Frame Relay service 1.544 Mbps or higher. Used in Southeast Region. In AT&T West region we would use CLCI “HC” with a 4th character modifier of “S” In all other regions we would use CLCI Service Code, “DH” with a 4th character Modifier of “S” |
| QJ | A circuit providing Frame Relay service at the digital rate of 384 Kbps. Used in Southeast Region. In AT&T we use the Fractional T1 Service Codes for this type of connection. |
| QK | A circuit providing Frame Relay service at the digital rate of 64 Kbps. Used in Southeast Region. In AT&T West region we would use CLCI Service Code “XD” with a 4th character Modifier of “S”. In all other regions we would use CLCI Service Code “DC” with a 4th character Modifier of “S”. |
| QL | A circuit providing Frame Relay service at the digital rate of 128 Kbps is used in the Southeast Region. In AT&T we use the Fractional T1 Service Codes for this type of connection. |
| UH | Digital High Capacity, 1.544 Mbps service. In AT&T West region we would use CLCI Service Code “HC” to identify this service. In all other regions we would use CLCI Service Code “DH” to identify this service. |

ADDENDUM for Temporary Coding Combinations

The following CLCI S/S coding combinations may be used on a temporary basis.  These temporary codes may be replaced in the future with more appropriate codes and will be incorporated into the base part of TAB 12 at that time.

These codes represent CLCI S/S codes used in Domestic Legacy AT&T (AT&T Core – cT), prior to AT&T’s efforts to ensure COMMON LANGUAGE® (CL) Compliance to the Iconectiv (formally known as Telcordia Technologies Inc.) industry-based coding.  Business processes and system changes must be completed before the more appropriate codes are the only ones accepted by Legacy AT&T (cT).

Please direct questions to your Account Manager or your CL Coordinator.

Section 1: InterLATA Core AT&T (cT) CLCI S/S Coding

Section 2: InterLATA Core AT&T (cT) CLCI S/S Coding for Ethernet Services

Section 1: InterLATA Core AT&T (cT) CLCI S/S Coding

##### Valid Service Code and Modifier (SC/Mod) Combinations

| cT SC/Mod code | Domestic cT code Description | Industry SC/Mod Code | Industry Recommended Codes and Descriptions |
| --- | --- | --- | --- |
| ABEC | DS0 - 56K -Interstate | ABYX | Packet- Network Trunk Interstate |
|  |  | ABXZ | Packet- Network Trunk Official Company Service (OCS) |
| ABEC | DS1 - 1.5M -Interstate | ACYX | SONET to speed specific code with Modifier, EX (interstate Ring topology). MGEX (0C3), MHEX (OC12) MJEX (OC48) MKEX (OC192) |
|  |  | ACXZ | SONET to speed specific code with Modifier, EX (interstate Ring topology). MGEX (0C3), MHEX (OC12) MJEX (OC48) MKEX (OC192) Official Company Service (OCS) |
| AFEC | DS1 - 1.5M -Interstate | AFYX | Commercial Audio Interstate |
|  |  | AFXZ | Commercial Audio Official company service (OCS). |
| AGEC | OC3 - 155M - Interstate | MGYX | OC3 Interstate |
|  |  | MGXZ | OC3 Official company service (OCS). |
| AQEC | DS0-9.6K Generic - Interstate | HRYX | Non-DDS DIGITAL DATA - 9.6 Kbps Interstate |
|  |  | HRXZ | Non-DDS DIGITAL DATA - 9.6 Kbps Official company service (OCS). |
| AREC | DS0-56K Generic - Interstate | HWYX | Non-DDS DIGITAL DATA - 56 Kbps Interstate |
|  |  | HWXZ | Non-DDS DIGITAL DATA - 56 Kbps Official company service (OCS) |
| BAEC | Protective Alarm (DC Interface at Customer Premises) - Interstate | BAYX | Protective Alarm (DC Interface at Customer Premises) - Interstate |
|  |  | BAXZ | Protective Alarm (DC Interface at Customer Premises) Official company service (OCS) |
| CAEC | DS0 - 56K - Interstate | CAYX | SST Access |
|  |  | CAXZ | SST Access Official company service (OCS) |
| CEEC | DS0 - 56K - Interstate | CEYX | SST Station Line Interstate |
|  |  | CEXZ | SST Station Line Interstate Official company service (OCS) |
| CLEC | DS0 - 56K - Interstate | CLYX | Centrex CO Line - Interstate |
|  |  | CLXZ | Centrex CO Line - Interstate Official company service (OCS) |
| CNEC | DS0 - 56K - Interstate | CNYX | SST Network Trunk Interstate |
|  |  | CNXZ | SST Network Trunk Official company service (OCS) |
| DBEC | DS1 - 1.5M - Interstate | DHYE | Digital Service - 1.544 Mbps Interstate Customer reconfigurable |
|  |  | DHXZ | Digital Service - 1.544Mbps Official company service (OCS) |
| DCEC | IBR - 384K - Interstate | GEYX | Digital Data - 384 Kbps Interstate |
|  |  | GEXZ | Digital Data - 384 Kbps Official company service (OCS) |
| DEEC | IBR - 512K - Interstate | GGYX | Digital Data - 512 Kbps Interstate |
|  |  | GGXZ | Digital Data - 512 Kbps Official company service (OCS) |
| DHEC | DS1 - 1.5M - Interstate | DHYX | Digital Service - 1.544 Mbps Interstate |
|  |  | DHXZ | Digital Service - 1.544Mbps Official company service (OCS) |
| DIEC | DS1 - 1.5M - Interstate | DIYX | Direct-In-Dial Interstate |
|  |  | DIXZ | Direct-In-Dial Interstate Official company service (OCS) |
| DNEC | DS3 - 45M - Interstate | HIYX | Digital Service- 44.736 Mbps Interstate |
|  |  | HIXZ | Digital Service- 44.736 Mbps Official company service (OCS) |
| DPEC | Digital Data - 2.4 Kbps - Interstate | DPYX | Digital Data - 2.4 Kbps Interstate |
|  |  | DPXZ | Digital Data - 2.4 Kbps Official company service (OCS) |
| DQEC | Digital Data - 4.8 Kbps - Interstate | DQYX | Digital Data - 4.8 Kbps Interstate |
|  |  | DQXZ | Digital Data - 4.8 Kbps Official company service (OCS) |
| DREC | Digital Data - 9.6 Kbps Interstate | DRYX | Digital Data - 9.6 Kbps |
|  |  | DRXZ | Digital Data - 9.6 Kbps Official company service (OCS) |
| DTEC | IBR - 768K - Interstate | GKYX | Digital Data - 768 Kbps Interstate |
|  |  | GKXZ | Digital Data - 768 Kbps Official company service (OCS) |
| DVEC | DS0 - 64K - Interstate | HYYX | Non-DDS Digital Data - 64 Kbps Interstate |
|  |  | HYXZ | Non-DDS Digital Data - 64 Kbps Official company service (OCS) |
| DWEC | DS0 – 56 Kbps - Interstate | DWYX | Digital Data - 56 Kbps Interstate |
|  |  | DWXZ | Digital Data - 56 Kbps Official company service (OCS) |
| DXEC | IBR – 128 Kbps - Interstate | GAYX | Digital Data - 128 Kbps Interstate |
|  |  | GAXZ | Digital Data - 128 Kbps Interstate Official company service (OCS) |
| DZEC | IBR – 256 Kbps - Interstate | GCYX | Digital Data - 256 Kbps Interstate |
|  |  | GCXZ | Digital Data - 256 Kbps Interstate Official company service (OCS) |
| EMEC | DS0 – 56 Kbps - Interstate | EMYX | Emergency Reporting Center Trunk Interstate |
|  |  | EMXZ | Emergency Reporting Center Trunk Official company service (OCS) |
| EQEC | Equipment - Interstate | EQYX | Equipment Only (Network Element) Assignment Interstate |
|  |  | EQXZ | Equipment Only (Network Element) Assignment Official company service (OCS) |
| FDEC | DS0 – 56 Kbps - Interstate | FDYX | Private Line- Data Interstate |
|  |  | FDXZ | Private Line- Data Official company service (OCS) |
| FTEC | DS0 – 56 Kbps - Interstate | FTYX | Foreign Exchange Trunk Interstate |
|  |  | FTXZ | Foreign Exchange Trunk Official company service (OCS) |
| FVEC | DS0 – 56 Kbps - Interstate | FVYX | Voice Grade Facility Interstate |
|  |  | FVXZ | Voice Grade Facility Official company service (OCS) |
| FXEC | DS0 – 56 Kbps - Interstate | FXYX | Foreign Exchange Line Interstate |
|  |  | FXXZ | Foreign Exchange Line Official company service (OCS) |
| IAEC | IBR – 192 Kbps - Interstate | GBYX | Digital Data - 192 Kbps Interstate |
|  |  | GBXZ | Digital Data - 192 Kbps Official company service (OCS) |
| IBDC IBEC | IBR – 1152 Kbps - Interstate | GQYX | Digital Data - 1152 Kbps Interstate |
|  |  | GQXZ | Digital Data - 1152 Kbps Official company service (OCS) |
| ICEC | IBR – 320 Kbps - Interstate | GDYX | Digital Data - 320 Kbps Interstate |
|  |  | GDXZ | Digital Data - 320 Kbps Official company service (OCS) |
| IDEC | IBR – 448 Kbps - Interstate | GFYX | Digital Data - 448 Kbps Interstate |
|  |  | GFXZ | Digital Data - 448 Kbps Official company service (OCS) |
| IEEC | IBR – 576 Kbps - Interstate | GHYX | Digital Data - 576 Kbps Interstate |
|  |  | GHXZ | Digital Data - 576 Kbps Official company service (OCS) |
| IFEC | IBR – 640 Kbps - Interstate | GIYX | Digital Data - 640 Kbps Interstate |
|  |  | GIXZ | Digital Data - 640 Kbps Official company service (OCS) |
| IGEC | IBR – 704 Kbps - Interstate | GJYX | Digital Data - 704 Kbps Interstate |
|  |  | GJXZ | Digital Data - 704 Kbps Official company service (OCS) |
| IIEC | IBR - 1.024 Mbps - Interstate | GOYX | Digital Data - 1024 Kbps Interstate |
|  |  | GOXZ | Digital Data - 1024 Kbps Official company service (OCS) |
| ITEC | DS0 – 56 Kbps - Interstate | ITYX | Intertandem Tie Trunk Interstate |
|  |  | ITXZ | Intertandem Tie Trunk Official company service (OCS) |
| IVEC | OC12 – 622 Mbps - Interstate | MHYX | OC12 Interstate |
|  |  | MHXZ | OC12 Official company service (OCS) |
| IWEC | OC48 – 2.5 Gbps - Interstate | MJYX | OC48 Interstate |
|  |  | MJXZ | OC48 Official company service (OCS) |
| IXEC | OC192– 10 Gbps - Interstate | MKYX | OC192 Interstate |
|  |  | MKXZ | OC192 Official company service (OCS) |
| IYEC | 6.3 Mbps - Interstate | MSYX | OC768 Interstate |
|  |  | MSXZ | OC768 Official company service (OCS) |
| JEEC | DS0 – 56 Kbps - Interstate | MMYX | SONET - VT1 Signal Interstate |
|  |  | MMXZ | SONET - VT1 Signal Official company service (OCS) |
| ONEC | DS0 – 56 Kbps - Interstate | ONYX | Off Network Access Line Interstate |
|  |  | ONXZ | Off Network Access Line Official company service (OCS) |
| OPEC | DS0 – 56 Kbps - Interstate | OPYX | Off Premise Extension Interstate |
|  |  | OPXZ | Off Premise Extension Official company service (OCS) |
| OSEC | DS0 – 56 Kbps - Interstate | OSYX | Off Premise PBX Extension Line Interstate |
|  |  | OSXZ | Off Premise PBX Extension Line Official company service (OCS) |
| PAEC | DS0 – 56 Kbps - Interstate | PAYX | Off Premise PBX Extension Line Interstate |
|  |  | PAXZ | Off Premise PBX Extension Line Official company service (OCS) |
| PLEC | DS0 – 56 Kbps - Interstate | PLYX | Private Line Voice Interstate |
|  |  | PLXZ | Private Line Voice Official company service (OCS) |
| PREC | DS0 – 56 Kbps - Interstate | PRYX | Protective Relaying Voice Grade Interstate |
|  |  | PRXZ | Protective Relaying Voice Grade Official company service (OCS) |
| PXEC | DS0 – 56 Kbps - Interstate | PXYX | PBX Station Line Interstate |
|  |  | PXXZ | PBX Station Line Official company service (OCS) |
| QLEC | DS0 – 56 Kbps - Interstate | QLYX | Frame Relay- 128 Kbps Interstate |
|  |  | QLXZ | Frame Relay- 128 Kbps Official company service (OCS) |
| QSEC | DS0 – 56 Kbps - Interstate | QSYX | Packet-Synchronous Access Line Interstate |
|  |  | QSXZ | Packet-Synchronous Access Line Official company service (OCS) |
| RTEC | DS0 – 56 Kbps - Interstate | RTYX | Radio Land Line Interstate |
|  |  | RTXZ | Radio Land Line Official company service (OCS) |
| SAEC | DS0 – 56 Kbps - Interstate | SAYX | Satellite/Tributary Tie Trunk Interstate |
|  |  | SAXZ | Satellite/Tributary Tie Trunk Official company service (OCS) |
| SNEC | DS0 – 56 Kbps - Interstate | SNYX | SST Special Access Termination Interstate |
|  |  | SNXZ | SST Special Access Termination Official company service (OCS) |
| SSEC | DS0 – 56 Kbps - Interstate | SSYX | Data-A-Phone® Select A Station Interstate |
|  |  | SSXZ | Data-A-Phone® Select A Station Official company service (OCS) |
| TAEC | DS0 – 56 Kbps - Interstate | TAYX | Tandem Tie Trunk Interstate |
|  |  | TAXZ | Tandem Tie Trunk Official company service (OCS) |
| TDEC | DS0 – 56 Kbps - Interstate | VVYX | Component Serial Digital Video –Uncompressed (I.e., 270 Mbps) Interstate |
|  |  | VVXZ | Component Serial Digital Video –Uncompressed (I.e., 270 Mbps) Official company service (OCS) |
| TLEC | DS0 – 56 Kbps - Interstate | TLYX | Non-Tandem Tie Trunk Interstate |
|  |  | TLXZ | Non-Tandem Tie Trunk Official company service (OCS) |
| UGDC UGEC | IBR – 832 Kbps - Interstate | GLYX | Digital Data - 832 Kbps Interstate |
|  |  | GLXZ | Digital Data - 832 Kbps Official company service (OCS) |
| UHDC UHEC | IBR – 896 Kbps - Interstate | GMYX | Digital Data - 896 Kbps Interstate |
|  |  | GMXZ | Digital Data - 896 Kbps Official company service (OCS) |
| UIDC UIEC | IBR – 960 Kbps - Interstate | GNYX | Digital Data - 960 Kbps Interstate |
|  |  | GNXZ | Digital Data - 960 Kbps Official company service (OCS) |
| UJDC UJEC | IBR – 1280 Kbps - Interstate | GSYX | Digital Data - 1280 Kbps Interstate |
|  |  | GSXZ | Digital Data - 1280 Kbps Official company service (OCS) |
| UTYX | OTN - OTU-1 Signal - Interstate | UTYX | OTN - OTU-1 Signal - Interstate |
| UVYX | OTN - OTU-2 Signal - Interstate | UVYX | OTN - OTU-2 Signal - Interstate |
| UWYX | OTN - OTU-3 Signal - Interstate | UWYX | OTN - OTU-3 Signal - Interstate |
| VLEC | VLAN - Interstate | CUYX | Metro Ethernet Virtual Connections (EVC/OVC) Interstate |
|  |  | CUXZ | Metro Ethernet Virtual Connections (EVC/OVC) Official company service (OCS) |
| VMEC | DS0 – 56 Kbps - Interstate | VMYX | Control/Remote Metering Voice Grade Interstate |
|  |  | VMXZ | Control/Remote Metering Voice Grade Official company service (OCS) |
| ZCEC | DS0 – 56 Kbps - Interstate | ZCYX | Call and Talk Circuits Interstate |
|  |  | ZCXZ | Call and Talk Circuits Official company service (OCS) |
| ZPEC | DS0 – 56 Kbps - Interstate | ZPYX | Test Circuits, Plant Service Center Interstate |
|  |  | ZPXZ | Test Circuits, Plant Service Center Official company service (OCS) |
| ZVEC | DS0 – 56 Kbps - Interstate | ZVYX | Order Circuits –Service Interstate |
|  |  | ZVXZ | Order Circuits –Service Official company service (OCS) |

Section 2: InterLATA Core AT&T (cT) CLCI S/S Coding for Ethernet Services

| Classic T Equivalent Service Code | COMPLIANT Service Code and Interstate Modifier Combination | Compliant Service Code Definition which signifies the Ethernet Port rate | Classic T 02 FIC | Classic T 04 FIC |
| --- | --- | --- | --- | --- |
| BB (GIGE - 50M) | L1YX | Rate adjustable Ethernet - 1 Gbps | 2ET050 | 4ET050 |
| BB (GIGE - 50M) | L2YX | Rate adjustable Ethernet - 100 Mbps. | 2ET050 | 4ET050 |
| BB (GIGE - 50M) | L4YX | Rate adjustable Ethernet - 10 Gbps | 2ET050 | 4ET050 |
| BC (GIGE - 150M) | L1YX | Rate adjustable Ethernet - 1 Gbps | 2ET150 | 4ET150 |
| BC (GIGE - 150M) | L4YX | Rate adjustable Ethernet - 10 Gbps | 2ET150 | 4ET150 |
| BD (GIGE - 300M) | L1YX | Rate adjustable Ethernet - 1 Gbps | 2ET300 | 4ET300 |
| BD (GIGE - 300M) | L4YX | Rate adjustable Ethernet - 10 Gbps | 2ET300 | 4ET300 |
| BE (GIGE - 600M) | L1YX | Rate adjustable Ethernet - 1 Gbps | 2ET600 | 4ET600 |
| BE (GIGE - 600M) | L4YX | Rate adjustable Ethernet - 10 Gbps | 2ET600 | 4ET600 |
| BF (GIGE - 10G) | L4YX | Rate adjustable Ethernet - 10 Gbps | 2ET10G | 4ET10G |
| BK (GIGE - 200M) | L1YX | Rate adjustable Ethernet - 1 Gbps | 2ET200 | 4ET200 |
| BK (GIGE - 200M) | L4YX | Rate adjustable Ethernet - 10 Gbps | 2ET200 | 4ET200 |
| BL (GIGE - 400M) | L1YX | Rate adjustable Ethernet - 1 Gbps | 2ET400 | 4ET400 |
| BL (GIGE - 400M) | L4YX | Rate adjustable Ethernet - 10 Gbps | 2ET400 | 4ET400 |
| BM (GIGE - 500M) | L1YX | Rate adjustable Ethernet - 1 Gbps | 2ET500 | 4ET500 |
| BM (GIGE - 500M) | L4YX | Rate adjustable Ethernet - 10 Gbps | 2ET500 | 4ET500 |
| BN (GIGE - 700M) | L1YX | Rate adjustable Ethernet - 1 Gbps | 2ET700 | 4ET700 |
| BN (GIGE - 700M) | L4YX | Rate adjustable Ethernet - 10 Gbps | 2ET700 | 4ET700 |
| BP (GIGE - 800M) | L1YX | Rate adjustable Ethernet - 1 Gbps | 2ET800 | 4ET800 |
| BP (GIGE - 800M) | L4YX | Rate adjustable Ethernet - 10 Gbps | 2ET800 | 4ET800 |
| BQ (GIGE - 900M) | L1YX | Rate adjustable Ethernet - 1 Gbps | 2ET900 | 4ET900 |
| BQ (GIGE - 900M) | L4YX | Rate adjustable Ethernet - 10 Gbps | 2ET900 | 4ET900 |
| BR (GIGE - 250M) | L1YX | Rate adjustable Ethernet - 1 Gbps | 2ET250 | 4ET250 |
| BR (GIGE - 250M) | L4YX | Rate adjustable Ethernet - 10 Gbps | 2ET250 | 4ET250 |
| BS (Ethernet - 450M) | L1YX | Rate adjustable Ethernet - 1 Gbps | 2ET450 | 4ET450 |
| BS (Ethernet - 450M) | L4YX | Rate adjustable Ethernet - 10 Gbps | 2ET450 | 4ET450 |
| IU (Ethernet - 100M) | L1YX | Rate adjustable Ethernet - 1 Gbps | 2ET100 | 4ET100 |
| IU (Ethernet - 100M) | L2YX | Rate adjustable Ethernet - 100 Mbps. | 2ET100 | 4ET100 |
| IU (Ethernet - 100M) | L4YX | Rate adjustable Ethernet - 10 Gbps | 2ET100 | 4ET100 |
| IZ (GIGE - 1G) | L1YX | Rate adjustable Ethernet - 1 Gbps | 2ET1GB | 4ET1GB |
| IZ (GIGE - 1G) | L4YX | Rate adjustable Ethernet - 10 Gbps | 2ET1GB | 4ET1GB |
| KP (Rate adjustable Ethernet - 10 Mbps) | L3YX | Rate adjustable Ethernet - 10 Mbps | 2ET010 | 4ET010 |
| KQ (Rate adjustable Ethernet - 100 Mbps) | L2YX | Rate adjustable Ethernet - 100 Mbps. | 2ET100 | 4ET100 |
| KR (Rate adjustable Ethernet - 1 Gbps) | L1YX | Rate adjustable Ethernet - 1 Gbps | 2ET1GB | 4ET1GB |
| L1YX | L1YX | Rate adjustable Ethernet - 1 Gbps -Interstate |  |  |
| L2YX | L2YX | Rate adjustable Ethernet - 100 Mbps -Interstate |  |  |
| L3YX | L3YX | Rate adjustable Ethernet - 10 Mbps-Interstate |  |  |
| L4YX | L4YX | Rate adjustable Ethernet - 10 Gbps-Interstate |  |  |
| L5YX | L5YX | Rate adjustable Ethernet - 40 Gbps-Interstate |  |  |
| L6YX | L6YX | Rate adjustable Ethernet - 100 Gbps-Interstate |  |  |
| KJ (Ethernet Connection Operating at 100 Gbps) | L8YX | Ethernet connection operating at 100 Gbps | 2ET100G | 4ET100G |
| MB (Ethernet - 1M) | L1YX | Rate adjustable Ethernet - 1 Gbps | 2ET001 | 4ET001 |
| MB (Ethernet - 1M) | L2YX | Rate adjustable Ethernet - 100 Mbps. | 2ET001 | 4ET001 |
| MB (Ethernet - 1M) | L3YX | Rate adjustable Ethernet - 10 Mbps | 2ET001 | 4ET001 |
| MB (Ethernet - 1M) | L4YX | Rate adjustable Ethernet - 10 Gbps | 2ET001 | 4ET001 |
| MC (Ethernet - 2M) | L1YX | Rate adjustable Ethernet - 1 Gbps | 2ET002 | 4ET002 |
| MC (Ethernet - 2M) | L2YX | Rate adjustable Ethernet - 100 Mbps. | 2ET002 | 4ET002 |
| MC (Ethernet - 2M) | L3YX | Rate adjustable Ethernet - 10 Mbps | 2ET002 | 4ET002 |
| MC (Ethernet - 2M) | L4YX | Rate adjustable Ethernet - 10 Gbps | 2ET002 | 4ET002 |
| MD (Ethernet - 3M) | L1YX | Rate adjustable Ethernet - 1 Gbps | 2ET003 | 4ET003 |
| MD (Ethernet - 3M) | L2YX | Rate adjustable Ethernet - 100 Mbps. | 2ET003 | 4ET003 |
| MD (Ethernet - 3M) | L3YX | Rate adjustable Ethernet - 10 Mbps | 2ET003 | 4ET003 |
| MD (Ethernet - 3M) | L4YX | Rate adjustable Ethernet - 10 Gbps | 2ET003 | 4ET003 |
| ME (Ethernet - 4M) | L1YX | Rate adjustable Ethernet - 1 Gbps | 2ET004 | 4ET004 |
| ME (Ethernet - 4M) | L2YX | Rate adjustable Ethernet - 100 Mbps. | 2ET004 | 4ET004 |
| ME (Ethernet - 4M) | L3YX | Rate adjustable Ethernet - 10 Mbps | 2ET004 | 4ET004 |
| ME (Ethernet - 4M) | L4YX | Rate adjustable Ethernet - 10 Gbps | 2ET004 | 4ET004 |
| MF (Ethernet - 5M) | L1YX | Rate adjustable Ethernet - 1 Gbps | 2ET005 | 4ET005 |
| MF (Ethernet - 5M) | L2YX | Rate adjustable Ethernet - 100 Mbps. | 2ET005 | 4ET005 |
| MF (Ethernet - 5M) | L3YX | Rate adjustable Ethernet - 10 Mbps | 2ET005 | 4ET005 |
| MF (Ethernet - 5M) | L4YX | Rate adjustable Ethernet - 10 Gbps | 2ET005 | 4ET005 |
| MG (Ethernet - 6M) | L1YX | Rate adjustable Ethernet - 1 Gbps | 2ET006 | 4ET006 |
| MG (Ethernet - 6M) | L2YX | Rate adjustable Ethernet - 100 Mbps. | 2ET006 | 4ET006 |
| MG (Ethernet - 6M) | L3YX | Rate adjustable Ethernet - 10 Mbps | 2ET006 | 4ET006 |
| MG (Ethernet - 6M) | L4YX | Rate adjustable Ethernet - 10 Gbps | 2ET006 | 4ET006 |
| MH (Ethernet - 7M) | L1YX | Rate adjustable Ethernet - 1 Gbps | 2ET007 | 4ET007 |
| MH (Ethernet - 7M) | L2YX | Rate adjustable Ethernet - 100 Mbps. | 2ET007 | 4ET007 |
| MH (Ethernet - 7M) | L3YX | Rate adjustable Ethernet - 10 Mbps | 2ET007 | 4ET007 |
| MH (Ethernet - 7M) | L4YX | Rate adjustable Ethernet - 10 Gbps | 2ET007 | 4ET007 |
| MJ (Ethernet - 8M) | L1YX | Rate adjustable Ethernet - 1 Gbps | 2ET008 | 4ET008 |
| MJ (Ethernet - 8M) | L2YX | Rate adjustable Ethernet - 100 Mbps. | 2ET008 | 4ET008 |
| MJ (Ethernet - 8M) | L3YX | Rate adjustable Ethernet - 10 Mbps | 2ET008 | 4ET008 |
| MJ (Ethernet - 8M) | L4YX | Rate adjustable Ethernet - 10 Gbps | 2ET008 | 4ET008 |
| ML (Ethernet - 10M) | L1YX | Rate adjustable Ethernet - 1 Gbps | 2ET010 | 4ET010 |
| ML (Ethernet - 10M) | L2YX | Rate adjustable Ethernet - 100 Mbps. | 2ET010 | 4ET010 |
| ML (Ethernet - 10M) | L3YX | Rate adjustable Ethernet - 10 Mbps | 2ET010 | 4ET010 |
| ML (Ethernet - 10M) | L4YX | Rate adjustable Ethernet - 10 Gbps | 2ET010 | 4ET010 |
| MM (Ethernet - 20M) | L1YX | Rate adjustable Ethernet - 1 Gbps | 2ET020 | 4ET020 |
| MM (Ethernet - 20M) | L2YX | Rate adjustable Ethernet - 100 Mbps. | 2ET020 | 4ET020 |
| MM (Ethernet - 20M) | L4YX | Rate adjustable Ethernet - 10 Gbps | 2ET020 | 4ET020 |
| MN (Ethernet - 30M) | L1YX | Rate adjustable Ethernet - 1 Gbps | 2ET030 | 4ET030 |
| MN (Ethernet - 30M) | L2YX | Rate adjustable Ethernet - 100 Mbps. | 2ET030 | 4ET030 |
| MN (Ethernet - 30M) | L4YX | Rate adjustable Ethernet - 10 Gbps | 2ET030 | 4ET030 |
| MP (Ethernet - 40M) | L1YX | Rate adjustable Ethernet - 1 Gbps | 2ET040 | 4ET040 |
| MP (Ethernet - 40M) | L2YX | Rate adjustable Ethernet - 100 Mbps. | 2ET040 | 4ET040 |
| MP (Ethernet - 40M) | L4YX | Rate adjustable Ethernet - 10 Gbps | 2ET040 | 4ET040 |
| MQ (Ethernet - 60M) | L1YX | Rate adjustable Ethernet - 1 Gbps | 2ET060 | 4ET060 |
| MQ (Ethernet - 60M) | L2YX | Rate adjustable Ethernet - 100 Mbps. | 2ET060 | 4ET060 |
| MQ (Ethernet - 60M) | L4YX | Rate adjustable Ethernet - 10 Gbps | 2ET060 | 4ET060 |
| MS (Ethernet - 70M) | L1YX | Rate adjustable Ethernet - 1 Gbps | 2ET070 | 4ET070 |
| MS (Ethernet - 70M) | L2YX | Rate adjustable Ethernet - 100 Mbps. | 2ET070 | 4ET070 |
| MS (Ethernet - 70M) | L4YX | Rate adjustable Ethernet - 10 Gbps | 2ET070 | 4ET070 |
| MT (Ethernet - 75M) | L1YX | Rate adjustable Ethernet - 1 Gbps | 2ET075 | 4ET075 |
| MT (Ethernet - 75M) | L2YX | Rate adjustable Ethernet - 100 Mbps. | 2ET075 | 4ET075 |
| MT (Ethernet - 75M) | L4YX | Rate adjustable Ethernet - 10 Gbps | 2ET075 | 4ET075 |
| MU (Ethernet - 80M) | L1YX | Rate adjustable Ethernet - 1 Gbps | 2ET080 | 4ET080 |
| MU (Ethernet - 80M) | L2YX | Rate adjustable Ethernet - 100 Mbps. | 2ET080 | 4ET080 |
| MU (Ethernet - 80M) | L4YX | Rate adjustable Ethernet - 10 Gbps | 2ET080 | 4ET080 |
| MV (Ethernet - 90M) | L1YX | Rate adjustable Ethernet - 1 Gbps | 2ET090 | 4ET090 |
| MV (Ethernet - 90M) | L2YX | Rate adjustable Ethernet - 100 Mbps. | 2ET090 | 4ET090 |
| MV (Ethernet - 90M) | L4YX | Rate adjustable Ethernet - 10 Gbps | 2ET090 | 4ET090 |
| MW (Ethernet - 0.5M) | L1YX | Rate adjustable Ethernet - 1 Gbps | 2ET0P5 | 4ET0P5 |
| MW (Ethernet - 0.5M) | L2YX | Rate adjustable Ethernet - 100 Mbps. | 2ET0P5 | 4ET0P5 |
| MW (Ethernet - 0.5M) | L3YX | Rate adjustable Ethernet - 10 Mbps | 2ET0P5 | 4ET0P5 |
| MW (Ethernet - 0.5M) | L4YX | Rate adjustable Ethernet - 10 Gbps | 2ET0P5 | 4ET0P5 |
| MX (Ethernet - 1.5M) | L1YX | Rate adjustable Ethernet - 1 Gbps | 2ET1P5 | 4ET1P5 |
| MX (Ethernet - 1.5M) | L2YX | Rate adjustable Ethernet - 100 Mbps. | 2ET1P5 | 4ET1P5 |
| MX (Ethernet - 1.5M) | L3YX | Rate adjustable Ethernet - 10 Mbps | 2ET1P5 | 4ET1P5 |
| MX (Ethernet - 1.5M) | L4YX | Rate adjustable Ethernet - 10 Gbps | 2ET1P5 | 4ET1P5 |

# Text boxes

AT&T

TAB 12

Private Line

CLCI S/S

Codes