Notes for entire document:

This Tab has been consolidated for all AT&T regions.  For the purposes of this document MW = AT&T Midwest region; SW = AT&T Southwest region; SE = AT&T Southeast region; W = AT&T West region.

Sample Network Channel (NC) Code format:

All four-character positions on an NC code must be filled to retain its 4-character structure.

- A hyphen (-) is a special that is used in positions 3 and/or 4 of the NC code to indicate a specific option, or to indicate the absence of features or options.

AT&T has removed references to many of the older technology related NC codes (Voice Grade, DS2, Fractional DS1s, etc.).    This is part of our “Six Sigma” clean-up effort to streamline the AT&T Carrier Coding Guide (CCG) usage and improve the overall Customer Experience.  If you do wish to order a coding combination that is no longer reflected; if you are an External Customer, please contact your AT&T Account Manager.  If you are an internal AT&T employee, please contact your AT&T Common Language® (CL) Coordinator, Diane Fletcher (df1685@att.com ) or 770-650-5841.

| NC | Network Channel Code Description | Pages |
| --- | --- | --- |
| AD | 2-Wire IDSL Capable Loop (Details in TAB 10) | 5 |
| BF | Broadband Facility | 5 |
| DS | Dense Wave Division Multiplexing (DWDM) system with a maximum of 2.5 Gbps per wavelength (Grandfathered for use only with existing rings) | 5 |
| DT | Dense Wave Division Multiplexing (DWDM) system with a maximum of 10 Gbps per wavelength | 5 |
| HC | DS1, High-Capacity Channel Service HC1, 1.544 Mbps | 5 |
| HE | DS2, High-Capacity Channel Service HC2, 6.312 Mbps | 12 |
| HF | DS3, High-Capacity Channel Service HC3, 44.736 Mbps | 13 |
| HH | DS5, High-Capacity Channel Service HC5, greater than 44.736 Mbps | 16 |
| HX | DS1, Fractional T1 | 16 |
| JI | SONET Electrical STS-1, 51.84 Mbps (Details in TAB 2, 10 and 15) | 17 |
| KD | Ethernet at 100 Mbps | 17 |
| KE | Ethernet at 100 Mbps | 17 |
| KF | Ethernet at 1 Gpbs | 17 |
| KG | Ethernet at 10 Gpbs | 17 |
| KH | Ethernet at 40 Gbps | 17 |
| KJ | Ethernet at 100 Gbps | 17 |
| KM | Ethernet at 400 Gbps | 17 |
| KP | Ethernet, Rate-Adjustable 10 Mbps Ethernet | 18 |
| KQ | Ethernet, Rate-Adjustable 100 Mbps Ethernet | 18 |
| KR | Ethernet, Rate-Adjustable 1 Gigabit Ethernet (Full Duplex) | 20 |
| KS | Ethernet, Rate-Adjustable 10 Gigabit Ethernet (Full Duplex) | 25 |
| KU | Ethernet, Rate-Adjustable 100 Gbps Ethernet | 26 |
| LB | Voice Grade Channel Service VG1, Non-Switched Line | 28 |
| LC | Voice Grade Channel Service VG2, Switched Line | 28 |
| LD | Voice Grade Channel Service VG3, Switched Trunk | 28 |
| LE | Voice Grade Channel Service VG4, Voice & Tone - Radio Land Line | 28 |
| LF | Voice Grade Channel Service VG5, Data, Low Speed | 29 |
| LG | Voice Grade Channel Service VG6, Basic Data and Voice | 29 |
| LH | Voice Grade Channel Service VG7, Voice and Data - PSN Access Tie Trunk | 29 |
| LJ | Voice Grade Channel Service VG8, Voice and Data - SSN Access | 30 |
| LN | Voice Grade Channel Service VG10, Data Extension, Voice Grade Data Facility | 31 |
| LR | Voice Grade Channel Service VG12, Protective Relay - Voice Grade | 31 |
| LX | Unbundled Dedicated Facility without equipment, dark fiber or copper loops with nominal 1004 Hz transducer loss of 8dB (unless otherwise specified) per T1.TRQ.7-2002 (Details in Tab 10) | 33 |
| LY | Unbundled Dedicated Facility with equipment, copper loops with nominal 1004 Hz transducer loss of 8dB (unless otherwise specified) per T1.TRQ.7-2002 (Details in Tab 10) | 33 |
| NT | Metallic/Telegraph Channel Service MT1, Protective Alarm - Metallic | 33 |
| NY | Metallic/Telegraph Channel Service TG2, Telegraph Grade Facility - 150 Baud | 33 |
| OB | SONET, OC3, 155.520 Mbps (Details in TAB 2 for OB-P and TAB 15 for other OB codes) | 34 |
| OD | SONET, OC12 Signal, 622.080 Mbps (Details in TAB 15) | 34 |
| OF | SONET, OC48 Signal 2488.320 Mbps (Details in TAB 15) | 34 |
| OG | SONET, OC192 Signal 9953.280 Mbps~SONET (Details in TAB 15) | 34 |
| OJ | OTN, OTU-1, Optical Transport Network (OTN) per ITU-T G.709 OTU 1 (255/238 x 2.488 3202.666057143 Gbps) also referred to as 2.7 Gbps. | 35 |
| OK | Optical Transport Network (OTN) OTU2 per ITU-T G.709 | 35 |
| OL | OTN, OTU-3, Optical Transport Network (OTN) per ITU-T G.709 OTU3 (255/236 x 39.813120 Gbps = 43.018413559 Gbps) also referred to as 43 Gbps. | 35 |
| OM | OTN, OTU-4, Optical Transport Network (OTN) per ITU-T G.709 OTU4 also referred to as 111.108 Gbps | 35 |
| OP | LAN, Optical Data Transport | 35 |
| OW | SDH, Optical STM-64 per ITU G.707 9953.280 Mbps | 37 |
| OX | SONET, Flexible Rate (Details in TAB 15) | 37 |
| PE | Program Audio Channel Service AP1, 200-3500 Hz | 37 |
| PF | Program Audio Channel Service AP2, 100-5000 Hz | 37 |
| PI | Wavelength Channel, Protocol Independent and Bit Rate Variable channel on DWDM | 37 |
| PJ | Program Audio Channel Service AP3, 50-8000 Hz | 38 |
| PK | Program Audio Channel Service AP4, 50-15,000 Hz | 38 |
| RP | Packet Ring Segment (Details in Tab 15) | 38 |
| SD | Switched Access 4-wire (Details in Tab 2 and 10) | 40 |
| SE | WATS Access Line - Standard | 42 |
| SF | WATS Access Line - Improved | 42 |
| SH | 4-Wire Switched Access Transmission Type A1 | 44 |
| SY | Synchronous Timing | 44 |
| SZ | Electronic Business Service | 44 |
| TD | Video, Serial Digital Video up to. 270 Mbps (Details in TAB 19) |  |
| TE | Component Serial Digital Video ~ Compressed (e.g. 270 Mb/s) (Details in TAB 19) |  |
| TR | Video, Flexible Rate (Details in TAB 19) |  |
| TS | Super Trunk Video, A 1Ghz or less Trunk TV5 for one-way Video (Details in TAB 19) |  |
| TV | Television Channel Service TV1, Video and Optional Audio (Details in TAB 19) |  |
| TZ | Video, Non-broadcast transmission of a 525 Line 60 field System M-NTSC composite television signal & Audio Channels. TV3 (Details in TAB 19) |  |
| UA | Line Sharing (CO based, and RT based) (See TAB 10 for details) |  |
| UB | Basic Rate ISDN (See TAB 10 for details) |  |
| UC | Voice Grade Channel Service VG32 - Voice Line (See TAB 10 for details) |  |
| UD | Voice Grade Channel Service VG33 - (UDG- Trunk for use with CALEA see TAB8a) all others (See TAB 10 for details) | 44 |
| UG | Voice Grade Channel Service VG36 - Analog Data (See TAB 10 for details) |  |
| UH | Voice Grade Channel Service - Digital High Capacity (See TAB 10 for details) |  |
| VL | Ethernet Virtual Connections (EVC) (See TAB 16 for details) | 45 |
| WA | Wideband Analog | 45 |
| WD | Wireline Transport for RF Spectrum (Future Offering) | 45 |
| WE | Wideband Digital WD2 Channel Service, 40.8 or 50 Kbps | 45 |
| XA | Digital Data, Digital Access Channel Service DA1 2.4 Kbps | 46 |
| XB | Digital Data, Digital Access Channel Service DA2 4.8 Kbps | 46 |
| XC | Digital Data, Digital Access Channel Service DA5 19.2 Kbps | 46 |
| XD | Digital Data, Digital Access Channel Service DA6 64 Kbps | 47 |
| XG | Digital Data, Digital Access Channel Service DA3 9.6 Kbps | 47 |
| XH | Digital Data, Digital Access Channel Service DA4 56 Kbps | 48 |
| XR | Digital Data Variable, Advanced Digital Network (ADN) | 49 |
| YH | DS3, Fractional DS3/NxDS1 (Limited Offering for BadgerNet) | 48 |
| YN | Signaling System 7 Links | 49 |

| NC Code | Description |
| --- | --- |
| ADPA (Not valid SE) | 2-Wire IDSL Capable Loop operating at 144 Kbps (Details in TAB 10) |

| NC Code | Description |
| --- | --- |
| BF- - (SE only) | Broadband Facility |
| BF- G (SE only) | Broadband Facility with Customer Reconfigurable |
| BFRG (SE only) | Broadband Facility Ring Topology with Customer Reconfigurable |

| NC Code | Description |
| --- | --- |
| DSDD (Not valid in SE) | Dense Wave Division Multiplexing (DWDM) system with a maximum of 2.5 Gbps per wavelength, Bi-directional Ring Segment, 16 wavelengths (Grandfathered for use only with existing rings) |
| DTDD | Dense Wave Division Multiplexing (DWDM) system with a maximum of 10 Gbps per wavelength, Bi-directional Ring Segment, 16 wavelengths |
| DTDE | Dense Wave Division Multiplexing (DWDM) system with a maximum of 10 Gbps per wavelength, Bi-directional Ring Segment, 32 wavelengths |
| DTDJ (SE only) | Dense Wave Division Multiplexing (DWDM) system with a maximum of 10 Gbps per wavelength, Bi-directional Ring Segment, 40 Wavelengths |

| NC Code | Description |
| --- | --- |
| HC-- | Digital High-Capacity Channel Service HC1 (DS1) - SF & AMI |
| HC-C (MW, SE, W only) | DS1, High-Capacity Channel Service HC1, 1.544 Mbps SF & AMI Customer Reconfigurable |
| HC-D | Digital High-Capacity Channel Service HC1 (DS1) - SF & AMI Direct Digital Connection on a Switch |
| HC-G (MW, W only) | Digital High-Capacity Channel Service HC1, 1.544 Mbps SF & AMI Central Office Multiplexer for analog and digital DS0 offerings |
| HC-H | Digital High-Capacity Channel Service HC1, 1.544 Mbps SF & AMI Direct Digital Connection on a switch with Common Channel Signaling (SS7) (to be used for either SS7 Links or SS7 Trunks terminating directly to a Switch) |
| HC-M | Digital High-Capacity Channel Service HC1, 1.544 Mbps SF & AMI CO Mux DS1 to Analog Voice (VG & Megalink may be mixed in SW) |
| HC-S (Not valid in SE) | Digital High-Capacity Channel Service HC1 (DS1) - SF & AMI - Central Office Multiplexer for analog and digital DS0 offerings + SS7 (Links) |
| HC-T | Digital High-Capacity Channel Service HC1 (DS1) - SF & AMI - and Transfer Arrangement |
| HC-V (MW only) | DS1 with SF & AMI Customer Reconfigurable + Central Office Multiplexer for analog and digital DS0 offerings |
| HC-Y | Digital High-Capacity Channel Service HC1 (DS1)-SF & AMI-with MUX at both ends |
| HC-7 (Not valid in SE) | Digital High-Capacity Channel Service HC1, 1.544 Mbps SF & AMI with Direct Digital connection on a Switch at both ends |
| HC-8 (Not valid in SE) | Digital High-Capacity Channel Service HC1, 1.544 Mbps SF & AMI with Multiplexer to a Switch |
| HCC- | Digital High-Capacity Channel Service HC1, 1.544 Mbps Central Office Termination at a DSX-1 Frame |
| HCCG | Digital High-Capacity Channel Service HC1, 1.544 Mbps Central Office Termination at a DSX-1 Frame Voice/Digital Multiplexer, SF & AMI (additional info: used in AT&T CO for Centrex or Plexar Services, or Digital Loop Services where the multiplexing function is billed external to the DS1 Service) |
| HCCH | Digital High-Capacity Channel Service HC1, 1.544 Mbps Central Office Termination at a DSX-1 Frame, Voice/Digital Multiplexer, SF & B8ZS (additional info: used in AT&T CO for Centrex or Plexar Services, or Digital Loop Services where the multiplexing function is billed external to the DS1 Service) |
| HCCK | Digital High-Capacity Channel Service HC1, 1.544 Mbps Central Office Termination at a DSX-1 Frame, Voice/Digital Multiplexer, ESF & AMI (additional info: used in AT&T CO for Centrex or Plexar Services, or Digital Loop Services where the multiplexing function is billed external to the DS1 Service) |
| HCCL | Digital High-Capacity Channel Service HC1, 1.544 Mbps Central Office Termination at a DSX-1 Frame, Voice/Digital Multiplexer, ESF & B8ZS (additional info: used in AT&T CO for Centrex or Plexar Services, or Digital Loop Services where the multiplexing function is billed external to the DS1 Service) |
| HCD- | Digital High-Capacity Channel Service HC1 (DS1) - ESF & AMI – |
| HCDA (SW only) | Digital High-Capacity Channel Service HC1 (DS1) – ESF & AMI –Service to Service Through-Connect at 1.544 Mb/s (DS1) in an AT&T Hub(s). (Two CFAs are required.) |
| HCDC (MW, SE, W only) | Digital High-Capacity Channel Service HC1, 1.544 Mbps Extended Super Framing (ESF) and AMI Customer Reconfigurable |
| HCDD | Digital High-Capacity Channel Service HC1 (DS1) - ESF & AMI -Direct Digital Connection on a switch |
| HCDG (MW, W only) | Digital High-Capacity Channel Service HC1, 1.544 Mbps Extended Super Framing (ESF) and AMI Central Office Multiplexer for analog and digital DS0 offerings |
| HCDH (Not valid in SE) | Digital High-Capacity Channel Service HC1, 1.544 Mbps Extended Super Framing (ESF) and AMI Direct Digital Connection on a switch with Common Channel Signaling (SS7) (to be used for either SS7 Links or SS7 Trunks terminating directly to a Switch) |
| HCDM | Digital High-Capacity Channel Service HC1 (DS1) - ESF & AMI -C.O. Multiplexing - DS1 to Voice |
| HCDS (Not valid in SE) | Digital High-Capacity Channel Service HC1, 1.544 Mbps Extended Super Framing (ESF) and AMI- Central Office Multiplexer for analog and digital DS0 offerings + SS7 (to be used for SS7 Links) |
| HCDT (Not valid in SE) | Digital High-Capacity Channel Service HC1 (DS1) - ESF & AMI -and Transfer Arrangement |
| HCDV (MW only) | Digital High-Capacity Channel Service HC1, 1.544 Mbps Extended Super Framing (ESF) and AMI Customer Reconfigurable + Central Office Multiplexer for analog and digital DS0 offerings |
| HCD7 (Not valid in SE) | Digital High-Capacity Channel Service HC1, 1.544 Mbps Extended Super Framing (ESF) and AMI with Direct Digital connection on a Switch at both ends |
| HCD8 | Digital High-Capacity Channel Service HC1, 1.544 Mbps Extended Super Framing (ESF) and AMI with Multiplexer to a Switch |
| HCE- | Digital High-Capacity Channel Service HC1 (DS1) - ESF & B8ZS - |
| HCEA | Digital High-Capacity Channel Service HC1 (DS1) - ESF & B8ZS -Service to Service Through-Connect of two one ended DS3 carrier systems in an AT&T Hub(s). (Two CFAs are required.) |
| HCEC | Digital High-Capacity Channel Service HC1 (DS1) - ESF & B8ZS -and Customer Reconfigurable |
| HCED | Digital High-Capacity Channel Service HC1 (DS1) - ESF & B8ZS -Direct Digital Connection on a switch |
| HCEG (Not valid in SE) | Digital High-Capacity Channel Service HC1 Extended Super Framing (ESF) and & B8ZS CO Mux Analog and Digital to DS0 |
| HCEH (Not valid in SE) | Digital High-Capacity Channel Service HC1, 1.544 Mbps ESF & B8ZS Direct Digital Connection on a switch [DS1 connects to any digital switch DFI where the switch and the Cust. is protected with a back-up channel.] with Common Channel Signaling (SS7) (to be used for either SS7 Links or SS7 Trunks terminating directly to a Switch) |
| HCEI | Digital High-Capacity Channel Service HC1 (DS1) -Extended Super Framing (ESF) and B8ZS ISDN B + D |
| HCEJ (SW only) | Digital High-Capacity Channel Service HC1 (DS1) - ESF & B8ZS -ATM Termination OCD PORT (Note: this is available in TEXAS only) |
| HCEM | Digital High-Capacity Channel Service HC1 (DS1) - ESF & B8ZS -C.O. Multiplexing- DS1 to Voice |
| HCEO (SE only) | Digital High-Capacity Channel Service HC1 (DS1) - ESF & B8ZS - Digital Packet, Frame Relay, NNI, bi-directional polling |
| HCER (SE only) | Digital High-Capacity Channel Service HC1 (DS1) - ESF & B8ZS - Digital Packet Frame Relay UNI (uni-directional polling) |
| HCES (Not valid in SE) | Digital High-Capacity Channel Service HC1, 1.544 Mbps ESF & B8ZS - Central Office Multiplexer for analog and digital DS0 offerings + SS7 (to be used for SS7 Links) |
| HCET (Not valid in SE) | Digital High-Capacity Channel Service HC1 (DS1) - ESF & B8ZS -and Transfer Arrangement |
| HCEU | Digital High-Capacity Channel Service HC1 (DS1) - Extended Super Framing (ESF) and & B8ZS ~ Primary Rate ISDN, 24 B Channels |
| HCEV (MW only) | Digital High-Capacity Channel Service HC1, 1.544 Mbps ESF & B8ZS - Customer Reconfigurable + Central Office Multiplexer for analog and digital DS0 offerings |
| HCEX (SE only) | Digital High-Capacity Channel Service HC1, 1.544 Mbps ESF & B8ZS - Digital Packet SMDS ISSI |
| HCE3 (SE only) | Digital High-Capacity Channel Service HC1 (DS1) - ESF & B8ZS - Digital Packet SMDS SNI |
| HCE4 (SE only) | Digital High-Capacity Channel Service HC1 (DS1) - ESF & B8ZS - Digital Packet SMDS ICI |
| HCE5 (MW only) | Digital High-Capacity Channel Service HC1 (DS1) - ESF & B8ZS - Primary Rate ISDN back-up D-channel. |
| HCE6 (SE only) | Digital High-Capacity Channel Service HC1 (DS1) - ESF & B8ZS - Digital Packet ATM UNI |
| HCE7 (Not valid in SE) | Digital High-Capacity Channel Service HC1 (DS1) - ESF & B8ZS - Direct Digital Connection on a Switch at both ends |
| HCE8 (Not valid in SE) | Digital High-Capacity Channel Service HC1 (DS1) - ESF & B8ZS - with Multiplexer to a Switch |
| HCE9 (MW only) | Digital High-Capacity Channel Service HC1 (DS1) - ESF & B8ZS - High Speed Data (HSD) Termination for Unchannelized Application (e.g., IP Routing Device) (Limited for BadgerNET ~ Wisconsin only) |
| HCH- (SW only) | Digital High-Capacity Channel Service HC1 (DS1) - Self Healing and Disaster Recovery, e.g., Customer Survivability |
| HCHA (SW only) | Digital High-Capacity Channel Service HC1 (DS1) - Self Healing and Disaster Recovery, e.g., Customer Survivability ~ Loop Protection One End |
| HCHB (SW only) | Digital High-Capacity Channel Service HC1 (DS1) - Self Healing and Disaster Recovery, e.g., Customer Survivability ~ Central Office Multiplexer DS1 to DS0 Subrate (T1DM) + Alternate Route Protection, Loop-only |
| HCHD (SW only) | Digital High-Capacity Channel Service HC1 (DS1) - Self Healing and Disaster Recovery, e.g., Customer Survivability ~ Loop Protection (One End) and Facilities Protection, (i.e., SWC Protection) (e.g. SecureNet® Service, SWC/FAC Redundancy on one end of the circuit) |
| HCHE (SW only) | Digital High-Capacity Channel Service HC1 (DS1) - Self Healing and Disaster Recovery, e.g., Customer Survivability ~ Central Office Multiplexer DS1 to DS0 D4 Format + Loop and Facility Protection (e.g. SecureNet® Service, SWC/FAC Redundancy) |
| HCHF (SW only) | Digital High-Capacity Channel Service HC1 (DS1) - Self Healing and Disaster Recovery, e.g., Customer Survivability ~ Loop, Facilities and HUB Protection (Works in conjunction with similarly optioned DS3 Mux service) (e.g. SecureNet® Service, HUB Redundancy and SWC/FAC Redundancy and Secondary Channel) |
| HCHG (SW only) | Digital High-Capacity Channel Service HC1 (DS1) - Self Healing and Disaster Recovery, e.g., Customer Survivability ~ Central Office Multiplexer DS1 to DS0 Subrate (T1DM) E/W Secondary Channel + Loop Protection |
| HCHJ (SW only) | Digital High-Capacity Channel Service HC1 (DS1) - Self Healing and Disaster Recovery, e.g., Customer Survivability ~ Alternate Central Office Routing (e.g. SecureNet® Service, SWC/FAC Redundancy and Secondary Channel and DS1 multiplexed Service that terminates in an AT&T Central Office for Centrex or PLEXAR Service where the multiplexing function is billed external to the DS1 Service) |
| HCHL (SW only) | Digital High-Capacity Channel Service HC1 (DS1) - Self Healing and Disaster Recovery, e.g., Customer Survivability ~ Loop Protection, Thru Connect Circuit, i.e., Central Office DSX-1 Termination |
| HCHM (SW only) | Digital High-Capacity Channel Service HC1 (DS1) - Self Healing and Disaster Recovery, e.g., Customer Survivability ~ CO Multiplexer DS1 to Analog Voice or any DS0 Application + Loop Protection |
| HCHN (SW only) | Digital High-Capacity Channel Service HC1 (DS1) - Self Healing and Disaster Recovery, e.g., Customer Survivability ~ Loop and Facilities Protection, i.e., Serving Wire Center Protection for Thru Connect Circuit, DSX-1 (e.g. SecureNet® Service, SWC/FAC Redundancy and Secondary Channel) |
| HCHO (SW only) | Digital High-Capacity Channel Service HC1 (DS1) - Self Healing and Disaster Recovery, e.g., Customer Survivability ~ Loop Protection with Central Office DSX-1 Termination for CENTREX (Assoc. with SMARTTRUNKS) |
| HCHR (SW only) | Digital High-Capacity Channel Service HC1 (DS1) - Self Healing and Disaster Recovery, e.g., Customer Survivability ~ Central Office Multiplexer DS1 to DS0 Subrate (T1DM) & Loop and Facilities Protection i.e., SWC Protection (e.g. SecureNet® Service, SWC/FAC Redundancy and Secondary Channel) |
| HCHS (Not valid in SE, MW) | Digital High-Capacity Channel Service HC1 (DS1) - Self Healing and Disaster Recovery, e.g., Customer Survivability ~ Central Office Multiplexer DS1 to Analog Voice & Loop and Facilities Protection i.e., SWC Protection (e.g. SecureNet® Service, SWC/FAC Redundancy and Secondary Channel) |
| HCHT (SW only) | Digital High-Capacity Channel Service HC1 (DS1) - Self Healing and Disaster Recovery, e.g., Customer Survivability ~ Primary Rate ISDN, 23 B + D Channels (e.g. Identifies an HC1 (DS1) circuit that terminates in an AT&T central office switch that provides ISDN functionality, with loop protection. The framing format is ESF and B8ZS and ISDN 23B+D.) |
| HCHU (SW only) | Digital High-Capacity Channel Service HC1 (DS1) - Self Healing and Disaster Recovery, e.g., Customer Survivability ~ Primary Rate ISDN, 24 B Channels (e.g. Identifies an HC1 (DS1) circuit that terminates in an AT&T central office switch that provides ISDN functionality, with loop protection. The framing format is ESF and B8ZS and ISDN 24B.) |
| HCHX (W only) | Digital High-Capacity Channel Service HC1 Self healing and Disaster recovery e.g., Customer Survivability Loop protection with Intelligent Mux e.g., DCS |
| HCHY (SW only) | Digital High-Capacity Channel Service HC1 (DS1) - Self Healing and Disaster Recovery, e.g., Customer Survivability ~ Direct Digital Connection on a Switch + Loop Protection (Assoc. with SMARTTRUNKS) |
| HCKA (SW, SE only) | Digital High-Capacity Channel Service HC1 (DS1) - per TR08 Digital Loop Carrier (DLC) multiplexing (i.e., specific time slot to channel unit mapping). Non-concentrated AMI/SF 4 DS1s 96 Channels |
| HCKB (SW, SE only) | Digital High-Capacity Channel Service HC1 (DS1) - per TR08 Digital Loop Carrier (DLC) multiplexing (i.e., specific time slot to channel unit mapping). Non-concentrated B8ZS/SF 4 DS1s 96 Channels |
| HCKC (SW, SE only) | Digital High-Capacity Channel Service HC1 (DS1) - per TR08 Digital Loop Carrier (DLC) multiplexing (i.e., specific time slot to channel unit mapping). Non-concentrated B8ZS/ESF 4 DS1s 96 Channels |
| HCKD (Not valid in MW) | Digital High-Capacity Channel Service HC1 (DS1) - per TR08 Digital Loop Carrier (DLC) multiplexing (i.e., specific time slot to channel unit mapping). Concentrated AMI/SF 2 DS1s 96 Channels |
| HCKE (SW, SE only) | Digital High-Capacity Channel Service HC1 (DS1) - per TR08 Digital Loop Carrier (DLC) multiplexing (i.e., specific time slot to channel unit mapping). Concentrated B8ZS/SF 2 DS1s 96 Channels |
| HCKF (SW, SE only) | Digital High-Capacity Channel Service HC1 (DS1) - per TR08 Digital Loop Carrier (DLC) multiplexing (i.e., specific time slot to channel unit mapping). Concentrated B8ZS/ESF 2 DS1s 96 Channels |
| HCMA (Not valid in SE) | Digital High-Capacity Channel Service HC1 (DS1) - Service to Service Through-Connect at 1.544 Mbps (DS1) level with SF and AMI of two one ended DS3 carrier systems in an AT&T Hub(s). Two CFAs are required. |
| HCP- (Not valid in SE) | Digital High-Capacity Channel Service HC1 (DS1) – SF and AMI - Premium Service and Loop Protection (e.g., ReliaNet®) |
| HCPA (MW only) | Digital High-Capacity Channel Service HC1, 1.544 Mbps Premium Service Parameters, SF & AMI, CENTREX Termination |
| HCPD (Not valid in SE, W) | Digital High-Capacity Channel Service HC1 (DS1) – SF and AMI - Premium Service and Direct Switch Interface (e.g., ReliaNet®) |
| HCPF (SW only) | Digital High-Capacity Channel Service HC1 (DS1) – SF and AMI - Premium Service and FAC and SWC Protection (e.g., ReliaNet®) |
| HCPG (MW, SW only) | Digital High-Capacity Channel Service HC1 (DS1) – SF and AMI - Premium Service and and Multiplex termination at a switch. Billing for the multiplex is done elsewhere (e.g., ReliaNet® SONET Xpress) |
| HCPH (MW, SW only) | Digital High-Capacity Channel Service HC1, 1.544 Mbps Premium Service with SF & AMI Direct Digital Connection with Common Channel Signaling (SS7) (to be used for either SS7 Links or SS7 Trunks terminating directly to a Switch) (e.g., ReliaNet® and SONET Xpress) |
| HCPM (Not valid in SE) | Digital High-Capacity Channel Service HC1 (DS1) – SF and AMI - Premium Service and & MUX (e.g., ReliaNet®) |
| HCT- (Not valid in SE) | Digital High-Capacity Channel Service HC1 (DS1) – SF and B8ZS - Premium Service and Loop Protection (e.g., ReliaNet®) |
| HCTA (MW only) | Digital High-Capacity Channel Service HC1, 1.544 Mbps Premium Service Parameters, SF & B8ZS, CENTREX Termination |
| HCTD (Not valid in SE, W) | Digital High-Capacity Channel Service HC1 (DS1) – SF and B8ZS - Premium Service Direct Switch Interface (e.g., ReliaNet®) |
| HCTF (SW only) | Digital High-Capacity Channel Service HC1 (DS1) – SF and B8ZS - Premium Service FAC and SWC Protection (e.g., ReliaNet®) |
| HCTG (Not valid in SE, W) | Digital High-Capacity Channel Service HC1 (DS1) – SF and B8ZS - Premium Service and Multiplex termination at a switch. Billing for the multiplex is done elsewhere (e.g., ReliaNet®) |
| HCTH (Not valid in SE) | Digital High-Capacity Channel Service HC1, 1.544 Mbps Premium Service with SF & B8ZS Direct Digital Connection with Common Channel Signaling (SS7) (to be used for either SS7 Links or SS7 Trunks terminating directly to a Switch) (e.g., ReliaNet®) |
| HCTM (Not valid in SE) | Digital High-Capacity Channel Service HC1 (DS1) – SF and B8ZS - Premium Service & MUX (e.g., ReliaNet®) |
| HCU- | Digital High-Capacity Channel Service HC1 (DS1) – ESF and AMI - Premium Service and Loop Protection (e.g., ReliaNet®) |
| HCUA (MW only) | Digital High-Capacity Channel Service HC1, 1.544 Mbps Premium Service Parameters, ESF & AMI, CENTREX Termination |
| HCUD (Not valid in SE, W) | Digital High-Capacity Channel Service HC1 (DS1) – ESF and AMI - Premium Service and Direct Switch Interface (e.g., ReliaNet®) |
| HCUF (Not valid in SE, W) | Digital High-Capacity Channel Service HC1 (DS1) – ESF and AMI - Premium Service and FAC and SWC Protection (e.g., ReliaNet®) |
| HCUG (Not valid in SE, W) | Digital High-Capacity Channel Service HC1 (DS1) – ESF and AMI - Premium Service and Multiplex termination at a switch. Billing for the multiplex is done elsewhere (e.g., ReliaNet®) |
| HCUH (Not valid in SE) | Digital High-Capacity Channel Service HC1, 1.544 Mbps Premium Service, with ESF & AMI Direct Digital Connection with Common Channel Signaling (SS7) (to be used for either SS7 Links or SS7 Trunks terminating directly to a Switch) (e.g., ReliaNet®) |
| HCUM | Digital High-Capacity Channel Service HC1 (DS1) – ESF and AMI - Premium Service and MUX (e.g., ReliaNet®) |
| HCV- | Digital High-Capacity Channel Service HC1 (DS1) – ESF and B8ZS - Premium Service and Loop Protection (e.g., ReliaNet®) |
| HCVA (MW only) | Digital High-Capacity Channel Service HC1, 1.544 Mbps Premium Service Parameters, ESF & B8ZS and CENTREX Termination |
| HCVC (MW, SE only) | Digital High-Capacity Channel Service HC1, 1.544 Mbps Premium Service Parameters, ESF & B8ZS and Termination at a DSX-1 Frame |
| HCVD (Not valid in SE, W) | Digital High-Capacity Channel Service HC1 (DS1) – ESF and B8ZS - Premium Service and Direct Switch interface (e.g., ReliaNet®) |
| HCVE (Not valid in SE) | Digital High-Capacity Channel Service HC1, 1.544 Mbps Premium Service, with ESF & B8ZS Direct Digital Connection with Common Channel Signaling (SS7) (to be used for either SS7 Links or SS7 Trunks terminating directly to a Switch) (e.g., ReliaNet®) |
| HCVF (SW only) | Digital High-Capacity Channel Service HC1 (DS1) – ESF and B8ZS - Premium Service and FAC and Loop Protection (e.g., ReliaNet®) |
| HCVG (Not valid in SE, W) | Digital High-Capacity Channel Service HC1 (DS1) – ESF and B8ZS - Premium Service and Multiplex termination at a switch. Billing for the multiplex is done elsewhere (e.g., ReliaNet®) |
| HCVH (SW only) | Digital High-Capacity Channel Service HC1 (DS1) – ESF and B8ZS - Premium Service and Primary Rate ISDN, 23 B + D Channels, Backup D Channel |
| HCVI (MW only) | Digital High-Capacity Channel Service HC1 (DS1) – ESF and B8ZS - Premium Service and Primary Rate ISDN, 23 B + D Channels |
| HCVM | Digital High-Capacity Channel Service HC1 (DS1) – ESF and B8ZS - Premium Service and MUX (e.g., ReliaNet®) |
| HCVU (MW only) | Digital High-Capacity Channel Service HC1 (DS1) – ESF and B8ZS - Premium Service and Primary Rate ISDN, 24 B Channels |
| HCV6 (SE only) | Digital High-Capacity Channel Service HC1 (DS1) – ESF and B8ZS - Premium Service, Digital Packet ATM UNI; A termination on an ATM digital packet switch that is associated with a User to Network Interface |
| HCX- (Not valid in SE) | Digital High-Capacity Channel Service HC1, 1.544 Mbps, Central Office Cross Connect, DS1 to DS1 Intact with Format and line code of SF and AMI |
| HCXA (Not valid in SE) | Digital High-Capacity Channel Service HC1, 1.544 Mbps, Central Office Cross Connect, DS1 to DS1 Intact with Format and line code of SF and B8ZS |
| HCXD (Not valid in SE) | Digital High-Capacity Channel Service HC1, 1.544 Mbps, Central Office Cross Connect, DS1 to DS1 Intact with Format and line code of ESF and AMI |
| HCXE (Not valid in SE) | Digital High-Capacity Channel Service HC1, 1.544 Mbps, Central Office Cross Connect, DS1 to DS1 Intact with Format and line code of ESF and B8ZS |
| HCZ- | Digital High-Capacity Channel Service HC1 (DS1) – SF and B8ZS |
| HCZA (SW only) | Digital High-Capacity Channel Service HC1 (DS1) – SF and B8ZS Service to Service Through-Connect of two one ended DS3 carrier systems in an AT&T Hub(s). Two CFAs required. |
| HCZC (MW, SE, W only) | Digital High-Capacity Channel Service HC1, 1.544 Mbps, SF & B8ZS, Customer Reconfigurable |
| HCZD | Digital High-Capacity Channel Service HC1 (DS1) – SF and B8ZS - Direct Digital Connection on a Switch. |
| HCZG (Not valid in SE) | Digital High-Capacity Channel Service HC1 (DS1) – SF and B8ZS - C.O. Multiplexing for analog and digital DS0 offerings |
| HCZH (Not valid in SE) | Digital High-Capacity Channel Service HC1, 1.544 Mbps, SF & B8ZS, Direct Switch Interface with Common Channel Signaling (SS7) (to be used for either SS7 Links or SS7 Trunks terminating directly to a Switch) |
| HCZI (SW only) | Identifies an HC1 (DS1) circuit that terminates in an AT&T central office switch that provides ISDN functionality. The service is SF and B8ZS and ISDN 23 B+D |
| HCZM | Digital High-Capacity Channel Service HC1 (DS1) – SF and B8ZS - C.O. Multiplexing- DS1 to Voice (VG and Megalink may be mixed) |
| HCZS (Not valid in SE) | Digital High-Capacity Channel Service HC1, 1.544 Mbps SF & B8ZS - Central Office Multiplexer for analog and digital DS0 offerings + SS7 (to be used for SS7 Links) |
| HCZV (MW only) | Digital High-Capacity Channel Service HC1, 1.544 Mbps, SF & B8ZS, Customer Reconfigurable + Central Office Multiplexer for analog and digital DS0 offerings |
| HCZ7 (Not valid in SE) | Digital High-Capacity Channel Service HC1, 1.544 Mbps, SF & B8ZS, with Direct Digital connection on a Switch at both ends |
| HCZ8 (Not valid in SE) | Digital High-Capacity Channel Service HC1, 1.544 Mbps, SF & B8ZS, with Multiplexer to a Switch |

NOTE:  NC codes without CO multiplexing identify DS1 facilities where the customer has not purchased multiplexing at an AT&T Hub.  These facilities may terminate directly into an AT&T digital switch or into an AT&T analog switch via an AT&T provided multiplexer (DCT, D4 Bank).

NOTE:  The NC code set for DS1 Service has been restructured on a National Level by iconectiv (previously known as Telcordia Technologies).  The restructure has created redundant intelligence in the NC and NCI codes regarding the framing format and clear channel capability of the HC/DS1 Service.  On embedded HC/DS1 Service, the expanded NC code definition regarding the framing format/clear channel capability may conflict with the NCI definition.  In these situations, the NCI code will take precedence over the NC code.  New DS1 Services ordered after June 30, 1992, must have matching NC and NCI codes.

| NC Code | Description |
| --- | --- |
| HE- - (MW only) | DS2, High-Capacity Channel Service HC2, 6.312 Mbps |

| NC Code | Description |
| --- | --- |
| HF-- | Digital High-Capacity Channel Service HC3, 44.736 Mbps |
| HF-4 (MW only) | Digital High-Capacity Channel Service HC3, 44.736 Mbps, each of the 28 channels is broken down to 7 groups. Each of the 7 can deliver 4 DS1 channels w/B8ZS |
| HF-6 | Digital High-Capacity Channel Service HC3, 44.736 Mbps Digital Packet ATM UNI (to be used with an OCD Termination) |
| HF-7 (MW only) | Digital High-Capacity Channel Service HC3, 44.736 Mbps, each of the 28 channels is broken down to 4 groups. Each of the 4 can deliver 7 DS1 channels with B8ZS. |
| HF-9 (Not valid in SE) | Digital High-Capacity Channel Service HC3, 44.736 Mbps High Speed Data (HSD) Termination on a Router, (e.g., IP Routing functionality). (Future Offering) |
| HF-A (West only) | Digital High-Capacity Channel Service HC3, 44.736 Mbps PLCP Mapped ATM/ Cell Relay Cells |
| HF-D (SE only) | Digital High-Capacity Channel Service HC3, 44.736 Mbps - Digital Packet Frame Relay UNI, unidirectional polling |
| HF-F (SE only) | Digital High-Capacity Channel Service HC3, 44.736 Mbps - Digital Packet SMDS SNI |
| HF-G (SE only) | Digital High-Capacity Channel Service HC3, 44.736 Mbps - Digital Packet SMDS ICI |
| HF-J | Digital High-Capacity Channel Service HC3, 44.736 Mbps ATM Termination NNI (to be used with an OCD Termination). |
| HF-M | Digital High-Capacity Channel Service HC3, 44.736 Mbps C.O. Multiplexing |
| HF-P | Digital High-Capacity Channel Service HC3, 44.736 Mbps ~ Multiplexing at both ends (this code replaces HF-Y which was retired as of 1/1/03) |
| HF-Q (SE only) | Digital High-Capacity Channel Service HC3, 44.736 Mbps ~Non-CO Multiplexer |
| HF-T | Digital High-Capacity Channel Service HC3, 44.736 Mbps ~ Transmux Asymmetrical Multiplexer, M23 Format to DS1 for Mapping to VT1.5 |
| HF-V (Not valid in SE) | Digital High-Capacity Channel Svc HC3, 44.736 Mbps ~ Customer Reconfigurable |
| HF-X (SE only) | Digital High-Capacity Channel Svc HC3, 44.736 Mbps ~ Digital Termination SMDS ISSI. |
| HFC- | Digital High-Capacity Channel Service HC3, 44.736 Mbps ~ C-Bit Parity |
| HFC6 | Digital High-Capacity Channel Service HC3, 44.736 Mbps ~ M Framed C-Bit Parity Digital Packet ATM UNI ~ Line Sharing OCD Port |
| HFCD (SE only) | Digital High-Capacity Channel Service HC3, 44.736 Mbps. ~ C-Bit Parity Digital Packet Frame Relay UNI |
| HFCE (SE only) | Digital High-Capacity Channel Service HC3, 44.736 Mbps. ~ C-Bit Parity Digital Packet Frame Relay NNI |
| HFCJ (SE only) | Digital High-Capacity Channel Service HC3, 44.736 Mbps. ~ C-Bit Parity Termination at an ATM device. |
| HFCM (Not valid in SE) | Digital High-Capacity Channel Service HC3, 44.736 Mbps. ~ C-Bit Parity A 3/1 multiplexer is located at the Access Provider's CO |
| HFCT (Not valid in SE) | Digital High-Capacity Channel Service HC3, 44.736 Mbps. ~ C-Bit Parity Transmux Asymmetrical Multiplexer C-Bit Format to DS1 for Mapping to VT1.5 |
| HFH- (Not valid in SE, MW) | Digital High-Capacity Channel Service HC3, 44.736 Mbps ~ Self Healing, Disaster Recovery, e.g., Customer Survivability (e.g., SecureNet® Service, Option 2 Serving Wire Center (SWC)& Facility (FAX) Redundancy on one end of ckt) |
| HFHA (SW only) | Digital High-Capacity Channel Service HC3, 44.736 Mbps ~ Self Healing, Disaster Recovery, e.g., Customer Survivability Loop Protection, One-End Only (e.g., SecureNet® Service, Option 3) |
| HFHB (Not valid in SE, MW) | Digital High-Capacity Channel Service HC3, 44.736 Mbps ~ Self Healing, Disaster Recovery, e.g., Customer Survivability Loop Protection and B8ZS Compatible Central Office Multiplex (e.g., SecureNet® Service, Option 3) |
| HFHC (SW only) | Digital High-Capacity Channel Service HC3, 44.736 Mbps ~ Self Healing, Disaster Recovery, e.g., Customer Survivability Loop and Facilities Protection, i.e., SWC Protection for Thru connect circuit – i.e., DSX-1 (e.g., SecureNet® Service, Option 2) |
| HFHD (SW only) | Digital High-Capacity Channel Service HC3, 44.736 Mbps ~ Self Healing, Disaster Recovery, e.g., Customer Survivability Loop Protection Both Ends of Circuit W/O SWC Protection (e.g., SecureNet® Service, Option 3) |
| HFHE (Not valid in SE, MW) | Digital High-Capacity Channel Service HC3, 44.736 Mbps ~ Self Healing, Disaster Recovery, e.g., Customer Survivability Loop (Both Ends) & Facilites Protection, i.e., SWC. (e.g., SecureNet® Service, Option 2 SWC/FAX Redundancy on both ends of circuit) |
| HFHF (SW only) | Digital High-Capacity Channel Service HC3, 44.736 Mbps ~ Self Healing, Disaster Recovery, e.g., Customer Survivability Loop Protection Thru Connect Circuit i.e., SWC. (e.g., SecureNet® Service, Option 3 Loop Redundancy and Service to Service Through-Connect) |
| HFHG (SW only) | Digital High-Capacity Channel Service HC3, 44.736 Mbps ~ Self Healing, Disaster Recovery, e.g., Customer Survivability Loop and Facilities Protection with B8ZS Compatible CO Mux and Auto Hub Protection (e.g., SecureNet® Service, Option 1) |
| HFHH (SW only) | Digital High-Capacity Channel Service HC3, 44.736 Mbps ~ Self Healing, Disaster Recovery, e.g., Customer Survivability Loop & Facilities Protection with CO Mux & Auto Hub Protection (e.g., SecureNet® Service, Option 1) |
| HFHI (SW only) | Digital High-Capacity Channel Service HC3, 44.736 Mbps ~ Self Healing, Disaster Recovery, e.g., Customer Survivability Loop & Facility Protection, i.e., SWC Protection with B8ZS Compatible CO Mux (e.g., SecureNet® Service, Option 2) |
| HFHJ (Not valid in SE, MW) | Digital High-Capacity Channel Service HC3, 44.736 Mbps ~ Self Healing, Disaster Recovery, e.g., Customer Survivability Loop & Facility Protection, i.e., SWC Protection with CO Mux (e.g., SecureNet® Service, Option 2 SWC/FAX Redundancy) |
| HFHK (W only) | Digital High-Capacity Channel Service HC3, 44.736 Mbps ~ Self Healing Disaster Recovery (e.g., Customer Survivability ~ CO-to-CO MUX both ends |
| HFHL* (Not valid in SE, MW) | Digital High-Capacity Channel Service HC3, 44.736 Mbps ~ Self Healing, Disaster Recovery, e.g., Customer Survivability, Facility Protection w/o Loop Protection – Thru connect circuit, i.e., CO DSX-3 Termination & Auto Hub Protection. (e.g., SecureNet® Service, Option 2 SWC/FAX Redundancy, Service to Service Through-Connect and Dual Mode Interconnection to a Self-Healing Transport Network *NOTE: HFHL and HFHU must be ordered together.) |
| HFHM (Not valid in MW) | Digital High-Capacity Channel Service HC3, 44.736 Mbps ~ Self Healing, Disaster Recovery, e.g., Customer Survivability Loop Protection & CO Mux (e.g., SecureNet® Service, Option 3) |
| HFHN (SE, W only) | Self Healing Disaster Recovery e.g., Customer Survivability ~ CO-to-CO MUX both ends & B8ZS |
| HFHT (Not valid in SE, MW) | Digital High-Capacity Channel Service HC3, 44.736 Mbps ~ Self Healing, Disaster Recovery, e.g., Customer Survivability, Facility Protection ~ (e.g., Self-Healing Transport Network (STN)) |
| HFHU* (Not valid in SE, MW) | Digital High-Capacity Channel Service HC3, 44.736 Mbps ~ Self Healing, Disaster Recovery, e.g., Customer Survivability ~ Facility & Node Protection (e.g., Self-Healing Transport Network (STN) with Dual Mode Interconnection to SecureNet( Service with Option 2 *NOTE: HFHL &HFHU must be ordered together.) |
| HFHV (SW, SE only) | Digital High-Capacity Channel Service HC3, 44.736 Mbps ~ Self Healing, Disaster Recovery, e.g., Customer Survivability ~ Facility Protection & B8ZS Compatible CO Mux ~ (e.g., Self-Healing Transport Network (STN)) |
| HFHW (SW only) | Digital High-Capacity Channel Service HC3, 44.736 Mbps ~ Self Healing, Disaster Recovery, e.g., Customer Survivability ~ B8ZS Compatible CO Mux (e.g., Self-Healing Transport Network (STN)) |
| HFP- (Not valid in SE) | DS3, High-Capacity Channel Service HC3, 44.736 Mbps ~Premium Service Parameters (e.g., ReliaNet (SM) Service) |
| HFPF (Not valid in SE, W) | DS3, High-Capacity Channel Service HC3, 44.736 Mbps ~Premium Service Parameters Protection and dual feed (e.g., ReliaNet (SM) Service DS3 Pipe with FAC and SWC Protection) |
| HFPM (Not valid in SE) | DS3, High-Capacity Channel Service HC3, 44.736 Mbps ~Premium Service Parameters with CO Multiplexing (e.g., ReliaNet (SM) Service For switched FGB, FGC and FGD, only) |
| HFPQ (MW & W only) | DS3, High-Capacity Channel Service HC3, 44.736 Mbps ~Premium Service @ DS3 ~ Customer Premise MUX self healing network |
| HFPS (MW only) | Digital High-Capacity Channel Service HC3, 44.736 Mbps. Premium Service Parameters. Self-Healing Network |
| HFX- | DS3, High-Capacity Channel Service HC3, 44.736 Mbps ~ Central Office Cross Connect~ DS3 –DS3 |
| HFXM (Not valid in W) | DS3, High-Capacity Channel Service HC3, 44.736 Mbps ~ Central Office Cross Connect~ Central Office Multiplexing |
| HFZ- | DS3, High-Capacity Channel Service HC3, 44.736 Mbps ~ B8ZS Compatible |
| HFZM | DS3, High-Capacity Channel Service HC3, 44.736 Mbps ~ B8ZS Compatible C.O. Multiplexing |
| HFZP (SE, W only) | Digital High-Capacity Channel Service HC3, 44.736 Mbps B8ZS Compatible ~ MUX at both ends (this code replaced HFZY) |
| HFZQ (SE, W only) | Digital High-Capacity Channel Service HC3, 44.736 Mbps B8ZS Compatible ~ Customer Premises MUX |
| HFZR (SE, W only) | Digital High-Capacity Channel Svc HC3, 44.736 Mbps B8ZS Compatible~ (Retired Nationally. Use as an ICB with CL Coor. review) |
| HFZT (SE only) | Digital High-Capacity Channel Service HC3, 44.736 Mbps B8ZS Compatible ~ Transmux Asymmetrical Multiplexer, M23 Format to DS1 for Mapping to VT1.5 |
| HFZV (MW, W only) | Digital High-Capacity Channel Service HC3, 44.736 Mbps B8ZS Compatible ~ Customer Reconfigurable |

| NC Code | Description |
| --- | --- |
| HH- - (SE, W only) | Digital High-Capacity Channel Service HC5, greater than 44.736 Mbps |
| HH-M (MW only) | Digital High-Capacity Channel Service HC5, greater than 44.736 Mbps, Central Office Multiplexing |

| NC Code | Description |
| --- | --- |
| HXGB | Identifies a Fractional T1 utilizing 2 channels (128 kb/s) (for use w/AA+) |
| HXGD | Identifies a Fractional T1 utilizing 4 channels (256 kb/s) (for use w/AA+) |
| HXGF | Identifies a Fractional T1 utilizing 6 channels (384 kb/s) (for use w/AA+) |
| HXGH | Identifies a Fractional T1 utilizing 8 channels (512 kb/s) (for use w/AA+) |
| HXGL | Identifies a Fractional T1 utilizing 12 channels (768 kb/s) (for use w/AA+) |
| HXRD (Not valid in SE) | Identifies a Fractional T1 utilizing 4 channels (256 kb/s) Termination on a Router (Future Offering) |
| HXRF (Not valid in SE) | Identifies a Fractional T1 utilizing 6 channels (384 kb/s) Termination on a Router (Future Offering) |
| HXRH (Not valid in SE) | Identifies a Fractional T1 utilizing 8 channels (512 kb/s) Termination on a Router (Future Offering) |
| HXRL (Not valid in SE) | Identifies a Fractional T1 utilizing 12 channels (768 kb/s) Termination on a Router (Future Offering) |
| HXRP (Not valid in SE) | Identifies a Fractional T1 utilizing 16 channels (1024 kb/s) Termination on a Router (Future Offering) |
| HXZB (Not valid in SE) | Identifies a Fractional T1 utilizing 2 channels (128 kb/s) |
| HXZD (Not valid in SE) | Identifies a Fractional T1 utilizing 4 channels (256 kb/s) |
| HXZF (Not valid in SE) | Identifies a Fractional T1 utilizing 6 channels (384 kb/s) |
| HXZH (Not valid in SE) | Identifies a Fractional T1 utilizing 8 channels (512 kb/s) |
| HXZX (W only) | Identifies a Fractional T1 utilizing 24 channels (1536 kb/s) B8ZS |

SONET Products / Offerings “Electrical” Coding

NC codes JI- - for SONET Electrical associated with DSRS services (including SMOA) has been moved from TAB 15 (SONET), as they represent the services riding the SONET products, not the products themselves.  JI- - and JJ-- coding for STN is still found in TAB 15.

| NC Code | Description |
| --- | --- |
| JI- - | SONET Electrical STS-1, 51.84 Mbps |
| JIAA (Valid In SE, SW only) | SONET Electrical STS-1, 51.84 Mbps ~ VT1 Structured~ Central Office Multiplexer |
| JIAC (Valid In SE, SW only) | SONET Electrical STS-1, 51.84 Mbps ~ VT1 Structured~ Multiplexer at both ends |

Ethernet Codes

| NC Code | Description |
| --- | --- |
| KDA- (SE only) | Ethernet at 10 Mbps ~ Full Duplex LAN ~ None, No Further options |
| KDAA (SE only) | Ethernet at 10 Mbps ~ Full Duplex LAN ~ Network Monitoring |
| KDAP (SE only) | Ethernet at 10 Mbps ~ Full Duplex LAN ~ Protected |
| KDAR (SE only) | Ethernet at 10 Mbps ~ Full Duplex LAN ~ Customer Reconfigurable |
| KEA- | Ethernet at 100 Mbps ~ Full Duplex LAN ~ None, No Further options |
| KEAP | Ethernet at 100 Mbps ~ Full Duplex LAN ~ Protected |
| KEAR (SE only) | Ethernet at 100 Mbps ~ Full Duplex LAN ~ Customer Reconfigurable |
| KFL- | Ethernet at 1 Gpbs ~ LAN ~ None, No Further options |
| KFLP | Ethernet at 1 Gpbs ~ LAN ~ Protected |
| KGL- | Ethernet at 10 Gpbs ~ LAN ~ None, No Further options |
| KGLP | Ethernet at 10 Gpbs ~ LAN ~ Protected |
| KGW- | Ethernet at 10 Gpbs ~ WAN (9.95328 Gbps) ~ None, No Further options |
| KGWP | Ethernet at 10 Gpbs ~ WAN (9.95328 Gbps) ~ Protected |
| KHL- | Ethernet at 40 Gbps ~ Full Duplex LAN PHY |
| KHLP | Ethernet at 40 Gbps ~ Full Duplex LAN PHY ~ Protected |
| KJL- | Ethernet at 100 Gbps ~ Full Duplex LAN PHY |
| KJLP | Ethernet at 100 Gbps ~ Full Duplex LAN PHY ~ Protected |
| KML- | Ethernet at 400 Gbps ~ Full Duplex LAN PHY |

Rate Adjustable Ethernet Codes

| NC Code | Description |
| --- | --- |
| KPA- | Ethernet, Rate-Adjustable 10 Mbps Ethernet, Full Duplex – 10 Mbps Full Rate |
| KPA5 | Ethernet, Rate-Adjustable 10 Mbps Ethernet, Full Duplex – 5 Mbps |
| KPA6 | Ethernet, Rate-Adjustable 10 Mbps Ethernet, Full Duplex – 2 Mbps |
| KPA7 | Ethernet, Rate-Adjustable 10 Mbps Ethernet, Full Duplex – 4 Mbps |
| KPA8 | Ethernet, Rate-Adjustable 10 Mbps Ethernet, Full Duplex – 8 Mbps |
| KPAA | Ethernet, Rate-Adjustable 10 Mbps Ethernet, Full Duplex, Rate Based on SONET transport at VT1.5-1v, 1.6 Mbps Nominal Payload Rate |
| KPAB | Ethernet, Rate-Adjustable 10 Mbps Ethernet, Full Duplex, Rate Based on SONET transport at VT1.5-2v, 3.2 Mbps Nominal Payload Rate |
| KPAD | Ethernet, Rate-Adjustable 10 Mbps Ethernet, Full Duplex, Rate Based on SONET transport at VT1.5-4v, 6.4 Mbps Nominal Payload Rate |
| KPAG | Ethernet, Rate-Adjustable 10 Mbps Ethernet, Full Duplex, Rate Based on SONET transport at VT1.5-7v, 11.2 Mbps Nominal Payload Rate |
| KPE- | Ethernet Rate-Adjustable at 10 Mbps, Full Duplex - Rate based on Ethernet Switch, Facility supporting Ethernet Virtual Connection (EVC) service multiplexing 10 Mbps |
| KPE5 | Ethernet Rate-Adjustable at 10 Mbps, Full Duplex - Rate based on Ethernet Switch, Facility supporting Ethernet Virtual Connection (EVC) service multiplexing 5 Mbps |
| KPE6 | Ethernet Rate-Adjustable at 10 Mbps, Full Duplex - Rate based on Ethernet Switch, Facility supporting Ethernet Virtual Connection (EVC) service multiplexing 2 Mbps |
| KPE7 | Ethernet Rate-Adjustable at 10 Mbps, Full Duplex - Rate based on Ethernet Switch, Facility supporting Ethernet Virtual Connection (EVC) service multiplexing 4 Mbps |
| KPE8 | Ethernet Rate-Adjustable at 10 Mbps, Full Duplex - Rate based on Ethernet Switch, Facility supporting Ethernet Virtual Connection (EVC) service multiplexing 8 Mbps |
| KPT6 (SE only) | Ethernet Rate-Adjustable at 10 Mbps, Full Duplex -Requires Protected Infrastructur -2 Mbps |
| KPT7 (SE only) | Ethernet Rate-Adjustable at 10 Mbps, Full Duplex - Requires Protected Infrastructure - 4 Mbps |
| KPT8 (SE only) | Ethernet Rate-Adjustable at 10 Mbps, Full Duplex - Requires Protected Infrastructure - 8 Mbps |
| KQA- | Ethernet, Rate-Adjustable 100 Mbps Ethernet -Full Duplex - Rate based on Ethernet Switch ~100 Mbps |
| KQA1 | Ethernet, Rate-Adjustable 100 Mbps Ethernet -Full Duplex - Rate based on Ethernet Switch ~10 Mbps |
| KQA2 | Ethernet, Rate-Adjustable 100 Mbps Ethernet -Full Duplex - Rate based on Ethernet Switch ~20 Mbps |
| KQA5 | Ethernet, Rate-Adjustable 100 Mbps Ethernet -Full Duplex - Rate based on Ethernet Switch ~50 Mbps |
| KQAJ | Ethernet, Rate-Adjustable 100 Mbps Ethernet -Full Duplex - Rate based on Ethernet Switch ~2 Mbps |
| KQAK | Ethernet, Rate-Adjustable 100 Mbps Ethernet -Full Duplex - Rate based on Ethernet Switch ~4 Mbps |
| KQAL | Ethernet, Rate-Adjustable 100 Mbps Ethernet -Full Duplex - Rate based on Ethernet Switch ~8 Mbps |
| KQAM | Ethernet, Rate-Adjustable 100 Mbps Ethernet -Full Duplex - Rate based on Ethernet Switch ~5 Mbps |
| KQE- | Ethernet Rate- Adjustable at 100 Mbps, Full Duplex - Rate based on Ethernet Switch, Facility supporting Ethernet Virtual Connection (EVC) service multiplexing 100 Mbps |
| KQE1 | Ethernet Rate-Adjustable at 100 Mbps, Full Duplex - Rate based on Ethernet Switch, Facility supporting Ethernet Virtual Connection (EVC) service multiplexing 10 Mbps |
| KQE2 | Ethernet Rate-Adjustable at 100 Mbps, Full Duplex - Rate based on Ethernet Switch, Facility supporting Ethernet Virtual Connection (EVC) service multiplexing 20 Mbps |
| KQE5 | Ethernet Rate-Adjustable at 100 Mbps, Full Duplex - Rate based on Ethernet Switch, Facility supporting Ethernet Virtual Connection (EVC) service multiplexing 50 Mbps |
| KQEJ | Ethernet Rate-Adjustable at 100 Mbps, Full Duplex - Rate based on Ethernet Switch, Facility supporting Ethernet Virtual Connection (EVC) service multiplexing 5 Mbps |
| KQEK | Ethernet Rate-Adjustable at 100 Mbps, Full Duplex - Rate based on Ethernet Switch, Facility supporting Ethernet Virtual Connection (EVC) service multiplexing 2 Mbps |
| KQEL | Ethernet Rate-Adjustable at 100 Mbps, Full Duplex - Rate based on Ethernet Switch, Facility supporting Ethernet Virtual Connection (EVC) service multiplexing 4 Mbps |
| KQEM | Ethernet Rate-Adjustable at 100 Mbps, Full Duplex - Rate based on Ethernet Switch, Facility supporting Ethernet Virtual Connection (EVC) service multiplexing 8 Mbps |
| KQFA | Ethernet Rate-Adjustable at 100 Mbps ~ Full-Duplexed Rate based on SONET transport STS-1, 48.382 Mbps Nominal Payload Rate |
| KQFB | Ethernet Rate-Adjustable at 100 Mbps ~ Full-Duplexed Rate based on SONET transport ~ STS-3c, (Full Rate at 100 Mbps) |
| KQFC | Ethernet Rate-Adjustable at 100 Mbps ~Full-Duplexed Rate based on SONET transport STS-1-1v, 48.382 Mbps Nominal Payload Rate |
| KQFD | Ethernet Rate-Adjustable at 100 Mbps ~ Full-Duplexed Rate based on SONET transport ~ STS-1-2v, 96.768 Mbps Nominal Payload Rate |
| KQFE | Ethernet Rate-Adjustable at 100 Mbps ~ Full-Duplexed Rate based on SONET transport VT1.5-2v, 3.2 Mbps Nominal Payload Rate |
| KQFF | Ethernet Rate-Adjustable at 100 Mbps ~ Full-Duplexed Rate based on SONET transport ~ VT1.5-4v, 6.4 Mbps Nominal Payload Rate |
| KQFG | Ethernet Rate-Adjustable at 100 Mbps ~ Full-Duplexed Rate based on SONET transport VT1.5-7v, 11.2 Mbps Nominal Payload Rate |
| KQFK | Ethernet Rate-Adjustable at 100 Mbps ~ Full-Duplexed Rate based on SONET transport ~ VT1.5-1v, 1.6 Mbps Nominal Payload Rate |
| KQFL | Ethernet Rate-Adjustable at 100 Mbps ~ Full-Duplexed Rate based on SONET transport VT1.5-13v, 20.8 Mbps Nominal Payload Rate |
| KQFN | Ethernet Rate-Adjustable at 100 Mbps ~ Full-Duplexed Rate based on SONET transport ~ VT1.5-3v, 4.8 Mbps |
| KQFP | Ethernet Rate-Adjustable at 100 Mbps ~ Full-Duplexed Rate based on SONET transport ~ VT1.5-5v, 8Mbps |
| KQFQ | Ethernet Rate-Adjustable at 100 Mbps ~ Full-Duplexed Rate based on SONET transport ~ VT1.5-6v, 9.6 Mbps |
| KQFR | Ethernet Rate-Adjustable at 100 Mbps ~ Full-Duplexed Rate based on SONET transport ~ VT1.5 – 10V, 16 Mbps |
| KQFS | Ethernet Rate-Adjustable at 100 Mbps ~ Full-Duplexed Rate based on SONET transport ~ VT1.5 – 8v, 12.8 Mbps Nominal Payload Rate (Not VCAT Capable) |
| KQPB (SE only) | Ethernet Rate-Adjustable at 100 Mbps ~ Protected Full-Duplexed Rate based on SONET transport ~ STS-3c, 149.76 Mbps Nominal Payload Rate |
| KQPC (SE only) | Ethernet Rate-Adjustable at 100 Mbps ~ Protected Full-Duplexed Rate based on SONET transport STS-1-1v, 48.382 Mbps Nominal Payload Rate |
| KQPD (SE only) | Ethernet Rate-Adjustable at 100 Mbps ~ Protected Full-Duplexed Rate based on SONET transport ~ STS-1-2v, 96.768 Mbps Nominal Payload Rate |
| KQPE (SE only) | Ethernet Rate-Adjustable at 100 Mbps ~ Protected Full-Duplexed Rate based on SONET transport VT1.5-2v, 3.2 Mbps Nominal Payload Rate |
| KQPF (SE only) | Ethernet Rate-Adjustable at 100 Mbps ~ Protected Full-Duplexed Rate based on SONET transport ~ VT1.5-4v, 6.4 Mbps Nominal Payload Rate |
| KQPG (SE only) | Ethernet Rate-Adjustable at 100 Mbps ~ Protected Full-Duplexed Rate based on SONET transport VT1.5-7v, 11.2 Mbps Nominal Payload Rate |
| KQPH (SE only) | Ethernet Rate-Adjustable at 100 Mbps ~ Protected Full-Duplexed Rate based on SONET transport ~ VT1.5-16v, 25.6 Mbps Nominal Payload Rate |
| KRA1 | Ethernet, Rate-Adjustable Gigabit Ethernet (Full Duplex) ~ Rate based on Ethernet Switch - 100 Mpbs |
| KRA2 | Ethernet, Rate-Adjustable Gigabit Ethernet (Full Duplex) ~ Rate based on Ethernet Switch - 200 Mpbs |
| KRA3 (SE only) | Ethernet, Rate-Adjustable Gigabit Ethernet (Full Duplex) ~ Rate based on Ethernet Switch - 300 Mpbs |
| KRA4 | Ethernet, Rate-Adjustable Gigabit Ethernet (Full Duplex) ~ Rate based on Ethernet Switch - 400 Mpbs |
| KRA5 | Ethernet, Rate-Adjustable Gigabit Ethernet (Full Duplex) ~ Rate based on Ethernet Switch - 500 Mpbs |
| KRA6 | Ethernet, Rate-Adjustable Gigabit Ethernet (Full Duplex) ~ Rate based on Ethernet Switch - 600 Mpbs |
| KRA0 | Ethernet, Rate-Adjustable Gigabit Ethernet (Full Duplex) ~ Rate based on Ethernet Switch - 1000 Mpbs |
| KRAA | Ethernet, Rate-Adjustable Gigabit Ethernet (Full Duplex) ~ Rate based on Ethernet Switch - 250 Mpbs |
| KRAB | Ethernet, Rate-Adjustable Gigabit Ethernet (Full Duplex) ~ Rate based on Ethernet Switch - 150 Mpbs |
| KRAK (SE only) | Ethernet, Rate-Adjustable Gigabit Ethernet (Full Duplex) ~ Rate based on Ethernet Switch - 450 Mpbs |
| KRB2 | Ethernet, Rate-Adjustable Gigabit Ethernet (Full Duplex) ~ Rate based on Ethernet Switch (5-95 Mbps in increments of 5 and mixed increments under 20 Mbps) - 2 Mpbs |
| KRB4 | Ethernet, Rate-Adjustable Gigabit Ethernet (Full Duplex) ~ Rate based on Ethernet Switch (5-95 Mbps in increments of 5 and mixed increments under 20 Mbps) - 4 Mpbs |
| KRB8 | Ethernet, Rate-Adjustable Gigabit Ethernet (Full Duplex) ~ Rate based on Ethernet Switch (5-95 Mbps in increments of 5 and mixed increments under 20 Mbps) - 8 Mpbs |
| KRBA | Ethernet, Rate-Adjustable Gigabit Ethernet (Full Duplex) ~ Rate based on Ethernet Switch (5-95 Mbps in increments of 5 and mixed increments under 20 Mbps) - 5 Mpbs |
| KRBB | Ethernet, Rate-Adjustable Gigabit Ethernet (Full Duplex) ~ Rate based on Ethernet Switch (5-95 Mbps in increments of 5 and mixed increments under 20 Mbps) - 10 Mpbs |
| KRBD | Ethernet, Rate-Adjustable Gigabit Ethernet (Full Duplex) ~ Rate based on Ethernet Switch (5-95 Mbps in increments of 5 and mixed increments under 20 Mbps) - 20 Mpbs |
| KRBJ | Ethernet, Rate-Adjustable Gigabit Ethernet (Full Duplex) ~ Rate based on Ethernet Switch (5-95 Mbps in increments of 5 and mixed increments under 20 Mbps) - 50 Mpbs |
| KRE1 | Ethernet, Rate-Adjustable Gigabit Ethernet (Full Duplex) Rate based on Ethernet Switch (100Mbps-1Gbps in increments of 25), Facility supporting Ethernet Virtual Connection (EVC) service multiplexing ~ 100 Mbps |
| KRE2 | Ethernet, Rate-Adjustable Gigabit Ethernet (Full Duplex) Rate based on Ethernet Switch (100Mbps-1Gbps in increments of 25), Facility supporting Ethernet Virtual Connection (EVC) service multiplexing ~ 200 Mbps |
| KRE3 | Ethernet, Rate-Adjustable Gigabit Ethernet (Full Duplex) Rate based on Ethernet Switch (100Mbps-1Gbps in increments of 25), Facility supporting Ethernet Virtual Connection (EVC) service multiplexing ~ 300 Mbps |
| KRE4 | Ethernet, Rate-Adjustable Gigabit Ethernet (Full Duplex) Rate based on Ethernet Switch (100Mbps-1Gbps in increments of 25), Facility supporting Ethernet Virtual Connection (EVC) service multiplexing ~ 400 Mbps |
| KRE5 | Ethernet, Rate-Adjustable Gigabit Ethernet (Full Duplex) Rate based on Ethernet Switch (100Mbps-1Gbps in increments of 25), Facility supporting Ethernet Virtual Connection (EVC) service multiplexing ~ 500 Mbps |
| KRE6 | Ethernet, Rate-Adjustable Gigabit Ethernet (Full Duplex) Rate based on Ethernet Switch (100Mbps-1Gbps in increments of 25), Facility supporting Ethernet Virtual Connection (EVC) service multiplexing ~ 600 Mbps |
| KRE0 | Ethernet, Rate-Adjustable Gigabit Ethernet (Full Duplex) Rate based on Ethernet Switch (100Mbps-1Gbps in increments of 25), Facility supporting Ethernet Virtual Connection (EVC) service multiplexing ~ 1000 Mbps (full rate) |
| KREA | Ethernet, Rate-Adjustable Gigabit Ethernet (Full Duplex) Rate based on Ethernet Switch (100Mbps-1Gbps in increments of 25), Facility supporting Ethernet Virtual Connection (EVC) service multiplexing ~ 250 Mbps |
| KREB | Ethernet, Rate-Adjustable Gigabit Ethernet (Full Duplex) Rate based on Ethernet Switch (100Mbps-1Gbps in increments of 25), Facility supporting Ethernet Virtual Connection (EVC) service multiplexing ~ 150 Mbps |
| KRF2 | Ethernet, Rate-Adjustable Gigabit Ethernet (Full Duplex) Rate based on Ethernet Switch (5-95 Mbps in increments of 5 and mixed increments under 20 Mbps) Facility supporting EVC service multiplexing ~ 2Mbps |
| KRF8 | Ethernet, Rate-Adjustable Gigabit Ethernet (Full Duplex) Rate based on Ethernet Switch (5-95 Mbps in increments of 5 and mixed increments under 20 Mbps) Facility supporting EVC service multiplexing ~ 8 Mbps |
| KRFA | Ethernet, Rate-Adjustable Gigabit Ethernet (Full Duplex) Rate based on Ethernet Switch (5-95 Mbps in increments of 5 and mixed increments under 20 Mbps) Facility supporting EVC service multiplexing ~ 5 Mbps |
| KRFB | Ethernet, Rate-Adjustable Gigabit Ethernet (Full Duplex) Rate based on Ethernet Switch (5-95 Mbps in increments of 5 and mixed increments under 20 Mbps) Facility supporting EVC service multiplexing ~ 10 Mbps |
| KRFD | Ethernet, Rate-Adjustable Gigabit Ethernet (Full Duplex) Rate based on Ethernet Switch (5-95 Mbps in increments of 5 and mixed increments under 20 Mbps) Facility supporting EVC service multiplexing ~ 20 Mbps |
| KRFJ | Ethernet, Rate-Adjustable Gigabit Ethernet (Full Duplex) Rate based on Ethernet Switch (5-95 Mbps in increments of 5 and mixed increments under 20 Mbps) Facility supporting EVC service multiplexing ~ 50 Mbps |
| KRG2 | Ethernet, Rate-Adjustable 1 Gigabit Ethernet (Full Duplex) Rate based on Ethernet Switch Facility supporting EVC service multiplexing - Asymmetric/Symmetric Data Services ~ 2 Mbps Downstream – 2 Mbps Upstream |
| KRG4 | Ethernet, Rate-Adjustable 1 Gigabit Ethernet (Full Duplex) Rate based on Ethernet Switch Facility supporting EVC service multiplexing - Asymmetric/Symmetric Data Services ~ 4 Mbps Downstream – 4 Mbps Upstream |
| KRGA | Ethernet, Rate-Adjustable 1 Gigabit Ethernet (Full Duplex) Rate based on Ethernet Switch Facility supporting EVC service multiplexing - Asymmetric/Symmetric Data Services |
| KRGB | Ethernet, Rate-Adjustable 1 Gigabit Ethernet (Full Duplex) Rate based on Ethernet Switch Facility supporting EVC service multiplexing - Asymmetric/Symmetric Data Services |
| KRGC | Ethernet, Rate-Adjustable 1 Gigabit Ethernet (Full Duplex) Rate based on Ethernet Switch Facility supporting EVC service multiplexing - Asymmetric/Symmetric Data Services |
| KRGD | Ethernet, Rate-Adjustable 1 Gigabit Ethernet (Full Duplex) Rate based on Ethernet Switch Facility supporting EVC service multiplexing - Asymmetric/Symmetric Data Services |
| KRGE | Ethernet, Rate-Adjustable 1 Gigabit Ethernet (Full Duplex) Rate based on Ethernet Switch Facility supporting EVC service multiplexing - Asymmetric/Symmetric Data Services |
| KRGF | Ethernet, Rate-Adjustable 1 Gigabit Ethernet (Full Duplex) Rate based on Ethernet Switch Facility supporting EVC service multiplexing - Asymmetric/Symmetric Data Services |
| KRJ2 | Ethernet, Rate-Adjustable 1 Gigabit Ethernet (Full Duplex) Rate based on Ethernet Switch, Asymmetric/Symmetric Data Services ~ 2 Mbps Downstream – 2 Mbps Upstream |
| KRJ4 | Ethernet, Rate-Adjustable 1 Gigabit Ethernet (Full Duplex) Rate based on Ethernet Switch, Asymmetric/Symmetric Data Services ~ 4 Mbps Downstream – 4 Mbps Upstream |
| KRJA | Ethernet, Rate-Adjustable 1 Gigabit Ethernet (Full Duplex) Rate based on Ethernet Switch, Asymmetric/Symmetric Data Services ~ 3 Mbps Downstream – 1 Mbps Upstream |
| KRJB | Ethernet, Rate-Adjustable 1 Gigabit Ethernet (Full Duplex) Rate based on Ethernet Switch, Asymmetric/Symmetric Data Services ~ 6 Mbps Downstream – 1 Mbps Upstream |
| KRJC | Ethernet, Rate-Adjustable 1 Gigabit Ethernet (Full Duplex) Rate based on Ethernet Switch, Asymmetric/Symmetric Data Services ~ 12 Mbps Downstream – 1.5 Mbps Upstream |
| KRJD | Ethernet, Rate-Adjustable 1 Gigabit Ethernet (Full Duplex) Rate based on Ethernet Switch, Asymmetric/Symmetric Data Services ~ 18 Mbps Downstream – 1.5 Mbps Upstream |
| KRJE | Ethernet, Rate-Adjustable 1 Gigabit Ethernet (Full Duplex) Rate based on Ethernet Switch, Asymmetric/Symmetric Data Services ~ 24 Mbps downstream – 3 Mbps upstream |
| KRJF | Ethernet, Rate-Adjustable 1 Gigabit Ethernet (Full Duplex) Rate based on Ethernet Switch, Asymmetric/Symmetric Data Services ~ 45 Mbps downstream – 6 Mbps upstream |
| KRP2 | Ethernet, Rate-Adjustable 1 Gbps Ethernet (Full Duplex) Protected, STS-24c, 1198.08 Mbps Nominal Payload Rate Nominal Payload Rate (24c is Not addressed specifically inGR-253 but the bit rate is accurate at STS-3c x8) |
| KRPU (SE only) | Ethernet, Rate-Adjustable 1 Gbps Ethernet (Full Duplex) Protected, STS-24c, 1198.08 Mbps Nominal Payload Rate STS-1-21v, 1016.064 Mbps Nominal Payload Rate |
| KRRA (Not valid in SE) | Ethernet, Rate-Adjustable 1 Gbps Ethernet (Full Duplex) ~ Rate based on SONET transport with Hi-Order VCAT (STS-3c and STS-12c base increments) ~ STS-3c-1v, 149.76 Mbps Nominal Payload Rate |
| KRRB (Not valid in SE) | Ethernet, Rate-Adjustable 1 Gbps Ethernet (Full Duplex) ~ Rate based on SONET transport with Hi-Order VCAT (STS-3c and STS-12c base increments) ~ STS-3c-2v, 299.52 Mbps Nominal Payload Rate |
| KRRC (Not valid in SE) | Ethernet, Rate-Adjustable 1 Gbps Ethernet (Full Duplex) ~ Rate based on SONET transport with Hi-Order VCAT (STS-3c and STS-12c base increments) ~ STS-3c-3v, 449.28 Mbps Nominal Payload Rate |
| KRRD (Not valid in SE) | Ethernet, Rate-Adjustable 1 Gbps Ethernet (Full Duplex) ~ Rate based on SONET transport with Hi-Order VCAT (STS-3c and STS-12c base increments) ~ STS-3c-4v,599.04 Mbps Nominal Payload Rate |
| KRRG (Not valid in SE) | Ethernet, Rate-Adjustable 1 Gbps Ethernet (Full Duplex) ~ Rate based on SONET transport with Hi-Order VCAT (STS-3c and STS-12c base increments) ~ STS-3c-7v, 1048.32 Mbps Nominal Payload Rate |
| KRRH (Not valid in SE) | Ethernet, Rate-Adjustable 1 Gbps Ethernet (Full Duplex) ~ Rate based on SONET transport with Hi-Order VCAT (STS-3c and STS-12c base increments) ~ STS-3c-8v, 1198.08 Mbps Nominal Payload Rate |
| KRS2 | Ethernet, Rate-Adjustable 1 Gbps Ethernet (Full Duplex) ~Rate based on STS transport level. ~ STS-24c, 1198.08 Mbps Nominal Payload Rate Nominal Payload Rate (24c is Not addressed specifically in GR-253 but the bit rate is accurate at STS-3c x 8) (Not VCAT Capable) |
| KRS6 (SE only) | Ethernet, Rate-Adjustable 1 Gbps Ethernet (Full Duplex) ~Rate based on STS transport level. ~ STS-6c, 299.52 Mbps Nominal Payload Rate Nominal Payload Rate (Not VCAT Capable) |
| KRS9 (SE only) | Ethernet, Rate-Adjustable 1 Gbps Ethernet (Full Duplex) ~Rate based on STS transport level. ~ STS-9c, 449.28 Mbps Nominal Payload Rate Nominal Payload Rate (Not VCAT Capable) |
| KRS0 | Ethernet, Rate-Adjustable 1 Gbps Ethernet (Full Duplex) ~Rate based on STS transport level. ~ STS-1-12v, 580.608 Mbps Nominal Payload Rate |
| KRSA | Ethernet, Rate-Adjustable 1 Gbps Ethernet (Full Duplex) ~Rate based on STS transport level. ~ STS-1, 48.382 Mbps Nominal Payload Rate (Not VCAT Capable) |
| KRSB (Not valid in SE) | Ethernet, Rate-Adjustable 1 Gbps Ethernet (Full Duplex) ~Rate based on STS transport level. ~ STS-1-2v, 96.768 Mbps Nominal Payload Rate |
| KRSC | Ethernet, Rate-Adjustable 1 Gbps Ethernet (Full Duplex) ~Rate based on STS transport level. ~ STS-3c, 149.76 Mbps Nominal Payload Rate (Not VCAT Capable) |
| KRSD (Not valid in SE) | Ethernet, Rate-Adjustable 1 Gbps Ethernet (Full Duplex) ~Rate based on STS transport level. ~ STS-1-4v, 193.536 Mbps Nominal Payload Rate |
| KRSF | Ethernet, Rate-Adjustable 1 Gbps Ethernet (Full Duplex) ~Rate based on STS transport level. ~ STS-1-6v, 290.304 Mbps Nominal Payload Rate |
| KRSI | Ethernet, Rate-Adjustable 1 Gbps Ethernet (Full Duplex) ~Rate based on STS transport level. ~ STS-1-9v, 435.46 Mbps Nominal Payload Rate |
| KRSL | Ethernet, Rate-Adjustable 1 Gbps Ethernet (Full Duplex) ~Rate based on STS transport level. ~ STS12c, 599.04 Mbps Nominal Payload Rate (Not VCAT Capable) |
| KRSU | Ethernet, Rate-Adjustable 1 Gbps Ethernet (Full Duplex) ~Rate based on STS transport level. ~ STS-1-21v, 1016.064 Mbps Nominal Payload Rate |
| KRSY (Not valid in SE) | Ethernet, Rate-Adjustable 1 Gbps Ethernet (Full Duplex) ~Rate based on STS transport level. ~ STS-1-1v, 48.384 Mbps Nominal Payload Rate |
| KRSZ | Ethernet, Rate-Adjustable 1 Gbps Ethernet (Full Duplex) ~Rate based on STS transport level. ~ STS-1-3v, 145.152 Mbps Nominal Payload Rate |
| KRT1 (Not valid in MW, SW, W) | Ethernet, Rate-Adjustable 1 Gbps Ethernet (Full Duplex) ~Rate based on Ethernet Switch - Requires Protected Infrastructure (APS) ~ 100 Mbps |
| KRT2 (Not valid in MW, SW, W) | Ethernet, Rate-Adjustable 1 Gbps Ethernet (Full Duplex) ~Rate based on Ethernet Switch - Requires Protected Infrastructure (APS) ~ 200 Mbps |
| KRT3 (Not valid in MW, SW, W) | Ethernet, Rate-Adjustable 1 Gbps Ethernet (Full Duplex) ~Rate based on Ethernet Switch - Requires Protected Infrastructure (APS) ~ 300 Mbps |
| KRT5 (Not valid in MW, SW, W) | Ethernet, Rate-Adjustable 1 Gbps Ethernet (Full Duplex) ~Rate based on Ethernet Switch - Requires Protected Infrastructure (APS) ~ 500 Mbps |
| KRT6 (Not valid in MW, SW, W) | Ethernet, Rate-Adjustable 1 Gbps Ethernet (Full Duplex) ~Rate based on Ethernet Switch - Requires Protected Infrastructure (APS) ~ 600 Mbps |
| KRT9 (Not valid in MW, SW, W) | Ethernet, Rate-Adjustable 1 Gbps Ethernet (Full Duplex) ~Rate based on Ethernet Switch - Requires Protected Infrastructure (APS) ~ 900 Mbps |
| KRT0 (Not valid in MW, SW, W) | Ethernet, Rate-Adjustable 1 Gbps Ethernet (Full Duplex) ~Rate based on Ethernet Switch - Requires Protected Infrastructure (APS) ~ 1000 Mbps |
| KRTA (Not valid in MW, SW, W) | Ethernet, Rate-Adjustable 1 Gbps Ethernet (Full Duplex) ~Rate based on Ethernet Switch - Requires Protected Infrastructure (APS) ~ 250 Mbps |
| KRTK (Not valid in MW, SW, W) | Ethernet, Rate-Adjustable 1 Gbps Ethernet (Full Duplex) ~Rate based on Ethernet Switch - Requires Protected Infrastructure (APS) ~ 450 Mbps |
| KRTT (Not valid in MW, SW, W) | Ethernet, Rate-Adjustable 1 Gbps Ethernet (Full Duplex) ~Rate based on Ethernet Switch - Requires Protected Infrastructure (APS) ~ 750 Mbps |
| KRV1 (Not valid in MW, SW, W) | Ethernet, Rate-Adjustable 1 Gbps Ethernet (Full Duplex) ~Rate based on Ethernet Switch -Requires Protected Infrastructure and Supports Service Multiplexing. ((VLAN/Q-Fwding Host & APS)) ~ 100 Mbps |
| KRV2 (Not valid in MW, SW, W) | Ethernet, Rate-Adjustable 1 Gbps Ethernet (Full Duplex) ~Rate based on Ethernet Switch -Requires Protected Infrastructure and Supports Service Multiplexing. ((VLAN/Q-Fwding Host & APS)) ~ 200 Mbps |
| KRV3 (Not valid in MW, SW, W) | Ethernet, Rate-Adjustable 1 Gbps Ethernet (Full Duplex) ~Rate based on Ethernet Switch -Requires Protected Infrastructure and Supports Service Multiplexing. ((VLAN/Q-Fwding Host & APS)) ~ 300 Mbps |
| KRV5 (Not valid in MW, SW, W) | Ethernet, Rate-Adjustable 1 Gbps Ethernet (Full Duplex) ~Rate based on Ethernet Switch -Requires Protected Infrastructure and Supports Service Multiplexing. ((VLAN/Q-Fwding Host & APS)) ~ 500 Mbps |
| KRV6 (Not valid in MW, SW, W) | Ethernet, Rate-Adjustable 1 Gbps Ethernet (Full Duplex) ~Rate based on Ethernet Switch -Requires Protected Infrastructure and Supports Service Multiplexing. ((VLAN/Q-Fwding Host & APS)) ~ 600 Mbps |
| KRV9 (Not valid in MW, SW, W) | Ethernet, Rate-Adjustable 1 Gbps Ethernet (Full Duplex) ~Rate based on Ethernet Switch -Requires Protected Infrastructure and Supports Service Multiplexing. ((VLAN/Q-Fwding Host & APS)) ~ 900 Mbps |
| KRV0 (Not valid in MW, SW, W) | Ethernet, Rate-Adjustable 1 Gbps Ethernet (Full Duplex) ~Rate based on Ethernet Switch -Requires Protected Infrastructure and Supports Srvc Multiplexing. ((VLAN/Q-Fwding Host & APS)) ~ 1000 Mbps |
| KRVA (Not valid in MW, SW, W) | Ethernet, Rate-Adjustable 1 Gbps Ethernet (Full Duplex) ~Rate based on Ethernet Switch -Requires Protected Infrastructure and Supports Service Multiplexing. ((VLAN/Q-Fwding Host & APS)) ~ 250 Mbps |
| KRVK (Not valid in MW, SW, W) | Ethernet, Rate-Adjustable 1 Gbps Ethernet (Full Duplex) ~Rate based on Ethernet Switch -Requires Protected Infrastructure and Supports Service Multiplexing. ((VLAN/Q-Fwding Host & APS)) ~ 450 Mbps |
| KRVT (Not valid in MW, SW, W) | Ethernet, Rate-Adjustable 1 Gbps Ethernet (Full Duplex) ~Rate based on Ethernet Switch -Requires Protected Infrastructure and Supports Service Multiplexing. ((VLAN/Q-Fwding Host & APS)) ~ 750 Mbps |
| KSA- | Ethernet, Rate-Adjustable 10 Gbps~Full Duplex LAN PHY, Rate based on Ethernet Switch (Port Based) ~ 10 Gbps (full rate) (Future Offering) |
| KSA1 | Ethernet, Rate-Adjustable 10 Gbps~Full Duplex LAN PHY, Rate based on Ethernet Switch (Port Based) ~ 1 Gbps |
| KSA2 | Ethernet, Rate-Adjustable 10 Gbps~Full Duplex LAN PHY, Rate based on Ethernet Switch (Port Based) ~ 2 Gbps |
| KSA4 | Ethernet, Rate-Adjustable 10 Gbps~Full Duplex LAN PHY, Rate based on Ethernet Switch (Port Based) ~ 4 Gbps |
| KSA5 | Ethernet, Rate-Adjustable 10 Gbps~Full Duplex LAN PHY, Rate based on Ethernet Switch (Port Based) ~ 5 Gbps |
| KSAD | Ethernet Rate-Adjustable 10 Gbps~Full Duplex LAN PHY Rate based on Ethernet Switch (Port Based) ~ 2.5 Gbps |
| KSAJ | Ethernet Rate-Adjustable 10 Gbps~Full Duplex LAN PHY Rate based on Ethernet Switch (Port Based) ~ 7.5 Gbps |
| KSAL | Ethernet Rate-Adjustable 10 Gbps~Full Duplex LAN PHY Rate based on Ethernet Switch (Port Based) ~ 9.5 Gbps |
| KSE- | Ethernet, Rate-Adjustable 10Gbps ~ Full Duplex LAN, Rate based on Ethernet Switch, and Supports Service Multiplexing. (VLAN Based) ~ 10 Gbps (full rate) |
| KSE1 | Ethernet, Rate-Adjustable 10Gbps ~ Full Duplex LAN, Rate based on Ethernet Switch, and Supports Service Multiplexing. (VLAN Based) ~ 1 Gbps |
| KSE2 | Ethernet, Rate-Adjustable 10Gbps ~ Full Duplex LAN, Rate based on Ethernet Switch, and Supports Service Multiplexing. (VLAN Based) ~ 2 Gbps |
| KSE4 | Ethernet, Rate-Adjustable 10Gbps ~ Full Duplex LAN, Rate based on Ethernet Switch, and Supports Service Multiplexing. (VLAN Based) ~ 4 Gbps |
| KSE5 | Ethernet, Rate-Adjustable 10Gbps ~ Full Duplex LAN, Rate based on Ethernet Switch, and Supports Service Multiplexing. (VLAN Based) ~ 5 Gbps |
| KSED | Ethernet, Rate-Adjustable 10Gbps ~ Full Duplex LAN, Rate based on Ethernet Switch, and Supports Service Multiplexing. (VLAN Based) ~ 2.5 Gbps |
| KSEJ | Ethernet, Rate-Adjustable 10Gbps ~ Full Duplex LAN, Rate based on Ethernet Switch, and Supports Service Multiplexing. (VLAN Based) ~ 7.5 Gbps |
| KSEL | Ethernet, Rate-Adjustable 10Gbps ~ Full Duplex LAN, Rate based on Ethernet Switch, and Supports Service Multiplexing. (VLAN Based) ~ 9.5 Gbps |
| KUA- | Ethernet, Rate-Adjustable 100 Gbps Ethernet ~ Full Duplex LAN PHY, Rate based on Ethernet Switch (Port Based) ~ 100Gbps |
| KUAB | Ethernet, Rate-Adjustable 100 Gbps Ethernet ~ Full Duplex LAN PHY, Rate based on Ethernet Switch (Port Based) ~ 10 Gbps |
| KUAC | Ethernet, Rate-Adjustable 100 Gbps Ethernet ~ Full Duplex LAN PHY, Rate based on Ethernet Switch (Port Based) ~ 15 Gbps |
| KUAD | Ethernet, Rate-Adjustable 100 Gbps Ethernet ~ Full Duplex LAN PHY, Rate based on Ethernet Switch (Port Based) ~ 20 Gbps |
| KUAE | Ethernet, Rate-Adjustable 100 Gbps Ethernet ~ Full Duplex LAN PHY, Rate based on Ethernet Switch (Port Based) ~ 25 Gbps |
| KUAF | Ethernet, Rate-Adjustable 100 Gbps Ethernet ~ Full Duplex LAN PHY, Rate based on Ethernet Switch (Port Based) ~ 30 Gbps |
| KUAG | Ethernet, Rate-Adjustable 100 Gbps Ethernet ~ Full Duplex LAN PHY, Rate based on Ethernet Switch (Port Based) ~ 35 Gbps |
| KUAH | Ethernet, Rate-Adjustable 100 Gbps Ethernet ~ Full Duplex LAN PHY, Rate based on Ethernet Switch (Port Based) ~ 40 Gbps |
| KUAJ | Ethernet, Rate-Adjustable 100 Gbps Ethernet ~ Full Duplex LAN PHY, Rate based on Ethernet Switch (Port Based) ~ 45 Gbps |
| KUAK | Ethernet, Rate-Adjustable 100 Gbps Ethernet ~ Full Duplex LAN PHY, Rate based on Ethernet Switch (Port Based) ~ 50 Gbps |
| KUAM | Ethernet, Rate-Adjustable 100 Gbps Ethernet ~ Full Duplex LAN PHY, Rate based on Ethernet Switch (Port Based) ~ 60 Gbps |
| KUAP | Ethernet, Rate-Adjustable 100 Gbps Ethernet ~ Full Duplex LAN PHY, Rate based on Ethernet Switch (Port Based) ~ 70 Gbps |
| KUAR | Ethernet, Rate-Adjustable 100 Gbps Ethernet ~ Full Duplex LAN PHY, Rate based on Ethernet Switch (Port Based) ~ 80 Gbps |
| KUAT | Ethernet, Rate-Adjustable 100 Gbps Ethernet ~ Full Duplex LAN PHY, Rate based on Ethernet Switch (Port Based) ~ 90 Gbps |
| KUE- | Ethernet, Rate-Adjustable 100 Gbps Ethernet ~ Full Duplex LAN PHY, Rate based on Ethernet Switch, and Supports Service Multiplexing ~ 100Gbps |
| KUEB | Ethernet, Rate-Adjustable 100 Gbps Ethernet ~ Full Duplex LAN PHY, Rate based on Ethernet Switch, and Supports Service Multiplexing ~ 10 Gbps |
| KUEC | Ethernet, Rate-Adjustable 100 Gbps Ethernet ~ Full Duplex LAN PHY, Rate based on Ethernet Switch, and Supports Service Multiplexing ~ 15 Gbps |
| KUED | Ethernet, Rate-Adjustable 100 Gbps Ethernet ~ Full Duplex LAN PHY, Rate based on Ethernet Switch, and Supports Service Multiplexing ~ 20 Gbps |
| KUEE | Ethernet, Rate-Adjustable 100 Gbps Ethernet ~ Full Duplex LAN PHY, Rate based on Ethernet Switch, and Supports Service Multiplexing ~ 25 Gbps |
| KUEF | Ethernet, Rate-Adjustable 100 Gbps Ethernet ~ Full Duplex LAN PHY, Rate based on Ethernet Switch, and Supports Service Multiplexing ~ 30 Gbps |
| KUEG | Ethernet, Rate-Adjustable 100 Gbps Ethernet ~ Full Duplex LAN PHY, Rate based on Ethernet Switch, and Supports Service Multiplexing ~ 35 Gbps |
| KUEH | Ethernet, Rate-Adjustable 100 Gbps Ethernet ~ Full Duplex LAN PHY, Rate based on Ethernet Switch, and Supports Service Multiplexing ~ 40 Gbps |
| KUEJ | Ethernet, Rate-Adjustable 100 Gbps Ethernet ~ Full Duplex LAN PHY, Rate based on Ethernet Switch, and Supports Service Multiplexing ~ 45 Gbps |
| KUEK | Ethernet, Rate-Adjustable 100 Gbps Ethernet ~ Full Duplex LAN PHY, Rate based on Ethernet Switch, and Supports Service Multiplexing ~ 50 Gbps |
| KUEM | Ethernet, Rate-Adjustable 100 Gbps Ethernet ~ Full Duplex LAN PHY, Rate based on Ethernet Switch, and Supports Service Multiplexing ~ 60 Gbps |
| KUEP | Ethernet, Rate-Adjustable 100 Gbps Ethernet ~ Full Duplex LAN PHY, Rate based on Ethernet Switch, and Supports Service Multiplexing ~ 70 Gbps |
| KUER | Ethernet, Rate-Adjustable 100 Gbps Ethernet ~ Full Duplex LAN PHY, Rate based on Ethernet Switch, and Supports Service Multiplexing ~ 80 Gbps |
| KUET | Ethernet, Rate-Adjustable 100 Gbps Ethernet ~ Full Duplex LAN PHY, Rate based on Ethernet Switch, and Supports Service Multiplexing ~ 90 Gbps |

| NC Code | Description |
| --- | --- |
| LB-- | Voice Grade 1 (VG1) |
| LB-A | Voice Grade 1 (VG1) Effective 4-wire |
| LB-D | Voice Grade 1 (VG1) Effective 4-wire + Improved Termination |
| LB-L | Voice Grade 1 (VG1) Improved termination at the End User's location |
| LBB- | Voice Grade 1 (VG1) Equal Level Echo Path Loss (ELEPL) Also known as ELEPL2 depicted in TR-NWT-000335) Specifications can only be met with limited facility configurations. |

| NC Code | Description |
| --- | --- |
| LC-- | Voice Grade 2 (VG2) |
| LC-A | Voice Grade 2 (VG2) Effective 4-wire |
| LC-B | Voice Grade 2 (VG2) Central Office Bridging |
| LC-C | Voice Grade 2 (VG2) Improved Return Loss for Effective 2-wire |
| LC-D | Voice Grade 2 (VG2) Effective 4-wire + Improved Termination |
| LC-E | Voice Grade 2 (VG2) Central Office Bridging + Improved Termination at the access customer's location |
| LC-F | Voice Grade 2 (VG2) Effective 4-wire + Central Office Bridging |
| LC-H | Voice Grade 2 (VG2) Central Office Bridging + Improved termination at the End User's location |
| LC-L | Voice Grade 2 (VG2) Improved termination at the End User's location |
| LC-P | Voice Grade 2 (VG2) Improved termination at the End User's location + Improved termination at the access customer's location |
| LCBC | Voice Grade 2 (VG2) Equal Level Echo Path Loss (ELEPL) Also known as ELEPL2. and Improved Return Loss for Effective 2-wire |
| LC1- | Voice Grade 2 (VG2) IntraLATA Service Performance for 2-point End-to-End Svc |
| LC1A (SW, SE only) | Voice Grade 2 (VG2) IntraLATA Service Performance for two-point End to End Service and Effective 4-wire |

| NC Code | Description |
| --- | --- |
| LD-- | Voice Grade 3 (VG3) |
| LD-A | Voice Grade 3 (VG3) Effective 4-wire |
| LD-D | Voice Grade 3 (VG3) Effective 4-wire + Improved Termination |
| LD-L | Voice Grade 3 (VG3) Improved termination at the End User's location |
| LD1- | Voice Grade 3(VG3) IntraLATA Service Performance |

| NC Code | Description |
| --- | --- |
| LE-- | Voice Grade 4 (VG4) |

| NC Code | Description |
| --- | --- |
| LF-- | Voice Grade 5 (VG5) |
| LF-A | Voice Grade 5 (VG5) Effective 4-wire |
| LF-B | Voice Grade 5 (VG5) Central Office Bridging |
| LF-R | Improved Termination at the access customer's location |
| LFG- | Voice Grade 5 (VG5) Improved Attenuation Distortion. Specific limits are depicted in TR-NWT-000335. |
| LFGA | Voice Grade 5 (VG5) Improved Attenuation Distortion and Effective 4-wire |
| LFJA | Voice Grade 5 (VG5) Improved Envelope Delay Distortion + Improved Attenuation Distortion. Effective 4-wire |

| NC Code | Description |
| --- | --- |
| LG-- | Voice Grade 6 (VG6) |
| LG-B | Voice Grade 6 (VG6) Central Office Bridging |
| LG-E | Voice Grade 6 (VG6) Central Office Bridging + Improved Termination at the access customer's location |
| LG-L | Voice Grade 6 (VG6) Improved termination at the End User's location |
| LG-P | Voice Grade 6 (VG6) Improved termination at the End User's location + Improved termination at the access customer's location |
| LG-R | Voice Grade 6 (VG6) Improved Termination at the access customer's location |
| LGC- | Voice Grade 6 (VG6) C- Conditioning |
| LGCB (MW, SE, W only) | Voice Grade 6 (VG6) C- Conditioning - Central Office Bridging |
| LGCL (MW, SE, W only) | Voice Grade 6 (VG6) C- Conditioning - Improved termination at the End User's location |
| LGD- | Voice Grade 6 (VG6) Data Capability |
| LGDB | Voice Grade 6 (VG6) Data Capability and Central Office Bridging |
| LGDL | Voice Grade 6 (VG6) Data Capability and Improved termination at the End User's location |
| LGDP | Voice Grade 6 (VG6) Data Capability and Improved termination at the End User's location + Improved termination at the access customer's location |
| LGDR | Voice Grade 6 (VG6) Data Capability and Improved Termination at the access customer's location |
| LGE- (MW, SE, W only) | Voice Grade 6 (VG6) C-Conditioning + Data Capability |
| LGF- | Voice Grade 6 (VG6) Improved Envelope Delay Distortion ~ Specific limits are depicted in TR-NWT-000335 |
| LGG- | Voice Grade 6 (VG6) Improved Attenuation Distortion. Specific limits are depicted in TR-NWT-000335 |
| LGGB | Voice Grade 6 (VG6) Improved Attenuation Distortion and Central Office Bridging |
| LGGE | Voice Grade 6 (VG6) Improved Attenuation Distortion and Central Office Bridging + Improved Termination at the access customer's location |
| LGGL | Voice Grade 6 (VG6) Improved Attenuation Distortion and Improved termination at the End User's location |
| LGGP | Voice Grade 6 (VG6) Improved Attenuation Distortion and Improved termination at the End User's location + Improved termination at the access customer's location |
| LGGR | Voice Grade 6 (VG6) Improved Attenuation Distortion and Improved Termination at the access customer's location |
| LGJ- | Voice Grade 6 (VG6) Improved Attenuation Distortion + Improved Envelope Delay Distortion |
| LGJL | Voice Grade 6 (VG6) Improved Attenuation Distortion + Improved Envelope Delay Distortion and Improved termination at the End User's location |
| LGJP | Voice Grade 6 (VG6) Improved Attenuation Distortion + Improved Envelope Delay Distortion and Improved termination at the End User's location + Improved termination at the access customer's location |
| LGJR | Voice Grade 6 (VG6) Improved Attenuation Distortion + Improved Envelope Delay Distortion and Improved Termination at the access customer's location |
| LGM- | Voice Grade 6 (VG6) Improved Attenuation Distortion + Data Capability |
| LGML | Voice Grade 6 (VG6) Improved Attenuation Distortion + Data Capability and Improved termination at the End User's location |
| LGMP | Voice Grade 6 (VG6) Improved Attenuation Distortion + Data Capability and Improved termination at the End User's location + Improved termination at the access customer's location |
| LGN- | Voice Grade 6 (VG6) Improved Attenuation Distortion + Data Capability + Improved Envelope Delay Distortion |
| LGNB | Voice Grade 6 (VG6) Improved Attenuation Distortion + Data Capability + Improved Envelope Delay Distortion and Central Office Bridging |
| LGNL | Voice Grade 6 (VG6) Improved Attenuation Distortion + Data Capability + Improved Envelope Delay Distortion and Improved termination at the End User's location |
| LGNP | Voice Grade 6 (VG6) Improved Attenuation Distortion + Data Capability + Improved Envelope Delay Distortion and Improved termination at the End User's location + Improved termination at the access customer's location |
| NC Code | Description |
| LH-- | Voice Grade 7 (VG7) |
| LH-A | Voice Grade 7 (VG7) Effective 4-wire |
| LH-C | Voice Grade 7 (VG7) Improved return loss for an effective 2-wire circuit. |
| LH-D | Voice Grade 7 (VG7) Effective 4-wire, a 4-wire facility with no intermediate 2-wire segments + Improved Termination at the access customer's location |
| LH-L | Voice Grade 7 (VG7) Improved termination at the End User's location |
| LHC- | Voice Grade 7 (VG7) C-Conditioning |
| LHG- | Voice Grade 7 (VG7) Improved Attenuation Distortion- Provides Stringent Attenuation Distortion performance parameters. Specific limits are in TR-NWT-000335 |
| LHGA | Voice Grade 7 (VG7) Improved Attenuation Distortionand Effective 4-wire |
| LH1A (SW, SE only) | Voice Grade 7 (VG7) IntraLATA Service Performance and Effective 4-wire |
| LH2- (SW, SE only) | Voice Grade 7 (VG7) IntraLATA Service Performance + C-Conditioning (Limits provided in TR-NWT-000335) |
| LH3A (SW, SE only) | Voice Grade 7 (VG7) IntraLATA Service Performance + Data Capability and Effective 4-wire |
| LH4- (Not valid in W) | Voice Grade 7 (VG7) IntraLATA Service Performance + C-Conditioning + Data Capability |

| NC Code | Description |
| --- | --- |
| LJ-- | Voice Grade 8 (VG8) |
| LJ-R | Voice Grade 8 (VG8) Improved Termination at the access customer's location |

| NC Code | Description |
| --- | --- |
| LN-- | Voice Grade 10 (VG10) |
| LN-B | Voice Grade 10 (VG10) Central Office Bridging |
| LN-L | Voice Grade 10 (VG10) Improved termination at the End User's location |
| LN-P | Voice Grade 10 (VG10) Improved termination at the End User's location + Improved termination at the access customer's location |
| LNCL | Voice Grade 10 (VG10) C- Conditioning - Improved termination at the End User's location |
| LND- | Voice Grade 10 (VG10) Data Capability - as depicted in TR-NWT-000335. |
| LNDB | Voice Grade 10 (VG10) Data Capability and Central Office Bridging |
| LNDP | Voice Grade 10 (VG10) Data Capability and Improved termination at the End User's location + Improved termination at the access customer's location |
| LNG- | Voice Grade 10 (VG10) Improved Attenuation Distortion Specific limits are depicted in TR-NWT-000335 |
| LN1- (Not valid in MW) | Voice Grade 10 (VG10) IntraLATA Service Performance |
| LN2- (Not valid in MW) | Voice Grade 10 (VG10) IntraLATA Service Performance + C-Conditioning Limits are depicted in TR-NWT-000335 |
| LN3- (SW, SE only) | Voice Grade 10 (VG10) IntraLATA Service Performance + Data Capability |
| LN4- (SW, SE only) | Voice Grade 10 (VG10) IntraLATA Service Performance + C-Conditioning + Data Capability |

| NC Code | Description |
| --- | --- |
| LR-- | Voice Grade 12 (VG12) |
| LR-B | Voice Grade 12 (VG12) Central Office Bridging |

| NC Code | Description |
| --- | --- |
| LX-- | Unbundled Dedicated Facility without equipment, dark fiber, or copper loops with nominal 1004 Hz transducer loss of 8dB (unless otherwise specified) per ATIS-0600401.2006(R2011) |

Voice Grade Notes

1.	Transfer Arrangements

Two transfer arrangements are available in the Interstate Access Tariff for Voice Grade Channels (VG1 through VG12).  Optional feature codes have Not been developed for these transfer arrangements due to the high number of codes required to accommodate these arrangements in combination with the existing codes; low expected requests for these transfer arrangements; and the need for the customer to provide additional information anyway (such as sketches and comments) to properly convey its requirements.  If a customer requires a transfer arrangement, the USOC for the required transfer arrangement should be placed on the Inf. Notes section of the ASR along with any accompanying sketches and comments.

VOICE GRADE TRANSFER ARRANGEMENTS

OPTION	USOC

4 Port Transfer	USY

5 Port Transfer	US5

- C- Conditioning

This is a Bundled offering of stringent attenuation distortion and envelope delay parameters.  This option is now obsolete, limited to existing installations at existing locations for existing customers as of February 8, 1989.  This applies to FCC 73 Interstate tariff and State Access tariffs that have been made and State Commissions have approved parity filings with FCC 73.  This option has been unbundled into two separate options, Attenuation Distortion performance parameters (IAD) and Improved Envelope Delay Distortion (IEDD).  In those states where parity filings have not been made, C- Conditioning may still be ordered and IAD and IEDD may not be ordered.

| NC Code | Description |
| --- | --- |
| LX-- | Unbundled Dedicated Facility without equipment, dark fiber, or copper loops with nominal 1004 Hz transducer loss of 8dB (unless otherwise specified) per T1.TRQ.7-2002 (Details in Tab 10) |
| LX-N (MW, SE only) | Unbundled Dedicated Facility without equipment, dark fiber, or copper loops with nominal 1004 Hz transducer loss of 8dB (unless otherwise specified) per T1.TRQ.7-2002 ~ Metallic portion of facility contains no load coils. (Details in Tab 10) |
| LXC- (SE only) | Unbundled Dedicated Facility without equipment, dark fiber, or copper loops with nominal 1004 Hz transducer loss of 8dB (unless otherwise specified) per T1.TRQ.7-2002 ~ CSA, Carrier Serving Area (Non-loaded less than 12 Kft) (Details in Tab 10) |
| LXR- (SE only) | Unbundled Dedicated Facility without equipment, dark fiber, or copper loops with nominal 1004 Hz transducer loss of 8dB (unless otherwise specified) per T1.TRQ.7-2002 ~ RRD, Revised Resistance Design, Non-loaded less than 18 Kft (Details in Tab 10) |
| LXT- (SW, SE only) | Unbundled Dedicated Facility without equipment, dark fiber, or copper loops with nominal 1004 Hz transducer loss of 8dB (unless otherwise specified) per T1.TRQ.7-2002~With Test Access (Details in Tab 10) |

| NC Code | Description |
| --- | --- |
| LY-- | Unbundled Dedicated Facility with equipment, copper loops with nominal 1004 Hz transducer loss of 8dB (unless otherwise specified) per T1.TRQ.7-2002 (Details in Tab 10) |
| LY-5 (SW only) | Unbundled Dedicated Facility with equipment, copper loops with nominal 1004 Hz transducer loss of 8dB (unless otherwise specified) per T1.TRQ.7-2002 ~ 5dB Facility (Details in Tab 10) |
| LYT- (SW, SE only) | Unbundled Dedicated Facility with equipment, copper loops with nominal 1004 Hz transducer loss of 8dB (unless otherwise specified) per T1.TRQ.7-2002 ~With Test Access (Details in Tab 10) |

Note:  LY - This NC code is also intended for services sold to the End User premises and will typically be used for the provision of conditioned services.

| NC Code | Description |
| --- | --- |
| NT- - | Metallic Channel Service MT1 (Formerly known as Narrowband 1) |
| NT-S (Not valid in SE, W) | Metallic Channel Service MT1 Switched Termination |

| NC Code | Description |
| --- | --- |
| NY-- (Not valid in MW) | Telegraph Channel Service TG2 ~ (Formerly known as Narrowband 5) |

SONET Products / Offerings Coding

AT&T has created a TAB 15 which contains the currently permissible Network Channel (NC) and Network Channel Interface (NCI); along with permissible combinations that should be used by AT&T Customers when ordering the SONET offerings # (see # Notes on next pages). SONET coding may also be found in TAB 18 as part of the MON Riding Services offerings.

| NC Code | Description |
| --- | --- |
| OB-P | SONET, OC3, 155.520 Mbps, Point-to-Point, Optical Termination on a Switch ~ Aggregator - (ATM, Frame Relay, etc.) With NNI Protocol (requires STS concatenation). (Details found in TAB 10) |
| OB-Z (SE only) | SONET, OC3, 155.520 Mbps, Point-to-Point, this service is transported over non-SONET infrastructure (overhead remains transparent to provider) |
| OBTZ (SE only) | SONET, OC3, 155.520 Mbps, Point to Point Requiring Protected Infrastructure, this service is transported over non-SONET infrastructure (overhead remains transparent to provider) |
| OD-P (SE only) | SONET, OC12, 622.080 Mbps, Point-to-Point, Optical Termination on a Switch ~ Aggregator - (ATM, Frame Relay, etc.) With NNI Protocol (requires STS concatenation). (Details found in TAB 10) |
| OD-Z (SE only) | SONET, OC12, 622.080 Mbps, Point-to-Point, this service is transported over non-SONET infrastructure (overhead remains transparent to provider) |
| ODTZ (SE only) | SONET, OC12, 622.080 Mbps, Point to Point Requiring Protected Infrastructure, this service is transported over non-SONET infrastructure (overhead remains transparent to provider) |
| OF-Z (SE only) | SONET, OC48, 2488.320 Mbps, Point-to-Point, this service is transported over non-SONET infrastructure (overhead remains transparent to provider) |
| OFTZ (SE only) | SONET, OC48, 2488.320 Mbps, Point to Point Requiring Protected Infrastructure, this service is transported over non-SONET infrastructure (overhead remains transparent to provider) |
| OG-Z (SE only) | SONET, OC192, 9953.280 Mbps, Point-to-Point, this service is transported over non-SONET infrastructure (overhead remains transparent to provider) |
| OGTZ (SE only) | SONET, OC192, 9953.280 Mbps, Point to Point Requiring Protected Infrastructure, this service is transported over non-SONET infrastructure (overhead remains transparent to provider) |

Optical Transport Network (OTN)

| NC Code | Description |
| --- | --- |
| OJ-- | OTN, OTU-1, Optical Transport Network (OTN) per ITU-T G.709 OTU 1 (255/238 x 2.488 3202.666057143 Gbps) also referred to as 2.7 Gbps. ~ Point-to-point |
| OK-- | Optical Transport Network (OTN) OTU2 per ITU-T G.709 ~ Optical Transport Network (OTN) per ITU-T G.709, Point-to-Point at 10.7 Gbps |
| OK-C | Optical Transport Network (OTN) OTU2 per ITU-T G.709 ~ Optical Transport Network (OTN) per ITU-T G.709, Point-to-Point at 10.7 Gbps ~ Central Office Terminal Add Drop Multiplexer |
| OKD- | Optical Transport Network (OTN) OTU2 per ITU-T G.709 ~ Optical Transport Network (OTN) per ITU-T G.709, overclocked to 11.09 Gbps; OTU2e per IEEE G. Sup43 |
| OKDP | Optical Transport Network (OTN) OTU2 per ITU-T G.709 ~ Optical Transport Network (OTN) per ITU-T G.709, overclocked to 11.09 Gbps; OTU2e per IEEE G. Sup43 ~ Protected |
| OKT- | Optical Transport Network (OTN) OTU2 per ITU-T G.709 ~ Point-to-point, Requires protected infrastructure |
| OL-- | OTN, OTU-3, Optical Transport Network (OTN) per ITU-T G.709 OTU3 (255/236 x 39.813120 Gbps = 43.018413559 Gbps) also referred to as 43 Gbps. ~ Point-to-point |
| OLT- | OTN, OTU-3, Optical Transport Network (OTN) per ITU-T G.709 OTU3 (255/236 x 39.813120 Gbps = 43.018413559 Gbps) also referred to as 43 Gbps. ~ Point-to-point, Requires protected infrastructure |
| OM-- | OTN, OTU-4, Optical Transport Network (OTN) per ITU-T G.709 OTU4 also referred to as 111.108 Gbps ~ Point-to-point |
| OM-C | OTN, OTU-4, Optical Transport Network (OTN) per ITU-T G.709 OTU4 also referred to as 111.108 Gbps ~ Point-to-point ~ Central Office Terminal Add Drop Multiplexer |
| OMT- | OTN, OTU-4, Optical Transport Network (OTN) per ITU-T G.709 OTU4 also referred to as 111.108 Gbps ~ Point-to-point, Requires protected infrastructure |

LAN

| NC Code | Description |
| --- | --- |
| OPA- (Not valid in SE) | LAN, Optical Data Transport~ETR, IBM External Timing Reference ~ Point-To-Point |
| OPB- | LAN, Optical Data Transport~ESCON, IBM Redbook Enterprise System CONnection ~ Point-To-Point |
| OPBB (Not valid in SE) | LAN, Optical Data Transport~ESCON, IBM Redbook Enterprise System CONnection ~ Point-To-Point ~ Rate adjustable via SONET transport at STS-6c, 311.04 Mbps Nominal Payload Rate |
| OPBC (Not valid in SE) | LAN, Optical Data Transport~ESCON, IBM Redbook Enterprise System CONnection ~ Point-To-Point ~ Protected, Rate adjustable via SONET transport at STS-6c, 311.04 Mbps Nominal Payload Rate |
| OPBP | LAN, Optical Data Transport~ESCON, IBM Redbook Enterprise System CONnection ~ Point-To-Point~ Requires Protected Infrastructure |
| OPC- (Not valid in SE) | LAN, Optical Data Transport~ISC, IBM Redbook Internal System Coupling~ Point-To-Point |
| OPCP (Not valid in SE) | LAN, Optical Data Transport~ISC, IBM Redbook Internal System Coupling~ Point-To-Point~ Requires Protected Infrastructure |
| OPD- | LAN, Optical Data Transport~FICON™ at 1.06 Gbps~ Point-To-Point |
| OPDD (Not valid in SE) | LAN, Optical Data Transport~FICON™ at 1.06 Gbps~ Point-To-Point ~ Rate adjustable via SONET transport at STS - 24c |
| OPDE | LAN, Optical Data Transport~FICON™ at 1.06 Gbps~ Point-To-Point ~ Protected, Rate adjustable via SONET transport at STS - 24c |
| OPDP | LAN, Optical Data Transport~FICON™ at 1.06 Gbps~ Point-To-Point Requires Protected Infrastructure |
| OPE- | LAN, Optical Data Transport~FICON™ at 2.125 Gbps~ Point-To-Point |
| OPEB (SE only) | LAN, Optical Data Transport~FICON™ at 2.125 Gbps~ Point-To-Point ~ Protected, Rate adjustable via SONET transport at STS-48c, (full rate) |
| OPEF | LAN, Optical Data Transport~FICON™ at 2.125 Gbps~ Point-To-Point ~ Rate adjustable via SONET transport at STS - 48c |
| OPEP | LAN, Optical Data Transport~FICON™ at 2.125 Gbps~ Point-To-Point Requires Protected Infrastructure |
| OPF- | LAN, Optical Data Transport~ Fibre Channel at 1.06 Gbps ~ Point-To-Point |
| OPFD (Not valid in SE) | LAN, Optical Data Transport~ Fibre Channel at 1.06 Gbps ~ Point-To- Point ~ Rate adjustable via SONET transport at STS - 24c |
| OPFE | LAN, Optical Data Transport~ Fibre Channel at 1.06 Gbps ~ Point-To- Point ~ Protected, Rate adjustable via SONET transport at STS - 24c |
| OPFP | LAN, Optical Data Transport~ Fibre Channel at 1.06 Gbps ~ Point-To-Point Requires Protected Infrastructure |
| OPJ- | LAN, Optical Data Transport~ Fibre Channel at 2.125 Gbps ~ Point-To-Point |
| OPJA (SE only) | LAN, Optical Data Transport~ Fibre Channel at 2.125 Gbps ~ Point-To-Point – Protected, Rate adjustable via SONET transport at STS-1-37v, 1790.208 Mbps Nominal Payload Rate |
| OPJB (SE only) | LAN, Optical Data Transport~ Fibre Channel at 2.125 Gbps ~ Point-To-Point ~ Protected, Rate adjustable via SONET transport at STS-48c, (full rate) |
| OPJF | LAN, Optical Data Transport~ Fibre Channel at 2.125 Gbps ~ Point-To-Point ~ Rate adjustable via SONET transport at STS - 48c |
| OPJP | LAN, Optical Data Transport~ Fibre Channel at 2.125 Gbps ~ Point-To-Point Requires Protected Infrastructure |
| OPK- (Not valid in SE) | LAN, Optical Data Transport~ ISC-3 – IBM Intersystem Channel at 2.125 Gbps~ Point-To-Point |
| OPKP (Not valid in SE) | LAN, Optical Data Transport~ ISC-3 – IBM Intersystem Channel at 2.125 Gbps~ Point-To-Point Requires Protected Infrastructure |

Note:

OPF-, OPFP, OPJ-, OPJF and OPJP are the only valid NC codes for the FibreMAN Product offering.  Protection Options for FibreMAN may be a future offering and should be verified to see if available.

| NC Code | Description |
| --- | --- |
| OW- - # (SE only) | SDH, Optical STM-64 per ITU G.707 9953.280 Mbps |
| OW-Z # (SE only) | SDH, Optical STM-64 per ITU G.707 9953.280 Mbps ~ This service is transported over non-SDH infrastructure (overhead remains transparent to provider) |
| OWTZ # (SE only) | SDH, Optical STM-64 per ITU G.707 9953.280 Mbps ~ Point to Point requiring protected infrastructure ~ This service is transported over non-SDH infrastructure (overhead remains transparent to provider) |

Note:

# = the “OW” SDH related codes will be reflected in TAB 2 and 8a.

| NC Code | Description |
| --- | --- |
| OX-A # | SONET, Flexible Rate (Rate will be adjusted without change order activity) ~ Point-To-Point ~ OC3 or OC12 |
| OXTA # | SONET, Flexible Rate (Rate will be adjusted without change order activity) ~ Point–to–Point, Protected ~ OC3 or OC12 |

Note:

# = the “OX” SONET related codes will be reflected in TAB 2 and 8a.

| NC Code | Description |
| --- | --- |
| PE-- | Program Audio Channel Service, 200 Hz – 3,500 Hz AP1– Non-Equalized |
| PE-B | Program Audio Channel Service, 200 Hz – 3,500 Hz AP1~ Bridging (Program Distribution Amplifier) |

| NC Code | Description |
| --- | --- |
| PF-- | Audio Program (AP2), 100-5000 Hz |

| NC Code | Description |
| --- | --- |
| PIB- (SE only) | Wavelength Channel, Protocol Independent on DWDM/CWDM ~ Bit Rate Variable Channel Up to 1.25 Gbps |
| PIBP (SE only) | Wavelength Channel, Protocol Independent on DWDM/CWDM ~ Bit Rate Variable Channel Up to 1.25 Gbps ~ Protected |
| PIC- | Wavelength Channel, Protocol Independent on DWDM/CWDM ~ Bit Rate Variable Channel Up to 2.5 Gbps |
| PICP (SE only) | Wavelength Channel, Protocol Independent on DWDM/CWDM ~ Bit Rate Variable Channel Up to 2.5 Gbps ~ Protected |
| PID- | Wavelength Channel, Protocol Independent on DWDM/CWDM ~ Bit Rate Variable Channel Up to 10 Gbps |
| PIG3 | Wavelength Channel, Protocol Independent on DWDM/CWDM ~ Bit Rate Specific due to Regeneration ~ 3.072 Gbps |
| PIS- (Not valid in SE) | Wavelength Channel, Protocol Independent on DWDM/CWDM ~ Sub-rate Multiplexed |
| PISP (Not valid in SE) | Wavelength Channel, Protocol Independent on DWDM/CWDM ~ Sub-rate Multiplexed ~ Protected |
| NC Code | Description |
| PJ-- (Not valid in SE) | Program Audio Channel Service, 50 Hz – 8,000 Hz AP3 |
| PJ-B (Not valid in SE) | Program Audio Channel Service, 50 Hz – 8,000 Hz AP3~ Bridging (Program Distribution Amplifier) |
| PJP- | Program Audio Channel Service, 50 Hz – 8,000 Hz AP3 ~ Gain Conditioning Provides a loss of 0DB plus or minus .5DB at initiation of Svc. |
| NC Code | Description |
| PK-- | Program Audio Channel Service, 50 Hz – 15,000 Hz AP4 |
| PK-S | Program Audio Channel Service, 50 Hz – 15,000 Hz AP4 ~ Stereo Provision of a pair of gain and phased matched channels for stereo Applications of audio offerings. Requires two AP4/PK channels. |
| PKP- | Program Audio Channel Service, 50 Hz – 15,000 Hz AP4 ~ Gain Conditioning Provides a loss of 0DB plus or minus .5DB at initiation of Svc. |
| PKPS | Program Audio Channel Service, 50 Hz – 15,000 Hz AP4~Gain Conditioning and Stereo |
| NC Code | Description |
| RPB1 (SE only) | Packet Ring Segment ~Unspecified Protocol, Bandwidth based on SONET/SDH PHY, up to STS-24 (1.244 Gbps) STS-1-21v, 1016.064 Mbps |
| RPB4 (SE only) | Packet Ring Segment~Unspecified Protocol, Bandwidth based on SONET/SDH PHY, up to STS-24 (1.244 Gbps) STS-1-24v, 1161.216 Mbps |
| RPBA (SE only) | Packet Ring Segment~Unspecified Protocol, Bandwidth based on SONET/SDH PHY, up to STS-24 (1.244 Gbps) STS-1, 51.84 Mbps |
| RPBB (SE only) | Packet Ring Segment~Unspecified Protocol, Bandwidth based on SONET/SDH PHY, up to STS-24 (1.244 Gbps) STS-3c, 149.76 Mbps |
| RPBC (SE only) | Packet Ring Segment~Unspecified Protocol, Bandwidth based on SONET/SDH PHY, up to STS-24 (1.244 Gbps) STS-6c, 311.04 Mbps |
| RPBD (SE only) | Packet Ring Segment~Unspecified Protocol, Bandwidth based on SONET/SDH PHY, up to STS-24 (1.244 Gbps) STS-9c, 466.56 Mbps |
| RPBE (SE only) | Packet Ring Segment~Unspecified Protocol, Bandwidth based on SONET/SDH PHY, up to STS-24 (1.244 Gbps) STS-12c, 599.04 Mbps |
| RPBF (SE only) | Packet Ring Segment~Unspecified Protocol, Bandwidth based on SONET/SDH PHY, up to STS-24 (1.244 Gbps) STS-24c, 1244.16 Mbps |
| RPBI (SE only) | Packet Ring Segment~Unspecified Protocol, Bandwidth based on SONET/SDH PHY, up to STS-24 (1.244 Gbps) STS-1-3v, 145.152 Mbps |
| RPBL (SE only) | Packet Ring Segment~Unspecified Protocol, Bandwidth based on SONET/SDH PHY, up to STS-24 (1.244 Gbps) STS-1-6v, 290.304 Mbps |
| RPBO (SE only) | Packet Ring Segment~Unspecified Protocol, Bandwidth based on SONET/SDH PHY, up to STS-24 (1.244 Gbps) STS-1-9v, 435.456 Mbps |
| RPBR (SE only) | Packet Ring Segment~Unspecified Protocol, Bandwidth based on SONET/SDH PHY, up to STS-24 (1.244 Gbps) STS-1-12v, 580.608 Mbps |

Switched Access Coding

AT&T has created the currently permissible Network Channel (NC) and Network Channel Interface (NCI) codes associated with Wireless “SB” and “SD” services.

The “SB” family of NC codes for 2-Wire Switched Access services is retired from usage in AT&T and is no longer reflected in the AT&T CCG.

The “SD” and “SH” family of NC codes for CLEC and CLEC Ancillary Trunk-Side services are found in TAB 17 and the regional TAB 10s.  Line-Side SD FGA codes are still found in TABs 2 and regional 8As.

|  | Description |
| --- | --- |
| SD | Switched Access 4-wire transmission type B1 |
| SD-B | Switched Access 4-wire transmission type B1- FGB multi frequency |
| SD-D | Switched Access 4-wire transmission type B1- FGD multi frequency |
| SD-Q | Switched Access 4-wire transmission type B1- FGD PSDS |
| SDFA | Switched Access 4-wire transmission type B1- MTS/WATS (2nd Dial Tone) FGA DPLS, TW |
| SDFE | Switched Access 4-wire transmission type B1- MTS/WATS (2nd Dial Tone) FGA DPGS, TW |
| SDFF | Switched Access 4-wire transmission type B1- MTS/WATS (2nd Dial Tone) FGA DTMF-LS, TW |
| SDFG | Switched Access 4-wire transmission type B1- MTS/WATS (2nd Dial Tone) FGA DTMF-GS, TW |
| SDFN | Switched Access 4-wire transmission type B1- MTS/WATS (2nd Dial Tone) FGA DPLS, TO |
| SDFP | Switched Access 4-wire transmission type B1- MTS/WATS (2nd Dial Tone) FGA DPGS, TO |
| SDFR | Switched Access 4-wire transmission type B1- MTS/WATS (2nd Dial Tone) FGA DTMF-LS, TO |
| SDFS | Switched Access 4-wire transmission type B1- MTS/WATS (2nd Dial Tone) FGA DTMF-GS, TO |
| SDFU (Not valid in SE) | Switched Access 4-wire transmission type B1- MTS/WATS (2nd Dial Tone) FGA LS, OO |
| SDFV (Not valid in SE) | Switched Access 4-wire transmission type B1- MTS/WATS (2nd Dial Tone) FGA GS, OO |
| SDGA | Switched Access 4-wire transmission type B1- Foreign Exchange, FGA DPLS, TW |
| SDGE | Switched Access 4-wire transmission type B1- Foreign Exchange, FGA DPGS, TW |
| SDGF | Switched Access 4-wire transmission type B1- Foreign Exchange, FGA DTMF-LS, TW |
| SDGG | Switched Access 4-wire transmission type B1- Foreign Exchange, FGA DTMF-GS, TW |
| SDGH (Not valid in SE) | Switched Access 4-wire transmission type B1- Foreign Exchange, FGA DP, GS, TW, AS |
| SDGN | Switched Access 4-wire transmission type B1- Foreign Exchange, FGA DPLS, TO |
| SDGP | Switched Access 4-wire transmission type B1- Foreign Exchange, FGA DPGS, TO |
| SDGR | Switched Access 4-wire transmission type B1- Foreign Exchange, FGA DTMF-LS, TO |
| SDGS | Switched Access 4-wire transmission type B1- Foreign Exchange, FGA DTMF-GS, TO |
| SDGU | Switched Access 4-wire transmission type B1- Foreign Exchange, FGA LS, OO |
| SDGV | Switched Access 4-wire transmission type B1- Foreign Exchange, FGA GS, OO |
| SDHA | Switched Access 4-wire transmission type B1- ONAL, Off Network Access Line, FGA DPLS, TW |
| SDHE | Switched Access 4-wire transmission type B1- ONAL, Off Network Access Line, FGA DPGS, TW |
| SDHF | Switched Access 4-wire transmission type B1- ONAL, Off Network Access Line, FGA DTMF-LS, TW |
| SDHG | Switched Access 4-wire transmission type B1- ONAL, Off Network Access Line, FGA DTMF-GS, TW |
| SDHN | Switched Access 4-wire transmission type B1- ONAL, Off Network Access Line, FGA DPLS, TO |
| SDHP | Switched Access 4-wire transmission type B1- ONAL, Off Network Access Line, FGA DPGS, TO |
| SDHR | Switched Access 4-wire transmission type B1- ONAL, Off Network Access Line, FGA DTMF-LS, TO |
| SDHS | Switched Access 4-wire transmission type B1- ONAL, Off Network Access Line, FGA DTMF-GS, TO |
| SDHU | Switched Access 4-wire transmission type B1- ONAL, Off Network Access Line, FGA LS, OO |
| SDHV | Switched Access 4-wire transmission type B1- ONAL, Off Network Access Line, FGA GS, OO |
| SDPC (Not valid in SE) | Voice over Packet (TDM trunks originating from a gateway) ~ Customer (i.e., CLEC, IXC, IP-VIS etc.) Switch to LEC Tandem with SS7 (Associated with TIPToP) |
| SDPD (Not valid in SE) | Voice over Packet (TDM trunks originating from a gateway) ~ Customer (i.e., CLEC, IXC, IP-VIS etc.) Switch to LEC End Office with SS7 (Associated with TIPToP) |
| SDPE (Not valid in SE) | Voice over Packet (TDM trunks originating from a gateway) ~ Customer (i.e., CLEC, IXC, IP-VIS etc.) Switch to LEC Tandem with SS7 and CCC (Associated with TIPToP) |
| SDPF (Not valid in SE) | Voice over Packet (TDM trunks originating from a gateway) ~ Customer (i.e., CLEC, IXC, IP-VIS etc.) Switch to LEC End Office with SS7 and CCC (Associated with TIPToP) |
| SDPG (Not valid in SE) | Voice over Packet (TDM trunks originating from a gateway) ~ Customer (i.e., CLEC, IXC, IP-VIS etc.) Switch to LEC Tandem with MF (Associated with TIPToP) |
| SDPH (Not valid in SE) | Voice over Packet (TDM trunks originating from a gateway) ~ Customer (i.e., CLEC, IXC, IP-VIS etc.) Switch to LEC Tandem with MF, Combined Operator Directory Assistance (Associated with TIPToP) |
| SDPJ (Not valid in SE) | Voice over Packet (TDM trunks originating from a gateway) ~ Customer (i.e., CLEC, IXC, IP-VIS etc.) Switch to LEC Tandem with SS7, Combined Operator Directory Assistance (Associated with TIPToP) |
| SDPK (Not valid in SE) | Voice over Packet (TDM trunks originating from a gateway) ~ Customer (i.e., CLEC, IXC, IP-VIS etc.) Switch to LEC Tandem with MF, Combined Operator Directory Assistance and Call Completion (Associated with TIPToP) |
| SDPL (Not valid in SE) | Voice over Packet (TDM trunks originating from a gateway) ~ Customer (i.e., CLEC, IXC, IP-VIS etc.) Switch to LEC Tandem with MF, Combined Operator Directory Assistance and Call Completion (Associated with TIPToP) |
| SDPM (Not valid in SE) | Switched Access 4- Wire Customer Voice over Packet ~ Customer (i.e., CLEC, IXC, etc.) Switch to LEC E911 Tandem with SS7 (Associated with TIPToP) |
| SDPN (Not valid in SE) | Switched Access 4- Wire Customer Voice over Packet ~Customer (i.e., CLEC, IXC, etc.) Switch to LEC E911 Tandem with Multi Frequency Signaling (Associated with TIPToP) |
| SDSA | Switched Access 4-wire transmission type B1- SS7- FGD |
| SDSB (MW only) | Switched Access 4-wire transmission type B1- SS7- FGB |
| SDSC | Switched Access 4-wire transmission type B1- SS7- FGD W/DS0 CCC (Not valid with 1AE s) |
| SDSF (SW only) | Switched Access 4-wire transmission type B1- FGD w/DS0 CCC - fixed channel scheme used w/SS7 (Not valid with 1AE s) |
| SDSG (SW only) | Switched Access 4-wire transmission type B1- FGD w/DS0 CCC - floating channel scheme used w/SS7 (Not valid w/ 1AE s) |
| SDSH (SW only) | Switched Access 4-wire transmission type B1- FGD w/DS0 CCC - flexible channel scheme used w/SS7 (Not valid w/ 1AE s) |

Grandfathered Note:   Regarding the codes below in red, effective November 20, 2019, this Service will no longer be available for purchase by new or existing customers, and service agreements may no longer be renewed. In addition, requests to move, add or change existing service arrangements will not be accepted. Following the expiration of a customer's existing term agreement, service will be provided on a month-to-month basis at the applicable monthly extension rates until the service is discontinued. AT&T currently plans to discontinue this Service on or after June 30, 2024.

| NC Code | Description |
| --- | --- |
| SE | WATS Access Line (WAL) |
| SEAA | WATS Access Lines – Standard -Effective 2-Wire- 2W, TW, LS, DP-AS |
| SEAE | WATS Access Lines – Standard -Effective 2-Wire- 2W, TW, GS, DP-AS |
| SEAF | WATS Access Lines – Standard -Effective 2-Wire- 2W, TW, LS, DTMF-AS |
| SEAG | WATS Access Lines – Standard -Effective 2-Wire- 2W, TW, GS, DTMF-AS |
| SEAN | WATS Access Lines – Standard -Effective 2-Wire- 2W, OO, LS, DP-AS |
| SEAP | WATS Access Lines – Standard -Effective 2-Wire- 2W, OO, GS, DP-AS |
| SEAR | WATS Access Lines – Standard -Effective 2-Wire- 2W, OO, LS, DTMF-AS |
| SEAS | WATS Access Lines – Standard -Effective 2-Wire- 2W, OO, GS, DTMF-AS |
| SEAT (MW, SE only) | WATS Access Lines – Standard -Effective 2-Wire- 2W, TO, DNIS/RB-SS |
| SEAU | WATS Access Lines – Standard -Effective 2-Wire- 2W, TO, DNIS/RB-SS |
| SEAV | WATS Access Lines – Standard -Effective 2-Wire- 2W, TO, LS |
| SEBN | WATS Access Lines – Standard -Effective 2-Wire- 2W, TO, GS |
| SEBP | WATS Access Lines – Standard -Effective 4-wire, 4W, OO, LS, DP-AS |
| SEBR | WATS Access Lines – Standard -Effective 4-wire, 4W, OO, GS, DP-AS |
| SEBS | WATS Access Lines – Standard -Effective 4-wire, 4W, OO, LS, DTMF-AS |
| SEBT (MW, SE only) | WATS Access Lines – Standard -Effective 4-wire, 4W, TO, DNIS/EM |
| SEBU | WATS Access Lines – Standard -Effective 4-wire, 4W, OO, GS, DTMF-AS |
| SEBV | WATS Access Lines – Standard -Effective 4-wire, Terminate Only, Ground Start |
| SEBW (MW only) | WATS Access Lines – Standard -Effective 4-wire, 4W, OO, EM-SS, DP-AS |
| SEBX (MW only) | WATS Access Lines – Standard -Effective 4-wire, 4W, TO, EM-SS |
| SEGA | WATS Access Lines – Standard -Effective 4-Wire, 2-Way- 4W, TW, LS, DP-AS |
| SEGE | WATS Access Lines – Standard -Effective 4-Wire, 2-Way- 4W, TW, GS, DP-AS |
| SEGF | WATS Access Lines – Standard -Effective 4-Wire, 2-Way- 4W, TW, LS, DTMF-AS |
| SEGG | WATS Access Lines – Standard -Effective 4-Wire, 2-Way- 4W, TW, GS, DTMF-AS |

| NC Code | Description |
| --- | --- |
| SF | WATS Access Line (WAL) |
| SFAA | WATS Access Lines – Improved Attenuation - Effective 2-wire, 2W/I, TW, LS, DP-AS |
| SFAE | WATS Access Lines – Improved Attenuation - Effective 2-wire, 2W/I, TW, GS, DP-AS |
| SFAF | WATS Access Lines – Improved Attenuation - Effective 2-wire, 2W/I, TW, LS, DTMF-AS |
| SFAG | WATS Access Lines – Improved Attenuation - Effective 2-wire, 2W/I, TW, GS, DTMF-AS |
| SFAN | WATS Access Lines – Improved Attenuation - Effective 2-wire, 2W/I, OO, LS, DP-AS |
| SFAP | WATS Access Lines – Improved Attenuation - Effective 2-wire, 2W/I, OO, GS, DP-AS |
| SFAR | WATS Access Lines – Improved Attenuation - Effective 2-wire, 2W/I, OO, LS, DTMF-AS |
| SFAS | WATS Access Lines – Improved Attenuation - Effective 2-wire, 2W/I, OO, GS, DTMF-AS |
| SFAT (MW, SE only) | WATS Access Lines – Improved Attenuation - Effective 2-wire, 2W/I, TO, DNIS/RB-SS |
| SFAU | WATS Access Lines – Improved Attenuation - Effective 2-wire, Terminate Only, Loop Start (IAD) |
| SFAV | WATS Access Lines – Improved Attenuation - Effective 2-wire, Terminate Only, Ground Start (IAD) |
| SFJA (Not valid in MW) | WATS Access Lines – Improved Attenuation - Effective 2-wire, Two Way, Dial Pulse/Loop Start (IAD) and Improved Echo and Singing Return Loss (IERL/ISRL) (Note) |
| SFJE (Not valid in MW) | WATS Access Lines – Improved Attenuation - Effective 2-wire, Two Way, Dial Pulse/Ground Start (IAD) and (IERL/ISRL) |
| SFJF (Not valid in MW) | WATS Access Lines – Improved Attenuation - Effective 2-wire, Two Way, DTMF/Loop Start (IAD) and (IERL/ISRL) |
| SFJG (Not valid in MW) | WATS Access Lines – Improved Attenuation - Effective 2-wire, Two Way, DTMF/Ground Start (IAD) and (IERL/ISRL) |
| SFJN (Not valid in MW) | Effective 2-wire, Originate Only, Dial Pulse/Loop Start (IAD) and (IERL/ISRL) |
| SFJP (Not valid in MW) | WATS Access Lines – Improved Attenuation - Effective 2-wire, Originate Only, Dial Pulse/Ground Start (IAD) and (IERL/ISRL) |
| SFJR (Not valid in MW) | WATS Access Lines – Improved Attenuation - Effective 2-wire, Originate Only, DTMF/Loop Start (IAD) and (IERL/ISRL) |
| SFJS (Not valid in MW) | WATS Access Lines – Improved Attenuation - Effective 2-wire, Originate Only, DTMF/Ground Start (IAD) and (IERL/ISRL) |
| SFJU (Not valid in MW) | WATS Access Lines – Improved Attenuation - Effective 2-wire, Terminate Only, Loop Start (IAD) and (IERL/ISRL) |
| SFJV (Not valid in MW) | WATS Access Lines – Improved Attenuation - Effective 2-wire, Terminate Only, Ground Start (IAD) and (IERL/ISRL) |

Note: Improved ERL/SRL (IERL/ISRL) specifications provided by this option can only be met with limited facility configurations.

| NC Code | Description |
| --- | --- |
| SH | 4-Wire Switched Access Transmission Type A1 |
| SH-A (SE only) | MF ~ Feature Group D ~ 800 access service (see TAB 10 and TAB 17 for details) |
| SH-D | MF ~ Feature Group D |
| SH-Q | MF ~ Microlink I Service (Switched 56 Kbps) w/inband signaling |
| SHSA | 4-Wire Switched Access Transmission Type A1 ~ SS7 ~ FGD |
| SHSC | 4-Wire Switched Access Transmission Type A1 ~ SS7 ~ FGD w/DS0 CCC (Not valid with 1AE s) |
| SHSD (SE only) | 4-Wire Switched Access Transmission Type A1 ~ SS7 ~ FGD ~ 800 Access Service (see TAB 10 and TAB 17 for details) |
| SHSE (SE only) | 4-Wire Switched Access Transmission Type A1 ~ SS7 ~ FGD ~ 800 Access Service w/DS0 CCC (see TAB 10 and TAB 17 for details) |

| NC Code | Description |
| --- | --- |
| SY-A (W only) | Synchronous Timing ~1.544 MBPs DS1 — Stratum 1 Traceable Sync Signal. |
| SY-B (W only) | Synchronous Timing ~ 1 DS0 level Stratum 1 Traceable Sync Signal. |

]

| NC Code | Description |
| --- | --- |
| SZ- - (MW only) | Electronic Business Service |

Video Products / Offerings Coding

AT&T has created a TAB 19 which contains the permissible Network Channel (NC) and Network Channel Interface (NCI) codes; along with permissible combinations that should be used by AT&T Customers when ordering the Video offerings.

#### See Details for the UA, UB, UC, UD (except UDG-), UG, and UH codes in TAB 10

| NC Code | Description |
| --- | --- |
| UDG- (Not valid in SE) | Voice Grade Channel Svc VG33 - Trunk - CO Switching Function (For use to order CALEA see TAB 8a) |

#### See Details for the VL codes in TAB 16

| NC Code | Description |
| --- | --- |
| VLC- | Metro Ethernet Virtual Connection (An association of two or more Physical Ethernet Access Links). Point-to-point Operator Virtual Connection (OVC) per MEF 51/26, which is an association of one UNI and one ENNI or an association of two ENNIs. |
| VLM- | Ethernet Virtual Connection or Operator Virtual Connection (EVC or OVC) (An association of two or more UNIs that limits the exchange of Service Frames to UNIs in the Ethernet Virtual Connection per MEF 10) ~ Multipoint-to-Multipoint Capable Ethernet Virtual Connection or Operator Virtual Connection (EVC or OVC) An association of two or more UNIs or NNIs. |
| VLP- | Ethernet Virtual Connection or Operator Virtual Connection (EVC or OVC) (An association of two or more UNIs that limits the exchange of Service Frames to UNIs in the Ethernet Virtual Connection per MEF 10) ~ Point-to-Point or Operator Virtual Connection (EVC or OVC). Defined in MEF 10 as an association of exactly two UNIs. |

| NC Code | Description |
| --- | --- |
| WA— (SE only) | Wideband Analog |

| NC Code | Description |
| --- | --- |
| WD-- | Wireline Transport for RF Spectrum |

Note:  WD- - is currently offered in Illinois only (future offering for other AT&T locations)

| NC Code | Description |
| --- | --- |
| WE— (SE, W only) | Wideband Data (WD2), 40.8 or 50 Kbps |
| WE-T (SE, W only) | Key Activated Transfer Arrangement |

NOTE:  The Following Digital Access codes are offered under different circumstances and tariffs between AT&T California and Nevada.  For NC codes XA, XB, XD, XG, and XH the 3rd character determines if it is available in AT&T California or Nevada.  Within AT&T when referencing the West region:

- All 3rd characters equal to a “- “or a “B” are offered ONLY in Nevada.

- All 3rd characters equal to an “A” or an “H” are offered ONLY in California.

- All XC and XR codes are ONLY offered in California.

| NC Code | Description |
| --- | --- |
| XA-- (Not valid in MW) | Digital Data, Digital Access Channel Service DA1 2.4 Kbps ~ DDS |
| XAA- (MW, W only) | Digital Data, Digital Access Channel Service DA1 2.4 Kbps BDDS, Basic Dedicated Digital Service (a.k.a. AT&T Midwest region Base Rate) |

NOTE: XA-- with 2 CFAs is a through ckt.

| NC Code | Description |
| --- | --- |
| XB-- (Not valid in MW) | Digital Data, Digital Access Channel Service (DA2) 4.8 Kbps ~ DDS |
| XB-B (Not valid in MW) | Digital Data, Digital Access Channel Service (DA2) 4.8 Kbps ~ DDS ~Bridging |
| XB-C (SE only) | Digital Data, Digital Access Channel Service (DA2) 4.8 Kbps ~ DDS ~ Customer Reconfigurable |
| XBA- (MW, W only) | Digital Data, Digital Access Channel Service DA2 4.8 Kbps BDDS, Basic Dedicated Digital Service. (a.k.a. AT&T Midwest region Base Rate) |
| XBBB (Not valid in MW) | Digital Access (DA2) 4.8 Kbps w/ Secondary Channel Bridging |

NOTE: XB-- with 2 CFAs is a through ckt. XB-B with 1 CFA is an MJU to SRDM ckt.

| NC Code | Description |
| --- | --- |
| XC- - (SE, SW, W only) | Digital Access (DA5) 19.2 Kbps |
| XCA- (MW, W only) | Digital Data, Digital Access Channel Service DA5 19.2 Kbps BDDS, Basic Dedicated Digital Service. (a.k.a. AT&T Midwest region Base Rate) |

NOTE: XC-- with 2 CFAs is a through ckt.  Also, for XC if your see available in W, it is only available in the California portion of the West region.

| NC Code | Description |
| --- | --- |
| XD- - | Digital Data, Digital Access Channel Service DA6 64 Kbps ~ DDS, Digital Data Service ~ |
| XD-C | Digital Data, Digital Access Channel Service DA6 64 Kbps ~ DDS, Digital Data Service ~ Customer Reconfigurable |
| XD-G (SE only) | Digital Data, Digital Access Channel Service DA6 64 Kbps ~ DDS, Digital Data Service ~ DDS, Digital Data Service ~ Digital Packet Uni-Directional Polling, e.g., Frame Relay |
| XD-R (SE only) | Digital Data, Digital Access Channel Service DA6 64 Kbps ~ DDS, Digital Data Service ~ Digital Packet |
| XDAC (MW, W only) | Digital Data, Digital Access Channel Service (DA6) 64 Kbps BDDS, Basic Dedicated Digital Service. Customer Reconfigurable (a.k.a. AT&T Midwest region Base Rate) |

NOTE: XD-- with 2 CFAs is a through ckt.

Effective 4-3-95 the NC code XE changed to XC.  Embedded services will retain the old NC code of XE until any order activity occurs, at which time it will be updated to the new code XC.  All 3rd and 4th character options will remain the same.

| NC Code | Description |
| --- | --- |
| XG- - (Not valid in MW) | Digital Access (DA3) 9.6 Kbps |
| XG-B (Not valid in MW) | Digital Access (DA3) 9.6 Kbps w/Bridging |
| XG-C (SE only) | Digital Data, Digital Access Channel Service (DA3) 9.6 Kbps ~ DDS ~ Customer Reconfigurable |
| XG-V (SE only) | Digital Data, Digital Access Channel Service (DA3) 9.6 Kbps ~ DDS ~ Bridging and Customer Reconfigurable |
| XGA- (MW, W only) | Digital Data, Digital Access Channel Service DA3 9.6 Kbps BDDS, Basic Dedicated Digital Service. (a.k.a. AT&T Midwest region Base Rate) |
| XGAB (MW, W only) | Digital Data, Digital Access Channel Service DA3 9.6 Kbps BDDS, Basic Dedicated Digital Service. Bridging (a.k.a. AT&T Midwest region Base Rate) |
| XGAP (MW, W only) | Digital Data, Digital Access Channel Service DA3 9.6 Kbps BDDS, Basic Dedicated Digital Service. Packet (a.k.a. AT&T Midwest region Base Rate) |
| XGAV (MW only) | Digital Data, Digital Access Channel Service DA3 9.6 Kbps BDDS, Basic Dedicated Digital Service. Bridging + Customer Reconfigurable (a.k.a. AT&T Midwest region Base Rate) |
| XGAX (MW only) | Digital Data, Digital Access Channel Service DA3 9.6 Kbps BDDS, Basic Dedicated Digital Service. Point-to-Point Without Error Correction (a.k.a. AT&T Midwest region Base Rate) |

NOTE: XG-- with 2 CFAs is a through ckt. XG-B with 1 CFA is an MJU to SRDM ckt.

| NC Code | Description |
| --- | --- |
| XH- - (Not valid in MW) | Digital Data, Digital Access Channel Service (DA4) 56 Kbps ~ DDS |
| XH-B (Not valid in MW) | Digital Data, Digital Access Channel Service (DA4) 56 Kbps ~ DDS Bridging |
| XH-C (SE only) | Digital Data, Digital Access Channel Service (DA4) 56 Kbps ~ DDS ~ Customer Reconfigurable |
| XH-G (SE only) | Digital Data, Digital Access Channel Service DA4 56 Kbps ~ DDS ~ Digital Packet Uni-Directional Polling e.g., Frame Relay |
| XH-R (SE only) | Digital Data, Digital Access Channel Service DA4 56 Kbps ~ DDS ~ Digital Packet |
| XHA- (MW, W only) | Digital Data, Digital Access Channel Service DA4 56 Kbps BDDS, Basic Dedicated Digital Service. (a.k.a. AT&T Midwest region Base Rate) |
| XHAB (MW, W only) | Digital Data, Digital Access Channel Service DA4 56 Kbps BDDS, Basic Dedicated Digital Service. Bridging (a.k.a. AT&T Midwest region Base Rate) |
| XHAC (MW, W only) | Digital Data, Digital Access Channel Service DA4 56 Kbps BDDS, Basic Dedicated Digital Service. Customer Reconfigurable (a.k.a. AT&T Midwest region Base Rate) |
| XHAE (MW only) | Digital Data, Digital Access Channel Service DA4 56 Kbps, BDDS, Basic Dedicated Digital Service, with Secondary Channel (a.k.a. AT&T Midwest region Base Rate) |
| XHAP (MW, W only) | Digital Data, Digital Access Channel Service DA4 56 Kbps BDDS, Basic Dedicated Digital Service. Packet (a.k.a. AT&T Midwest region Base Rate) |
| XHAV (MW only) | Digital Data, Digital Access Channel Service DA4 56 Kbps BDDS, Basic Dedicated Digital Service. Bridging + Customer Reconfigurable (a.k.a. AT&T Midwest region Base Rate) |
| XHB- (Not valid in MW) | Digital Access (DA4) 56 Kbps Secondary Channel (Note Secondary Channel and Transfer Arrangements are Not allowed when interfacing with DovLink Service. DovLink Service is identified by an NCI code of 02DV5BA. |
| XHH- (MW, W only) | Digital Data, Digital Access Channel Service DA4 56 Kbps BDDS, Basic Dedicated Digital Service, with Secondary Channel (a.k.a. AT&T Midwest region Base Rate) |

NOTE: XH-- with 2 CFAs is a through ckt. XH-B with 1 CFA is an MJU to SRDM ckt.

| NC Code | Description |
| --- | --- |
| XRF- (W only) | Advanced Digital Network ~ Fixed Speed -DDs without Diagnostic Capability or Secondary Channel |
| XRFB (W only) | Advanced Digital Network ~ Fixed Speed -DDs without Diagnostic Capability or Secondary Channel – Bridging |
| XRFC (W only) | Advanced Digital Network ~ Fixed Speed -DDs without Diagnostic Capability or Secondary Channel - Customer Reconfigurable |
| XRFP (W only) | Advanced Digital Network ~ Fixed Speed -DDs without Diagnostic Capability or Secondary Channel - Public Packet Switching |
| XRH- (W only) | Advanced Digital Network ~ Fixed Speed - Over GDT with Secondary Channel |
| XRS- (W only) | Advanced Digital Network ~ Fixed Speed -DDs w/Secondary Channel Capability |
| XRSB (W only) | Advanced Digital Network ~ Fixed Speed -DDs w/Secondary Channel Capability – Bridging |
| XRSC (W only) | Advanced Digital Network ~ Fixed Speed -DDs w/Secondary Channel Capability - Customer Reconfigurable |
| NC Code | Description |
| YHGA (SE only) | DS3, Fractional DS3/NxDS1 Fast Packet, Frame Relay, UNI at 3.0 MBPS |
| YHGB (SE only) | DS3, Fractional DS3/NxDS1 Fast Packet, Frame Relay, UNI at 4.5 MBPS |
| YHGC (SE only) | DS3, Fractional DS3/NxDS1 Fast Packet, Frame Relay, UNI at 6.0 MBPS |
| YHGD (SE only) | DS3, Fractional DS3/NxDS1 Fast Packet, Frame Relay, UNI at 7.5 MBPS |
| YHGE (SE only) | DS3, Fractional DS3/NxDS1 Fast Packet, Frame Relay, UNI at 9.0 MBPS |
| YHGF (SE only) | DS3, Fractional DS3/NxDS1 Fast Packet, Frame Relay, UNI at 10.5 MBPS |
| YHGG (SE only) | DS3, Fractional DS3/NxDS1 Fast Packet, Frame Relay, UNI at 12.0 MBPS |
| YHUA (SE only) | DS3, Fractional DS3/NxDS1 ATM UNI at 3.0 MBPS |
| YHUB (SE only) | DS3, Fractional DS3/NxDS1 ATM UNI at 4.5 MBPS |
| YHUE (SE only) | DS3, Fractional DS3/NxDS1 ATM UNI at 9.0 MBPS |

| NC Code | Description |
| --- | --- |
| YNS- (Not valid in SE) | Voice Grade, Signaling Link ~Signaling System 7 Links |
| YNSA (Not valid in SE, W) | Voice Grade, Signaling Link ~Signaling System 7 Links Line Information Data Base (LIDB) |
| YNSD (Not valid in SE, W) | Voice Grade, Signaling Link ~ Signaling System 7 Links Feature Group D (FGD) |
| YNSE (SE only) | Voice Grade, Signaling Link~ Signaling System 7 Links; SS7 link End Office to STP |
| YNSF (SE only) | Voice Grade, Signaling Link~ Signaling System 7 Links; SS7 link between STPs |
| YNSX (Not valid in SE, W) | Voice Grade, Signaling Link ~Signaling System 7 Links: All Offered Services |

# Text boxes

AT&T

TAB 2

3rd & 4th Character

Network Channel

(NC) Codes