As a result of a Six Sigma improvement process; The AT&T Carrier Coding Guide (CCG) is being revamped and modified to help improve the Ease of Use for our Customers.

Effectively Immediately

TABs 3 through 7 have been consolidated into TAB 3.  TABs 4 through 7 have been retired and the information previously found in those TABs are now found in TAB 3 as separate sections with the Network Channel Interface (NCI) component definitions.

| Section | Contents | Page |
| --- | --- | --- |
| 1 2 | Network Channel Interface (NCI) Physical Conductors Code (Previously found in TAB 3) NCI Impedance Code (Previously found in TAB 5) | 3 4 |
| 3 | NCI Protocol and Protocol Option Codes (Previously found in TAB 4 and 6 ~ now consolidated into a single section) | 7 |
| 4 | NCI Transmission Level Point Code | 28 |
|  | (Previously found in TAB 7) |  |

Sample Network Channel Interface Code format:

Section 1	     Section 3    Sec 2            Section 3			Section 4

Notes:

- References to a SECNCI are from a field identification created by the Order and Billing Forum (OBF).

- NCI codes can be used in either the NCI or SECNCI fields for ordering purposes between trading partners.

NCIs are a minimum of 5 characters in length.  If Protocol Options and TLPs are required, they are reflected left justified.

Section 1 ~ Network Channel Interface (NCI) Physical Conductors Code

(Previously found in TAB 3)

Physical Conductors - The Physical Conductors Code describes the number of wires that transverse the POT at the Customer and the Customer’s End User.  The number of conductors include the signaling leads.  Examples:

- A 4-wire Full Duplex Data circuit would normally have a 04 in this field.

- A 4-wire Tie Line with Type I E&M signaling at the POT would have a 06 in this field.

- A 150 baud Telegraph channel using a 108 Data Set at the POT would have a 10 in this field.

- A 2-wire Tie Line interface with Type I E&M at the POT would have a 04 in this field.

NUMBER OF CONDUCTORS             CODE

1		01

2		02

4		04

6		06

7		07

8		08

9		09

10		10

12		12

14	14

16		16

- 18

20		20

Section 2 ~ NCI Impedance Code

(Previously found in TAB 5)

The impedance presented by the Customer or the End User terminal equipment to AT&T.  This is the normal reference impedance with which the Customer or the End User will terminate the channel for the purpose of evaluating transmission performance. Below is a listing of the currently approved Impedance Codes that may be used in AT&T.

Impedance Code

VALUE (ohms)			CODE

110	0 &

600	2

- 3 ^

135	5

75	6

VARIABLE	8@

- 9

50		C %

FIBER	F

## Multi Impedance	M

NONE	N

& = Limited use in Southeast Region only

^ = Limited use in AT&T

@ = Not used with SONET…use "F"

% = this is offered only in AT&T Illinois and only with the WD NC code.

Additional Notation:  Numeric Impedance values are used when service is provided with an Electrical handoff (generally over Copper). Optical services and Fiber facilities use normally use the “F” designation.

Section 3 ~ NCI Protocol and Protocol Option Codes (previously found in TABs 4 & 6 now consolidated into a single section); Protocol Code (PC) - The PC will identify the signaling and/or the transmission characteristics at the POT at the Customer or End User location interfacing AT&T’s provided segment.  The PC combinations for the Customer and the End User POT are listed in the tariff(s).  Examples of PC’s are:

- A Switched Access FGA at the IC POT may have a Protocol Code of LS or GS at the Customer (Loop Start or Ground Start Signaling-closed end).  See LATA 2 below.

- A Special Access VG2/LC channel used for an End-to-End FX circuit may have a Protocol Code of LO (Loop Start-open end) at the IC POT and LS (Loop Start-Closed End) at the EU premises.  See LATA 1 below.

- A Special Access VG3/LD channel used for an End-to-End Tie Line is typically requested with E&M type I interface at the End User.  The Protocol Code for this configuration is EA.

- A Special Access VG6/LG channel used for data operation would typically be requested with a DA Protocol Code at the End User premises.

NOTE -	The term "IC" in the following pages refers to the InterLATA customer.

-	The term "End User" in the following pages refers to the IC's customer.

LATA 1				LATA 2

F

A	B	C	D	E

/		  \

S	S

F	F	F	F	F	F

X	X	/	/	X	X

S	O	F      Analog	F	S	O

Cable                    T-CXR         Cable       X       CXR	X	Cable	 	T-CXR

S	O

POT	POT	POT

PC=LS	PC=LO	PC=LS

<               VG2/LC Channel        > < IntraLATA Customer    > <      FGA/SD Channel       >

<                                                        End to End FX Circuit                                                   >

A = SWC of EU in LATA 1				D = IC Premises in LATA 2

B = SWC of IC in LATA 1				E = SWC of IC in LATA 2

C = IC Premises in LATA 1				F = FGA Office

Protocol Option Codes - Provides a further definition of the transmission and signaling requirements at the Point of Termination (POT) at the Customer or the End User or the handoff in the Central Office.  This option code specifies such things as the digital format, bandwidth, or signaling ranges for the equipment that terminates the channel.

Example : 	Protocol Code CS (Digital Cross-Connect System (DCS) Termination)

Protocol Option =	 10 = DS1 to DS0

10R = DS1 to DS0 Customer Reconfigurable

1S = 1.544 Mbps (DS1) ANSI ESF and B8ZS Clear Channel Capability

per GR-342-CORE.

In this example the options describe the type of handoff and/or features.

Example:     Protocol Code DS (Digital Hierarchy Interface @ either Customer or End User Premises)

Protocol Option Code = 44 = 44.736 Mbps, (DS3), M2/3 Format

44A = Asynchronous Fiber 1-DS3 or 45 Mb/s Unchannelized

Application and C-Bit Parity

44R = M-Framed, Unchannelized

NOTE: When a customer can indicate “C-Bit Parity” in the NC code, then they do NOT have to use the NCI code that speaks to C-Bit Parity.  The distinction in the NCI codes is only needed if the customer is ordering C-Bit Parity but it is not reflected in the NC code.

When a Protocol Option Code is required, and transmission levels are not specified, a delimiter (.) must be placed immediately after the Impedance Code.

Example: 06EA2.M = Protocol EA with M option and no specified transmission levels.

When a Protocol Option Code is required, and transmission levels are specified, one delimiter (.) must be placed between the Impedance Code and the Protocol Option Code and a second delimiter (.) must be placed between the Protocol Option and the Transmission Level Codes.

Ex:  06EA2.M.AZ = Protocol EA with M option and transmission levels AZ specified.

If a Protocol Option Code is not applicable and transmission levels are specified, then two delimiters (..) must be placed after the Impedance Code followed by the Transmission Level Codes.

Example:  04DB2.  AZ = Protocol DB without option and Transmission Levels AZ specified.

If a Protocol Option Code is not applicable and transmission levels are not specified, then no delimiters are required.

Example:  04DB2 = CI with no options and no transmission levels specified.

Effectively Immediately, ER4 optics, for NCI Protocol, LN, OT, QB; Options, 403 and CE4 have been Manufacture Discontinued and are NO LONGER ORDERABLE.

| Protocol | Protocol Option | Definition |
| --- | --- | --- |
| AB (Not available in MW) | Connects an IC To an Access Service for The Transmission of Voice And 20-Hz Ring down (Pushbutton) Signaling (in both directions; Typically, IC FHN or equivalent.) |
|  |  | No Protocol Option required for this code. |
| Protocol | Protocol Option | Definition |
| AH (Not available in MW) | Connects an IC To an Access Service for the Transmission of Voice And 20-Hz Ring down (Pushbutton) Signaling (in both directions; Typically, IC FHN or equivalent.) |
|  |  | Cannot be ordered without a Protocol Option |
|  | B | 60 kHz to 108 kHz (12 Channels) |
|  | C | 312 kHz to 552 kHz (60 Channels) |
|  | D | 564 kHz to 3084 kHz (600 Channels) |
| Protocol | Protocol Option | Definition |
| CM | SONET ADM Termination |
|  |  | Cannot be ordered without a Protocol Option |
|  | C3 | OC-3 Drop-Side, ADM Port |
|  | C12 | OC-12 Drop-Side, ADM Port |
|  | C48 | OC-48 Drop-Side, ADM Port |
|  | C92 | OC-192 Drop-Side, ADM Port |
|  | S | STS-1 Drop-Side, ADM Port |
|  | 1 | DS1 Drop-Side, ADM Port |
|  | 100 | 100 Mbps Ethernet |
|  | 3 | DS3 Drop-Side, ADM Port |
|  | 9 | 100 Ohms |
| Protocol | Protocol Option | Definition |
| CN (SE only) | Central Office Monitoring Node Termination |
|  |  | Cannot be ordered without a Protocol Option |
|  | 100 | 100 Mbps Ethernet |
|  | 1GE | 1 Gbps Ethernet |
| Protocol | Protocol Option | Definition |
| CS | Digital Cross-Connect System (DCS) Termination |
|  |  | Cannot be ordered without a Protocol Option |
|  | 9 | 100 Ohms |
|  | 10 | DS1 to DS0 |
|  | 10R | DS1 to DS0 Customer Reconfigurable |
|  | 11 | DS1 to DS1 (available only in Midwest region) |
|  | 11R | DS1 to DS1 Customer Reconfigurable |
|  | 15 | 1.544 Mbps (DS1) Super Frame (SF) format and AMI per GR-342-CORE |
|  | 15B | 1.544 Mbps (DS1) Super Frame (SF) format and B8ZS Clear Channel Capability per GR-342-CORE |
| Protocol | Protocol Option | Definition |
| CS (cont.) | 1S | 1.544 Mbps (DS1) ANSI ESF and B8ZS Clear Channel Capability per GR-342-CORE. |
|  | 31 | DS3 to DS1 |
|  | 31R | DS3 to DS1 Customer Reconfigurable |
|  | 33 | DS3 to DS3 |
|  | 33R | DS3 to DS3 Customer Reconfigurable |
|  | BM | OC-3 DCS Port Termination - SONET STS-3 Path is terminated at the DCS (typical DCS multiplexing may occur) (available only in Midwest region) |
|  | D1 | OC-12 DCS Port Termination - SONET STS-12 path is not terminated at the DCS (it passes intact through the DCS) (available only in the Midwest region) |
|  | DM | OC-12 DCS Port Termination - SONET STS-12 Path is Terminated at the DCS (typical DCS Multiplexing may occur) (available only in the Midwest region) |
|  | GO | Ground-Start Loop Signaling Open End (available only in the Midwest region) |
|  | LS | Loop-Start Signaling Closed End (available only in the Southwest & West regions) |
|  | NO | Transmission Only- No Signaling (available only in the Midwest region) |
|  | R | Customer Reconfigurable (available only in the West region) |
|  | S1 | 51.840 Mbps (STS-1) (not applicable in the West region) |
|  | S1R | 51.840 Mbps (STS-1) Customer Reconfigurable Note: (available only in the Southeast and Southwest regions) |

| Protocol | Protocol Option | Definition |
| --- | --- | --- |
| CT | CENTREX TIE TRUNK TERMINATION. Connects an End User to Theoretical CO Centrex Tie Trunk Equipment. This code will identify the drop side of the Centrex Tie Trunk. The Customer will be able to order tie trunk terminations without having to concern itself with the type (Type I, II or III) of E&M signaling or the loss of the Centrex Tie Trunk. The Customer will now be able to specify the desired receive level into the Centrex switch. |
|  | Note: Cannot be ordered without a Protocol Option |

| Protocol | Protocol Option | Definition |
| --- | --- | --- |
| CX | Digital Termination on A Switch/Router |
|  |  | Can be ordered with no Protocol Option if applicable (note: when no protocol Option is used, this protocol will indicate that the termination is at the DS1 rate (i.e., 04CX9 means digital termination on a switch/router at the DS1 rate). |
|  | 10G | 10 Gbps Ethernet |
|  | 10T | 10 Base T Ethernet |
| Protocol | Protocol Option | Definition |
| CX | 1CC | 100 Mbps Ethernet User to Network Interface (UNI) with CNM (Customer Network Management) (available only in Southeast Region) |
|  | 1CD | Ethernet User to Network Interface (UNI) with bursting up to 100 Mbps and CNM (Customer Network Management) (available only in the Southeast region) |
|  | 1CE | 100 Mbps Ethernet User to Network Interface (UNI) with Priority (allows customer to prioritize their data) |
|  | 1CF | Ethernet User to Network Interface (UNI) with bursting up to 100 Mbps and Priority (allows customer to prioritize their data) (available only in the Southeast region) |
|  | 1CG | 100 Mbps Ethernet User to Network Interface (UNI) with Priority and CNM (available only in the Southeast Region) |
|  | 1CH | Ethernet User to Network Interface (UNI) with bursting up to 100 Mbps, Priority and CNM (available only in the Southeast region) |
|  | 1CT | 100Base-T Ethernet User to Network Interface (UNI) |
|  | 1E | 1.544 Mb/s (DS1) termination on a Switch/Router dedicated to an E911 network |
|  | 1GB | Ethernet User to Network Interface (UNI) with bursting up to 1 Gbps (available only in the Southeast region) |
|  | 1GC | 1 Gbps Ethernet User to Network Interface (UNI) with CNM (Customer Network Management) (available only in the Southeast region) |
|  | 1GD | Ethernet User to Network Interface (UNI) with bursting up to 1 Gbps and CNM (Customer Network Management) (available only in the Southeast region) |
|  | 1GE | 1 Gbps Ethernet User to Network Interface (UNI) |
|  | 1GF | Ethernet User to Network Interface (UNI) with bursting up to 1 Gbps and Priority (allows customer to prioritize their data) (available only in the Southeast region) |
|  | 1GG | 1 Gbps Ethernet User to Network Interface (UNI) with Priority and CNM (available only in the Southeast region) |
|  | 1GH | Ethernet User to Network Interface (UNI) with bursting up to 1 Gbps, Priority and CNM (available only in the Southeast Region) |
|  | 1GJ | 1 Gbps Ethernet User to Network Interface (UNI) with Priority (allows customer to prioritize their data) (available only in the Southeast region) |
|  | 1GT | 1 Gbps Ethernet User to Network Interface (UNI) with Network Edge Interface for Cloud access. |
|  | 1HG | 100 Gbps Ethernet User to Network Interface (UNI) |
|  | 1HT | 10 Gbps Ethernet User to Network Interface (UNI) with Network Edge Interface for Cloud access. |
|  | 1P | 1.544 Mb/s (DS1) termination on an ISDN Switch |
|  | 2A | DS1 termination dedicated to End User Aggregation (available only in the Southeast region) |
|  | 2S | DS1 termination for End User Aggregation with shared ATM traffic (available only in the Southeast region) |
| Protocol | Protocol Option | Definition |
| CX (cont.) | Digital Termination on A Switch/Router |
|  | 3 | 44.736 Mbps (DS3) |
|  | 3A | DS3 termination dedicated to End User Aggregation (available only in the Southeast region) |
|  | 3E | 44.736 Mbps (DS3) termination on a Switch/Router dedicated to an E911 network |
|  | 3S | DS3 termination for End User Aggregation with shared ATM traffic (available only in the Southeast region) |
|  | 31M | DS3 Termination with Inverse Multiplexing over ATM (IMA) per ATM Forum IMA 1.1 (available only in the Southeast region) |
|  | A | OC3 Termination on a switch |
|  | AA | OC-3 termination dedicated to End User Aggregation (available only in the Southeast region) |
|  | AS | OC-3 termination for End User Aggregation with shared ATM traffic (available only in the Southeast region) |
|  | B | OC12 Termination on a switch (available only in the Southeast region) |
|  | BA | OC-12 termination dedicated to End User Aggregation (available only in the Southeast region) |
|  | BM | OC12 Termination with multiplexing capabilities |
|  | BS | OC-12 termination for End User Aggregation with shared ATM traffic (available only in the Southeast region) |
|  | ML1 | DS1 termination supporting Multi-Link Frame Relay per FRF.16 (available only in the Southeast region) |
|  | ML3 | DS3 termination supporting Multi-Link Frame Relay per FRF.16 (available only in the Southeast region) |
|  | NXC | 10 Gbps Ethernet ENNI termination per MEF 26, COS Enabled. (Supports multiple classes of service via the subsequently ordered OVCs. |
|  | XGT | 10 Gbps Ethernet User to Network Interface (UNI) with Network Edge Interface for Cloud access. |
|  | X20 | 400G BASE-FR4, 400 Gbps over wavelengths of 1264.5 – 1277.5, 1284.5 – 1297.5, 1304.5 – 1317.5 or 1324.5 – 1337.5 nm with reach up to 2000m. |

| Protocol | Protocol Option | Definition |
| --- | --- | --- |
| DA | Connects End-User Premise to An Access Service Suitable for The Transmission Of Data And/or Control Supervisory Signals (Data Stream in VF Band at Cust. or End User Premises. AT&T equipment is required at the customer premises. |
|  |  | No Protocol Option required for this code. |
|  | L | Line Powered (Sealing Current) data station termination, for backup power only. |
|  | S | Sealing Current Option for 4W Transmission ~ AT&T will provide sealing current generator at CO and will provide equipment (829 or EQVLT) at Customer or End User Premises to complete the simplex path. Typically, applicable for VG5, VG6 and VG10. |

| Protocol | Protocol Option | Definition |
| --- | --- | --- |
| DB | Connects an Interexchange CXR To an Access Service Suitable for The Transmission Of Data And/or Control Supervisory Signals |
|  |  | No Protocol Option required for this code. |
|  | 10 | Frequency Shift (108 Data Set Type) VF for TG1 and TG2. |
|  | 43 | 43A1 to 43B1 Carrier format ~ Telegraph carrier type signals, TG1 and TG2. (not available in the Midwest region) |

| Protocol | Protocol Option | Definition |
| --- | --- | --- |
| DC | Direct Current or Voltage @ either Customer or End User Premises |
|  |  | Cannot be ordered without a Protocol Option |
|  | 1 | Monitoring Interface with Series RC Combination (McCulloh Format) |
|  | 2 | Telephone company energized alarm signal |
|  | 3 | Metallic Facility (DC continuity), DC Current/Low Frequency Control Signals or Low Speed Data (30 Baud) |

Note: The “DC” Protocol code and associated Options are not available in the Midwest region

| Protocol | Protocol Option | Definition |
| --- | --- | --- |
| DD | Connects an IC To an Access Service Suitable for The Transmission of Data or Tones |
|  |  | No Protocol Option required for this code. |

| Protocol | Protocol Option | Definition |
| --- | --- | --- |
| DE | Connects A Customer to An Access Service Suitable for The Transmission of Data or Tones ~ Dataphone Select-A-Station interface @ End User Premises; AT&T -CSU or 829 DAS. Requires AT&T equipment at customer premises. |
|  |  | No Protocol Option required for this code. |

Note: The “DE” Protocol code is not available in the Midwest region.

| Protocol | Protocol Option | Definition |
| --- | --- | --- |
| DM | Data Stream in VF Or Digital Band at CO Location. (Interface at Data Modem at Central Office) |
|  |  | Cannot be ordered without a Protocol Option |
|  | 1 | 300 Bps 103J Type Modem Operation |
|  | 2 | 1200 Bps 212A Type Modem Operation |
|  | 6 | 9600 Bps ITU-T V .29 Type Modem |
|  | E | CSU/DSU (available only in the Southeast region) |

Note: The “DM” Protocol code and associated Options are only available in the West, Southeast & Southwest regions

| Protocol | Protocol Option | Definition |
| --- | --- | --- |
| DS | Digital Hierarchy Interface @ either Customer or End User Premises |
|  |  | Cannot be ordered without a Protocol Option |
|  | 15 | 1.544 Mbps (DS1) Super Frame (SF) Format and AMI per GR-342-CORE |
|  | 15B | 1.544 Mbps (DS1) Super Frame (SF) Format and B8ZS Clear Channel Capability per GR-342-CORE |
|  | 15E | 8-Bit PCM Encoded in one 64 Kbps of the DS1 Signal |
|  | 15F | 8-Bit PCM Encoded in two 64 Kbps of the DS1 Signal |
|  | 15G | 8-Bit PCM Encoded in three 64 Kbps of the DS1 Signal |
|  | 15H | 14/11-Bit PCM Encoded in six 64 Kbps contiguous time slots of a Digital High Cap Carrier System |
|  | 1K | 1.544 Mbps (DS1) ANSI Extended Super Frame Format (ESF) and AMI per GR-342-CORE |
|  | 1KP | 1.544 Mbps (DS1) ANSI Extended Super Frame Format (ESF) and AMI per GR-342-CORE with (NPRM) Network Performance Report Message per ANSI T1.403. |
|  | 1S | 1.544 Mbps (DS1) ANSI Extended Super Frame Format (ESF) and B8ZS Clear Channel Capability per GR-342-CORE |
|  | 1SP | 1.544 Mbps (DS1) ANSI Extended Super Frame Format (ESF) and B8ZS Clear Channel Capability per GR-342-CORE with (NPRM) Network Performance Report Message per ANSI T1.403. |
|  | 31 | 3.152 Mbps, (DS1C), Robbed Bit |
|  | 44 | 44.736 Mbps, (DS3), M2/3 Format |

## NOTE: 44A through 44J are shown in approximate multiples of DS3 bit rates, actual rates may vary

|  | 44 | 44.736 Mbps, (DS3), M2/3 Format |
| --- | --- | --- |
|  | 44A | Asynchronous Fiber 1-DS3 or 45 Mb/s Unchannelized Application and C-Bit Parity. |
|  | 44B | Asynchronous Fiber 2-DS3 or 90 Mb/s (not available in the West region) |
|  | 44C | Asynchronous Fiber 3-DS3 or 135 Mb/s |
|  | 44D | Asynchronous Fiber 4-DS3 or 180 Mb/s |
|  | 44E | Asynchronous Fiber 6-DS3 or 270 Mb/s |
|  | 44F | Asynchronous Fiber 9-DS3 or 405 Mb/s |
|  | 44G | Asynchronous Fiber 12-DS3 or 540 Mb/s |
|  | 44H | Asynchronous Fiber 18-DS3 or 810 Mb/s (not available in the West region) |
|  | 44I | Asynchronous and Channelized Application C-Bit Parity |
|  | 44J | Asynchronous Fiber 36-DS3 or 1,620 Mb/s (not available in the West region) |
|  | 44R | M-Framed, Unchannelized |

| Protocol | Protocol Option | Definition |
| --- | --- | --- |
| DS (Cont.) | Digital Hierarchy Interface @ either Customer or End User Premises |
|  | 63 | 6.312 Mbps, (DS2), Robbed Bit (available only in the Southeast region) |
|  | EA | E&M Lead Signaling at AT&T Hub for voice Through-Connect and NRS service |
|  | GO | Ground start loop signaling, open end at AT&T) Hub for Through-Connect / NRS |
|  | GS | Ground start loop signaling, closed end at AT&T Hub for Through-Connect/ NRS |
|  | LO | Loop start loop signaling, open end at AT&T Hub for Through-Connect or NRS |
|  | LS | Loop start loop signaling, closed end at AT&T Hub for Through-Connect or NRS |
|  | NO | No signaling, transmission only at AT&T Hub for voice Through-Connect / NRS |
|  | M10 | DS1 Multiplexer at an Access Customer (for use with double-ended mux circuits) |
|  | M31 | DS3 Multiplexer at an End User or Access Customer (available only in the Southeast region) |
|  | SY | Unidirectional Synch Interface (available only in the West region) |

| Protocol | Protocol Option | Definition |
| --- | --- | --- |
| DU | Digital Access Interface @ End User Premises |
|  |  | Cannot be ordered without a Protocol Option |
|  | 001 | Spectrum Management Class 1. |
|  | 002 | Spectrum Management Class 2. |
|  | 003 | Spectrum Management Class 3. |
|  | 004 | Spectrum Management Class 4. |
|  | 005 | Spectrum Management Class 5. |
|  | 007 | Spectrum Management Class 7. |
|  | 008 | Spectrum Management Class 8. |
|  | 00A | ADSL Using Discrete Multi-Tone (DMT) format |
|  | 00H | HDSL per iconectiv (previously known as Telcordia Technologies) TA-NWT-001210 |
|  | 19 | 19.2 Kbps |
|  | 19S | 19.2 Kbps with Secondary Channel |
|  | 1KN | 1.544 Mbps (DS1) ANSI ESF Format and AMI, without line power per GR-54-CORE |
|  | 1KP | 1.544 Mbps (DS1) ANSI ESF Format and AMI, without line power per GR-54-CORE with (NPRM) Network Performance Report Message per ANSI T1.403 |
|  | 1KX | 1.544 Mbps (DS1) ANSI ESF Format and AMI, with 0 attenuation (guaranteed DSX1 signal template per GR-342-CORE), without line power per GR-54-CORE |
|  | 1NP | 1.544 Mbps (DS1) ANSI ESF Format with B8ZS Clear Channel Capability, without line power per GR-54-CORE with (NPRM) Network Performance Report Message Per ANSI T1.403. |
|  | 1SN | 1.544 Mbps (DS1) ANSI ESF Format with B8ZS Clear Channel Capability, without line power per GR-54-CORE |
|  | 1SP | 1.544 Mbps (DS1) ANSI ESF Format with B8ZS Clear Channel Capability, without line power and with 0 attenuation (guaranteed DSX1 signal template per GR-342-CORE), per GR-54-CORE and with (NPRM) Network Performance Report Message per ANSI T1.403. |

| Protocol | Protocol Option | Definition |
| --- | --- | --- |
| DU (Cont.) | Digital Access Interface @ End User Premises |
|  | 1XP | 1.544 Mbps (DS1) ANSI ESF Format and AMI, with 0 attenuation (guaranteed DSX1 signal template per GR-342-CORE), without line power per GR-54-CORE and with (NPRM) Network Performance Report Message per ANSI T1.403. |
|  | 24 | 2.4 Kb/s |
|  | 24S | 2.4 Kb/s with Secondary Channel (available only in the West region) |
|  | 48 | 4.8 Kb/s |
|  | 48S | 4.8 Kb/s with Secondary Channel (available only in the West region) |
|  | 56 | 56 Kb/s |
|  | 56A | Non- LEC switched (e.g., switched 56 Kbps/s service i.e., Accunet) (available only in the West region) |
|  | 56C | Non- LEC switched 56 Kb/s (Dedicated 56 Kb/s to IC optioned for call setup signaling). Technician performs call completion test from end users network interface. |
|  | 56S | 5.6 Kb/s w/ Secondary Channel |
|  | 64 | 64 Kb/s |
|  | 96 | 9.6 Kb/s |
|  | 96S | 9.6 Kb/s with Secondary Channel (available only in the West region) |
|  | BN | 1.544 Mbps (DS1) Super Frame (SF) Format and AMI, without line power per GR-54-CORE |
|  | DN | 1.544 Mbps (DS1) Super Frame (SF) Format with B8ZS Clear Channel Capability and without line power per Technical Reference GR-54-CORE |
|  | LR | Automatic Ring Down Signaling (only valid w/NC = LCI-) |
|  | LS5 | Loop Start Signal + High Frequency Portion with Spectrum Management Class 5. (Used with Line Splitting and Line Sharing) |
|  | M10 | DS1 Multiplexer at an End User Premises (for use with double-ended mux circuits) |
|  | SY | Uni-directional Sync Interface (available only in the West region) |

| Protocol | Protocol Option | Definition |
| --- | --- | --- |
| DV | Data and Voice Multiplexing at AT&T central office for DovLink service |
|  |  | Cannot be ordered without a Protocol Option |
|  | BA | 2.4 Kb/s Digital Data over Voice |
|  | BB | 4.8 Kb/s Digital Data over Voice |
|  | BC | 9.6 Kb/s Digital Data over Voice |
|  | BL | 19.2 Kb/s Digital Data over Voice |

Note: DV Protocol code is not available in the Midwest region.

| Protocol | Protocol Option | Definition |
| --- | --- | --- |
| DW | Unidirectional Digital Signal |
|  |  | Cannot be ordered without a Protocol Option |
|  | 44V | Video Signal, M-framed at 44.736 Mbps using B3ZS Line Code |

| Protocol | Protocol Option | Definition |
| --- | --- | --- |
| EA | Type I, E&M Lead Signaling |
|  |  | Cannot be ordered without a Protocol Option |
|  | E | IC or End User originates on E-Lead |
|  | M | IC or End User originates on M-Lead |

| Protocol | Protocol Option | Definition |
| --- | --- | --- |
| EB | Type II, E&M Lead Signaling |
|  |  | Cannot be ordered without a Protocol Option |
|  | E | IC or End User originates on E-Lead |
|  | M | IC or End User originates on M-Lead |

| Protocol | Protocol Option | Definition |
| --- | --- | --- |
| EC | Type III, E&M Lead Signaling |
|  |  | Cannot be ordered without a Protocol Option |
|  | E | IC or End User originates on E-Lead |
|  | M | IC or End User originates on M-Lead |

| Protocol | Protocol Option | Definition |
| --- | --- | --- |
| EX | Back-to-back carrier using 4-state signaling, AT&T and Customer Tandem units. |
|  |  | Cannot be ordered without a Protocol Option |
|  | A | LEC has closed end of circuit; VG2 (LC) or equivalent. |
|  | B | LEC has open end of circuit; AT&T dial tone; Feature Group A or equal |

| Protocol | Protocol Option | Definition |
| --- | --- | --- |
| FC | Fiber Optic Interface (Non-SONET) |
|  |  | Cannot be ordered without a Protocol Option |
|  | 10 | Transmission bit rate up to 100 Mbps |
|  | 10C | LR-MLM, Fast Ethernet, 1310 nm, NRZ, 100 Mbps, SLM Fiber |
|  | 10D | IR-MLM, Fast Ethernet, 1310 nm, NRZ, 100 Mbps, 62.5-micron Fiber |
|  | 125 | 1.25 Gbps |
|  | 19 | 1900 MHz (Offered in AT&T Illinois only) |
|  | 24 | 2.4 Gbps (available only in the Southeast region) |
|  | 62 | 622.080 Mbps |
|  | 8 | Pass Band from 824 to 894 MHz (Offered in AT&T Illinois only- Future offering in other AT&T locations (verify availability) |
|  | X | Dark Fiber |
| Protocol | Protocol Option | Definition |
| FM | Wavelength Division Multiplexing Interface (DWDM per ITU-694.1 or CWDM per ITU-G.694.2) |
|  |  | Cannot be ordered without a Protocol Option |
|  | 004 | Multiplexer with access to 4 wavelengths |
|  | 008 | Multiplexer with access to 8 wavelengths |
|  | 012 | Multiplexer with access to 12 wavelengths |
|  | 016 | Multiplexer with access to 16 wavelengths |
|  | 024 | Multiplexer with access to 24 wavelengths (available only in the Southeast) |
|  | 032 | Multiplexer with access to 32 wavelengths |
|  | 064 | Multiplexer with access to 64 wavelengths (available only in the Southeast) |
|  | 080 | Multiplexer with access to 80 wavelengths (available only in the Southeast) |
|  | S | Sub Rate Mux, 4 ports @ 50-270 Mbps each |
|  | S3 | Sub Rate Mux, 2 ports @ up to 1.25 Gbps each (GigE, Fibre Channel, FICON) |
|  | S4 | Sub Rate Mux, 8 ports of ESCON @ 200 Mbps each. |
|  | S5 | Sub Rate Mux, 4 ports of SONET/SDH @ OC3 or OC12. |
|  | S8 | Sub Rate Mux, a 10-port sub rate mux supporting any combination of 1 & 2 Gbps services up to the 10 Gbps limit |
|  | S9 | Sub Rate Mux, 4-ports of SONET OC48/OC48c |
|  | S11 | Sub Rate Mux, 8 Ethernet ports @ 1 Gbps each |
|  | S12 | Sub Rate Mux, 8-port sub rate mux supporting any combination of 1 Gbps (GigE, Fibre Channel, FICON) & 2 Gbps (Fibre Channel, FICON) services up to the 10 Gbps limit. |

| Protocol | Protocol Option | Definition |
| --- | --- | --- |
| FT | Optical Transport Network (OTN) Line-side Multiplexer Termination |
|  | T2C | OTU2, GigE and OTU1 |
|  | T4C | OTU4, supporting drops of OTU2, OTU2e, 10 Gbps WAN PHY, 10 Gbps LAN PHY |

| Protocol | Protocol Option | Definition |
| --- | --- | --- |
| GO | Ground Start Signaling Open-End (Switch) Function Presented by IC At Interface to The Telephone Company Access Service. |
|  |  | Can be ordered with no Protocol Option if applicable |
|  | X | Simplex Reversal (4-Wire) |

| Protocol | Protocol Option | Definition |
| --- | --- | --- |
| GS | Ground Start Signaling Closed-End (Station) Function Presented by IC or End-User At Interface to LEC Access Service |
|  |  | Can be ordered with no Protocol Option if applicable |
|  | C | CENTREX Foreign Exchange Trunk Termination (Used to identify CO Centrex ground start trunk termination. Drop side of trunk) |
|  | M | CO Answering Service Concentrator (Interface appears in an AT&T Central Office concentrator provided for a Telephone Answering Service (TAS) customer.) |
|  | T | Coin Tone Operated (available only in the West region) |
|  | U | Coin Battery Operated (available only in the West region) |
|  | X | Simplex Reversal (4-Wire) (Provides for a reversal of the standard simplex leads depicted in TR-NWT-000335 for 4-wire interfaces at Customer end of circuit.) |

| Protocol | Protocol Option | Definition |
| --- | --- | --- |
| IA | E.I.A. (25 Pin RS 232) Note: The “IA” Protocol code is not available in Midwest or West region and not available in any region for new services. This code is no longer offered by AT&T. |
|  |  | Can be ordered with no Protocol Option if applicable |
| Protocol | Protocol Option | Definition |
| IS | 2B1Q Signaling Format - U Interface Per TR-NWT-000393, E.G., Basic Rate ISDN, Digital Subscriber Line (DSL) (Details in Tab 10) |
| Protocol | Protocol Option | Definition |
| LA | Type A Registered Port ~ Loop start loop signaling open-end (0-199 ohms range); End User PREM-PORT A. Note: The “LA” Protocol code not available in Midwest region |
|  |  | Can be ordered with no Protocol Option if applicable |
| Protocol | Protocol Option | Definition |
| LB | Type B Registered Port ~ Loop start loop signaling - open end (200-899 ohms range); End User PREM-PORT B. Note: The “LB” Protocol code not available in Midwest region |
|  |  | Can be ordered with no Protocol Option if applicable |
| Protocol | Protocol Option | Definition |
| LC | Type C Registered Port ~ Loop start loop signaling - open end (900 ohms range); End User PREM-PORT C. Note: The “LC” Protocol code not available in Midwest region |
|  |  | Can be ordered with no Protocol Option if applicable |
| Protocol | Protocol Option | Definition |
| LD | Local Area Data Channel |
|  |  | Cannot be ordered without a Protocol Option |
|  | A | Protection Unit AC Option (available only in the Southwest region) |
|  | D | Protection Unit DC Option (available only in the Southwest region) |
| Protocol | Protocol Option | Definition |
| LE | Electronic Business Set Interface, 8 KHz ASK Signaling |
|  |  | Can be ordered with no Protocol Option if applicable |

Note: The “LE” Protocol code is only available in Midwest and West regions

| Protocol | Protocol Option | Definition |
| --- | --- | --- |
| LN | Local Area/Wide Area Network (LAN/WAN) Interface |
|  |  | Cannot be ordered without a Protocol Option |
|  | 10T | Ethernet 10 Base-T |
|  | 1A | 10 Base-T Ethernet w/Auto Negotiation |
|  | 1B | 10 Base-T Ethernet w/Auto Negotiation and Flow Control |
|  | 1CA | 100 Base-T Ethernet w/Auto Negotiation |
|  | 1CB | 100 Base-T Ethernet w/Auto Negotiation and Flow Control |
|  | 1CF | 100 Base-T Ethernet w/Flow Control |
|  | 1CT | Ethernet 100 Base-T |
|  | 1F | 10 Base-T Ethernet w/Flow Control |
|  | 1GA | 1000BASE-T Ethernet w/Auto Negotiation |
|  | 1GE | Ethernet 1000 Base-T |
|  | A | Ethernet, Optical characteristics determined by provider. |
|  | A0A | 1550 nm, Single-mode Fibre (e.g., 10GBASE-ZR, 10GBASE-ZW and 1000BASE-ZX base on specific vendor implémentations) with an operating range of 80 km |
|  | A0B | 1550 nm, Single-mode Fiber (e.g., 10GBASE-ER, and 10GBASE-EW based on specific vendor implementations) with an operating range of 40 km |
|  | A02 | 1310 nm, Single-mode Fiber (e.g., 100BASE-LX10, 1000BASE-LX, 10GBASE-LR and 10GBASE-LW in IEEE 802.3) |
|  | A03 | 1550 nm, Single-mode Fiber (e.g., 10GBASE-ER and 10GBASE-EW in IEEE 802.3, and 1000BASE-ZX, 10GBASE-ZR, and 10GBASE-ZW based on specific vendor implementations) |
|  | A04 | 850 nm, 50-micron multimode Fiber (e.g., specified for 10BASE-FL, 1000BASE-SX, 10GBASE-SR and 10GBASE-SW in IEEE 802.3) |
|  | A05 | 1310 nm, 50-micron multimode Fiber (e.g., 100BASE-FX and 1000BASE-LX in IEEE 802.3) |
|  | A07 | 850 nm, 62.5 micron multimode Fiber (e.g., 10BASE-FL, 1000BASE-SX, 10GBASE-SR and 10GBASE-SW in IEEE 802.3) (Southeast region only) |
|  | A08 | 1310 nm, 62.5 micron multimode Fiber (e.g. 100BASE-FX and 1000BASE-LX in IEEE 802.3) (Southeast region only) |
|  | AA2 | 1310 nm, Single-mode Fiber (e.g., 100BASE-LX10, 1000BASE-LX, 10GBASE-LR and 10GBASE-LW in IEEE 802.3) w/Auto Negotiation |
|  | AA3 | 1550 nm, Single-mode Fiber (e.g., 10GBASE-ER and 10GBASE-EW in IEEE 802.3, and 1000BASE-ZX, 10GBASE-ZR, and 10GBASE-ZW based on specific vendor implementations) w/Auto Negotiation |
|  | AA4 | 850 nm, 50-micron multimode Fiber (e.g., specified for 10BASE-FL, 1000BASE-SX, 10GBASE-SR and 10GBASE-SW in IEEE 802.3) w/Auto Negotiation. |
|  | AA5 | 1310 nm, 50-micron multimode Fiber (e.g., 100BASE-FX and 1000BASE-LX in IEEE 802.3) w/Auto Negotiation |
| LN (cont.) | AB2 | 1310 nm, Single-mode Fiber (e.g., 100BASE-LX10, 1000BASE-LX, 10GBASE-LR and 10GBASE-LW in IEEE 802.3) w/Auto Negotiation and Flow Control |
|  | AB3 | 1550 nm, Single-mode Fiber (e.g., 10GBASE-ER and 10GBASE-EW in IEEE 802.3, and 1000BASE-ZX, 10GBASE-ZR, and 10GBASE-ZW based on specific vendor implementations) w/Auto Negotiation and Flow Control |
|  | AB4 | 850 nm, 50-micron multimode Fiber (e.g., specified for 10BASE-FL, 1000BASE-SX, 10GBASE-SR and 10GBASE-SW in IEEE 802.3) w/Auto Negotiation and Flow Control |
|  | AB5 | 1310 nm, 50-micron multimode Fiber (e.g., 100BASE-FX and 1000BASE-LX in IEEE 802.3) w/Auto Negotiation and Flow Control |
|  | AEA | 1550 nm, Single-mode Fiber (e.g., 10GBASE-ZR, 10GBASE-ZW and 1000BASE-ZX based on specific vendor implementations) with an operating range of 80 km with Provider optical loopback/monitoring device. |
|  | AEB | 1550 nm, Single-mode Fiber (e.g., 10GBASE-ER, and 10GBASE-EW based on specific vendor implementations) with an operating range of 40 km with Provider optical loopback/monitoring device. |
|  | AE2 | 1310 nm, Single-mode Fiber (e.g., 100BASE-LX10, 1000BASE-LX, 10GBASE-LR and 10GBASE-LW in IEEE 802.3) with Provider optical loopback/monitoring device. |
|  | AF2 | 1310 nm, Single-mode Fiber (e.g., 100BASE-LX10, 1000BASE-LX, 10GBASE-LR and 10GBASE-LW in IEEE 802.3) w/Flow Control |
|  | AF3 | 1550 nm, Single-mode Fiber (e.g., 10GBASE-ER and 10GBASE-EW in IEEE 802.3, and 1000BASE-ZX, 10GBASE-ZR, and 10GBASE-ZW based on specific vendor implementations) w/Flow Control |
|  | AF4 | 850 nm, 50-micron multimode Fiber (e.g., specified for 10BASE-FL, 1000BASE-SX, 10GBASE-SR and 10GBASE-SW in IEEE 802.3) w/Flow Control |
|  | AF5 | 1310 nm, 50-micron multimode Fiber (e.g., 100BASE-FX and 1000BASE-LX in IEEE 802.3) w/Flow Control |
|  | CE4 | 100GBASE-ER4, 100 Gbps PHY using 100GBASE-R encoding over four WDM lanes via two 1310 nm single-mode fibers, with reach up to at least 40 km per IEEE 802.3ba-2010. |
|  | CEL | 100GBASE-ER4, 100 Gbps PHY using 100GBASE-R encoding with 1310 nm over four WDM lanes via two single-mode fibers, with reach up to at least 40 km per IEEE 802.3ba-2010 with Provider optical loopback/monitoring device. |
|  | CL4 | 100GBASE-LR4, 100 Gbps PHY using 100GBASE-R encoding over four WDM lanes via two 1310 nm single-mode fibers, with reach up to at least 10 km per IEEE 802.3ba-2010. |
|  | CLL | 100GBASE-LR4, 100 Gbps PHY using 100GBASE-R encoding with 1310 nm over four WDM lanes via two single-mode fibers, with reach up to at least 10 km per IEEE 802.3ba-2010 with Provider optical loopback/monitoring device. |
|  | CSX | 100GBASE-SR10, 100 Gbps PHY using 100GBASE-R encoding over ten WDM lanes via 50-micron, 850 nm multimode fiber, with reach up to at least 100 m per IEEE 802.3ba-2010. |
|  | 4E4 | 40GBASE-ER4 with 1310 nm over four WDM lanes support transmission up to 40 km over single-mode fiber per IEEE 802.bg March 2011. |
| Protocol | Protocol Option | Definition |
| LN (cont.) | Local Area/Wide Area Network (LAN/WAN) Interface |
|  | 4L4 | 40GBASE-LR4, 40 Gbps PHY using 40GBASE-R encoding over four WDM lanes via a 1310 nm single-mode fiber, with reach up to at least 10 km per IEEE 802.3ba-2010 |
|  | 4LL | 100GBASE-LR4, 100 Gbps PHY using 100GBASE-R encoding with 1310 nm over four WDM lanes via two single-mode fibers, with reach up to at least 10 km per IEEE 802.3ba-2010 with Provider optical loopback/monitoring device. |
|  | X20 | 400G BASE-FR4, 400 Gbps over wavelengths of 1264.5 – 1277.5, 1284.5 – 1297.5, 1304.5 – 1317.5 or 1324.5 – 1337.5 nm with reach up to 2000m. |

| Protocol | Protocol Option | Definition |
| --- | --- | --- |
| LO | Loop Start Signaling Open-End (Switch) Function Presented by The Customer at Interface to The LEC Access Service |
|  |  | Can be ordered with no Protocol Option if applicable |
|  | X | Simplex Reversal |
| Protocol | Protocol Option | Definition |
| LR | Private Line Automatic Ring down (PLAR) With PLAR Equipment Provided by the LEC |
|  |  | Can be ordered with no Protocol Option if applicable |
|  | A | D4 PLAR Channel Unit Signaling Format |
|  | B | D3 PLAR Channel Unit Signaling Format |
| Protocol | Protocol Option | Definition |
| LS | Loop-Start Signaling-Closed End (Station) Function Presented by The Customer at The Interface to LEC Access Service |
|  |  | Can be ordered with no Protocol Option if applicable |
|  | M | CO Answering Service Concentrator |
|  | X | Simplex Reversal |

| Protocol | Protocol Option | Definition |
| --- | --- | --- |
| NO | Connects Customer to An Access Service Suitable for Voice Transmission with No Signaling Provided By LEC |
|  |  | Can be ordered with no Protocol Option if applicable |
| NO | 17P | Loop Back 1713 Hz and line power. ~ This code is only applicable when the customer orders the Improved Termination Option (ITO) with 0 dB TLPs at the Interface. (Not available in Midwest region) |
| NO | 19P | Loop Back 1913 Hz and line power. ~ This code is only applicable when the customer orders the Improved Termination Option (ITO) with 0 dB TLPs at the interface. (Not available in Midwest region) |
| NO | 24P | Loop Back 2413 Hz and line power. ~ This code is only applicable when the customer orders the Improved Termination Option (ITO) with 0 dB TLPs at the Interface. (Not available in the Midwest region) |
| NO (cont.) | 27P | Loop Back 2713 Hz and line power. ~ This code is only applicable when the customer orders the Improved Termination Option (ITO) with 0 dB TLPs at the interface. (not available in Midwest region) |
| NO | Connects Customer to An Access Service Suitable for Voice Transmission with No Signaling Provided by LEC |
| NO | G | Ground Potential Rise (GPR) protection (used for High Voltage Protection) |
| NO | S | Sealing Current Option for 4W Transmission. ~ AT&T will provide sealing current generator at CO. However, it will be the responsibility of the customer to provide the equipment (829 or EQVLT) to complete the simplex path at its premises. The only exception is if the customer orders the Improved Termination Option (ITO). |
| Protocol | Protocol Option | Definition |
| OA | Optical Amplifier (functionality to be used with the DWDM Ring configuration) |
|  |  | Can be ordered with no Protocol Option if applicable |

| Protocol | Protocol Option | Definition |
| --- | --- | --- |
| OP | Optical Data Transport (IBM Redbook Services) |
|  |  | Cannot be ordered without a Protocol Option |
|  | A02 | 1310 nm, Single-mode Fiber |
|  | A04 | 850 nm, 50-micron Multimode Fiber |
|  | A05 | 1310 nm, 50-micron Multimode Fiber |

| Protocol | Protocol Option | Definition |
| --- | --- | --- |
| OT | Optical Transport Network (OTN) Optical Interface |
|  | 102 | OTU1 with 1310 nm IR1 supports transmission up to 20 km over single-mode fiber per ITU-T G.959.1 / G.709. |
|  | 103 | OTU1 with 1550 nm LR2 supports transmission up to 80 km over single-mode fiber per ITU-T G.959.1 / G.709. |
|  | 104 | OTU1 with 1310 nm SR1 supports transmission up to 2 km over single-mode fiber per ITU-T G.959.1 / G.709 |
|  | 1L2 | OTU1 with 1310 nm, Single-mode Fiber with Provider optical loopback/monitoring device. |
|  | 1L3 | OTU1 with 1550 nm, Single-mode Fiber with Provider optical loopback/monitoring device. |
|  | 202 | OTU2 with 1310 nm SR supports transmission up to 2 km over single-mode fiber per ITU-T G.959.1 / G.709 |
|  | 203 | OTU2 with 1550 nm IR2 supports transmission up to 40 km over single-mode fiber per ITU-T G.959.1 / G.709 |
|  | 204 | OTU2 with 1550 nm LR2 supports transmission up to 80 km over single-mode fiber per ITU-T G.959.1 / G.709 |
|  | 2E2 | OTU2e with 1310 nm SR-1 supports transmission up to 2 km over single-mode fiber per ITU-T G.959.1 / G.709. |
|  | 2E3 | OTU2e with 1550 nm IR2 supports transmission up to 40 km over single-mode fiber per ITU-T G.959.1 / G.709. |
| OT (cont.) | 2E4 | OTU2e with 1550 nm LR2 supports transmission up to 80 km over single-mode fiber per ITU-T G.959.1 / G.709. |
|  | 2L3 | OTU2 with 1550 nm IR2 supports transmission up to 40 km over single-mode fiber per ITU-T G.959.1 / G.709 with Provider optical loopback/monitoring device. |
|  | 2L4 | OTU2 with 1550 nm LR2 supports transmission up to 80 km over single-mode fiber per ITU-T G.959.1 / G.709 with Provider optical loopback/monitoring device. |
|  | 2L5 | OTU2e with 1550 nm IR2 supports transmission up to 40 km over single-mode fiber per ITU-T G.959.1 / G.709 with Provider optical loopback/monitoring. |
|  | 2L6 | OTU2e with 1550 nm LR2 supports transmission up to 80 km over single-mode fiber per ITU-T G.959.1 / G.709 with Provider optical loopback/monitoring. |
|  | 301 | OTU3 with 1550 nm, supports transmission up to 2 km over single-mode fiber per ITU-T G.959.1 / G.709 |
|  | 304 | OTU3 with 1310 nm over four WDM lanes on single-mode fiber, with reach up to at least 10 km per ITU-T G.959.1 / G.709 |
|  | 305 | OTU3 with 1310 nm over four WDM lanes on single-mode fiber, with reach up to at least 40 km per ITU-T G.959.1 / G.709 |
|  | 3L2 | OTU3 with 1310 nm over four WDM lanes on single-mode fiber, with reach up to at least 10 km per ITU-T G.959.1 / G.709 with Provider optical loopback/monitoring device. |
|  | 3L3 | OTU3 with 1310 nm over four WDM lanes on single-mode fiber, with reach up to at least 40 km per ITU-T G.959.1 / G.709 with Provider optical loopback/monitoring device. |
|  | 402 | OTU4 with 1310 nm over four WDM lanes via two single-mode fibers, with reach up to at least 10 km per ITU-T G.959.1 / G.709 |
|  | 403 | OTU4 with 1310 nm over four WDM lanes via two single-mode fibers, with reach up to at least 40 km per ITU-T G.959.1 / G.709 |
|  | 4L2 | OTU4 with 1310 nm over four WDM lanes via two single-mode fibers, with reach up to at least 10 km per ITU-T G.959.1 / G.709 with Provider optical loopback/monitoring device. |
|  | 4L3 | OTU4 with 1310 nm over four WDM lanes via two single-mode fibers, with reach up to at least 40 km with Provider optical loopback/monitoring device. |
| Protocol | Protocol Option | Definition |
| PC | Program Audio Circuit Equipped with a Commentator Channel in the Reverse Direction |
|  |  | Cannot be ordered without a Protocol Option |
|  | 1 | 15 kHz |
|  | 3 | 3.5 kHz |
|  | 8 | Program Audio Circuit Equipped with A Commentator Channel in The Reverse Direction |

| Protocol | Protocol Option | Definition |
| --- | --- | --- |
| PG | Program Transmission - No DC Signaling |
|  |  | Cannot be ordered without a Protocol Option |
|  | 1 | Nominal Passband from 50 to 15,000 Hz |
|  | 2 | Non-Equalized (Available only in Southeast and West regions) |
|  | 3 | Nominal Passband from 200 to 3,500 Hz |
|  | 5 | Nominal Passband from 100 to 5,000 Hz |
|  | 8 | Nominal Passband from 50 to 8,000 Hz |
| Protocol | Protocol Option | Definition |
| PR | Connects End-User Premise Protective Relaying Terminal Equipment to An Access Service Suitable for The One-Way Transmission of Control Signal |
|  |  | Can be ordered with no Protocol Option if applicable |

Note: The “PR” Protocol code not available in Midwest region

| Protocol | Protocol Option | Definition |
| --- | --- | --- |
| QA | Central Office Termination at A Multiplexer (Note: can be, but not limited to Collocation) |
|  |  | Cannot be ordered without a Protocol Option |
|  | 10 | 1/0 Mux (e.g., D4 or D5 type bank) |
|  | 30 | 3/0 Mux |
|  | 31 | 3/1 Mux |
| Protocol | Protocol Option | Definition |
| QB | Central Office Manual Cross Connect Termination with No Sub-Rating Capability for Non-Multiplexed Facilities Only. (Note: Can be, but not limited to Collocation) |
|  |  | Cannot be ordered without a Protocol Option |
|  | 00 | MDF Cross-Connect |
|  | 001 | Spectrum Management Class 1 w/unspecified cross connect cable shielding requirements. |
|  | 002 | Spectrum Management Class 2 w/unspecified cross connect cable shielding requirements. |
|  | 003 | Spectrum Management Class 3 w/unspecified cross connect cable shielding requirements. |
|  | 004 | Spectrum Management Class 4 w/unspecified cross connect cable shielding requirements. |
|  | 005 | Spectrum Management Class 5 w/unspecified cross connect cable shielding requirements. |
|  | 007 | Spectrum Management Class 7 w/unspecified cross connect cable shielding requirements. |
|  | 00A | ADSL Using Discrete Multi-Tone (DMT) format (limited to contracts where presently existing in West region only) |
|  | 00H | HDSL per iconectiv (previously known as Telcordia Technologies) TA-NWT-001210 (limited to contracts where presently existing in West region only) |
|  | 0S1 | Spectrum management Class 1 w/shielded cross connect cable (Not available in Midwest region) |
|  | 0S2 | Spectrum management Class 2 w/shielded cross connect cable (Not available in Midwest region) |
|  | 0S3 | Spectrum management Class 3 w/shielded cross connect cable (Not available in Midwest region) |
|  | 0S4 | Spectrum management Class 4 w/shielded cross connect cable (Not available in Midwest region) |
| QB (cont.) | 0S5 | Spectrum management Class 5 w/shielded cross connect cable (Not available in Midwest region) |
|  | 0S7 | Spectrum management Class 7 w/shielded cross connect cable (Not available in Midwest region) |
|  | 10T | Ethernet 10base-T |
|  | 102 | OTU1 with 1310 nm, Single-mode Fiber |
|  | 103 | OTU1 with 1550 nm, Single-mode Fiber |
|  | 104 | QB 104 OTU1 with 1310 nm SR1 supports transmission up to 2 km over single-mode fiber per ITU-T G.959.1 / G.709. |
|  | 11 | DS1 to DS1 this code may or may not meet DS1 Signal levels as specified by GR-342-CORE |
|  | 11P | DS1 to DS1 this code may or may not meet DS1 Signal levels as specified by GR-342-CORE with (NPRM) Network Performance Report Message per ANSI T1.403. |
|  | 11R | DS1 to DS1 with regeneration (available only in Midwest region) |
|  | 1A | 10 Base-T Ethernet w/Auto Negotiation |
|  | 1CA | 100 Base-T Ethernet w/Auto Negotiation |
|  | 1CB | 100 Base-T Ethernet w/Auto Negotiation and Flow Control |
|  | 1CF | 100 Base-T Ethernet w/Flow Control |
|  | 1CT | Ethernet 100 Base-T |
|  | 1F | 10 Base-T Ethernet w/Flow Control |
|  | 202 | OTU2 with 1310 nm, Single-mode Fiber |
|  | 203 | OTU2 with 1550 nm, Single-mode Fiber |
|  | 204 | OTU2 with 1550 nm LR2 supports transmission up to 80 km over single-mode fiber per ITU-T G.959.1 / G.709 |
|  | 2E2 | OTU2e with 1310 nm SR-1supports transmission up to 2 km over single-mode fiber per ITU-T G.959.1 / G.709. |
|  | 2E3 | OTU2e with 1550 nm IR2 supports transmission up to 40 km over single-mode fiber per ITU-T G.959.1 / G.709. |
|  | 2E4 | OTU2e with 1550 nm LR2 supports transmission up to 80 km over single-mode fiber per ITU-T G.959.1 / G.709. |
|  | 301 | OTU3 with 1550 nm supports transmission up to 2 km over single-mode fiber per ITU-T G.959.1 / G.709 / IEEE.802.3 |
|  | 302 | OTU3 with 1310 nm, Single-mode Fiber |
|  | 303 | OTU3 with 1550 nm, Single-mode Fiber |
|  | 304 | OTU3 with 1550 nm supports transmission up to 2 km over single-mode fiber per ITU-T G.959.1 / G.709 / IEEE.802.3 |
|  | 305 | OTU3 with 1310 nm over four WDM lanes on single-mode fiber, with reach up to at least 40 km per ITU-T G.959.1 / G.709 / IEEE 802.3bm |
|  | 33 | M2/3 Format Channelized |
|  | 402 | OTU4 with 1310 nm over four WDM lanes via two single-mode fibers, with reach up to at least 10 km per ITU-T G.959.1 / G.709 |
|  | 403 | OTU4 with 1310 nm over four WDM lanes via two single-mode fibers, with reach up to at least 40 km per ITU-T G.959.1 / G.709 |
| QB (cont.) | 4E4 | 40GBASE-ER4, supports transmission up to 40 km over 1310 nm single-mode fiber per IEEE 802.3bm |
|  | 4F4 | 40GBASE-FR with 1550 nm, supports transmission up to 2km over single-mode fiber per IEEE 802.bg March 2011. |
|  | 4L4 | 40GBASE-LR4, 40 Gbps PHY using 40GBASE-R encoding over four WDM lanes on 1310 nm single-mode fiber, with reach up to at least 10 km per IEEE 802.3ba-2010. |
|  | CE4 | 100GBASE-ER4, 100 Gbps PHY using 100GBASE-R encoding over four WDM lanes via two 1310 nm single-mode fibers, with reach up to at least 40 km per IEEE 802.3ba-2010. |
|  | CL4 | 100GBASE-LR4, 100 Gbps PHY using 100GBASE-R encoding over four WDM lanes via two 1310 nm single-mode fibers, with reach up to at least 10 km per IEEE 802.3ba-2010. |
|  | K | Ethernet, Optical characteristics determined by provider |
|  | K0A | 1550 nm, Single-mode Fiber (e.g., 10GBASE-ZR, 10GBASE-ZW and 1000BASE-ZX based on specific vendor implementations) with an operating range of 80 km. |
|  | K0B | 1550 nm, Single-mode Fiber (e.g., 10GBASE-ER, and 10GBASE-EW based on specific vendor implementations) with an operating range of 40 km. |
|  | K02 | Ethernet, 1310 nm, Single-mode Fiber (e.g., 100BASE-LX10, 1000BASE-LX, 10GBASE-LR and 10GBASE-LW in IEEE 802.3) |
|  | K03 | Ethernet, 1550 nm, Single-mode Fiber (e.g., 10GBASE-ER and 10GBASE-EW in IEEE 802.3, and 1000BASE-ZX, 10GBASE-ZR, and 10GBASE-ZW based on specific vendor implementations) |
|  | K04 | Ethernet, 850 nm, 50-micron multimode Fiber (e.g., specified for 10BASE-FL, 1000BASE-SX, 10GBASE-SR and 10GBASE-SW in IEEE 802.3) |
|  | K07 | Ethernet, 850 nm, 62.5-micron multimode Fiber (e.g., 10BASE-FL, 1000BASE-SX, 10GBASE-SR and 10GBASE-SW in IEEE 802.3) (Available only in SE Region) |
|  | K08 | Ethernet, 1310 nm, 62.5-micron multimode Fiber (e.g., 100BASE-FX and 1000BASE-LX in IEEE 802.3) (Available only in SE Region) |
|  | KA2 | Ethernet, 1310 nm, Single-mode Fiber (e.g., 100BASE-LX10, 1000BASE-LX, 10GBASE-LR and 10GBASE-LW in IEEE 802.3) w/Auto Negotiation |
|  | KB2 | Ethernet, 1310 nm, Single-mode Fiber (e.g., 100BASE-LX10, 1000BASE-LX, 10GBASE-LR and 10GBASE-LW in IEEE 802.3) w/Auto Negotiation and Flow Control |
|  | KF2 | Ethernet, 1310 nm, Single-mode Fiber (e.g., 100BASE-LX10, 1000BASE-LX, 10GBASE-LR and 10GBASE-LW in IEEE 802.3) w/Flow Control |
|  | LL | SONET/SDH Optical on a fiber distribution bay |
|  | LLX | Dark Fiber |
|  | P02 | IBM Redbook Optical, 1310 nm, Single-mode Fiber |
|  | P08 | IBM Redbook Optical, 1310 nm, 62.5-micron multimode Fiber |
|  | S1 | STS1 Cross-Connect |
|  | W02 | Wavelength Channel, 1310 nm, Single-mode Fiber (Available only in SE region) |
|  | W07 | Wavelength Channel, 850 nm, 62.5-micron Multi- mode Fiber (available only in SE region) |
|  | W08 | Wavelength Channel, 1310 nm, 62.5-micron Multi-mode Fiber (available only in SE region) |
|  | X20 | 400G BASE-FR4, 400 Gbps over wavelengths of 1264.5 – 1277.5, 1284.5 – 1297.5, 1304.5 – 1317.5 or 1324.5 – 1337.5 nm with reach up to 2000m. |

| Protocol | Protocol Option | Definition |
| --- | --- | --- |
| QC | Central Office Manual Cross Connect DS0/Voice Termination (Note: Can be, but not limited to Collocation) |
|  |  | Cannot be ordered without a Protocol Option |
|  | A | D4 PLAR Channel Unit Signaling Format (available only in West region) |
|  | B | D3 PLAR Channel Unit Signaling Format (available only in West region) |
|  | DB | Data and/or Control Supervisory Signals in VF Frequency Band. These Options can be Provided on Derived Facilities. (Available only in West region) |
|  | E1A | Type I E&M Signaling IC or End User Originates on the E-Lead (available only in West region) |
|  | E2A | Type II E&M LEAD Signaling IC or End User Originates on E-Lead (available only in West region only) |
|  | LRA | Manual Cross-Connect DS0/Voice Termination D4 PLAR Channel Unit Signal Format - with PLAR Equipment Provided by the LEC. |
|  | LRB | D3 PLAR Channel Unit Signal Format with PLAR Equipment Provided by the LEC. |
|  | M1A | Type I E&M Lead Signaling IC or End User Originates on M-Lead (available only in West region) |
|  | M2A | Type II E&M Lead Signaling IC or End User Originates on the M-Lead (Available only in the West region) |
|  | OOB | GS Loop Signaling Open End |
|  | OOC | GS Loop Signaling Closed End |
|  | OOD | LS Loop Signaling Open End |
|  | OOE | LS Loop Signaling Closed End |
|  | OOF | Transmission Only, No Signaling |
|  | OOJ | 2.4 KB/S Digital Service, DS0A Level |
|  | OOK | 4.8 KB/S Digital Service, DS0A Level |
|  | OOL | 9.6 KB/S Digital Service, DS0A Level |
|  | OOM | 19.2 KB/S Digital Service, DS0A Level |
|  | OOP | 56.0 KB/S Digital Service, DS0A Level |
|  | OOQ | 64.0 KB/S Digital Service, DS0A Level |
|  | OOR | Electronic Business Set (Available in Midwest region only) |
|  | OOS | Basic Rate ISDN (Digital Subscriber Line -DSL), LT function presented to Service Provider |
|  | RVO | Reverse Battery Originating: Loop Closure Provided by the Access Customer (AC) to the Access Provider (AP); Battery provided by AP to AC. |
|  | RVT | Reverse Battery Terminating: Loop Closure Provided by the Access Provider (AP) to the Access Customer (AC); Battery Provided by AC to AP. |
|  | TT2 | 20.0 MA |

| Protocol | Protocol Option | Definition |
| --- | --- | --- |
| QD | Field Location Manual Cross Connect DS0/Voice Termination [Outside Plant Cross Connect Location] |
|  |  | Cannot be ordered without a Protocol Option |
|  | OOB | Ground Start Loop Signaling Open End |
|  | OOC | Ground Start Loop Signaling Closed End |
|  | OOD | Loop Start Loop Signaling Open End |
|  | OOE | Loop Start Loop Signaling Closed End |
|  | OOF | Transmission Only, No Signaling |
|  | OOS | Basic Rate ISDN |
|  | RVO | Reverse Battery: Loop Closure provided by Customer |
|  | RVT | Reverse Battery: Loop Closure Provided by Service Provider |

| Protocol | Protocol Option | Definition |
| --- | --- | --- |
| QE | Field Location Manual Cross Connect Termination with No Sub-Rating Capability [Outside Plant Cross Connect location] |
|  |  | Cannot be ordered without a Protocol Option |
|  | 001 | Spectrum Management class 1 |
|  | 002 | Spectrum Management class 2 |
|  | 003 | Spectrum Management class 3 |
|  | 004 | Spectrum Management class 4 |
|  | 005 | Spectrum Management class 5 |
|  | 007 | Spectrum Management class 7 |
|  | 11 | DS1 to DS1 this code may or may not meet DS1 signal levels as specified by GR-342-CORE |
|  | 33 | DS3 to DS3 this code may or may not meet DS3 signal levels as specified by GR-342-CORE |
|  | LL | Fiber Cross Connect (available only in Midwest region) |
|  | X | Dark Fiber |

| Protocol | Protocol Option | Definition |
| --- | --- | --- |
| QR | Line Sharing/Splitting, Customer provides the non-CO-based splitter function. This NCI represents two points o termination. |
|  |  | Cannot be ordered without a Protocol Option |
|  | L05 | Loop Start Signaling + Spectrum Management Class 5 (available only in Southeast region) |

| Protocol | Protocol Option | Definition |
| --- | --- | --- |
| QS | Line Sharing/Splitting, Customer Provides the Co-Based Splitter Function. This NCI Represents Two Points of Termination. |
|  |  | Cannot be ordered without a Protocol Option |
|  | L05 | Loop Start Signaling + Spectrum Management Class 5. (Available only in Southwest region) |
|  | LS5 | Loop Start Signaling + Spectrum Management Class 5 w/shielded cross connect cable |

| Protocol | Protocol Option | Definition |
| --- | --- | --- |
| QV | Central Office Video Services for Collocation |
| See Video Services TAB 19 for these Video Protocol Codes |

| Protocol | Protocol Option | Definition |
| --- | --- | --- |
| RG | Regenerator (Stand-alone with no drops) |
|  |  | Cannot be ordered without a Protocol Option |
|  | 004 | 4 Wavelengths |
|  | 008 | 8 Wavelengths |
|  | 012 | 12 Wavelengths |
|  | 016 | 16 Wavelengths |
|  | 032 | 32 Wavelengths |
|  | A | Full System Regeneration |

| Protocol | Protocol Option | Definition |
| --- | --- | --- |
| RP | Packet Ring Termination |
|  |  | Cannot be ordered without a Protocol Option |
|  | I | 10/100 Mbps Port Speeds w/Electrical Interface |
|  | J | Rate Adjustable 1000 Mbps Ethernet w/850nm Optical Interface |

| Protocol | Protocol Option | Definition |
| --- | --- | --- |
| RV | Reverse Battery (Trunk Signaling) at Interface) |
|  |  | Cannot be ordered without a Protocol Option |
|  | O | Loop Closure Provided by IC to the LEC; Battery Provided by LEC to IC. |
|  | T | Loop Closure Provided by LEC to End User; Battery Provided by End User to LEC. |

| Protocol | Protocol Option | Definition |
| --- | --- | --- |
| SF | Provides Supervisory Signaling by Use of Single Frequency (2600 Hz) Tone On-Off Conditions (Not available after 3-31-95) |
|  |  | Can be ordered with no Protocol Option if applicable |
|  | EA | Single Frequency Signaling to E&M Signaling (Not available in West region) |
|  | GO | Single Frequency Signaling to Ground-Start Loop Signaling, Open End |
|  | GS | Single Frequency Signaling to Ground-Start Loop Signaling, Closed End |
| Protocol | Protocol Option | Definition |
| SF (cont.) | Provides Supervisory Signaling by Use of Single Frequency (2600 Hz) Tone On-Off Conditions (Not available after 3-31-95) |
|  | LO | Single Frequency Signaling to Loop-Start Loop Signaling, Open End |
|  | LS | Single Frequency Signaling to Loop-Start Loop Signaling, Closed End |
| Protocol | Protocol Option | Definition |
| SM | SONET Multiplexer supporting drops of OC3/STS-3C, STS-1/DS3, and VT1.5/DS1 |
| SN | SONET Multiplexer supporting drops of OC12/STS-12C, OC3/STS-3C, and STS-1/DS3 |
| SO | SONET /SDH Optical Interface |
| SP | SONET Multiplexer supporting drops of OC48, OC12/STS-12C, and OC3/STS-3C |
| SS | SONET Next Generation Multiplexer (Drop Options/Multiplexer Capability identified in Protocol options. It does not imply drop card placement or wired configurations) |
| See SONET TAB 15 for these SONET Protocol Codes |
| ST | Synchronous Transmission Signal (STS). This is an electrical interface. |
|  |  | Cannot be ordered without a Protocol Option |
|  | 12 | STS-12 |
|  | A | STS-1 |
|  | B | STS-3 |
|  | C | STS-3C |
| Protocol | Protocol Option | Definition |
| TA | Central Office Transfer Arrangement |
|  |  | Cannot be ordered without a Protocol Option |
|  | C | Common |
|  | NC | Normally Closed |

Note: TA Protocol code and associated Protocol Options available only in the West region.

| Protocol | Protocol Option | Definition |
| --- | --- | --- |
| TD | Component Digital Video |
|  |  | Cannot be ordered without a Protocol Option |
| TE | Component Digital Video – Compressed |
|  |  | Cannot be ordered without a Protocol Option |
| TG | Flexible Video Interface, Auto-Sensing port accommodates several video interfaces Types as designated in the protocol options. (The customer my change video type without notifying the provider). |
|  |  | Cannot be ordered without a Protocol Option |
| TH | Digital Video Broadcast-Asynchronous Serial Interface (DVB-ASI) For Single or Multiple Mpeg2 Transport Signals and Embedded Related Digital Audio Signals. |
|  |  | Can be ordered with no Protocol Option if applicable |
| TR | Video, Flexible Rate |
|  |  | Cannot be ordered without a Protocol Option |
| See Video Services TAB 19 for these Video Protocol Codes |

| Protocol | Protocol Option | Definition |
| --- | --- | --- |
| TT | Telegraph/Teletypewriter Interface |
|  |  | Cannot be ordered without a Protocol Option |
|  | 2 | 20.0 Milli-amperes |
|  | 3 | 3.0 Milli-amperes (Available only to existing customers) |
|  | 6 | 62.5 Milli-amperes |

| Protocol | Protocol Option | Definition |
| --- | --- | --- |
| TV | Television Interface |
|  |  | Cannot be ordered without a Protocol Option |
| See Video Services TAB 19 for these Video Protocol Codes |

| Protocol | Protocol Option | Definition |
| --- | --- | --- |
| VL | Ethernet Virtual Connection (EVC) Termination (EVC/UNI/NNI Map Type) |
|  |  | Cannot be ordered without a Protocol Option |
|  | A2 | PORT MAP WITH ALL TO ONE BUNDLE (This EVC accepts ALL frames ingressing the UNI/NNI, No service multiplexing) |
|  | UNT | PORT + UNTAGGED FRAMES MAP (This EVC maps to all untagged frames on a UNI/NNI) |
|  | V | PORT + VLAN MAP (This EVC accepts only tagged frames with a specific CEVLAN ID) |
|  | VST | PORT + S-VLAN MAP. (This OVC accepts only tagged frames with a specific S-VLAN ID within an S-Tag per MEF 26. The S-Tag may be stacked on a C-Tag (see 802.1ad for info on tag stacking) or it may be the sole tag on the frames at the ENNI.) |

| Protocol | Protocol Option | Definition |
| --- | --- | --- |
| WA | Wideband Bandwidth Interface at End User Premises |
|  |  | Cannot be ordered without a Protocol Option |
|  | 1 | Nominal Pass Band from 10 Hz to 20,000 Hz (Limited Bandwidth) (Not available in West region) |
|  | 2 | Nominal Pass Band from 29,000 to 44,000 Hz (Not available in West region) |
|  | 7 | 50-750 MHz Nominal Pass Band (Not available in West region) |
|  | 8 | 824 to 894 MHz Pass Band (Offered in AT&T Illinois only- Future offering in other AT&T locations ~verify availability) |
|  | 19 | 1900 MHz (Offered in AT&T Illinois only- Future offering in other AT&T locations ~verify availability) |

| Protocol | Protocol Option | Definition |
| --- | --- | --- |
| WB | Wideband Data Interface at IC Terminal Location |
|  |  | Cannot be ordered without a Protocol Option |
|  | 40S | 40.8 Kbps, Synchronous |
|  | 50A | UP to 50.0 Kbps, Asynchronous |
|  | 50S | 50.0 Kbps, Synchronous |

| Protocol | Protocol Option | Definition |
| --- | --- | --- |
| WC | Wideband Data Interface at End User Premises |
|  |  | Cannot be ordered without a Protocol Option |
|  | 40 | 40.8 Kbps, Synchronous |
|  | 50 | For 12 Wire Interface: 50.0 Kbps, Synchronous; for 10 Wire Interface up to 50.0 Kbps Asynchronous |

| Protocol | Protocol Option | Definition |
| --- | --- | --- |
| WL | Transparent Wavelength Channel |
|  |  | Cannot be ordered without a Protocol Option |
|  | A02 | 1310 nm, Single-mode Fiber |
|  | A03 | 1550 nm, Single-mode Fiber |
|  | A07 | 850 nm, 62.5-micron Multimode Fiber |
|  | A08 | 1310 nm, 62.5-micron Multimode Fiber |
|  | TA | 1471 nm Transmit / 1491 nm Receive CWDM Single-mode Fiber |
|  | TB | 1491 nm Transmit / 1471 nm Receive CWDM Single-mode Fiber |
|  | TC | 1511 nm Transmit / 1531 nm Receive CWDM Single-mode Fiber |
|  | TD | 1531 nm Transmit / 1511 nm Receive CWDM Single-mode Fiber |
|  | TE | 1551 nm Transmit / 1571 nm Receive CWDM Single-mode Fiber |
|  | TF | 1571 nm Transmit / 1551 nm Receive CWDM Single-mode Fiber |
|  | TG | 1591 nm Transmit / 1611 nm Receive CWDM Single-mode Fiber |
|  | TH | 1611 nm Transmit / 1591 nm Receive CWDM Single-mode Fiber |

| Protocol | Protocol Option | Definition |
| --- | --- | --- |
| WV | Video Interface |
|  |  | Cannot be ordered without a Protocol Option |
| See Video Services TAB 19 for these Video Protocol Codes |

Section 4 ~ NCI Transmission Level Point Code

(Previously found in TAB 7)

The Network Channel Interface Code is comprised of a ten-character and two delimiter field which describes the NCI at the End User and the Customer POT.  The eleventh- and twelfth-character position represent transmit and receive levels at the POT(s).  Below are directionality definitions for character positions 11 and 12:

This TAB is provided to show what values may be used or seen in the eleventh and twelfth positions of the NCI code.  Unlike the other TABs in the CCG, these items are not always “orderable” by the customer.  This information, when appropriate, will be provided back to the customer in the form of the NCI code.  Only certain products can specify the TLPs.  (i.e., On DS0 level products, TLPs may be specified if they do not conflict with other design standards, like FGA, B, C, and D, which only allows for a digital level of "0" on Tandem Access trunks and not on End Office trunks (3 or 6 dB).  DS1 and DS3 product interface levels have industry standards and FCC/ACTA rules that override the Carrier Coding Guides due to technical issues associated with the T1 Span engineering guidelines (T1.403) and design standards.)

The required POT levels at the Customer and End User locations will be determined based on its needs and on the range of levels available with each channel offering as documented in the Technical References.  A default level is specified in the Technical References for each direction at a customer and/or End User POT.  AT&T   will provide the nominal default level as long as additional equipment is not required solely to provide the default level.

NCI Position 11 - The coded alpha value defines the signal level when transmitting from AT&T   to the Customer or End User, which equates to the signal level received at the Customer or End User interface.

NCI Position 12 - The coded alpha value defines the signal level when Transmitting from the Customer or End User to AT&T, which equates to the signal level received at AT&T’s interface.

EXAMPLE:	1	2	3	4	5	6	7	8	9	10	11	12

NCI -	0	4	S	F	2	.				.	A	Z

Character Positions 1 and 2 = Number of wires

Character Positions 3 and 4 = Protocol

Character Position 5 = Customer or EU Impedance

Character Position 6 = Delimiter

Character Positions 7, 8 and 9 = Protocol Options

Character Position 10 = Delimiter (.)

Character Position 11 = Transmission Level (-16.0) from AT&T to the Customer Interface

Character Position 12 = Transmission Level (+7.0) from the Customer at the Interface.

In the example above the transmission levels are shown in character positions 11 and 12 respectively.  However, since Protocol Options are not applicable for the above Protocol Code, instead of leaving character positions 7, 8, and 9 as blank. The above example could have also been described as:

EXAMPLE:	1	2	3	4	5	6	7	8	9	10	11	12

NCI -	0	4	S	F	2	.	.	A	Z

The key to describing the channel interface at the Customer or End User POT is the placement of delimiter(s) and the requirements of character positions 6 through 12.  Character position 1 through 5 are fixed positions which must always be populated with the proper alpha/numeric characters.  However, as depicted in the examples following, character positions 6 through 12 are made flexible by using a delimiter(s) or leaving the fields blank.

Examples:

NCI Example	1.	0	6	E	A	2	.	M			.	A	Z

ASR Field		1	2	3	4	5	6	7	8	9	10	11	12

NCI Example	2.	0	6	E	A	2	.	M	.	A	Z

ASR Field		1	2	3	4	5	6	7	8	9	10	11	12

Examples 1 and 2 above depict two methods of identifying the same interface.

NCI Example	3.	0	6	E	A	2	.	M

ASR Field		1	2	3	4	5	6	7	8	9	10	11	12

Example 3 	depicts the NCI and CI options with no transmission levels specified.

NCI Example	4.	0	4	S	F	2

ASR Field		1	2	3	4	5	6	7	8	9	10	11	12

Example 4 depicts an SF interface without NCI options or transmission levels specified.

NCI Example	5.	0	4	S	F	2	.				.	A	Z

ASR Field		1	2	3	4	5	6	7	8	9	10	11	12

NCI Example	6.	0	4	S	F	2	.	.	A	Z

ASR Field		1	2	3	4	5	6	7	8	9	10	11	12

Examples 5 and 6 depicts two acceptable methods of requesting SF signaling and specifying

Transmission levels.  Protocol options are not applicable for SF interfaces.  If a particular level or levels is desired, and no code is provided in the code table, the letter "I" is placed in character position 11 and/or 12 (or equivalent when delimiters are used) and the required level(s) is specified in the twelve-character TLV field of the ASR.

Below are directionality definitions for the TLV field:

TLV Positions 1-6 - The numeric transmission level value, including + or - sign, for the signal level when transmitting from AT&T to the Customer or End User, which equates to the signal level Received by the Customer or End User when the level value is not to be encoded in Position 11 (or equivalent) of the NCI Code.

In this case an "I" is required in Position 11 of the CI Code.  The SECTLV Positions 1-6 will also be used to specify the signal level arriving at AT&T’s switch.

TLV Positions 7-12 - The numeric transmission level value including + or - sign for the signal level when Transmitting from the Customer or End User to AT&T which equates to the signal level received by AT&T   the level is not to be encoded in Position 12 (or equivalent) of the NCI Code.  In this case an "I" is required in Position 12 (or equivalent) of the NCI Code.  Positions 7-12 will not be used to describe any levels at the AT&T switch.

EXAMPLE: 	1 2	3	4	5	6	7	8	9	10	 11 	12					1	2	3	4	5	6	7	8	9	10	 11	 12

NCI=	0	4	S	F	2.				I	I   			TLV=	-	0	5	.	5	T	+	0	4	.	5	R

-5.5 in TLV above equals AT&Ts transmit to Customer

+4.5 in TLV above equals AT&Ts receive from Customer

NOTE - TLV positions 4, 6, 10, and 12 are fixed on blank ASR forms.

CAUTION:  Character positions 11 and 12 or equivalent of the NCI and the TLV field levels must be compatible with Network Channel (NC) code.  Technical References reflect the directionality of transmit and receive TLPs in relationship to the Customer and the End User.  Technical References should be reviewed to assure compatibility.

CLARIFYING EXAMPLES for DIRECTIONALITY:

We are adding the attached iconectiv (previously known as Telcordia Technologies) description and examples to help clarify the appropriate directionality when assigned TLPs.

TLP	CODE

-16.0	A

-15.0	B

-14.0	C

-13.0	D

-12.0	E

-11.0	F

-10.0	G

- 9.0	H

Specify on ASR TLV Field	I

- 8.0	J

- 7.0	K

- 6.0	L

- 5.0	M

- 4.0	N

None this direction	O

- 3.0	P

- 2.0	Q

- 1.0	R

0.0	S

+ 1.0	T

+ 2.0	U

+ 3.0	V

+ 4.0	W

+ 5.0	X

+ 6.0	Y

+ 7.0	Z

Default value	- or leave field blank

EU POT							Customer POT

REC >>		XMT >>

## AT&T

XMT <<		REC <<

XMT = NCI character position eleven (or equivalent)

TLV Field character positions 1 through 6

REC = NCI character position twelve (or equivalent)

TLV Field character positions 7 through 12

# Text boxes

AT&T

TAB 3

NCI

Components