General Information

AT&T TAB 15 contains the currently permissible Network Channel (NC) and Network Channel Interface (NCI) codes; along with permissible combinations that should be used by AT&T Customers when ordering SONET offerings.  Because of the complexity of the SONET coding structure and the variations possible, TAB 15 will present the codes in a “Product-based” format, versus a technical code format usually used.  This format is a simplified way to determine the proper codes used by AT&T.  This “Product-based” format allows you to see not only the valid codes for the specific AT&T region you are currently viewing, but also the full SONET products and offerings throughout the AT&T enterprise.    See the following Notes:

- It is important to pay attention to which AT&T region you are planning to order from, and make sure the correct SONET offering / coding for that region is what is requested.

- Although most NC/NCI coding for the SONET offerings should be found in this tab, Customers should still familiarize themselves with the other CCG tabs for understanding how NC/NCIs are structured; proper CLCI/SS codes and/or SPEC codes, as appropriate.

- When determining which NCI to use, those starting with a “02” means this product does not allow protection.  The use of an NCI starting with a “04” indicates this product allows for the customer to order protection.

- For the purposes of this document, and 1Gig and GigE is considered the same interface

- There may be exceptions for Meet Point Services where the NC/NCI codes of the controlling company may conflict with what is documented in AT&T’s CCG.  When this occurs, the Industry Meet Point Services rules as outlined by the Order and Billing Forum (OBF) will take precedence and coding may be used that is not found in this document.

- For Government Services the NC/NCI codes may conflict with what is documented in AT&T’s CCG.  All Telecommunications companies can be mandated by the Federal Government to provision any service that is “Technically Feasible” even if the company does not regularly offer that product of service.  These would be done on Individual Case Basis (ICBs) which are not reflected in the AT&T CCG.  Coding provided on Governmental orders will take precedence and coding may be used that is not found in this document.

- Please familiarize yourself with the attached document which describes the NCI Application Rules for Various Configurations:

This will help with the Hierarchy of assigning/determining NCI and SECNCI coding choices.

- When the 02SOF. (*) or 04SOF. (*) NCI Codes are used, the AT&T guideline is for orders to use the Protocol Option of “X” = Provider Engineered Reach Factor unless instructed to use a different valid Protocol Option by AT&T. (02SOF.X or 04SOF.X)

| Table of Contents SONET PRODUCT / OFFERING NAME | Valid in these AT&T Regions | Page |
| --- | --- | --- |
|  | MW | SW |  | W | SE |  |
| Dedicated SONET Ring (DSR) Service | X | X |  | X | N/A | 4 |
| LightGate SONET | N/A | N/A |  | N/A | X | 10 |
| Optical Carrier Network (OCN) Point-To-Point Service | X | X |  | X | X | 12 |
| Optical to Electrical DS1s Add / Drop Capability | X | X |  | X | N/A | 21 |
| Optical to Electrical DS3s Add / Drop Capability | X | X |  | X | N/A | 23 |
| SMARTRing / SMARTRing with Hub Extension and Associated Services | N/A | N/A |  | N/A | X | 25 |
| SONET ATM services | N/A | N/A |  | N/A | X | 27 |
| SONET Dedicated Interconnection Network/SMOA with MUX | X | X |  | X | N/A | 29 |
| SONET Mapped Optical Arrangement (SMOA) | X | X |  | X | N/A | 31 |
| SONET Services associated with MON Offerings (Moved to new TAB 18) |  |
| SONET Services associated with EEL Offerings | N/A | N/A |  | X | N/A | 34 |
| SONET Services associated with Ethernet Over SONET (moved from TAB 16 Product Matrix, as this is more closely aligned with SONET) | X | X |  | X | See SMARTRing section | 36 |
| NCI “SS”, “SM”, “SN”, “SO”, and “SP” Protocol Option tables | X | X |  | X | X | 44 |
| Retired Product lines ~ not available for new services ReliaNET Self-Healing Transport Network (STN) Service SONET Ring and Access Services SONET Xpress | X | X |  | X |  | 52 |

Grandfathered Note for the following SONET services:

SMARTRing (OC3, OC12, O48 and OC192) a.k.a BellSouth SPA Dedicated Ring

DSRS a.k.a. OC-n Dedicated Ring, OC-3, OC-12, OC-48, OC-192 SONET Ring Service, OC192 Dedicated SONET ring Service

All will be grandfathered as of 12/1/2021 with the following terms and conditions:

Effective December 1, 2021, pending regulatory approval (where required) Service offered under the AT&T Interstate Access Guidebook and the applicable state tariffs or guidebooks will no longer be available to new customers (not current contract or service) in the states of XX, YY and ZZ.  As a current AT&T customer, you may retain your existing service(s) subject to the following changes in service:

- Effective December 1, 2021, Moves, Additions, and Change orders will no longer be accepted with the following exceptions.

  - Existing customers will be permitted to modify their existing service and will be able to add new circuits to their existing service but will not be permitted to add new nodes in any locations. Any such new circuits will be subject to and coterminous with the customer’s existing term payment plan or term agreement for the service to which they are added.

  - Neither Upgrades nor Downgrades will be permitted.

  - AT&T will be introducing a new 12-month term plan on 12/1/21. Customers with expiring contracts may enter a 12-month term plan or continue to purchase service on a month-to-month basis.

- Effective November 30, 2023, unless specified to the contrary in their existing service agreements, existing customers may not renew Term Payment Plans or term agreements.  No Move, Add or Change orders of any type will be accepted. Following the expiration of existing term payment plans or term agreements, AT&T will provide this service on a month-to-month basis until the service is discontinued. During any month-to-month service period, AT&T may change the rates, terms, and conditions of the service upon required notification.

AT&T

Product/Offering

Title Page

For

DEDICATED SONET RING (DSR) Services

Product/Offering ~ 	DEDICATED SONET RING (DSR) Services

### AT&T Midwest, Southwest & West Regions

| Network Channel | Definitions |
| --- | --- |
| JI-- | SONET Electrical STS-1, 51.84 Mbps |
| OBUE ^ | Digital High Capacity, SONET - OC3 (155.520 Mbps) ~ Uni-Directional Ring with Multiplexer at both ends |
| ODUE ^ | Digital High Capacity, SONET - OC12, 622.080 Mbps ~ Uni-Directional Ring with Multiplexer at both ends |
| OFUE ^ | Digital High Capacity, SONET – OC48, 2488.320 Mbps ~ Uni-Directional Ring with Multiplexer at both ends |
| OFVE ^ | Digital High Capacity, SONET – OC48, 2488.320 Mbps ~ Bi-Directional Ring with Multiplexer at both ends |
| OGUE ^ | Digital High Capacity, SONET, OC192, 9953.280 Mbps ~ Uni-Directional Ring with Multiplexer at both ends |
| OGVE ^ | Digital High Capacity, SONET, OC192, 9953.280 Mbps ~ Bi-Directional Ring with Multiplexer at both ends |

Notes:

- ^ = These codes indicate AT&T does not offer Customer provided Multiplexers.  The only valid configuration is with a multiplexer at both ends.

- AT&T West region has two SONET Ring Products; Dedicated SONET Ring Service (DSRS) or AT&T West Region SONET Ring and Access Service (SRAS).    This Section is only speaking to DSRS.

- For Port-to-Port configurations see OCN Pt-to-Pt Matrix (using OB--, OB-R, OD--, OD-R, OF--, OF-R, OG- -, or OG-R).

Product/Offering ~ 	DEDICATED SONET RING (DSR) Services (Cont’d)

### AT&T   Midwest, Southwest & West Regions

| SONET STS1, OC3, OC12, OC48 and OC192 |
| --- |
| NC Code | Location | NCI | SEC NCI |
| JI- - | AC - AC or AC - EU | 04ST6.A | 04ST6.A |
| OBUE | AC-AC, AC-EU, EU-EU | 02SSF. +++, 02SMF. * | 02SSF. +++, 02SMF. * |
| OBUE | AC-CO | 02SSF. +++, 02SMF. * | 02SSF. +++, 02SMF. *, 02RGF. * |
| OBUE | CO-CO | 02SSF. +++, 02SMF. *, 02RGF. * | 02SSF. +++, 02SMF. *, 02RGF. * |
| OBUE | CO-EU | 02SSF. +++, 02SMF. *, 02RGF. * | 02SSF. +++, 02SMF. * |
| OBUE | ARC connections | 02CMF.C3 | 02SSF. +++, 02RGF. * |
| ODUE | AC-AC, AC-EU, EU-EU | 02SSF. +++, 02SMF. *, 02SNF. * | 02SSF. +++, 02SMF. *, 02SNF. * |
| ODUE | AC-CO | 02SSF. +++, 02SMF. *, 02SNF. * | 02SSF. +++, 02SMF. *, 02SNF. *, 02RGF. * |
| ODUE | CO-CO | 02SSF. +++,02SMF. *,02SNF. *, 02RGF. * | 02SSF. +++, 02SMF. *, 02SNF. *, 02RGF. * |
| ODUE | CO-EU | 02SSF. +++, 02SMF. *,02SNF. *, 02RGF. * | 02SSF. +++, 02SMF. *, 02SNF. * |
| ODUE | ARC connections | 02CMF.C12 | 02SSF. +++, 02RGF. * |
| OFUE | ARC connections | 02CMF.C48 | 02SSF. +++, 02RGF. * |
| OFUE, OFVE | AC-AC, AC-EU, EU-EU | 02SSF. +++, 02SNF. *, 02SPF. * | 02SSF. +++, 02SNF. *, 02SPF. * |
| OFUE, OFVE | AC-CO | 02SSF. +++, 02SNF. *, 02SPF. * | 02SSF. +++, 02SNF. *, 02SPF. *, 02RGF. * |
| OFUE, OFVE | CO-CO | 02SSF. +++, 02SNF. *, 02SPF. *, 02RGF. * | 02SSF. +++, 02SNF. *, 02SPF. *, 02RGF. * |
| OFUE, OFVE | CO-EU | 02SSF. +++, 02SNF. *,02SPF. *, 02RGF. * | 02SSF. +++, 02SNF. *, 02SPF. * |
| OGUE, OGVE | AC-AC, AC-EU, EU-EU | 02SSF. +++, 02SPF. * | 02SSF. +++, 02SPF. * |
| OGUE, OGVE | AC-CO | 02SSF. +++, 02SPF. * | 02SSF. +++, 02SPF. *, 02RGF. * |
| OGUE, OGVE | CO-CO | 02SSF. +++, 02SPF. *, 02RGF. * | 02SSF. +++, 02SPF. *, 02RGF. * |
| OGUE, OGVE | CO-EU | 02SSF. +++, 02SPF. *, 02RGF. * | 02SSF. +++, 02SPF. * |

Notes:  See Next page

NOTES:

- AC= Access Customer (POP), CO= Central Office, EU= End User

- This product does not allow for protection.  All NCI/SECNCI codes will start with a “02”” except for the 04ST6.A electrical handoff.

- “RG” which is used for a Regenerator is used only at a Central Office location and is treated like a “Muxing” code.

- For the 02SSF. +++ NCI codes, the “*” indicates any valid Muxing configs per Protocol tables towards the end of this document in the SONET Table portion before the Retired portion.

- The 02SMF. *, 02SNF. *, and 02SPF. * NCI codes can only be used on existing rings.  Any new rings as of 03/18/06 should use the “02SSF. +++” or “02RGF. *” NCI codes.  The “*” indicates any valid Muxing configs per Protocol tables at the end of this document or in TAB 3 for the 02RGF. * NCI code

- “SQ” is a new NCI Protocol code associated with the OC192 service at the National level.  AT&T does not offer the “SQ” currently.  The “SP” is used if you are muxing down to these levels~ supporting drops of OC48, OC-12/STS-12C, and OC3/STS-3C only.  The “SQ” code would be used if you are muxing down to the full lower levels ~ supporting drops of OC48, OC-12/STS-12C, OC3/STS-3C and STS-1/DS3.  AT&T does not offer Direct STS-1/DS3 drops from our OC192 Platform services.

- Based on the orientation of the service being ordered the location configuration could be reversed (e.g., CO-EU could also be EU-CO).

- All the above coding combinations for DSRS may be applicable when the CLFI (facilities) connecting DSRS nodes are assigned CFA(s) (wavelength (s)) of a MON Ring network.  See TAB 18 for the MON Ring and Riding Services coding.

Product/Offering ~ 	DEDICATED SONET RING (DSR) Services (Con’t)

AT&T

Product/Offering

Title Page

For

LightGate SONET

AT&T Southeast region only

LightGate SONET and Riding Services

This section provides COMMON LANGUAGE® (CL) coding matrixes for the LightGate SONET and the various services offered which ride LightGate SONET (for Southeast region only) see below.

These codes are still represented in the other Carrier Coding Guide (CCG) TABs.

This section captures the LightGate SONET, SMARTRing and SONET ATM services with a convenient matrix to guide coding decisions.

This section captures Ethernet over SONET associated with LightGate with a convenient matrix to guide coding decisions.

AT&T

Product/Offering

Title Page

For

Optical Carrier Network (OCN) Point-To-Point Service

Product/Offering ~ Optical Carrier Network (OCN) Point-To-Point Service

| NC Code | Product Description | Loc Config | NCI | SEC NCI | SPEC |
| --- | --- | --- | --- | --- | --- |
| OB- - | Digital High Capacity, SONET - OC3 (155.520 Mbps) Point to Point | AC- EU EU-EU | 02SOF.X, 04SOF.X & | 02SOF.X, 04SOF.X & | OCNPNT |
| OB- - | Digital High Capacity, SONET - OC3 (155.520 Mbps) Point to Point | CO-AC | 02QBF.LL, 04QBF.LL | 02SOF.X, 04SOF.X & | OCNPNT |
| OB- - | Digital High Capacity, SONET - OC3 (155.520 Mbps) Point to Point | CO-CO | 02QBF.LL, 04QBF.LL | 02QBF.LL, 04QBF.LL | OCNPNT |
| OB- - | Digital High Capacity, SONET - OC3 (155.520 Mbps) Point to Point | CO-EU | 02QBF.LL, 04QBF.LL | 02SOF.X, 04SOF.X & | OCNPNT |
| OB-C | Digital High Capacity, SONET - OC3 (155.520 Mbps) Point to Point ~ CO Mux | AC-CO EU-CO | 02SOF.X, 04SOF.X & | 02SSF. +++, 04SSF. +++ 02SMF. *, 04SMF. * | OCNPNT |
| OB-C | Digital High Capacity, SONET - OC3 (155.520 Mbps) Point to Point ~ CO Mux | CO-CO | 02QBF.LL, 04QBF.LL | 02SSF. +++, 04SSF. +++ 02SMF. *, 04SMF. * | OCNPNT |
| OB-P | SONET, OC3, 155.520 Mbps, Point-to-Point, Optical Termination on a Switch ~ Aggregator - (ATM, Frame Relay, etc.) With NNI Protocol (requires STS concatenation). | AC-CO | 02SOF.X | 02CXF.A | OCNPNT |
|  |  | CO-CO | 02QBF.LL | 02CXF.A | OCNPNT |
| OB-R | Digital High Capacity, SONET - OC3 (155.520 Mbps) Point to Point ~ STS3C Payload (Concatenated Signal) | AC-EU EU-EU | 02SOF.X, 04SOF.X & | 02SOF.X, 04SOF.X & | CONCATN |
| OB-R | Digital High Capacity, SONET - OC3 (155.520 Mbps) Point to Point ~ STS3C Payload (Concatenated Signal) | AC-CO | 02SOF.X, 04SOF.X & | 02QBF.LL, 04QBF.LL | CONCATN |
| OB-R | Digital High Capacity, SONET - OC3 (155.520 Mbps) Point to Point ~ STS3C Payload (Concatenated Signal) | CO-CO | 02QBF.LL | 02QBF.LL | CONCATN |
|  |  |  | 04QBF.LL | 04QBF.LL | CONCATN |
| OB-R | Digital High Capacity, SONET - OC3 (155.520 Mbps) Point to Point ~ STS3C Payload (Concatenated Signal) | CO-EU | 02QBF.LL, 04QBF.LL | 02SOF.X, 04SOF.X & | CONCATN |

All Regions

| NC Code | Product Description | Loc Config | NCI | SEC NCI | SPEC |
| --- | --- | --- | --- | --- | --- |
| OD- - | Digital High Capacity SONET, OC12, 622.080 Mbps Point to Point | AC- EU EU-EU | 02SOF.X, 04SOF.X & | 02SOF.X, 04SOF.X & | OCNPNT |
| OD- - | Digital High Capacity SONET, OC12, 622.080 Mbps Point to Point | CO-AC | 02QBF.LL, 04QBF.LL | 02SOF.X, 04SOF.X & | OCNPNT |
| OD- - | Digital High Capacity SONET, OC12, 622.080 Mbps Point to Point | CO-CO | 02QBF.LL, 04QBF.LL | 02QBF.LL, 04QBF.LL | OCNPNT |
| OD- - | Digital High Capacity SONET, OC12, 622.080 Mbps Point to Point | CO-EU | 02QBF.LL, 04QBF.LL | 02SOF.X, 04SOF.X & | OCNPNT |
| OD-2 | Digital High Capacity SONET, OC12, 622.080 Mbps Point to Point ~ Custom Mapped STS Facility (Facility defaults to individual STS-1 assignments but allows for customer-designated concatenation of sub-rate payloads via subsequent orders, i.e., up to four STS-3cs) | AC- EU EU-EU | 02SOF.X, 04SOF.X & | 02SOF.X, 04SOF.X & | OCNPNT |
| OD-2 | Digital High Capacity SONET, OC12, 622.080 Mbps Point to Point ~ Custom Mapped STS Facility (Facility defaults to individual STS-1 assignments but allows for customer-designated concatenation of sub-rate payloads via subsequent orders, i.e., up to four STS-3cs) | CO-AC | 02QBF.LL, 04QBF.LL | 02SOF.X, 04SOF.X & | OCNPNT |
| OD-2 | Digital High Capacity SONET, OC12, 622.080 Mbps Point to Point ~ Custom Mapped STS Facility (Facility defaults to individual STS-1 assignments but allows for customer-designated concatenation of sub-rate payloads via subsequent orders, i.e., up to four STS-3cs) | CO-CO | 02QBF.LL, 04QBF.LL | 02QBF.LL, 04QBF.LL | OCNPNT |
| OD-2 | Digital High Capacity SONET, OC12, 622.080 Mbps Point to Point ~ Custom Mapped STS Facility (Facility defaults to individual STS-1 assignments but allows for customer-designated concatenation of sub-rate payloads via subsequent orders, i.e., up to four STS-3cs) | CO-EU | 02QBF.LL, 04QBF.LL | 02SOF.X, 04SOF.X & | OCNPNT |

Product/Offering ~ Optical Carrier Network (OCN) Point-To-Point Service (con’t)

Product/Offering ~ Optical Carrier Network (OCN) Point-To-Point Service (con’t)

| NC Code | Product Description | Loc Config | NCI | SEC NCI | SPEC |
| --- | --- | --- | --- | --- | --- |
| OD-C | Digital High Capacity SONET, OC12, 622.080 Mbps Point to Point ~ CO Mux | AC-CO EU-CO | 02SOF.X, 04SOF.X & | 02SSF. +++, 04SSF. +++ 02SMF. *, 04SMF. * | OCNPNT |
| OD-C | Digital High Capacity SONET, OC12, 622.080 Mbps Point to Point ~ CO Mux | CO-CO | 02QBF.LL, 04QBF.LL | 02SSF. +++, 04SSF. +++ 02SMF. *, 04SMF. * | OCNPNT |
| OD-R | Digital High Capacity SONET, OC12, 622.080 Mbps Point to Point ~ STS12C Payload (Concatenated Signal) | AC-EU EU-EU | 02SOF.X, 04SOF.X & | 02SOF.X, 04SOF.X & | CONCATN |
| OD-R | Digital High Capacity SONET, OC12, 622.080 Mbps Point to Point ~ STS12C Payload (Concatenated Signal) | AC-CO | 02SOF.X, 04SOF.X & | 02QBF.LL, 04QBF.LL | CONCATN |
| OD-R | Digital High Capacity SONET, OC12, 622.080 Mbps Point to Point ~ STS12C Payload (Concatenated Signal) | CO-CO | 02QBF.LL | 02QBF.LL | CONCATN |
|  |  |  | 04QBF.LL | 04QBF.LL | CONCATN |
| OD-R | Digital High Capacity SONET, OC12, 622.080 Mbps Point to Point ~ STS12C Payload (Concatenated Signal) | CO-EU | 02QBF.LL, 04QBF.LL | 02SOF.X, 04SOF.X & | CONCATN |

### All Regions

See Notes regarding “&” at the end of this section

Product/Offering ~ Optical Carrier Network (OCN) Point-To-Point Service (con’t)

All Regions

| NC Code | Product Description | Location Configuration | NCI | SEC NCI | SPEC |
| --- | --- | --- | --- | --- | --- |
| OF- - | Digital High Capacity, SONET OC48, 2488.320 Mbps Point to Point | AC-EU EU-EU | 02SOF.X, 04SOF.X & | 02SOF.X, 04SOF.X & | OCNPNT |
| OF- - | Digital High Capacity, SONET OC48, 2488.320 Mbps Point to Point | CO-AC | 02QBF.LL, 04QBF.LL | 02SOF.X, 04SOF.X & | OCNPNT |
| OF- - | Digital High Capacity, SONET OC48, 2488.320 Mbps Point to Point | CO-CO | 02QBF.LL, 04QBF.LL | 02QBF.LL, 04QBF.LL | OCNPNT |
| OF- - | Digital High Capacity, SONET OC48, 2488.320 Mbps Point to Point | CO-EU | 02QBF.LL, 04QBF.LL | 02SOF.X, 04SOF.X & | OCNPNT |
| OF-2 | Digital High Capacity SONET, OC48, 2488.320 Mbps Point to Point ~ Custom Mapped STS Facility (Facility defaults to individual STS-1 assignments but allows for customer-designated concatenation of sub-rate payloads, i.e., any combination of STS-3c or STS-12c) | AC- EU EU-EU | 02SOF.X, 04SOF.X & | 02SOF.X, 04SOF.X & | OCNPNT |
| OF-2 | Digital High Capacity SONET, OC48, 2488.320 Mbps Point to Point ~ Custom Mapped STS Facility (Facility defaults to individual STS-1 assignments but allows for customer-designated concatenation of sub-rate payloads, i.e., any combination of STS-3c or STS-12c) | CO-AC | 02QBF.LL, 04QBF.LL | 02SOF.X, 04SOF.X & | OCNPNT |

Product/Offering ~ Optical Carrier Network (OCN) Point-To-Point Service (con’t)

All Regions

| OF-2 | Digital High Capacity SONET, OC48, 2488.320 Mbps Point to Point ~ Custom Mapped STS Facility (Facility defaults to individual STS-1 assignments but allows for customer-designated concatenation of sub-rate payloads, i.e., any combination of STS-3c or STS-12c) | CO-CO | 02QBF.LL, 04QBF.LL | 02QBF.LL, 04QBF.LL | OCNPNT |
| --- | --- | --- | --- | --- | --- |
| OF-2 | Digital High Capacity SONET, OC48, 2488.320 Mbps Point to Point ~ Custom Mapped STS Facility (Facility defaults to individual STS-1 assignments but allows for customer-designated concatenation of sub-rate payloads, i.e., any combination of STS-3c or STS-12c) | CO-EU | 02QBF.LL, 04QBF.LL | 02SOF.X, 04SOF.X & | OCNPNT |
| OF-C | Digital High Capacity, SONET OC48, 2488.320 Mbps Point to Point ~ CO Mux | AC-CO EU-CO | 02SOF.X, 04SOF.X & | 02SSF. +++, 04SSF. +++ 02SNF. *, 04SNF. * | OCNPNT |
| OF-C | Digital High Capacity, SONET OC48, 2488.320 Mbps Point to Point ~ CO Mux | CO-CO | 02QBF.LL, 04QBF.LL | 02SSF. +++, 04SSF. +++ 02SNF. *, 04SNF. * | OCNPNT |
| OF-E | Digital High Capacity, SONET OC48, 2488.320 Mbps Pt to Pt ~ Mux both ends | AC-EU, AC-CO, EU-EU CO-EU | 02SSF. +++, 04SSF. +++ 02SNF. *, 04SNF. * | 02RGF. *, 04RGF. * | OCNMDRP, NBLREGN |
| OF-R | Digital High Capacity, SONET OC48, 2488.320 Mbps Point to Point ~ STS48C Payload (Concatenated Signal) | AC-EU EU-EU | 02SOF.X, 04SOF.X & | 02SOF.X, 04SOF.X & | CONCATN |
| OF-R | Digital High Capacity, SONET OC48, 2488.320 Mbps Point to Point ~ STS48C Payload (Concatenated Signal) | AC-CO | 02SOF.X, 04SOF.X & | 02QBF.LL, 04QBF.LL | CONCATN |
| OF-R | Digital High Capacity, SONET OC48, 2488.320 Mbps Point to Point ~ STS48C Payload (Concatenated Signal) | CO-CO | 02QBF.LL | 02QBF.LL | CONCATN |
|  |  |  | 04QBF.LL | 04QBF.LL | CONCATN |

See Notes regarding “&” at the end of this section

Product/Offering ~ Optical Carrier Network (OCN) Point-To-Point Service (con’t)

All Regions

| NC Code | Product Description | Loc Config | NCI | SEC NCI | SPEC |
| --- | --- | --- | --- | --- | --- |

| OF-R | Digital High Capacity, SONET OC48, 2488.320 Mbps Point to Point ~ STS48C Payload (Concatenated Signal) | CO-EU | 02QBF.LL, 04QBF.LL | 02SOF.X, 04SOF.X & | CONCATN |
| --- | --- | --- | --- | --- | --- |
| OG- - | Digital High Capacity SONET, OC192, 9953.280 Mbps Point to Point | AC-EU EU-EU | 02SOF.X, 04SOF.X & | 02SOF.X, 04SOF.X & | OCNPNT |
| OG- - | Digital High Capacity SONET, OC192, 9953.280 Mbps Point to Point | CO-AC | 02QBF.LL, 04QBF.LL | 02SOF.X, 04SOF.X & | OCNPNT |
| OG- - | Digital High Capacity SONET, OC192, 9953.280 Mbps Point to Point | CO-CO | 02QBF.LL, 04QBF.LL | 02QBF.LL, 04QBF.LL | OCNPNT |
| OG- - | Digital High Capacity SONET, OC192, 9953.280 Mbps Point to Point | CO-EU | 02QBF.LL, 04QBF.LL | 02SOF.X, 04SOF.X & | OCNPNT |
| OG-2 | Digital High Capacity SONET, OC192, 9953.280 Mbps Point to Point ~ Custom Mapped STS Facility (Facility defaults to individual STS-1 assignments but allows for customer-designated concatenation of sub-rate payloads, i.e., any combo of STS-3c, STS-12c, or STS-48c) | AC- EU EU-EU | 02SOF.X, 04SOF.X & | 02SOF.X, 04SOF.X & | OCNPNT |
| OG-2 | Digital High Capacity SONET, OC192, 9953.280 Mbps Point to Point ~ Custom Mapped STS Facility (Facility defaults to individual STS-1 assignments but allows for customer-designated concatenation of sub-rate payloads, i.e., any combo of STS-3c, STS-12c, or STS-48c) | CO-AC | 02QBF.LL, 04QBF.LL | 02SOF.X, 04SOF.X & | OCNPNT |
| OG-2 | Digital High Capacity SONET, OC192, 9953.280 Mbps Point to Point ~ Custom Mapped STS Facility (Facility defaults to individual STS-1 assignments but allows for customer-designated concatenation of sub-rate payloads, i.e., any combo of STS-3c, STS-12c, or STS-48c) | CO-CO | 02QBF.LL, 04QBF.LL | 02QBF.LL, 04QBF.LL | OCNPNT |

Product/Offering ~ Optical Carrier Network (OCN) Point-To-Point Service (con’t)

All Regions

| NC Code | Product Description | Loc Config | NCI | SEC NCI | SPEC |
| --- | --- | --- | --- | --- | --- |

| OG-2 | Digital High Capacity SONET, OC192, 9953.280 Mbps Point to Point ~ Custom Mapped STS Facility (Facility defaults to individual STS-1 assignments but allows for customer-designated concatenation of sub-rate payloads, i.e. any combo of STS-3c, STS-12c, or STS-48c) | CO-EU | 02QBF.LL, 04QBF.LL | 02SOF.X, 04SOF.X & | OCNPNT |
| --- | --- | --- | --- | --- | --- |
| OG-C | Digital High Capacity SONET, OC192, 9953.280 Mbps Point to Point ~ CO Mux | AC-CO | 02SOF.X, 04SOF.X & | 02SSF. +++, 04SSF. +++ 02SPF. *, 04SPF. * | OCNPNT |
| OG-C | Digital High Capacity SONET, OC192, 9953.280 Mbps Point to Point ~ CO Mux | CO-CO | 02QBF.LL, 04QBF.LL | 02SSF. +++, 04SSF. +++ 02SPF. *, 04SPF. * | OCNPNT |
| OG-E % | Digital High Capacity SONET, OC192, 9953.280 Pt to Pt ~ Mux both ends | AC-EU, AC-CO, EU-EU CO-EU | 02SSF. +++, 04SSF. +++ 02SPF. *, 04SPF. * | 02RGF. *, 04RGF. * | 192MCLF, NBLREGN |
| OG-R | Digital High Capacity, SONET OC192, 9953.280 Mbps Point to Point ~ STS192C Payload (Concatenated Signal) | AC-EU EU-EU | 02SOF.X & | 02SOF.X & | CONCATN |
| OG-R | Digital High Capacity, SONET OC192, 9953.280 Mbps Point to Point ~ STS192C Payload (Concatenated Signal) | AC-EU EU-EU | 04SOF.X & ^ | 04SOF.X & ^ | CONCATN |
| OG-R | Digital High Capacity, SONET OC192, 9953.280 Mbps Point to Point ~ STS192C Payload (Concatenated Signal) | AC-CO | 02SOF.X, 04SOF.X & | 02QBF.LL, 04QBF.LL | CONCATN |
| OG-R | Digital High Capacity SONET, OC192, 9953.280 Mbps Point to Point ~ STS192C Payload (Concatenated Signal) | CO-CO | 02QBF.LL | 02QBF.LL | CONCATN |
|  |  |  | 04QBF.LL | 04QBF.LL | CONCATN |
| OG-R | Digital High Capacity, SONET OC192, 9953.280 Mbps Point to Point ~ STS192C Payload (Concatenated Signal) | CO-EU | 02QBF.LL, 04QBF.LL | 02SOF.X, 04SOF.X & | CONCATN |

See Notes on the next page:

Product/Offering ~ Optical Carrier Network (OCN) Point-To-Point Service (con’t)

All Regions

See Note indicators from previous pages:

- & = the customer should use the “X” = Provider Engineered Reach Factor unless instructed to use a different valid Protocol Option by AT&T. Multi-Mode Setting Protocol Options are not valid with the OCN Products.

- # = this is only offered in the AT&T Midwest region.

- % = this code is only applicable if you are ordering a Stand-alone Regenerator in the CO and also showing the Muxing configurations at a CO.

- Based on the orientation of the service being ordered the location configuration could be reversed (e.g., CO-EU could also be EU-CO).   The NCI and SECNCI could be swapped based on the orientation as well.

- OCN SECNCI may use both Next Generation & Non-Next Generation codes. For the 02SMF. *, 02SNF. *, 02SPF. *, 02SSF. +++ NCI codes, the “*” indicates any valid Muxing configuration per Protocol tables towards the end of this document in the SONET Table portion before the Retired portion.

- Next Generation codes 02SSF. * & 04SSF. *; only valid if EoS MUX is requested & Telco engineering has advised to use.

- For Collocation related coding for this product line, see OCN Point-to-Point matrix.

- ^ = Protection for the OC192 Concatenated product is only offered in the AT&T Midwest and Southwest regions.

- For more serving arrangements connecting to Collocators see OCN Point-to-Point Matrix.

- See TAB 9 for full list of SPEC codes used in AT&T.

- See TAB 18 for OCN Point-to-Point coding for MON riding services.

- The Circuit ID format for the OCN products are as follows:

| Formatting | NC codes |
| --- | --- |
| CLS (Special Services) | OB--, OB-P, OB-R, OD--, OD-R, OF--, OF-R, OG--, OG-R |
| CLF (Facility) | OB-C, OD-2, OD-C, OF-2, 0F-C, OF-E, OG-2, OG-C, OG-E |

AT&T

Product/Offering

Title Page

For

Optical to Electrical

DS1s Add / Drop Capability

Product/Offering ~ Optical to Electrical DS1s Add / Drop Capability

AT&T all regions

| NC Code | Product Description | Location Configuration | NCI | SEC NCI |
| --- | --- | --- | --- | --- |
| OB-E | Digital High Capacity, SONET - OC3 (155.520 Mbps) Point to Point ~ Mux at both ends | AC-AC, EU-EU, CO -CO | 02CMF.C3 | 02SMF. *, |

Notes:

- AC= Access Customer (POP), CO= Central Office, EU= End User

- This product does not allow for 4-fiber protection.  All NCI/SECNCI codes will start with an “02”

- This is an OC3 Point –to-Point product associated with either an OC12, OC48 or OC192 Ring.

- For the 02SMF. * NCI codes, the “*” indicates any valid Muxing configuration per Protocol tables towards the end of this document in the SONET Table portion before the Retired portion.  This product limits configuration mapping to DS1s only.

Based on the orientation of the service being ordered the location configuration could be reversed.   The NCI and SECNCI could be swapped based on the orientation.

AT&T

Product/Offering

Title Page

For

Optical to Electrical

DS3s Add / Drop Capability

Product/Offering ~ Optical to Electrical DS3s Add / Drop Capability

AT&T all regions

| NC Code | Product Description | Location Configuration | NCI | SEC NCI |
| --- | --- | --- | --- | --- |
| OB-E | Digital High Capacity, SONET - OC3 (155.520 Mbps) Point to Point ~ Mux at both ends | AC-AC, EU-EU, CO -CO | 02CMF.C3 | 02SMF. * |
| OD-E | Digital High Capacity SONET, OC12, 622.080 Mbps Point to Point ~ Mux at both ends | AC-AC, EU-EU, CO -CO | 02CMF.C12 | 02SMF. * |
| OF-E | Digital High Capacity SONET, OC48, 2488.320 Mbps Point to Point ~ Mux at both ends | AC-AC, EU-EU, CO -CO | 02CMF.C48 | 02SNF. * |

Notes:

- AC= Access Customer (POP), CO= Central Office, EU= End User

- This product does not allow for 4-fiber protection.  All NCI/SECNCI codes will start with an “02”

- This is a Point-to-Point product associated with an OC192 Ring.

- For the 02SMF. *, 02SNF. * NCI codes, the “*” indicates any valid Muxing configuration Protocol tables towards the end of this document in the SONET Table portion before the Retired portion.  This product limits configuration mapping to DS3s only.

- Based on the orientation of the service being ordered the location configuration could be reversed.  The NCI and SECNCI could be swapped based on the orientation.

AT&T

Product/Offering

Title Page

For

SMARTRing ® Services

Product/Offering ~ SMARTRing ®

AT&T Southeast region only

SMARTRing SONET and associated Services

This section provides COMMON LANGUAGE® (CL) coding matrixes for the SMARTRing SONET and the various services offered or associated with SMARTRing SONET (for Southeast region only) see below.

These codes are still represented in the other Carrier Coding Guide (CCG) TABs.

This section captures the LightGate SONET, SMARTRing SONET and SONET ATM services with a convenient matrix to guide coding decisions.

This section captures Ethernet over SONET; Virtual Packet Ring; and Ethernet Access links associated with SMARTRing with a convenient matrix with multiple worksheets on the single spreadsheet to guide coding decisions.

AT&T

Product/Offering

Title Page

For

SONET ATM Services

Product/Offering ~ SONET ATM Services

AT&T Southeast region only

SONET ATM Services

This section provides Common Language® (CL) coding matrixes for the SONET ATM Services offered (for Southeast region only) see below.

These codes are still represented in the other Carrier Coding Guide (CCG) TABs.

This section captures both the LightGate SONET, SMARTRing SONET and SONET ATM Services with a convenient matrix to guide coding decisions.

AT&T

Product/Offering

Title Page

For

SONET Dedicated Interconnection Network (DIN and

SMOA with a MUX (SMUX)

Product/Offering ~ ~ SONET Dedicated Interconnection Network (DIN and SMOA with a MUX (SMUX) ~

AT&T all regions

| NC Code | Product Description | Location Configuration | NCI | SEC NCI |
| --- | --- | --- | --- | --- |
| OB-E | Digital High Capacity, SONET - OC3 (155.520 Mbps) Point to Point ~ Mux at both ends | CO-CO | 02CMF.C3 | 02CMF.C3 |
|  |  |  | 04CMF.C3 | 04CMF.C3 |
| OB-E | Digital High Capacity, SONET - OC3 (155.520 Mbps) Point to Point ~ Mux at both ends | CO-CO | 02CMF.C3 | 02SSF. +++ |
|  |  |  | 04CMF.C3 | 04SSF. +++ |
| OD-E | Digital High Capacity, SONET - OC12 (622.080 Mbps) Point to Point ~ Mux at both ends | CO-CO | 02CMF.C12 | 02CMF.C12 |
|  |  |  | 04CMF.C12 | 04CMF.C12 |
| OD-E | Digital High Capacity, SONET - OC12 (622.080 Mbps) Pt to Pt ~ Mux at both ends | CO-CO | 02CMF.C12 | 02SSF. +++ |
|  |  |  | 04CMF.C12 | 04SSF. +++ |
| OF-E | Digital High Capacity, SONET - OC48 (2488.320 Mbps) Point to Point ~ Mux at both ends | CO-CO | 02CMF.C48 | 02CMF.C48 |
|  |  |  | 04CMF.C48 | 04CMF.C48 |
| OF-E | Digital High Capacity, SONET - OC48 (2488.320 Mbps) Point to Point ~ Mux at both ends | CO-CO | 02CMF.C48 | 02SSF. +++ |
|  |  |  | 04CMF.C48 | 04SSF. +++ |

Notes:

- SMUX is only offered with similar number of conductors at each end of the service, i.e., 02-02 or 04-04.  This product is not offered with a configuration of 02-04 or 04-02.

- Orientation of the NCI and SECNCI could swap based on location orientation.

- SMUX must always be designed off a Dedicated SONET Ring node.

- SONET Next Generation Multiplexing SECNCI Protocol “SS” capable of Ethernet Add/drop.

AT&T

Product/Offering

Title Page

For

SONET Mapped Optical Arrangement (SMOA)

Product/Offering ~ SONET Mapped Optical Arrangement (SMOA)

AT&T West region

| NC Code | Product Description | Location Configuration | NCI | SEC NCI |
| --- | --- | --- | --- | --- |
| OB-C | Digital High Capacity, SONET - OC3 (155.520 Mbps) Point to Point ~ CO Mux | AC- CO EU-CO | 02SOF.X & | 02CMF.C3 |
|  |  |  | 04SOF.X & | 04CMF.C3 |
| OB-C | Digital High Capacity, SONET - OC3 (155.520 Mbps) Point to Point ~ CO Mux | CO-CO | 02QBF.LL | 02CMF.C3 |
|  |  |  | 04QBF.LL | 04CMF.C3 |
| OB-D | Digital High Capacity, SONET - OC3 (155.520 Mbps) Point to Point ~Non-CO Mux | AC- AC EU-EU | 02SOF.X & | 02CMF.C3 |
|  |  |  | 04SOF.X & | 04CMF.C3 |
| OD-C | Digital High Capacity, SONET - OC12 (622.080 Mbps) Point to Point ~ CO Mux | AC- CO EU-CO | 02SOF.X & | 02CMF.C12 |
|  |  |  | 04SOF.X & | 04CMF.C12 |
| OD-C | Digital High Capacity, SONET - OC12 (622.080 Mbps) Point to Point ~ CO Mux | CO-CO | 02QBF.LL | 02CMF.C12 |
|  |  |  | 04QBF.LL | 04CMF.C12 |
| OD-D | Digital High Capacity, SONET - OC12 (622.080 Mbps) Pt to Pt ~ Non-CO Mux | AC- AC EU-EU | 02SOF.X & | 02CMF.C12 |
|  |  |  | 04SOF.X & | 04CMF.C12 |
| OF-C | Digital High Capacity, SONET - OC48 (2488.320 Mbps) Point to Point ~ CO Mux | AC- CO EU-CO | 02SOF.X & | 02CMF.C48 |
|  |  |  | 04SOF.X & | 04CMF.C48 |
| OF-C | Digital High Capacity, SONET - OC48 (2488.320 Mbps) Point to Point ~ CO Mux | CO-CO | 02QBF.LL | 02CMF.C48 |
|  |  |  | 04QBF.LL | 04CMF.C48 |
| OF-D | Digital High Capacity, SONET - OC48 (2488.320 Mbps) Point to Point ~Non-CO Mux | AC- AC EU-EU | 02SOF.X & | 02CMF.C48 |
|  |  |  | 04SOF.X & | 04CMF.C48 |

AT&T West region (cont’d)

| NC Code | Product Description | Location Configuration | NCI | SEC NCI |
| --- | --- | --- | --- | --- |
| OG-C | Digital High Capacity, SONET – OC192 (9953.280 Mbps) Point to Point ~ CO Mux | AC- CO EU-CO | 02SOF.X & | 02CMF.C92 |
|  |  |  | 04SOF.X & | 04CMF.C92 |
| OG-C | Digital High Capacity, SONET - OC192 (9953.280 Mbps) Point to Point ~ CO Mux | CO-CO CO-CO | 02QBF.LL | 02CMF.C92 |
|  |  |  | 02QBF.LL | 02CMF.C92 |
| OG-D | Digital High Capacity, SONET - OC192 (9953.280 Mbps) Point to Point ~Non-CO Mux | AC- AC EU-EU | 02SOF.X & | 02CMF.C92 |
|  |  |  | 04SOF.X & | 04CMF.C92 |

See Notes following the SMOA section on the next page.

Product/Offering ~ SONET Mapped Optical Arrangement (SMOA)

AT&T   Midwest and Southwest regions

| NC Code | Product Description | Location Configuration | NCI | SEC NCI |
| --- | --- | --- | --- | --- |
| OB-C | Digital High Capacity, SONET - OC3 (155.520 Mbps) Point to Point ~ CO Mux | AC- CO EU-CO | 02SOF.X & | 02CMF.C3 |
|  |  |  | 04SOF.X & | 04CMF.C3 |
| OB-C | Digital High Capacity, SONET - OC3 (155.520 Mbps) Point to Point ~ CO Mux | CO-CO | 02QBF.LL | 02CMF.C3 |
|  |  |  | 04QBF.LL | 04CMF.C3 |
| OB-D | Digital High Capacity, SONET - OC3 (155.520 Mbps) Point to Point ~Non-CO Mux | AC- AC EU-EU | 02SOF.X & | 02CMF.C3 |
|  |  |  | 04SOF.X & | 04CMF.C3 |
| OD-C | Digital High Capacity, SONET - OC12 (622.080 Mbps) Point to Point ~ CO Mux | AC- CO EU-CO | 02SOF.X & | 02CMF.C12 |
|  |  |  | 04SOF.X & | 04CMF.C12 |
| OD-C | Digital High Capacity, SONET - OC12 (622.080 Mbps) Point to Point ~ CO Mux | CO-CO | 02QBF.LL | 02CMF.C12 |
|  |  |  | 04QBF.LL | 04CMF.C12 |
| OD-D | Digital High Capacity, SONET - OC12 (622.080 Mbps) Point to Point ~ Non-CO Mux | AC- AC EU-EU | 02SOF.X & | 02CMF.C12 |
|  |  |  | 04SOF.X & | 04CMF.C12 |
| OF-C | Digital High Capacity, SONET - OC48 (2488.320 Mbps) Point to Point ~ CO Mux | AC- CO EU-CO | 02SOF.X & | 02CMF.C48 |
|  |  |  | 04SOF.X & | 04CMF.C48 |
| OF-C | Digital High Capacity, SONET - OC48 (2488.320 Mbps) Point to Point ~ CO Mux | CO-CO | 02QBF.LL | 02CMF.C48 |
|  |  |  | 04QBF.LL | 04CMF.C48 |

AT&T   Midwest and Southwest regions (cont’d)

| NC Code | Product Description | Location Configuration | NCI | SEC NCI |
| --- | --- | --- | --- | --- |
| OF-D | Digital High Capacity, SONET - OC48 (2488.320 Mbps) Point to Point ~Non-CO Mux | AC- AC EU-EU | 02SOF.X & | 02CMF.C48 |
|  |  |  | 04SOF.X & | 04CMF.C48 |
| OG-C | Digital High Capacity, SONET – OC192 (9953.280 Mbps) Point to Point ~ CO Mux | AC- CO EU-CO | 02SOF.X & | 02CMF.C92 |
|  |  |  | 04SOF.X & | 04CMF.C92 |
| OG-C | Digital High Capacity, SONET - OC192 (9953.280 Mbps) Point to Point ~ CO Mux | CO-CO CO-CO | 02QBF.LL | 02CMF.C92 |
|  |  |  | 04QBF.LL | 04CMF.C92 |
| OG-D | Digital High Capacity, SONET - OC192 (9953.280 Mbps) Point to Point ~Non-CO Mux | AC- AC EU-EU | 02SOF.X & | 02CMF.C92 |
|  |  |  | 04SOF.X & | 04CMF.C92 |

Notes:

- & = the customer should use the “X” = Provider Engineered Reach Factor unless instructed to use a different valid Protocol Option by AT&T.

- SMOA is only offered with similar number of conductors at each end of the service, i.e., 02-02 or 04-04.  This product is not offered with a configuration of 02-04 or 04-02.

- Orientation of the NCI and SECNCI could swap based on location orientation.

- CO-CO configurations for SMOA require one end to be at a Collocation point.  CO-CO configurations are not offered in the AT&T Nevada portion of AT&T West region.

- The “SP” Protocol code can also be used with OC48 configurations for RING family of services if the OC48 is being handed off intact (e.g., 02SPF.B would indicate an OC48 with a single OC48 Pipe).

AT&T

Product/Offering

Title Page

For

SONET Services associated with EELs

Product/Offering ~ SONET Services associated with EELs

| NC Code | Product Description | Location Configuration | NCI | SEC NCI |
| --- | --- | --- | --- | --- |
| OB-- | Digital High Capacity, SONET - OC3 (155.520 Mbps) Point to Point | AC- AC AC-EU EU-EU | 02SOF.X | 02SOF.X |
| OB-- | Digital High Capacity, SONET - OC3 (155.520 Mbps) Point to Point | AC- CO EU-CO | 02SOF.X | 02QBF.LL |

AT&T West region

Note: The Enhanced Extended Loop (EEL) is not offered with Protection currently.

AT&T

Product/Offering

Title Page

For

SONET Services

associated with

Ethernet Over SONET (EoS)

Product Offering ~ Ethernet over SONET (EoS)

### AT&T Midwest, Southwest & West Regions         Network Channel (NC) Codes

| Network Channel | Definitions |
| --- | --- |
| KQFA | Ethernet, Rate-Adjustable 100 Mbps Ethernet ~ Full-Duplex Rate based on SONET transport STS-1, 48.382 Mbps Nominal Payload Rate (Not VCAT Capable) |
| KQFB | Fractional 100 Mbps Ethernet ~ Full-Duplex Rate based on SONET transport STS-3c, (Full Rate at 100 Mbps) (not VCAT Capable) |
| KQFC | Ethernet, Rate-Adjustable 100 Mbps Ethernet ~ Full-Duplex Rate based on SONET transport STS1-1v, 48.382 Mbps Nominal Payload Rate |
| KQFD | Ethernet, Rate-Adjustable 100 Mbps Ethernet ~ Full-Duplex Rate based on SONET transport STS1-2v, 96.768 Mbps Nominal Payload Rate |
| KQFE | Ethernet, Rate-Adjustable 100 Mbps Ethernet ~ Full-Duplex Rate based on SONET transport VT1.5-2v, 3.2 Mbps Nominal Payload Rate |
| KQFF | Ethernet, Rate-Adjustable 100 Mbps Ethernet ~ Full-Duplex Rate based on SONET transport VT1.5-4v, 6.4 Mbps Nominal Payload Rate |
| KQFG | Ethernet, Rate-Adjustable 100 Mbps Ethernet ~ Full-Duplex Rate based on SONET transport VT1.5-7v, 11.2 Mbps Nominal Payload Rate |
| KQFK | Ethernet, Rate-Adjustable 100 Mbps Ethernet ~ Full-Duplex Rate based on SONET transport VT1.5-1v, 1.6 Mbps Nominal Payload Rate |
| KQFL | Ethernet, Rate-Adjustable 100 Mbps Ethernet ~ Full-Duplex Rate based on SONET transport VT1.5-13v, 20.8 Mbps Nominal Payload Rate |
| KQFN | Ethernet, Rate-Adjustable 100 Mbps Ethernet ~ Full-Duplex Rate based on SONET transport VT1.5-3v, 4.8 Mbps |
| KQFP | Ethernet, Rate-Adjustable 100 Mbps Ethernet ~ Full-Duplex Rate based on SONET transport VT1.5-5v, 8Mbps |
| KQFQ | Ethernet, Rate-Adjustable 100 Mbps Ethernet ~ Full-Duplex Rate based on SONET transport VT1.5-6v, 9.6 Mbps |
| KQFR | Ethernet, Rate-Adjustable 100 Mbps Ethernet ~ Full-Duplex Rate based on SONET transport VT1.5 – 10V, 16 Mbps |
| KQFS | Ethernet, Rate-Adjustable 100 Mbps Ethernet ~ Full-Duplex Rate based on SONET transport VT1.5-8v, 12.8 Mbps Nominal Payload Rate |
| KRRA | Ethernet, Rate-Adjustable 1 Gbps Ethernet (Full Duplex) - Rate based on SONET transport with Hi-Order VCAT (STS-3c and STS-12c base increments) ~ STS-3c-1v, 149.76 Mbps Nominal Payload Rate |
| KRRB | Ethernet, Rate-Adjustable 1 Gbps Ethernet (Full Duplex) ~ Rate based on SONET transport with Hi-Order VCAT (STS-3c and STS-12c base increments) ~ STS-3c-2v, 299.52 Mbps Nominal Payload Rate |
| KRRC | Ethernet, Rate-Adjustable 1 Gbps Ethernet (Full Duplex) ~ Rate based on SONET transport with Hi-Order VCAT (STS-3c and STS-12c base increments) ~ STS-3c-3v, 449.28 Mbps Nominal Payload Rate |
| KRRD | Ethernet, Rate-Adjustable 1 Gbps Ethernet (Full Duplex) ~ Rate based on SONET transport with Hi-Order VCAT (STS-3c and STS-12c base increments) ~ STS-3c-4v, 599.04 Mbps Nominal Payload Rate |
| KRRG | Ethernet, Rate-Adjustable 1 Gbps Ethernet (Full Duplex) ~ Rate based on SONET transport with Hi-Order VCAT (STS-3c and STS-12c base increments) ~ STS-3c-7v, 1048.32 Mbps Nominal Payload Rate |
| KRRH | Ethernet, Rate-Adjustable 1 Gbps Ethernet (Full Duplex) ~ Rate based on SONET transport with Hi-Order VCAT (STS-3c and STS-12c base increments) ~ STS-3c-8v, 1198.08 Mbps Nominal Payload Rate |
| KRSA | Ethernet, Rate-Adjustable 1 Gbps Ethernet (Full Duplex) ~Rate based on SONET transport level ~ STS-1, 48.382 Mbps Nominal Payload Rate (Not VCAT Capable) |
| KRSB | Ethernet, Rate-Adjustable 1 Gbps Ethernet (Full Duplex) ~Rate based on SONET transport level ~ STS-1-2v, 96.768 Mbps Nominal Payload Rate |
| KRSC | Ethernet, Rate-Adjustable 1 Gbps Ethernet (Full Duplex) ~Rate based on SONET transport level. ~ STS-3c, 149.76 Mbps Nominal Payload Rate (Not VCAT Capable) |
| KRSD | Ethernet, Rate-Adjustable 1 Gbps Ethernet (Full Duplex) ~Rate based on SONET transport level. ~ STS-1-4v, 193.536 Mbps Nominal Payload Rate |
| KRSE | Ethernet, Rate-Adjustable 1 Gbps Ethernet (Full Duplex) ~Rate based on SONET transport level. ~ STS-1-5v, 241.92 Mbps Nominal Payload Rate |
| KRSF | Ethernet, Rate-Adjustable 1 Gbps Ethernet (Full Duplex) ~Rate based on SONET transport level. ~ STS-1-6v, 290.304 Mbps Nominal Payload Rate |
| KRSI | Ethernet, Rate-Adjustable 1 Gbps Ethernet (Full Duplex) ~Rate based on SONET transport level. ~ STS1-9v, 435.46 Mbps Nominal Payload Rate |
| KRSL | Ethernet, Rate-Adjustable 1 Gbps Ethernet (Full Duplex) ~Rate based on SONET transport level. ~ STS-12c, 599.04 Mbps Nominal Payload Rate (Not VCAT Capable) |
| KRSU | Ethernet, Rate-Adjustable 1 Gbps Ethernet (Full Duplex) ~Rate based on SONET transport level. ~ STS-1-21v, 1016.064 Mbps Nominal Payload Rate |
| KRSY | Ethernet, Rate-Adjustable 1 Gbps Ethernet (Full Duplex) ~Rate based on SONET transport level. ~ STS-1-1v, 48.384 Mbps Nominal Payload Rate |
| KRSZ | Ethernet, Rate-Adjustable 1 Gbps Ethernet (Full Duplex) ~Rate based on SONET transport level. ~ STS-1-3v, 145.152 Mbps Nominal Payload Rate |
| KRS0 | Ethernet, Rate-Adjustable 1 Gbps Ethernet (Full Duplex) ~Rate based on SONET transport level. ~ STS-1-12v, 580.608 Mbps Nominal Payload Rate |
| KRS2 | Ethernet, Rate-Adjustable 1 Gbps Ethernet (Full Duplex) ~Rate based on SONET transport level. ~ STS-24c, 1198.08 Mbps Nominal Payload Rate Nominal Payload Rate (24c is not addressed specifically in GR-253 but the bit rate is accurate at STS-3c x 8) (Not VCAT Capable) |

Product Offering ~ Ethernet Over SONET (EoS)

| Ethernet Rate Adjustable at 100 Mbps |
| --- |
| NC Code | Location | NCI | SEC NCI |
| KQFA, KQFB | AC or EU to AC or EU | 04LN9.1CT, 04LN9.1CA, 04LN9.1CB, 04LN9.1CF, 02SOF.X, 04SOF.X, 02LNF.A02, 02LNF.A04, 02LNF.AA2, 02LNF.AA4, 02LNF.AB2, 02LNF.AB4 02LNF.AF2, 02LNF.AF4, | 04LN9.1CT, 04LN9.1CA, 04LN9.1CB, 04LN9.1CF, 02LNF.A02, 02LNF.A04, 02LNF.AA2, 02LNF.AA4, 02LNF.AB2, 02LNF.AB4, 02LNF.AF2, 02LNF.AF4, 02SOF.X, 04SOF.X |
| KQFA, KQFB | AC or EU to CO | 04LN9.1CT, 04LN9.1CA, 04LN9.1CB, 04LN9.1CF, 02LNF.A02, 02LNF.AA2, 02LNF.AB2, 02LNF.AF2, 02SOF.X, 04SOF.X | 04QB9.1CT, 04QB9.1CA, 04QB9.1CB, 04QB9.1CF 02QBF.K02, 02QBF.KA2, 02QBF.KB2, 02QBF.KF2, 02QBF.LL, 04QBF.LL |
| KQFA, KQFB | CO to CO | 02QBF.LL, 04QBF.LL | 02QBF.LL, 04QBF.LL |
| KQFC, KQFD, KQFE, KQFF, KQFG, KQFK, KQFL, KQFN, KQFP, KQFQ, KQFR, KQFS | AC or EU to AC or EU | 04LN9.1CT, 04LN9.1CA, 04LN9.1CB, 04LN9.1CF, 02LNF.A02, 02LNF.A03, 02LNF.A04, 02LNF.AA2, 02LNF.AA3, 02LNF.AA4, 02LNF.AA5, 02LNF.AB2, 02LNF.AB3, 02LNF.AB4, 02LNF.AB5, 02LNF.AF2, 02LNF.AF3, 02LNF.AF4, 02LNF.AF5 | 04LN9.1CT, 04LN9.1CA, 04LN9.1CB, 04LN9.1CF, 02LNF.A02, 02LNF.A03, 02LNF.A04, 02LNF.AA2, 02LNF.AA3, 02LNF.AA4, 02LNF.AA5, 02LNF.AB2, 02LNF.AB3, 02LNF.AB4, 02LNF.AB5, 02LNF.AF2, 02LNF.AF3, 02LNF.AF4, 02LNF.AF5 |
| KQFC, KQFD, KQFE, KQFF, KQFG, KQFK, KQFL, KQFN, KQFP, KQFQ, KQFR, KQFS | AC or EU to CO | 04LN9.1CT, 04LN9.1CA, 04LN9.1CB, 04LN9.1CF, 02LNF.A02, 02LNF.AA2, 02LNF.AB2, 02LNF.AF2 | 04QB9.1CT, 04QB9.1CA, 04QB9.1CB, 04QB9.1CF 02QBF.K02, 02QBF.KA2, 02QBF.KB2, 02QBF.KF2 |

Product Offering ~ Ethernet over SONET (EoS)

| Ethernet Rate Adjustable at 1 Gbps |
| --- |
| NC Code | Location | NCI | SEC NCI |
| KRRA, KRRB, KRRC, KRRD, KRRG, KRRH | AC or EU to AC or EU | 02LNF.A02, 02LNF.A04 02LNF.AA2, 02LNF.AA4 02LNF.AB2, 02LNF.AB4 02LNF.AF2, 02LNF.AF4 | 02LNF.A02, 02LNF.A04 02LNF.AA2, 02LNF.AA4 02LNF.AB2, 02LNF.AB4 02LNF.AF2, 02LNF.AF4 |
| KRRA, KRRB, KRRC, KRRD, KRRG, KRRH | AC or EU to CO | 02LNF.A02, 02LNF.AA2, 02LNF.AB2, 02LNF.AF2 | 02QBF.K02, 02QBF.KA2, 02QBF.KB2, 02QBF.KF2, 02QBF.LL |
| KRSA, KRSC, KRSL, KRS2 | AC or EU to AC or EU | 02LNF.A02, 02LNF.A04 02LNF.AA2, 02LNF.AA4 02LNF.AB2, 02LNF.AB4 02LNF.AF2, 02LNF.AF4, 02SOF.X, 04SOF.X | 02LNF.A02, 02LNF.A04 02LNF.AA2, 02LNF.AA4 02LNF.AB2, 02LNF.AB4 02LNF.AF2, 02LNF.AF4 02SOF.X, 04SOF.X |
| KRSA, KRSC, KRSL, KRS2 | AC or EU to CO | 02LNF.A02, 02LNF.AA2, 02LNF.AB2, 02LNF.AF2, 02SOF.X | 02QBF.K02, 02QBF.KA2, 02QBF.KB2, 02QBF.KF2, 02QBF.LL |
| KRSA, KRSC, KRSL, KRS2 | CO to CO | 02QBF.LL | 02QBF.LL |
| KRSB, KRSD, KRSE, KRSF, KRSI, KRSU, KRSY, KRSZ, KRS0 | AC or EU to AC or EU | 02LNF.A02, 02LNF.A04 02LNF.AA2, 02LNF.AA4 02LNF.AB2, 02LNF.AB4 02LNF.AF2, 02LNF.AF4, | 02LNF.A02, 02LNF.A04 02LNF.AA2, 02LNF.AA4 02LNF.AB2, 02LNF.AB4 02LNF.AF2, 02LNF.AF4 |
| KRSB, KRSD, KRSE, KRSF, KRSI, KRSU, KRSY, KRSZ, KRS0 | AC or EU to CO | 02LNF.A02, 02LNF.AA2, 02LNF.AB2, 02LNF.AF2 | 02QBF.K02, 02QBF.KA2, 02QBF.KB2, 02QBF.KF2 |

Product Offering ~ Ethernet Over SONET (EoS)

Network Channel Interface (NCI) and Secondary Network Channel Interface (SECNCI) Codes:

NCI Code 04LN9. xxx

04	= 4 Conductors (4-wire)

LN	= Local Area Network Interface

9	= 100 Ohms

1CA	= 100 Base-T Ethernet w/Auto Negotiation

1CB	= 100 Base-T Ethernet w/Auto Negotiation and Flow Control

1CF	= 100 Base-T Ethernet w/ Flow Control

1CT	= 100 Base-T Ethernet

NCI Codes 02LNF.xxx

02	= 2 Conducators (2-fiber)

LN	= Local Area Network Interface

F	= Fiber

A02	= 1310 nm, Single-mode Fiber (e.g. 100BASE-LX10, 1000BASE-LX, 10GBASE-LR and

10GBASE-LW in IEEE 802.3)

A04	= 850 nm, 50 micron multimode Fiber (e.g. specified for 10BASE-FL, 1000BASE-SX,

10GBASE-SR and 10GBASE-SW in IEEE 802.3)

AA2	= 1310 nm, Single-mode Fiber (e.g. 100BASE-LX10, 1000BASE-LX, 10GBASE-LR and 10GBASE-LW in IEEE 802.3) w/Auto Negotiation

AA4	= 850 nm, 50-micron multimode Fiber (e.g., specified for 10BASE-FL, 1000BASE-SX, 10GBASE-SR and 10GBASE-SW in IEEE 802.3) w/Auto

Negotiation

AB2	= 1310 nm, Single-mode Fiber (e.g., 100BASE-LX10, 1000BASE-LX, 10GBASE-LR and 10GBASE-LW in IEEE 802.3) w/Auto Negotiation and

Flow Control

AB4	= 850 nm, 50-micron multimode Fiber (e.g., specified for 10BASE-FL, 1000BASE-SX, 10GBASE-SR and 10GBASE-SW in IEEE 802.3) w/Auto

Negotiation and Flow Control

AF2	= 1310 nm, Single-mode Fiber (e.g., 100BASE-LX10, 1000BASE-LX, 10GBASE-LR and 10GBASE-LW in IEEE 802.3) w/Flow Control

AF4	= 850 nm, 50 micron multimode Fiber (e.g. specified for 10BASE-FL, 1000BASE-SX, 10GBASE-SR and 10GBASE-SW in IEEE 802.3) w/Flow

Control

NCI Codes   02QBF.xxx or 04QBF.xxx

02	= 2 Conductors (2- fiber)

04	= 4 Conductors (4-fiber)

QB	= Central Office Manual Cross Connect Termination with No Sub-Rating Capability For

Non-Multiplexed Facilities Only.

F	= Fiber

K02	= Ethernet, 1310 nm, Single-mode Fiber (e.g., 100BASE-LX10, 1000BASE-LX, 10GBASE-LR and 10GBASE-LW in IEEE 802.3)

KA2	= Ethernet, 1310 nm, Single-mode Fiber (e.g., 100BASE-LX10, 1000BASE-LX, 10GBASE-LR and 10GBASE-LW in IEEE 802.3)

W/Auto Negotiation

KB2	= Ethernet, 1310 nm, Single-mode Fiber (e.g., 100BASE-LX10, 1000BASE-LX, 10GBASE-LR and 10GBASE-LW in IEEE 802.3) w/Auto

Negotiation and Flow Control

KF2	= Ethernet, 1310 nm, Single-mode Fiber (e.g., 100BASE-LX10, 1000BASE-LX, 10GBASE-LR and 10GBASE-LW in IEEE 802.3) w/Flow Control

NCI Codes 02SOF.X or 04SOF.X

02 	= 2 Conductors (2- fiber) 04 	= 4 Conductors (4-fiber)

SO 	= SONET Optical Interface

F = Fiber

X = Provider Engineered Reach Factor Note: Customer’s ordering from AT&T should use the “X” Protocol Option unless otherwise determined by Joint Engineering discussions with AT&T (see Tables at end of this TAB for definitions of other SO options).

Product Offering ~ Ethernet Over SONET (EoS)

##### ACCESS CLCI S/S Codes

| KQFS | Access | Fractional 100 Mb/s. Ethernet ~ Intrastate modifier: the interstate usage is less than 10% interstate as determined by the "PIU" FID, or for feature group “a “services, the "UTNT" FID initially indicated less than 10% interstate usage. Customer/provider interface. |
| --- | --- | --- |
| KQGS | Access | Fractional 100 Mb/s. Ethernet ~ Interstate: The interstate usage is more than 10% interstate as determined by the "PIU" FID, or Feature Group A services, the "UTNT' FID initially indicated more than 10% interstate usage. Customer/provider interface. |
| KRFS | Access | Rate adjustable gigabit Ethernet ~ Intrastate modifier: the interstate usage is less than 10% interstate as determined by the "PIU" FID, or for feature group “a” service, the "UTNT" FID initially indicated less than 10% interstate usage. Customer/provider interface. |
| KRGS | Access | Rate adjustable gigabit Ethernet~ Interstate: The interstate usage is more than 10% interstate as determined by the "PIU" FID, or Feature Group A services, the "UTNT' FID initially indicated more than 10% interstate usage. Customer/provider interface. |
| KRXZ | Access | Rate adjustable gigabit Ethernet~ No Further Parameters. Official Company Services. |

NON-ACCESS CLCI S/S Codes

| L1XX | Non-Access (IntraLATA) | Rate adjustable Gigabit Ethernet~ No Further Parameters. |
| --- | --- | --- |
| L1XZ | Non-Access (IntraLATA) | Rate adjustable Gigabit Ethernet~ Official Company Services. |
| L1YX | Non-Access (IntraLATA) | Rate adjustable Gigabit Ethernet~ Interstate: No Further Parameters. |
| L2XX | Non-Access (IntraLATA) | Rate adjustable 100Mbps Ethernet~ No Further Parameters. |

Notes:

- EoS CL Coding is consistent across the different vendor platforms and is the same across the AT&T Midwest, Southwest & West regions.  See EoS CL Coding for the Southeast region in the SMARTRing / SMARTRing with Hub Extension and Associated Services section.

AT&T

Product/Offering

Title Page

For

SONET

Network Channel Interface Protocol Option Tables

The following table for SONET Next Generation NCI Protocol Code “SS” and associated Protocol Option codes to be used in AT&T on a going forward basis:

| Protocol | NC rate | Option | Description |
| --- | --- | --- | --- |
| SS |  | SONET Next Generation Multiplex Supporting Drops of: |
|  | All | 000 | Capability Not Specified |
|  | OC3 | E18 | 1 Gbps, OC3, 100 Mbps Ethernet, STS-1, DS3, DS3 Transmux, 10 Mbps Ethernet, DS1 |
|  | OC12 | E19 | 1 Gbps, OC3, OC12, 100 Mbps Ethernet, STS-1, DS3, DS3 Transmux, 10 Mbps Ethernet, DS1 |
|  | OC48 | F14 | 1 Gbps, OC3, OC12, OC48, 100 Mbps Ethernet, STS-1, DS3, DS3 Transmux, 10 Mbps Ethernet, DS1 |
|  | OC192 | G02 | 1 Gbps, OC3, OC12, OC48, OC192, 100 Mbps Ethernet, STS-1, DS3, DS3 Transmux, 10 Mbps Ethernet, DS1 |

Notes:

- DS3 alone equates to no “Transmux”

- The Protocol Option codes for Next Generation SONET only indicates what the offering Capable is of; not how it is Configured.  Other communication vehicles will be used to convey the configuration between the Customer and AT&T.

- For the purposes of this document, and STS-1 and an EC-1 is considered the same interface and 1Gig and GigE is considered the same interface

- For the purposes of this document, the order of the drop capabilities has been altered for readability.  The actual content for each Protocol Option is still consistent with the iconectiv (previously known as Telcordia Technologies) standard definitions.

- Use of the “0” s in the 7th, 8th & 9th = No drops specified at this time.  This option is only valid for use with our Ring products.  The “No drops specified at this time” option is not applicable with any Point-to-Point products or offerings.

- SONET Next Generation NCI Protocol Code “SS” (02SSF. +++) will be used for all new DSRS requests.    OCN SECNCI may use both Next Generation & Non-Next Generation codes.

The previously used table for “SS” and associated Protocol Option codes is being provided as reference only to see definitions for changes.  Only the codes listed above should be used for new activity.

Code			Option	Definition

SM			Network Channel Interface (NCI) Codes for SONET

Figure 1:  NCI Protocols (Positions 3, 4) & Protocol Options (Positions 7, 8, 9) for OC-12 & below

| Pos.s 1 & 2 | Pos.s 3 & 4 | Positions 5 & 6 | Position 7 | Position 8 | Position 9 |
| --- | --- | --- | --- | --- | --- |
| No. of conductors | OC -12 and below | Impedance & Delimiter | 155.520 Mbps OC3/STS-3C | 51.840 Mbps STS-1/DS3s | 1.544 Mbps VT 1.5/DS1s |
|  | SM |  | 0 = 0 % A = 0 B = 1 C = 2 D = 3 E = 4 | 0 = 0 1 = 1 2 = 2 3 = 3 4 = 4 5 = 5 6 = 6 7 = 7 8 = 8 9 = 9 A = 10 B = 11 C = 12 | 0 = 0% 1 = 7 2 = 14 3 = 21 4 = 28 5 = 35 6 = 42 7 = 49 8 = 56 9 = 63 A = 70 B = 77 C = 84 D = 168 E = 252 F = 336 |

SEE NOTES ON NEXT PAGE:

Notes associated with the “SM” Protocol codes.

- The seventh protocol option describes the total number of OC3s or STS3Cs.

- The eighth protocol option describes the total number of STS1s or DS3s.

- The ninth protocol option describes the total number of STSs wired with DS1 visibility.

- Protocol Options are left justified.  If you have described your desired configuration with the 7th or 8th positions, you do not need to reflect the option codes associated with “Zero” in the 8th or 9th position…these would be assumed.

- The following is an example of how to use this interface:

An OC12 multiplexer with 2 OC3/STS-3Cs; 5 STS-1/DS3s; 7 VT 1.5/DS1s wired for DS1 visibility would be coded 02SMF.C51

- This code can be used to represent multiplexers for SONET rates from OC3 to OC12 and will depict how the drop side of the multiplexer is to be wired.  Plugs are not provided until drop level services are ordered.

- % = Use the “A” for zero if using with other values in the 8th and/or 9th positions.

Use of the “0” s in the 7th, 8th & 9th = No drops specified at this time.  This option is only valid for use with our Ring products.  The “No drops specified at this time” option is not applicable with any Point-to-Point products or offerings.

- Code		Option	Definition

# SN			NCI Protocols (Positions 3, 4) & Protocol Options (Positions 7, 8, 9) for OC-48

| Positions 1 & 2 | Positions 3 & 4 | Positions 5 & 6 | Position 7 | Position 8 | Position 9 |
| --- | --- | --- | --- | --- | --- |
| No. of conductors | OC - 48 | Impedance & Delimiter | 622.080 Mbps OC12/STS-12Cs | 155.520 Mbps OC3/STS-3C | 51.840 Mbps STS-1/DS3s |
|  | SN |  | 0 = 0 % A = 0 B = 1 C = 2 D = 3 E = 4 | 0 = 0 1 = 1 2 = 2 3 = 3 4 = 4 5 = 5 6 = 6 7 = 7 8 = 8 9 = 9 A = 10 B = 11 C = 12 D = 13 E = 14 F = 15 G = 16 | 0 = 0 % 1 = 3 2 = 6 3 = 9 4 = 12 5 = 15 6 = 18 7 = 21 8 = 24 9 = 27 A = 30 B = 33 C = 36 D = 39 E = 42 F = 45 G = 48 |

See Notes on next page:

Notes associated with the “SN” Protocol codes

- The seventh protocol option describes the total number of OC12s or STS12Cs.

- The eighth protocol option describes the total number of OC3s or STS3Cs.

- The ninth protocol option describes the total number of STS1s or DS3s.

- Protocol Options are left justified.  If you have described your desired configuration with the 7th or 8th positions, you do not need to reflect the option codes associated with “Zero” in the 8th or 9th position…these would be assumed.

- The following is an example of how to use this interface:

- An OC48 multiplexer with 2 OC12/STS-12Cs; 4 OC3/STS-3Cs; 12 STS-1/DS3s would be coded 02SNF.C44

- This code can be used to represent an OC48 multiplexer and will depict how the drop side of the multiplexer is to be wired.  Plugs are not provided until drop level services are ordered.

- % = Use the “A” for zero if using with other values in the 8th and/or 9th positions.

- Use of the “0” s in the 7th, 8th & 9th = No drops specified at this time.  This option is only valid for use with our Ring products.  The “No drops specified at this time” option is not applicable with any Point-to-Point products or offerings.

# Code	Option	             Definition

SO	B	SONET Optical Long Reach 1, Single Longitudinal Mode Laser, 1310 nm (ITU-T: L-1.1 OR L-4.1 OR L-16.1 &SLM)

C	SONET Optical Intermediate Reach-1, Multi-Longitudinal Mode Laser, 1310 nm (ITU-T: S-1.1 or S-4.1 & MLM) (only valid for use with MON Sub-Rating services)

D	SONET Optical Intermediate Reach – 1, Single Longitudinal Mode Laser, 1310 nm (ITU-T: S-16.1 & SLM)

## E	SONET Optical Short Reach – 1, Multi Longitudinal Mode Laser/Light Emitting Diode, 1310 nm (ITU-T: I-1 or I-4 & MLM/LED) (limited use based on Joint Engineering.  As example: Not available at all with OCN product.)

X		Provider Engineered Reach Factor

3		OC3 Optical (this code was created for use with non-SONET channels with SONET handoffs and the

Specific OC rate must be specified)

12		OC12 Optical (this code was created for use with non-SONET channels with SONET handoffs and the

Specific OC rate must be specified)

Note: Customer’s ordering from AT&T should use the “X” Protocol Option unless otherwise determined by Joint Engineering discussions with AT&T.

# Code		Option	Definition

SP		NCI Protocols (Positions 3, 4) & Protocol Options (Positions7, 8, 9) for OC192

| Positions 1 & 2 | Positions 3 & 4 | Positions 5 & 6 | Option 7 | Option 8 | Option 9 |
| --- | --- | --- | --- | --- | --- |
| No. of conductors | OC - 192 | Impedance & Delimiter | 2488.42 Mb/s Number of OC48s | 622.08 Mb/s OC12/STS-12Cs | 155.520 Mb/s, OC3/STS-3Cs |
|  | SP |  | 0 = 0 % A = 0 B = 1 C = 2 D = 3 E = 4 | 0 = 0 1 = 1 2 = 2 3 = 3 4 = 4 5 = 5 6 = 6 7 = 7 8 = 8 9 = 9 A = 10 B = 11 C = 12 D = 13 E = 14 F = 15 G = 16 | 0 = 0 % 1 = 1 2 = 2 3 = 3 4 = 4 5 = 5 6 = 6 7 = 7 8 = 8 9 = 9 A = 10 B = 11 C = 12 D = 16 E = 20 F = 24 G = 28 H = 32 J = 36 K = 40 L = 44 M = 48 N = 52 P = 56 Q = 60 R = 64 |

See Notes on next page:

Notes associated with the “SP” Protocol codes

- The seventh protocol option describes the total number of OC48s or STS48Cs.

- The eighth protocol option describes the total number of OC12s or STS12Cs.

- The ninth protocol option describes the total number of OC3s or STS3Cs.

- Protocol Options are left justified.  If you have described your desired configuration with the 7th or 8th positions, you do not need to reflect the option codes associated with “Zero” in the 8th or 9th position…these would be assumed.

- The following is an example of how to use this interface: An OC192 multiplexer with 2 OC48s; 4 OC12/STS-12Cs; 4 OC3/STS-3Cs would be coded 02SPF.C44.

- This code will depict how the drop side of the multiplexer is to be wired.  Plugs are not provided until drop level services are ordered.

- OC-192 may not yet be approved for use but the NCI table is all inclusive.

- % = Use the “A” for zero if using with other values in the 8th and/or 9th positions.

- Use of the “0” s in the 7th, 8th & 9th = No drops specified at this time.  This option is only valid for use with our Ring products.  The “No drops specified at this time” option is not applicable with any Point-to-Point products or offerings.

- The “SP” Protocol code can also be used with OC48 configurations for RING family of services if the OC48 is being handed off intact (e.g., 02SPF.B would indicate an OC48 with a single OC48 Pipe).

AT&T

Product/Offering

Title Page

For

Retired Product lines

Not available for new services

Retired Product lines ~ not available for new services

| Table of Contents Retired Product lines ~ not available for new services | Valid in these AT&T Regions | Page |
| --- | --- | --- |
|  | Midwest | Southwest | East | West | Southeast |  |
| ReliaNET | N/A | X | N/A | N/A | N/A | 49 |
| Self-Healing Transport Network (STN) Service | N/A | X | N/A | N/A | N/A | 57 |
| SONET Ring and Access Services | N/A | N/A | N/A | X | N/A | 61 |
| SONET Xpress | X | N/A | N/A | N/A | N/A | 67 |

AT&T

Product/Offering

Title Page

For

ReliaNET

Retired ~ not available for new services

Product/Offering ~ ReliaNET

AT&T  Southwest region

| NC Code | Product Description | Location Configuration | NCI | SEC NCI |
| --- | --- | --- | --- | --- |
| HCP- | Digital High-Capacity Channel Service HC1 (DS1) – SF and AMI - Premium Service and Loop Protection (e.g., ReliaNET®) | AC-AC | 04DS6. *, 02SOF.X, 04SOF.X & | 04DS6. *, 02SOF.X, 04SOF.X & |
|  |  | AC-CO | 04DS6. *, 02SOF.X, 04SOF.X & | 04CS6. *, 04QB6. *, 02QBF.LL, 04QBF.LL |
|  |  | AC-EU | 04DS6. *, 02SOF.X, 04SOF.X & | 04DS6. *, 02SOF.X, 04SOF.X & |
|  |  | CO-EU | 04CS6. *, 04QB6. *, 02QBF.LL, 04QBF.LL | 04DS6. *, 02SOF.X, 04SOF.X & |
| HCPM | Digital High-Capacity Channel Service HC1 (DS1) – SF and AMI - Premium Service and & MUX (e.g., ReliaNET®) | AC-AC | 04DS6. *, 02SOF.X, 04SOF.X & | 04DS6. *, 02SOF.X, 04SOF.X & |
|  |  | AC-CO | 04DS6. *, 02SOF.X, 04SOF.X & | 04CS6. *, 04QB6. *, 02QBF.LL, 04QBF.LL |
|  |  | AC-EU | 04DS6. *, 02SOF.X, 04SOF.X & | 04DS6. *, 02SOF.X, 04SOF.X & |
|  |  | CO-EU | 04CS6. *, 04QB6. *, 02QBF.LL, 04QBF.LL | 04DS6. *, 02SOF.X, 04SOF.X & |
| HCT- | Digital High-Capacity Channel Service HC1 (DS1) – SF and B8ZS - Premium Service and Loop Protection (e.g., ReliaNET®) | AC-AC | 04DS6. *, 02SOF.X, 04SOF.X & | 04DS6. *, 02SOF.X, 04SOF.X & |
|  |  | AC-CO | 04DS6. *, 02SOF.X, 04SOF.X & | 04CS6. *, 04QB6. *, 02QBF.LL, 04QBF.LL |
|  |  | AC-EU | 04DS6. *, 02SOF.X, 04SOF.X & | 04DS6. *, 02SOF.X, 04SOF.X & |
|  |  | CO-EU | 04CS6. *, 04QB6. *, 02QBF.LL, 04QBF.LL | 04DS6. *, 02SOF.X, 04SOF.X & |
| HCTM | Digital High-Capacity Channel Service HC1 (DS1) – SF and B8ZS - Premium Service & MUX (e.g., ReliaNET®) | AC-AC | 04DS6. *, 02SOF.X, 04SOF.X & | 04DS6. *, 02SOF.X, 04SOF.X & |
|  |  | AC-CO | 04DS6. *, 02SOF.X, 04SOF.X & | 04CS6. *, 04QB6. *, 02QBF.LL, 04QBF.LL |
|  |  | AC-EU | 04DS6. *, 02SOF.X, 04SOF.X & | 04DS6. *, 02SOF.X, 04SOF.X & |
|  |  | CO-EU | 04CS6. *, 04QB6. *, 02QBF.LL, 04QBF.LL | 04DS6. *, 02SOF.X, 04SOF.X & |

Product/Offering ~ ReliaNET

AT&T Southwest region

| NC Code | Product Description | Location Configuration | NCI | SEC NCI |
| --- | --- | --- | --- | --- |
| HCU- | Digital High-Capacity Channel Service HC1 (DS1) – ESF and AMI - Premium Service and Loop Protection (e.g., ReliaNET®) | AC-AC | 04DS6. *, 02SOF.X, 04SOF.X & | 04DS6. *, 02SOF.X, 04SOF.X & |
|  |  | AC-CO | 04DS6. *, 02SOF.X, 04SOF.X & | 04CS6. *, 04QB6. *, 02QBF.LL, 04QBF.LL |
|  |  | AC-EU | 04DS6. *, 02SOF.X, 04SOF.X & | 04DS6. *, 02SOF.X, 04SOF.X & |
|  |  | CO-EU | 04CS6. *, 04QB6. *, 02QBF.LL, 04QBF.LL | 04DS6. *, 02SOF.X, 04SOF.X & |
| HCUM | Digital High-Capacity Channel Service HC1 (DS1) – ESF and AMI - Premium Service and & MUX (e.g., ReliaNET®) | AC-AC | 04DS6. *, 02SOF.X, 04SOF.X & | 04DS6. *, 02SOF.X, 04SOF.X & |
|  |  | AC-CO | 04DS6. *, 02SOF.X, 04SOF.X & | 04CS6. *, 04QB6. *, 02QBF.LL, 04QBF.LL |
|  |  | AC-EU | 04DS6. *, 02SOF.X, 04SOF.X & | 04DS6. *, 02SOF.X, 04SOF.X & |
|  |  | CO-EU | 04CS6. *, 04QB6. *, 02QBF.LL, 04QBF.LL | 04DS6. *, 02SOF.X, 04SOF.X & |
| HCV- | Digital High-Capacity Channel Service HC1 (DS1) – ESF and B8ZS - Premium Service and Loop Protection (e.g., ReliaNET®) | AC-AC | 04DS6. *, 02SOF.X, 04SOF.X & | 04DS6. *, 02SOF.X, 04SOF.X & |
|  |  | AC-CO | 04DS6. *, 02SOF.X, 04SOF.X & | 04CS6. *, 04QB6. *, 02QBF.LL, 04QBF.LL |
|  |  | AC-EU | 04DS6. *, 02SOF.X, 04SOF.X & | 04DS6. *, 02SOF.X, 04SOF.X & |
|  |  | CO-EU | 04CS6. *, 04QB6. *, 02QBF.LL, 04QBF.LL | 04DS6. *, 02SOF.X, 04SOF.X & |
| HCVM | Digital High-Capacity Channel Service HC1 (DS1) – ESF and B8ZS - Premium Service & MUX (e.g., ReliaNET®) | AC-AC | 04DS6. *, 02SOF.X, 04SOF.X & | 04DS6. *, 02SOF.X, 04SOF.X & |
|  |  | AC-CO | 04DS6. *, 02SOF.X, 04SOF.X & | 04CS6. *, 04QB6. *, 02QBF.LL, 04QBF.LL |
|  |  | AC-EU | 04DS6. *, 02SOF.X, 04SOF.X & | 04DS6. *, 02SOF.X, 04SOF.X & |
|  |  | CO-EU | 04CS6. *, 04QB6. *, 02QBF.LL, 04QBF.LL | 04DS6. *, 02SOF.X, 04SOF.X & |

Product/Offering ~ ReliaNET

AT&T Southwest region

| NC Code | Product Description | Location Configuration | NCI | SEC NCI |
| --- | --- | --- | --- | --- |
| HFP- | DS3, High-Capacity Channel Service HC3, 44.736 Mbps ~Premium Service Parameters (e.g., ReliaNET (SM) Service) | AC-AC | 04DS6. *, 02SOF.X, 04SOF.X & | 04DS6. *, 02SOF.X, 04SOF.X & |
|  |  | AC-CO | 04DS6. *, 02SOF.X, 04SOF.X & | 04CS6. *, 04QB6. *, 02QBF.LL, 04QBF.LL |
|  |  | AC-EU | 04DS6. *, 02SOF.X, 04SOF.X & | 04DS6. *, 02SOF.X, 04SOF.X & |
|  |  | CO-EU | 04CS6. *, 04QB6. *, 02QBF.LL, 04QBF.LL | 04DS6. *, 02SOF.X, 04SOF.X & |

| HFPF | DS3, High-Capacity Channel Service HC3, 44.736 Mbps ~Premium Service Parameters (e.g., ReliaNET (SM) Service DS3 Pipe with FAC and SWC Protection) | AC-AC | 04DS6. *, 02SOF.X, 04SOF.X & | 04DS6. *, 02SOF.X, 04SOF.X & |
| --- | --- | --- | --- | --- |
|  |  | AC-CO | 04DS6. *, 02SOF.X, 04SOF.X & | 04CS6. *, 04QB6. *, 02QBF.LL, 04QBF.LL |
|  |  | AC-EU | 04DS6. *, 02SOF.X, 04SOF.X & | 04DS6. *, 02SOF.X, 04SOF.X & |
|  |  | CO-EU | 04CS6. *, 04QB6. *, 02QBF.LL, 04QBF.LL | 04DS6. *, 02SOF.X, 04SOF.X & |

| HFPM | DS3, High-Capacity Channel Service HC3, 44.736 Mbps ~Premium Service Parameters with CO Multiplexing (e.g., ReliaNET (SM) Service For switched FGB, FGC and FGD, only) | AC-AC | 04DS6. *, 02SOF.X, 04SOF.X & | 04DS6. *, 02SOF.X, 04SOF.X & |
| --- | --- | --- | --- | --- |
|  |  | AC-CO | 04DS6. *, 02SOF.X, 04SOF.X & | 04CS6. *, 04QB6. *, 02QBF.LL, 04QBF.LL |
|  |  | AC-EU | 04DS6. *, 02SOF.X, 04SOF.X & | 04DS6. *, 02SOF.X, 04SOF.X & |
|  |  | CO-EU | 04CS6. *, 04QB6. *, 02/04QBF.LL, | 04DS6. *, 02SOF.X, 04SOF.X & |
| OA--^ | Digital High Capacity, SONET – SONET, OC1, 51.84 Mbps Point to Point ~ | AC-EU, EU-EU | See Notes | See Notes |
| OB-R | Digital High Capacity, SONET - OC3 (155.520 Mbps) Point to Point ~ STS3C Payload (Concatenated Signal) | AC-EU, EU-EU | 02SOF.X, 04SOF.X & | 02SOF.X, 04SOF.X & |

# Notes:

- ReliaNET is retired from the AT&T product line.  Codes can still be used for existing service and for new service for those customers with capacity on their existing contract.

- AC= Access Customer (POP), CO= Central Office, EU= End User

- The “*” indicates any valid / appropriate Protocol Options per TAB 6 of the Carrier Coding Guides (CCGs).

- & = the customer should use the “X” = Provider Engineered Reach Factor unless instructed to use a different valid Protocol Option by AT&T.

- ReliaNET is offered only at the DS1, DS3, OC1^ and OC3 rates.

- AT&T does not offer SONET with electrical handoffs ~ e.g., the “J” NC codes.  We use the Optical handoff “O” codes.

- ^ = The OC1 rate code of “OA” has been retired at the National level.  If the request is truly for an OC1 rate of service, and you are the external customer of AT&T, please contact your companies COMMON LANGUAGE® (CL) Coordinator or your AT&T Account Manager for assistance.  If you are an internal AT&T employee, helping an AT&T customer, please contact the AT&T CL Coordinator, Diane Fletcher (df1685@att.com)  at 770-650-5841.

- For Collocation related coding for this product line, see OCN Point-to-Point matrix.

- Based on the orientation of the service being ordered the location configuration could be reversed (e.g., CO-EU could also be EU-CO).   The NCI and SECNCI could be swapped based on the orientation as well.

AT&T

Product/Offering

Title Page

For

Self-Healing Transport Network (STN) Service

(Retired ~ not available for new services)

Product/Offering ~ Self-Healing Transport Network (STN) Service

AT&T Southwest region

| NC Code | Product Description | Location Configuration | NCI | SEC NCI |
| --- | --- | --- | --- | --- |
| HFHT | DS3, High-Capacity Channel Service HC3, 44.736 Mbps ~ Self Healing, Disaster Recovery, e.g., Customer Survivability ~Facility Protection (e.g., STN) | AC-AC | 04DS6. *, 02SOF.X, 04SOF.X & | 04DS6. *, 02SOF.X, 04SOF.X & |
|  |  | AC-CO | 04DS6. *, 02SOF.X, 04SOF.X & | 04CS6. *, 04QB6. *, 02QBF.LL, 04QBF.LL |
|  |  | AC-EU | 04DS6. *, 02SOF.X, 04SOF.X & | 04DS6. *, 02SOF.X, 04SOF.X & |
|  |  | CO-EU | 04CS6. *, 04QB6. *, 02QBF.LL, 04QBF.LL | 04DS6. *, 02SOF.X, 04SOF.X & |
| HFHU | DS3, High-Capacity Channel Service HC3, 44.736 Mbps ~ Self Healing, Disaster Recovery, e.g., Customer Survivability ~Facility & Node Protection (e.g., STN with Dual Mode Interconnection to SecureNet( Service with Option 2 *NOTE: HFHL and HFHU must be ordered together). | AC-AC | 04DS6. *, 02SOF.X, 04SOF.X & | 04DS6. *, 02SOF.X, 04SOF.X & |
|  |  | AC-CO | 04DS6. *, 02SOF.X, 04SOF.X & | 04CS6. *, 04QB6. *, 02QBF.LL, 04QBF.LL |
|  |  | AC-EU | 04DS6. *, 02SOF.X, 04SOF.X & | 04DS6. *, 02SOF.X, 04SOF.X & |
|  |  | CO-EU | 04CS6. *, 04QB6. *, 02QBF.LL, 04QBF.LL | 04DS6. *, 02SOF.X, 04SOF.X & |
| HFHV | DS3, High-Capacity Channel Service HC3, 44.736 Mbps ~ Self Healing, Disaster Recovery, e.g., Customer Survivability ~ Facility Protection & B8ZS Compatible CO Mux (e.g., STN). | AC-CO | 04DS6. *, 02SOF.X, 04SOF.X & | No SECNCI |
|  |  | CO-CO | 04CS6. *, 04QB6. *, 02QBF.LL, 04QBF.LL | No SECNCI |
|  |  | EU-CO | 04DS6. *, 02SOF.X, 04SOF.X & | No SECNCI |
| HFHW | DS3, High-Capacity Channel Service HC3, 44.736 Mbps ~ Self Healing, Disaster Recovery, e.g., Customer Survivability ~B8ZS Compatible CO Mux (e.g., STN). | AC-CO | 04DS6. *, 02SOF.X, 04SOF.X & | No SECNCI |
|  |  | CO-CO | 04CS6. *, 04QB6. *, 02QBF.LL, 04QBF.LL | No SECNCI |
|  |  | EU-CO | 04DS6. *, 02SOF.X, 04SOF.X & | No SECNCI |

Product/Offering ~ Self-Healing Transport Network (STN) Service (con’t)

AT&T Southwest region

| NC Code | Product Description | Location Config | NCI | SEC NCI |
| --- | --- | --- | --- | --- |
| JI-- | SONET Electrical STS-1, 51.84 Mbps | AC-AC | 02SOF. *, 04SOF. *, 04ST6. * | 02SOF. *, 04SOF. *, 04ST6. * |
|  |  | AC-CO | 02SOF. *, 04SOF. *, 04ST6. * | 02QBF.LL, 04CS6. *, 04QB6. *, 04QBF.LL, 04ST6. * |
|  |  | AC-EU | 02SOF. *, 04SOF. *, 04ST6. * | 02SOF. *, 04SOF. *, 04ST6. * |
|  |  | CO-EU | 02QBF.LL, 04CS6. *, 04QB6. *, 04QBF.LL, 04ST6. * | 02SOF. *, 04SOF. *, 04ST6. * |
| JIA- | SONET Electrical STS-1, 51.84 Mbps, VT1 Structured | AC-CO | 02SOF. *, 04SOF. *, 04ST6. * | 02QBF.LL, 04CS6. *, 04ST6. *,04QB6. *, 04QBF.LL |
|  |  | AC-EU | 02SOF. *, 04SOF. *, 04ST6. * | 02SOF. *, 04SOF. *, 04ST6. * |
|  |  | CO-EU | 02QBF.LL, 04CS6. *, 04QB6. *, 04QBF.LL, 04ST6. * | 02SOF. *, 04SOF. *, 04ST6. * |
| JIAA | SONET Electrical STS-1, 51.84 Mbps, VT1 Structured, Central Office Multiplexer | AC-CO | 02SOF. *, 04SOF. *, 04ST6. * | 04CS6.S1 |
| JIAB | SONET Electrical STS-1, 51.84 Mbps, VT1 Structured, Non-CO Multiplexer | AC-EU | 02SOF. *, 04SOF. *, 04ST6. * | No SECNCI |
|  |  | CO-EU | 02QBF.LL, 4QBF.LL, 04ST6. * | No SECNCI |
| JIAC | SONET Electrical STS-1, 51.84 Mbps, VT1 Structured, Multiplexer at both ends | CO-CO | 04CS6.S1, 04CS6.S1R | 04CS6.S1, 04CS6.S1R |
| JJCD | SONET Electrical STS-3, 155.520 Mbps, Concatenated, Interoffice and wire center protection. | AC-CO | 04SOF. *, 04ST6. * | 04QBF.LL, 04ST6. * |
|  |  | AC-EU | 04SOF. *, 04ST6. * | 04SOF. *, 04ST6. * |
|  |  | CO-EU | 04QBF.LL, 04ST6. * | 04SOF. *, 04ST6. * |

Product/Offering ~ Self-Healing Transport Network (STN) Service (con’t)

| NC Code | Product Description | Location Configuration | NCI | SEC NCI |
| --- | --- | --- | --- | --- |
| OA--^ | Digital High Capacity, SONET – OC1, 51.84 Mbps Point to Point | AC-EU, EU-EU | See Notes | See Notes |
| OB-R | Digital High Capacity, SONET - OC3 (155.520 Mbps) Point to Point ~ STS3C Payload (Concatenated Signal) | AC-EU, EU-EU | 02SOF.X, 04SOF.X & | 02SOF.X, 04SOF.X & |
| OD-R | Digital High Capacity, SONET – OC12 (622.080 Mbps) Point to Point ~ STS12C Payload (Concatenated Signal) | AC-EU, EU-EU | 02SOF.X, 04SOF.X & | 02SOF.X, 04SOF.X & |

Notes:

- Self-Healing Transport Network (STN) is retired from the AT&T product line.  Codes can still be used for existing service and for new service for those customers with capacity on their existing contract.

- AC= Access Customer (POP), CO= Central Office, EU= End User

- The “*” indicates any valid / appropriate Protocol Options per the Protocol tables towards the end of this document in the SONET Table portion before the Retired portion.

- & = the customer should use the “X” = Provider Engineered Reach Factor unless instructed to use a different valid Protocol Option by AT&T.

- STN is offered only at the DS3 and OC1^, OC3 and OC12 rates.

- ^ = The OC1 rate code of “OA--” has been retired at the National level.  If the request is truly for an OC1 rate of service, and you are the external customer of AT&T, please contact your companies COMMON LANGUAGE® (CL) Coordinator or your AT&T Account Manager for assistance.  If you are an internal AT&T employee, helping an AT&T customer, please contact the AT&T CL Coordinator, Diane Fletcher (df1685@att.com) or 770-650-5841.

- For Collocation related coding for this product line, see OCN Point-to-Point matrix.

AT&T

Product/Offering

Title Page

For

SONET Ring and Access Services

(Retired ~ not available for new services)

Product/Offering ~ SONET Ring and Access Services

AT&T West region

This Product section will be split into several smaller unique offerings that fall under the SONET Ring and Access Services umbrella.

### SONET Circuit Service

| NC Code | Product Description | Location Configuration | NCI | SEC NCI |
| --- | --- | --- | --- | --- |
| OB-R | Digital High Capacity, SONET - OC3 (155.520 Mbps) Point to Point ~ STS3C Payload (Concatenated) | AC-AC, AC-EU, EU-EU | 02SOF.X & | 02SOF.X & |

Notes:

- AC= Access Customer (POP), CO= Central Office, EU= End User

- This product does not allow for protection.  All NCI/SECNCI codes will start with an “02”

- & = the customer should use the “X” = Provider Engineered Reach Factor unless instructed to use a different valid Protocol Option by AT&T.

- This matrix is only showing the Optical codes for SONET Circuit Service.  This product is offered at the DS1 and DS3 rates as well, but those are not covered in this document.

- Based on the orientation of the service being ordered the location configuration could be reversed (e.g., CO-EU could also be EU-CO).

Product/Offering ~ SONET Ring and Access Services

AT&T West region

OC12C 622 Mbps Transport Service

| NC Code | Product Description | Location Configuration | NCI | SEC NCI |
| --- | --- | --- | --- | --- |
| OD-R | Digital High Capacity SONET, OC12, (622.080 Mbps) Point to Point ~ STS12C Payload (Concatenated) | AC-AC. AC-EU, EU-EU | 02SOF.X & | 02SOF.X & |

Notes:

- AC= Access Customer (POP), CO= Central Office, EU= End User

- This product does not allow for protection.  All NCI/SECNCI codes will start with an “02”

- & = the customer should use the “X” = Provider Engineered Reach Factor unless instructed to use a different valid Protocol Option by AT&T.

Product/Offering ~ SONET Ring and Access Services

AT&T West region

### Dedicated SONET Ring

| Network Channel | Definitions |
| --- | --- |
| OBU- | Digital High Capacity, SONET - OC3 155.520 Mbps ~ Uni-Directional Ring |
| OBUC | Digital High Capacity, SONET - OC3 155.520 Mbps ~ Uni-Directional Ring with Central Office Multiplexer |
| OBUD | Digital High Capacity, SONET - OC3 155.520 Mbps ~ Uni-Directional Ring with Non-CO Multiplexer |
| OBUE | Digital High Capacity, SONET - OC3 155.520 Mbps ~ Uni-Directional Ring with Multiplexer at both ends |
| ODU- | Digital High Capacity, SONET - OC12, 622.080 Mbps ~ Uni-Directional Ring |
| ODUC | Digital High Capacity, SONET - OC12, 622.080 Mbps ~ Uni-Directional Ring with Central Office MU |
| ODUD | Digital High Capacity, SONET - OC12, 622.080 Mbps ~ Uni-Directional Ring with Non-CO Multiplexer |
| ODUE | Digital High Capacity, SONET - OC12, 622.080 Mbps ~ Uni-Directional Ring with Multiplexer at both ends |
| OFU- | Digital High Capacity, SONET, OC48, 2488.320 Mbps ~ Uni-Directional Ring |
| OFUC | Digital High Capacity, SONET, OC48, 2488.320 Mbps ~ Uni-Directional Ring with Central Office MU |
| OFUD | Digital High Capacity, SONET, OC48, 2488.320 Mbps ~ Uni-Directional Ring with Non-CO Multiplexer |
| OFUE | Digital High Capacity, SONET, OC48, 2488.320 Mbps ~ Uni-Directional Ring with Multiplexer at both ends |
| OFV- | Digital High Capacity, SONET, OC48, 2488.320 Mbps ~ Bi-Directional Ring |
| OFVC | Digital High Capacity, SONET, OC48, 2488.320 Mbps ~ Bi-Directional Ring with Central Office Multiplexer |
| OFVD | Digital High Capacity, SONET, OC48, 2488.320 Mbps ~ Bi-Directional Ring with Non-CO Multiplexer |
| OFVE | Digital High Capacity, SONET, OC48, 2488.320 Mbps ~ Bi-Directional Ring with Multiplexer at both ends |

See Notes on next page:

Product/Offering ~ SONET Ring and Access Services

AT&T West region

Note:

- The Ring portion of SRAS has been retired and is not available for new services.

- These codes indicate that AT&T West region does offer Customer provided Multiplexers.

- AT&T West region offers only Uni-Directional Rings at OC3 and OC12 rates.  This is designated with the third character of “U”.  AT&T West region offers both Bi-Directional and Uni-Directional rings for the OC48 rate.  The third position would be a “V” or a “U”.

- For Ring offerings at OC192 rate are described under the Dedicated SONET Ring product Matrix, external to the SONET Ring and Access Services matrix.

- For Port-to-Port configurations see OCN Pt-to-Pt Matrix (using OB--, OB-R, OD--, OD-R, OF--, or OF-R).

Dedicated SONET Ring

| SONET OC3, OC12 and OC48 |
| --- |
| NC Code | Location | NCI | SEC NCI |
| OBU- | AC-AC, AC-EU, EU-EU | 02SOF.X & | 02SOF.X & |
| OBUC | AC-CO, CO-CO | 02SOF.X & | 02SMF. *, 02RGF. * |
| OBUC | CO-EU | 02SMF. *, 02RGF. * | 02SOF.X & |
| OBUD | AC-AC, AC-EU, EU-EU | 02SOF.X & | 02SMF. * |
| OBUE | AC-CO | 02SMF. * | 02SMF. *, 02RGF. * |
| OBUE | CO-CO, EU-EU | 02SMF. *, 02RGF. * | 02SMF. *, 02RGF. * |
| OBUE | CO-EU | 02SMF. *, 02RGF. * | 02SMF. * |
| ODU- | AC-AC, AC-EU, EU-EU | 02SOF.X & | 02SOF.X & |
| ODUC | AC-CO, CO-CO | 02SOF.X & | 02SMF. *, 02SNF. *, 02RGF. * |
| ODUC | CO-EU | 02SMF. *, 02SNF. *, 02RGF. * | 02SOF.X & |
| ODUD | AC-AC, AC-EU, EU-EU | 02SOF.X & | 02SMF. *, 02SNF. * |
| ODUE | AC-CO | 02SMF. *, 02SNF. * | 02SMF. *, 02SNF. *, 02RGF. * |
| ODUE | CO-CO, EU-EU | 02SMF. *, 02SNF. *, 02RGF. * | 02SMF. *, 02SNF. *, 02RGF. * |
| ODUE | CO-EU | 02SMF. *, 02SNF. *, 02RGF. * | 02SMF. *, 02SNF. * |

Product/Offering ~ SONET Ring and Access Services (con’t)

AT&T West region

Dedicated SONET Ring

| SONET OC3, OC12 and OC48 |
| --- |
| NC Code | Location | NCI | SEC NCI |
| OFU-, OFV- | AC-AC, AC-EU, EU-EU | 02SOF.X & | 02SOF.X & |
| OFUC, OFVC | AC-CO, CO-CO | 02SOF.X & | 02SMF. *, 02SNF. *, 02RGF. * |
| OFUC, OFVC | CO-EU | 02SNF. *, 02SPF. *, 02RGF. * | 02SOF.X & |
| OFUD, OFVD | AC-AC, AC-EU, EU-EU | 02SOF.X & | 02SNF. *, 02SPF. * |
| OFUE, OFVE | AC-CO | 02SNF. *, 02SPF. * | 02SNF. *, 02SPF. *, 02RGF. * |
| OFUE, OFVE | CO-CO, EU-EU | 02SNF. *, 02SPF. *, 02RGF. * | 02SNF. *, 02SPF. *, 02RGF. * |
| OFUE, OFVE | CO-EU | 02SNF. *, 02SPF. *, 02RGF. * | 02SNF. *, 02SPF. * |

Notes:

- The Ring portion of SRAS has been retired and is not available for new services.

- AC= Access Customer (POP), CO= Central Office, EU= End User

- & = the customer should use the “X” = Provider Engineered Reach Factor unless instructed to use a different valid Protocol Option by AT&T.

- This product does not allow for protection.  All NCI/SECNCI codes will start with an “02”

- “RG” which is used for a Regenerator is used only at a Central Office location and is treated like a “Muxing” code.

- Based on the orientation of the service being ordered the location configuration could be reversed (e.g., CO-EU could also be EU-CO).   The NCI and SECNCI could be swapped based on the orientation as well.

- For the 02SMF. *, 02SNF. * NCI codes, the “*” indicates any valid Muxing configuration per Protocol tables towards the end of this document in the SONET Table portion before the Retired portion.

- For Ring offerings at OC192 rate are described under the Dedicated SONET Ring product Matrix, external to the SONET Ring and Access Services matrix.

AT&T

Product/Offering

Title Page

For

SONET Xpress

(Retired ~ not available for new services)

Product/Offering ~ SONET Xpress

AT&T Midwest region

| NC Code | Product Description | Location Configuration | NCI | SEC NCI |
| --- | --- | --- | --- | --- |
| OB-- | Digital High Capacity, SONET - OC3 (155.520 Mbps) Point to Point | AC- EU | 02SOF.X, 04SOF.X & | 02SOF.X, 04SOF.X & |
| OB-C | Digital High Capacity, SONET - OC3 (155.520 Mbps) Point to Point ~ CO Mux | AC-CO | 02SOF.X, 04SOF.X & | 02SSF. +++, 04SSF. +++ 02SMF. *, 04SMF. * |
| OD-- % | Digital High Capacity SONET, OC12, 622.080 Mbps Point to Point | AC-AC EU-EU | 02SOF.X, 04SOF.X & | 02SOF.X, 04SOF.X & |
| OD-C | Digital High Capacity SONET, OC12, 622.080 Mbps Point to Point ~ CO Mux | AC-CO | 02SOF.X, 04SOF.X & | 02SSF. +++, 04SSF. +++ 02SMF. *, 04SMF. * |

Notes:

- SONET Xpress is retired from the AT&T product line.  Codes can still be used for existing service and for new service for those customers with capacity on their existing contract.

- % = this code is used for a standard OC12 when no SPEC code is used.  If there is a SPEC code of OPTNAC then this code represents an OC12 Optical Network Access Connection (NAC) not grouped nor sorted.

- This is only offered in the Prem-to-Prem configuration.  The A and the Z end of the service can be in the same “Prem”.

- SONET Xpress is only offered with optical interface handoffs.

- & = the customer should use the “X” = Provider Engineered Reach Factor unless instructed to use a different valid Protocol Option by AT&T.

- AT&T does not offer SONET with electrical handoffs (e.g., the “J” NC codes.  We use the Optical handoff “O” codes).

- For Collocation related coding for this product line, see OCN Point-to-Point matrix.

- Based on the orientation of the service being ordered the location configuration could be reversed (e.g., CO-EU could also be EU-CO).   The NCI and SECNCI could be swapped based on the orientation as well.

- For the 02SMF. *, 02SNF. *, 02SSF. +++ NCI codes, the “*” indicates any valid Muxing configuration per Protocol tables towards the end of this document in the SONET Table portion before the Retired portion.

# Text boxes

AT&T

TAB 15

SONET Codes