## Channelized Trunks

## Channelized Trunks® Service (Trunks) / Channelized Trunks® Service (DS1)

### Description

Channelized Trunks® Service is a flat rate channelized DS1 (1.544 Mbps circuit) service provisioned for voice grade quality service only.  Each DS1 has 24 channels, which transmit a rate of 64 Kbps.

Channelized Trunks is provisioned for three trunk types:

- Direct Inward Dial Trunks (DID)

  - Can have more than one number

  - No Inward Only without DID

- Outgoing only Private Branch exchange (PBX) Trunks

- Combination PBX Trunks

The DS1 can be configured as:

- AMI (Alternate Mark Inversion)

- B8ZS (Binary 8 Zero Substitution with Clear Channel Capability)

- SF (Super Frame)

- ESF (Extended Super Frame)

The DS1 work with:

- CNM-FlexServ® Service

- LightGate® Service

- SMARTPath®

- SMARTRing® Service

- MegaLink® Plus

Each analog trunk connect to a DS1 (1.544 Mbps) circuit, with a D4 Channel Bank or Digital cross Connect (DCS) in BellSouth’s Central Office (CO).  The CLEC is responsible for providing the equipment at the premises, which connects to the PBX equipment (D4 Channel Bank or Digital Trunk Interface Card)