Unbundled ADSL/HDSL Compatible Loop

CLEC Information Package

AT&T Southeast Region

Version 5

May 31, 2006

Table of Contents

1.	Introduction and Scope	3

2.	Contract Specific Provisions	3

3.	Revisions	4

4.	Service Description	5

5. 	Service Capabilities	5

6. 	Technical Requirements	6

6.1   ADSL Compatible loop	6

6.2   HDSL Compatible loop	6

7. 	Network Configuration	7

8. 	Ordering Scenarios	8

8.1 Electronic Ordering	8

8.1.1   Electronic Ordering without ULM	8

8.1.2   Electronic Ordering with ULM	9

8.1.3  ADSL/HDSL with Pre-Approved ULM - Electronic Ordering	10

8.2 Manual Ordering	10

8.2.1   LSR Manual Ordering without ULM	11

8.2.2   LSR Manual Ordering with Pre-Approved ULM	11

8.2.3   Service Inquiry (SI)/LSR Manual Ordering without ULM	11

8.2.4   SI/ LSR Manual Ordering with specified ULM	12

8.3. Ordering Scenarios Summary	12

9. 	Service Inquiry Requirements	12

10. 	NC/NCI Codes	13

11.  Rate Elements & USOCs	13

12.  Intervals	14

13.  Maintenance & Repair Procedures	14

14.  Acronyms	15

# 1.	Introduction and Scope

This Product Information Package is intended to provide to CLECs a product description and general ordering information specific to the UNE described herein.  Detailed ordering guidelines are provided in documents located on the Interconnection Web site.

This product information package is applicable in AT&T Alabama, AT&T Florida, AT&T Georgia, AT&T Kentucky, AT&T Louisiana, AT&T Mississippi, AT&T North Carolina, AT&T South Carolina and AT&T Tennessee (collectively referred to for purposes of this document as “AT&T Southeast Region and AT&T”).

The information contained in this document is subject to change.  AT&T will provide notification of changes to the document through the CLEC Notification Process.

Please contact your AT&T Local Support Manager, if you have any questions about the information contained herein.

# 2.	Contract Specific Provisions

Before the ADSL or HDSL Loops can be ordered, the CLEC must have an Interconnection Agreement that includes terms, conditions and rates for each loop type that is being requested.  This agreement must be in effect for all states where the CLEC plans to order these unbundled loops.

The information contained herein applies to the ADSL or HDSL Loop general offerings.  The general offering is in accordance with AT&T policies, procedures and regulatory obligations as well as the Standard Interconnection Agreement.

The general offering does not address specific contract issues within a CLEC’s Interconnection Agreement that may be different from the general offering.  Where specific contract issues differ from the information provided here, the contract provisions will prevail for the term of the specific CLEC Interconnection Agreement.  Otherwise, the general offering provisions will apply.

# 3.	Revisions

###### Version 5

- Contract Specific Provisions section moved to section 2.0

- Added  new section 8.1.2 Electronic Ordering with ULM.

- Deleted old section 9.1.2 ADSL/HDSL with Pre-Approved ULM – Electronic Ordering Interim Process since it is no longer available.

- Revised old section 9 Service Inquiry Requirements to reflect the removal of ICE as an option to submit ADSL/HDSL SIs (see Carrier Notification SN91086085)

###### Version 4

- Included new Section 2 Triennial Review Remand Order (TRRO) Exceptions

- Moved old Section 11 Contract Specific Provisions to new Section 3 Contract Specific Provisions

###### Version 3

- Section 7.1.2 is updated to show that Pre-Approved ULM Electronic Ordering Interim Process will not be available as of 08/26/04.

- Added section 7.1.3 to include the availability of electronic ordering for Pre-Approved ULM

- Updated the table in section 7.3 to reflect the changes in #1 and #2 above.

###### Version 2

- In ‘7.1 SI & LSR Firm Order Transmittal via ICE’ section, added interim instructions for using the Interconnection CLEC Enabler (ICE) web interface when ordering one of the Unbundled Loop Modification-Bridged Tap removal options.

- In ‘7.2 SI & LSR Firm Order Transmittal via CRSG’ section, new ‘Service Inquiry/Instructions for Preparing Service Inquiry’ dated 12/11/03 will be downloaded from this section.

# 4.	Service Description

The Unbundled Asymmetrical Digital Subscriber Line (ADSL) or the High Bit Rate Digital Subscriber Line (HDSL) Compatible Loop is a dedicated digital transmission facility from AT&T’s Main Distribution Frame (MDF) to an end-user’s premises.  These loops will be unloaded copper only loops.  The loop facility will include a Network Interface Device (NID) or equivalent demarcation point at the end-user’s location for the purpose of connecting the loop to the customer’s inside wire.

AT&T offers the following:

2 Wire ADSL Compatible Loop

2 Wire HDSL Compatible Loop

4 Wire HDSL Compatible Loop

# 5. 	Service Capabilities

AT&T will only provide the loop facilities with these offerings.  AT&T does not provide the Enhanced Electronics such as the Digital Subscriber Line Access Multiplexer (DSLAM) or any other electronics with the unbundled ADSL or HDSL Compatible Loops.

The ADSL/HDSL Compatible Loops will be designed circuits and are provisioned with test points.  AT&T will provide a Design Layout Record (DLR).

AT&T will perform installation testing (other than switch-based) that is needed to ensure the loop meets the specifications of Technical Reference 73600 (TR-73600)  Interconnection Services Technical Reference web site.

If the end-user’s existing facility can be re-used, AT&T will perform order coordination (OC) activities associated with Number Portability and/or the disconnect orders.  OC is intended to convert an existing customer to a new local service provider using the ADSL/HDSL Compatible Loops in a manner that minimizes the end-user’s dial-tone interruption.

Order Coordination – Time Specific is a chargeable option and allows the CLEC to order a specific time for OC to take place.  AT&T will make every effort to accommodate the specific conversion time request.

If the CLEC requests work after normal working hours, overtime rates will apply for work outside of 8:00 a.m. to 5:00 p.m. local time.

Unbundled ADSL/HDSL Loops are not available for purchase if the Loops will be used to provide telecommunications services to wireless cell sites or Mobile Telephone Switching Office (MTSO) locations.

The Unbundled ADSL & HDSL Loops will be delivered to the CLEC at its collocation space via a cross-connect ordered out of the Collocation offering.

# 6. 	Technical Requirements

## 6.1   ADSL Compatible loop

The ADSL Compatible Loop is a two wire metallic facility only.  If the loop is available, it will be provided with no Digital Loop Carrier (DLC), load coils or repeaters. These loops will conform to the Revised Resistance Design (RRD) guidelines for non-loaded facilities as described in Bellcore SR-TSV-002275.  The loop facility will consist of a loop 18kft or less which may include 6kft of bridge tap with a resistance of 1300 ohms or less if the loop is available.

Where the loop facility does not meet ADSL Compatible Loop specifications and it is determined that the loop can be modified to meet these specifications, the CLEC may request AT&T’s Unbundled Loop Modification (ULM).  In these situations and as a chargeable option, AT&T will use the ULM process to modify the loop facility to ADSL Compatible Loop specifications.  Refer to the Unbundled Loop Modification for Copper Loops CLEC Information Package located on the  Interconnection Services web site for additional ULM information.  The rates for ULM are in addition to the ADSL loop rate.

AT&T does not guarantee a particular bit rate associated with these loops.  The transmission and bit rate speed of ADSL type services is dependent on the CLEC’s equipment.

ADSL Compatible Loops will meet the parameters specified in the TR-73600.

## 6.2   HDSL Compatible loop

High-bit rate Digital Subscriber Line (HDSL) is a transport technology that can utilize a 2 or 4 Wire circuit.  The HDSL Compatible Loop can be ordered as a 2 Wire or 4 Wire HDSL Compatible Loop. The loop facility consists of only metallic facilities and will be provisioned according to CSA guidelines as described in Committee T1 Technical Report No. 28.  These loops include no more than 2500 feet of bridge tap/end section with a resistance of 850 ohms or less.

Where the loop facility does not meet HDSL Compatible Loop specifications and it is determined that the loop can be modified to meet these specifications, the CLEC may request AT&T’s ULM.  In these situations and as a chargeable option, AT&T will use the ULM process to modify the loop facility to HDSL Compatible Loop specifications. Refer to the Unbundled Loop Modification for Copper Loops CLEC Information Package located on the  Interconnection Services web site for additional ULM information. The rates for ULM are in addition to the HDSL loop rate.

AT&T does not guarantee a particular bit rate associated with these loops.  The bit rate speed is dependent upon the CLEC’s equipment.

HDSL Compatible Loops will meet the parameters specified in the TR-73600.

# 7. 	Network Configuration

# 8. 	Ordering Scenarios

This section will describe electronic and manual ordering scenarios available to the CLEC for ADSL or HDSL Compatible Loop ordering.

## 8.1 Electronic Ordering

When placing an order for a new facility, the CLEC must obtain a Loop Make-up (LMU) with a facility reservation number (FRN) prior to placing an electronic order.  The LMU with Facility Reservation Number (FRN) option enables the CLEC to receive LMU and reserve a loop facility.  For additional detail regarding the LMU/FRN process, refer to the LMU Product Package which is located on the  Interconnection Services web site.

The CLEC will use the FRN when it submits an electronic order for an ADSL or HDSL loop.  However, it should be noted that the specific loop type (ADSL or HDSL) ordered must match the specifications of the reserved facility for which the FRN has been obtained.  If the loop type the CLEC has ordered does not match the reserved facility, AT&T Provisioning will override the FRN and attempt to provision a facility that matches the specifications of the loop type ordered.  For information regarding ADSL and HDSL Loop technical specifications refer to the TR73600.

If the CLEC has verified that an existing facility to an end user is compatible for an ADSL or HDSL Loop, the CLEC may place the electronic order without obtaining a FRN.

The following sections will provide highlights of the various ordering scenarios for an ADSL or HDSL Loop electronic order with and without Unbundled Loop Modification (ULM).  For complete and detailed ordering information, refer to the  Local Ordering Handbook (LOH).

### 8.1.1   Electronic Ordering without ULM

New Facility (Pre-Order LMU/FRN required)

- Obtain LMU with FRN

- Populate the RESID field with the FRN

- Submit the electronic order

Reuse of Existing Facility

If the ADSL/HDSL loop being ordered is a reuse of an existing facility and the CLEC is certain that the facility is compatible to the loop type being ordered, it is not necessary to obtain a FRN.  The following applies:

- Prepare the electronic order and populate the RESID field with all “Xs”

- Submit the electronic order

###### Electronic Ordering (continued)

### 8.1.2   Electronic Ordering with ULM

CLECs now have the ability to electronically order loop modifications in conjunction with the ADSL or HDSL Loop order.  This will eliminate the need for a CLEC to submit a paper service inquiry (SI) for loop modifications.  There are two new fields on the electronic order which are summarized below.  For additional ordering details, refer to the Electronic Ordering of Loop Modification section in the LENS User Guide or the LOH.

- Loop Modification Type (LMT) Field

The LMT field identifies the loop changes involved in this service request. Only one field may be populated as follows:

- B – Remove all load coils

- D – Remove specified Bridged Taps

- G – Remove specified bridged taps and all load coils

- Bridged Tap Removal Location (BTRL) Field

The BTRL field must be populated if the LMT field is populated with D or G.  The BTRL field identifies the location of the bridged tap to be removed from the loop. This field is also used to indicate which of three groups of bridged tap removals this BTRL will fall under.

A label will appear above the BTRL dropdown menu that reads “Format B, C or D” CLEC must choose according to the following:

- Format B - BT <6000’ – This indicates that the CLEC is requesting that enough BT be removed to bring the total BT under 6000 feet.  When this option is chosen, no additional BTRL fields are to be populated.

- Format C - 2500 > BT <6000 – If this option is chosen the CLEC must populate at least one or more BTRL field (see Format A Fields below).   The CLEC may also choose to populate up to four (4) BTRL fields. This would allow the CLEC to remove four separate BTs by specifying one in each additional BTRL field.

- Format D - BT < 2500 feet – This option indicates that the CLEC wants to bring the BT down below 2500 feet.  This option triggers the special construction process.  All costs associated with removing the BTs specified should be billed as applicable.  The CLEC will populate additional BTRL fields (Format A fields) to specify the specific BTs to be removed up to a maximum of four.

Note: For additional details about Bridged Tap Removal requirements, refer to the ULM CLEC Information Package

Electronic Ordering (continued)

Format A Field

There are four (4) input text boxes available for entering a BRTL with Format A and will allow up to eleven (11) character alphanumeric and special characters as follows:

Position 1 & 2 are required and represent the kilofeet (kft) to be removed

        - Position 3 is always a decimal point.

        - Positions 4 & 5 represent factions of kilofeet of bridged tap to be removed or zero (0).

  - Position 6 is an alpha character and is always the symbol “@” and represents “at”.

  - Positions 7, 8 & 9 are numeric and represent the distance or location in kilofeet (kft) from the central office.

  - Position 10 is always a decimal point

  - Position 11 is numeric and represents the fraction of kilofeet of the distance or location from the central office or zero (0).

  - Example of a BTRL Format A field – 12.45 kft of BTRL at 789 kft from the CO:

| 1 | 2 | . | 4 | 5 | @ | 7 | 8 | 9 | . | 0 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

### 8.1.3  ADSL/HDSL with Pre-Approved ULM( - Electronic Ordering

Pre-Approved ULM option may be ordered on an electronic ADSL/HDSL Loop order.  Refer to the Unbundled Loop Modification CLEC Information Package for additional Pre-Approved ULM detail.

- Obtain LMU with FRN

- Populate the RESID field with the FRN

- Populate the SCA field with a Y.

- Submit the electronic order

## 8.2 Manual Ordering

The CLEC may submit ADSL and HDSL Loop manual orders by the following methods:

- Submit manual LSR directly to the LCSC – CLEC must obtain and review LMU, qualify the facility for the Loop based on LMU and obtain a FRN prior to the order (Pre-Order LMU).

- Submit Service Inquiry (SI) & LSR Firm Order – AT&T will qualify the facility for the ADSL or HDSL Loop; or CLEC is requesting specified ULM.

Manual Ordering (continued)

The following sections will provide ordering highlights for submitting an ADSL or HDSL Loop manual order ‘with’ and ‘without’ Unbundled Loop Modification.  For complete and detailed ordering information, refer to the LOH.

### 8.2.1   LSR Manual Ordering without ULM

New Facility

- Obtain LMU with FRN

- Input the FRN in the RMKS section of the LSR

- Submit the manual order LSR to the Local Carrier Service Center (LCSC)

- No SI required

Reuse of Existing Facility

If the ADSL/HDSL loop being ordered is a reuse of an existing facility and the CLEC is certain that the facility is compatible to the loop type being ordered, it is not necessary to obtain a FRN.  The following applies:

- Prepare the manual LSR business as usual for indicating a reuse of facility according to the guidelines in the LOH

- Submit the manual order LSR to the LCSC

- No SI required

### 8.2.2   LSR Manual Ordering with Pre-Approved ULM(

- Obtain LMU with FRN

- Input the FRN in the RMKS section of the LSR

- Populate SCA field with a “Y”

- Submit the manual order LSR to the Local Carrier Service Center (LCSC)

- No SI required

### 8.2.3   Service Inquiry (SI)/LSR Manual Ordering without ULM

- CLEC is not required to obtain a FRN since AT&T will qualify the facility for an ADSL or HDSL Loop.  AT&T will provide a FRN to the LCSC

- Prepare the LSR

- Prepare the SI according to the requirements in the Service Inquiry Requirements section 8.

Manual Ordering (continued)

### 8.2.4   SI/ LSR Manual Ordering with specified ULM(

- Obtain LMU with FRN

- Prepare the LSR

- Prepare the SI with the appropriate ULM information and include the FRN of the reserved facility according to the requirements in the Service Inquiry Requirements in section 8.

## 8.3. Ordering Scenarios Summary

| Ordering Scenario | Submission Method | CLEC Provided FRN | SCA field |
| --- | --- | --- | --- |
| Electronic Ordering without ULM | Electronic | FRN -- RESID field on LSR | NA |
| Electronic Ordering with ULM | Electronic | FRN – RESID field | NA |
| Electronic Ordering with Pre-Approved ULM | Electronic | FRN – RESID field | Y |
| LSR Manual Ordering without ULM (No SI required) | Submit to LCSC | FRN – RMKS section on LSR | NA |
| LSR Manual Ordering with Pre-Approved ULM (No SI required) | Submit to LCSC | FRN – RMKS section on LSR | Y |
| SI Manual Ordering without ULM | CSRG* | NA | NA |
| SI Manual Ordering with specified ULM | CSRG* | FRN on the SI Indicate BT and BT location on SI | NA |

* Note: See Service Inquiry Requirements section below for details.

# 9. 	Service Inquiry Requirements

A Service Inquiry/LSR is required dependent on the ordering scenarios described in the Ordering Scenarios section.  The CLEC may submit SIs by the following method:

- CLEC will prepare the SI:

- The CLEC will email the SI form to AT&T's CRSG at crsgune@bellsouth.com.  The CLEC will populate the PON number in the subject heading of the e-mail.

- SI receipt acknowledgement by AT&T will be in the same manner in which the CLEC submitted the SI.

# 10. 	NC/NCI Codes

| Loop Type | NC | NCI2 at CLEC | SEC NCI2 at End User |
| --- | --- | --- | --- |
| 2 Wire ADSL | LXR- | 02QB9.00A | 02DU9.00A |
| 2 Wire HDSL | LXC- | 02QB9.00H | 02DU9.00H |
| 2 Wire HDSL1 | LXC | 02QB9.004 | 02DU9.004 |
| 4 Wire HDSL3 | LXC- | 04QB9.00H | 04DU9.00H |

1 Optional NCI code that can be used for a 2 Wire HDSL at the discretion of the CLEC – currently, this NCI code is only available to be used with an order placed manually.

2 “0” is a numeric zero character

3 Orders for 4 Wire HDSL must include two CLEC cable and pairs on the LSR.

# 11.  Rate Elements & USOCs

Rates for ADSL and HDSL Compatible Loops must be in the CLEC’s Interconnection Agreement.  Rates will vary by state according to local state commission orders and filed cost studies.

| Rate Element | USOC |
| --- | --- |
| 2 Wire Unbundled ADSL Compatible Loop, includes manual service inquiry and facility reservation | UAL2X |
| 2 Wire Unbundled ADSL Compatible Loop, without manual service inquiry and facility reservation | UAL2W |
| 2 Wire Unbundled HDSL Compatible Loop, includes manual service inquiry and facility reservation | UHL2X |
| 2 Wire Unbundled HDSL Compatible Loop, without manual service inquiry and facility reservation | UHL2W |
| 4 Wire Unbundled HDSL Compatible Loop, includes manual service inquiry and facility reservation | UHL4X |
| 4 Wire Unbundled HDSL Compatible Loop, without manual service inquiry and facility reservation | UHL4W |
| Order Coordination – Time Specific (per order) | OCOSL |

###### Other Non-Recurring Charges

Expedite Charge – applies if CLEC requests an order interval less than the stated “standard interval” in the Products and Services Interval Guide.

Manual Service Order – applies if order is manually submitted

Electronic Service Order – applies if order is submitted electronically

Order Cancellation – applies if the CLEC cancels an order.  This charge is for work associated with provisioning either ADSL or HDSL loop pairs at the time the CLEC cancels an order.

Service Order Modification Charge – Applies if the CLEC modifies a service order after the Firm Order Confirmation has been issued.

Overtime Charge – Applies for work requested outside of normal working hours.

Time & Material – Applies for CLEC requested dispatch, (outside the central office) if “no trouble found”

# 12.  Intervals

Provisioning intervals for ADSL/HDSL loops can be found in the Interval Guide section of the LOH.

# 13.  Maintenance & Repair Procedures

The CLEC is responsible for testing and pre-screening any trouble conditions to make sure the trouble is with ADSL/HDSL Compatible Loop pair before calling AT&T.  If the CLEC’s testing isolates the repair problem to AT&T’s unbundled loop, the CLEC should notify the Customer Wholesale Interconnection Network Services (CWINS) Center.

The CLEC must provide the following information to CWINS Center when reporting a repair problem:

- ADSL/HDSL pair Circuit ID

- Description of the trouble

If AT&T dispatches a technician on a CLEC reported trouble call and no ADSL /HDSL loop trouble is found, AT&T will charge the CLEC for time spent on the dispatch and for time spent testing the ADSL or HDSL Compatible Loop.

AT&T UNE Maintenance Targets are used for the service repair target intervals.  The Maintenance Target Intervals can be found in the  Operational Understanding Guide in Appendix B.

# 14.  Acronyms

ADSL	Asymmetrical Digital Subscriber Line

BTRL	Bridged Tap Removal Location

CDP	Clear Defective Pair

CLEC	Competitive Local Exchange Carrier

CLLI	Common Language Location Identifier

CRSG	Complex Resale Support Group

DLC	Digital Loop Carrier

DLR	Design Layout Record

DSLAM	Digital Subscriber Line Access Multiplexer

ECD	Estimated Completion Date

EE	Enhanced Electronic

FOC	Firm Order Confirmation

FRN	Facility Reservation Number

HDSL	High Bit Rate Digital Subscriber Line

ICE	Interconnection CLEC Enabler

ID	Identification

LCSC	Local Carrier Service Center

LMT	Loop Modification Type

LMU	Loop Make-up

LSOGv2	Local Service Ordering Guidelines version 2

LSOGv4	Local Service Ordering Guidelines version 4

LSR	Local Service Request

LST	Line & Station Transfer

MDF	Main Distribution Frame

NC	Network Channel

NCI	Network Channel Interface

NID	Network Interface Device

OBF	Ordering & Billing Forum

OC	Order Coordination

OSPE	Outside Plant Engineering

PON	Purchase Order Number

RESID	Reservation Identification

###### Acronyms (continued)

RRD	Revised Resistance Design

SC	Special Construction

SECNCI	Secondary Network Channel Interface

SI	Service Inquiry

TR73600	Technical Reference 73600

UCL/L	Unbundled Copper Loop/Long

UCL/S	Unbundled Copper Loop/Short

ULM	Unbundled Loop Modification

ULM-BT	Bridged Tap

ULM-LC	Load Coil

UNE	Unbundled Network Element

USOC	Universal Service Order Code

# Footnotes

( Note: AT&T will attempt to perform a pair change in lieu of ULM.  If a pair change is feasible, the facility provisioned will meet or exceed specifications of the requested loop modification.  The standard interval for the ADSL or HDSL Loop will be applied and will begin at the time the service order is updated to indicate “pair change in lieu of ULM”.  If a pair change is performed, the CLEC will not be charged for ULM.

( Note: AT&T will attempt to perform a pair change in lieu of ULM.  If a pair change is feasible, the facility provisioned will meet or exceed specifications of the requested loop modification.  The standard interval for the ADSL or HDSL Loop will be applied and will begin at the time the service order is updated to indicate “pair change in lieu of ULM”.  If a pair change is performed, the CLEC will not be charged for ULM.

( Note: AT&T will attempt to perform a pair change in lieu of ULM.  If a pair change is feasible, the facility provisioned will meet or exceed specifications of the requested loop modification.  The standard interval for the ADSL or HDSL Loop will be applied and will begin at the time the service order is updated to indicate “pair change in lieu of ULM”.  If a pair change is performed, the CLEC will not be charged for ULM.