Unbundled Voice Loop – SL2

CLEC Information Package

AT&T Southeast Region

(Version 2)

Table of Contents

Introduction & Scope	3

Revisions	4

Version 2	4

Service Capabilities	5

Technical Requirements	5

Network Configuration	6

Ordering	7

Service Order Requirements	7

Rate Elements & USOCs	8

Intervals	8

Maintenance & Repair Procedures	9

Contract Specific Provisions	9

Acronyms	10

# Introduction & Scope

This Product Information Package is intended to provide to CLECs a product description and general ordering information specific to the UNE described herein.  Detailed ordering guidelines are provided in documents located on the Interconnection Web site.

This product information package is applicable in AT&T Alabama, AT&T Florida, AT&T Georgia, AT&T Kentucky, AT&T Louisiana, AT&T Mississippi, AT&T North Carolina, AT&T South Carolina and AT&T Tennessee (collectively referred to for purposes of this document as “AT&T Southeast Region and AT&T”).

The information contained in this document is subject to change.  AT&T will provide notification of changes to the document through the CLEC Notification Process.

Please contact your AT&T Local Support Manager, if you have any questions about the information contained herein.

# Revisions

## Version 2

- Service Capabilities section: Added the “Loop Tagging” option to the last paragraph.

- Ordering section; Service Order Requirements sub-section: added the “Remarks” field to the “LSR Field” column; added the “Loop Tagging Requested” to the “Information Required” column.

Rate Elements & USOCs section: Added the Loop Tagging USOC.

# Service Description

The voice grade Unbundled Voice Loop – Service Level 2 (UVL - SL2) is a dedicated analog transmission facility from AT&T’s main distribution frame (MDF) to an end user’s premises.  This facility will allow an end user to send and receive normal voice telecommunications traffic when it is connected to a dial-tone-providing switch. This facility will include a Network Interface Device (NID) at the customer’s location for the purpose of connecting the loop to the customer’s inside wire.

# Service Capabilities

The UVL - SL2 loop is a designed circuit.  It will include a Design Layout Record (DLR) and will be provisioned with test points.

AT&T will perform installation testing (other than switch-based) that is needed to ensure the loop meets the specifications as described in Technical Reference (TR) 73600.

Order Coordination (OC) will be provided and is included in the non-recurring cost of the loop.  The purpose of OC is to minimize dial tone interruption by coordinating the UVL - SL2 installation with the disconnect of an existing end-user’s service and/or number portability service.  Order Coordination-Time Specific (OC-TS) is also offered as a chargeable option.  OC-TS allows the CLEC to specify the time that the coordinated conversion will take place.

For an additional one-time charge, AT&T will ensure that the UVL-SL2 loop is tagged during the provisioning process.  Tagging on the loop will include the CLEC name and the Circuit ID Number.  Loop Tagging is only available on manual orders at this time.

# Technical Requirements

The UVL - SL2 loop can be configured as a 2 Wire or 4 Wire circuit.  The 2 Wire circuit can be provisioned with loop start, ground start or reverse battery signaling.  The 4 Wire circuit can be provided with loop-start or ground start signaling.

The CLEC may provision any telecommunications service over the UVL - SL2 loop so long as those services are consistent with industry standards and do not adversely affect other services.  However, the UVL - SL2 loop offerings are intended for analog voice grade services and accordingly will be provisioned, maintained and repaired in a manner that supports voice grade service.

The UVL - SL2 loop will meet technical specifications described in TR73600.

# Network Configuration

# Ordering

The CLEC will submit the Local Service Request (LSR) form to the Local Carrier Service Center (LCSC) for processing UVL - SL2 loops

## Service Order Requirements

The CLEC will complete and submit a LSR form according to Local Ordering Handbook (LOH).

The following information that is unique to UVL - SL2 is also required on the LSR:

| LSR Field | Information Required |
| --- | --- |
| NC/NCI | Loop Type | NC | NCI at CLEC* | SEC NCI at End User* |
|  | 2 Wire UVL - SL2, Loop Start | LY-- | 02QC3.OOD | 02LS2 |
|  | 2 Wire UVL - SL2, Ground Start | LY-- | 02QC3.OOB | 02GS2 |
|  | 2 Wire UVL - SL2, Reverse Battery | LY-- | 02QC3.RVO | 02RV2.T |
|  | 4 Wire UVL - SL2, Loop Start | LY-- | 04QC2.OOD | 04LS2 |
|  | 4 Wire UVL - SL2, Ground Start | LY-- | 04QC2.OOB | 04GS2 |
| Remarks (Manual only) | For a Loop Tagging request add the following: Loop Tagging Requested |

*  “0” is a numeric zero character

*  “O” is an alpha (letter O)

# Rate Elements & USOCs

Rates, terms and conditions for UVL – SL2 loops will need to be included in the CLEC’s Interconnection Agreement prior to issuing an UVL-SL2 order.  Rates may be interim and subject to true up pending approval of final rates by the respective State Commissions.  Commission orders will specify the dates back to which true-ups are applicable.

| Rate Element | USOC |
| --- | --- |
| 2 Wire UVL – SL2, Loop Start or Ground Start Signaling | UEAL2 |
| 2 Wire UVL – SL2, Reverse Battery Signaling | UEAR2 |
| 4 Wire UVL – SL2, Loop Start or Ground Start Signaling | UEAL4 |
| Unbundled Miscellaneous Rate Element, Tag Loop at End User Premises | URETL |
| Order Coordination – Time Specific (per LSR) | OCOSL |

###### Other Non-Recurring Charges

Expedite Charges – applies if CLEC requests order interval less than the stated “standard interval” in the Interval Guide.

Manual Service Order -- applies if order is manually submitted and electronic ordering is available.

Order Cancellation – applies if the CLEC cancels an order after the Firm Order Confirmation (FOC) has been issued.

Service Order Modification Charge – applies if the CLEC modifies a service order after the Firm Order Confirmation has been issued.

Overtime Charge – applies for work requested outside of normal working hours.  Normal working hours for provisioning work are between 8 a.m. and 5 p.m. local time.

Time & Material – applies for dispatch outside the central office if “no trouble found”.

# Intervals

Provisioning intervals for UVL – SL2 loops can be found in the Interval Guide in the  LOH. .

# Maintenance & Repair Procedures

The CLEC is responsible for testing and pre-screening any trouble conditions to make sure the trouble is with the UVL – SL2 loop before calling AT&T.  If the CLEC’s testing isolates the repair problem to AT&T’s unbundled loop, the CLEC should notify the Customer Wholesale Interconnection Network Services (CWINS) Center.  The CLEC will provide the results of the CLEC test which indicates a problem on the UVL – SL2.

The CLEC must provide the following information to UNE Center when reporting a repair problem:

- UVL - SL2 pair Circuit ID

- Description of the trouble

If AT&T must dispatch a technician outside the central office on a CLEC reported trouble call and no trouble is found on the UVL-SL2, AT&T will charge the CLEC for time spent on the dispatch and for time spent testing the UVL – SL2 loop.

# Contract Specific Provisions

Before any UVL – SL2 loop can be ordered, the CLEC must have an Interconnection Agreement that includes terms, conditions and rates for each loop type that is being requested.  This agreement must be in effect for all states where the CLEC plans to order these unbundled loops.

The information contained herein applies to the UVL – SL2 general offering and is part the standard AT&T agreement.  The general offering is in accordance with AT&T policies, procedures and regulatory obligations as well as the Standard Interconnection Agreement.

The general offering does not address specific contract issues within a CLEC’s Interconnection Agreement that may be different from the general offering.  Where specific contract issues differ from the information provided here, the contract provisions will prevail for the term of the specific CLEC Interconnection Agreement.  Otherwise, the general offering provisions will apply.

# Acronyms

| CLEC | Competitive Local Exchange Carrier |
| --- | --- |
| CWINS | Customer Wholesale Interconnection Network Service |
| DLR | Design Layout Record |
| FOC | Firm Order Confirmation |
| LCSC | Local Carrier Service Center |
| LSR | Local Service Request |
| MDF | Main Distribution Frame |
| NC | Network Channel |
| NCI | Network Channel Interface |
| NID | Network Interface Device |
| OC | Order Coordination |
| OC-TS | Order Coordination – Time Specific |
| TR73600 | Technical Reference 73600 |
| UVL – SL2 | Unbundled Voice Loop – Service Level 2 |