Unbundled Sub-Loop (USL)(Distribution Facility)

CLEC Information Package

AT&T Southeast Region

Version 1

Table of Contents

1.  Introduction & Scope	3

2.  Service Description	4

3.  Service Capabilities	4

4.  Technical Requirements	5

5. Network Configuration	5

5.1 Field Cross-Connect Configuration	5

5.2 Building Equipment Room Configuration	6

6.  Ordering & Provisioning	7

6.1.	Service Inquiry/Site Setup	7

6.2.	Ordering USL Pairs	8

6.3.	Ordering USL Pairs with Modifications	8

7.  Rate Elements & USOCs	9

8.  Other Non-Recurring Charges	10

9.  Intervals	10

10.  Maintenance & Repair Procedures	10

11.  Contract Specific Provisions	11

12.  Acronyms	12

# 1.  Introduction & Scope

This Product Information Package is intended to provide CLECs with the product description and general ordering information to the Unbundled Network Element (UNE) described herein.

The information contained in this document is subject to change.  AT&T will provide notification of changes to the document through the CLEC Notification Process.

This product information package is applicable in AT&T Alabama, AT&T Florida, AT&T Georgia, AT&T Kentucky, AT&T Louisiana, AT&T Mississippi, AT&T North Carolina, AT&T South Carolina and AT&T Tennessee (collectively referred to for purposes of this document as “AT&T Southeast Region and AT&T”).

Please contact your AT&T Local Support Manager (LSM), if you have any questions about the information contained herein.

# 2.  Service Description

The Unbundled Sub-Loop  (USL) UNE is the distribution portion of AT&T’s cable facilities and is comprised of copper twisted pairs. The USL is a dedicated transmission facility that AT&T provides from a AT&T cross connect device to a customer’s point of demarcation.  The AT&T cross-connect device may be located within a remote terminal (RT) or a stand-alone cross-box in the field or in the equipment room of a building.  AT&T will make the following USL offerings available where facilities exist:

- Unbundled Sub-Loop-Distribution (USL-D) 
USL-D is a voice grade facility from the cross-box in the field up to and including the end-user’s point of demarcation.  USL-D can be configured as 2-Wire (2W) or 4-Wire (4W) voice grade facilities and are non-designed circuits.

- Unbundled Sub-Loop– Intrabuilding Network Cable (USL-INC) 
USL-INC (a.k.a. Riser Cable) is a non-designed facility from the cross-connect device in the building equipment room up to and including the end-user’s point of demarcation.  USL-INC is the distribution facility inside a subscribers’ buildings or between buildings on one customer’s same premises (continuous property not separated by a public street or road).

- Unbundled Copper Sub-Loop (UCSL) 
UCSL is a non-designed “non-loaded copper facility” from the cross-box in the field up to and including the end user's point of demarcation.  If available, this facility will not have any intervening equipment such as load coils, repeaters, etc. between the end user and the cross-box.  UCSL will be non-designed and will not be provisioned with a Design Layout Record (DLR) or a test point.

# 3.  Service Capabilities

Loop Testing is a chargeable option the CLEC may use to test the loop.  The request for Loop Testing must be included on the Local Service Request (LSR) form.

Order Coordination (OC) is required when reuse of existing facilities that are currently serving an end user has been requested by the CLEC.  The purpose of the OC is to convert an existing facility to the CLEC’s service in a manner that minimizes dial-tone interruption for the end user.

The CLEC may request AT&T’s Unbundled Loop Modification (ULM) to condition a copper sub-loop loop as a UCSL.

CLEC cannot use AT&T USL UNE facilities to provision to wireless cell sites or Mobile Telephone Switching Offices (MTSO).

The USL UNEs are not intended to support any particular service.  CLECs may use USL UNEs to provide telecommunication services dependent upon the CLEC’s equipment and its transmission facility, so long as those services are consistent with industry standards and do not disrupt other services on the AT&T network.

# 4.  Technical Requirements

The Unbundled Sub-Loop (USL) may be provisioned as a 2 Wire / 4 Wire Copper Loop.  The USL technical specifications are documented in the Technical Reference 73600 (TR-73600).

# 5. Network Configuration

## 5.1 Field Cross-Connect Configuration

Cross-connect device – AT&T Remote Terminal or stand alone cross-box

## 5.2 Building Equipment Room Configuration

Cross-connect device – Building Equipment Room

# 6.  Ordering & Provisioning

Before USL pairs can be ordered, a Service Inquiry (SI) is required to determine if existing facilities are available in the cross-connect device (at the requested address) to perform the site set-up.  If existing capacity in the cross-connect device is not sufficient to perform the site set-up work, the CLEC may request a quote for AT&T’s Special Construction (SC) process.  If SC is feasible and a SC quote is provided, the CLEC may either proceed with the SC process or decline.  In any event, the CLEC will be charged for the time spent on the SC quote.

The CLEC must also have its facilities in place before AT&T can begin the site set-up.  Therefore, the CLEC must deliver its feeder facilities in 25 pair increments to the AT&T cross-connect device.

## Service Inquiry/Site Setup

- CLEC submits the SI to the CRSGUNE@bellsouth.com email address.

- Refer to the USL Service Inquiry and Instructions below for the SI and Instructions.

- If USL facilities are available and the CLEC has delivered its feeder facilities up to the cross-connect device, AT&T Outside Plant Engineering (OSPE) will complete the site set-up work.  (OSPE will not check to see if any loops conform to USL specifications on the setup SI.)

- The site set-up includes splicing the CLEC cable and connecting the cable to the cross-connect panel in the cross-connect device or on a separate cross-connect panel if access to sub-loops is inside a building equipment room.  (Set-up charges are separate from the monthly recurring and non-recurring charges for the USL pairs.)

    - If the CLEC desires to access USL-INC (Riser Cable), a separate cross-connect block will be installed in 25 pair increments in the building equipment room.  The cross-connect block will be used to cross connect the requested USL-INC pair(s) for the CLEC to access.  The CLEC is responsible for terminating its facilities on the cross-connect block.

    - Once site set-up is completed, the SI will be sent to the LCSC to issue an order to bill the CLEC for the set-up.

    - The SI will also be returned to the CLEC.  The CLEC will use the cable and pair ranges from the SI when ordering the USL pairs.

    - If the CLEC exhausts all of its meet point in the cable and pair range assigned on the SI, then a new SI must be submitted to establish more meet points.

## Ordering USL Pairs

Once the set-up is complete, the CLEC may begin ordering the USL pairs.  To order USL pairs, the CLEC will complete the Local Service Request (LSR) form according to the  Local Ordering Handbook (LOH).

Additionally, the following information is unique to USL and must be included on the LSR:

| LSR Field | USL Information |
| --- | --- |
| NC (2 Wire) | TXCT |
| NC (4 Wire) | TXCF |
| NCI | NA (Not Needed – Non-Design) |
| SECNCI | NA (Not Needed – Non-Design) |
| Cable ID Field* | USL-D or UCSL: X, 3 character ACNA of the CLEC and the Cable Number USL-INC: Z, 3 character ACNA of the CLEC and the Cable Number |

* NOTE:  Cable ID Field is 5 characters.  The first character of the Cable ID is always an “X” or “ Z” (denotes a Cross-Box), the second/third and fourth character of the Cable ID is CLEC’s unique 3 character ACNA code and fifth character is the cable number assigned by AT&T OSPE and provided to the CLEC on the SI form.

## Ordering USL Pairs with Modifications

The CLEC may request AT&T’s Unbundled Loop Modification (ULM) process to condition a copper sub-loop facility as a UCSL by specifying ULM options using a Service Inquiry (SI).

For additional ULM information, refer to the Unbundled Loop Modification for Copper Loops CLEC Information Package that can be found on the Unbundled Network Elements (UNEs) Guides web site.

The CLEC must submit the ULM request on a Service Inquiry (SI).  Following are the requirements for submitting a SI.

- CLEC will prepare the SI request and the LSR for the UCSL pair(s).

- Refer to the New UCSL-2W or UCSL-4W Loop Modification and Loop Request Service Inquiry/Instructions for Preparing Service Inquiry for the SI.

- CLEC sends the SI and LSR Firm Order to the CRSG UNE Team.

- Send the SI to the CRSGUNE@bellsouth.com email address.

# 7.  Rate Elements & USOCs

Terms, conditions, rate elements and rates must be included in the CLEC’s Interconnection Agreement before USL UNEs can be ordered.

| USL-D |
| --- |
| USOC | USL-D |
| USBN2 | Loop Distribution per 2-Wire Analog VG Loop (includes Riser Cable), per month |
| USNB4 | Loop Distribution per 4-Wire Analog VG Loop (includes Riser Cable), per month |
| USBSA | NRC – Set-Up per Cross Box location in the field – CLEC Feeder Facility Set-Up |
| USBSB | NRC – Set-Up per Cross Box location in the field – per 25 pair panel set-up |

| USOC | USL-INC USOC DESCRIPTION |
| --- | --- |
| USBR2 | Loop Distribution per 2 Wire Analog VG Loop (includes Riser Cable), per month |
| USBR4 | Loop Distribution per 4-Wire Analog VG Loop (includes Riser Cable), per month |
| USBSC | NRC – Set-Up per Building Equipment Room – CLEC Feeder Facility set-up |
| USBSD | NRC – Set-Up per Building Equipment Room – per 25 pair panel set-up |

| USOC | USL-INC USOC (GA) DESCRIPTION |
| --- | --- |
| USBRA | Unbundled Intrabuilding Network Cable (Riser), 2 Wire Set-Up |
| USBRB | Unbundled Intrabuilding Network Cable (Riser), 4 Wire Set-Up |
| USBRC | Unbundled Sub-Loops, Riser, 2-Wire per Loop, Working and Spare Loop Activation (Georgia) |
| USBRD | Unbundled Sub-Loops, Riser, 4-Wire per Loop, Working and Spare Loop Activation (Georgia) |

| USOC | UCSL USOC DESCRIPTION |
| --- | --- |
| UCS2X | Loop Distribution per 2-W Unbundled Copper Sub-Loop, per month |
| UCS4X | Loop Distribution per 4-Wire Unbundled Copper Sub-Loop, per month |
| USBSA | NRC – Set-Up per Cross Box location in the field – CLEC Feeder Facility Set-Up |
| USBSB | NRC – Set-Up per Cross Box location in the field – per 25 pair panel set-up |

# 8.  Other Non-Recurring Charges

Expedite Charges – Applies if CLEC requests order interval less than the stated standard interval.

Manual Service Order – Applies if order is submitted manually.

Electronic Service Order – Applies if order is submitted electronically.

Order Cancellation – Applies if the CLEC cancels an order after the Firm Order Confirmation (FOC) has been issued.

Service Order Modification Charge – Applies if the CLEC modifies a service order after the Firm Order Confirmation has been issued.

Overtime Charge – Applies for work requested outside of normal working hours.

Time and Material – Applies for CLEC requested dispatch, (outside central office), if “No Trouble found” (NTF).

# 9.  Intervals

Provisioning intervals for USL UNEs can be found in the Interval Guide in the LOH..

# 10.  Maintenance & Repair Procedures

The CLEC is responsible for testing and pre-screening any trouble conditions to make sure the trouble is with the USL pair before calling AT&T.  If the CLEC’s testing isolates the repair problem to the USL pair, the CLEC should notify the Customer Wholesale Interconnection Network Services (CWINS) Center.

The CLEC must provide the following information to CWINS Center when reporting a repair problem:

- USL pair Circuit ID

- Description of the trouble

If AT&T dispatches a technician on a CLEC reported trouble call and no USL trouble is found, AT&T will charge the CLEC for time spent on the dispatch and for time spent testing the USL pair.

AT&T UNE Maintenance Targets are used for the service repair target intervals.  The Maintenance Target Intervals can be found in the Operational Understanding Guide  in Appendix B.

# 11.  Contract Specific Provisions

Before USL UNEs can be ordered, the CLEC must have an Interconnection Agreement that includes the USL terms, conditions and rates.  This agreement must be in effect for all states where the CLEC plans to order USL.

The general offering is in accordance with AT&T policies, procedures and regulatory obligations as well as the standard AT&T Interconnection Agreement.

The general offering does not address specific contract issues within a CLEC’s Interconnection Agreement that may be different from the general offering.  Where specific contract issues differ from the information provided here, the contract provisions would prevail for the term of the specific CLEC Interconnection Agreement.  Otherwise, the general offering provisions will apply.

# 12.  Acronyms

ACNA					Access Carrier Name

CLEC					Competitive Local Exchange Carrier

CRSG					Complex Resale Support Group

CWINS				Customer Wholesale Interconnection Networks Systems

DLR					Design Layout Record

FOC					Firm Order Confirmation

ID					Identification

LCSC					Local Carrier Service Center

LSM					Local Support Manager

LSR					Local Service Request

MTSO					Mobile Telephone Switching Office

NC 					Network Channel

NCI					Network Channel Interface

NID					Network Interface Device

NTF					No Trouble Found

OC					Order Coordination

OSPE					Outside Plant Engineer

RT					Remote Terminal

SECNCI				Secondary Network Channel Interface

SI					Service Inquiry

TR73600				Technical Reference 73600

UCSL					Unbundled Copper Sub-Loop

ULM					Unbundled Loop Modifications

UNE					Unbundled Network Element

USL					Unbundled Sub-Loop

USL-D					Unbundled Sub-Loop – Distribution

USL-INC				Unbundled Sub-Loop – Intrabuilding Network Cable

USOC					Universal Service Order Code

2W					2 Wire

4W					4 Wire

# Text boxes

# Cross- Connects

Access to sub-loops on spare binding posts on existing panel

# Existing AT&T Cross-Box

CLEC

FEEDER

CLEC RT or Cross-Box

NID

NID

NID

##### NID

NID

Existing

Dist.

Cross

Connect

Panel

USL

#### CLEC 25 pair Complement

Existing

AT&T Feeder

Cross

Connect Panel

Cross Connects

Panel installed as part of set-up for access to USL-INC

CLEC 25 pair complement

CLEC

FEEDER

CLEC RT or Cross Box

SUB-LOOPS

# Cross connects

Exist. Dist. Cross

Connect Panel

New AT&T Feeder Cross

Connect Panel

Existing AT&T Building

Terminal XBOX

NID

NID

NID

NID

NID