# Unbundled Dedicated Transport –

# Currently Combined UNE Combinations

# CLEC Information Package

# March 16, 2009

# Version 16

# Table of Contents

Scope	4

Product Name	4

Product Category	4

Product and Technical Description	4

Service Description	4

Features and Benefits	4

Basic Service Capabilities	5

Commingling	5

Service Rearrangements	6

Pre-Ordering Checklist	7

Availability	7

Billing Information	8

ORDERING INFORMATION	9

Ordering Process Description	9

Required Fields by Form	10

Critical Fields and Entries	11

Any Applicable USOCs and/or FIDs	17

Pricing	18

Intervals	18

Provisioning	18

Maintenance and Repair Process	18

| Version Number | Date | Change |
| --- | --- | --- |
| 1 | 05/21/02 | Initial Version |
| 2 | 06/20/02 | Added configuration 56-58 to Critical Fields table. General editing. Clarified any currently combined network elements may be converted. Rules apply to Special Access loop transport combinations. |
| 3 | 08/02/02 | In Critical Fields and Entries: correct codes for 1, 19, 44, 49-55; delete configurations 36-38; add picture for 40, add 41-42 configurations. Add Note regarding TOS code in Required Fields section. |
| 4 | 08/27/02 | In Critical Fields and Entries, add configuration 42. Update to reflect policy that this service is not available to wireless companies. |
| 5 | 09/19/02 | In Critical Fields and Entries: insert label for channelized facilities and delete 55-57. |
| 6 | 09/30/02 | In Critical Fields and Entries: corrected NCI code for DS3 Local Channel in items 12 and 42. |
| 7 | 11/01/02 | In Critical Fields and Entries: corrected code for DS1 Local Channel in items 5, 8, 11, 21, 30, 38, 39, 40, 41, and 47. |
| 8 | 05/15/03 | Added copy of certification letter, service rearrangement information |
| 9 | 06/09/05 | Update with TRO/TRRO information and offer multiple bandwidth commingling of SPA. |
| 10 | 09/30/05 | Update to reflect the addition of SWA and SBWC support. |
| 11 | 01/27/06 | Include conversion to single bandwidth spreadsheet commingling form |
| 12 | 03/28/06 | Include corrected single bandwidth spreadsheet commingling form |
| 13 | 10/02/06 | Update the Service Rearragement spreadsheet. Update Critical Fields and Entries table and schematics to reflect the TRO/TRRO . |
| 14 | 07/14/06 | Update name change of BellSouth to AT&T and the UNE to EEL spreadsheet. Also a new spreadsheet process that will allow a Facility-based CLEC to send the conversion spreadsheet within this package to the account team rather than to the CLEC Care group |
| 15 | 07/17/08 | In Required Fields by Form section, additional information required on the Remarks Section of the LSR. |
| 16 | 03/16/09 | Replace “Account Team/Local Contract Manager” with LSC. |

# Scope

This document is provided to CLECs as information regarding conversion of facilities consisting of currently combined wholesale combinations to facilities consisting of unbundled network elements (UNEs) or commingled facilities or visa versa.

This product information package is applicable in AT&T Alabama, AT&T Florida, AT&T Georgia, AT&T Kentucky, AT&T Louisiana, AT&T Mississippi, AT&T North Carolina, AT&T South Carolina and AT&T Tennessee.

# Product Name

Currently Combined UNE/Commingled Combinations

# Product Category

# Unbundled High Capacity Loop and Dedicated Transport

# Product and Technical Description

## Service Description

Where necessary to comply with an effective FCC and/or State Commission order, AT&T will convert currently combined wholesale transport combinations to combinations of unbundled network elements.  The use of UNE elements exclusively for the provisioning of telecommunications services in the mobile wireless and long distance markets is prohibited.

## Features and Benefits

High Capacity Loop/Dedicated transport is a point-to-point service and may consist of the following: Local Channel, Interoffice Channel and Local Loops.  Channelization may or may not be present.

The following definitions apply to the elements:

- Local Channel is the transport facility between the customer’s Point of Presence (POP) and the POP Serving Wire Center.  AT&T is no longer obligated to provide entrance facilities (Local Channels).

- Interoffice Channel is a network element that provides a dedicated point-to-point transmission path and its associated electronics between AT&T wire centers.

- Local Loop (Subscriber Line) is a network element that provides a transmission facility between a distribution frame in a AT&T Serving Wire Center (SWC) and the network interface device (NID) at the end user premises

- Channelization is an optional functionality performed when a higher-level facility is separated into lower level services, e.g. DS3 to 28 DS1s or DS1 to 24 DS0s.  Channelization can be accomplished through the use of a multiplexer or a Digital Cross-connect System (DCS).  Once the basic channelization system has been installed, channels can be activated all at once or on an as-needed basis.   Channelization is available on a limited basis as described in NECA 4 tariff.

The elements above may be combined to form local loop/transport combinations at TELRIC rates known as Enhanced Extended Links (EELs).  AT&T is no longer obligated to provide unbundled local channels, also known as entrance facilities.  Transport as defined within the TRO consists of Interoffice Channel.  Therefore, there is one UNE EEL configurations: (1) Local Loop + Interoffice Channel.

The main benefits of requesting currently combined network elements to be converted to unbundled network elements is cost savings due to the difference in price.

Voice Grade, DS0, DS1, DS3, and STS-1 facilities are supported as unbundled network elements, although DS1, DS3 and STS-1 facilities are not available as UNEs in certain wire centers or on certain routes.

## Basic Service Capabilities

If requested, AT&T will convert currently combined wholesale tariff services within its network to unbundled network elements where those elements are available as UNEs.   Wholesale tariff circuit will not be converted to a UNE (or UNE combination) if the conversion would result in the CLEC exceeding the maximum number of UNEs available on a particular route or at a particular location, as described in the interconnection agreement.  Service eligibility criteria set forth in the interconnection agreement apply to the conversion of AT&T wholesale tariff services (Special Access) to form combinations of high capacity loop and transport.

Existing currently combined configurations of wholesale tariff services may be converted to currently combined configurations of unbundled network elements or may be commingled (i.e., converted to a combination of wholesale tariff services and unbundled network elements, where such conversions do not violate the restrictions or limitations set forth within the interconnection agreement.)

## Commingling

With TRO and later based interconnection agreements, UNE loop/transport may be connected to wholesale tariff service, i.e. commingling.  Commingling means UNE loop/transport combination or standalone element is connected, attached, or otherwise linked to one or more facilities or services that a requesting CLEC has obtained at wholesale from AT&T.

UNE loop/transport commingled with a wholesale circuit is not available for purchase if the commingled circuit will be used to provide telecommunication services to wireless cell sites or Mobile Telephone Switching Office (MTSO) locations.

Either AT&T Special Access (SPA) or Switched Access (SWA) connected to UNE transport or loop services will be supported, with the exception of AT&T packet offerings.  Any request for unsupported architectures should utilize the BFR process.

Commingling authorization is required within the CLEC’s interconnection agreement in order to acquire either types of commingling (MBWC & SBWC)

Multiple Bandwidth Commingling (MBWC)

Multiple Bandwidth Commingling (MBWC) arrangement allows the connecting, attaching, or otherwise linking of UNE combination, to one or more facilities or services that a CLEC has obtained at wholesale from AT&T.  CLEC may requests a conversion of an existing UNE combination circuit that will result in the connection of that UNE combination circuit to a higher bandwidth wholesale tariff circuit.

AT&T MBWC service, provisioning and maintenance centers that support wholesale and UNE products, respectively, will remain responsible for the support of their respective products. The conversion of the higher bandwidth UNE to SPA Requests for conversion of UNE Combinations will result in a MBWC circuit should be submitted to the Local Service Center (LSC). Higher bandwidth of the circuit will need to be converted prior to the conversion of the UNE to MBWC.

Single Bandwidth Commingled (SBWC)

A Single Bandwidth Commingled (SBWC) circuit is a single circuit consisting of a mixture of UNE and wholesale jurisdictions on a network element by network element basis (i.e. UNE DS1 local loop and wholesale DS1 interoffice channel).  When a CLEC requests this type of circuit, the entire circuit is considered commingled.  Requests for conversion of network elements that will result in a SBWC or a new SBWC circuit should be submitted to the LSC.  Provisioning will be handled by CWINS.  Maintenance requests should be directed to CWINS.

## Service Rearrangements

AT&T will, at a requesting CLEC’s request, rearrange an existing facility.  The Local Service Request (LSR) may be used to submit the request.   A Service Inquiry must be submitted before submitting an LSR for a rearrangement.  For a request of 15 or more service rearrangements of like services within a state, a spreadsheet will be accepted and the request will be project managed. The interconnection agreement must have rates, terms and conditions for rearrangements before the CLEC can request these services.

Types of Rearrangements:

1) Change in Facility Assignment

This request is for AT&T to move a working customer circuit from a CLEC Connecting Facility Assignment (CFA) to another of the CLEC’s CFA.  This assumes that the old and new CFA terminates at the same point of interface in the same building and the ACTL does not change.

If an LSR is used, the Change in Facility Assignment per Circuit Service Rearrangement non-recurring charge is applicable.  If a spreadsheet is used, the Change in Facility Assignment per Circuit Service Rearrangement non-recurring charge and the Change in Facility Assignment per Circuit Project Management non-recurring charge are applicable.

The minimum billing period is not impacted by this change.

When a manual service order is issued, the manual service order charge will apply.

2) Service Rearrangements (EEL to EEL Retermination (ACTL Change))

AT&T will, at a CLEC’s request, rearrange existing facility by moving one end from one building to another.  CLECs may submit LSRs CRO’d together or if 15 or more a spreadsheet. The existing circuit will be disconnected and a new facility established.

When a manual service order is issued, the manual service order charge will apply.

Service rearrangements that consist of moving one end a customer purchased circuit are considered the issuance of new service and disconnection of an existing service and all associated non-recurring charges apply.  The minimum billing period does apply to the disconnection of existing facilities.  A new minimum billing period begins upon the issuance of new service.

# Pre-Ordering Checklist

## Availability

Currently Combined UNEs are available in AT&T Southeast locations where each component of the combination exists in the network and is available as an unbundled network element.

On those routes or in those wire centers that State Commissions in its Region has approved List of Unimpaired Wire Centers, AT&T began rejecting Unbundled Network Element (UNE) orders for high capacity loop and transport circuits that were not available as UNEs in Alabama, Florida, Georgia, North Carolina, South Carolina, Mississippi, and Louisiana.

## Billing Information

- Any applicable termination liabilities associated with tariff services will be applied where a wholesale service is converted to a UNE or a UNE combination.

- The conversions of Currently Combined wholesale services to unbundled network elements, or vice versa, as described in this package are result in conversions either from CABS services to CABS services or from CRIS services to CABS services.  CABS to CABS conversions consist of an in-place conversion, while CRIS to CABS conversions will require Project Coordination for a physical facility change.

- Manual Order Coordination is included in the non-recurring charge.

- Overtime rates apply for work outside of 08:00am and 05:00pm local time. (Handled by CWINS on E0135 if this applies to the CLEC.)

- Recurring UNE Charges:

Recurring charges will be applicable to the following components per circuit on each LSR:

- Local Loop (may have mileage)

- Interoffice Facility Termination

- Interoffice Mileage

- Channelization (3/1 or 1/0)

- Central Office Channel Interface (COCI)

- Non-Recurring Charges:

- The above UNE services may have non-recurring changes in the states were AT&T has been ordered to provide ordinarily combined network elements.

- Optional Features & Functions:

- Clear Channel Capability (B8ZS/ESF) Option per DS1

- Clear Channel Capability (B8ZS/SF) Option per DS1

- C-bit parity option per DS3

- A Switch-As-Is-Conversion charge will apply in all states.

- The USOC SOMAN will be added to the S&E of the service order to charge for the handling of each circuit on a manual LSR service request. A manual LSR received in the LSC may be via FAX Server, U.S. Mail, or Courier Service.

- State-specific Missed Appointment credits will apply.

- Expedite charges for shorter intervals will apply.

- Cancellation charges will apply.

- Service Order Modification charges will apply.

MBWC: Since optional multiplexing and interfaces are a part of the higher-bandwidth and lower-bandwidth circuits, respectively, they are billed from those jurisdictions.

SBWC: Since optional multiplexing and interfaces may be a part of a SBWC and if ordered, are billed at wholesale rates.  SBWC facilities will have a wholesale Basic Class of Service.

# ORDERING INFORMATION

## Ordering Process Description

To convert existing wholesale services to Currently Combined UNEs, the steps below must be followed.  If the facility involves channelization a CLEC must convert the lower level services first, then convert the higher-level service.

- For non-high capacity wholesale tariff conversions, the CLEC will submit an LSR with a Change (C) activity type to the LSC only to convert a previously ordered service to a Currently Combined UNE.  All CLEC ordering documents should be sent to the LSC who will forward the documents to the appropriate organizations.

- Mass conversions of services will be handled via a spreadsheet (15 or more circuits per state) (Florida is split between North and South) provided by the customer to the LSC. All CLEC ordering documents should be sent to the LSC who will forward the documents to the appropriate organizations.

When requesting conversions of Currently Combined wholesale services to UNEs or UNE combinations, the CLEC will not be able to change the design or any other aspects of the circuit (CKT). Only the CKT ID, the Class of Service, and the billed USOC elements will be changed.

3.	The LSC receives the LSR and issues a Firm Order Confirmation (FOC) when a due date is set for the conversion. The LSC will be the point of contact for converting a qualified CKT to a UNE circuit.

- No changes are permitted.

- A converted circuit will have a different circuit ID and service establishment date from the original circuit. The following changes to a Common Language Circuit ID Serial Number (CLS) circuit identity will occur: SPA (H*GS) to UNE (H*FU) and UNE (H*FU) to SPA (H*GS). (The * in the CLS ID will be replaced with the correct character relative to the level of service involved.)  The service establishment date will be the date the new circuit was converted, i.e. installed.

Service eligibility criteria for high capacity Enhanced Extended Links (EELs) must be satisfied (1) to convert a special access circuit to a high-capacity EEL; (2) to obtain a new high-capacity EEL; or (3) to obtain a high-capacity loop and transport combination that is partially a UNE and partially a special access service (commingled EEL). See the service eligibility criteria within your interconnection agreement.

## Required Fields by Form

- Information regarding Local Service Request (LSR) form preparation can be found in the Local Ordering Handbook (LOH).

http://wholesale.att.com/reference_library/guides/html/leo.html

- “Special Handling” must be added to the Remarks Section of the LSR.

| Ref | Service Level | NC Code | NCI Code | SECNCI Code | CLEC Interface (CFA) |
| --- | --- | --- | --- | --- | --- |
| 1-4: SBWC Note: All Entrance Facilities (Local Channel) are no longer available as UNEs |
| 1 | 2-wire VG Local Channel, IOC, and Local Channel | LY-- | 02LO (LPS) 02GO (GST) 02RV2.O (RVB) | 02LS2 (LPS) 02LS2 (GST) 02RV2.T (RVB) | NA |
| 2 | 4-wire VG Local Channel, IOC, and Local Channel | LY-- | 04LO2 (LPS) 04GO2 (GST) | 04LS2 (LPS) 04LS2 (GST) | NA |
| 3 | 56 KBPS Local Channel, Interoffice Channel, and Local Loop | LY-- | 04DU5.56 | 04DU5.56 | NA |
| 4 | 64 KBPS Local Channel, Interoffice Channel, and Local Loop | LY-- | 04DU5.64 | 04DU5.64 | NA |
| 5-7: SBWC Note: All Entrance Facilities (Local Channel) are no longer available as UNEs |
| 5 | DS1 Local Channel and DS1 Local Loop | HC-- (AMI-SF) HCD- (AMI-ESF) HCZ- (B8ZS-SF) HCE- (B8ZS-ESF) | 04DS9.15 04DS9.1K 04DS9.15B 04DS9.1S | 04DU9.BN (AMI-SF) 04DU9.1KN (AMI-ESF) 04DU9.DN (B8ZS-SF) 04DU9.1SN (B8ZS-ESF) | NA |
| 6 | DS3 Local Channel and Loop | HF- - HFC- | 04DS6.44 | 04DS6.44 | NA |
| 7 | STS-1 Local Channel and Loop | JI- - | 04ST6.A | 04ST6.A | NA |

# Critical Fields and Entries

NC, NCI, and SECNCI Fields on the LSR Form

CFA field on the LS Form

| Ref | Service Level | NC Code | NCI Code | SECNCI Code | CLEC Interface (CFA) |
| --- | --- | --- | --- | --- | --- |
| 8-10: SBWC Note: All Entrance Facilities (Local Channel) are no longer available as UNEs |
| 8 | DS1 Local Channel and IOC terminating in collocation | HC-- (AMI-SF) HCD- (AMI-ESF) HCZ- (B8ZS-SF) HCE- (B8ZS-ESF) | 04DS9.15 04DS9.1K 04DS9.15B 04DS9.1S | 04QB9.11 | PE1P1 (physical) or CNC1X (virtual) |
| 9 | DS3 Local Channel and IOC terminating in collocation | HF- - HFC- | 04DS6.44 | 04QB6.44 | PE1P3 (physical) or CNC3X (virtual) |
| 10 | STS-1 Local Channel and IOC terminating in collocation | JI-- | 04ST6.A | 04QB6.S1 | PE1P3 (physical) or CNCSX (virtual) |
| 11-17 Note: Available as EELs or SBWC |
| 11 | 2-wire VG Local Loop and IOC terminating in collocation | LY- - | 02QC3.OOD_LPS) 02QC3.OOB(GST) 02QC3.RVO(RVB) | 02LS2 (LPS) 02GS2 (GST) 02RV2.T(RVB) | PE1P2 (physical) |
| 12 | 4-wire VG Local Loop and IOC terminating in collocation | LY- - | 02QC3.OOD(LPS) 02QC3.OOB(GST) | 04LS2(LPS) 02GS2(GST) | PE1P4 (physical) |
| 13 | 4-wire 56 kbps Local Loop and IOC terminating in collocation | LY- - | 04QC5.OOP | 04DU5.56 | PE1P4 (physical) |
| 14 | 4-wire 64 kbps Local Loop and IOC terminating in collocation | LY- - | 04QC5.OOQ | 04DU5.64 | PE1P4 (physical) |
| 15 | DS1 Local Loop and IOC terminating in collocation | HC—(AMI-SF) HCD- (AMI-ESF) HCZ –(B8ZS-SF) HCE –(B8ZS-ESF) | 04QB9.11 | 04DU9.BN (AMI-SF) 04DU9.1KN (AMI-ESF) 04DU9.DN (B8ZS-SF) 04DU9.1SN (B8ZS-ESF) | PE1P1 (physical) or CNC1X (virtual) |
| 16 | DS3 Local Loop and IOC terminating in collocation | HF- - HFC- | 04QB6.33 | 04DS6.44 | PE1P3 (physical) or CND3X (virtual) |
| 17 | STS-1 Local Loop and IOC terminating in collocation | JI-- | 04QB6.S1 | 04ST6.A | PE1P3 (physical) or CNCSX (virtual) |

| Ref | Service Level | NC Code | NCI Code | SECNCI Code | CLEC Interface (CFA) |
| --- | --- | --- | --- | --- | --- |
| 19: MBWC Note: Mux and associated Transport must be ordered as Wholesale |
| 19 | Channelized DS1 IOC | HC-M (AMI-SF) HCDM (AMI-ESF) HCZM (B8ZS-SF) HCEM (B8ZS-ESF) | 04QB9.11 | NA | PE1P1 (physical) or CNC1X (virtual) |
| 20-22 Note: For commingled arrangement, see UNE Loop Multiple Bandwidth Commingling - CLEC Information Package |
| 20 | Channelized DS1 Interoffice Channel from collocation | HC-M (AMI-SF) HCDM (AMI-ESF) HCZM (B8ZS-SF) HCEM (B8ZS-ESF) | 04QB9.11 | NA | PE1P1 (physical) or CNC1X (virtual) |
| 21 | Channelized DS3 Interoffice Channel from collocation | HF-M HFZM | 04QB6.33 | NA | PE1P3 (physical) or CNC3X (virtual) |
| 22 | Channelized STS-1 Interoffice Channel from collocation | JIAA | 04QB6.S1 | NA | PE1P3 (physical) or CNCSX (virtual) |

| Ref | Service Level | NC Code | NCI Code | SECNCI Code | CLEC Interface (CFA) |
| --- | --- | --- | --- | --- | --- |
| 23: SBWC Note: All Entrance Facilities (Local Channel) are no longer available as UNEs |
| 23 | Channelized DS1 Local Channel and IOC with mux in EU SWC | HC-M (AMI-SF) HCDM (AMI-ESF) HCZM (B8ZS-SF) HCEM (B8ZS-ESF) | 04DS9.15 04DS9.1K 04DS9.15 B 04DS9.1S | NA | NA |
| 29-33: MBWC Note: Mux must be ordered as Wholesale and in place prior to submission of 29-33 |
| 29 | 2-wire Voice Grade Local Loop and IOC CFA mux | LY-- (LSP) LY-- (GST) LY-- (RVB) | 04QB9.11 | 02LS2 (LPS) 02GS2 (GST) 02RV2.T(RVB) | DS1 mux |
| 30 | 4-wire Voice Grade Local Loop and IOC CFA mux | LY-- (LSP) LY-- (GST) | 04QB9.11 | 04LS2(LPS) 02GS2(GST) | DS1 mux |
| 31 | 4-wire 56 kbps Local Loop and IOC CFA mux | LY- - | 04QB9.11 | 04DU5.56 | DS1 mux |
| 31 | 4-wire 64 kbps Local Loop and IOC CFA mux | LY- - | 04QB9.11 | 04DU5.64 | DS1 mux |
| 33 | DS1 Local Loop and IOC CFA mux to collo | HC—(AMI-SF) HCD- (AMI-ESF) HCZ- (B8ZS-SF) HCE- (B8ZS-ESF) | 04QB6.33 [DS3] 04QB6.1S [STS-1] | 04DU9.BN (AMI-SF) 04DU9.1KN (AMI-ESF) 04DU9.DN (B8ZS-SF) 04DU9.1SN (B8ZS-ESF) | DS3 mux |

| Ref | Service Level | NC Code | NCI Code | SECNCI Code | CLEC Interface (CFA) |
| --- | --- | --- | --- | --- | --- |
| 34-37: MBWC Note: Wholesale Local Channel and Wholesale Mux must be in place prior to the submission of the Lower Level Services |
| 34 | 4-wire Local Loop and IOC CFA Channelized DS1 Local Channel | LY—(LPS) LY—(GST) | 04DS9.15 04DS9.1K 04DS9.15 B 04DS9.1S | 04LS2 04GS2 | DS1 mux |
| 35 | 2-wire Local Loop and IOC CFA Channelized DS1 Local Channel | LY—(LPS) LY- -(GST) LY- -(RVB) | 04DS9.15 04DS9.1K 04DS9.15 B 04DS9.1S | 02LS2 (LPS) 02LS2 (GST) 02RV2.T (RVB) | DS1 mux |
| 36 | 4-wire 56 kbps Local Loop and IOC CFA DS1 Mux | LY- - | 04DS9.15 04DS9.1K 04DS9.15B 04DS9.1S | 04DU5.56 | DS1 mux |
| 37 | 4-wire 64 kbps Local Loop and IOC CFA DS1 Mux | LY- - | 04DS9.15 04DS9.1K 04DS9.15B 04DS9.1S | 04DU5.64 | DS1 mux |
| 38: MBWC Note: Wholesale Local Channel and Wholesale Mux must be in place prior to the submission of the Lower Level Services |
| 38 | DS1 Interoffice from collocation in EU SWC CFA DS3 [STS-1] mux | HC—(AMI-SF) HCD- (AMI-ESF) HCZ- (B8ZS-SF) HCE- (B8ZS-ESF) | 04DS6.44 04ST6.A | 04QB9.11 | PE1P1 (physical) or CNC1X (virtual) and DS3 mux |
| 39-45: EELs Note: For commingled arrangement, see UNE Loop Multiple Bandwidth Commingling - CLEC Information Package |
| 39 | 2-wire VG Local Loop CFA to Channelized DS 1 IOC terminating in collocation | LY- - | 04QB9.11 (LPS) 04QB9.11 (GST) 04QB9.11 (RVB) | 02LS2 (LPS) 02GS2 (GST) 02RV2.T (RVB) | DS1 Mux |
| 40 | 4-wire VG Local Loop CFA to Channelized DS 1 IOC terminating in collocation | LY- - | 04QB9.11 (LPS) 04QB9.11 (GST) | 04LS2 (LPS) 04GS2 (GST) | DS1 Mux |
| 41 | 2-wire ISDN Local Loop CFA to Channelized DS 1 IOC terminating in collocation | LY- - | 04QB9.11 | 02IS5 | DS1 Mux |
| 42 | 4-wire 56kbps Local Loop CFA to Channelized DS 1 IOC terminating in collocation | LY- - | 04QB9.11 | 04DU5.56 | DS1 Mux |
| 43 | 4-wire 64kbps Local Loop CFA to Channelized DS 1 IOC terminating in collocation | LY- - | 04QB9.11 | 04DU5.64 | DS1 Mux |
| 44 | DS1 Local Loop CFA to Channelized DS 3 IOC terminating in collocation | HC- - (AMI-SF) HCD- (AMI-ESF) HCZ- (B8ZS-SF) HCE- (B8ZS-ESF) | 04QB6.33 | 04DU9.BN (AMI-SF) 04DU9.1KN (AMI-ESF) 04DU9.DN (B8ZS-SF) 04DU9.1SN (B8ZS-ESF) | DS3 Mux |
| 45 | DS1 Local Loop CFA to Channelized STS-1 IOC terminating in collocation | HC- - (AMI-SF) HCD- (AMI-ESF) HCZ- (B8ZS-SF) HCE- (B8ZS-ESF) | 04QB6.S1 | 04DU9.BN (AMI-SF) 04DU9.1KN (AMI-ESF) 04DU9.DN (B8ZS-SF) 04DU9.1SN (B8ZS-ESF) | STS-1 Mux |

# Notes:

- NC/NCI codes are determined by architecture and not billing jurisdiction

- The NCI always represents the highest service involved in the request.

- The SECNCI, if there is any, always represents the lowest level of service involved.

- Two orders are required for facilities of MBWC arrangements.  One is required for the channelized facility and another is required for the facility riding the channelized facility

- UNE elements above are available in the Impaired Serving Wire Center (SWC)

- All Entrance Facilities (Local Channel) are no longer available as UNEs

- In some scenarios mux must be ordered as Wholesale

In addition to the NC, NCI, SECNCI and any CFA fields on the LSR, the REMARKS and APOT fields on the LSR are critical for ordering.  Please populate the REMARKS field with the exact product name you are ordering.

## Any Applicable USOCs and/or FIDs

# Collocation / HTN

| Level of Service | USOC Description | USOC | CFA |
| --- | --- | --- | --- |
| DS1 | Holding USOC | HTN | T3 |
| DS1 | Physical Collocation Cross Connect | PE1P1 | T1TIE |
| DS1 | Physical Collocation Pot Bay | PE1PG | T1TIE |
| DS1 | Virtual Collocation Cross Connect | CNC1X | T1TIE |

Service Rearrangement

| Description | USOC |
| --- | --- |
| Change in Facility Assignment per Circuit - Service Rearrangement | URETD |
| Change in Facility Assignment per Circuit - Project Management | URETB |
| Order Coordination Specific Time - Dedicated Transport | OCOSR |

# Central Office Channel Interface

| Level of Service | USOC Description | USOC |
| --- | --- | --- |
| Voice Grade | Central Office Channel Interface (COCI) | 1D1VG |
| Data DS0 | Central Office Channel Interface (COCI) | 1D1DD |
| DS1 | Central Office Channel Interface (COCI) | UC1D1 |

# Interoffice Channel

| Level of Service | USOC Description | USOC |
| --- | --- | --- |
| ALL | Interoffice Channel (Per Mile) | 1L5XX |
| 2 Wire Voice Grade | 2 Wire Interoffice Channel (Facility Termination) | U1TV2 |
| 4 Wire Voice Grade | 4 Wire Interoffice Channel (Facility Termination) | U1TV4 |
| 4 Wire Data DS0 | 4 Wire 56KB Interoffice Channel (Facility Termination) | U1TD5 |
| 4 Wire Data DS0 | 4 Wire 64KB Interoffice Channel (Facility Termination) | U1TD6 |
| DS1 | DS1 Interoffice Channel (Facility Termination) | U1TF1 |
| DS3 | DS3 Interoffice Channel (Facility Termination) | U1TF3 |
| STS-1 | STS-1 Interoffice Channel (Facility Termination) | U1TFS |

# Channelization

| Level of Service | USOC Description | USOC |
| --- | --- | --- |
| DS1 | 1/0 channelization system | MQ1 |
| DS3/STS-1 | 3/1 channelization system | MQ3 |

# Loop

| Level of Service | USOC Description | USOC |
| --- | --- | --- |
| DS3 & above | Local Loop Mileage | 1L5ND |
| 2 Wire Voice Grade analog | 2 Wire Voice Grade Loop | UEAL2 |
| 4 Wire Voice Grade analog | 4 Wire Voice Grade Loop | UEAL4 |
| 4 Wire 56KB Data DS0 | 4 Wire 4KB Data Loop | UDL56 |
| 4 Wire 64KB Data DS0 | 4 Wire 64KB Data Loop | UDL64 |
| DS1 | DS1 Loop | USLXX |
| DS3 | DS3 Loop | UE3PX |
| STS-1 | STS-1Loop | UDLS1 |

# Pricing

# All pricing is specific to the CLEC’s Interconnection Agreement.

# Intervals

# All Due Date/Intervals are calculated upon the receipt of an error free LSR from the CLEC and can be found in the Interval Guide section of the LOH.

# Provisioning

ACAC will provision orders for wholesale circuits.

CWINS will provision orders for UNE circuits.

# Maintenance and Repair Process

- AT&T will maintain and repair the facilities and equipment that it furnishes. The CLEC or CLEC’s end user may not rearrange, disconnect, remove, or attempt to repair any equipment installed by AT&T.

- The CLEC is responsible for testing and isolation of all troubles to the AT&T network. AT&T is responsible for testing, sectionalizing, and repair of all customer reported troubles. The trouble reporting procedure must conform to the established trouble receipt process.

- Customer Wholesale Interconnection Network Service (CWINS) will process EO-135 charges based on applicable tariff rules.

	The CWINS will handle CLEC calls.

	Maintenance intervals for unbundled transport are the same as the maintenance intervals for comparable retail services.

	The CWINS will enter the CLEC trouble report in WFA-C and test to isolate the source of the trouble.  The WFA ticket will be dispatched to the Central Office as needed for additional testing or trouble resolution.

	The CLEC may call to request status on the report or escalate to CWINS management if commitment time is exceeded.  After all problems within the AT&T area of responsibility have been tested and corrected, the CWINS Technician will contact the CLEC to report the results for testing and repair.

The following apply to commingled orders:

For Multiple Bandwidth Commingling (MBWC) situations, the CLEC must diagnose which circuit has the trouble and contact the appropriate service center, i.e. ACAC (wholesale circuits) or CWINS (UNE circuits).  If through AT&T trouble-shooting AT&T determines the trouble is in the other circuit, there will be a soft hand off between AT&T centers.

# Text boxes

POP

EU

POP

SWC

EU

SWC

collo

### Non-channelized Facilities

EU

SWC

POP

SWC

POP

Wholesale

Local Channel

IOC

UNE Loop

M

collo

EU

UNE IOC

EU SWC

POP  SWC

Lower-Level Facility Riding Higher-Level Channelized Portion of Facility Above

Channelized Local Channel and Interoffice Channel with mux in EU SWC

M

EU SWC

POP SWC

POP

Wholesale

Local Channel

IOC

Channelized Interoffice Channel with mux in EU SWC

collo

M

POP SWC

UNE IOC

EU SWC

EU SWC

IOC

POP SWC

M

collo

Collocated Channelized Interoffice Channel with mux in POP SWC

IOC

Loop

POP

Collo

EU SWC

M

POP SWC

M

Loop

IOC

EU SWC

POP SWC

POP

collo

M

POP SWC

EU

EU

Wholesale

Local Channel

EU SWC

Wholesale

Local Channel

POP/EU SWC

EU

POP

Wholesale

Local Channel

Loop

Loop

IOC

Wholesale

Local Channel

Higher-Level Portion of Channelized Facility

LEGEND:

POP: Point of Presence

SWC: Serving Wire Center

EU: End User

IOC: Interoffice Channel

M: Multiplexer

NA: Not Applicable

Collo: Collocation

---- : lower-level

EU

collo

EU SWC

POP SWC

IOC

Loop

Non-channelized to collocation

Wholesale Mux

Wholesale

Mux

IOC

UNE MUX