Unbundled Dedicated Transport –

Unbundled Dark Fiber (UDF)

CLEC Information Package

March 25, 2013

Version 13

Table of Contents

Scope	4

Product Name	4

Product Category	4

Product and Technical Description	4

Service Description	4

Features and Benefits	5

Technical Specifications	5

Service Arrangements	6

Pre-Ordering Checklist	7

Collocation Arrangement Considerations	7

Billing Information	8

Ordering Information	8

Required/Valid Forms	8

Critical Fields and Entries for this Product (Standalone)	9

Unbundled Dark Fiber Process Flow	10

Pricing	11

Intervals	11

Maintenance and Repair Process	11

| Version Number | Date | Revision |
| --- | --- | --- |
| 1 | 09/13/00 | Initial version |
| 2 | 02/22/01 | Update Critical Fields information |
| 3 | 01/15/02 | Include the appropriate BellSouth contact for a loss report and update service availability |
| 4 | 03/11/02 | Updated NCI/SECNCI and SI to change from ordering two 2-fiber segments to ordering one 4-fiber segment. |
| 5 | 06/03/02 | Added sentence to clarify that collocation must be in place prior to ordering UDF. |
| 6 | 06/28/02 | Updated to reflect BellSouth policies: This service is not available to wireless companies and BellSouth does not connect UNEs to tariffed services. |
| 7 | 12/15/03 | Update to add “ordinarily combined” UNEs to package |
| 8 | 01/16/04 | Delete sub loop feeder due to TRO, correct interoffice NRC, and supply current SI |
| 9 | 06/09/05 | Updated to reflect TRO/TRRO |
| 10 | 09/30/05 | Update to reflect commingling |
| 11 | 07/14/07 | Update will include the name change from BellSouth to AT&T and the conversion spreadsheet. Remove Dark Fiber combination reference. A new spreadsheet process that will allow a facility-based CLEC to send the conversion spreadsheet within this package to the account team rather than to the CLEC Care group. |
| 12 | 09/17/08 | Update to the SI |
| 13 | 03/25/13 | Updated Ordering Information part |

# Scope

This document is intended as informational to prospective CLEC customers.

This product information package is applicable in AT&T Alabama, AT&T Florida, AT&T Georgia, AT&T Kentucky, AT&T Louisiana, AT&T Mississippi, AT&T North Carolina, AT&T South Carolina and AT&T Tennessee.

# Product Name

Unbundled Dark Fiber

# Product Category

Unbundled Dedicated Transport

# Product and Technical Description

## Service Description

AT&T is no longer obligated to provide Unbundled Dark Fiber Local Channel, also known as Entrance Facilities, and Unbundled Dark Fiber Local Loop.

Unbundled Dark Fiber (UDF) Transport is offered as a point-to-point arrangement between AT&T Wire Centers.  UDF is spare optical fiber and is offered without optical signal regeneration to compensate for signal losses.  This arrangement consists of four optical fibers and fiber terminating equipment.

UDF Transport may be ordered within all AT&T Southeast states where available.  UDF will not be deemed available if:  (1) it is used by AT&T for maintenance and repair purposes; (2) it is designated for use pursuant to a firm order placed by another customer; (3) it is restricted for use by all carriers, including AT&T, because of transmission problems or because it is scheduled for removal due to documented changes to roads and infrastructure; or (4) AT&T has plans to use the fiber within a two-year planning period.  AT&T is not required to place the fiber for UDF if none is available.

Triennial Review Order or later agreement prohibits the use of UNEs exclusively for the provisioning of telecommunications services in the mobile wireless and long distance markets.

## Features and Benefits

UDF Transport allows a CLEC to construct its facilities utilizing spare AT&T optical fiber between two locations.  AT&T makes no representations regarding the transmission capability of the facilities.  Interoffice Channel is the transport between two wire centers owned by AT&T.

## Technical Specifications

AT&T Technical Reference TR 73603, Unbundled Dark Fiber (UDF) Technical Specifications, provides the technical specifications for Unbundled Dark Fiber Service offered by AT&T.

Mechanical Interface

At the Network Interface (NI), AT&T will provide duplexable SC type (EIA/TIA SCFOC/2.5) plug and jack type connectors.  AT&T will install the connector jack to serve as the NI.  AT&T and the Carrier must each provide connector plugs to terminate their fibers at the NI.  Each connector plug will contain 2 fibers, one for each direction of transmission.  The connector jack will be the demarcation point between AT&T and the Carrier installation.  Figure 2, at the end of the document, depict the Fiber Optic Mechanical Network Interface.

Optical Fiber Termination and Arrangement

Optical fibers are terminated at the customer premises in a AT&T approved and constructed cabinet or Fiber Distributing Frame (FDF). AT&T typically uses a "tray" type splice on the customer premises and connectorized fibers from that splice to the cabinet or FDF.

Regeneration

Unbundled Dark Fiber is offered without regeneration, so it will be incumbent upon the customer to insure that, given the AT&T provided loss budget values, adequate margins are maintained to insure proper working of the fiber optic system.

Service Performance Objectives

Other than meeting manufacturer’s design specifications, there will not be any specified performance objectives for this UNE.  However, at the request of the customer through contact with the Customer Wholesale Interconnection Network Service (CWINS), if made prior to providing access to the facilities, AT&T will attempt to estimate the transmission loss of the channel at the customer’s intended transmission wavelength: provided, however, that AT&T does not warrant that the customer’s channel will operate at that estimated loss or that the transmission loss will remain constant during the period in which the customer obtains the facilities from AT&T.

## Service Arrangements

Architecture #1: UDF Transport (Standalone) a.k.a. single network element

Central Office to Central Office with a collocation cross connect on each end:

Fiber optic cross connect from one central office to a fiber optic cross connect in another central office, see Figure 1. Under TRRO based interconnection agreements, CLECs may not obtain an Interoffice Channel if both end points defining the route are either Tier 1 or Tier 2 wire centers.  Once a wire center is determined to be a Tier 1 wire center, that wire center is not subject to later reclassification as a Tier 2 or Tier 3 wire center.  Once a wire center is determined to be a Tier 2 wire center, that wire center is not subject to later reclassification as a Tier 3 wire center.

FIGURE 1

Unbundled network elements (UNEs) are not available for purchase or for conversion from Special Access or Private Line Circuits if such network elements will be used exclusively to provide wireless or long distance services.

In TRO and later based interconnection agreements, UNE transport may be connected to wholesale tariffed service, i.e. commingling.  Commingling means the connecting, attaching, or otherwise linking of an unbundled network element, or a combination of unbundled network elements, to one or more facilities or services that a requesting CLEC has obtained at wholesale from AT&T, or the combining of an unbundled network element, or a combination of unbundled network elements, with one or more such facilities or services.

When a CLEC requests a conversion of a part of an existing Dry Fiber circuit which will result in a Dry Fiber (Special Access) portion and a portion Dry Fiber, the resulting circuit shall be known as Single Bandwidth Commingled (SBWC) circuit.

# Pre-Ordering Checklist

## Collocation Arrangement Considerations

Standalone Interoffice application: Collocation is required at both ends of the facility.

With TRO or later based interconnection agreements, CLECs may convert a wholesale facility to a UNE facility described within this document or visa versa. Converting a single network element may be accomplished by submitting an ASR to the ICSC to disconnect the wholesale facility and an LSR to the LCSC to install the UNE facility.  The orders should be CRRO’d to reduce the likelihood of a service disruption.  A CLEC may request batch of fifteen or more single network elements requested to be converted from wholesale to UNE by submitting a spreadsheet to its Account Team/Local Contract Manager, which will submit it for project management coordination.

With TRRO or later based interconnection agreements, CLECs may commingle AT&T wholesale and UNE facilities on an element-by-element basis.

Please note that all requests for SBWC transport must appropriately coded LSRs.  The second character of the TOS field should be “G”.  The new field CMA (Commingled Arrangement) must have one of the following codes: B, E or G that corresponds to the architecture listed below.

B = architecture consisting of Wholesale Local Channel (to the POP), UNE Interoffice Channel, and Wholesale Local Channel (to the EU).

E = UNE Interoffice Channel and Wholesale Local Channel (to the EU).

G = Wholesale Local Channel (to the POP)and UNE Interoffice Channel

# Billing Information

Billing will be accomplished through CABS.

The following applies to Unbundled Dark Fiber when commingled:

- SIG will not apply.

- SAW will not apply.

- Billing Guarantee will not apply.

- State Missed Appointment Credits will apply.

- Expedite Charges for shorter intervals will apply.

- Cancellation Charges will apply.

- Service Order Modification charges will apply.

# Ordering Information

Ordering CLEC must have this service within its interconnection agreement before placing an order. Unbundled Dark Fiber may be ordered by submitting a Service Inquiry (SI) via email to attselscrequest@att.com and Firm Order (LSR) electronically with “Special Handling” in the Remarks to the LSC.  The LSC will forward the SI to Network.  Network will determine availability of facilities.  If facilities are not available, it will be so noted and returned to the LSC, who will return the documents to the CLEC.  The CLEC should then cancel the LSR electronically.  If facilities are available the LSC will forward start the service order process. Additionally, the CLEC may submit a SI prior to ordering to ascertain availability of the fiber; however this may delay the service order process because of the interval between the SI response and the receipt of the LSR as compared to the above process.

Inquiry facility checks do not reserve Dark Fiber.  In order to secure UDF Dark Fiber Transport, CLECs must place a firm order, the inquiry process only determines fiber availability at that time.

When CLECs submit a Dark Fiber inquiry, appropriate rates for the inquiry will be charged.  CLEC inquiries will be billed one non-recurring charge per CLEC request, not per service order and not per strand.

Required/Valid Forms

Please refer to the Local Ordering Handbook (LOH) for Local Ordering .

http://wholesale.att.com/reference_library/guides/html/leo.html

Critical Fields and Entries for this Product (Standalone)

Note: NC/NCI codes describe architecture and are not related to billing jurisdiction, NC/NCI/SECNCI

| Service Standalone | Class of Service | NC Code | NCI Code | SECNCI Code |
| --- | --- | --- | --- | --- |
| UDF Interoffice Channel | UDF | LX - - | 04QBF.LLX | 04QBF.LLX |

Examples of collocation fiber CFA are:

PFWUA/LG/1/ATLNGACS/ATLNGACS1MD

(selects fibers 1, 2, 3, and 4 for a 4-fiber order)

VMATX/LG/10/ATLNGAPP/ATLNGAPPWA1 (10, 11, 12, 13)

VFUTC/LG/9/ORLDFLCL/ORLDFLCL3MD (9, 10, 11, 12)

PWFIM/LG/43/BRHMALMT/BRHMALMTWD1 (43, 44, 45, 46)

PF2UT/LG/7/RLGHNCMO/RLGHNCMOBMD

(illustrates cable name with numeric, fibers 7, 8, 9, 10)

Any Applicable USOCs

| Description | USOC |
| --- | --- |
| Dark Fiber - Interoffice Transport Interoffice mileage | 1L5DF |
| Dark Fiber - Interoffice Transport Interoffice NRC | UDF14 |

# Unbundled Dark Fiber Process Flow

- The LSR and the SI will be submitted by the CLEC to the LSC.

The LSC will forward the SI to SE Network Engineering

- SE Network Engineering will review fiber availability in the requested cross sections.

- If fiber is not available the SI is returned to the LSC who will then forward the response to the CLEC.

- If fiber is available Network Engineering will respond to the LSC, providing the total fiber length being provided on the request.

- The LSC will receive the SI from Network Engineering and convert the total lengths to the appropriate state/CLEC billing structure.  Any conversion to a mileage billing structure will be rounded up to the next mile.

- The SI will be forwarded to the LCS. The LCS will write the Service Order and will apply the appropriate USOC configuration for billing.

- The CPG will issue one word document containing any assignments provided by CCM and using the collocation CFA given by the customer.

- CCM will have issued jobs to any fibers, if required.

- The CWINS will coordinate a continuity test of the fiber service.

- The CWINS will turn up the service to the CLEC.

- Maintenance issues will be referred to the CWINS center.

- The CWINS will dispatch the appropriate work group on maintenance issues.

# Pricing

All pricing is specific to the CLEC’s Interconnection Agreement

# Intervals

All Due Date/Intervals are calculated upon the receipt of an error free LSR from the CLEC and can be found in the Interval Guide section of the LOH.

# Maintenance and Repair Process

The customer must cooperatively disable (turn-off) any optical transmission equipment on an unbundled dark fiber arrangement whenever AT&T must perform maintenance on those facilities.

AT&T will maintain and repair the facilities and equipment, which it furnishes. The customer or customer’s end-user may not rearrange, disconnect, remove, or attempt to repair any equipment installed by AT&T.

The customer is responsible for testing and isolation of all reported troubles to the AT&T network. AT&T is responsible for testing, sectionalizing, and repair of all customer-reported troubles to AT&T’s facilities. The trouble reporting procedure must conform to AT&T’s established trouble receipt process.

# Text boxes

LGX	Fiber Distribution Frame

POT BAY	Point of Termination Bay

Note:	* The arrangement shown above is applicable to Physical 	Collocation.

* Current policies concerning recombination of elements will be adhered to.

Collocation Area

Unbundled Dark Fiber Interoffice Channel

BST Central Office

G

L

X

4 Single Mode

Fiber Strands

POT

BAY

L

G

X

CABLE

VAULT

BST Central Office

POT

BAY

L

G

X

G

L

X

CABLE

VAULT

Network

Interface

Network

Interface

Collocation

Cross-connect

Element

Collocation

Cross-connect

Element

Collocation Area

Collocation Area