# Unbundled Dedicated Transport –

# Ordinarily Combined UNE Combinations

# CLEC Information Package

April 15, 2010

Version 17

# Table of Contents

Scope	1

Product Name	1

Product Category	1

Product and Technical Description	1

Service Description	1

Features and Benefits	1

Basic Service Capabilities	3

Commingling	3

Pre-Ordering Checklist	4

Availability	4

Billing Information	5

Ordering Information	6

Ordering Process Description	6

Required/Valid Forms	6

Required Fields by Form	6

Critical Fields and Entries	7

Any Applicable USOCs and/or FIDs	12

Pricing	13

Intervals	13

Provisioning	13

Maintenance and Repair Process	13

| Version Number | Date | Change |
| --- | --- | --- |
| 1 | 05/21/02 | Initial Version |
| 2 | 06/19/02 | Add the Critical Fields and Entries Reference numbers 56, 57, & 58 |
| 3 | 08/02/02 | In Critical Fields and Entries: correct codes for 1, 19, 44, 49-55; delete configurations 36-38; add picture for 40, add 41-42 configurations. Add Note regarding TOS code in Required Fields section. |
| 4 | 08/27/02 | In Critical Fields and Entries, add configuration 42. Update to reflect policy that this service is not available to wireless companies. |
| 5 | 09/19/02 | In Critical Fields and Entries: insert label for channelized facilities and deleted entries 55-57, and added (55) DS1Local Channel + DS1 Sub Loop Feeder. |
| 6 | 09/30/02 | In Critical Fields and Entries: corrected DS3 Local Channel NCI code (items 12 and 42). |
| 7 | 11/01/02 | In Critical Fields and Entries: corrected DS1 Local Channel code in items 5, 8, 11, 21, 30, 38, 39, 40, 41, 47, and 55. |
| 8 | 11/20/02 | Update to include EELs information and obsolete EELs CLEC Information Package |
| 9 | 02/19/03 | Correct Note on page 6 regarding TOS field. Second TOS=9 for EELs and not =9 for non-EEL combinations (either B or A). Enclose SI. |
| 10 | 03/07/03 | Add language to distinguish EELs within Ordinarily Combined UNE Combinations |
| 11 | 05/02/03 | Reorganize Critical Fields Table, added LOA |
| 12 | 08/05/03 | Corrected codes in line 1 and 23, Critical Fields and Entries |
| 13 | 06/09/05 | Update document to state that EELs may be ordered electronically and includes TRO/TRRO information and updated for TRO & TRRO. Offer multiple bandwidth commingling of SPA. |
| 14 | 09/30/05 | Update to reflect addition of SWA and SBWC support. |
| 15 | 10/02/06 | Update Critical Fields and Entries table and schematics to reflect the TRO/TRRO. |
| 16 | 07/14/07 | Update name change from BellSouth to AT&T |
| 17 | 4/15/2010 | Update ordering information |

# Scope

This document is provided to CLECs as information regarding Ordinarily Combined UNE Combinations or Commingled facilities.

This product information package is applicable in AT&T Alabama, AT&T Florida, AT&T Georgia, AT&T Kentucky, AT&T Louisiana, AT&T Mississippi, AT&T North Carolina, AT&T South Carolina and AT&T Tennessee.

# Product Name

Ordinarily Combined UNE Combinations/Commingled

# Product Category

# Unbundled High Capacity Loop and Dedicated Transport

# Product and Technical Description

## Service Description

Where necessary to comply with an effective FCC and/or State Commission order, AT&T offers Dedicated Transport - Ordinarily Combined UNE Combinations.  Ordinarily Combined UNEs are to be used for new services.  A Triennial Review Order or later agreement prohibits the use of UNEs exclusively for the provisioning of telecommunications services in the mobile wireless and long distance markets.

## Features and Benefits

Ordinarily Combined UNE Combinations that include unbundled high capacity loop and dedicated transport by definition, dedicated to a particular customer.  Unbundled High Capacity Loop and Dedicated transport is a point-to-point service and may consist of the following elements: Interoffice Channel, and Local Loop.

The following definitions apply to the elements:

- Interoffice Channel is a network element that provides a dedicated point-to-point transmission path and its associated electronics between AT&T wire centers.

- Channelization is an optional functionality performed when a higher-level facility is separated into lower level services, e.g. DS3 to 28 DS1s or DS1 to 24 DS0s.  Channelization can be accomplished through the use of a multiplexer or a Digital Cross-connect System (DCS).  Once the basic channelization system and associated transport has been installed, channels can be activated all at once or on an as-needed basis.  Lower level services ride the channelized facility.  Channelization is available on a limited based as described in NECA 4 tariff.

- Local Loop UNE (Subscriber Line) is a network element that provides a transmission facility between a distribution frame in a AT&T central office (SWC) and an end user customer premise (NID).

- Local Channel is the transport facility between the customer’s Point of Presence (POP) and the POP Serving Wire Center.  AT&T is no longer obligated to provide entrance facilities (Local Channels).

The elements may be combined to form local loop/transport combinations at TELRIC rates known as Enhanced Extended Links (EELs).  AT&T is no longer obligated to provide unbundled local channels, also known as entrance facilities. Transport as defined within the TRO consists of Interoffice Channel.  Therefore, there is one UNE EEL configurations: (1) Local Loop + Interoffice Channel.   Channelization may or may not be included.

Voice Grade, DS0, DS1, DS3, and STS-1 facilities are supported as unbundled network elements, although DS1, DS3 and STS-1 facilities are not available as UNEs in certain wire centers or on certain routes.

The set of Channelization capabilities will be as follows:

- DS1 Channelization System:  The device breaks down a DS1 signal into 24 DS0s. It has the following Central Office Channel Interfaces (COCI): Voice Grade, ISDN or Digital Data.

- DS3 Channelization System:  The device breaks down a DS3 signal into 28 DS1s.  It has a DS1 Central Office Channel Interface.

- STS-1 Channelization System:  The device breaks down a STS-1 signal into 28 DS1s.  It has a DS1 Central Office Channel Interface.  It is utilizes SONET protocol.

Channelization Systems should be ordered with a Transport facility in order to allow the lower-level facility to be subdivided into channels.  Each lower-level facility that should be connected to a channel on a higher-level facility should be ordered with a central office channel interface.

## Basic Service Capabilities

Customer may obtain this service in within AT&T’s Southeast area, where available.  No wholesale circuit will be installed to a UNE (or UNE combination) if the circuit would result in the CLEC exceeding the maximum number of UNEs available on a particular route or at a particular location, as described in the interconnection agreement.   Service eligibility criteria set forth in the interconnection agreement apply to installation of AT&T Special Access services to form combinations of high capacity loop and transport.

## Commingling

With TRO and later based interconnection agreements, UNE loop/transport may be connected to wholesale tariff service, i.e. commingling.  Commingling means UNE loop/transport combination or standalone element is connected, attached, or otherwise linked to one or more facilities or services that a requesting CLEC has obtained at wholesale from AT&T.

UNE loop/transport commingled with a wholesale circuit is not available for purchase if the commingled circuit will be used to provide telecommunication services to wireless cell sites or Mobile Telephone Switching Office (MTSO) locations.

Either AT&T Special Access (SPA) or Switched Access (SWA) connected to UNE transport or loop services will be supported, with the exception of AT&T packet offerings.  Any request for unsupported architectures should utilize the BFR process.

Commingling authorization is required within the CLEC’s interconnection agreement in order to acquire either types of commingling (MBWC & SBWC)

Multiple Bandwidth Commingling (MBWC)

AT&T Multiple Bandwidth Commingling (MBWC) service, provisioning and maintenance centers that support wholesale and UNE products, respectively, will remain responsible for the support of their respective products; therefore, one may use an LSR to order a UNE circuit through the LSC with a connection facility assignment of a wholesale tariff circuit (Special Access) or an ASR to order a wholesale tariff circuit (Special Access) with a connecting facility assignment of a UNE circuit.

Single Bandwidth Commingled (SBWC)

A Single Bandwidth Commingled (SBWC) circuit is a single circuit consisting of a mixture of UNE and wholesale jurisdictions on a network element by network element basis, e.g. a UNE local loop and wholesale interoffice channel.  When a CLEC requests this type of circuit, the entire circuit is considered SBWC.  Requests for conversion of network elements that will result in a SBWC or a new SBWC circuit should be submitted to the LSC.  Provisioning will be handled by CWINS.  Maintenance requests should be directed to CWINS.

# Pre-Ordering Checklist

## Availability

Ordinarily Combined UNEs may be order in AT&T Southeast location where available.  If the ordered transport combination is to terminate in a collocation, the collocation must be in place prior to ordering the transport.  If the ordered transport combination will ride higher-level transport, then the higher-level transport should be in place prior to submitting the lower-level transport order.

An ordering CLEC may connect its UNE transport combination to a different carrier’s collocation or higher–level UNE transport, if a Letter of Authorization (LOA) is completed authorizing the use of another CLEC’s specific Connecting Facility Assignment (CFA). The ordering CLEC must have the UNE combination (and cross-connect if connected to collocation) within its Interconnection Agreement.

On those routes or in those wire centers that State Commissions in its Region has approved List of Unimpaired Wire Centers.  AT&T began rejecting Unbundled Network Element (UNE) orders for high capacity loop and transport circuits that were not available as UNEs in Alabama, Florida, Georgia, North Carolina, South Carolina, Mississippi and Louisiana.

## Billing Information

- Minimum mileage is one mile.

- Manual Order Coordination is included in the non-recurring charges.

- Overtime rates apply for work outside of 08:00am and 05:00pm local time. (Handled by CWINS on E0135 if this applies to the CLEC.)

- Recurring UNE Charges:

Recurring charges will be applicable to the following components per circuit on each LSR:

- Local Loop (may have mileage)

- Interoffice Facility Termination

- Interoffice Mileage (Minimum mileage is one mile)

- Channelization (3/1 or 1/0)

- Central Office Channel Interface (COCI)

- Non-Recurring UNE Charges:

- The above services may have non-recurring changes in a state.

- Optional Features & Functions:

Clear Channel Capability (B8ZS/ESF) Option per DS1

Clear Channel Capability (B8ZS/SF) Option per DS1

- C-bit parity option per DS3

- The USOC SOMAN will be added to the S&E of the service order to charge for the handling of each circuit on a manual LSR service request. A manual LSR received in the LSC may be via FAX Server, U.S. Mail, or Courier Service.

- State-specific Missed Appointment Credits will apply.

- Expedite charges for shorter intervals will apply.

- Cancellation charges will apply.

- Service Order Modification charges will apply.

MBWC: Since optional multiplexing and interfaces are a part of the higher-bandwidth and lower-bandwidth circuits, respectively, they are billed from those jurisdictions.

SBWC: Optional multiplexing and interfaces may be a part of a SBWC and if ordered, are billed at wholesale rates.  SBWC facilities will have a wholesale Basic Class of Service.

# Ordering Information

## Ordering Process Description

Ordinarily Combined UNE Combinations are ordered through LSC using the  Local Service Request (LSR) ordering process, unless a Service Inquiry is involved then the combination is ordered through the SE -SSG  (Southeast Sales Support Group) /Account Team.  The same data fields will be used, however the data within certain fields will be unique to identify the type of Ordinarily Combined UNE Combination being ordered.   Ordinarily Combined UNE Combination orders will carry new USOCs (included in this document).  The USOCs will map to the appropriate Service Type for the service being installed (i.e. POTS1 for 2-wire unbundled loop start voice loop, SS11 for DS1 level service, etc.).   If an LOA is used, the APOT fields should contain the host ACTL.

All EEL configurations comprised of DS1 and below and Activity type: New (N), Change (C), and Disconnect (D) may be ordered electronically. To obtain detailed information regarding electronic ordering, refer to the Local Service Ordering Requirements (LSOR).

## Required/Valid Forms

Refer to LSOR for ordering Ordinarily Combined UNE Combinations.  The Service Inquiry (SI) form is required for channelized DS1s and DS3 and above services.   Please contact Account Team if more information is needed regarding this requirement.

## Required Fields by Form

When ordering Ordinarily Combined UNE Combinations other than EELs, the Type of Service (TOS) field second character should be ‘A’ or ‘B’.   Using “9” in this position is reserved for EELs only.   When ordering SBWC, the second character of the TOS should be “G”.

For Multibandwidth Commingling, refer to the LSOR Activities Tables by individual fields for REQTYP A-Commingled-Ordinarily Combined UNEs (OCU)/EELs connected to Wholesale.

For Single Commingling, refer to the LSOR Activities Tables by individual fields for REQTYP A-Single Bandwidth Commingling (SBWC).

## Critical Fields and Entries

NC, NCI, and SECNCI Fields on the LSR Form

CFA field on the LS Form

Note: NC/NCI codes are determined by architecture and not billing jurisdiction.

| Ref | Service Level | NC Code | NCI Code | SECNCI Code | CLEC Interface (CFA) |
| --- | --- | --- | --- | --- | --- |
| 1-4: SBWC Note: All Entrance Facilities (Local Channel) are no longer available as UNEs |
| 1 | 2-wire VG Local Channel, IOC, and Local Channel | LY-- | 02LO2 (LPS) 02GO2 (GST) 02RV2.O (RVB) | 02LS2 (LPS) 02LS2 (GST) 02RV2.T (RVB) | NA |
| 2 | 4-wire VG Local Channel, IOC, and Local Channel | LY-- | 04LO2 (LPS) 04GO2 (GST) | 04LS2 (LPS) 04LS2 (GST) | NA |
| 3 | 56 KBPS Local Channel, Interoffice Channel, and Local Loop | LY-- | 04DU5.56 | 04DU5.56 | NA |
| 4 | 64 KBPS Local Channel, Interoffice Channel, and Local Loop | LY-- | 04DU5.64 | 04DU5.64 | NA |
| 5-7: SBWC Note: All Entrance Facilities (Local Channel) are no longer available as UNEs |
| 5 | DS1 Local Channel and DS1 Local Loop | HC-- (AMI-SF) HCD- (AMI-ESF) HCZ- (B8ZS-SF) HCE- (B8ZS-ESF) | 04DS9.15 04DS9.1K 04DS9.15B 04DS9.1S | 04DU9.BN (AMI-SF) 04DU9.1KN (AMI-ESF) 04DU9.DN (B8ZS-SF) 04DU9.1SN (B8ZS-ESF) | NA |
| 6 | DS3 Local Channel and Loop | HF- - | 04DS6.44 | 04DS6.44 | NA |
| 7 | STS-1 Local Channel and Loop | JI- - | 04ST6.A | 04ST6.A | NA |
| 8-10: SBWC Note: All Entrance Facilities (Local Channel) are no longer available as UNEs |
| 8 | DS1 Local Channel and IOC terminating in collocation | HC-- (AMI-SF) HCD- (AMI-ESF) HCZ- (B8ZS-SF) HCE- (B8ZS-ESF) | 04DS9.15 04DS9.1K 04DS9.15B 04DS9.1S | 04QB9.11 | PE1P1 (physical) or CNC1X (virtual) |
| 9 | DS3 Local Channel and IOC terminating in collocation | HF- - HFC- | 04DS6.44 | 04QB6.33 | PE1P3 (physical) or CNC3X (virtual) |
| 10 | STS-1 Local Channel and IOC terminating in collocation | JI-- | 04ST6.A | 04QB6.S1 | PE1P3 (physical) or CNCSX (virtual) |
| 11-17 Note: Available as EELs or SBWC |
| 11 | 2-wire VG Local Loop and IOC terminating in collocation | LY- - | 02QC3.OOD_LPS) 02QC3.OOB(GST) 02QC3.RVO(RVB) | 02LS2 (LPS) 02GS2 (GST) 02RV2.T(RVB) | PE1P2 (physical) |
| 12 | 4-wire VG Local Loop and IOC terminating in collocation | LY- - | 02QC3.OOD(LPS) 02QC3.OOB(GST) | 04LS2(LPS) 02GS2(GST) | PE1P4 (physical) |
| 13 | 4-wire 56 kbps Local Loop and IOC terminating in collocation | LY- - | 04QC5.OOP | 04DU5.56 | PE1P4 (physical) |
| 14 | 4-wire 64 kbps Local Loop and IOC terminating in collocation | LY- - | 04QC5.OOQ | 04DU5.64 | PE1P4 (physical) |
| 15 | DS1 Local Loop and IOC terminating in collocation | HC—(AMI-SF) HCD- (AMI-ESF) HCZ –(B8ZS-SF) HCE –(B8ZS-ESF) | 04QB9.11 | 04DU9.BN (AMI-SF) 04DU9.1KN (AMI-ESF) 04DU9.DN (B8ZS-SF) 04DU9.1SN (B8ZS-ESF) | PE1P1 (physical) or CNC1X (virtual) |
| 16 | DS3 Local Loop and IOC terminating in collocation | HF- - HFC- | 04QB6.33 | 04DS6.44 | PE1P3 (physical) or CND3X (virtual) |
| 17 | STS-1 Local Loop and IOC terminating in collocation | JI-- | 04QB6.S1 | 04ST6.A | PE1P3 (physical) or CNCSX (virtual) |
| 18-22:MBWC Note: Wholesale Mux must be in place prior to the submission of the Lower Level Services |
| 18 | 2-wire Voice Grade Local Loop and IOC CFA mux | LY-- (LSP) LY-- (GST) LY-- (RVB) | 04QB9.11 | 02LS2 (LPS) 02GS2 (GST) 02RV2.T(RVB) | DS1 mux |
| 19 | 4-wire Voice Grade Local Loop and IOC CFA mux | LY-- (LSP) LY-- (GST) | 04QB9.11 | 04LS2(LPS) 02GS2(GST) | DS1 mux |
| 20 | 4-wire 56 kbps Local Loop and IOC CFA mux | LY- - | 04QB9.11 | 04DU5.56 | DS1 mux |
| 21 | 4-wire 64 kbps Local Loop and IOC CFA mux | LY- - | 04QB9.11 | 04DU5.64 | DS1 mux |
| 22 | DS1 Local Loop and IOC CFA mux | HC—(AMI-SF) HCD- (AMI-ESF) HCZ- (B8ZS-SF) HCE- (B8ZS-ESF) | 04QB6.33 [DS3] 04QB6.S1 [STS-1] | 04DU9.BN (AMI-SF) 04DU9.1KN (AMI-ESF) 04DU9.DN (B8ZS-SF) 04DU9.1SN (B8ZS-ESF) | DS3/STS-1 mux |
| 23- 36: MBWC Note: Wholesale Entrance Facilities and Wholesale Mux must be in place prior to the submission of the Lower Level Services for EELS or MBWC |
| 23 | 2-wire Local Loop and IOC CFA DS1 mux | LY—(LPS) LY- -(GST) LY- -(RVB) | 04DS9.15 04DS9.1K 04DS9.15B 04DS9.1S | 02LS2 (LPS) 02LS2 (GST) 02RV2.T (RVB) | DS1 mux |
| 24 | 4-wire Local Loop and IOC CFA DS1 mux | LY—(LPS) LY—(GST) | 04DS9.15 04DS9.1K 04DS9.15B 04DS9.1S | 04LS2 04GS2 | DS1 mux |
| 25 | 4-wire 56 kbps Local Loop and IOC CFA DS1 Mux | LY- - | 04DS9.15 04DS9.1K 04DS9.15B 04DS9.1S | 04DU5.56 | DS1 mux |
| 26 | 4-wire 64 kbps Local Loop and IOC CFA DS1 Mux | LY- - | 04DS9.15 04DS9.1K 04DS9.15B 04DS9.1S | 04DU5.64 | DS1 mux |
| 31: MBWC Note: All Entrance Facilities (Local Channel) are no longer available as UNEs |
| 31 1st order | Channelized DS1 SPA Local Channel and UNE DS1 IOC with mux in EU SWC | HC-M HCDM HCZM HCEM | 04DS9.15 04DS9.1K 04DS9.15B 04DS9.1S | N/A | NA |
| 31 2nd order | VG/DS0 Local Loop CFA DS1 mux in EU SWC | LY-- | 04DS9.15 04DS9.1K 04DS9.15B 04DS9.1S | 02LS202GS2 02RV2.T 04LS2 04GS2 | DS1 mux |
| 32: MBWC Note: Wholesale Entrance Facilities and Wholesale Mux must be in place prior to the submission of the Lower Level Services |
| 32 | DS1 Interoffice from collocation in EU SWC CFA DS3 [STS-1] mux | HC—(AMI-SF) HCD- (AMI-ESF) HCZ- (B8ZS-SF) HCE- (B8ZS-ESF) | 04DS6.44 04ST6.A | 04QB9.11 | PE1P1 (physical) or CNC1X (virtual) and DS3 mux |
| 33-41: EELS Note: For commingled arrangement, see UNE Loop Multiple Bandwidth Commingling - CLEC Information Package. |
| 33 1st order | Channelized DS1 Interoffice Channel terminating in POP SWC collocation | HC-M (AMI-SF) HCDM (AMI-ESF) HCZM (B8ZS-SF) HCEM (B8ZS-ESF) | 04QB9.11 | NA | PE1P1 (physical) or CNC1X (virtual) |
| 33 2nd order | 2-wire VG Local Loop CFA DS 1 mux in EU SWC | LY- - | 04QB9.11 (LPS) 04QB9.11 (GST) 04QB9.11 (RVB) | 02LS2 (LPS) 02GS2 (GST) 02RV2.T (RVB) | DS1 Mux |
| 34 1st order | Channelized DS1 Interoffice Channel terminating in POP SWC collocation | HC-M (AMI-SF) HCDM (AMI-ESF) HCZM (B8ZS-SF) HCEM (B8ZS-ESF) | 04QB9.11 | NA | PE1P1 (physical) or CNC1X (virtual) |
| 34 2nd order | 4-wire VG Local Loop CFA DS 1 mux in EU SWC | LY- - | 04QB9.11 (LPS) 04QB9.11 (GST) | 04LS2 (LPS) 04GS2 (GST) | DS1 Mux |
| 35 1st order | Channelized DS1 Interoffice Channel terminating in POP SWC collocation | HC-M (AMI-SF) HCDM (AMI-ESF) HCZM (B8ZS-SF) HCEM (B8ZS-ESF) | 04QB9.11 | NA | PE1P1 (physical) or CNC1X (virtual) |
| 35 2nd order | 2-wire ISDN Local Loop CFA DS 1 mux in EU SWC | LY- - | 04QB9.11 | 02IS5 | DS1 Mux |
| 36 1st order | Channelized DS1 Interoffice Channel terminating in POP SWC collocation | HC-M (AMI-SF) HCDM (AMI-ESF) HCZM (B8ZS-SF) HCEM (B8ZS-ESF) | 04QB9.11 | NA | PE1P1 (physical) or CNC1X (virtual) |
| 36 2nd order | 4-wire 56kbps Local Loop CFA to DS 1 mux in EU SWC | LY- - | 04QB9.11 | 04DU5.56 | DS1 Mux |
| 37 1st order | Channelized DS1 Interoffice Channel terminating in POP SWC collocation | HC-M (AMI-SF) HCDM (AMI-ESF) HCZM (B8ZS-SF) HCEM (B8ZS-ESF) | 04QB9.11 | NA | PE1P1 (physical) or CNC1X (virtual) |
| 38 2nd order | 4-wire 64kbps Local Loop CFA DS 1 mux in EU SWC | LY- - | 04QB9.11 | 04DU5.64 | DS1 Mux |
| 39 1st order | Channelized DS3 Interoffice Channel terminating in POP SWC collocation | HF-M HFZM | 04QB6.33 | NA | PE1P3 (physical) or CNC3X (virtual) |
| 40 2nd order | DS1 Local Loop CFA to DS 3 mux in EU SWC | HC- - (AMI-SF) HCD- (AMI-ESF) HCZ- (B8ZS-SF) HCE- (B8ZS-ESF) | 04QB6.33 | 04DU9.BN (AMI-SF) 04DU9.1KN (AMI-ESF) 04DU9.DN (B8ZS-SF) 04DU9.1SN (B8ZS-ESF) | DS3 Mux |
| 41 1st order | Channelized STS-1 Interoffice Channel terminating in POP SWC collocation | JIAA | 04QB6.S1 | NA | PE1P3 (physical) or CNCSX (virtual) |
| 41 2nd order | DS1 Local Loop CFA DS 3 mux in EU SWC | HC- - (AMI-SF) HCD- (AMI-ESF) HCZ- (B8ZS-SF) HCE- (B8ZS-ESF) | 04QB6.33 | 04DU9.BN (AMI-SF) 04DU9.1KN (AMI-ESF) 04DU9.DN (B8ZS-SF) 04DU9.1SN (B8ZS-ESF) | DS3 Mux |

# Notes:

- The NCI always represents the highest service involved in the request.

- The SECNCI, if there is any, always represents the lowest level of service involved.

- Two orders are required for facilities of mixed bandwidth.  One is required for the Higher-Level Portion of Channelized Facility and another is required for the Lower-Level Facility Riding Higher-Level Channelized Portion of Facility.

- UNE elements above are available in the Impaired Serving Wire Center (SWC)

- All Entrance Facilities (Local Channel) are no longer available as UNEs

- In some scenarios mux must be ordered as Wholesale

In addition to the NC, NCI, SECNCI and any CFA fields on the LSR, the REMARKS and APOT fields on the LSR are critical for ordering.  Please populate the REMARKS field with the exact product name you are ordering.

## Any Applicable USOCs and/or FIDs

# Collocation / HTN

| Level of Service | USOC Description | USOC | CFA |
| --- | --- | --- | --- |
| DS1 | Holding USOC | HTN | T3 |
| DS1 | Physical Collocation Cross Connect | PE1P1 | T1TIE |
| DS1 | Physical Collocation Pot Bay | PE1PG | T1TIE |
| DS1 | Virtual Collocation Cross Connect | CNC1X | T1TIE |

# Channelization

| Level of Service | USOC Description | USOC | CFA |
| --- | --- | --- | --- |
| 1/0 multiplexing | DS1 Channelization | MQ1 | NA |
| 3/1 multiplexing | DS3 Channelization | MQ3 | NA |

# Central Office Channel Interface

| Level of Service | USOC Description | USOC |
| --- | --- | --- |
| Voice Grade | Central Office Channel Interface (COCI) | 1D1VG |
| 2-Wire ISDN | Central Office Channel Interface (COCI) | UC1CA |
| Data DS0 | Central Office Channel Interface (COCI) | 1D1DD |
| DS1 | Central Office Channel Interface (COCI) | UC1D1 |

Interoffice Channel

| Level of Service | USOC Description | USOC |
| --- | --- | --- |
| ALL | Interoffice Channel (Per Mile) | 1L5XX |
| 2 Wire Voice Grade | 2 Wire Interoffice Channel (Facility Termination) | U1TV2 |
| 4 Wire Voice Grade | 4 Wire Interoffice Channel (Facility Termination) | U1TV4 |
| 4 Wire Data DS0 | 4 Wire 56KB Interoffice Channel (Facility Termination) | U1TD5 |
| 4 Wire Data DS0 | 4 Wire 64KB Interoffice Channel (Facility Termination) | U1TD6 |
| DS1 | DS1 Interoffice Channel (Facility Termination) | U1TF1 |
| DS3 | DS3 Interoffice Channel (Facility Termination) | U1TF3 |
| STS-1 | STS-1 Interoffice Channel (Facility Termination) | U1TFS |

# Loop

| Level of Service | USOC Description | USOC |
| --- | --- | --- |
| DS3 & above | Local Loop Mileage | 1L5ND |
| 2 Wire Voice Grade analog | 2 Wire Voice Grade Loop | UEAL2 |
| 4 Wire Voice Grade analog | 4 Wire Voice Grade Loop | UEAL4 |
| 2-wire ISDN BRI | 2-wire ISDN BRI | U1L2X |
| 4 Wire 56KB Data DS0 | 4 Wire 4KB Data Loop | UDL56 |
| 4 Wire 64KB Data DS0 | 4 Wire 64KB Data Loop | UDL64 |
| DS1 | DS1 Loop | USLXX |

# Pricing

# All pricing is specific to the CLEC’s Interconnection Agreement.

# Intervals

All Due Date/Intervals are calculated upon the receipt of an error free LSR from the CLEC and can be found in the Interval Guide section of the Standard Due Date Interval Website

# Provisioning

ACAC will provision orders for wholesale circuits.

CWINS will provision orders for UNE circuits.

# Maintenance and Repair Process

- AT&T will maintain and repair the facilities and equipment that it furnishes. The customer or customer’s end-user may not rearrange, disconnect, remove, or attempt to repair any equipment installed by AT&T.

- The customer is responsible for testing and isolation of all troubles to the AT&T network. AT&T is responsible for testing, sectionalizing, and repair of all customer-reported troubles. The trouble reporting procedure must conform to the established trouble receipt process.

- Customer Wholesale Interconnection Network Service (CWINS) will process EO-135 charges based on applicable tariff rules.

	The CWINS will handle CLEC calls as they do for CLEC referrals.

	Maintenance intervals for unbundled transport are the same as the maintenance for comparable services ordered as retail service.

	The CWINS will enter the CLEC trouble report in WFA-C and test to isolate the source of the trouble.  The WFA ticket will be dispatched to the Central Office as needed for additional testing or trouble resolution.

	The CLEC may call to request status on the report or escalate to CWINS management if commitment time is exceeded.  After all problems within the AT&T area of responsibility have been tested and corrected, the CWINS Technician will contact the CLEC to report the results of testing and repair.

The following apply to commingled orders:

For MBWC situations, the CLEC must diagnose which circuit has the trouble and contact the appropriate service center, i.e. ACAC (wholesale circuits) or CWINS (UNE circuits).  If through AT&T trouble-shooting AT&T determines the trouble is in the other circuit, there will be a soft hand off between AT&T centers.

# Text boxes

EU

Loop

IOC

EU SWC

### Channelized Loop/Transport terminating in POP SWC

EU

Collo

POP SWC

M

EU SWC

UNE IOC

UNE Loop

Collo

M

POP SWC

Collo

EU SWC

M

POP SWC

POP

Wholesale

Local Channel

IOC

POP

EU

M

Wholesale

Local Channel

POP SWC

EU SWC

UNE

IOC

UNELoop

IOC

Loop

POP

POP SWC

M

EU

EU SWC

Wholesale

Local Channel

EU SWC

POP SWC

EU

POP

Wholesale

Local Channel

IOC

Loop

EU

### Non-channelized Facilities

Collo

EU SWC

POP SWC

IOC

Loop

Non-channelized to collocation

Collo

EU

SWC

POP

SWC

POP

Wholesale

Local Channel

IOC

POP/EU SWC

EU

POP

Wholesale

Local Channel

Loop

LEGEND:

POP: Point of Presence

SWC: Serving Wire Center

EU: End User

IOC: Interoffice Channel

M: Multiplexer

NA: Not Applicable

Collo: Collocation

---- : lower-level