21 ISDN

21.1 ISDN

21.1.1 Description

ISDN Individual Line Business Service (IBS) and Individual Line Residence Service (IRS) are groups of IntraLATA offerings supported by the Integrated Services Digital Network (ISDN) architecture. These services support simultaneous transmission of voice, data and packet services over the same exchange access line.

ISDN Individual Line Business/Residence Services are offered via “Basic Rate” access / interface technology. This Basic Rate interface provides for up to two 64 kilobits (kbps) “Bearer” (B) channels and one 16 kbps “D” channel.

Basic service capabilities provided over ISDN channels are: B channels which are provisioned for circuit switched voice/data provide bi-directional synchronous channels capable of supporting the inter-office transmission of voice or data. This option permits the user to utilize either circuit switched voice or data (CSV/D) transmission paths on a per call basis.

- Circuit Switched Voice/Data (CSV/ D), and/or

- Packet Switched Data (PSD).

B channels which are provisioned for ISDN packet switched data utilize a data transport service based on the CCITT X.25 protocol. These B channels provide for transmission of packet data at a throughput of up to 64 kbps.

Each D-channel is a 16 kbps digital signaling channel that can also be provisioned to be capable of supporting 9.6 kbps of packet data. Enhancements to the basic IBS/IRS packet service are available through vendors who subscribe to BellSouth's PulseLink Public Packet Switching Network service BellSouth® Telecommunications, Inc., (d/b/a AT&T Alabama, AT&T Florida, AT&T Georgia, AT&T Kentucky, AT&T Louisiana, AT&T Mississippi, AT&T North Carolina, AT&T South Carolina, AT&T Tennessee -collectively referred to for purposes of this document as “AT&T Southeast Region”.)

ISDN Individual Line service may be offered as the standard “National-ISDN 1 ” or as Custom ISDN. Either National or Custom ISDN allows for BRI offerings in some combination below the standard, (i.e., “1B+D”, “0B+D”, etc.). All ISDN capable central offices are equipped with National ISDN 1 software.

IBS/IRS is offered in following pricing configurations: The Threshold Pricing plan allows up to a specified number of minutes-of-use per month, per DSL at a flat rate. Usage rates apply for minutes-of-use above the specified threshold. All pricing options are not available in all states. Use the “USOC / Feature Code” table as a guide for pricing options by state. Refer to General Subscriber Services Tariff (GSST) for a comprehensive list of state pricing options.

- Flat Rate “Non-Threshold Pricing” Service

- Usage Sensitive Service

- Flat Rate “Threshold Pricing” Service (currently available in FL, GA, KY, MS, and SC only.)

ORDERING CONSIDERATIONS

AT&T Southeast Region Carrier Account Team involvement is recommended when ordering IBS/IRS. The Universal Service Ordering Codes (USOCs) and Field Identifier Detail (FIDs) associated with ordering IBS/IRS vary significantly, depending on the central office type from which service is provisioned. Utilize the information contained within this section and the GSST to provide compatibility of basic ordering detail. Additional switch-specific ordering documentation may be available through account teams servicing reseller accounts.

The negotiator/reseller is responsible for securing circuit numbers and the appropriate quantity of telephone numbers for each B-channel and Secondary Directory number activated. Additionally, the negotiator/reseller is responsible for determining if IBS/IRS is available in the end-user location through verification in the Products & Services Inventory Management System (P/SIMS). This should include noting the central office type (5ESS, DMS 100, or EWSD), and the type of ISDN service that is available within that office, (i.e., National or Custom ISDN).

After determining that the end-user central office is capable of supporting IBS/IRS, a request for service may be initiated. Effective January 1998, requests for IBS /IRS will carry a fifteen (15) day “conditional” due date that will include a “service inquiry” process. This inquiry process will determine if cable and pair facilities are available to serve the end-user location. If facilities do not exist to serve the user, he/she will be notified within this 15 day interval and a new due date will be negotiated. If adequate facilities are available the due date will remain “as-is”, requiring no further user notification.

The ordering of IBS/IRS is accomplished by selecting an appropriate “Basic Class of Service (BCS)” and elements from the following tariff categories: IBS/IRS provisioned from a central office other than the one from which the end-user is normally served will require interoffice facilities per DSL.

- The Basic Rate Interface (BRI). BRI is provisioned via a Digital Subscriber Loop (DSL), which provides the end-user with a local transport loop (wire pair) and central office switching electronics.

- Channel Activation. The specific use of the DSL is specified by selecting a channel configuration. Within the DSL at least one channel, “B” or “D”, must be ordered and activated. Each Basic Rate Interface / DSL supports a maximum of two B-channels and a maximum of one D-channel.

- User Profile Services. Define the ISDN services to which a given end-user has access. Users are required to subscribe to at least one Profile Service, related to either a “B” or “D” channel. A maximum of eight User Profiles may be associated with any DSL.

When ordering IBS/IRS at least one element from each of the aforementioned categories must be selected. These basic ordering elements may be selected by using the “USOC / FEATURE CODE” table contained within this section. Compatibility must exist between selected options for BCS, DSL, Channel Activation, and User Profiles categories. For example, if a measured rate BCS USOC is selected, then the USOCs associated with channel activation and user profiles must reflect measured service in their definitions. Additionally, Customer Premises Equipment (CPE) that is compatible with the ISDN interface must be provided by the end-user. This station/terminal equipment may be an Electronic Key Telephone Set (EKTS) or a non-EKTS device. Calling/Called Number Delivery and Call Hold are features that are provided with IBS/IRS. Additional features are available as options, and may be subscribed to on an as-needed basis. These optional features may be selected from section A.42 of the GSST.

ISDN PACKAGES

To simplify BRI - ISDN ordering, customers may order ISDN service by selecting from several “package” offerings. Capability Package “S” (CPS) offers basic IBS/IRS, and is available with National ISDN lines in both Threshold and Non-Threshold configurations. Super-set “EZ” packages EZ1, EZ1A, EZ2 and EZ2A offer enhanced IBS/IRS, and are available for use with National ISDN lines in both Threshold and Non-Threshold configurations. The EZ packages, with corresponding credits, have only been tariffed in connection with Threshold Pricing. EZ packages may be ordered in Non-Threshold configurations, but these packages will not receive a credit. Packages are not available on Custom ISDN lines.

Package Descriptions: 
Capability Package “S”- 
Supports non-EKTS equipment. Package includes:

- Low Speed DSL

- Two (2) B-channel CSV/CSD - Channel Activation

- Two (2) B-channel CSV/CSD - User Profile.

Package EZ1- 
Supports non-EKTS equipment. Package includes:

- Low Speed DSL

- Two (2) B-channel CSV/CSD - Channel Activation

- Two (2) B-channel CSV/CSD - User Profile

- Two (2) Additional Call Offerings

- One (1) Conference, Drop, Hold & Transfer

- One (1) Call Forwarding Variable (Feature Button)

Package EZ1A- 
Supports non-EKTS equipment. Package includes: Voice Mail service is an option with this package

- Low Speed DSL

- Two (2) B-channel CSV/CSD - Channel Activation

- Two (2) B-channel CSV/CSD - User Profile

- Two (2) Additional Call Offerings

- One (1) Conference, Drop Hold, & Transfer

- One (1) Call Forwarding Variable (Feature Button)

- Visual Message Waiting

- Call Forwarding Busy Line

- Call Forwarding Don't Answer

Package EZ2- 
Supports one EKTS and one non-EKTS user. Package includes:

- Low Speed DSL

- Two (2) B-channel CSV/CSD - Channel Activation

- Two (2) B-channel CSV/CSD - User Profile

- Two (2) Additional Call Appearances

- One (1) Conference, Drop, Hold & Transfer

- One (1) Call Forwarding Variable (Feature Button)

- Two (2) Secondary only, Directory Numbers (DN)

Package EZ2A - 
Supports one EKTS and one non-EKTS user. Package includes: Voice Mail service is an option with this package.

- Low Speed DSL

- Two (2) B-channel CSV/CSD - Channel Activation

- Two (2) B-channel CSV/CSD - User Profile

- Two (2) Additional Call Appearances

- One (1) Conference, Drop, Hold & Transfer

- One (1) Call Forwarding Variable (Feature Button)

- Two (2) Secondary only, Directory Numbers (DN)

- Visual Message Waiting

- Call Forwarding Busy Line

- Call Forwarding Don't Answer

In states where the EZ packages are tariffed, a credit will be applied to the monthly billing for customers purchasing IBS/IRS via one of the four “EZ” packages. This credit is given to the customer each month via a credit USOC. This credit is not available in states where the EZ packages, and corresponding credit, have not been tariffed. EZ packages must be ordered exactly as indicated in the tariffs. If any feature listed in the package description is deleted or provisioning options changed, the package credit will no longer apply.

Additional optional features compatible with the package configurations are allowed with the packages. These features may only be added to the User Profile that is already provisioned with features. The addition of one D-Channel Low Speed Packet is allowed per package.

The “EZ” package credit is applied by using specific USOCs:

Term Definition Package EZ1 Credit LPEO1 Package EZ1A Credit LPE1A Package EZ2 Credit LPEO2 Package EZ2A Credit LPE2A

There are no credits associated with Capability Package “S”.
Ordering Capability Package “S” in Non-Threshold Service Areas (Flat Rate Service, - 5ESS Central Office)

Refer to the Ordering Considerations section of this document for pre-order activities. Orders that are issued for packages must show the FID “ICPK” followed by the package identifier. This FID is floated behind the Digital Subscriber Line (DSL) USOC.

Following is an example of a CPS service order:

Ordering an EZ Package in THRESHOLD PRICING Service Areas (Provisioned from a - 5ESS central office) 
Refer to the Ordering Considerations section of this document for pre-order activities. Orders that are issued for packages must show the FID “ICPK” followed by the package identifier. This fid is floated behind the Digital Subscriber Line (DSL) USOC. Additionally, “EZ” package orders should reflect the USOC that assigns a credit specific to that package.

Following is an example of an ISDN EZ package service order:

S&E					Explanation

I1		NONB1				Wiring related USOCs

I1		NONB2										I1		NONB6/BI WIC

I1		LPE1A					Credit USOC for EZ1A

I1		S4B					Basic Class of Service-											(Business)

IG1		KS 1/TSW 5E				Key System/C.O. Switch Type

/ITTYP1-A	DISP/TCGU CGSTDPK1		Terminal Type

/ITTYP2-A	DISP

I1		LQTTB/CLS				DSL,-(Business)/Circuit ID

21.1.2 Restrictions

- Available where central office and outside plant facilities permit.

- Customer is responsible for provisioning and ensuring compatibility of Customer Premises Equipment (CPE) with ISDN Individual Line Service Interface specifications. Suspension of service is not allowed.

- A minimum service period of three months will be required on the Flat Rate Threshold Pricing Plan.

Please refer to the General Services Subscriber Tariff (GSST) for a complete list of limitations and restrictions associated with this service.

21.1.3 Tariff References

Please refer to Section A.42 of the GSST for details regarding IBS/IRS, including:

- Current package offering definitions and conditions.

- A comprehensive list of channel options and optional features.

- A comprehensive list of state specific pricing options associated with this service.

- Description of ISDN Packet Switching Services and its associated usage rates.

Refer to Section A.29 of the GSST for usage rates and details regarding PulseLink® Public Packet Switching Network service. Circuit Switched usage rates are specified in Section A3 of the GSST.

21.1.4 USOC/FID References

The provisioning of IBS/IRS utilizes a vast array of USOCs/FIDs, depending upon combinations of the following:

- State in which service is requested

- National ISDN versus Custom ISDN service

- Electronic Key Telephone Set (EKTS) versus Non-EKTS utilized

- Optional Features selected

- IBS/IRS Central Office Switch Type

Please refer to the General Services Subscriber Tariff (GSST) for a comprehensive list of USOCs associated with these combinations.

Table 205. ISDN "Non-Threshold Pricing" -- Service Elements

USOC FEATURE CODE RES BUS DESCRIPTION 1A ESS DM DM-R 5E 5E-R EW SBCR D-10 AL FL GA KY LA MS NC SC TN BASIC CLASSES OF SERVICE LTRUK Flat Rate, Schools X X X LTA5K Measured Rate, Schools X X X LTA5R X Measured Rate, Res X X X X 6 X X 6 X X LTE5B X Measured Rate, Bus X X X X 6 X X 6 X X LTFDK Measured Rate, Schools X X X LTFDR X Measured Rate, Res X X X X6 X X6 X X LTKDB X Measured Rate, Bus X X X X6 X X6 X X LTNMR X Message Rate, Res X X X6 USOC FEATURE CODE RES BUS DESCRIPTION 1A ESS DM DM-R 5E 5E-R EW SBCR D-10 AL FL GA KY LA MS NC SC TN LTPMB X Message Rate, Bus X X X6 LTRJB X Flat Rate, Bus X X X X6 X6 X6 X X6 X X6 X LTRJK Flat Rate, Schools X X X LTRJR X Flat Rate, Res X X X X6 X6 X6 X X6 X X6 X LTRUB X Flat Rate, Bus X X X X6 X6 X6 X X6 X X6 X LTRUR X Flat Rate, Res X X X X6 X6 X6 X X6 X X6 X LTSDR X Message Rate, Res X X X6 LTTDB X Message Rate, Bus X X X6 S1B X Flat Rate, Bus X X X6 X6 X6 X X6 X X6 X S1R X Flat Rate, Res X X X6 X6 X6 X X6 X X6 X S1S X Measured Rate, Bus X X6 X6 X6 X S2S Measured Rate, Schools X X6 X6 X6 X S2B X Measured Rate, Bus X X X6 X6 X6 X X6 X X6 X S2R X Measured Rate, Res X X X6 X6 X6 X X6 X X6 X S3B X Message Rate, Bus X X6 X6 X6 X6 X6 BASIC RATE NTERFACE - DIGITAL SUBSCRIBER LOOP (DSL) USOC FEATURE CODE RES BUS DESCRIPTION 1A ESS DM DM-R 5E 5E-R EW SBCR D-10 AL FL GA KY LA MS NC SC TN S3R X Message Rate, Res X X6 X6 X6 X X6 X6 LTBLB X 5ESS/DMS DSL X X X X X X X X LTBLR X 5ESS/DMS DSL X X X X X X X X LTCHC X 5ESS/DMS High Speed Packet DSL X X X X X X X X LTCHR X 5ESS/DMS High Speed Packet DSL X X X X X X X X LTBEB X EWSD DSL X X X X LTBER X EWSD DSL X X X X LTCEB X EWSD High Speed Packet DSL X X X X LTCER X EWSD High Speed Packet DSL X X X X CHANNEL ACTIVATION LPRFX X X CSV/CSD, B Channel , Flat Rate Svc X X X X X X X X X LPSMX X X CSV/CSD, B Channel, Measured Rate Svc X X X X X X X X X USOC FEATURE CODE RES BUS DESCRIPTION 1A ESS DM DM-R 5E 5E-R EW SBCR D-10 AL FL GA KY LA MS NC SC TN LPUNX X X CSV/CSD, B Channel ,Message Rate Svc X X X X X X X X LPWHX X X Permanent High Speed Packet, B Channel X X X X X X X X X LPXOX 1, 3 X X On-Demand High Speed Packet, B Channel X X X X X X X X X2 LPYLX X D Channel Low Speed Packet, with B Channel Service X X X X X X X X LTQDX X D Channel Low Speed Packet as Single Service X X X X X X X X X USER PROFILE EWSTP X X Terminal Service Profile (EWSD) X X X X X LTQ8Y X X Flat Rate Access to B Channel CSV/CSD X X X X X X X X USOC FEATURE CODE RES BUS DESCRIPTION 1A ESS DM DM-R 5E 5E-R EW SBCR D-10 AL FL GA KY LA MS NC SC TN LTQ81 X Measured Rate (MR) - Area Calling Service (ACS), Option 1 X X X X X LTQ82 X MR - ACS, Option 2 X X X X X LTQ8P X MR - ACS, Option 1 X X X X X LTQ8Q X MR - ACS, Option 2 X X X X X LTQ86 X MR - RegionServ Svc, without discount X X X X X LTQ87 X MR - RegionServ Svc, discount usage option X X X X X LTQ8A X MR - ACS, Option 1 X X X X X LTQ8B X MR - ACS, Option 2 X X X X X LTQ8F X MR - RegionServ Svc, without discount X X X X X USOC FEATURE CODE RES BUS DESCRIPTION 1A ESS DM DM-R 5E 5E-R EW SBCR D-10 AL FL GA KY LA MS NC SC TN LTQ8G X MR - RegionServ Svc, discount usage option X X X X X LTQ8U X Measured Rate (MR) - ACS, Option 1 X X X LTQ8V X MR - ACS, Option 2 X X X X X LTQCY X X Expanded Local Svc (ELS), Community Caller Plus w/o inward call billing X X X X X LTQEL X X Community Circle Plan (CCP)-, Community Caller Plus w/o inward call billing X X X X X LTQVB 4 X Flat Rate Access to B Channel CS-Voice -(EWSD) X X X X USOC FEATURE CODE RES BUS DESCRIPTION 1A ESS DM DM-R 5E 5E-R EW SBCR D-10 AL FL GA KY LA MS NC SC TN LTQVN X Measured Rate (MR) - ACS (ACS), Option 1- (EWSD-VOICE) X X LTQVO X MR - ACS, Option 2- (EWSD-VOICE) X X LTQVP X MR - Local Optional Svc (LOS), Option 1- (EWSD-VOICE) X X LTQVQ X MR - LOS, Option 2- (EWSD-VOICE) X X LTQAV X CCP-, Community Caller Plus w/o inward call billing (EWSD-VOICE) X X LTQCV X X Expanded Local Svc (ELS), Community Caller Plus w/o inward call billing, (EWSD-VOICE) X X USOC FEATURE CODE RES BUS DESCRIPTION 1A ESS DM DM-R 5E 5E-R EW SBCR D-10 AL FL GA KY LA MS NC SC TN LTQVR X Flat Rate Access to B Channel CS-Voice -(EWSD) X X X X X LTQV1 X MR - ACS, Option 1- (EWSD-VOICE) X X LTQV2 X MR - ACS, Option 2- (EWSD-VOICE) X X LTQVU X MR - LOS, Option 1- (EWSD-VOICE) X X LTQVV X MR - LOS, Option 2- (EWSD-VOICE) X X LTQNV X CCP-, Community Caller Plus w/o inward call billing (EWSD-VOICE) X X LTQDB 4 X Flat Rate Access to B Channel CS-Data -(EWSD) X X X X X USOC FEATURE CODE RES BUS DESCRIPTION 1A ESS DM DM-R 5E 5E-R EW SBCR D-10 AL FL GA KY LA MS NC SC TN LTQDN X MR - ACS, Option 1- (EWSD-DATA) X X LTQDO X MR - ACS, Option 2- (EWSD-DATA) X X LTQDP X MR - LOS, Option 1- (EWSD-DATA) X X LTQDQ X MR - LOS, Option 2- (EWSD-DATA) X X LTQAD X CCP, Community Caller Plus w/o inward call billing (EWSD-DATA) X X LTQCD X X ELS, Community Caller Plus w/o inward call billing, (EWSD-DATA) X X LQTDR X Flat Rate Access to B Channel CS-Data -(EWSD) X X X X X USOC FEATURE CODE RES BUS DESCRIPTION 1A ESS DM DM-R 5E 5E-R EW SBCR D-10 AL FL GA KY LA MS NC SC TN LTQD1 X MR - ACS, Option 1- (EWSD-DATA) X X LTQD2 X MR - ACS, Option 2- (EWSD-DATA) X X LTQDU X MR -LOS, Option 1- (EWSD-DATA) X X LTQDV X MR - LOS, Option 2- (EWSD-DATA) X X LTQND X CCP-, Community Caller Plus w/o inward call billing (EWSD-DATA) X X LTQ3X X X Access to B Channel Permanent High Speed Pkt, without Unique DN X X X X X X X X X USOC FEATURE CODE RES BUS DESCRIPTION 1A ESS DM DM-R 5E 5E-R EW SBCR D-10 AL FL GA KY LA MS NC SC TN AAQ3X 5 X X Access to B Channel Permanent High Speed Pkt, without Unique DN X X X X X X X X LTQ7X 5, 1 X X Access to On-Demand B Channel High Speed Pkt, with Unique DN X X X X X X X2 AAQ7X X X Access to On-Demand B Channel High Speed Pkt, without Unique DN X X X X X X X LTQ4O X X Access to D Channel Low Speed Pkt as Single Service X X X X X X X X X LTQ4X X X Access to D Channel Low Speed Pkt with Unique DN X X X X X X X X X USOC FEATURE CODE RES BUS DESCRIPTION 1A ESS DM DM-R 5E 5E-R EW SBCR D-10 AL FL GA KY LA MS NC SC TN AAQ4X X X Access to D Channel Low Speed Pkt without Unique DN X X X X X X X X X PACKAGE OPTIONS X X Capability Package "S" (CPS) 9 X X X X X X X X X X X Package EZ1 (EZ1) 9 X X X X X X X X X X X Package EZ1A (EZ1A ) 9 X X X X X X X X X X X Package EZ2 (EZ2) 9 X X X X X X X X X X X Package EZ2A (EZ2A) 9 X X X X "EZ" CREDIT USOCs LPEO1 X X Package EZ1 Credit 9 X X X X X X 10 X 10 X 10 X 10 LPE1A X X Package EZ1A Credit 9 X X X X X X 10 X 10 X 10 X 10 LPEO2 X X Package EZ2 Credit 9 X X X X X X 10 X 10 X 10 X 10 LPE2A X X Package EZ2A Credit 9 X X X X X X 10 X 10 X 10 X 10 NOTES: 1 - On Demand High Speed Packet (B Channel), requires basic B Channel activation 2 - Available in 5E Central Office only 3 - On Demand High Speed Packet available only on EWSD 4 - Both Voice and Data USOCs are required when served from "EW" Central Office 5 - Shares a Directory Number (DN) with any other bearer service on same (5E or EW) user profile 6 - Class of service grandfathered relative to new service, moves, or additions to ISDN service in these areas. See "Threshold Pricing" 9 - Class of Service USOCs for orders pertaining to aforementioned activities. 10 - Package available on National ISDN lines only. USOC is "zero-rated" in these states.

Table 206. ISDN "Threshold" Pricing -- Service Elements

USOC FEATURE CODE RES BUS DESCRIPTION 1A ESS DM DM-R 5E 5E-R EW SBCR D-10 AL FL GA KY LA MS NC SC TN BASIC CLASSES OF SERVICE S4R X Threshold Pricing, - Residence Service X X X X X X X X X X S4B X Threshold Pricing, -Business Service X X X X X X X X X X S4S Threshold Pricing, -Schools (K-12) X X X X X X X X X X BASIC RATE INTERFACE - DIGITAL SUBSCRIBER LOOP (DSL) X X X X X LQTTB X 5ESS/DMS DSL X X X X X X X X X LQTTR X 5ESS/DMS DSL X X X X X X X X X LQTHB X 5ESS/DMS High Speed Packet DSL X X X X X X X X X LQTHR X 5ESS/DMS High Speed Packet DSL X X X X X X X X X USOC FEATURE CODE RES BUS DESCRIPTION 1A ESS DM DM-R 5E 5E-R EW SBCR D-10 AL FL GA KY LA MS NC SC TN LQTEB X EWSD DSL X X X X X X LQTER X EWSD DSL X X X X X X LQTDB X EWSD High Speed Packet DSL X X X X X X LQTDR X EWSD High Speed Packet DSL X X X X X X CHANNEL ACTIVATION X X X X X LQGFX X X CSV/CSD Threshold Pricing, B Channel X X X X X X X X X X LQGHX X X Permanent High Speed Packet, B Channel X X X X X X X X X X LQGOX X X On-Demand High Speed Packet, B Channel X X X X X X X X X LQRLB X D Channel Low Speed Packet with B Channel Service X X X X X X X X X X LQRDB X D Channel Low Speed Packet as Single Service X X X X X X X X X X USER PROFILE EWSTQ X X Terminal Service Profile (EWSD) X X X X X X USOC FEATURE CODE RES BUS DESCRIPTION 1A ESS DM DM-R 5E 5E-R EW SBCR D-10 AL FL GA KY LA MS NC SC TN LQAFX X X Threshold Pricing B Channel CSV/CSD X X X X X X X X X LQAVX X X Threshold Pricing B Channel, CS-VOICE X X X X X X LQADX X X Threshold Pricing B Channel, CS-DATA X X X X X X LQAAX X X B Channel Permanent High Speed Pkt, with Unique DN X X X X X X X X X X LQABX X X B Channel Permanent High Speed Pkt, without Unique DN X X X X X X X X X X LQACX X X On-Demand B Channel High Speed Pkt, with Unique DN X X X X X X X X LQAOX X X On-Demand B Channel High Speed Pkt, without Unique DN X X X X X X X X X X USOC FEATURE CODE RES BUS DESCRIPTION 1A ESS DM DM-R 5E 5E-R EW SBCR D-10 AL FL GA KY LA MS NC SC TN LQCAX X X D Channel Low Speed Pkt as Single Service X X X X X X X X X X LQCCX X X D Channel Low Speed Pkt with Unique DN X X X X X X X X X X LQCOX X X D Channel Low Speed Pkt without Unique X X X X X X X X X X LQCPX X X D-Channel Low Speed Packet with Unique DN (for use with ISDN packages) X X X X X X X X X X PACKAGE OPTIONS X X Capability Package "S" (CPS) X X X X X X X X X X X X Package EZ1 (EZ1) 9 X X X X X X X X X X X X Package EZ1A (EZ1A ) 9 X X X X X X X X X X X X Package EZ2 (EZ2) 9 X X X X X X X X X X X X Package EZ2A (EZ2A) 9 X X X X X X X X X X "EZ" PACKAGE CREDITS USOC FEATURE CODE RES BUS DESCRIPTION 1A ESS DM DM-R 5E 5E-R EW SBCR D-10 AL FL GA KY LA MS NC SC TN LPE01 X X Package EZ1 Credit 9 X X X X X X X X X X LPE1A X X Package EZ1A Credit 9 X X X X X X X X X X LPE02 X X Package EZ2 Credit 9 X X X X X X X X X X LPE2A X X Package EZ2A Credit 9 X X X X X X X X X X NOTES: 1 - On Demand High Speed Packet (B Channel), requires basic B Channel activation 2 - Available in 5E Central Office only 3 - On Demand High Speed Packet available only on EWSD 4 - Both Voice and Data USOCs are required when served from "EW" Central Office 5 - Shares a Directory Number (DN) with any other bearer service on same (5E or EW) user profile 6 - Class of service grandfathered relative to new service, moves, or additions to ISDN service in these areas. See "Threshold Pricing Class of Service USOCs for orders pertaining to aforementioned activities. 9 - Packages and credits are available on National ISDN lines only.

Table 207. USOCs Common To "Threshold" and "Non-Threshold" ISDN

USOC FEATURE CODE RES BUS DESCRIPTION 1A ESS DM DM-R 5E 5E-R EW SBCR D-10 AL FL GA KY LA MS NC SC TN INTEROFFICE MILEAGE (Per DSL) M1GNC X X First Mile X X X X X X X X X X X X X X M1GNM X X Each additional mile X X X X X X X X X X X X X X OPTIONAL FEATURE SAMPLING LLAVP X X Visual Message Waiting Indicator X X X X X X X X X X X X X X LLNCV X X Call Forwarding Variable X X X X X X X X X X X X X X USOC FEATURE CODE RES BUS DESCRIPTION 1A ESS DM DM-R 5E 5E-R EW SBCR D-10 AL FL GA KY LA MS NC SC TN LLQCV X X Call Forwarding Busy Line X X X X X X X X X X X X X X LLSCV X X Call Forwarding Don't Answer X X X X X X X X X X X X X X DS1FJ X X Shared Primary DN X X X X X X X X X X X X X X DS1FN X X Conference Drop, Hold, Transfer X X X X X X X X X X X X X X DS1FG X X Additional Call Appearance X X X X X X X X X X X X X X GJXCF X X Call Forwarding Variable, Feature Button X X X X X X X X X X X NOTES: All Fids normally associated with the listed features are applicable when ordering IBS/IRS

Table 208. USOC / FID Feature Detail Table (Section 1 of 4)

FID / FEATURE DETAIL ACOS ADSR BCN BS CAPI CAPP CAT CHD CLS CSGP CSO DCLS USOC / FEATURE CODE LTRUK LTA5K LTA5R LTE5B LTFDK LTFDR LTKDB FID / FEATURE DETAIL ACOS ADSR BCN BS CAPI CAPP CAT CHD CLS CSGP CSO DCLS USOC / FEATURE CODE LTNMR LTPMB LTRJB LTRJK LTRJR LTRUB LTRUR LTSDR LTTDB S1B S1R S1S S2S S2B S2R S3B S3R DIGITAL SUBSCRIBER LINE LTBLB X X X X X LTBLR X X X X X LTCHC X X X X X FID / FEATURE DETAIL ACOS ADSR BCN BS CAPI CAPP CAT CHD CLS CSGP CSO DCLS USOC / FEATURE CODE LTCHR X X X X X LTBEB X X X X X LTBER X X X X X LTCEB X X X X X LTCER X X X X X CHANNEL ACTIVATION LPRFX X X LPSMX X X LPUNX X X LPWHX X X LPXOX X X LPYLX X LTQDX X USER PROFILE EWSTP LTQ8Y X X X X X X LTQ81 X X X X X X LTQ82 X X X X X X LTQ8P X X X X X X LTQ8Q X X X X X X LTQ86 X X X X X X FID / FEATURE DETAIL ACOS ADSR BCN BS CAPI CAPP CAT CHD CLS CSGP CSO DCLS USOC / FEATURE CODE LTQ87 X X X X X X LTQ8A X X X X X X LTQ8B X X X X X X LTQ8F X X X X X X LTQ8G X X X X X X LTQ8U X X X X X X LTQ8V X X X X X X LTQCY X X X X X X LTQEL X X X X X X LTQVB X X X X X X LTQVN X X X X X X LTQVO X X X X X X LTQVP X X X X X X LTQVQ X X X X X X LTQAV X X X X X X LTQCV X X X X X X LTQVR X X X X X X LTQV1 X X X X X X LTQV2 X X X X X X LTQVU X X X X X X FID / FEATURE DETAIL ACOS ADSR BCN BS CAPI CAPP CAT CHD CLS CSGP CSO DCLS USOC / FEATURE CODE LTQVV X X X X X X LTQNV X X X X X X LTQDB X X X X X X LTQDN X X X X X X LTQDO X X X X X X LTQDP X X X X X X LTQDQ X X X X X X LTQAD X X X X X X LTQCD X X X X X X LQTDR X X X X X X LTQD1 X X X X X X LTQD2 X X X X X X LTQDU X X X X X X LTQDV X X X X X X LTQND X X X X X X LTQ3X X X X X X X AAQ3X X X X X X X LTQ7X X X X X X X AAQ7X X X X X X X LTQ4O X X X X X X FID / FEATURE DETAIL ACOS ADSR BCN BS CAPI CAPP CAT CHD CLS CSGP CSO DCLS USOC / FEATURE CODE LTQ4X X X X X X X AAQ4X X X X X X X BASIC CLASSES OF SERVICE S4R S4B S4S DIGITAL SUBSCRIBER LINE LQTTB X X X X X LQTTR X X X X X LQTHB X X X X X LQTHR X X X X X LQTEB X X X X X LQTER X X X X X LQTDB X X X X X LQTDR X X X X X CHANNEL ACTIVATION X LQGFX X X LQGHX X X LQGOX X X LQRLB X LQRDB X FID / FEATURE DETAIL ACOS ADSR BCN BS CAPI CAPP CAT CHD CLS CSGP CSO DCLS USOC / FEATURE CODE USER PROFILE EWSTQ LQAFX X X X X X X LQAVX X X X X X X LQADX X X X X X X LQAAX X X X X X X LQABX X X X X X X LQACX X X X X X X LQAOX X X X X X X LQCAX X X X X X X LQCCX X X X X X X LQCOX X X X X X X LQCPX X X X X X X

Table 209. USOC / FID Feature Detail Table (Section 2 of 4)

FID / FEATURE DETAIL DPG DSNA FC FCA ICPK KEY KS KSH LCC LPCA LPIC LKLD USOC / FEATURE CODE LTRUK X LTA5K X LTA5R X LTE5B X FID / FEATURE DETAIL DPG DSNA FC FCA ICPK KEY KS KSH LCC LPCA LPIC LKLD USOC / FEATURE CODE LTFDK X LTFDR X LTKDB X LTNMR X LTPMB X LTRJB X LTRJK X LTRJR X LTRUB X LTRUR X LTSDR X LTTDB X S1B X S1R X S1S X S2S X S2B X S2R X S3B X S3R X FID / FEATURE DETAIL DPG DSNA FC FCA ICPK KEY KS KSH LCC LPCA LPIC LKLD USOC / FEATURE CODE DIGITAL SUBSCRIBER LINE LTBLB X X X X LTBLR X X X X LTCHC X X X X LTCHR X X X X LTBEB X X X X LTBER X X X X LTCEB X X X X LTCER X X X X CHANNEL ACTIVATION LPRFX LPSMX LPUNX LPWHX LPXOX LPYLX LTQDX USER PROFILE EWSTP LTQ8Y X X X X X X LTQ81 X X X X X X FID / FEATURE DETAIL DPG DSNA FC FCA ICPK KEY KS KSH LCC LPCA LPIC LKLD USOC / FEATURE CODE LTQ82 X X X X X X LTQ8P X X X X X X LTQ8Q X X X X X X LTQ86 X X X X X X LTQ87 X X X X X X LTQ8A X X X X X X LTQ8B X X X X X X LTQ8F X X X X X X LTQ8G X X X X X X LTQ8U X X X X X X LTQ8V X X X X X X LTQCY X X X X X X LTQEL X X X X X X LTQVB X X X X X X LTQVN X X X X X X LTQVO X X X X X X LTQVP X X X X X X LTQVQ X X X X X X LTQAV X X X X X X LTQCV X X X X X X FID / FEATURE DETAIL DPG DSNA FC FCA ICPK KEY KS KSH LCC LPCA LPIC LKLD USOC / FEATURE CODE LTQVR X X X X X X LTQV1 X X X X X X LTQV2 X X X X X X LTQVU X X X X X X LTQVV X X X X X X LTQNV X X X X X X LTQDB X X X X X X LTQDN X X X X X X LTQDO X X X X X X LTQDP X X X X X X LTQDQ X X X X X X LTQAD X X X X X X LTQCD X X X X X X LQTDR X X X X X X LTQD1 X X X X X X LTQD2 X X X X X X LTQDU X X X X X X LTQDV X X X X X X LTQND X X X X X X LTQ3X X X X X X X FID / FEATURE DETAIL DPG DSNA FC FCA ICPK KEY KS KSH LCC LPCA LPIC LKLD USOC / FEATURE CODE AAQ3X X X X X X X LTQ7X X X X X X X AAQ7X X X X X X X LTQ4O X X X X X X LTQ4X X X X X X X AAQ4X X X X X X X BASIC CLASSES OF SERVICE S4R X S4B X S4S X DIGITAL SUBSCRIBER LINE LQTTB X X X X LQTTR X X X X LQTHB X X X X LQTHR X X X X LQTEB X X X X LQTER X X X X LQTDB X X X X LQTDR X X X X CHANNEL ACTIVATION LQGFX FID / FEATURE DETAIL DPG DSNA FC FCA ICPK KEY KS KSH LCC LPCA LPIC LKLD USOC / FEATURE CODE LQGHX LQGOX LQRLB LQRDB USER PROFILE EWSTQ LQAFX X X X X X X LQAVX X X X X X X LQADX X X X X X X LQAAX X X X X X X LQABX X X X X X X LQACX X X X X X X LQAOX X X X X X X LQCAX X X X X X X LQCCX X X X X X X LQCOX X X X X X X LQCPX X X X X X X

Table 210. USOC / FID Feature Detail Table (Section 3 of 4)

FID / FEATURE DETAIL LSO LTID MAXB MDPK MTER MVP MXK NBC ODBR PCA PIC PN SPID USOC / FEATURE CODE LTRUK LTA5K LTA5R LTE5B LTFDK LTFDR LTKDB LTNMR LTPMB LTRJB LTRJK LTRJR LTRUB LTRUR LTSDR LTTDB S1B S1R S1S S2S S2B S2R S3B S3R DIGITAL SUBSCRIBER LINE LTBLB X X X X LTBLR X X X X LTCHC X X X X LTCHR X X X X LTBEB X X X X LTBER X X X X LTCEB X X X X LTCER X X X X CHANNEL ACTIVATION LPRFX LPSMX LPUNX LPWHX LPXOX LPYLX LTQDX USER PROFILE EWSTP LTQ8Y X X X X X X X X LTQ81 X X X X X X X X LTQ82 X X X X X X X X LTQ8P X X X X X X X X LTQ8Q X X X X X X X X LTQ86 X X X X X X X X LTQ87 X X X X X X X X LTQ8A X X X X X X X X LTQ8B X X X X X X X X LTQ8F X X X X X X X X LTQ8G X X X X X X X X LTQ8U X X X X X X X X LTQ8V X X X X X X X X LTQCY X X X X X X X X LTQEL X X X X X X X X LTQVB X X X X X X X X LTQVN X X X X X X X X LTQVO X X X X X X X X LTQVP X X X X X X X X LTQVQ X X X X X X X X LTQAV X X X X X X X X LTQCV X X X X X X X X LTQVR X X X X X X X X LTQV1 X X X X X X X X LTQV2 X X X X X X X X LTQVU X X X X X X X X LTQVV X X X X X X X X LTQNV X X X X X X X X LTQDB X X X X X X X X LTQDN X X X X X X X X LTQDO X X X X X X X X LTQDP X X X X X X X X LTQDQ X X X X X X X X LTQAD X X X X X X X X LTQCD X X X X X X X X LQTDR X X X X X X X X LTQD1 X X X X X X X X LTQD2 X X X X X X X X LTQDU X X X X X X X X LTQDV X X X X X X X X LTQND X X X X X X X X LTQ3X X X X X X X X X X AAQ3X X X X X X X X X X LTQ7X X X X X X X X X X AAQ7X X X X X X X X X X LTQ4O X X X X X X X X X LTQ4X X X X X X X X X X AAQ4X X X X X X X X X X BASIC CLASSES OF SERVICE S4R S4B S4S FID / FEATURE DETAIL USOC / FEATURE CODE LSO LTID MAXB MDPK MTER MVP MXK NBC ODBR PCA PIC PN SPID DIGITAL SUBSCRIBER LINE LQTTB X X X X LQTTR X X X X LQTHB X X X X LQTHR X X X X LQTEB X X X X LQTER X X X X LQTDB X X X X LQTDR X X X X CHANNEL ACTIVATION LQGFX LQGHX LQGOX LQRLB LQRDB USER PROFILE EWSTQ X LQAFX X X X X X X X X LQAVX X X X X X X X X LQADX X X X X X X X X LQAAX X X X X X X X X X LQABX X X X X X X X X X LQACX X X X X X X X X X LQAOX X X X X X X X X X LQCAX X X X X X X X X X LQCCX X X X X X X X X X LQCOX X X X X X X X X X LQCPX X X X X X X X X X

Table 211. USOC / FID Feature Detail Table (Section 4 of 4)

FID / FEATURE DETAIL SSP TN TSPD TSW TTYD TTYP TTYT USOC / FEATURE CODE LTRUK X LTA5K X LTA5R X LTE5B X LTFDK X LTFDR X LTKDB X LTNMR X LTPMB X LTRJB X LTRJK X LTRJR X LTRUB X LTRUR X LTSDR X LTTDB X S1B X S1R X S1S X S2S X S2B X S2R X S3B X S3R X DIGITAL SUBSCRIBER LINE LTBLB X LTBLR X LTCHC X LTCHR X LTBEB X LTBER X LTCEB X LTCER X CHANNEL ACTIVATION LPRFX LPSMX LPUNX LPWHX LPXOX LPYLX LTQDX USER PROFILE EWSTP X LTQ8Y X X X X LTQ81 X X X X LTQ82 X X X X LTQ8P X X X X LTQ8Q X X X X LTQ86 X X X X LTQ87 X X X X LTQ8A X X X X LTQ8B X X X X LTQ8F X X X X LTQ8G X X X X LTQ8U X X X X LTQ8V X X X X LTQCY X X X X LTQEL X X X X LTQVB X X X X LTQVN X X X X LTQVO X X X X LTQVP X X X X LTQVQ X X X X LTQAV X X X X LTQCV X X X X LTQVR X X X X LTQV1 X X X X LTQV2 X X X X LTQVU X X X X LTQVV X X X X LTQNV X X X X LTQDB X X X X LTQDN X X X X LTQDO X X X X LTQDP X X X X LTQDQ X X X X LTQAD X X X X LTQCD X X X X LQTDR X X X X LTQD1 X X X X LTQD2 X X X X LTQDU X X X X LTQDV X X X X LTQND X X X X LTQ3X X X X X AAQ3X X X X X LTQ7X X X X X AAQ7X X X X X LTQ4O X X X X LTQ4X X X X X AAQ4X X X X X BASIC CLASSES OF SERVICE S4R X S4B X S4S X DIGITAL SUBSCRIBER LINE LQTTB X LQTTR X LQTHB X LQTHR X LQTEB X LQTER X LQTDB X LQTDR X CHANNEL ACTIVATION LQGFX LQGHX LQGOX LQRLB LQRDB USER PROFILE EWSTQ X LQAFX X X X X LQAVX X X X X LQADX X X X X LQAAX X X X X LQABX X X X X LQACX X X X X LQAOX X X X X LQCAX X X X X LQCCX X X X X LQCOX X X X X LQCPX X X X X

21.2 FID ANALYSIS AND MAPPING PRODUCTS & SERVICES

ISDN BRI
5ESS, EWSD, DMS

21.2.1 FID Name

(ACOS) - ADDITIONAL CALL OFFERING

21.2.2 Purpose

Indicates the type of additional call offering service to be provided and the total number of calls which can be supported for an ISDN user over a standard interface. This FID is applicable only with non-EKTS equipment.

WHEN ACOS APPEARS, IT MUST APPEAR IN ONE OF THE FOLLOWING FORMATS:

5ESS FORMAT) 
/ACOS CSVACO.U, CSVLIMIT.1; CSDACO.U, CSDLIMIT.2

- WHERE CSVACO = ADDITIONAL CALL OFFERING ATTRIBUTE NAME(6 ALPHABETICS OF:) (OPTIONAL)

  - CSVACO = CIRCUIT SWITCHED VOICE ADDITIONAL CALL OFFERING

  - CSDACO = CIRCUIT SWITCHED DATA ADDITIONAL CALL OFFERING

- WHERE U = ADDITIONAL CALL OFFERING ATTRIBUTE VALUE (1 ALPHABETIC OF U (UNRESTRICTED) PRECEDED BY A PERIOD AND FOLLOWED BY A COMMA AND SPACE) (OPTIONAL)

- WHERE CSVLIMIT = CALL LIMIT ATTRIBUTE NAME (8 ALPHABETICS OF:) (OPTIONAL

  - CSVLIMIT = CIRCUIT SWITCHED VOICE CALL LIMIT

  - CSDLIMIT = CIRCUIT SWITCHED DATA CALL LIMIT

- WHERE 1. = CALL LIMIT ATTRIBUTE VALUE (1-2 NUMERICS FROM 1-16 PRECEDED BY A PERIOD) (OPTIONAL

(DMS100 FORMAT) 
/ACOS ACOU NBL.3

- WHERE ACOU = ADDITIONAL CALL OFFERING FEATURE NAME (4 ALPHABETICS OF ACOU - (ADDITIONAL CALL OFFERING UNRESTRICTED) (OPTIONAL)

- WHERE NBL = ADDITIONAL CALL OFFERING ATTRIBUTE NAME (3 ALPHABETICS OF NBL - (NOTIFICATION BUSY LIMIT) - PRECEDED BY A SPACE) (OPTIONAL)

- WHERE 3. = ADDITIONAL 0-4 PRECEDED BY A PERIOD) (OPTIONAL)

(EWSD FORMAT) 
ACOS UNRES, CRBL.3, NBL.2

- WHERE UNRES = ADDITIONAL CALL OFFERING ATTRIBUTE NAME

- WHERE 3 = CRBL ATTRIBUTE VALUE (OPTIONAL) 1-2 NUMERICS FROM 1 TO 16)

- WHERE 2 = NBL ATTRIBUTE VALUE (OPTIONAL) (1-2 NUMERICS FROM 0 TO 15). (MUST BE LESS THAN CRBL)

21.2.3 Usage

FEATURE LEVEL ACTIVITY

A C D O O O

21.2.4 Data Characteristics

Term Definition Length of Element: 10-74 Alpha/Numeric/Any ANY ALLOWABLE SERVICE ORDER CHARACTER

ISDN BRI
EWSD, 5ESS, DMS100

21.2.5 FID Name

(ADSR) - ADMINISTRATION OF DESIGNED SERVICE REVIEW

21.2.6 Purpose

Identifies service as a “designed” service offering, therein warranting special attention to ensure proper provisioning.
/ADSR

21.2.7 Usage

FEATURE LEVEL ACTIVITY

A C D R C O

Required if service request involves the installation of a new DSL. Otherwise not applicable.

21.2.8 Data Characteristics

Term Definition Length of Element: There are no associated data elements. Alpha/Numeric/Any There are no associated data elements.

ISDN BRI
EWSD

21.2.9 FID Name

(BCN) - BEARER CAPABILITY NAME

21.2.10 Purpose

Indicates the type of bearer capability service for a B-channel. These capabilities must be established before service can be activated for the end-user.
WHEN BCN APPEARS IT MUST BE FORMATTED AS FOLLOWS:

Term Definition When associated with DSL USOC /BCN SP 3AU 56C 64C PMD When associated with CS Voice Service USOC /BCN SP 3AU When associated with CS Data Service USOC\ /BCN 56C 64C\ When associated with Packet Service USOC /BCN PMD

WHERE SP = (2-3 ALPHANUMERICS) (REQUIRED)

Term Definition SP SPEECH 3AU - 3.1 KHZ AUDIO 56C 56 KBPS CIRCUIT MODE DATA 64C 65 KBPS CIRCUIT MODE DATA PMD PACKET MODE DATA

Note: Data may appear in a series separated by a space.

21.2.11. Usage:

FEATURE LEVEL ACTIVITY

A C D R C O

Required for each B-channel activated within a DSL.
Otherwise not applicable.

21.2.12 Data Characteristics

Term Definition Length of Element: Two to eighteen (2-18) characters. Alpha/Numeric/Any Valid data types are alpha / numerics and blanks.

ISDN BRI
5ESS, DMS, EWSD

21.2.13 FID Name

(BS) - BEARER SERVICE

21.2.14 Purpose

Identifies the types of services that are carried over a Digital Subscriber Line (DSL).

BS DATA MUST APPEAR IN THE FOLLOWING FORMAT:

(DMS100 Format) 
/BS CSDV CSDV XONLY XISDN

- WHERE CSDV = CHANNEL B1 SERVICE (3 OR 4 ALPHANUMERICS OF:)

  - CSD = CIRCUIT SWITCHED DATA - 5ESS (5E4), DMS - 100

  - CSDV = CIRCUIT SWITCHED DATA/VOICE - 5ESS (5E4), DMS -100

  - CSV = CIRCUIT SWITCHED VOICE - 5ESS (5E4), DMS - X25 PACKET SWITCHED DATA X.25 - 5ESS

  - NONE = NO TYPE OF SERVICES - 5ESS (5E4), DMS - 100

  - PSB = PUBLIC PACKET SWITCHED NETWORK - DMS - 100

  - DMD = 5ESS (%E5) SERVICES ON DEMAND

- WHERE CSDV = CHANNEL B2 SERVICE (3 OR 4 ALPHANUMERICS OF:)

  - CSD = CIRCUIT SWITCHED DATA - 5ESS (5E4), DMS - 100

  - CSDV = CIRCUIT SWITCHED DATA/VOICE - 5ESS (5E4), DMS -100

  - CSV = CIRCUIT SWITCHED VOICE - 5ESS (5E4), DMS - 100

  - X25 = PACKET SWITCHED DATA X.25 - 5ESS

  - NONE = NO TYPE OF SERVICES - 5ESS (5E4), DMS - 100

  - PSB = PUBLIC PACKET SWITCHED NETWORK - DMS - 100

  - DMD = 5ESS (%E5) SERVICES ON DEMAND

- WHERE XONLY = D CHANNEL SERVICE (2 TO 5 ALPHABETICS OF:)

  - ADMIN = X.25 ON B. NONE ON D-5ESS

  - SONLY = CSV, CSD, CSD/V ON B, D - SIGNALING - 5ESS

  - SX = CSV, CSD, CSD/V ON B, X.25 ON D - 5ESS

  - XONLY = X.25 ON D ONLY - 5ESS

  - XMP = D CHANNEL MODEM POOLING - 5ESS

  - BLANK = NO ENTRY

  - PSD = PUBLIC PACKET SWITCHED NETWORK - DMS - 100

- WHERE XISDN = DIGITAL SUBSCRIBER LINE LEVEL PROFILE (2 TO 5 ALPHABETICS OF:)

  - DX = X.25 ON D CHANNEL

  - ISDN = CIRCUIT SWITCHED SERVICE

  - XISDN = X.25 AND SIGNALING ON D CHANNEL

WHEN THE FID TSW WITH DATA OF 5E APPEARS, BS DATA MUST BE IN THE FOLLOWING FORMAT:

(5ESS OR EWSD Format) 
/BS DMD DMD SX

- WHERE DMD = CHANNEL B1 SERVICE (3 ALPHAS OF DMD (CHANNEL ON DEMAND SERVICES) OR X.25 (PERMANENT PACKET SWITCHED DATA)

- WHERE DMD = CHANNEL B2 SERVICE (3 ALPHAS OF DMD (CHANNEL ON DEMAND SERVICES) OR X.25 (PERMANENT PACKET SWITCHED DATA)

- WHERE SX = D CHANNEL SERVICE (2-5 ALPHAS OF SX (Q.931 SIGNALING AND X.25 PACKET SIGNALING) OR SONLY (Q.931 SIGNALING (USED FOR AN ISDN ATTENDANT) (POINT TO POINT ONLY). SONLY OPTION IS NOT APPLICABLE IN EWSD

21.2.15 Usage

FEATURE LEVEL ACTIVITY

A C D R C O

21.2.16 Data Characteristics

Term Definition Length of Element: 10-21 Alpha/Numeric/Any ALPHA/NUMERIC

ISDN BR
EWSD

21.2.17 FID Name

(CAPI) Call Appearance Identifier

21.2.18 Purpose

Provides the assignment of a call appearance of a Primary Directory Number (DN) or call type to a corresponding central office switch identifier. Applicable with EKTS use only.

WHEN CAPI APPEARS IT MUST BE FORMATTED AS FOLLOWS:
/CAPI 1.1, 2.2, 3.3; AP.D

- WHERE 1 = CALL APPEARANCE (1-2 NUMERICS OF 1-16) (REQUIRED)

- WHERE 1 = CALL APPEARANCE IDENTIFIER NUMBER (1-5 NUMERICS OF 1-16383 PRECEDED BY A PERIOD) (REQUIRED)

- WHERE AP = ALERTING PATTERN ATTRIBUTE NAME (2 ALPHABETICS OF AP PRECEDED BY A SEMICOLON AND SPACE) (OPTIONAL

- WHERE D = ALERTING PATTERN ATTRIBUTE VALUE (OPTIONAL) (1 OF THE FOLLOWING ALPHABETICS PRECEDED BY A PERIOD:)

  - N = NORMAL

  - A = ABBREVIATED

  - D = DELAYED

  - ABBR = ABBREVIATED

  - DELAYED = DELAYED

  - NORMAL = NORMAL

  - NONE = NONE

Note: When element 3 appears, element 4 must also appear.

Note: Element 1 and 2 may appear in a series separated by a comma and a space.

Note: When element 1 appears without element 2 it may not appear in a series.

21.2.19 Usage

FEATURE LEVEL ACTIVITY

A C D O O O

21.2.20 Data Characteristics

Term Definition Length of Element: One to one hundred sixty-five (1-165) characters. Alpha/Numeric/Any Valid entries are any allowable service order character. EKTS sets can only have one (1) call appearance for data calls.

ISDN BRI
5ESS

21.2.21 FID Name

(CAPP) - CALL APPEARANCE - 5ESS

21.2.22 Purpose

Indicates the initial button location and total number of consecutive call appearance of all lines appearing on an end-user's set.

CAPP DATA MUST APPEAR IN ONE OF THE FOLLOWING FORMATS:
/CAPP CA.1, NBR.2, CALLEXCL.A, ADRPAT.DEL, ADRTIME.15

- WHERE CA = CALL APPEARANCE (2 ALPHABETICS OF CA) (OPTIONAL)

- WHERE 1 = CALL APPEARANCE DATA (1-3 NUMERICS FROM 1- 254) (OPTIONAL) (PRECEDED BY A PERIOD)

- WHERE NBR = NUMBER OF CALL APPEARANCES (3 ALPHABETICS OF NBR) (OPTIONAL) (PRECEDED BY A COMMA AND SPACE)

- WHERE 2 = NUMBER OF CALL APPEARANCES DATA (1-2 NUMERICS FROM 1-16) (OPTIONAL) (PRECEDED BY A PERIOD)

- WHERE CALLEXCL.A = CALL EXCLUSION AND INDICATOR (8 ALPHABETICS OF CALLEXCL, A PERIOD AND 1 ALPHABETIC A (AUTOMATIC), M (MANUAL), OR N (NO PRIVACY) (OPTIONAL) (PRECEDED BY A PERIOD)

- WHERE ADRPAT.DEL = ABBREVIATED RINGING OR DELAY PATTERN AND VALUE (6 ALPHABETICS OF ADRPAT AND 3 ALPHABETICS OF:)

  - NON = RINGING DELETE (ADRPAT

  - DEL = DELAYED (ADRPAT)

  - ABR = ABBREVIATED (ADRPAT)

  - NOR = NORMAL (ADRPAT)

  - DRI = DELAYED RINGING IMMEDIATE DISPLAY (ADRPAT)

  - NRN = NO RINGING INTO DISPLAY (ADRPAT) (PRECEDED BY A COMMA AND SPACE)

- WHERE ADRTIME.15 = ABBREVIATED/DELAY RINGING TIME AND SECONDS (7 ALPHABETICS OF ADRTIME, A PERIOD AND 1-3 NUMERICS FROM 0-255) (OPTIONAL) (PRECEDED BY A COMMA AND SPACE )

21.2.23 Usage

FEATURE LEVEL ACTIVITY

A C D O O O

Note: CAPP may not appear when key appears

21.2.24 Data Characteristics

Term Definition Length of Element: 5-51 Alpha/Numeric/Any ALPHA/NUMERIC

ISDN BRI
5ESS, DMS

21.2.25 FID Name

(CAT) Customer Access Treatment

21.2.26 Purpose

Identifies the users Network Class of Service (NCOS).The CAT is associated with the line and reflects the type of Customized Code Restriction (CREX) options chosen. If a CREX option is not chosen, the Flat Rate CAT 0 will be used.

Example:

Example:  /CAT XXX

(DMS 100, NON-THRESHOLD STATES)

Term Definition FLAT RATE SVC.(no Restrictions) CAT 0 CREX1 CAT 1 CREX2 CAT 2 CREX3 Cat 3 CREX4 CAT 4

(DMS 100, THRESHOLD STATES)

Term Definition FLAT RATE SVC.(no Restrictions) CAT 30 CREX1 CAT 31 CREX2 CAT 32 CREX3 CAT 33 CREX4 CAT 34

(5ESS) 
Always- -CAT 0

Note: Please refer to the appropriate section of the General Services Subscriber Tariff (GSST) for details regarding additional Customized Code Restrictions not listed above.

21.2.27 Usage

FEATURE LEVEL ACTIVITY

A C D R C O

21.2.28 Data Characteristics

Term Definition Length of Element: One to three (1-3) numerics. Alpha/Numeric/Any -

ISDN BRI
EWSD

21.2.29 FID Name

(CHD) CALL HOLD

21.2.30 Purpose

Indicates that a station line has Call Hold. This feature is provided as part of the basic service offering. This option sends a notification to the held party when a call is holding.

/CHD CHDN

The data following CHD will always be CHDN.

21.2.31 Usage

FEATURE LEVEL ACTIVITY

A C D R C O

21.2.32 Data Characteristics

Term Definition Length of Element: Four alpha characters. Alpha/Numeric/Any Valid entry is CHDN.

ISDN BRI
5ESS, DMS100, EWSD

21.2.33 FID Name

(CLS) - COMM. LANGUAGE. CIRCUIT ID - SERIAL NO.

21.2.34 Purpose

Identifies the circuit used in provisioning end-user service.

CLS DATA MUST APPEAR IN THE FOLLOWING FORMAT:
/CLS 12.PLNT.123456.66.SB

- WHERE 12 = PREFIX (OPTIONAL) (1-2 ALPHANUMERICS)

- WHERE PL = SERVICE CODE (2 ALPHABETICS PRECEDED BY A PERIOD)

- WHERE NT = MODIFIER (2 ALPHABETICS OR 1 ALPHABETIC AND 1 ALPHANUMERIC)

- WHERE 123456 = SERIAL NUMBER (1-6 NUMERICS OF 1-999999 PRECEDED BY A PERIOD)

- WHERE 66 = SUFFIX (OPTIONAL) (1-3 NUMERICS OF 1-999 PRECEDED BY A PERIOD)

- WHERE SB = ASSIGNING COMPANY IDENTIFICATION (2 OR 4 ALPHABETICS PRECEDED BY A PERIOD)

Note: THE ABSENCE OF THE SUFFIX DATA IS INDICATED BY 2 PERIODS BETWEEN THE SERIAL NUMBER AND THE ASSIGNING COMPANY IDENTIFICATION.

21.2.35 Usage

FEATURE LEVEL ACTIVITY

A C D R R R

21.2.36 Data Characteristics

Term Definition Length of Element: Eleven to twenty-three characters. Alpha/Numeric/Any Valid entries include any allowable service order character.

ISDN BRI
EWSD

21.2.37 FID Name

CSGP (CUSTOMER GROUP IDENTIFIER)

21.2.38 Purpose

Indicates the customer group for EKTS subscribers.

/CSGP 1

The CSGP number will always be one (1)

21.2.39 Usage

A C D C C O

Required if “TTYT” FID option of “ EKTS Y” is selected.

21.2.40 Data Characteristics

Term Definition Length of Element: One numeric character. Alpha/Numeric/Any Valid entry is the number one (1).

ISDN BRI
5ESS

21.2.41 FID Name

(CSO) - CIRCUIT SWITCHED CHANNEL OPTIONS

21.2.42 Purpose

Indicates quantity of B channels allowed for use and which B channel is assigned to ISDN circuit switched bearer service.

CSO MUST APPEAR IN THE FOLLOWING FORMAT:
/CSO CSV.1, CSVC.B1

- WHERE CSV = CIRCUIT SWITCHED BEARER SERVICE NAME (3 ALPHABETICS OF:)

  - CSV = CIRCUIT SWITCHED VOICE

  - CSD = CIRCUIT SWITCHED DATA

- WHERE 1 = QUANTITY OF CHANNELS ALLOWED FOR USE (1 NUMERIC OF 0-2)

- WHERE CSVC = ATTRIBUTE NAME - CHANNELS TO BE USED (4 ALPHABETICS OF:)

  - CSVC = CIRCUIT SWITCHED VOICE CHANNEL

  - CSDC = CIRCUIT SWITCHED DATA CHANNEL

- WHERE B1 ATTRIBUTE VALUE - CHANNEL TO BE USED (2-3 ALPHA-CIRCUIT SWITCHED CHANNEL OPTIONS NUMERICS OF:

  - B1 = B1 CHANNEL

  - B2 = B2 CHANNEL

  - ANY = EITHER CHANNEL

  - NO = NONE

21.2.43 Usage

A C D O O O

Note: CSO NOT VALID WHEN LCTL APPEARS

21.2.44 Data Characteristics

Term Definition Length of Element: 14-32 Alpha/Numeric/Any ANY ALLOWABLE SERVICE ORDER CHARACTER

ISDN BRI
5ESS

21.2.45 FID Name

(DCLS) - DIGITAL SUBSCRIBER LINE CLASS OF SERVICE

21.2.46 Purpose

Indicates a point-to-point or multi-point (up to 8) digital subscriber line (DSL).

/DCLS STD

DCLS OPTION MUST CONSIST OF ONE OF THE FOLLOWING CODES:

- M P = MULTIPOINT POINT (Used with Custom ISDN)

- PP = POINT TO POINT (Used with Custom ISDN).

- STD = STANDARD (Q.931 PROTOCOL) (Used with National ISDN)

21.2.47 Usage

A C D R C O

21.2.48 Data Characteristics

Term Definition Length of Element: 2 - 3 Alpha/Numeric/Any ALPHA

ISDN BRI
5ESS

21.2.49 FID Name

(DPG) - DIALING PLAN GROUP

21.2.50 Purpose

Indicates the central office “common block” from which service is provisioned.

/DPG ISINDVLN

21.2.51 Usage

A C D C C O

Required when added or changing User Profiles. Otherwise optional.

21.2.52 Data Characteristics

Term Definition Length of Element: 2-8 Alpha/Numeric/Any ALPHANUMERIC ALPHANUMERIC FIRST CHARACTER OF MUST BE AN ALPHABETIC

ISDN BRI
5ESS and DMS 100

21.2.53 FID Name

(DSNA) - DIGITAL SERVICES NETWORK ASSIGNMENT

21.2.54 Purpose

Identifies the facilities used in the provisioning of central office channelized services.

DSNA DATA MUST APPEAR IN ONE OF THE FOLLOWING FORMATS:

/DSNA 12.DHMC.1135.12.SC

- WHERE 12 REFIX (2 ALPHANUMERICS)

- WHERE DH SERVICE CODE (2 ALPHABETICS PRECEDED BY A PERIOD)

- WHERE MC MODIFIER (2 ALPHANUMERICS)

- WHERE 1135 SERIAL NUMBER (1-6 NUMERICS FROM 1-999999 PRECEDED BY A PERIOD)

- WHERE 12 SUFFIX (1-3 NUMERICS FROM 1-999 PRECEDED BY A PERIOD. THE ABSENCE OF THE SUFFIX IS INDICATED BY 2 PERIODS)

- WHERE SC ASSIGNING COMPANY (2 ALPHABETICS OF SC OR SB PRECEDED BY A PERIOD

/ DSNA 205 529-1111

- WHERE 205 NPA (3 NUMERICS) (OPTIONAL)

- WHERE 529 NXX (3 NUMERICS FOLLOWED BY A HYPHEN)

- WHERE 1111 LINE NUMBER (4 NUMERICS

21.2.55 Usage

A C D R C O

Required when added or changing User Profiles. Otherwise optional.

21.2.56 Data Characteristics

Term Definition Length of Element: 8-21 Alpha/Numeric/Any ANY ALLOWABLE SERVICE ORDER CHARACTER

ISDN BRI
EWSD

21.2.57 FID Name

(FC) - FLEXIBLE CALLING

21.2.58 Purpose

Indicates the billing record type for a Primary Directory Number (DN), or the Flexible Calling features assigned to a Terminal Service Profile (TSP).

Enter the appropriate features requested by the customer as noted below. This is the only applicable data.

/FC DNBFC.Y

- Where DNBFC = FC Terminal Service Profile Attribute Name ( 2-5 alphas )

- Where Y refers to DN Bridging. Populate with 1 alpha of “Y” for Yes, or “N” for No

21.2.59 Usage

A C D C C O

Note: Applicable with EKTS only.

21.2.60 Data Characteristics

Term Definition Length of Element: Four to thirty-one (4 - 31) characters. Alpha/Numeric/Any Acceptable data type is any valid service order character

ISDN BRI
EWSD

21.2.61 FID Name

(FCA) - FEATURE CONTROL ABILITY

21.2.62 Purpose

Indicates the activation of an assigned feature. Currently used only with the Call Forwarding Variable feature. Used with EKTS only.

If the Call Forwarding Variable feature is selected, the following entry must appear:

/FCA CFVRC

21.2.63 Usage

A C D O O O

21.2.64 Data Characteristics

Term Definition Length of Element: Five (5) alpha characters. Alpha/Numeric/Any Valid entry is CFVRC.

ISDN BRI
5ESS, DMS, EWSD

21.2.65 FID Name

(ICPK) - ISDN CAPABILITY PACKAGES

21.2.66 Purpose

Identifies ISDN package offerings.

WHEN ICPK APPEARS IT MUST BE IN ONE OF THE FOLLOWING FORMATS:

/ICPK E

WHERE E = ISDN CAPABILITY PACKAGE (1-3 ALPHAS) EZ1, EZ1A, EZ2, EZ2A, CPS 
OR

/ICPK BS311OR

- WHERE BS = BELLSOUTH REGIONAL CAPABILITY PACKAGE (2 ALPHAS OF BS)

- WHERE 311 = REGIONAL CAPABILITY PACKAGE NUMBER (3 NUMERICS)

/ICPK A1B2C3D4E5F6G7

WHERE A1B2C3 D4E5F6G7 =) ISDN ORDERING CODE (1-25 ALPHANUMERICS)

21.2.67 Usage

A C D C C O

Required if service request involves the provisioning of pre-configured ISDN packages. Otherwise prohibited.

21.2.68 Data Characteristics

Term Definition Length of Element: One to twenty-five (1-25) characters. Alpha/Numeric/Any Valid entries include any allowable service order character.

ISDN BRI
DMS 100, EWSD

21.2.69 FID Name

(KEY) - KEY DESIGNATION

21.2.70 Purpose

Indicates the key designation and associate key list for features associated with an electronic telephone or an ISDN terminal.

KEY MUST APPEAR IN ONE OF THE FOLLOWING FORMATS:

(DMS 100 FORMAT)
/KEY 1 NUMC 3

- WHERE 1 = KEY DESIGNATION (1-2 NUMERICS FROM 1-69)

- WHERENUMC 3 = NUMBER OF CALLS INDICATOR (4 ALPHABETICS OF NUMC FOLLOWED BY A SPACE AND 1 NUMERIC FROM 1-5) (OPTIONAL)

(EWSD FORMAT)
/KEY 1V

- WHERE 1 = KEY DESIGNATION (1-2 NUMERICS FROM O-99)

- WHERE V = CALL TYPE DESIGNATION (1 ALPHABETIC OF V (VOICE) OR D (DATA)) (OPTIONAL)

21.2.71 Usage

A C D C C O

Required if service request involves EKTS terminating devices. Otherwise not applicable.

21.2.72 Data Characteristics

Term Definition Length of Element: 1-500 Alpha/Numeric/Any Any allowable service order characters

ISDN BRI
5ESS, DMS, EWSD,

21.2.73 FID Name

(KS) - KEY SYSTEM NUMBER

21.2.74 Purpose

Identifies the key system number associated with a terminal device.
/KS XXXX

21.2.75 Usage

A C D R C O

21.2.76 Data Characteristics

Term Definition Length of Element: 1 - 4 Alpha/Numeric/Any N

ISDN BRI
5ESS , EWSD, DMS 100

21.2.77 FID Name

(LCC) - LINE CLASS CODE

21.2.78 Purpose

Indicates the originating and terminating restriction, or combinations of restrictions, for a line in a stored program controlled switch.

/LCC XXXXXXXX

(DMS FORMAT) 
Always /LCC ISDNKSET

21.2.79 Usage

FEATURE LEVEL ACTIVITY

A C D R C O

21.2.80 Data Characteristics

Term Definition Length of Element: 3-8 Alpha/Numeric/Any SB - ANY ALLOWABLE SERVICE ORDER CHARACTER SCB - ABCDEFGHIJKLM NOPQRSTUVWXYZ0123456789

ISDN BRI
5ESS, DMS, EWSD

21.2.81 FID Name

LPCA - (INTRALATA PRE-SUBSCRIPTION CARRIER ARRANGEMENT)

21.2.82 Purpose

Identifies the selection code by which the intraLATA Pre-subscription Indicator Code (LPIC) was identified to the Local Operating Company, and the application date of the LPIC selection.

/LPIC XXXX / LPCA SC, MM-DD-YY

The LPCA selection code (SC)must be two alphabetics from the following list, followed by a comma ,space and the application date.

- BO= BUSINESS OFFICE NEGOTIATED - CUSTOMER/END USER INITIATED

- FR= PIC FREEZE

- SR= SUBMITTED RESELLER

The LPCA application date must be a valid calendar date formatted MM-DD-YY.

21.2.83 Usage

FEATURE LEVEL ACTIVITY

A C D C C O

Required when the LPIC field identifier is used. Otherwise its' use is prohibited.

21.2.84 Data Characteristics

Term Definition Length of Element: Twelve (12) alpha/numerics, dashes (-), or blanks. Alpha/Numeric/Any -

ISDN BRI
5ESS, DMS, EWSD

21.2.85 FID Name

LPIC - (INTRALATA PRE-SUBSCRIPTION INDICATOR CODE)

21.2.86 Purpose

Identifies the Pre-subscription Indicator Code (PIC) for the carrier the customer has selected to carry intraLATA calls.

When LPIC appears, it must be in the following format: /LPIC 0124

Where 0124 = abbreviated carrier name (4 numerics beginning with 0, 5 or 6)

21.2.87 Usage

FEATURE LEVEL ACTIVITY

A C D C C O

LPIC is required in some states when establishing or modifying User Profiles. Check the state's tariff for LPIC applicability.

21.2.88 Data Characteristics

Term Definition Length of Element: Four (4) numerics representing valid carrier codes. Alpha/Numeric/Any -

ISDN BRI
EWSD

21.2.89 FID Name

(LKLD - LINK LEVEL PARAMETERS D - CHANNEL

21.2.90 Purpose

Indicates the D CHANNEL data link parameters for an ISDN interface in the EWSD switch.

WHEN LKLD APPEARS IT MUST BE FORMATTED AS FOLLOWS:

/LKLD LO.DYNPAL

- WHERE LO = LINK OPTION ATTRIBUTE NAME (2 ALPHABETICS OF LO)

- WHERE DYNPAL = LINK OPTION ATTRIBUTE VALUE (6 ALPHABETICS) DYNPAL - DYNAMIC LINKS WITH PACKET LINKS

21.2.91 Usage

FEATURE LEVEL ACTIVITY

A C D R R O

21.2.92 Data Characteristics

Term Definition Length of Element: Three to sixty-one (3-61) characters. Alpha/Numeric/Any Acceptable data type is any valid service order character.

ISDN BRI
5ESS, DMS, EWSD

21.2.93FID Name

(LSO) - LOCAL SERVING OFFICE

21.2.94 Purpose

Identifies, by NPA NXX codes, the service provisioning central office.

LSO MUST APPEAR IN THE FOLLOWING FORMAT:

/LSO 101 555

- WHERE 101 = NPA (3 NUMERICS)

- WHERE 555 =NXX (3 NUMERICS)

21.2.95 Usage

FEATURE LEVEL ACTIVITY

A C D R C O

Required if service request involves the installation of a new DSL . Otherwise optional.

21.2.96 Data Characteristics

Term Definition Length of Element: Seven (7) characters. Alpha/Numeric/Any Valid data types are numerics and blanks.

ISDN BRI
DMS 100

21.2.97 FID Name

(LTID) - LOGICAL TERMINAL IDENTIFIER

21.2.98 Purpose

Uniquely identifies ISDN terminals in a DMS digital switch.

LTID DATA MUST APPEAR IN THE FOLLOWING FORMAT:

/LTID ISDN 1020

- WHERE ISDN = GROUP NAME (1-8 ALPHANUMERICS)

- WHERE 1020 = LINE NUMBER TERMINATION (1-4 NUMERICS FROM 0- 1022)

21.2.99 Usage

FEATURE LEVEL ACTIVITY

A C D O O O

21.2.100 Data Characteristics

Term Definition Length of Element: 3 - 13 Alpha/Numeric/Any A/N, (-), and BLANK

ISDN BRI
5ESS

21.2.101 FID Name

(MAXB) - MAXIMUM B CHANNELS

21.2.102 Purpose

Indicates the maximum number of B channels to be used on a demand basis for circuit switched services on basic rate ISDN.

/ MAXB 2

21.2.103 Usage

FEATURE LEVEL ACTIVITY

A C D R C O

21.2.104 Data Characteristics

Term Definition Length of Element: 1 Alpha/Numeric/Any N MAXB DATA MUST BE ONE NUMERIC FROM 0-2

ISDN BRI
5ESS

21.2.105 FID Name

(MDPK) - MAXIMUM D CHANNEL PACKET USERS

21.2.106 Purpose

Indicates the maximum number of packet users on a D channel on a basic rate access digital subscriber line.

/MDPK 3

21.2.107 Usage

FEATURE LEVEL ACTIVITY

A C D O O O

21.2.108 Data Characteristics

Term Definition Length of Element: 1 Alpha/Numeric/Any N MDPK DATA MUST APPEAR AS ONE NUMERIC OF 0-8.

ISDN BRI
5ESS

21.2.109 FID Name

(MTER) - MAXIMUM NUMBER OF TERMINALS

21.2.110 Purpose

Indicates the maximum number of terminals in operation on a channel.

/MTER 8

21.2.111 Usage

FEATURE LEVEL ACTIVITY

A C D O O O

21.2.112 Data Characteristics

Term Definition Length of Element: 1 Alpha/Numeric/Any N

ISDN BRI
DMS100, 5ESS

21.2.113 FID Name

(MVP) - MULTILINE VARIETY PACKAGE

21.2.114 Purpose

Identifies the common customer group, (common block) . The first code set following the FID MVP is CG (Centrex Group), followed by the group name.

/MVP CG ISL101:0 (When service provisioned from DMS100)
or

/MVP CG ISDNSNGL (When service provisioned from 5ESS)

21.2.115 Usage

FEATURE LEVEL ACTIVITY

A C D R R O

21.2.116 Data Characteristics

Term Definition Length of Element: One to twenty-four (1-24) characters for ISDN service in GA,FL,NC, and SC. Four to forty-seven (4-47) characters for ISDN service in AL, MS,LA,TN, and KY. Alpha/Numeric/Any Valid entries are illustrated in the above example.

ISDN BRI 
DMS 100

21.2.117 FID Name

(MXK) - MAXIMUM NUMBER OF KEYS

21.2.118 Purpose

Indicates the maximum number of keys in use on a terminal or an ISDN-like service in a DMS digital switch.

/MXK XX

21.2.119 Usage

FEATURE LEVEL ACTIVITY

A C D C C O

21.2.120. Data Characteristics

Term Definition Length of Element: 2 Alpha/Numeric/ N MXK MUST BE FROM 1-64

ISDN BRI
EWSD

21.2.121 FID Name

(NBC) - NUMBER OF B CHANNELS

21.2.122 Purpose

The number of B channels the customer is activating.

/NBC 2

21.2.123 Usage

FEATURE LEVEL ACTIVITY

A C D R C O

Required if service request involves the installation of a new DSL or the activation of a new B-channel within an existing DSL. Otherwise not applicable.

21.2.124 Data Characteristics

Term Definition Length of Element: One numeric. Alpha/Numeric/Any Valid entries are the number one (1) or two (2).

ISDN BRI
EWSD

21.2.125 FID Name

(ODBR) - B-CHANNELS RESERVATIONS

21.2.126 Purpose

Indicates the number of B-channels that are to be available to the end-user for voice calls.

WHEN ODBR APPEARS IT MUST BE FORMATTED AS FOLLOWS:

/ODBR NBCCTOEDN 2; OAR 1
or

/ODBR NBCCTOEDN 2, NOBCOEDN 1, OAR 1

- WHERE NBCCTOEDN = QUANTITY OF ON-DEMAND B-CHANNELS FEATUR

  - NAME (OPTIONAL) (5-9 ALPHABETICS OF:)

  - NBCCTOEDN - NUMBER OF ON-DEMAND B-CHANNELS

  - PER CALL TYPE PER OEDN

  - NOBCOEDN - NUMBER OF ON-DEMAND B-CHANNELS

  - PER OEDN (FOLLOWED BY A SPACE)

- WHERE 2 = QUANTITY OF ON-DEMAND B-CHANNELS (1 NUMERIC OF 1 OR 2) (OPTIONAL)

- WHERE OAR = B-CHANNEL Restrictions FEATURE NAME (OPTIONAL)

  - (3 ALPHABETICS OF:)

  - IAR - INCOMING ACCESS ALLOWED

  - IBCHT - INCOMING NUMBER OF CALLS

  - OAR - OUTGOING ACCESS ALLOWED

  - OBCHCT - OUTGOING NUMBER OF B CHANNELS

  - IOR - INCOMING/OUTGOING ACCESS ALLOWED (PRECEDED BY A SEMICOLON AND SPACE)

- WHERE 1 = QUANTITY OF B-CHANNELS ALLOWED ACCESS (OPTIONAL) (1 NUMERIC FROM 0 TO 2 PRECEDED BY A SPACE)

Note: WHEN ELEMENT 3 FOLLOWS ELEMENT 2, THEY MUST BE SEPARATED BY A SEMICOLON AND SPACE.

Note: WHEN ELEMENT 3 APPEARS, ELEMENT 4 MUST APPEAR PRECEDED BY A SPACE.

Note: ELEMENT 3 AND 4 MAY APPEAR IN A SERIES SEPARATED BY A COMMA AND A SPACE.

Note: ELEMENT 1 AND 2 MAY APPEAR IN A SERIES SEPARATED BY A COMMA AND SPACE (SEE EXAMPLE 2).

21.2.127 Usage

FEATURE LEVEL ACTIVITY

A C D O O O

21.2.128 Data Characteristics

Term Definition Length of Element: One to forty (1-40) characters. Alpha/Numeric/Any Acceptable data type is any valid service order character.

ISDN BRI
5ESS, DMS, EWSD

21.2.129 FID Name

PCA - (PRE-SUBSCRIPTION CARRIER ARRANGEMENT)

21.2.130 Purpose

Identifies the selection code by which the Pre-subscription Indicator Code (PIC) was obtained by the Local Operating Company, and the application date of the selection.

/PIC XXXX / PCA SC, MM-DD-YY

The PCA selection code (SC)must be two alphabetics from the following list, followed by a comma ,space and the application date.

- BO = BUSINESS OFFICE NEGOTIATED - CUSTOMER/END USER INITIATED

- FR = PIC FREEZE

- SR = SUBMITTED RESELLER

The PCA application date must be a valid calendar date formatted MM-DD-YY.

21.2.131 Usage

FEATURE LEVEL ACTIVITY

A C D C C O

Required when the PIC field identifier is populated. Otherwise its' use is prohibited.

21.2.132 Data Characteristics

Term Definition Length of Element: Twelve (12) Alpha/Numeric/Any alpha/numerics, dashes (-), or blanks

ISDN BRI
5ESS, DMS, EWSD

21.2.133 FID Name

PIC - (PRIMARY INTEREXCHANGE CARRIER)

21.2.134 Purpose

Identifies the Pre-subscription Indicator Code (PIC) for the carrier that the customer has selected to carry interLATA calls.

PIC must appear in the following format:

/ PIC 0333

Where 0333 = abbreviated carrier name (4 numerics beginning with 0, 5, 6)

21.2.135 Usage

FEATURE LEVEL ACTIVITY

A C D C C O

Required when establishing or modifying User Profiles. Otherwise not applicable.

21.2.136 Data Characteristics

Term Definition Length of Element: Four (4) numerics representing valid carrier code Four (4) numerics representing valid carrier codes. Alpha/Numeric/Any -

ISDN BRI
5ESS, DMS, EWSD

21.2.137 FID Name

(PN) - PRIMARY DIRECTORY NUMBER

21.2.138 Purpose

Defines the number that appears on Key one of an ISDN terminal device. A PN may have additional appearances on the same terminal device or appear on other terminal devices depending on the type of CPE.

WHEN PN DATA APPEARS, IT MUST BE IN THE FOLLOWING FORMAT:

/PN 555-1234

- WHERE 555 = CENTRAL OFFICE (3 NUMERICS)

- WHERE 1234 = LINE NUMBER (4 NUMERICS)

21.2.139 Usage

FEATURE LEVEL ACTIVITY

A C D R C O

Required when establishing or modifying User Profiles. Otherwise not applicable.

21.2.140 Data Characteristics

Term Definition Length of Element: Eight to fifteen (8-15) characters. Alpha/Numeric/Any Valid entries are alpha\ numerics, dashes, and blanks.

ISDN BRI
5ESS and DMS 100

21.2.141 FID Name

(SPID) - SERVICE PROFILE ID

21.2.142 Purpose

Identifies each individual end-user to the ISDN serving central office switch.

SPID DATA MUST BE IN THE FOLLOWING FORMATS: (FORMAT FOR NATIONAL ISDN IN DMS AND 5ESS OFFICES)

/SPID 205 555-1234 01

- WHERE 205 = NPA (3 NUMERICS FOLLOWED BY A SPACE)

- WHERE 555 = NXX (3 NUMERICS FOLLOWED BY A HYPHEN)

- HERE 1234 = LINE NUMBER (4 NUMERICS FOLLOWED BY A HYPHEN)

- WHERE 01 = SPID SUFFIX (2 NUMERICS)

21.2.143 Usage

FEATURE LEVEL ACTIVITY

A C D R C O

Required when adding or modifying a User Profile. Otherwise not applicable.

21.2.144 Data Characteristics

Term Definition Length of Element: 0 - 21 Alpha/Numeric/Any ANY ALLOWABLE SERVICE ORDER CHARACTER

ISDN BRI
5ESS, DMS, EWSD,

21.2.145 FID Name

(SSP) - SPECIAL SERVICE PROTECTION

21.2.146 Purpose

This FID prevents testing on the line that might disrupt service.

/SSP

21.2.147 Usage

FEATURE LEVEL ACTIVITY

A C D O O O

21.2.148 Data Characteristics

Term Definition Length of Element: There are no data elements associated with this FID. Alpha/Numeric/Any There are no data elements associated with this FID.

ISDN BRI
5ESS, DMS, EWSD

21.2.149 FID Name

(TN ) - telephone number

21.2.150 Purpose

Identifies the telephone number associated with end-user service.

TN MUST APPEAR ACCORDING TO ONE OF THE FOLLOWING FORMATS:

/TN 101 555-1234

- WHERE 101 = NPA (3 NUMERICS)

- WHERE 555 = NXX (3 NUMERICS)

- WHERE 1234 = LINE NUMBER (4 NUMERICS)

21.2.151 Usage

FEATURE LEVEL ACTIVITY

A C D R C O

Required when establishing or modifying User Profiles. Otherwise not applicable.

21.2.152 Data Characteristics

Term Definition Length of Element: Ten to five-hundred (10-500) character. Alpha/Numeric/Any Valid entries are numerics, dashes, and blanks.

ISDN BRI
EWSD

21.2.153 FID Name

(TSPD) - TERMINAL SERVICE PROFILE IDENTIFIER

21.2.154 Purpose

Indicates the telephone number of the Terminal Service Profile.

/TSPD 205 555-1234-01

- Where 205 555-1234 = telephone number of the TSP

- Where 01 = TSP Identifier (2 numerics)

21.2.155 Usage

FEATURE LEVEL ACTIVITY

A C D R C O

21.2.156 Data Characteristics

Term Definition Length of Element: Fifteen (15) characters. Alpha/Numeric/Any Valid entries are numerics, dashes, and blanks.

ISDN BRI
5ESS and DMS100

21.2.157 FID Name

(TSW) - TYPE OF SWITCH

21.2.158 Purpose

Indicates the central office type from which end-user service is provisioned.

WHEN TSW APPEARS, IT MUST BE IN THE FOLLOWING FORMAT:

/TSW XXXXX
WHERE XXXXX ONE OF THE FOLLOWING CHOICES

- 5E-(AT&T) 5ESS SWITCH)

- D100-(NTI DMS-100)

- EWSD--SEIMENS )

21.2.159 Usage

FEATURE LEVEL ACTIVITY

A C D R C O

21.2.160 Data Characteristics

Term Definition Length of Element: 2 - 5 Alpha/Numeric/Any ANY ALLOWABLE SERVICE ORDER CHARACTER

ISDN BRI
DMS

21.2.161 FID Name

(TTYD) - TERMINAL TYPE

21.2.162 Purpose

Identifies the specific EKTS terminal device type used.

WHEN TTYD APPEARS IT MUST APPEAR IN THE FOLLOWING FORMAT:

/TTYD EKTS, CACH

- WHERE EKTS = 4 ALHABETICS OF EKTS ((ELECTRONIC KEY TELEPHONE SERVICE)(ISDN ONLY)) (REQUIRED)

- WHERE CACH = 4 ALPHABETICS OF CACH ((CALL APPEARANCE CALL HANDLING (BCS 34 OR LATER)) PRECEDED BY A COMMA AND A SPACE (OPTIONAL)

21.2.163 Usage

FEATURE LEVEL ACTIVITY

A C D C C O

Required service requests entails provisioning service involving EKTS terminal equipment. Otherwise not applicable.

21.2.164 Data Characteristics

Term Definition Length of Element: Four to ten (4-10) characters. Alpha/Numeric/Any Valid data types include any allowable service order character.

ISDN BRI
5ESS

21.2.165 FID Name

(TTYP) - TERMINAL TYPE

21.2.166 Purpose

Indicates the end user device type and related options for multibutton service on an ISDN terminal.

WHEN TTYP APPEARS IT MUST BE IN THE FOLLOWING FORMAT:

/TTYP X 
WHERE X = 1-3 NUMERICS OF 1-999

21.2.167 Usage

FEATURE LEVEL ACTIVITY

A C D C C O

Note: WHEN THE FID CSO APPEARS ON AN INWARD ACTION CODE, THE FID TTYP MUST ALSO APPEAR.

21.2.168 Data Characteristics

Term Definition Length of Element: 1 - 500 Alpha/Numeric/Any ANY ALLOWABLE SERVICE ORDER CHARACTER

ISDN BRI
EWSD

21.2.169 FID Name

(TTYT) TERMINAL TYPE

21.2.170 Purpose

Defines the terminal type used in an ISDN configuration, e.g., EKTS, CACH, BCE, and terminal options.

WHEN TTYT APPEARS IT MUST BE FORMATTED AS FOLLOWS:

/TTYT EKTS.Y; BCE.Y; CACH.Y; ICOM.Y, ICG.2 3 5

- WHERE EKTS = TERMINAL OPTIONS ATTRIBUTE NAME (REQUIRED) 3- 4 ALPHABETICS OF:

  - EKTS -LECTRONIC KEY TELEPHONE SERVICE

  - BCE-BRIDGED CALL EXCLUSION

  - CACH-CALL APPEARANCE CALL HANDLING

  - PCA-PRIVACY CHANGE ALLOWED

  - SRT-STATION RINGING TRANSFER

  - ICG-INTERCOM

  - ICOM-NTERCOM GROUPS

- WHERE Y = TERMINAL OPTIONS ATTRIBUTE VALUE (OPTIONAL) (1 ALPHABETIC OF:)

  - Y-(YES)

  - N-(NO)

- WHERE 2 = TERMINAL OPTION ICG ATTRIBUTE VALUE (OPTIONAL) (1-6 NUMERICS FROM 1 TO 999999)

- WHERE 3 = TERMINAL OPTION ICG CALL APPEARANCE ATTRIBUTE VALUE (OPTIONAL) (1-5 NUMERICS FROM 1 TO 16383)

- WHERE 5 = TERMINAL OPTION ICG INTERCOM ADDRESS ATTRIBUTE VALUE (OPTIONAL) (1-2 NUMERICS FROM 1 TO 99)

Note: Elements 1 and 2 may appear in a series separated by a semicolon and a space.

Note: Terminal options attribute name date of ICG may only appear when terminal option attribute name data of ICOM appears.

Note: When element 2 appears it must be separated from element 1 by a period.

Note: Elements 3, 4 and 5 must and may only appear when terminal options attribute name data of ICG appears and they must be separated from element 1 by a period.

Note: When Elements 3, 4 and 5 appear they must be separated by a space.

21.2.171 Usage

FEATURE LEVEL ACTIVITY

A C D C C O

Required when EKTS terminal equipment is used as terminating device in an ISDN service arrangement.

21.2.172 Data Characteristics

Term Definition Length of Element: Three to sixty-four (3-64) characters. Alpha/Numeric/Any Any allowable service order character is valid.

Note: Applicable for EKTS only