32 PBX ON / OFF PREMISE

32.1 PBX On / Off Premise

32.1.1 Description

PBX Station Lines or Extensions of Station Lines can be extended to locations on the same continuous property or to a different address within the same LATA. This documentation provides information relative to the “On Same Premises” and “Off Premises” located at a Different Premise. This Document is limited to cases where the PBX Switch and the Off Premises locations are in the same Exchange (Intraexchange/IntraLATA) PBX Stations that are extended to a different Exchange are called Interexchange/IntraLATA and are not added to the PBX Class of Service. These Interexchange/IntraLATA PBX Extensions are treated as FX Service and have a unique Class of Service and will be found in the Foreign Exchange section..

ALL OFF PREMISE PBX EXTENSIONS ARE DESIGNED SERVICES AND REQUIRE SPECIAL PROVISIONING AND TESTING.

32.1.1.1 Ordering Considerations

CLCI/SS (Common Language Circuit Identification/Special Services) On or Off Premise PBX Extensions must be Circuit Identified. The CLS FID is used on the record. The Circuit ID is entered in the ECCKT Field on the Resale Services Form. The Service Code assigned is OS. New CLS ID's are assigned by AT&T Southeast Region. On existing circuits use the CLS data found on the records.

32.1.1.2 ON PREMISE PBX EXTENSIONS

PBX On Premise Extensions are obsolete and are only provided where existing facilities are in place. See the appropriate Private Line Tariff (B103) for additional information.

In those locations where it is appropriate to order a new On Premise PBX Extension, the USOC 1LV+E should be entered on the order Resale Services form in the Feature Field. When the On Premise Extension is at the same address enter the FID LOC and the location (Room, Suite, Floor) where the extension is to be placed in the Feature Detail Field. If the Addresses are not the same enter the FID DPA on the order as explained below. Typically addresses on the same premises are less than 1/10 mile apart. Since the 1LV+E USOC quantity must be greater than 1 is these locations are more than 1/10 mile apart enter the FID QTY in the Feature Detail Field followed by the quantity greater than 1. The quantity will be entered with the USOC on the order and the FID QTY will not be found on the records.

32.1.1.3 Different Premise Address (DPA) Fid REQUIRED For Off Premises

The address where an Off Premise PBX Extension is located or desired must be provided following the FID DPA on the Resale Service form preceding the USOCs desired at this location. The address where the PBX Switch is located should appear on the End User form and any USOCs requested at the PBX Switch location should precede the appearance of the DPA FID. Both addresses must be RSAG validated.

Review the FID specs for DPA. One of the components is the Numeric Identifier that is used for sorting on the records. Review an existing account to determine if a DPA may already exist at the address where service is requested. If so use the numeric identifier associated with the existing DPA. When the account is new. assign the DPA Numeric Identifier starting with 1.

32.1.1.4 OFF PREMISE PBX EXTENSIONS-SERVED DIRECT (NOT FROM CENTRAL OFFICE)

In rare cases, facilities may be available to provide an Off Premise PBX Extension to a location within an airline mile of the main station location “served direct” rather than from a central office channel. If this type of circuit is ordered and can not be provided, the order must be canceled and reissued to request an Off Premise PBX Extension that is provided from the Central Office.

Enter the USOC SDD2X or ILVBM on the Resale Services form in the Feature Field.

A signaling USOC SALSD, SAUSD or SAYSD must be entered in the Feature field of the Resale form

32.1.1.5 TWO LOCAL CHANNELS AND SIGNALING ARE REQUIRED FOR OFF PREMISE

To provide an Off Premise PBX Extension two Local Channels (P2JHX or LCQSQ) and associated signaling equipment (SAL, SAU OR SAY) are needed. One local Channel connects the PBX Switch to the serving Central Office. The second Local Channel connects the Different Premise Address (DPA) to it's serving Central Office.

These USOCs and required FID Data should be entered on the Resale Services Form.

32.1.1.6 INTEROFFICE CHANNEL MAY Be Added To Order

When the serving Central Offices at the PBX Switch location and the DPA Location are not the same, an Interoffice Channel will be added to connect the circuit between the two central offices to complete the path. Channel Terminals are required for each end of an Interoffice Channel in some tariffs.

32.1.1.7 FACILITY INTERFACE CODE (FIC) MUST BE PROVIDED

The Facility Interface Code (FIC) is critical in the Design process for Off Premise PBX Extensions (USOCs P2JHX or LCQSQ). This information is provided by the customer or the PBX Vendor. The valid codes are OL13A, OL13B, OL13C or OPS. These FIDs must be entered in the Feature Detail Field on the Resale Form following the P2JHX or LCQSQ USOCS.

32.1.1.8 LINK CONNECT TO CUSTOMER PURCHASED HICAP

The appropriate Network Access Service Feature Activation Charge USOC can replace the Local Channels or Interoffice Channels when a portion of the circuit rides a customer purchased Hicap arrangement. The FIDs CFA, DSNA and XPOI must be provided with the Feature Activation Charge USOC (1PQWP) in lieu of the Local Channel or Interoffice Channel USOCs. The Signally USOCs (SAL, SAU or SAY) and the FIC Code must still be provided for the special signaling and design for the Off Premise PBX Extension.

32.1.2 Restrictions

- Extension service must be located on the same premises of the subscriber on which the main station is located and is restricted to the use of the subscriber, his representatives and associates, or to members of the subscriber's immediate family or domestic establishment.

- On an individual basis, when facilities permit and there are no technical limitations, extensions for individual line subscribers may be located on a different premises, under certain conditions as listed below:

  - When two or more premises of the same subscriber are used in the conduct of one establishment or business.

  - When the extension is located on premises other than the subscriber's premises for the purpose of answering calls at such time as the subscriber is not available at the main station, but only when separate exchange is also provided on these other premises.

  - When the extension is located on the premises of a joint user.

- TouchStar Caller ID is not compatible with services that have Different Premises Addresses.

32.1.3 Tariff References

General Subscribers Service Tariff (GSST) Section A113. B3 Private Line Tariff

32.1.4 USOC/FID References

See PBX On/Off Premise Extension FIDs/Feature Details Table

Table 396. PBX ON OR OFF PREMISE EXTENSION USOCs / FEATURE CODES

USOC DESCRIPTION AL FL GA KY LA MS NC SC TN DD5 PBX EXTENSION-DIFFERENT BLDG - ON SAME PREMISE X X X X X X X X LCQSQ OFF PREMISE EXTENSION-LOCAL CHANNEL-1 EACH TO MAIN STATION AND OFF PREMISE ADDRESS X OMC ORDER MODIFICATION CHARGE X X X X X X X X X PMN CHANNEL TERMINAL-EACH END OF AN INTEROFFICE CHANNEL X P2JHX OFF PREMISE PBX EXTENSION-LOCAL CHANNEL 1 EACH CENTRAL OFFICE TO MAIN STATION AND CENTRAL OFFICE TO OFF PREMISE ADDRESS X X X X X X X X SAL PBX OFF PREMISE EXT-TYPE A SIGNALLING 0-199 OHMS-WITH EACH LOCAL CHANNEL X X X X X X X X X SALSD PBX OFF PREMISE EXT-TYPE A SIGNALLING 0-199 OHMS-WITH EACH LOCAL CHANNEL-SERVED DIRECT X X X X X X X X X USOC DESCRIPTION AL FL GA KY LA MS NC SC TN SAU PBX OFF PREMISE EXTENSION TYPE B SIGNALLING 200-899 OHMS-WITH EACH LOCAL CHANEL X X X X X X X X X SAUSD PBX OFF PREMISE EXTENSION TYPE B SIGNALLING 200-899 OHMS SERVED DIRECT-WITH EACH LOCAL CHANNEL X X X X X X X X X SAY PBX OFF PREMISE EXTENSION TYPE C SIGNALLING 900 OR MORE OHMS-WITH EACH LOCAL CHANNEL X X X X X X X X X SAYSD PBX OFF PREMISE EXTENSION TYPE C SIGNALLING 900 OR MORE OHMS SERVED DIRECT-WITH EACH LOCAL CHANNEL X X X X X X X X X SDD2X PBX OFF PREMISE EXTENSION-NON WIRE CENTER CONNECTED-SERVED DIRECT X X X X X X X X 1LPGH INTEROFFICE CHANNEL MILEAGE FOR PBX OFF PREMISE EXTENSION PER MILE-INTRAEXCHANGE X 1LV+E MMILEAGE PER 1/10 MILE FOR ON PREMISE PBX EXTENSIONS X X X X X X X X X 1LVBM PBX OFF PREMISE EXTENSION-NON WIRE CENTER CONNECTED-SERVED DIRECT X X 3LBBS INTEROFFICE CHANNEL MILEAGE FOR PBX OFF PREMISE EXTENSION FIXED AND PER MILE-INTRAEXCHANGE X X X X X X X X

Table 397. PBX ON OR OFF PREMISE EXTENSION FIDs / FEATURE DETAILS

FID/FEATURE DETAIL DPA FIC LOC USOC/FEATURE CODE DD5 X LCQSQ X R OMC PMN P2JHX X R SAL SALSD SAU SAUSD SAY SAYSD SDD2X X FID/FEATURE DETAIL DPA FIC LOC USOC/FEATURE CODE 1LPGH 1LV+E X 1LVBM X 3LBBS

32.2 FID ANALYSIS AND MAPPING PRODUCTS & SERVICES

32.2.1 FID Name

DPA - DIFFERENT PREMISES ADDRESS

32.2.2 Purpose

Indicates services that appear following (under) the DPA FID appearance on the order are located at an address different from the main address.

32.2.3 Usage

FEATURE LEVEL ACTIVITY

A C D O O O

32.2.4 Data Characteristics

Term Definition Length of Element: Minimum Data Characters: 1 Maximum Data Characters: 500 Alpha/Numeric/Any Any valid character

Example:

Example:   DPA 2-123-A MAIN ST, ANYTOWN, GA

32.2.5 FID Name

FIC - FACILITY INTERFACE CODE

32.2.6 Purpose

Indicates the Facility Interface Code for Customer Provided Equipment (CPE) to assure circuit design is compatible with the customer's premises equipment.

32.2.7 Usage

FEATURE LEVEL ACTIVITY

A C D O O O

32.2.8 Data Characteristics

Term Definition Length of Element: Minimum Data Characters: 3 Maximum Data Characters: 8 Alpha/Numeric/Any Alphanumerics

Example:

Example:   FIC OL13B

32.2.9 FID Name

LOC

32.2.10 Purpose

Identifies the specific location of a station or item of equipment by hierarchical level.

32.2.11 USAGE RULES

The levels and level identifiers are as follows:

- LEVEL ONE

  - BLDG - BUILDING

  - WNG - WING

  - PIER - PIER

- LEVEL TWO 
FLR - FLOOR

- LEVEL THREE

  - APT - APARTMENT

  - RM - ROOM

  - LOT - LOT

  - SLIP - SLIP

  - SUIT - SUITE

  - UNIT - UNIT

- LEVEL FOUR 
Description

32.2.12 Usage

FEATURE LEVEL ACTIVITY

A C D O O O

32.2.13 Data Characteristics

Term Definition Length of Element: Minimum Data Characters: 1 Maximum Data Characters: 300 Alpha/Numeric/Any Any valid service order characters

Example:

- /LOC BLDG 1493; FLR 45; APT 76; DES Third apartment on right side of hall, red door
or

- /LOC APT 13 
or

- /LOC DES Desk in the corner by the window

Note: LOC Code Sets are separated by a semicolon.