## Multi-Service Optical Network (MON) Ring

Description	1

Features	2

MON Wavelength Channel (Riding Services)	2

Channel Protection	3

Basic MON RING Network	3

Availability	3

Restrictions/Limitations	3

Port limitations	4

PreOrdering	4

Ordering	5

Due Dates	5

USOCs/FIDs	5

Bulk Power	5

Mileage	5

Node Shelves	5

Optical Amplifier	5

Regenerator	5

Port	5

NC/NCI Codes	6

MON Ring, Optical amplifier, Regenerator	7

10-Gbps OFA & Regen	7

SONET & Subrate System MUX	8

Order Process Steps	10

Classes of Service	10

Common Language Circuit Identification (CLCI)	10

MON RING Network	10

MON RING Wavelength Channels (Riding Circuits)	10

Subrate System and Riding Circuits provisioned only on a Subrate System	11

Billing	11

Term Pricing Plans (TPP)	11

# Description

Multi-Service Optical Network (MON) Ring Service is designed for the physical transport of multiple data signals utilizing multiplexing technology in a dedicated ring configuration.  MON uses Cisco-based Dense Wavelength Division Multiplexing (DWDM) technology in a ring configuration. Multiple data signals are transmitted over fiber-optic cable using different wavelengths of light. Each wavelength represents a transmission channel in the MON Ring system and is protocol independent of every other channel.

## Features

- Offered in two configurations:

  - MON Ring with growth capacity up to 16 Wavelengths

  - MON Ring with growth capacity up to 32 Wavelengths

- Available in different Ring configurations utilizing central office nodes and customer premises nodes with a maximum of 8 sites and/or 40 shelves.

- Route Diversity is an available fiber configuration for the MON Ring and included in the cost of the MON Ring:

  - Configured with diversely routed fiber from the End User's property line to their Serving Wire Center or Alternate Wire Center as determined by the Utility where facilities and operating conditions permit. Diversity ensures loop fibers follow separate paths to the Serving Wire Centers or Alternate Wire Center.

  - The Interoffice Facility fiber paths may be diversely routed between Serving Wire Centers or Alternate Wire Centers, where facilities and operating conditions permit, to ensure any Central Office node fibers do not egress and ingress at the same location.

- At the end user’s  request, additional protection to the end user’s premise nodes may be provided via diverse dual entrance facilities and will be considered Special Construction.

  - In the case where dual entrance facilities are established at the end user’s premises, facilities routed through the same duct structure from the property line to the building MPOE location are not considered diverse and route diversity has not been established.

#### MON Wavelength Channel (Riding Services):

- Unprotected Channel configuration

- Protected Channel configuration.

  - Channel Protection provides protection for a single channel toward the network and does not protect the channel against failure towards the customer's interface

  - Protection reduces the maximum individual channel capacity of the system

- Subrate System protection

  - Wavelength Channels riding this Subrate System will receive protection

- Subrate System unprotected

  - Wavelength Channels riding this Subrate System can not receive protection

- Wavelength Channels SONET OC-3, Fast Ethernet, FICON, ESCON, ETR, ISC and Digital Video D1 Services can not terminate outside of a MON Ring.

- Wavelength Channels SONET OC-3, Fast Ethernet, ESCON and Digital Video D1 Services must be provisioned on the MON Ring using a Subrate Mux

### Channel Protection

Provides protection for a single channel toward the network and does not protect the channel against failure towards the customer's interface.   Note: Channel Protection may not be available for all interface types.

### Basic MON RING Network

# Availability

### Service is only available within the Local Access Transport Areas (LATAs) served by and within service territories of AT&T California and AT&T Nevada.

## Restrictions/Limitations

- Multi-service Optical Network (MON) Ring may have distance limitations based on the services carried and may require routing through Serving Wire Centers based on loss limitation between nodes.

- Services with facility length limitations may not be available on some MON Rings, or may not be available between some nodes on certain MON Rings.

- Additional services added (to the MON RING Network) subsequent to the initial installation may cause a service interruption to existing unprotected channels or a protection switch on protected channels.

- Optical Amplifiers and/or regenerators may be required subsequent to the initial installation.

- Service is only available within the Local Access Transport Areas (LATAs) served by and within service territories of AT&T California, not available in a meet point billing configuration.

- Neither electrical interfaces nor optical add/drop multiplexing are available with this service.

- Services with time-delay sensitive protocols have facility length limitations and may affect the design/availability of MON RING (e.g. CPU to CPU communications have a maximum distance limitation.).

  - These services will not be available on MON Rings between nodes when facility length limitations exceed the service specifications.

- The customer provided equipment must deliver the data signals for the Multi-service transport within the industry specification for the subscribed data services.

- The maximum capacity of a Multi-service Optical Network Ring is 32 wavelengths.

- A protective channel provides protection for a single channel toward the network. It does not protect the channel against failure towards the customer interface. Protection reduces the maximum individual channel capacity of the MON Ring.

- Conversion from Multi-Service Optical Network Point to Point or any other lower speed service to MON Ring is not available

- Mileage provides for the transmission facilities between the Serving Wire Centers of each Node involved on the ring.

- Minimum Mileage charges are also applicable to Optical Amplifiers or Regenerators that are located in the same SWC as a CO or Premises Node.

Note:  OC-192 and 10 Gbps WAN-PHY services will be available on MON Rings that offer only those services.  MON Ring service will not offer both the lower rate (e.g. 2.5 Gbps) services and the 10Gbps OC-192/OC-192c services on the same Ring.

#### Port limitations

- Fibre Channel port channel is limited to a maximum distance of 100 km and actual data throughput is distance sensitive.

- ESCON port channel is limited to a maximum distance of 43 km and actual data throughput is distance sensitive.

- ETR is limited to a maximum distance of 40 km

- FICON is limited to a maximum distance of 100 km and actual data throughput is distance sensitive.

- ISC is limited to a maximum distance of 40 km

- The maximum distance fiber length the protocol can travel before the signal degrades varies by protocol.

# PreOrdering

Mechanized pre-ordering Operational Support System (OSS) is available to assist the CLECs on obtaining pre-ordering information. However, certain orders require a manual pre-ordering transaction before an LSR can be submitted successfully.  Refer to the Pre-Ordering section of the handbook for additional information.

When performing a manual pre-ordering transaction, fill in the LSR request as completely as possible using EDI/WebLEX. When the needed manual pre-ordering information is filled out, save the LSR request. Print a copy of the request and fax it to AT&T along with the Manual Pre-Ordering Information Cover Sheet.  AT&T will fax back the needed pre-ordering information so the CLEC can successfully submit a firm LSR.

# Ordering

## Due Dates

- Due Dates are determined during negotiation process.

## USOCs/FIDs

### Bulk Power

| Description | USOC |
| --- | --- |
| Bulk Power Shelves 1-4 | CBVDX |
| Subsequent Shelves 5-8 | CBVDS |

### Mileage

| Description | USOC |
| --- | --- |
| Per Mile (36 month term) | 1L5X3 |
| Per Mile (60 month term) | 1L5X5 |
| Per Mile (monthly extension) | 1L5XS |

### Node Shelves

| Description | USOC |
| --- | --- |
| Customer Premise Node/includes first shelf | F2ND1 |
| Per Subsequent Shelf | F2NDS |
| Central Office Node/includes first shelf | F2NC1 |
| Per Subsequent Shelf | F2NCS |

### Optical Amplifier

| Description | USOC |
| --- | --- |
| Per location C Band | 67QXX |
| Per location L Band | 67QSX |

### Regenerator

| Description | USOC |
| --- | --- |
| Up to 2.5 Gbps | V8RXX |
| Up to 10 Gbps | V8R2C |

### Port

| Description | USOC |
| --- | --- |
| D1 Video | POYVX POYVP |
| ETR | POYKW |

## NC/NCI Codes

- Wavelength Channels SONET OC-3, Fast Ethernet, FICON, ESCON, ETR, ISC and Digital Video D1 Services cannot terminate outside of a MON Ring.

- Wavelength Channels SONET OC-3, Fast Ethernet, ESCON and Digital Video D1 Services must be provisioned on the MON Ring using a Subrate Mux

| Service Type | NC Code | NC Code Unprotected | NCI Premise/POP | NCI Central Ofc. |
| --- | --- | --- | --- | --- |
| Digital Video D1 | TD-P | TD - - | 02TDF.E | NA |
| ETR (16 Mbps) | - | OPA | 02OPF.A02 (1310nm,SMF) | NA |
| Ethernet WAN PHY (9.953) | KGWP | KGW- | 02LNF.A02 (1310nm,SM) 02LNF.A04 (850nm,MM) 02LNF.A05 (1310nm,MM) | NA |
| ESCON (200 Mbps,MMF) | - | OPB- | 02OPF.A02 (SMF) 02OPF.A05 (MMF) | NA |
| Fast Ethernet (100 Mbps) | - | KEA- | 02LNF.A02 | NA |
| Fibre Channel (1.06 Gbps) | OPFP | OPF- | 02OPF.A04 (850nm,MMF) 02OPF.A02 (1310nm, SMF) | NA |

| Service Type | NC Code | NC Code Unprotected | NCI Premise/POP | NCI Central Ofc. |
| --- | --- | --- | --- | --- |
| Fibre Channel (2.125 Gbps) | OPJP | OPJ- | 02OPF.A02 (1310nm,SMF) | NA |
| FICON (1.06 Gbps) | OPDP | OPD- | 02OPF.A02 (1310nm,SFM) 02OPF.A04 (850nm,MMF) | NA |
| FICON (2.125 Gbps) | OPEP | OPE- | 02OPF.A02 (1310nm,SMF) | NA |
| Gigabit Ethernet (1.25Gbps) | KFLP | KFL- | 02LNF.A02 (1310nm,SMF) 02LNF.A04 (850nm,MMF) 02LNF.A05 (1310nm,MMF) | NA |

Note:  Wavelength Channels SONET OC-3, Fast Ethernet, FICON, ESCON, ETR, ISC and Digital Video D1 Services cannot terminate outside of a MON Ring and must be provisioned on the MON Ring using a Subrate MUX.

### MON Ring, Optical amplifier, Regenerator

| Service Type | NC Code | Description | NCI Premise/POP | NCI Central Ofc. |
| --- | --- | --- | --- | --- |
| MON Ring | DSDC | Provides 2.5Gbps Wavelength Channel Capacity | 02FMF.004 (4 Wavelengths) 02FMF.008 (8 Wavelengths) 02FMF.012 (12 Wavelengths) 02FMF.016 (16 Wavelengths) | 02FMF.004 02FMF.008 02FMF.012 02FMF.016 |
| MON Ring | DTDC | Provides 10Gbps Wavelength Channel Capacity | 02FMF.004 (4 wavelengths) 02FMF.008 (8 Wavelengths) 02FMF.012 (12 Wavelengths) 02FMF.016 (16 Wavelengths) | 02FMF.004 02FMF.008 02FMF.012 02FMF.016 |
| Optical Amplifier | DSDC | Optical Fiber Amplifier 2.5Gpbs Wavelength Channel Capacity | 02OAF | 02OAF |
| Regenerator | DSDD | Optical Regenerator 2.5 Gbps Wavelength Channel Capacity | 0SOAF | 02OAF |

### 10-Gbps OFA & Regen

| Service Type | NC Code Protected | NC Code Unprotected | NCI Premise/POP | NCI Central Ofc. |
| --- | --- | --- | --- | --- |
| Optical Amplifier | DTDC | Provides 10-Gbps Wavelength Channel Capacity | 02OAF | 02OAF |
| Regenerator | DTDC | Provides 10-Gbps Wavelength Channel Capacity | 02RGF.004 (4 Wavelengths) 02RGF.008 (8 Wavelengths) 02RGF.012 (12 Wavelengths) 02RGF.016 (16 Wavelengths) | 02RGF.004 02RGF.008 02RGF.012 02RGF.016 |

Note:  Wavelength Channels SONET OC-3, Fast Ethernet, FICON, ESCON, ETR, ISC and Digital Video D1 Services cannot terminate outside of a MON Ring and must be provisioned on the MON Ring using a Subrate MUX.

### SONET & Subrate System MUX

| Service Type | NC Code Protected | NC Code Unprotected | NCI Premise/POP | NCI Central Ofc. |
| --- | --- | --- | --- | --- |
| SONET OC3 (155 Mbps) | OBT - | OB - - | 02SOF.X | 02QBF.LL |
| SONET OC-3c (155 Mbps) | OBTR (Concatenated) | OB-R (Concatenated) | 02SOF.X | 02QBF.LL |
| SONET OC-12 (622 Mbps) | ODT - | OD - - | 02SOF.X | 02QBF.LL |
| SONET OC-12c (622 Mbps) | ODTR (Concatenated) | OD-R (Concatenated) | 02SOF.X | 02QBF.LL |
| SONET OC-48 (2.5 Mbps) | OFT - | OF - - | 02SOF.X | 02QBF.LL |
| SONET OC-48c (2.5 Mbps) | OFTR (Concatenated) | OF-R (Concatenated) | 02SOF.X | 02QBF.LL |
| SONET OC-192 (9.953 Mbps) | OGT - | OG - - | 02SOF.X | 02QBF.LL |
| SONET OC-192c (9.953 Mbps) | OGTR (Concatenated) | OG-R (Concatenated) | 02SOF.X | 02QBF.LL |
| (4:1) Subrate System (Mux) 270 Mbps | PISP | PIS- | 02FMF.S | 02FMF.S |

Note:  Wavelength Channels SONET OC-3, Fast Ethernet, FICON, ESCON, ETR, ISC and Digital Video D1 Services cannot terminate outside of a MON Ring and must be provisioned on the MON Ring using a Subrate MUX.

## Order Process Steps

- CLEC contacts Account Manager to request MON and assist in determining MON requirements.

- When CLEC accepts the contract, an Interdepartmental Meeting is arranged with Account Manager, LSC, LOC and Network team to discuss project and critical dates

- CLEC submits LSR for MON with agreed upon dates

- MON and associated riding service orders must be related using the RPON field

## Classes of Service

| Description | Class of Service |
| --- | --- |
| CPUC | CPUC |
| MON Ring Monthly Intraex-Intradistrict | HCXRM |
| MON Ring Monthly Intraex-Interdistrict | HCXRR |
| MON Ring Monthly Interexchange | HCXRT |
| MON Ring 3 - Year Intraex-Intradistrict | HCXSM |
| MON Ring 3 - Year Intraex-Interdistrict | HCXSR |
| MON Ring 3 - Year Interexchange | HCXST |
| MON Ring 5 - Year Intraex-Intradistrict | HCXTM |
| MON Ring 5 - Year Intraex-Interdistrict | HCXTR |
| MON Ring 5 - Year Interexchange | HCXTT |

## Common Language Circuit Identification (CLCI)

### MON RING Network

| 3rd & 4th Service Code | 5th & 6th Position Modifiers | MON RING Network |
| --- | --- | --- |
| WC | XS | No Further Parameters Required |
| WC | XZ | Official Company Services |

### MON RING Wavelength Channels (Riding Circuits)

| 3rd & 4th Service Code | 5th & 6th Position Modifiers | MON RING Riding Circuits |
| --- | --- | --- |
| OF | FS | OC-48/OC-48c |
| OD | FS | OC-12/OC-12c |
| OZ | XS | Fibre Channel 1.06Gbps (850nm MMF) |
| OZ | XS | Fibre Channel 1.06Gbps & 2.125Gbps (1310nm, SMF) |
| OZ | XS | FICON Channel 1.06Gbps (850NM, MMF) |
| OZ | XS | FICON Channel 1.06Gbps & 2.125Gbps (1310NM SMF) |
| OZ | XS | ISC |
| OZ | XS | ETR |
| KG | FS | Ethernet WAN PHY 9.953 Gbps (SMF & MMF) |
| OG | FS | OC-192/OC-192c (SMF) |
| KF | FS | Gigabit Ethernet 1.25 Gbps 1000base-SX (850nm, MMF) (1310nm, SMF & MMF) |

### Subrate System and Riding Circuits provisioned only on a Subrate System

| 3rd & 4th Service Codes | 5th & 6th Position Modifiers | Subrate System and Riding Circuits |
| --- | --- | --- |
| WC | XS | Subrate System |
| KE | FS | Fast Ethernet (100Mbps) |
| OZ | XS | ESCON (200Mbps SMF & MMF) |
| TD | FS | Digital Video |
| OB | FS | OC-3/OC-3c |

# Billing

Refer to state tariff for additional information.

## Term Pricing Plans (TPP)

- End user must select either a 36 or 60 month plan. (The minimum service period for Multi-service Optical Network Ring is 36 months.)

- When a service is discontinued prior to the expiration of the minimum period, termination charges are applicable for the remaining portion of the minimum period (whether the service is used or not) and will be based on the rates in effect for the service at the time of discontinuance.

- If the end user does not elect a new TPP after completion of a TPP and does not request discontinuance of service, service will be continued at the monthly extension rate currently in effect. At a later date the customer may elect any TPP option currently in effect for new customers.

  - Monthly extension rates for Multi-service Optical Network Ring will apply only after a customer has completed a TPP term.

  - Monthly extension TPP prices applicable for the new term are those currently in effect for new customers.