OC-N Point To Point

Description	1

Features	2

Standard	2

Optional	2

Availability	3

Restrictions/Limitations	3

Ordering	3

USOC	3

Classes of Service	3

CLCI Code / SN Code	3

Technical Publications	3

Billing	4

Term Pricing Plan	4

# Description

OC-N Point to Point (PTP) service is designed to provide the CLEC with a custom point to point linear network.  The Optical PTP service will offer a highly reliable transport service that is designed to connect CLEC end user locations and AT&T wire centers in a linear configuration.  Large volumes of information can be transported between two locations in a dedicated, high-bandwidth optical path.  Specifically, the OC-N PTP services can handle voice, data, video, imaging, internet traffic and other advanced broadband applications.

OC-N PTP service provides optical data transmission channels that may be used to connect:

- An end user designated premises to another end user designated premises with add/drop multiplexing capability at wire center locations between the two premises.

- An end user designated premises to another end user designated premises without the add/drop multiplexing capability.

- An end user designated premises to a Telephone Company location where add/drop multiplexing, add/drop functions and/or cross connections are performed.

Basic OC-N PTP service provides non-protected 2-fiber paths between the two designated locations where facilities exist.  All OC-N circuits will be configured based on end user requirements that have been provided to AT&T at the time of ordering.

Optical data transmission will be provided with the following characteristics:

- OC-3 service provides channels operating at the terminating bit rate of 155.52 Mbps

- OC-12 service provides channels operating at the terminating bit rate of 622.08 Mbps.

- OC-48 service provides channels operating at the terminating bit rate of 2488.32 Mbps.

- OC-192 service provides channels operating at the terminating bit rate of 9953.28 Mbps.

## Features

### Standard

- Local Distribution Channel

- Interoffice Transport

### Optional

- OC-n Add/Drop Multiplexing

- Protection

  - 1+1 Protection

  - 1+1 Protection with Cable Survivability

  - 1+1 Protection with Route Survivability

- Point-to-point regenerator

- Add/Drop Function

|  | DS1 | DS3 | OC-3 | OC-12 | OC-48 |
| --- | --- | --- | --- | --- | --- |
| OC-192 | No* | Yes^ | Yes | Yes | Yes |
| OC-48 | No* | Yes | Yes | Yes | N/A |
| OC-12 | Yes | Yes | Yes | N/A | N/A |
| OC-3 | Yes | Yes | N/A | N/A | N/A |

Note:  (*) To add/drop a DS1 from an Oc-12 and/or OC-48, an intermediate step at either OC-3 or DS3 must be taken.
Note:  (^) Only the first 24 DS3s will be dropped directly off an OC-192; 25th DS3 requires an OC-3, OC-12 or OC-48 subtended shelf.

# Availability

Effective June 4, 2002 in California and Nevada

## Restrictions/Limitations

- OC-N PTP service is available only on a point-to-point intraLATA basis to end users served by and within the service territories of PB/NB only.

- OC-N PTP service can only be provided within the same LATA where existing facilities and equipment permit.

- Services between serving wire centers must have appropriate service components between all intermediate offices to have the ability to provide the service.

- Additional service features may be available only at selected central offices as determined by AT&T.

- Service connectivity is available to other Special Access Services as long as the service level is identical.

- Concatentated services cannot be multiplexed.

AT&T Nevada OC-N Service channels may be connected by:

- Using the appropriate OC-N add/drop multiplexer along with the add/drop function to a High Capacity DS1 and/or DS3 service at suitably equipped wire centers or,

- Using the full bandwidth premises to premises.

# Ordering

- End user is responsible to identify the STS signal configuration.

## USOC

Refer to USOC Search Tool for USOC/FID information.

## Classes of Service

XSN2X                        OC-192 Point to Point

## CLCI Code / SN Code

Please refer to the Carrier Coding Guide, Tabs 11 and 12, for SN code / CLCI code information.

# Technical Publications

Technical References (AM-TR-NIS-000111, AM-TR-TMO-000101)  can be obtained from:

Manager-TIRM Office
2000 W. Ameritech Center Drive, Locn 3A09F
Hoffman Estates, IL 60196

# Billing

Refer to tariff for additional information regarding recurring/non-recurring charges as well as Term Pricing Plan and termination charges.

## Term Pricing Plan

- TPP provides for rate stabilization with a 3 or 5-year term agreement.

- If end user cancels prior to the expiration of the term agreement, termination charges will apply.