National ISDN 2

Description	2

Feature Descriptions	2

ISDN Calling Name Delivery	2

Two B Channel Transfer	2

Redirected Number	3

Availability	3

Restrictions/Limitations	3

ISDN Calling Name Delivery	3

Two B Channel Transfer	3

DMS 100 specific information	4

5ESS specific information	4

Redirected Number	4

Selective Class of Call Screening	4

Ordering	4

# Description

National ISDN 2 (NI-2) is an industry standard for implementing PRI switch features nationwide.  It supports cost-effective applications.  National ISDN 2 specifications define PRI call control and provide platform stability via:

- Uniformity of end user interfaces and services

- Uniform PRI services

- Improved data capabilities

The features below are available to end users with PRI configured with NI-2:

- Caller ID - standard

- Call-by-call service selection - standard

- ISDN Calling Name Delivery - optional

- Two B channel Transfer - optional

- Redirected Number - optional

- Selective Class of Call Screening -optional

- Dialing Plan (5ESS only) – optional

- Alternate Routing – optional

- Enhanced Alternate Routing – optional

# Feature Descriptions

## ISDN Calling Name Delivery

Allows ISDN Calling Name Delivery with call control to send calling party name to ISDN Class II equipment on inbound calls to the PRI.

## Two B Channel Transfer

Allows the ISDN PRI to connect two calls, transfer the calls together and then release the parties from the ISDN PRI.

## Redirected Number

Provides the redirected number (ie., the directory number to which the call was last presented) to the PRI CPE as well as the calling number in cases when call forwarding is invoked.

If, during call establishment phase, the call is redirected to another directory number by call forwarding, both the calling party number and redirected number are delivered to the called party on the PRI.

Example:  Caller A (non-PRI) calls Caller B (non-PRI) who forwards the call to Caller C over a PRI trunk.  In this scenario, caller B is the “originally called directory number” and the feature generates one redirecting number that becomes part of the redirection information that the PRI receives.

If a call is redirected multiple times, only the first and last redirecting numbers are delivered.  The calling party number, not the “redirecting number” is delivered to the Caller ID device.

# Availability

Available in 5ESS, DMS100 and NI-2 Protocol only

# Restrictions/Limitations

## ISDN Calling Name Delivery

Is not available with Custom.    Calling Name Delivery is a terminating feature available only for inbound calls to the PRI.

## Two B Channel Transfer

- Available with NI-2 only and not available with Custom.

- Available on a per trunk group basis only

- Custom PRI feature equivalent is Deluxe Call Transfer (DMS100 only)

- Available for:

  - Voice and date in the Nortel switch

  - Voice only in the Lucent 5E switch

  - Usage billing applies to each call transferred

### DMS 100 specific information

- For Notel Inter-PRI Trunk Group B Channel Transfer, the feature must be established on all PRI trunk groups involved.

- A service group name must be created and applies to all trunk groups involved.  The service group name can be up to 16 alphanumeric characters.

### 5ESS specific information

For Lucent Inter-PRI Trunk Group B Channel Transfer:

- The feature must be established on all PRI Trunk Groups involved.  Important:  The PRIs involved MUST be served from the same switch module.

- A service group name must be created and applied to all trunk groups involved.

## Redirected Number

- Not available with Custom

- If the redirected number is blocked, it will not be sent

- Redirected Number is a terminating feature for inbound calls to the PRI and does not apply to outbound calls.

## Selective Class of Call Screening

Allows the user, by means of Telephone Company operator identification, to restrict outgoing calls to those which are charged to the called telephone number, a third number or a Telephone Company calling card.

Note:  Effective in Nevada only as of February 18, 2003.

# Ordering

CLEC must determine compatibility of features with CPE or provide compatible CPE.  CLEC must determine CPE requirements for translations or reprogramming to accommodate feature.

USOCs are noted below.  Refer to USOC/Search tool for further USOC/FID information.

- NM1PG – ISDN Calling Name Delivery

- 2BTPG – Two B Channel Transfer

- RN4PQ – Redirected Number