SmartTrunk

Description	1

SmartTrunk Technology	1

Optional Features	2

Aliases	2

Availability	2

Restrictions/Limitations	2

PreOrdering	3

Ordering	3

Due Dates	3

USOC/FIDs	3

Class of Service	3

Billing	3

Term Agreements	4

Contract Pricing	4

# Description

Primary Rate ISDN SmartTrunk service provides access to and from the Public Switched Telephone Network for Circuit Switched Voice (CSV) and Circuit Switched Data (CSD) communications.

- Allows the end user to transmit data at high-speeds to accommodate voice, data, image and video over the same digital facility

- Creates a completely digital connection, using ISDN technology, between an End User's digital Private Branch Exchange (PBX) and the SBC Central Office (CO)

- Provisioned as a 1.544 Mbps DS1 pipe and configured as:

  - 23 B (64 kbps) channels

  - 1 D (64 kbps) channel

## SmartTrunk Technology

Each SmartTrunk PRI span requires Bipolar eight-bit Zero Substitution (B8ZS) encoding and Extended Superframe Format (ESF), to allow unrestricted, clear-channel transmission at a rate of 64 Kbps on each channel.

Service components consist of:

- SmartTrunk Interface

- Integrated Services Digital CSV/CSD transport option

  - 2-way trunks

  - 1 way in only trunks

  - 1 way out only trunks

  - DID trunks

### Optional Features

- Dynamic Channel Allocation

- Network Ring Again

- Backup D-Channel

- Loop Protection

- Calling Line Identification

- Enhanced Alternate Route

- E9-1-1 Upgrade

- Station Record Detail

- SmartTrunk port

- Circular Hunt

- 2B Channel Transfer

- Redirected Number

- Loop protection

- Common Line 800 Service

- Link Extension

- Outward WATS Option

- High Speed Transport (Texas only)

## Aliases

- ISDN PRI

- Primary Rate Interface

# Availability

SmartTrunk service is available in Arkansas, Kansas, Missouri, Oklahoma and Texas dependent on facilities and availability in central office.

## Restrictions/Limitations

- Requires PRI ISDN compatible equipment.

- SmartTrunk service is not offered on a stand-alone basis.

- Vacation Service is not offered for SmartTrunk service.

- Upon subscribing to SmartTrunk, end user may be required to change telephone numbers.

- Redirected number is available over National ISDN-2 PRIs only.

  - End user CPE must be capable of identifying the information element standards for redirected number.

  - Redirected number is incompatible with Customer ISDN PRI access

- CSV/CSD Transport option is not required with tie line services.

- The primary and backup D Channels must be located on different trunk facilities.

- Private CPN Delivery is available only to those certified end users who request the capability.

  - Qualifying end user is described in FCC Memorandum Opinion and Order, CC Docket 91-281, adopted January 4, 2002.

  - End user must certified compliance with the waiver order’s eligibility requirements.

  - CLEC is responsible for keeping all end user compliance certification and must provide proof of certification if requested

- Sharing of common transport or SmartTrunk arrangements between multiple users is not permitted.

- Packet Switching is no longer available for SmartTrunk and is scheduled to be withdrawn August 1, 2006.

- Loop protection is available where fiber optic facilities are available.

# PreOrdering

Mechanized preordering Operational Support System (OSS) is available to assist the CLEC on obtaining preordering information.  However, certain orders require a manual preordering transaction before an LSR can be submitted successfully.  The manual preordering process is described in detail under the PreOrdering section of the handbook.

When performing a manual preordering transaction, fill in the LSR request as completely as possible using EDI/WebLEX.  When the needed manual preordering information is filled out, save the LSR request.  Print a copy of the request and fax it to AT&T along with the  Manual Preordering Information Cover Sheet.  AT&T will fax back the needed preordering information so the CLEC can successfully submit a firm LSR.

# Ordering

## Due Dates

Refer to the Resale Due Date matrix for standard due date intervals.

## USOC/FIDs

Refer to USOC Search Tool for USOC/FID information

## Class of Service

| USOC | Description |
| --- | --- |
| N1W++ | Flat-Custom ISDN |
| NP7++ | Flat-National ISDN |
| SZZ++ | Measured |
| SJN++ | Message |
| SGB++ | Hotel/Motel Flat |
| SJB++ | Hotel/Motel Message |

# Billing

Refer to state tariff for information regarding recurring and non-recurring charges.

## Term Agreements

Term Agreements are available for 12, 24, 36, 48, or 60 months.

- Renewal terms are not available in Arkansas, Kansas and Texas.

- Termination charges may apply if service is disconnected prior to the end of the term agreement.

## Contract Pricing

End users in Oklahoma that commit to a minimum of 24 months and subscribe to a minimum of 5 SmartTrunk interfaces or ports qualify for an additional discount.

# Footnotes

CLEC05-379, CLEC06-046, CLEC06-155