Channel Services - Series 1000

Description	1

Up to 20 Baud - Type 1011 Indiana	2

Up to 30 Baud	2

Up to 45 Baud - Type 1002B Ohio	3

Up to 55 Baud - Type 1002C Ohio	3

Up to 75 Baud	3

Up to 150 Baud - (Type 1006 Illinois	4

Civil Air Defense Warning System Channels	4

McCulloh Channel - Type 101 Michigan	5

Aliases	5

Features	5

Up to 30 Baud - Type 1102 Ohio	5

Up to 75 Baud - Types 1001 and 1002A Ohio	6

Availability	6

Restrictions/Limitations	7

Interactions	11

CPE Involvement	11

Pre-Ordering	11

Ordering	12

Circuit IDs (CLCI) & Secondary Classes of Service	14

Circuit Function Table	20

Due Dates	21

USOCs	21

NC/NCI	40

Miscellaneous Ordering Procedures	41

Billing	41

# Description

- Series 1000 Channel Service represents a signal grade category of services, furnished between specific points, for the transmission of signals generated by station equipment.

- These services are below voice grade and are used primarily for low-speed data transmission, supervisory control, remote metering and miscellaneous signaling purposes.

- They operate at rates up to 150 baud.

- Series 1000 Channels are furnished for intra-exchange or inter-exchange service on a two-point or multi-point basis.

## Up to 20 Baud - Type 1011 Indiana

- Type 1011 channels are furnished in Indiana for unidirectional transmission of contact closure or voltage or current transmissions.

- Type 1011 channels are two-wire interfaces with two-wire facilities suitable for signaling up to 20 baud; furnished for remote metering, supervisory control and miscellaneous signaling purposes.

- They are available for intra-exchange two-point or three- point service and inter-exchange two or three point service to a contiguous exchange.

- The Class of Service is RMT1+.

Note:

+ L = Intra-Exchange, S = Inter-Exchange

Up to 30 Baud - (Type 1001A Illinois, Type 1012 Indiana, Metallic MT3 Michigan, Type 1102 Ohio, Type 9001 Wisconsin, Type 9002 Wisconsin)

- These channels permit unidirectional transmission of contact closure or voltage or current transmissions at speeds up to 15 bits per second.

- They are two-wire interface with two-wire facilities.

- These channels are suitable for transmission of signals at rates up to 30 baud for remote metering, supervisory control and miscellaneous signaling.

- They may be provided using either end-to-end metallic facilities or using a combination of metallic and digital carrier facilities.

- Unconditioned metallic facilities, using a wire pair, will be provided where facilities and operating conditions permit.

- Where facilities will not allow for end-to-end metallic continuity, a digital carrier conditioning option is available.

- Digital carrier conditioning will convert most customer generated DC type signals to digital carrier system.

- For two-point and multi-point channels, the number of terminations coincides with the number of premises connect to the channel.

- These channels may be connected to the services or facilities of a carrier.

- All of these local channel services utilizing pairs from Service Transport Facility (STF) complements will require one pair per termination.

- They are available for intra-exchange, for inter-exchange two or three-point service to non-contiguous exchanges or four point or more inter-exchange services to all other exchanges.

- Channels that operate up to 30 Baud are identified as follows:

| ST | TYPE | NOTES |
| --- | --- | --- |
| IL | 1001A | Same/Inter-SA (Two/Multi-Point) |
| IN | 1012 | Class of Service: RMT2+ |
| MI | Metallic MT3 | Class of Service: XZM1+ |
| OH | 1102 | Class of Service: RMT2L |
| WI | 9001 | Class of Service: RMT1+ (Two Point Only) |
| WI | 9002 | Class of Service: RMT2+ (Two/Multi-Point) |

+ L = Intra-Exchange, S= Inter-Exchange

## Up to 45 Baud - Type 1002B Ohio

- Type 1002B Channels are available in Ohio.

- They provide transmission up to 45 baud for teletypewriter or data purposes.

- The Class of Service is TWPD+.

## Up to 55 Baud - Type 1002C Ohio

- Type 1002C channels are available in Ohio.

- These channels provide transmission up to 55 baud for teletypewriter or data purposes.

- The Class of Service is TWPE+.

Note:

+ L = Intra-Exchange, S = Inter-Exchange

Up to 75 Baud - (Telegraph Michigan, Type 1001 Ohio, Type 1002A Ohio, Type 1005 Ohio, Type 1050 Wisconsin)

- These channels may be used for such purposes as indicating readings of meters at distant locations, operating switches (which in turn perform some desired operation) or operating special signaling services of the customer.

- They are furnished on a twenty-four hour per day, seven-day per week basis.

- Channels that operate up to 75 Baud are identified as follows:

| ST | TYPE | NOTES |
| --- | --- | --- |
| MI | Telegraph | Class of Service = XZG1+ |
| OH | 1001 | Operate up to 15 Hertz per second: CS = RMT3+ |
| OH | 1002A | Operate up to 60 Hertz per second: CS = RMT4+ |
| OH | 1005 | Class of Service = TWPG+ |
| WI | 1050 | Class of Service = RMT7L |

+ L = Intra-Exchange, S = Inter-Exchange

Up to 150 Baud - (Type 1006 Illinois, Telegraph Michigan, Type 1006 Ohio, Type 1051 Wisconsin)

- These channels are suitable for transmission of data signals for teletypewriter, data, remote metering, supervisory control and miscellaneous signaling purposes at rates up to and including 150 baud.

- There are two terminations for two-point channels.

- The number of terminations for multi-point channels will be the total of the number of primary and central office terminations.

- All channels utilizing pairs from Service Transport Facility (STF) complements will require two-pair termination.

- Due to the method of providing these channel services, end-to-end D.C. continuity is not to be assumed.

- Channels that operate up to 150 Baud are identified as follows:

| ST | TYPE | NOTES |
| --- | --- | --- |
| IL | 1006 | Same SA/Inter-SA Data Transmission = DATO+ Teletype Transmission = TWPJ+ Remote Metering = RMTM+ |
| MI | Telegraph | Class of Service = XZG2+ |
| OH | 1006 | Class of Service = TWPJ+ |
| WI | 1051 | Class of Service = RMT7L |

Civil Air Defense Warning System Channels - Type 1002AA Ohio

- Type 1002AA Channels are used in Ohio for Civil Air Defense Warning Systems.

- These channels provide transmission-signaling frequencies up to 60 Hertz.

- They provide transmission between the control station and receiving stations of a customer’s Civil Air Defense Warning System.

## McCulloh Channel - Type 101 Michigan

- MT2 Channel is available in Michigan.

- These channels are metallic.

- They can be used for Burglar/Fire Alarm Service.

- The Class of Service is RMC2+

Note:

+ L = Intra-Exchange, S = Inter-Exchange

## Aliases

- Burglar Alarm Channels

- CS Channels

- DC Circuits

- Direct Connect

- Direct Wire

- Fire Alarm Channels

- Ground Return Loop

- McCulloh Channel

- Metallic Circuits

- Series Loop

- Signal Circuits

### Features

### Up to 30 Baud - Type 1102 Ohio

- Channels of similar grade furnished by the Telephone Company for the purposes of: indicating readings of meters at distant locations, operating switches which in turn perform some desired operation, or operating special signaling services of the customer; may be interconnected by the customer on his premises.

- When such interconnection is made, the Telephone Company’s responsibility is limited to providing and maintaining satisfactory transmission capabilities only between the terminal points of each individual channel that it furnishes.

Switching Arrangements for Teletypewriter Service

    - Switching arrangements are provided to permit the customer to connect two or more separate inter-exchange channels to form two-point or multi-point connections.

    - Such arrangements will be furnished where facility conditions permit at rates and charges based upon costs incurred.

Note: Each inter-exchange channel connected to a switching arrangement is priced as a separate service but remains as an integral part of the customer’s network.

### Up to 75 Baud - Types 1001 and 1002A Ohio

- Channels of similar grade furnished by the Telephone Company for the purposes of: indicating readings of meters at distant locations, operating switches which in turn perform some desired operation, or operating special signaling services of the customer; may be interconnected by the customer on his premises.

- When such interconnection is made, the Telephone Company’s responsibility is limited to providing and maintaining satisfactory transmission capabilities only between the terminal points of each individual channel that it furnishes.

Switching Arrangements for Teletypewriter Service

    - Switching arrangements are provided to permit the customer to connect two or more separate inter-exchange channels to form two-point or multi-point connections.

    - Such arrangements will be furnished where facility conditions permit at rates and charges based upon costs incurred.

Note: Each inter-exchange channel connected to a switching arrangement is priced as a separate service but remains as an integral part of the customer’s network.

# Availability

Type 1000 channels are provided only where facilities and operating conditions permit. Metallic facilities (wire pairs) are in diminishing supply, and can be expected to become less available as optical fiber is deployed and wire pair cables are removed.

## Restrictions/Limitations

- Series 1000 Service is furnished only where facilities and operating conditions permit.

- Type 1000 Channels are generally not suitable for the transmission of alternating current signals.

- These channels may not be connected to facilities furnished for exchange or toll service or with any other classification of telecommunications channel service.

- Temporary suspension of service is not allowed.

- No credit is allowed for interruptions to service of less than 30 minutes. Interruptions of 30 minutes or over are credited to the customer at the proportionate monthly charge in half hour multiples for each half hour or major fraction there of interruption.

- Connection of customer-provided station equipment to a series 1000 channel is subject to provisions of the tariff. Such equipment must operate at a line signaling speed not to exceed that specified for the channel service furnished.

- Local service area channels are furnished on a half-duplex basis only.

Up to 20 Baud – Type 1011 Indiana

- The maximum direct current voltage shall not exceed 270 volts conductor to conductor or 135 volts from either conductor to ground.

- Alternating current voltages shall be limited to a value of 62.5 milliampere (MA) (70.7 volts peak) conductor to conductor or either conductor to ground, and the shortest signaling element shall not be less than 33 millisecond (ms) (.033 seconds).

- The direct and alternating current voltage sources shall limit the maximum current, conductor to conductor or either conductor to ground, to a value not to exceed 50 MA (.05 ampere) for Type 1011 Channels.

Up to 30 Baud

Type 1001A Illinois

- Availability depends upon the results of a service inquiry that will be initiated at the time service is ordered.

- Type 1001A channels are not suitable for connection to a central office multiplexer.

- Customer equipment connected to 1001A channels equipped with digital carrier conditioning must operate within the following limits:

Voltage Range: ± 130 Volts Direct Current
Current Limit: 60 MA
Pulsing Rate: Up to 30 baud limited by the transmission characteristics of the channel.
Maximum Ground: 
Return Current Flow - limited to an average of .5 MA per day per circuit.

  - Use of the digital carrier conditioning option will extend the life of many type 1001A channels. This option, however, does not guarantee the continued availability of type 1001A channel service.

  - Type 1001A channels, equipped with the digital carrier conditioning option, is limited by transmission characteristics to one digital carrier facility per circuit.

  - For multi-point circuits, the only digital facility allowed is restricted to an inter-office facility.

  - Only one inter-office digital carrier facility per circuit may be provided, therefore, as inter-office metallic facilities are removed, the availability of multi-point channels comprised of more than two serving central offices and equipped with the digital carrier conditioning option will become increasingly limited.

Type 1012 Indiana

- The maximum direct current voltage shall not exceed 270 volts conductor to conductor or 135 volts from either conductor to ground.

- Alternating current voltages shall be limited to a value of 62.5 MA (70.7 volts peak) conductor to conductor or either conductor to ground, and the shortest signaling element shall not be less than 33 ms. (.033 seconds)

- The direct and alternating current voltage sources shall limit the maximum current, conductor to conductor or either conductor to ground, to a value not to exceed 20 MA (.02 ampere) for Type 1012 channels.

- Multi-point service is limited to a maximum of 26 points served from a total of no more than three different serving central offices and may be further limited by the transmission distance limitations of customer provided terminal equipment.

- Additional terminations furnished in the same building or on the same continuous property are not subject to the limitations specified in the preceding paragraph.

Type 1100 Ohio

- Local service area channels are furnished on a half-duplex basis only. However where the customer desires grounded channel facilities, the Telephone Company will undertake, if possible, to make such channels available by subdividing a metallic channel to create two grounded channels.

- Multi-point service is limited to a maximum of 26 points served from a total of no more than three different serving central offices and may be further limited by the transmission distance limitations of customer-provided terminal equipment.

- Where a station of an intra-state inter-exchange private line teletypewriter service is furnished:

  - by the Telephone Company, or

  - of an interstate service furnished by the Telephone Company, or

  - furnished under contract with a Bell Company

  - If located in an exchange area of a connecting company, the Telephone Company will furnish private line teletypewriter service between points within such exchange area if:

    - one of such points is in the building, or

    - on the continuous property

    - where the station of the inter-exchange service is located, and

    - satisfactory arrangements can be made with the connecting company involved.

  - When duplex service is furnished on a portion of an inter-exchange channel, switching arrangements are required at the junction points of the half-duplex and duplex sections and are charged based upon costs incurred.

  - These channels may be used by the customer, in accordance with the normal transmission characteristics of such channels, to transmit more than one signal in sequence or simultaneously except when used in connection with private land radiotelephone stations established for communication with mobile units.

  - The use of these channels is available on two-point services; such use on a multi-point service is available only where facility conditions permit.

  - All equipment and facilities at station locations, other than equipment, necessary or suitably terminating the channel facilities on the premises of or within the building occupied by the customer or authorized user, shall be provided by the customer.

  - Exception: Upon the customer’s request, the Telephone Company will furnish at station locations, signaling and selective equipment and facilities of the kind ordinarily furnished by the Telephone company for use with channels for remote metering, supervisory control or miscellaneous signaling purposes.

Up to 75 Baud – Types 1001 and 1102 Ohio

- Local service area channels are furnished on a half-duplex basis only. However where the customer desires grounded channel facilities, the Telephone Company will undertake, if possible, to make such channels available by subdividing a metallic channel to create two grounded channels.

- Where a station of an intra-state inter-exchange private line teletypewriter service is furnished:

  - by the Telephone Company, or

  - of an interstate service furnished by the Telephone Company, or

  - furnished under contract with a Bell Company

  - If located in an exchange area of a connecting company, the Telephone Company will furnish private line teletypewriter service between points within such exchange area if:

    - one of such points is in the building, or

    - on the continuous property

    - where the station of the inter-exchange service is located, and

    - satisfactory arrangements can be made with the connecting company involved.

  - When duplex service is furnished on a portion of an inter-exchange channel, switching arrangements are required at the junction points of the half-duplex and duplex sections and are charged based upon costs incurred.

  - These channels may be used by the customer, in accordance with the normal transmission characteristics of such channels, to transmit more than one signal in sequence or simultaneously except when used in connection with private land radiotelephone stations established for communication with mobile units.

  - The use of these channels is available on two-point services; such use on a multi-point service is available only where facility conditions permit.

  - All equipment and facilities at station locations, other than equipment, necessary or suitably terminating the channel facilities on the premises of or within the building occupied by the customer or authorized user, shall be provided by the customer.

  - Exception: Upon the customer’s request, the Telephone Company will furnish at station locations, signaling and selective equipment and facilities of the kind ordinarily furnished by the Telephone company for use with channels for remote metering, supervisory control or miscellaneous signaling purposes.

Up to 150 Baud – Type 1006 Ohio

- Station arrangements are required for stations or terminations on a Type 1006 channel when such stations or terminations are located on different premises (i.e. same building or on same or non-continuous property).

- Transmission between only two stations at the same time is normally provided, however, arrangements may be made to provide for transmission between more than two stations at the same time, for which special equipment and arrangements are furnished at rates or charges based upon costs incurred.

Civil Air Defense Warning System Channels – Type 1002AA Ohio

- These Civil Air Defense Warning System channels may not be directly or indirectly connected with any other facilities of the Telephone Company nor with other customer-provided equipment or facilities.

### Interactions

- The uses of 1000 series services are very dependent on the customer-provided devices used at each end of the channel.

### CPE Involvement

- The type and quality of the customer premises equipment determines the type of 1000 series channel used.

- Customer Premises Equipment (e.g. Alarm Panels)

# Pre-Ordering

SBC mechanized pre-ordering Operational Support System (OSS) is available to assist the CLECs on obtaining pre-ordering information. However, certain orders require a manual pre-ordering transaction before an LSR can be submitted successfully. The manual pre-ordering process is described in detail under the Preordering section of this handbook.

When performing a manual pre-ordering transaction, fill in the LSR request as completely as possible using EDI/WebLEX. When the needed manual pre-ordering information is filled out, save the LSR request. Print a copy of the request and fax it to SBC along with the Manual Preordering Information Cover Sheet. SBC will fax back the needed pre-ordering information so the CLEC can successfully submit a firm LSR.

# Ordering

End User Negotiations

New Connect

1.  Determine the type of Channel Service the end user is requesting.

2.  Determine if all circuit locations are within the same LATA.

  - If yes, go to next step

  - If no, the order must go through an InterExchange Carrier (IXC).

3.  Determine the type of Controlling Company

  - If AOC, go to the next step

  - If Independent Company, order should go through that Company

4.  Determine the circuit exchange locations and the number of locations per circuit.

5.  Obtain the following:

    - End user name

    - Address for each location

    - Contact names and telephone numbers for each location

    - Termination equipment, jack, etc.

    - Signaling, if needed

6.  If 1001A Channel, must have copper facilities before confirming order or due date (Illinois only).

7.  Negotiate due date.

Subsequent Order Activity

1.  Obtain the circuit and billing numbers.

2.  Determine the type of Controlling Company

  - If AOC, go the next step

  - If Independent Company, order should go through that Company

3.  Determine the nature of the end user’s request.

4.  If 1001A Channel, must have copper facilities before confirming order or due date

5.  Obtain contact names and telephone numbers for all locations if premises work is being requested.

6.  Negotiate due date and access if required.

7.  Remember, anytime work is being done on a leg of a two-point or multi-point circuit, the entire circuit will be out of service for the period of time it takes to complete the work.

Mileage

Mileage is measured using V & H coordinates. These coordinates provide the airline mileage used to bill for the circuit. Both InterExchange and Interoffice Channel mileage is calculated this way. Therefore, it is mandatory that the LSO (Local Serving Office) for all locations be provided.

| If the Circuit Locations Are: | And the NXXs are: | Then the mileage is Measured as Follows: |
| --- | --- | --- |
| Same Exchange | Served from same wire center (WC) | No mileage applies |
| Same Exchange | Served from different WCs | WC to WC (Interoffice mileage) |
| Different but Contiguous Exchanges | Served from different WCs | WC to WC (Interoffice mileage) |
| Different Exchanges-No rate center | Served from different WCs | WC to WC (Interoffice mileage) |
| Different, Non-contiguous exchanges | Served from the rate centers | Rate Center to Rate Center (InterExchange Mileage) |
| Different, Non-contiguous exchanges | Served from different WCs than are the Rate Centers | Rate Center to Rate Center between principal exchanges (Interexchange Mileage) AND Rate Center to Serving WC (Interoffice Mileage) |

Ordering Procedures for: Type 6005 – Illinois, Type 6011 & 6020 – Indiana, Type 6003 – Ohio, Type 6060 – Wisconsin

These channels are most commonly used to provide Music-On-Hold for Centrex service.

- The end user must supply the music source, which usually is CPE, that’s located at the end user’s premise. Therefore, it is necessary to know the type of CPE being connected to the circuit.

- SBC provides the interface from the Centrex serving switch to the end user’s premises.

- Note: These ordering procedures are in addition to the standard procedures. See End User Negotiations above.

Ordering Procedures for: Type 9001 and 9002 Wisconsin

- Determine if two-point or multi-point service is needed.

- If two-point, then either 9001 or 9002 can be ordered. See 'Up to 30 Baud' information.

- Will be used in McCulloh loop type application.

- Determine if all legs of the circuit are in the same wire center.

- Yes, same Wire Center and requires Line Power Option, then type 9001 is generally used.

- No, different Wire Center and requires Line Power Option, then type 9002 is generally used.

- Note: These ordering procedures are in addition to the standard procedures. See End User Negotiations above.

## Circuit IDs (CLCI) & Secondary Classes of Service

Illinois

| CLCI Code (Service Code) | Class of Service Intra SA | Class of Service Inter SA | Baud Rate | Description |
| --- | --- | --- | --- | --- |
| Type 1001A |
| BA++ | RMT3L | RMT3S | 30 | Protective Alarm (DC interface at end user premise) |
| CS++ | RMT3L | RMT3S | 30 | Channel Service |
| Type 1006 |
| CS++ | DATOL | DATOS | 150 | Channel Service-Data Transmission |
| TC++ | RMTML | RMTMS | 150 | Control/Remote Metering – Telegraph Guide |
| TT++ | TWPJL | TWPJS | 150 | Teletypewriter Channel |
| Type 6005 |
| MT++ | POMML | POMMS | NA | Wired Music |

Indiana

| CLCI Code (service code) | Class of Service IntraExchange | Class of Service InterExchange | Baud Rate | Description |
| --- | --- | --- | --- | --- |
| Type 1011 |
| BA++ | RMT1L | RMT1S | 20 | Protective Alarm (DC interface at end user premises) |
| CS++ | RMT1L | RMT1S | 20 | Channel Services |
| PW++ | RMT1L | RMT1S | 20 | Protective Relaying – Signal Grade |
| SG++ | RMT1L | RMT1S | 20 | Control/Remote Metering – Signal Grade |
| Type 1012 |
| BA++ | RMT2L | RMT2S | 30 | Protective Alarm (DC interface at end user premises) |
| CS++ | RMT2L | RMT2S | 30 | Channel Service |
| PW++ | RMT2L | RMT2S | 30 | Protective Alarm (DC interface at end user premises) |
| SG++ | RMT2L | RMT2S | 30 | Control/Remote Metering – Signal Grade |
| Type 6011 – Intra and InterExchange |
| MT++ | POMAL | POMAS | NA | Wired Music |
| Type 6020 – Same Central Office |
| MT++ | POMEL | NA | NA | Wired Music |

Michigan

| CLCI Code (Service Code) | Class of Service | Baud Rate | Description |
| --- | --- | --- | --- |
| Metallic MT3 |
| UY++ | XZM1+ | 30 | Two/Multi Point |
| Telegraph |
| NW++ | XZG1+ | 75 |  |
| NY++ | XZG2+ | 150 |  |
| Type 102 |
| UC++ | RMC2+ | NA | McCulloh Channel |

Note: + fifth(5 th) Character – Secondary Class of Service:

L = IntraExchange – Intra Wire Center

1 = IntraExchange – Inter Wire Center

S – InterExchange – Inter Wire Center

Ohio

| CLCI Code (Service Code) | Class of Service IntraExchange | Class of Service InterExchange | Baud Rate | Description |
| --- | --- | --- | --- | --- |
| Type 1001 |
| BA++ | RMT3L | RMT3S | 75 - up to 15 hertz per second | Protective Alarm (DC interface at end user premises) |
| BL++ | RMT3L | RMT3S | 75 – up to 15 hertz per second | Bells and Lights |
| CS++ | RMT3L | RMT3S | 75 – up to 15 hertz per second | Channel Service |
| Type 1002 |
| BA++ | RMT2L | NA | 30 | Protective Alarm (DC Interface at end user premises) |
| BL++ | RMT2L | NA | 30 | Bells and Lights |
| CS++ | RMT2L | NA | 30 | Channel Service |
| Type 1002A |
| BA++ | RMT4L | RMT4S | 75 – up to 60 hertz per second | Protective Alarm (DC interface at end user premises) |
| BL++ | RMT4L | RMT4S | 75 – up to 60 hertz per second | Bells and Lights |
| CS++ | RMT4L | RMTRS | 75 – up to 60 hertz per second | Channel Service |
| Type 1002B |
| TC++ | TWPDL | TWPDS | 45 | Control/Remote Metering – Telegraph Grade |
| TT++ | TWPDL | TWPDS | 45 | Teletypewriter channel |
| Type 1002C |
| TC++ | TWPEL | TWPES | 55 | Control/Remote Metering-Telegraph Grade |
| TT++ | TWPEL | TWPES | 55 | Teletypewriter channel |
| Type 1005 |
| TC++ | TWPGL | TWPGS | 75 | Control/Remote Metering – Telegraph Grade |
| TT++ | TWPGL | TWGS | 75 | Teletypewriter channel |
| Type 1006 |
| TC++ | TWPJL | TWPJS | 150 | Control/Remote Metering – Telegraph Grade |
| TT++ | TWPJL | TWPJS | 150 | Teletypewriter channel |
| Type 3001 |
| BA++ | RMTVL | RMTVS | NA | Protective Alarm (DC Interface at end user premises) |
| BL++ | RMTVL | RMTVS | NA | Bells and Lights |
| CS++ | RMTVL | RMTVS | NA | Channel service |
| Type 6000 |
| MT++ | POMLL | POMLS | NA | Wired Music |

Wisconsin

| CLCI Code (Service Code) | Class of Service IntraExchange | Class of Service InterExchange | Baud Rate | Description |
| --- | --- | --- | --- | --- |
| Type 1050 |
| BA++ | RMT7L | NA | 75 | Protective Alarm (DC Interface at end user premises) |
| CS++ | RMT7L | NA | 75 | Channel Service |
| TC++ | TWP7L | NA | 75 | Control/Remote Metering – Telegraph Grade |
| TT++ | TWP7L | NA | 75 | Teletypewriter channel |
| Type 1051 |
| CS++ | DAT8L | NA | 150 | Channel Service – Data Transmission |
| TC++ | RMT8L | NA | 150 | Control/Remote Metering – Telegraph Grade |
| TT++ | TWP7L | NA | 150 | Teletypewriter Channel |
| Type 6060 |
| MT++ | POMAL | POMAS | NA | Wired Music |
| Type 9001 |
| BA++ | RMT1L | RMT1S | 30 | Protective Alarm (DC Interface at end user premises – 2 point only) |
| CS++ | RMT1L | RMT1S | 30 | Channel Service – 2 point only |
| Type 9002 |
| BA++ | RMT2L | RMT2S | 30 | Protective Alarm (DC Interface at end user premises – 2 point only) |
| CS++ | RMT2L | RMT2S | 30 | Channel Service – 2 or multi point |

## Circuit Function Table

| Bellcore Code | Code Meaning | Description |
| --- | --- | --- |
| BA | Protective Alarm | Protective alarm (DC interface at customer premises) Provides a channel for an alarm system. The alarm points may be arranged in series or parallel configurations. |
| BL | Bell and Lights | A signal grade circuit between a Civil Defense Control Center bell and light receiving siren and warning system control equipment installed in a telephone company building. |
| BS | Siren Control | Provides a channel for the control of a siren or warning system |
| CS | Channel Service | Provides a channel, which has the capacity of transmitting up to 30 baud's. The channel does not have access to the switched message network. |
| FR | Fire Dispatch | Provides a group alerting system that operates warning devices at various locations from a central point. This service is used by fire or ambulance companies to alert their members. |
| MT | Wired Music | Provides for the transmission of either speech or music between two or more locations. |
| PW | Protective Relaying | A signal grade circuit between two or three electric power utility locations. It is used to transmit control signals for the operation of circuit breakers, which protect sections of high voltage power lines and associated equipment during a fault condition. This circuit, commonly known as a 'pilot wire,' requires a metallic pair to which a DC current is applied and monitored for continuity test purposes. Pilot wire circuits are limited to about ten miles in length by the allowable resistance and capacitance. |
| RT | Radio Land Line | A channel used to provide access to non-broadcast radio transceivers. |
| SG | Control/Remote Metering Signal Grade | A signal grade circuit between a central point and a remote location(s). It is used to selectively monitor or control quantities or operations at the remote location(s). |
| TC | Control/Remote Metering | A telegraph grade circuit between a central point and a remote location(s). It is used to selectively monitor or control quantities or operations at the remote location(s). |
| TT | Teletypewriter Channel | A telegraph grade circuit between two or more customer and/or central office locations. |

CLCI Service Code Key for 3rd and 4th Characters

Third (3rd) Character

- A = Alternate Voice and Data

- D = Data

- N = Non-Data

- S = Simultaneous Data & Data and/or Data & Voice

Fourth (4th) Character

- T = Circuit is Telco Customer and all facilities and equipment are Telco provided.

- C = Circuit is Telco Customer to Telco Customer. Part of facilities and/or equipment is customer provided.

- A = Circuit is Telco Customer to Telco Customer. All facilities are Telco provided. All Electrically Connected Equipment is customer provided.

- S = Terminates at an InterExchange Carrier’s Point of Termination

Note: The most common code combination is ++NC.

## Due Dates

Refer to Resale Due Date for standard due date intervals.

## USOCs

Illinois

SERIES 1001A (Illinois)

| SAME SA CHANNELS - 2 WIRE |
| --- |
| TYPE | USOC |
| LOCAL CHANNELS 2 POINT, EACH POINT - STF NOT APPLICABLE - STF APPLICABLE - C.O. TERMINATION | WWAA+ OWAA+ CTG |
| MULTI-POINT, EACH POINT - STF NOT APPLICABLE - STF APPLICABLE | WWZA+ OWZA+ |

| INTER-SA CHANNELS |
| --- |
| TYPE | USOC |
| MILEAGE |  |
| 2 POINT - SHORT HAUL METALLIC - 1st 1/4 MILE - EACH ADDITIONAL 1/4 MILE | JZNDJ JZNDC |
| DIGITAL CARRIER CONDITIONING - 1st 1/4 MILE - EACH ADDITIONAL 1/4 MILE | JZNFJ JZNFC |
| LONG HAUL METALLIC - 1st mile - EACH ADDITIONAL MILE | JZNDX JZNDB |
| DIGITAL CARRIER CONDITIONING - 1st MILE - EACH ADDITIONAL MILE | JZNFX JZNFB |
| LOCAL CHANNELS (1 PER POINT) - STF NOT APPLICABLE - STF APPLICABLE | WWYA+ OMYA+ |
| MULTI-POINT |  |
| SHORT HAUL METALLIC - 1st 1/4 MILE - EACH ADDITIONAL 1/4 MILE | JZNCJ JZNCC |
| DIGITAL CARRIER CONDITIONING - 1ST MILE - EACH ADDITIONAL MILE | JZNKJ JZNKC |
| LONG HAUL METALLIC - 1st MILE - EACH ADDITIONAL MILE | JZNCX JZNCB |
| DIGITAL CARRIER CONDITIONING - 1st MILE - EACH ADDITIONAL MILE | JZNKX JZNKB |
| LOCAL CHANNELS (1 PER POINT) - STF NOT APPLICABLE - STF APPLICABLE | WWVA+ OWVA+ |

| TYPE 1001A | USOC |
| --- | --- |
| DIGITAL CARRIER CONDITIONING (Per Channel) | CQ2 |
| DUAL SERVICE ENTRANCE (At least 10 feet from primary Aerial Entrance) (Per Channel) | 1L33A |
| JOINT USER ARRANGEMENT | JNP |

+ Access Area A = A Access Area B = B Access Area C = C

SERIES 1006 (Illinois)

| SAME SA CHANNELS - 2 WIRE |
| --- |
| TYPE | USOC |
| LOCAL CHANNELS 2 POINT, EACH POINT - STF NOT APPLICABLE - STF APPLICABLE - C.O. TERMINATION | WWAC+ OWBC+ WUE1+ |
| MULTI-POINT - STF NOT APPLICABLE - STF APPLICABLE | WWZC+ OWZC+ |
| C.O. MUX TERMINATION | ZZZPE |

| INTER-SA CHANNELS |
| --- |
| TYPE | USOC |
| MILEAGE 2-POINT |
| SHORT HAUL BETWEEN SAs - 1st 1/4 MILE - EACH ADDITIONAL 1/3 MILE | JZNGJ JZNGC |
| LONG HAUL BETWEEN SAs - 1st MILE - EACH ADDITIONAL MILE | JZNJX JZNGB |
| LOCAL CHANNELS (1 PER POINT) |  |
| - STF NOT APPLICABLE | WWYC+ |
| - STF APPLICABLE | OMYC+ |
| - C.O. TERMINATION | WUG1+ |
| C.O. MUX TERMINATION | ZZZPE |
| MILEAGE MULTI-POINT |
| SHORT HAUL BETWEEN SAs - 1st 1/4 MILE - EACH ADDITIONAL 1/3 MILE | JZNLJ JZNLC |
| LONG HAUL BETWEEN SAs - 1st MILE - EACH ADDITIONAL MILE | JZNLX JZNLB |
| LOCAL CHANNELS (1 PER POINT) - STF NOT APPLICABLE - STF APPLICABLE | WWVC+ OMVC+ |
| C.O. MUX TERMINATION | ZZZPE |

+ Access Area A = A Access Area B = B Access Area C = C

SERIES 6005 – Illinois

| INTRA SA CHANNELS |
| --- |
| TYPE | USOC |
| 2 POINT LOCAL CHANNELS (1 PER POINT) - STF NOT APPLICABLE - STF APPLICABLE | WXQA+ OXQA+ |
| INTER SA CHANNELS |
| 2 POINT LOCAL CHANNELS & MILEAGE - STF NOT APPLICABLE - STF APPLICABLE | WXVA+ TBD |
| SHORT HAUL MILEAGE - 1st 1/4 MILE - EACH ADDITIONAL 1/4 MILE | JZNNJ NZNNC |
| LONG HAUL MILEAGE - 1st MILE - EACH ADDITIONAL MILE | JZNNX JZNNB |
| MILEAGE MULTI-POINT |
| SHORT HAUL - 1st 1/4 MILE - EACH ADDITIONAL ¼ MILE | JZNUA JZNUC |
| LONG HAUL - 1st MILE - EACH ADDITIONAL MILE | JZNUX JZNUB |
| MISCELLANEOUS USOCs |
| Primary Distributing Center | 67R |
| Additional Bridging Equipment | 67N |

Indiana

SERIES 1011 (Indiana) (BA, CS, PW, SG)

| INTRA-EXCHANGE (2 OR 3 Point Circuits) CS: RMT1L |
| --- |
| TYPE USOC |
| LOCAL DISTRIBUTION CHANNEL - 1 AT EACH END USER PREMISE | 2UC |
| ADDITIONAL TERM AT SAME LOCATION - PER ADDITIONAL POINT | 2UA |
| INTER-OFFICE CHANNEL MILEAGE - PER MILE OR FRACTION | 1L31S |
| INTER-OFFICE CHANNEL TERMINATION - 1 AT EACH END OF INTER-OFFICE CHANNEL | 24E |
| CONTINUOUS PROPERTY CHANNEL (Between Buildings) - 10,000 FEET OR LESS - OVER 10,000 FEET | 1L311 1L312 |

| CONTIGUOUS EXCHANGES INTER-EXCHANGE (2 or 3 Point Circuits) CS: RMT1S |
| --- |
| TYPE | USOC |
| INTER-EXCHANGE MILEAGE (per mile) - 1 to 25 MILES - 26 or MORE MILES | 1L314 1L314 |
| INTER-EXCHANGE CHANNEL TERMINATION - 1 AT EACH END OF EXCHANGE CHANNEL - 1 to 25 MILES - 26 or MORE MILES | O1N O3N |
| LOCAL DISTRIBUTION CHANNEL - 1 AT EACH CUSTOMER PREMISES | 2UC |
| ADDITIONAL TERM AT SAME LOCATION - PER ADDITIONAL POINT | 2UA |
| CONTINUOUS PROPERTY CHANNEL (Between Buildings) - 10,000 FEET OR LESS - OVER 10,000 FEET | 1L311 1L312 |

SERIES 1012 (Indiana) (BA, CS, PW, SG)

| INTRA-EXCHANGE 4 OR MORE POINTS CS: RMT2L |
| --- |
| TYPE | USOC |
| LOCAL DISTRIBUTION CHANNEL - 1 AT EACH CUSTOMER PREMISES | 2UC |
| INTER-OFFICE CHANNEL MILEAGE - PER MILE OR FRACTION | 1L31S |
| INTEROFFICE CHANNEL MILEAGE - 1 AT EACH END OF IO CHANNEL | 24E |
| ADDITIONAL TERM AT SAME LOCATION - PER ADDITIONAL POINT | 2UA |
| ON-PREM BUILDING CHANNEL TERMINATION - 1 AT EACH POINT | 267AR |
| CONTINUOUS PROPERTY CHANNEL - BETWEEN BUILDINGS - 10,000 FEET OR LESS - OVER 10,000 FEET | 1L311 1L312 |

| INTER-EXCHANGE 2 OR MORE POINTS: NON-CONTIGUOUS 4 OR MORE POINTS - ALL EXCHANGES CS: RMT2S |
| --- |
| TYPE | USOC |
| INTER-EXCHANGE MILEAGE (per Mile) - 1 to 25 MILES - 26 or MORE MILES | 1L314 1L314 |
| INTER-EXCHANGE CHANNEL TERMINATION 1 AT EACH END OF IX CHANNEL - 1 to 25 MILES - 26 or MORE MILES | O1N O3N |
| LOCAL CHANNEL - 1 AT EACH CUSTOMER PREMISES | 2UC |
| CUSTOMERS NOT IN RATE CENTER - ADD INTER-OFFICE CHANNEL MILEAGE (PER MILE) | 1L31P |
| INTEROFFICE CHANNEL MILEAGE TERMINATION - 1 AT EACH END OF IO CHANNEL | 24E |
| ADDITIONAL TERM AT SAME LOCATION - PER ADDITIONAL POINT | 2UA |
| CONTINUOUS PROPERTY CHANNEL (BETWEEN BUILDINGS) - 10,000 FEET OR LESS - OVER 10,000 FEET | 1L311 1L312 |

SERIES 6011 and 6020 (Indiana) (MT)

| INTRA-EXCHANGE CS: POMAL & POMAS |
| --- |
| TYPE | USOC |
| LOCAL DISTRIBUTION CHANNEL | 6KA |
| INTEROFFICE CHANNEL MILEAGE | 1LGAS |
| INTEROFFICE CHANNEL MILEAGE | 6LD |
| BUILDING CHANNEL TERMINATION | 6KB |
| INTEREXCHANGE MILEAGE 1 – 40 MILES 41 + MILES | 1L6A4 1L6A4 |
| INTEREXCHANGE MILEAGE TERMINATION – 1 AT EACH END OF CIRCUIT 1 – 40 MILES 41 + MILES | U1N U3N |
| CONTINUOUS PROPERTY CHANNEL 1 - 10,000 FEET OVER 10,000 FEET | 1LGA1 1LGA2 |

| SAME CENTRAL OFFICE CS: POMEL |
| --- |
| TYPE | USOC |
| LOCAL DISTRIBUTION CHANNEL | 6LC |
| BUILDING CHANNEL TERMINATION | 6KC |
| CONTINUOUS PROPERTY CHANNEL 1 - 10,000 FEET OVER 10,000 FEET | 1LGA1 1LGA2 |
| MULTI-POINT SERVICE | 6SA |

Michigan

METALLIC SERVICE (Michigan)

| TYPE | USOC |
| --- | --- |
| CLASS OF SERVICE XZM1+ |  |
| LOCAL DISTRIBUTION CHANNEL | T6ECS |
| CHANNEL MILEAGE (Per Mile) | 1L5XX |
| CHANNEL TERMINATION | CM6 |
| 3 PREMISES BRIDGING | BCNM3 |
| SERIES BRIDGING | BCNMS |
| CLASS OF SERVICE XZM1L |
| ROUTED DIRECT CHANNEL | CPD |

TELEGRAPH GRADE (75 BAUD) Michigan

| TYPE | USOC |
| --- | --- |
| CLASS OF SERVICE XZG1+ |  |
| TWO-WIRE LOCAL CHANNEL (Half Duplex) | T6E2X |
| FOUR-WIRE LOCAL CHANNEL (Full Duplex) | T6E4X |
| INTER-WIRE CENTER MILEAGE (Per Mile) | 1L5XX |
| CHANNEL TERMINATIONS | CM6 |
| 2-WIRE BRIDGING | BCNT2 |
| 4-WIRE BRIDGING | BCNT4 |

150 BAUD (Michigan)

| TYPE | USOC |
| --- | --- |
| CLASS OF SERVICE XZG2+ |  |
| TWO-WIRE LOCAL CHANNEL (Half Duplex) | T6E2X |
| FOUR-WIRE LOCAL CHANNEL (Full Duplex) EIA Interface | T6E4X |
| INTER-WIRE CENTER MILEAGE (Per Mile) | 1L5XX |
| CHANNEL TERMINATIONS | CM6 |
| 2-WIRE BRIDGING | BCNT2 |
| 4-WIRE BRIDGING | BCNT4 |

TYPE 102 (Michigan)

| TYPE | USOC |
| --- | --- |
| CLASS OF SERVICE RMC2+ |  |
| BURGLAR/FIRE ALARM, McCULLOH (Intra-Exch) |  |
| INTER-EXCHANGE CHANNEL | 1LDCX |
| MULTI-POINT BRIDGING | MSK |
| ROUTED DIRECT CHANNEL | CPD |
| RURAL ZONE | 1LS1A |
| LOCALITY RATE AREA | 1LS1F |
| INTER-WIRE CENTER MILEAGE (Per Mile) | 1LWBX |
| CHANNEL TERMINATIONS | CHV |
| LOCAL CHANNEL | 246 |

+ L = Intra-exchange - Intra Wire Center

1 = Intra-exchange - Inter Wire Center

S = Inter-exchange

Ohio

SERIES 1001

| INTRA/INTER-EXCHANGE |
| --- |
| CLASS OF SERVICE RMT3+ |  |
| TYPE | USOC |
|  | 2-WIRE | 4-WIRE |
| SAME C.O. - LOCAL CHANNEL - SAF (1 Per Channel) | 1L3AJ OPMAA | --- --- |
| DIFFERENT C.O. - LOCAL CHANNEL - SAF (1 Per Channel) | 1L3AJ OPMAB | 1L3CJ OPMAB |
| DIFFERENT EXCHANGE - LOCAL CHANNEL - SAF (1 Per Channel) | 1L3AJ OPMAC | 1L3CJ OPMAF |
| Same Continuous Property* | UA7NA | UA7NA |
| Interoffice Channels, per mile | IL3AS | IL3CS |
| Interexchange Channels, per mile | IL3A4 | IL3C4 |
| Service Terminals | P3N | P3N |

SERIES 1002A (Ohio)

| INTRA/INTER-EXCHANGE |
| --- |
| CLASS OF SERVICE RMT4+ |  |
| TYPE | USOC |
|  | 2-WIRE | 4-WIRE |
| SAME C.O. - LOCAL CHANNEL - SAF | 1L3AJ OPMAD | --- --- |
| DIFFERENT C.O. - LOCAL CHANNEL - SAF | 1L3AJ OPMAE | --- --- |
| DIFFERENT EXCHANGE - LOCAL CHANNEL - SAF | 1L3AJ OPMAF | 1L3CJ OPMAF |
| Interoffice Channels, per mile | 1L3AS | 1L3CS |
| Interexchange Channels, per mile | 1L3A4 | 1L3C4 |
| Same Continuous Property * | UA7NA | UA7NA |
| Service Terminal | P3N | P3N |

SERIES 1002B (Ohio)

| INTRA/INTER-EXCHANGE |
| --- |
| CLASS OF SERVICE TWPD+ |  |
|  | USOC |
| TYPE | 2-WIRE | 4-WIRE |
| SAME C.O. - LOCAL CHANNEL - SAF (1 Per Channel) | 1LNHB OPMAG | 1LNFB OPMAG |
| DIFFERENT C.O. - LOCAL CHANNEL - SAF (1 Per Channel) | 1LNHB OPMAH | 1LNFB OPMAH |
| DIFFERENT EXCHANGE - LOCAL CHANNEL - SAF (1 Per Channel) | 1LNHB OPMAJ | 1LNFB OPMAJ |
| INTER-OFFICE CHANNELS - PER MILE | 1LNHC | 1LNFC |
| INTER-EXCHANGE CHANNELS - PER MILE | 1LNHD | 1LNFD |
| Service Terminal | P3N | P3N |
| Same Continuous Property* | UA7NA | UA7NA |

SERIES 1002C (Ohio)

| INTRA/INTER-EXCHANGE |
| --- |
| CLASS OF SERVICE TWPE+ |  |
|  | USOC |
| TYPE | 2-WIRE | 4-WIRE |
| SAME C.O. - LOCAL CHANNEL - SAF (1 Per Channel) | 1LNHB OPMAK | 1LNFB OPMAK |
| DIFFERENT C.O. - LOCAL CHANNEL - SAF (1 Per Channel) | 1LNHB OPMAL | 1LNFB OPMAL |
| DIFFERENT EXCHANGE - LOCAL CHANNEL - SAF (1 Per Channel) | 1LNHB OPMAM | 1LNFB OPMAM |
| Same Continuous Property* | UA7NA | UA7NA |
| Interoffice Channels, per mile | 1LNHC | 1LNFC |
| Interexchange Channels, per mile | 1LNHD | 1LNFD |
| Service Terminal | P3N | P3N |

SERIES 1005 (Ohio)

| INTRA/INTER-EXCHANGE |
| --- |
| CLASS OF SERVICE TWPG+ |  |
|  | USOC |
| TYPE | 2-WIRE | 4-WIRE |
| SAME C.O. - LOCAL CHANNEL - SAF | 1LNHB OPMAN | 1LNFB OPMAN |
| DIFFERENT C.O. - LOCAL CHANNEL - SAF | 1LNHB OPMAO | 1LNFB OPMAO |
| DIFFERENT EXCHANGE - LOCAL CHANNEL - SAF | 1LNHB OPMAP | 1LNFB OPMAP |
| INTER-OFFICE CHANNELS - PER MILE | 1LNHC | 1LNFC |
| INTER-EXCHANGE CHANNELS - PER MILE | 1LNHD | 1LNFD |
| Service Terminal | P3N | P3N |
| Same Continuous Property* | UA7NA | UA7NA |

SERIES 1006 (Ohio)

| INTRA/INTER-EXCHANGE |
| --- |
| CLASS OF SERVICE TWPJ+ |  |
|  | USOC |
| TYPE | 2-WIRE | 4-WIRE |
| SAME C.O. - LOCAL CHANNEL - SAF | 1LNHB OPMAQ | 1LNFB OPMAQ |
| DIFFERENT C.O. - LOCAL CHANNEL - SAF | 1LNHB OPMAR | 1LNFB OPMAR |
| DIFFERENT EXCHANGE - LOCAL CHANNEL - SAF | 1LNHB OPMAS | 1LNFB OPMAS |
| INTER-OFFICE CHANNELS - PER MILE | 1LNHC | 1LNFC |
| INTER-EXCHANGE CHANNELS - PER MILE | 1LNHD | 1LNFD |
| Service Terminal | P3N | P3N |
| Same Continuous Property* | UA7NA | UA7NA |

SERIES 1102 (Ohio)

| INTRA/INTER-EXCHANGE 2 - WIRE |
| --- |
| CLASS OF SERVICE RMT2L |  |
| TYPE | USOC |
| SAME C.O. - LOCAL CHANNEL - SAF (1 PER CHANNEL) | 1L3QJ OPMAT |
| DIFFERENT C.O. - LOCAL CHANNEL - SAF (1 PER CHANNEL) | 1L3QJ OPMAU |
| Interoffice Channels, per mile | 1L3QS |
| Same Continuous Property* | UA7NA |

*Deregulated Inside Wire

ALTERNATE USE (Ohio)

| TYPE | USOC |
| --- | --- |
| Teletype up to 75 Baud, Remote Metering, Supervisory Control & Miscellaneous Signaling |  |
| 1002B (+1001/1002A) per terminal | TTW |
| 1002C (+1001/1002A) per terminal | TYW |
| 1005 (+1001/1002A) per terminal | TYW |
| Teletype & Data up to 75 Baud On 2 point half-duplex only |  |
| 1002B per station equipped | TTV |
| 1002C per station equipped | TYV |
| 1005 per station equipped | TYV |

+ L = INTRA-EXCHANGE
S = INTER-EXCHANGE
SAF - 1 PER CHANNEL

SERIES 3001 (Ohio)

| INTRA/INTER-EXCHANGE |
| --- |
| CLASS OF SERVICE RMTV+ |  |
|  | USOC |
| TYPE | 2-WIRE | 4-WIRE |
| SAME C.O. - LOCAL CHANNEL - SAF | 1L3AJ OPMBW | 1LCJ OPMBW |
| DIFFERENT C.O. - LOCAL CHANNEL - SAF | 1L3AJ OPMBX | 1L3CJ OPMBX |
| DIFFERENT EXCHANGE - LOCAL CHANNEL - SAF | 1L3AJ OPMBY | 1L3CJ OPMBY |
| Interoffice Channel Mileage, per mile | 1L3AS | 1L3C4 |
| Interexchange Channel Mileage, per mile | 1L3A4 | 1L3C4 |
| Service Terminal | P3N | P3N |
| Same Continuous Property* | UA7NA | UA7NA |

SERIES 6003

| TYPE | USOC |
| --- | --- |
| Station Connection, per connection | 5FT |
| InterExchange Channel (IXC) |
| Per Mile | 1LGN4 |
| Station Connection | 5FT |
| Local Service Area Channels |
| Non-Continuous Property – 2 point Channel non-equalized First 1 /4 mile or fraction thereof Each additional 1/ 4 mile or fraction thereof | 1LNH4 |
| Non-Continuous Property – 2 point channel – Equalized with appropriate frequency range of: 100 to 5000 Hertz First 1 /4 mile or fraction thereof Each additional 1/ 4 mile or fraction thereof | 1LG3Y 1LUGR |
| Non-Continuous Property – Multi Point Channel (per 1/ 4 mile or fraction thereof) Non-Equalized Equalized 100 to 5000 50 to 8000 50 to 15,000 | 1LGUY 1LG5R 1LG8R 1LG1R |
| Distribution Center 50 to 8000 Hertz First 1/ 4 mile Each additional mile 50 to 15,000 First 1/ 4 mile Each additional mile | 67R 1LG4Y 1LNH7 1LG7Y 1LNH8 |

Wisconsin

SERIES 1050 (Wisconsin)

| CLASS OF SERVICE RMT7L, TWP7L, DAT8L |  |
| --- | --- |
| TYPE | USOC |
| WIRE CENTER CHANNEL (WCC) - INITIAL 1/4 MILE - SUBSEQUENT 1/4 MILE | 1L9X6 1L9X6 |
| LOCAL DISTRIBUTION CHANNEL - INITIAL 1/4 MILE - SUBSEQUENT 1/4 MILE - Provisioning Only 2-Wire/Same CO/2 Point/CKL 2 | 1LDHJ 1LDHJ AS32X |
| MULTI-POINT - PER CHANNEL | MPY1X |

SERIES 1051 (Wisconsin)

| INTER-EXCHANGE ONLY 2 POINT OR MULTI-POINT |
| --- |
| CLASS OF SERVICE RMT7L, TWP7L, DAT8L |  |
| TYPE | USOC |
| WIRE CENTER CHANNEL (WCC) - INITIAL 1/4 MILE - SUBSEQUENT 1/4 MILE | 1L9X7 1L9X7 |
| LOCAL DISTRIBUTION CHANNEL - INITIAL 1/4 MILE - SUBSEQUENT 1/4 MILE - Provisioning Only 2-Wire/Same CO/2 Point/CKL2 | 1LDFJ 1LDFJ AS32X |
| MULTI-POINT - PER CHANNEL | MPY2X |

SERIES 6060

| INTRA or INTER-EXCHANGE 2 POINT |
| --- |
| CLASS OF SERVICE POMAL, POMAS |  |
| TYPE | USOC |
| LOCAL DISTRIBUTION CHANNEL - INITIAL 1/4 MILE - SUBSEQUENT 1/4 MILE | 1LDUJ 1LDUJ |
| Inter-Wire Center Channel Mileage - Initial Mile - Subsequent Mile(s) | 1LNUX 1LNUX |

SERIES 9001 (Wisconsin)

| INTRA OR INTER-EXCHANGE 2 POINT ONLY |
| --- |
| CLASS OF SERVICE RMT1+ |  |
| TYPE | USOC |
| SAME WIRE CENTER (WCC) - INITIAL 1/4 MILE - SUBSEQUENT 1/4 MILE | 1L9X6 1L9X6 |
| DIFFERENT WIRE CENTER (WCC) - INITIAL 1/4 MILE - SUBSEQUENT 1/4 MILE | 1LNDX 1LNDX |
| LOCAL DISTRIBUTION CHANNEL (PER CHANNEL) - INITIAL 1/4 MILE - SUBSEQUENT 1/4 MILE) - Provisioning Only 2-Wire, 2-Point, Same CO, CKL2 | 1LDDJ 1LDDJ AS32X |

SERIES 9002 (Wisconsin)

| INTRA OR INTER-EXCHANGE 2 POINT OR MULTI-POINT |
| --- |
| CLASS OF SERVICE RMT2+ |  |
| TYPE | USOC |
| SAME WIRE CENTER (WCC) - INITIAL 1/4 MILE - SUBSEQUENT 1/4 MILE | 1L9X7 1L9X7 |
| DIFFERENT WIRE CENTER (WCC) - INITIAL 1/4 MILE - SUBSEQUENT 1/4 MILE | 1LNDX 1LNDX |
| LOCAL DISTRIBUTION CHANNEL (PER CHANNEL) - INITIAL 1/4 MILE - SUBSEQUENT 1/4 MILE) - Provisioning Only 2-Wire, 2-Point, Same CO, CKL2 | 1LDDJ 1LDDJ AS32X |

LINE POWER (Wisconsin)

| SERIES 9001 OR 9002 2 POINT ONLY |
| --- |
| TYPE | USOC |
| SAME WIRE CENTER - 9001 DIFFERENT WIRE CENTER - 9002 | PWG1X PWG2X |

+ L = INTRA-EXCHANGE
S = INTER-EXCHANGE

Note: If installed at same time as 9001 or 9002 Channel, an additional Design Order Charge does not apply.

FIDs

| FID | Description |
| --- | --- |
| CKL | Circuit Location Example: CKL 1-1234 Any AV, My Town, AA Order Placement: Not required |
| CLS | Common Language Circuit Identification – Serial Number Format Example: .AAAA.######..AA Order placement: ECCKT Field |
| FSO | Foreign Serving Office – Identifies that service is provided from a Central Office that does not normally serve the street address. Example: NPA NXX Order Placement: FSO Field on Resale Private Line Form |
| LSO | Local Serving Office Example: NPA NXX Order Placement: LSO Field on Resale Private Line Form |
| NC | Network Channel – Required on Michigan orders only Example: .UGPA.######..MB/NC UG- Order Placement: NC Field on Resale Private Line Form |
| NCI | Network Channel Interface Code - Required on Michigan orders only Example: CKL 1-225 N Randolph, Grand Rapids, MI/NCI 02DA2 Order Placement: NCI and SECNCI Fields on Resale Private Line Form |
| SCS and ZSCS | Secondary Class of Service – Indicates a Class of Service different from the main class of service. Example: SCS LDCDL Order Placement: STOS Field on Resale Private Line Form |
| SGN | Segment Number – Indicates the segments in a multi-point circuit which carries a Common Language Circuit Identification (CLCI). Example: USOC/CKL 3-609 N Grand, Indpls, IN/SGN C Order Placement: Not required |

## NC/NCI

Michigan

Metallic Circuits

| CKT Description | NC Code | NCI Code – End User |
| --- | --- | --- |
| 2W McCulloh Series Bridging | NU-B | 02DC8.1 |
| 2W Non-McCulloh 2 Point | NT-- | 02DC8.3 |
| 2W Non-McCulloh Multipoint Series Bridging | NT-B | 02DC8.3 |
| 4W McCulloh Series Bridging | NU-B | 04DC8.1 |
| 4W Non-McCulloh 2 point | NT-- | 04DC8.3 |
| 4W Non-McCulloh Multipoint Series Bridging | NT-B | 04DC8.3 |

Telegraph Service

| 75 Baud |
| --- |
| CKT Description | NC Code | NCI Code – End User |
| 2W Standard | NW-- | 02TT8.2 |
| Bridging 4W | NW-B | 04TT8.2 |
| 150 Baud |
| 2W Standard | NY-- | 02TT8.2 |
| Bridging 4W | NY-B | 04TT8.2 |
| EIA Interface | ----- | 10IA8 |

## Miscellaneous Ordering Procedures

- Channel Services in the 1000, 3000, 6000 and 9000 Series are ordered on a REQ TYP 'K'.

- Channel mileage USOCs should be shown first in the FEATURE field.

# Billing

See individual state tariffs for recurring and nonrecurring charges.