CHANNEL SERVICES -SERIES 2000

Description	4

Type 2001	4

Conferencing and Signaling	5

Conferencing	5

Signaling Feature and Arrangements	5

Type 2301	6

Aliases	6

Availability	6

Restrictions/Limitations	6

General – All states	6

Type 2001	7

Type 2001B	7

Type 2001C	7

Type 2002 – Additional Limitations	7

Type 2301 – Additional Limitations	8

Tie Lines	8

Conditioning	8

Type C4 Conditioning	8

Type D Conditioning	9

Interactions	9

CPE Involvement	9

Pre-Ordering	9

Ordering	10

New Connect	10

Subsequent Order Activity	12

Mileage Application	12

Circuit Specific Requirements	14

Tie Lines	14

PBX to Centrex or Centrex to Centrex	14

Pulsing Type	15

Off Premises Extensions	18

Continuous Property	18

Michigan Only	18

Non-Continuous Property	18

Circuit IDs (CLCI) & Secondary Classes of Service	18

Illinois	18

Indiana	20

Michigan	21

Ohio	21

Wisconsin	22

Circuit Function Table	24

CLCI Service Code Key for 3rd and 4th Characters	26

Listings	26

Facility Interface Codes (FIC)	27

The FIC code needs to be populated on the product form in the Feature Detail field against the line assignable USOC for IL, OH, IN, WI. Example: /FI	27

Illinois	27

Indiana	27

Michigan	27

Ohio	28

Wisconsin	28

FIC Code Translator	28

Jacks	29

Due Dates	30

USOCs	30

Illinois	30

Type 2001	30

Miscellaneous USOCs	32

Talk Battery	32

Interface Conversion	33

Type 2001A	33

Type 2001B	33

Centrex Terminations	34

Type 2001C	35

Type 2001D	36

Type 2002	36

Type 2301	38

Type 2335 – Common Equipment	39

Type 2335 – Same SA – Local Channels	39

Type 2335 – Inter SA – Local Channels and Mileage	40

Type 2336 – Common Equipment Charges	41

Type 2336 – Same SA – Local Channels	41

Type 2336 – Inter SA – Local Channels and Mileage	41

Indiana	41

Type 2001	41

Continuous Property Terminations	41

Non-Continuous Property Terminations	42

Non-Continuous Property:	42

Type 2002	43

Type 2014	44

Type 2021	45

PBX to PBX	45

Type 2026	46

Michigan	47

Direct Analog – VG32	47

Ohio	50

Type 2001	50

Signaling and Switching Arrangements:	51

Type 2002	51

Type 2013	52

Type 2014	52

Type 2020, 2021, 2024, 2025 and 2026	53

Miscellaneous Tie Line USOCs	53

Off Premises Extension	54

Wisconsin	55

Type 2001	55

Signaling	55

Type 2002	55

Type 2003	56

Type 2004	56

Type 2005	57

Signaling	57

Type 2006	57

Type 2010	57

FIDs	58

NC/NCI	59

VG32 – Formerly Type 1	59

VG32 – Formerly Voice Dry Pair, Hoot & Holler	60

VG32 – Voice Burglar & Fire Alarm (non-Morse), Two-Way Radio, Traffic Signal, Telemetering, Wired Music, Electrowriter	60

VG32 – Toll Terminal and Mobile Radio Telephone, Two-Way Radio – Additional Terminal	60

VG32 – PBX Off Premises Station	60

VG32 – Off Premises Extension	60

VG – Tie Lines	61

NCI Codes	61

VG32 – Formerly Type 1 – (PL)	61

VG32 – Formerly Type 1 – (RT)	61

VG32 – Formerly Type 1 – (PL & RT) Bridging	61

VG32 – Formerly Voice Dry Pair, Hoot & Holler	62

VG32 – Formerly Voice Dry Pair, Hoot & Holler-Bridging	62

VG32 – Voice Burglar & Fire Alarm (non-Morse), Two Way Radio, Traffic Signal, Telemetering, Wired Music, Electrowriter	62

VG32 – Voice Burglar & Fire Alarm (non-Morse), Two Way Radio, Traffic Signal, Telemetering, Wired Music, Electrowriter – Bridging	62

VG32 – Toll Terminal and Mobile Radio Telephone, Two-Way Radio – Additional Terminal	63

VG32 – PBX Off Premises Station	63

VG32 – Off Premises Extension	63

VG32 – Tie Lines	63

Miscellaneous Ordering Procedures	64

Billing	65

# Description

These services represent a category of analog services primarily to address a variety of voice communications needs.

Note:  Effective January 1, 2004, Illinois HB 2489 states when a telecommunications carrier initiates a disconnection of service on a known emergency system or fire alarm system that is required by the local authority to be a dedicated phone line or circuit to the central dispatch of the fire protection district or, if applicable, the police department, the carrier shall also transmit a copy of the written notice of disconnection to the local authority.

- Channels are furnished with the approximate bandwidth of 300-3000Hz for a single (half-duplex) operation.

- For two-point circuits, there are two terminations (either two primary terminations or one primary termination and one central office termination) for connection to CO multiplexer.

- For multi-point circuits, the number of terminations is the number of premises and the CO multiplexer termination connected to the channel.

## Type 2001

- Type 2001 channels provide voice communication between two or more stations directly connected to the channel.

- Type 2001 channels are two wire or four wire. At full conference channels are four wire. Multi-point channels without conferencing are only available within the same SA, same central office.

- Type 2001 channels are not connected to the Telephone Exchange Network.

- Type 2001 channels terminate in subscriber provided telephone equipment other than a switch.

- Type 2001 channels may terminate at locations of separate subscribers - Joint user does not apply.

- For two-point circuits, there are two terminations: either two primary terminations or one primary termination and one central office termination for connection to a Central Office Multiplexer.

- For multi-point circuits, the number of terminations is the number of premises and the Central Office Multiplexer termination connected to the channel.

The Channel Services Series 2000 is identified by different numbers in the following states. The services below are used for Tie Lines(TL) to connect two PBX locations, a Centrex and a PBX, or two Centrex accounts:

| Channel Types | States |
| --- | --- |
| 2001B | Illinois |
| 2021, 2026 | Indiana |
| VG33 | Michigan |
| 2020, 2021, 2024, 2025, 2026 | Ohio |
| 2010 | Wisconsin |

The services below are channels to extend either terminal from a PBX or an intercom station, from a key system to another location to be terminated in customer provided telephone equipment other than a switch.

| Channel Types | States |
| --- | --- |
| 2001C | Illinois |
| 2014 | Indiana |
| 2013, 2014 | Ohio |
| 2005 | Wisconsin |

The services below are channels are used for voice transmission or combined voice transmission and control in connection with remote metering, supervisory control and miscellaneous signaling purposes. These channels can also be used as a radio Land Line to provide access to non-broadcast radio transceivers.

| Channel Types | States |
| --- | --- |
| 20002 | Illinois, Indiana, Ohio |
| 2002, 2004 | Wisconsin |

## Conferencing and Signaling

### Conferencing

- Boosts transmission on multi-point circuits

- Allows multiple pre-designated parties to participate in a conference call with guaranteed transmission.

### Signaling Feature and Arrangements

Two point signaling:

- CLEC may provide own signaling

- Automatic two-point signaling is activated by going off-hook at either end.

Automatic multi-point signaling:

- On 2-wire channels, the remote locations signal the main location

- On 4-wire channels, the main location signals the remotes.

- Stations at the same address cannot signal one another.

- A talk battery not arranged for signaling is available to activate end user-provided paging systems.

- Concentrator identifier channels require loop start or reverse battery signaling.

Interface Conversion Unit

- Converts a 4-wire channel into a 2-wire interface.

- Installed at end user’s location on SBC side of network interface

- Billed per location.

E and M Type – All States

- Applicable to both ends of PBX-to-PBX tie lines.

- Not applicable to Centrex-to-Centrex tie lines.

- Not applicable to Centrex end of a PBX/Centrex Tie line

- All signaling is billed to main account.

- Generated by a Facility Interface Arrangement required at each end of a tie line terminating in PBX.  The end user’s side of the Facility Interface Arrangement may be arranged for:

  - 2-wire or 4-wire terminations

  - Wiring the talk pair and E&M leads in certain sequences

## Type 2301

Type 2301 channels transmit voice quality tone signals at a rate up to 400 baud for operating customer provided alarm, remote control or remote metering equipment.

## Aliases

- Private Line

- Burglar Alarm

- Fire Alarm

- Direct Analog

# Availability

Availability of these services apply to:

- Non-continuous property ( not campus-like building arrangements)

- Intra and InterExchange within a LATA

- Two-point or Multi-point

## Restrictions/Limitations

### General – All states

- Channel service may not be connected to facilities furnished for exchange or toll service.

- Temporary supervision of service is not allowed.

- Tie lines may only be two-point service. (i.e., not multi-point)

- Continuous property (campus like setting with multiple buildings)

- Off-premise extensions cannot stand alone

- Off-premise extensions are not allowed to migrate

### Type 2001

- Paging circuits are voice grade channels provided for the interconnections of Centrex, PBX. CPE paging systems. When used in conjunction with Centrex, these circuits are engineered for 2 pair. One is a talk pair and the other is used for a control lead. This lead provides an arrangement to make busy talk pair. This make busy arrangement is provided and included in the EW3CX or ER8CX rate.

- The CLEC’s end user provides a switch or other CPE arrangement which sends a short to an interconnect device when they want to activate the central office make busy arrangement.

- Joint User does not apply

- On multi-point circuits, remote locations cannot signal one another.

- CO Termination can only be used for connection to a CO multiplexer.

- The number of stations permitted on a non-conference circuit is limited by operating and transmission factor.

- Note: ERBCX and EW3CX USOCS are grandfathered as of 6-2-95.

### Type 2001B

- Signaling (E&M Type)

- Applicable to both ends of PBX to PBX tie lines

- Not applicable to Centrex to Centrex tie lines

- Not applicable to Centrex end of a PBX/Centrex tie-line

### Type 2001C

- Signaling Arrangements: (PBX only)

- Customer may provide own signaling in one of three types:

  - Type A is provided for ports capable of operation over loops with resistance in the range of 0-1999 ohms.

  - Type B is provided for ports capable of operation over loops with resistance in the range of 200-899 ohms.

  - Type C is provided for ports capable of operation over loops with resistance in the range of 900 ohms or more.

- Location of PBX determines the Access Area code to use for rating purposes.

- Only one signaling arrangement is needed per channel.

### Type 2002 – Additional Limitations

- Type 2002 Channels are not designed for connection to the switching network to access exchange or toll service.

- To assure satisfactory transmission levels, engineering may have to limit the number of stations connected to a multi-point circuit. Distance is a factor in the satisfactory performance of the circuit.

- These circuits are designed solely for intrastate operation. A channel will be classified as interstate if transmissions will be sent to vehicles operating outside of Illinois.

### Type 2301 – Additional Limitations

- Only two-point channels may be installed.

- Type 2301 Channels are not designed for connection to the switching network to access exchange or toll service.

- Type 2301 Channels are not suitable for transmission of direct current pulses.

- Not suitable for transmission of direct current pulses.

- Remote stations:

  - Can transmit only to the master station

  - May be either 2-wire or 4-wire configuration but must all be identical.

    - If 2-wire, the master station may be furnished with filters capable of limiting transmission and reception to certain selected frequencies.

- Joint User Arrangement:

  - Offered only on interexchange channels located outside of MSA 1.

  - Allows other individuals, firms or corporations to use the service of another subscriber.

  - Orders accepted only for the subscriber responsible for payment of all charges incurred.

### Tie Lines

- Available only as two-point services in Illinois, Indiana, Michigan and Ohio.

- In Wisconsin, may be two-point or multi-point service.

- May not be connected to facilities furnished for exchange or toll service.

- Not available on continuous property in Michigan, Ohio and Wisconsin.

- Not all systems work with certain types of tie lines.

- Special screening arrangements are needed to ensure toll calls made over tie lines are billed properly.

### Conditioning

- Acts like a filter to remove static, fading or noise that could cause errors from the channel by means of electrical equipment installed on the circuit at prescribed intervals.

- The same channel cannot be extended to more than two off-premises addresses without special authority agreements to provide acceptable performance.

#### Type C4 Conditioning

- Available only on two-point circuits

- Envelope delay shall not exceed the maximum difference as follows:

| If Envelope Delay is between: | The maximum difference should not exceed: |
| --- | --- |
| 1000 and 2600 Hz | 300 mcs |
| 800 and 2800 Hz | 500 mcs |
| 600 and 3000 Hz | 1500 mcs |
| 500 and 3000 Hz | 3000 mcs |

The loss deviation with frequency (from a 1000 Hz reference) shall not exceed:

- -2 to -3 db from 500 to 3000 Hz.

- -2 to +6 db from 300 to 3200 Hz.

#### Type D Conditioning

- Available on two-point.

- High performance conditioning.

- The ratio of signal to C-notched noise shall be at least 28 db.

- The ratio of signal to second order non-linear shall be at least 35 db.

- The ratio signal to their order non-linear distortion shall be at least 40 db.

- D conditioning does not make channels suitable for voice transmission and may not be available in all locations.

## Interactions

The use of these 2000 Series Services are very dependent on the devices used at each end of a connection. Type and quality of the following can influence services.

- Switching Systems (ie., PBX or Centrex)

- Customer Premises equipment (ie., Key Sets)

## CPE Involvement

The type and quality of the items below impacts uses of these Analog Services.

- Switching systems (ie. PBX or Centrex).

- Customer Premises Equipment (ie. Key Sets)

- Jacks for terminating the PBX end of a tie line must be compatible with the Facility Interface Arrangement.

# Pre-Ordering

SBC mechanized pre-ordering Operational Support System (OSS) is available to assist the CLECs on obtaining pre-ordering information. However, certain orders require a manual pre-ordering transaction before an LSR can be submitted successfully. The manual pre-ordering process is described in detail under the PreOrdering section of this handbook.

When performing a manual pre-ordering transaction, fill in the LSR request as completely as possible using EDI/WebLEX. When the needed manual pre-ordering information is filled out, save the LSR request. Print a copy of the request and fax it to SBC along with the Manual PreOrdering Information Cover Sheet. SBC will fax back the needed pre-ordering information so the CLEC can successfully submit a firm LSR.

# Ordering

Type 2000 channels provide voice communications between two or more stations directly connected to the channel. Channels may be two wire or four wire.

## New Connect

- Determine the type of 2000 Series Channel that the end user wants to order. Questions that can be asked to determine the correct service to order are:

  - Is this circuit for a voice, data or signal application?

  - If this is a data application see Channel Series 3000.

  - If this is a signal application, see Channel Series 1000.

  - If this is a voice application, what type of CPE does the end user have?

PBX

- Does the end user want to extend an extension of the PBX to another location? This will enable the end user to communicate with a station user at a physically different address without using the public network. This type of station can also be allowed access to the public switched network through the PBX.

- Yes, go to next step.

- No, keep asking questions.

- Does the end user want to tie two PBXs or a PBX and Centrex or two Centrex systems together so that they can intercommunicate?

- Yes, go to next step.

- No, keep asking questions.

- What does the end user want this circuit to do?

Key System

- Does the end user want to extend an intercom station to another location? This will enable the end user to communicate with a station located at a physically different address without using the public network. However, there is no network access with this type of circuit.

- Yes, go to next step.

- No, keep asking questions.

- What does the end user want this circuit to do? Keep asking questions until the type or function of the circuit has been determined.

- Determine if all circuit locations are within the same LATA.

- If yes, go to next step.

- If no, the request will have to go to an IXC InterExchange Carrier.

- Determine the type of Controlling Company.

- If AOC, go to next step.

- If Independent Company, is the PBX or Key System located in AOC territory?

    - If yes, go to next step.

    - If no, the request will have to go to the Independent Company for provisioning.

- Obtain the following information:

  - Account Telephone Number

  - End User’s name

  - Address of all locations, including City, State, Zip Code and cross street (Wisconsin only)

  - How many circuits at each address are required

  - Contact Names and Telephone Numbers for each location

  - Termination equipment, jacks, etc.

  - Signaling/FIC Code if applicable.

  - Determine type of start call control to be used:

    - Wink

    - Delay

    - Immediate

  - If the Channel Service is for a Homebound application, obtain the following:

    - Student’s name, address and residence telephone number.

    - Name and address of the school, telephone number and responsible party.

    - Room numbers involved.

  - If the type of circuit being ordered is for a Tie Line and one or both ends will terminate in a Centrex, obtain the following:

  - Centrex Account Telephone Number at both ends of the circuit.

  - Determine if the tie line(s) will be:

    - One Way In

    - One Way Out

    - Two Way

  - Determine if the tie line should be:

    - Senderized

    - Cut-through

    - Pseudo cut-through

    - Manual

  - Determine which end will supply the dial tone:

    - Distant end

    - Local end

  - Determine the DAC (Dial Access Code) for each Centrex.

  - Determine which facilities the tie line(s) will be able to access at the other end:

    - Stations only

    - Network access (dial 9+)

    - Private Facilities, if multiple which ones

  - If access to the public switched network is allowed, obtain a Centrex telephone number to be used for billing purposes only.

  - Obtain a station number to call for testing.

- Negotiate due date and premise access.

- Submit request to the LSC.

## Subsequent Order Activity

- Obtain the circuit and account telephone numbers.

- Determine the type of Controlling Company.

  - If AOC, go to next step.

  - If Independent Company, is the PBX or Key System located in AOC territory?

  - If yes, go to next step.

  - If no, the request will have to go to the Independent Company for provisioning.

- Determine type of change to be made

- Negotiate due date and premise access, if necessary.

- Submit request to the LSC.

## Mileage Application

- Type 2000 channels can be provided from general facilities or Service Transport Facilities (STF) complement. STF is an arrangement in Illinois only for providing and charging for central offices to end user facilities.     Note:  See respective State Exchange tariffs for definitions and descriptions of service area. There is some variation from state to state.

- 2 point, 2-wire termination requires one pair from STF complement (Illinois only).

- 2 point, 4-wire termination requires two pair from STF complement (Illinois only).

- A local channel termination, based on account area, is billed for each subscriber premises connected to the channel.

- Inter SA (Service Area) circuits are billed short haul (less than 12 miles) or long haul (12 miles & over) mileage.

- Each segment between points is treated independently. Use that combination of distances that produce the shortest mileage between points.

Short haul and long haul can be intermixed on the same channel.

| State | If the Circuit Locations Are | And the NNXs are | Then the mileage is measured as follows |
| --- | --- | --- | --- |
| IL, IN, MI, OH | Same Exchange | Served from same wire center | No mileage applies |
| IL, IN, MI, OH | Same Exchange | Served from different WCs | WC to WC (Interoffice Mileage) |
| IN | Different but contiguous exchanges | Served from different WCs | WC to WC (Interoffice Mileage) |
| IN | Different Exchanges – no rate center | Served from different WCs | WC to WC (Interoffice Mileage) |
| IL, IN, MI, OH | Different, non-contiguous exchange | Served from the Rate Centers | Rate Center to Rate Center (InterExchange Mileage) |
| IN, OH | Different, non-contiguous exchanges | Served from different WCs than are the Rate Centers | Rate Center to Rate Center between the principal exchanges (InterExchange Mileage) AND Rate Center to Serving WC (Interoffice Mileage) |
| WI | Same CO & 2 Point | N/A | 1 /4 miles from address to address |
| WI | Same CO & Multi-point | N/A | 1/ 4 miles from CO to each address |
| WI | Different CO, 2 point or multi-point | N/A | Miles between COs AND 1 /4 miles from serving CO to each address |

## Circuit Specific Requirements

### Tie Lines

#### PBX to Centrex or Centrex to Centrex

Information must be determined for each end of a PBX to Centrex or Centrex to Centrex Tie Line.  Service options for outgoing calls include the following:

| Service Options | Description |
| --- | --- |
| Senderized | May be used to limit a station user’s access when the distant system is unable to restrict access on the Tie Line. The local end always supplies dial tone. Senderization is required for use with speed calling and as part of Centrex Flexible Route Selection (FRS). May be senderized in one direction and cut through in another. The Centrex system collects all of the digits dialed and sends them all at once to the distant system. Centrex can be optioned to send a variable or fixed number of digits. |
| Variable Number of Digits | Any number of digits between one and fifteen are sent. When a variable number of digits is specified, the ESS will begin inter-digital timing after each digit is dialed. If no digits are dialed within three to five seconds of the last digit dialed, the ESS will assume that all digits collected to that point are the total digits to be sent. The switch will seize the Tie line, wait for a start dial, signal and then transmit all the digits. |
| Fixed Number of Digits | The same number of digits, between one and fifteen, is always sent. When a fixed number of digits is specified, the ESS will wit until that number of digits is received before transmitting. An end user’s dialing plan must be considered when using this operation. The end user may wish to reach only 3-, 4-, or 5-digit extensions at the distant end. This could be the case on a point-to-point Tie Line. |
| Cut-Through | Connected to a dial pulse conversion circuit that accepts incoming signals and regenerates as dial pulses to transmit to the distant end. The calling party directly controls the routing of each tandem point. Outgoing callers will dial an access code and receive a second dial tone. If the distant end provides this, provision as Dial Tone Distant. If the distant switch cannot provide dial tone, provision as Dial Tone Local. The Centrex sends each digit as it is dialed to the distant end. No limit to the number of digits that may be dialed. The distant end generally supplies dial tone. Used with all types of Tie Lines. Engineered to maintain a quality transmission level in tandem operation. |
| Pseudo Cut-Through | Does not use dial pulse converter. Digits pulsed directly from the calling party’s touch-tone telephone. Not compatible with rotary dial telephones. Designated as Dial Pulse for the purpose of assigning a Cut-Through Trunk Class Code. No limit to the number of digits that may be dialed. Used with all types of Tie Lines. Engineered to maintain a quality transmission level in a tandem operation. Provision second dial tone distant end and start dial tone. |
| Manual | Does not provide signaling or pulsing. Can be used as connection between Centrex user and jack on switchboard where an operator will manually connect call to the desired station. Digits are dialed over the distant end’s dial tone. Dial tone always supplied by the distant end. No limit to the number of digits that may be dialed. Does not use transmitters to send digits to the distant end. The calling party has to use the touch-tone pad to signal the distant end. Used with tandem, non-tandem and satellite tie lines but may use transmission quality used in a tandem operation. Pulsing Types: Incoming and Outgoing pulsing types are determined by the PBXs capabilities on a PBX to Centrex Tie Line. See the Pulsing Type table below for guidance in selecting pulsing types. |

##### Pulsing Type

| Pulsing Type | Description |
| --- | --- |
| Multi-Frequency (MF) | Outgoing calls use MF transmitter. Incoming calls use MF receiver. Outpulsing takes approximately 1/ 2 second. This is the fastest type of outpulsing. MF transmitters and receivers are available in all COs. |
| Touch-Tone | Also referred to as Dual Tone/Multi-Frequency (DTMF). Originating system transmits digits on a touch-tone transmitter. Distant end system receives digits on a touch-tone receiver. Centrex systems use one receiver that accepts touch-tone or dial pulsing in 1ESS or 1AESS. 5ESS or DMS require specific information as to the type of impulse. Outpulsing takes approximately one second. Touch-tone receivers are available in all C.O. Touch-tone transmitters are available in all 5ESS and DMS offices and all 1ESS and 1AESS offices in Chicago. All other 1ESS and 1AESS offices must be checked individually for available facilities. |
| Dial Pulse (DP) | Originating system transmits dial pulses using a Dial Pulse transmitter. Distant end system receives dial pulses on a dial pulse receiver. Centrex uses one receiver that accepts dial pulse or touch-tone signaling in a 1ESS or 1AESS. 5ESS or DMS require specific information as to the type of pulsing. Outpulsing takes approximately six seconds. It is the slowest form of outpulsing. Dial pulse receivers and transmitters are available in all C.Os. Generally used for Centrex to Centrex Tie Lines as outpulsing in a Cut-Through operation. |
| None | Transmitters and receivers are not used. The digits are dialed or touch-toned over the circuit. Used only with Cut-Through, Psuedo Cut-Through and Manual operations. |
| Dial Tone Supply | Local: The local end supplies dial tone. Used with Senderized Service Option. Could be used with Cut-Through if the distant end cannot supply dial tone. Distant: The distant end supplies dial tone. Used with Cut-Through and Manual Service options. |
| Start Dial Signals | Outpulsing start signals apply to the type of start signal originated from the distant switch. Incoming start signals apply to the type of start signal originated from the local Centrex system. The switch receiving the digits will give the signal to the PBX/Centrex system being called. Tells the calling PBX/Centrex system that the distant system has been seized and is ready to accept digits. When used with a PBX to Centrex Tie Line, the type of start dial signaling used is determined by the PBX’s capabilities. The type of incoming start signal used may be the same or different from the outgoing start signal on a Tie Line. Specify one of the following on any incoming and outgoing basis. None: Also referred to as Immediate or No Start. No signal is sent. The originating system sends digits and the distant system is ready to accept these digits as soon as the connection is made. Used for Cut-Through operation. Delay Dial: The originating system pauses after the connection is made before sending digits. The distant system expects a delay after the connection is made before receiving digits. Wink Start: Positive signal is received from the distant system after the circuit is connected and before digits are sent by the Centrex system (outgoing), or if a positive signal is given by the Centrex system before digits are sent from the distant system (incoming). Use for all Centrex to Centrex senderized Tie Lines. Dial Tone: Once the connection is made, the distant end provides dial tone back to the originating system. Only used when the distant end provides dial tone. Used for all Centrex to Centrex Cut-Through Tie Lines. |

### Off Premises Extensions

Off Premises Extensions are:

- An additional termination of an exchange line.

- Located at another premise in the same or different exchange.

- Within the same Local Access and Transport Area (LATA).

### Continuous Property

Continuous Property extensions are handled as deregulated inside wire.

- CLEC MUST have an Inside Wire contract with SBC.

- Select type3 of deregulated jack to be installed.

- Obtain contact name and telephone number.

- In the REMARKS field of the LSR, explain where the extension is to be installed.

#### Michigan Only

| If Extension Is | Then |
| --- | --- |
| Less than 528 feet | Issue request for deregulated jack and note the REMARKS field on the LSR with location information. |
| 528 feet or more | The extension must be routed through the Central Office. Mileage and Surcharge USOCs must be on the request. |

### Non-Continuous Property

- Provide the address location (if applicable), city, state and zip code that the line is to be extended to. This information will have to go in the FEATURE DETAIL Field on the product form if this is for a residential or business POTS line. The information should follow the line assignable USOCs for the extension.

- Requests for this service always require a premise visit.

## Circuit IDs (CLCI) & Secondary Classes of Service

### Illinois

| CLCI Code (Service Code) | Class of Service Intra SA | Class of Service Inter SA | Description |
| --- | --- | --- | --- |
| Type 2001 |
| FR++ | PLYVL | PLYVS | Fire Dispatch provides a group alerting system that operates warning devices at various locations from a central point. Service is used by fire or ambulance companies to alert members. |
| PG++ | PLYVL | PLYVS | Paging voice-grade circuit between two or more end user locations used for transmission of announcements or signals via loud speakers. |
| PL++ | PLYVL | PLYVS | Private Line – Voice provides full-time service for transmission of voice only between two or more stations. |
| Type 2002 |
| RT++ | ORMVL | ORMVS | Radio Land Line channel used to provide access to non-broadcast radio transceivers |
| Type 2301 |
| VM++ | RMTVL | RMTVS | Control/Remote Metering – Voice Grade circuit between a central point and remote location used to selectively monitor or control quantities or operations at remote locations. |
| PM++ | RMTVL | RMTVS | Protective Monitoring voice-grade circuit between an end user’s premise and an alarm monitoring device. |
| Type 2001C |
| OS++ | PYCLL | PYCLS | Off Premises PBX Station Line |
| OI++ | PYCLL | PYCLS | Off Premises Intercommunications Station Line |
| Type 2001A |
| OP++ | N/A | N/A | Off Premises Extension – Voice Line |
| Type 2001B |
| IT++ | PTBVL | PTBVS | Intertandem Tie Trunk |
| SA++ | PTBVL | PTBVS | Satellite/Tributary Tie Trunk |
| TA++ | PTBVL | PTBVS | Tandem Tie Trunk |
| TL++ | PTBVL | PTBVS | Non-Tandem Tie Trunk |

### Indiana

| CLCI Code (Service Code) | Class of Service Intra SA | Class of Service Inter SA | Description |
| --- | --- | --- | --- |
| Type 2001 |
| PL++ | PLYVL | PLYVS | Private Line – Voice |
| PG++ | PLYVL | PLYVS | Paging |
| OI++ | PLYVL | FPSVS | Off Premises Intercommunications Station Line |
| VM++ | PLYVL | FPSVS | Control/Remote Metering – Voice Grade |
| PM++ | PLYVL | FPSVS | Protective Monitoring |
| OP++ | N/A | N/A | Off Premises Extension – Voice Line |
| Type 2002 |
| RT++ | OMRVL | OMRVS | Radio Land Line |
| Type 2014 |
| OS++ | PVLLL | PVLLS | Off Premises PBX Station Line |
| Type 2021 – PBX to PBX |
| IT++ | PTBVL | PTBVS | Intertandem Tie Trunk |
| SA++ | PTBVL | PTBVS | Satellite/Tributary Tie Trunk |
| TA++ | PTBVL | PTBVS | Tandem Tie Trunk |
| TL++ | PTBVL | PTBVS | Non-Tandem Tie Trunk |
| Type 2026 – Centrex to Centrex & Centrex to PBX |
| IT++ | PTBCL | PTBCS | Intertandem Tie Trunk |
| SA++ | PTBCL | PTBCS | Satellite/Tributary Tie Trunk |
| TA++ | PTBCL | PTBCS | Tandem Tie Trunk |
| TL++ | PTBCL | PTBCS | Non-Tandem Tie Trunk |

### Michigan

| CLCI Code (Service Code) | Class of Service |
| --- | --- |
| VG32 – Burglar & Fire Alarm (Non-Morse) – 2 Way Radio Traffic Signal, Telemetering, Wired Music, Electrowriter, Mobile Radio Telephone Channel-Dispatch Services, Voice, Dry Pair, Hoot & Holler, Toll Terminals, Break Hunt, Off Premises Extension-Line, PBX Off Premises Stations |
| UC++ | XZV2+ |
| VG32 – Tie Lines |
| UD++ | XZV3+ |

Note: + 5th Character – Secondary Class of Service:

L = IntraExchange – Intra Wire Center

I = IntraExchange – Inter Wire Center

S = InterExchange – Inter Wire Center

### Ohio

| CLCI Code (Service Code) | Class of Service Intra-Exchange | Class of Service Inter-Exchange | Description |
| --- | --- | --- | --- |
| Type 2001 |
| DL++ | FPSVL | FPSVS | Dictation Line |
| PA++ | FPSVL | FPSVS | Protective Alarm |
| PG++ | FPSVL | FPSVS | Paging |
| PL++ | FPSVL | FPSVS | Private Line – Voice |
| PM++ | FPSVL | FPSVS | Protective Monitoring |
| VM++ | FPSVL | FPSVS | Control/Remote Metering – Voice Grade |
| Type 2002 |
| RT++ | OMRVL | OMRVS | Radio Land Line |
| Type 2013 – Use End User’s Signaling |
| OS++ | PYCLL | PYCLS | Off Premises PBX Station Line |
| Type 2014 – Use SBC Signaling |
| OS++ | PYCLL | PYCLS | Off Premises PBX Station Line |
| Type 2020, 2021, 2024, 2025, 2026 |
| IT++ | PTBVL | PTBVS | Intertandem Tie Trunk |
| SA++ | PTBVL | PTBVS | Satellite/Tributary Tie Trunk |
| TA++ | PTBVL | PTBVS | Tandem Tie Trunk |
| TL++ | PTBVL | PTBVS | Non-Tandem Tie Trunk |
| Circuit – Off Premise Voice Line |
| OP++ | N/A | N/A | Off Premises Extension – Voice Line |

### Wisconsin

| CLCI Code (service Code) | Class of Service Intra-Exchange | Class of Service InterExchange | Description |
| --- | --- | --- | --- |
| Type 2001 – 2 Wire, 2 Point or Multi-Point |
| PG++ | PLYVL | PLYVS | Paging |
| PL++ | PLYVL | PLYVS | Private Line – Voice |
| PM++ | PLYVL | PLYVS | Protective Monitoring |
| VM++ | PLYVL | PLYVS | Control/Remote Metering – Voice Grade |
| Type 2002 – 4 Wire, 2 Point or Multi-Point |
| PG++ | PLYVL | PLYVS | Paging |
| PL++ | PLYVL | PLYVS | Private Line – Voice |
| PM++ | PLYVL | PLYVS | Protective Monitoring |
| VM++ | PLYVL | PLYVS | Control/Remote Metering – Voice Grade |
| Type 2003 – 2 Wire, 2 Point or Multi-Point |
| RT++ | OMRVL | OMRVS | Radio Land Line |
| Type 2004- 4 Wire, 2 Point or Multi-Point |
| RT++ | OMRVL | OMRVS | Radio Land Line |
| Type 2005 |
| OS++ | PLYPL | PLYPS | Off Premises PBX Station Line |
| OI++ | PLYPL | PLYPS | Off Premises Intercommunications Station Line |
| Type 2006 |
| OP++ | N/A | FXSTL | Off Premises Extension – Voice Line |
| Type 2010 |
| IT++ | PBX-PBX PTBVL PBX-CTX PTBCL CTX-CTX PTBTL | PBX-PBX PTBVS PBX-CTX PTBCS CTX-CTX PTBTS | Intertandem Tie Trunk |
| SA++ | PBX-PBX PTBVL PBX-CTX PTBCL CTX-CTX PTBTL | PBX-PBX PTBVS PBX-CTX PTBCS CTX-CTX PTBTS | Satellite/Tributary Tie Trunk |
| TA++ | PBX-PBX PTBVL PBX-CTX PTBCL CTX-CTX PTBTL | PBX-PBX PTBVS PBX-CTX PTBCS CTX-CTX PTBTS | Tandem Tie Trunk |
| TL++ | PBX-PBX PTBVL PBX-CTX PTBCL CTX-CTX PTBTL | PBX-PBX PTBVS PBX-CTX PTBCS CTX-CTX PTBTS | Non-Tandem Tie Trunk |

## Circuit Function Table

| Bellcore Code | Code Meaning | Description |
| --- | --- | --- |
| DL | Dictation Line | Provides a connection between PBX, Centrex or Central Office and a dictation device. |
| FR | Fire Dispatch | Provides a group alerting system that operates warning devices at various locations from a central point. Fire or ambulance companies use this service to alert their members. |
| IT | InterTandem Tie Trunk | Connects two tandem PBX or Centrex in a PBX Tie Trunk Network. An Intertandem Tie Trunk may be connected to other Tie Trunks at both ends. |
| OI | Off Premises Intercommunications Station Line | A voice grade circuit between telephone equipment and a station at a remote location. It is used for intercommunication only. |
| OP | Off Premises Extension | Provides connection from an extension telephone state to the main station line. The extension telephone is located at a customer’s location which is remote from the main station location. |
| OS | Off Premises PBX Station Line | A voice grade channel between a PBX or a system providing similar functions and a station at a remote location. |
| PA | Protective Alarm (AC Interface at Customer Premises) | A voice grade channel for an alarm system in which information is transmitted by means of varying frequencies or tones (ie., TABS, etc.) |
| PG | Paging | A voice grade circuit between two or more customer locations. It is used for the transmission of announcements of signals via loudspeaker(s). |
| PL | Private Line – Voice | Provides a full-time service for the transmission of voice only between two or more stations or order equipment (eg., turrets, order tables, etc). A private line is for the exclusive use of certain stations or order equipment and has no access to the switched message network. Signaling between stations or order equipment may be voice, manual, automatic, dial or there may be no signal condition. |
| PM | Protective Monitoring | A voice grade circuit between a customer’s premise and an alarm-monitoring device. |
| RT | Radio Land Line | A channel used to provide access to non-broadcast radio transceivers. |
| SA | Satellite/Tributary Tie Trunk | Interconnects a main PBX or Centrex to a satellite/tributary PBX. When a satellite/tributary PBX is involved, this code takes precedence over the trunk codes: IT, TA and TL. |
| TA | Tandem Tie Trunk | Provides an interconnection from a non-tandem PBX, ETN Main PBX or Centrex. A tandem tie trunk may be connected to another tie trunk at either end. |
| TL | Non-Tandem Tie Trunk | Provides interconnection between PBXs, Centrex or systems providing similar functions. A Non-tandem Tie Trunk may not be connected to another Tie Trunk at either end. |
| VM | Control/Remote Metering – Voice Grade | A voice grade circuit between a central point and a remote location(s). It is used to selectively monitor or control quantities of operations at the remote locations. |

## CLCI Service Code Key for 3rd and 4th Characters

Third (3rd) Character

- A = Alternate Voice and Data

- D = Data

- N = Non-Data

- S = Simultaneous Data & Data and/or Data & Voice

Fourth (4th) Character

- T = Circuit is Telco customer and all facilities and equipment are Telco provided.

- C = Circuit is Telco customer to Telco customer. Part of facilities and/or equipment is customer provided.

- A = Circuit is Telco customer to Telco customer. All facilities are Telco provided. All Electrically Connected Equipment is customer provided.

- S = Terminates at an InterExchange Carrier’s Point of Termination.

Note: The most common code combination is ++NC.

## Listings

Not applicable.

## Facility Interface Codes (FIC)

## The FIC code needs to be populated on the product form in the Feature Detail field against the line assignable USOC for IL, OH, IN, WI. Example: /FI

### Illinois

| Circuit Type | FIC Code Options |
| --- | --- |
| 2001C | OL13A OL13B OL13C |
| 2001B | TL11M or TL11E TL12M or TL12E TL31M or TL31E TL32M or TL32E TC31M or TC31E TC32M or TC32E |

### Indiana

| Circuit Type | FIC Code Options |
| --- | --- |
| 2014 | OL13A OL13B OL13C |
| 2021 & 2026 | TL11M or TL11E TL12M or TL12E TL31M or TL31E TL32M or TL32E TC31M or TC31E TC32M or TC32E |

### Michigan

| Circuit Type | FIC Code Options |
| --- | --- |
| VG32 | OL13A OL13B OL13C |
| VG32 – Tie Lines | TL11M or TL11E TL12M or TL12E TL31M or TL31E TL32M or TL32E TC31M or TC31E TC32M or TC32E |

### Ohio

| Circuit Type | FIC Code Options |
| --- | --- |
| 2013 & 2014 | OL13A OL13B OL13C |
| 2020, 2021, 2024, 2025 & 2026 | TL11M or TL11E TL12M or TL12E TL31M or TL31E TL32M or TL32E TC31M or TC31E TC32M or TC32E |

### Wisconsin

| Circuit Type | FIC Code Options |
| --- | --- |
| 2005 | OL13A OL13B OL13C |
| 2010 | TL11M or TL11E TL12M or TL12E TL31M or TL31E TL32M or TL32E TC31M or TC31E TC32M or TC32E |

## FIC Code Translator

OL13A, B or C

| Letter | Description |
| --- | --- |
| O | Off Premises Station |
| L | Lossless Interface |
| 1 | Two-wire Interface |
| 3 | Loop Signaling Interface |
| A | Registered Port & Type of Signal, 0-199 ohms |
| B | Registered Port & Type of Signal, 200-899 ohms |
| C | Registered Port & Type of Signal, 900 or more ohms |

TL11M, TL12M, TL31M, TL32M, TC31M, TC32M, TL11E, TL12E, TL31E, TL32E, TC31E or TC32E

| Character Position | Description |
| --- | --- |
| First | T = Tie Trunk |
| Second | L = Lossless Interface C = Conventional Term Set |
| Third | 1 = Two Wire Interface 3 = Four Wire Interface |
| Fourth | 1 = Type I E&M Signal Interface 2 = Type II E&M Signal Interface |
| Fifth | E = Registered equipment provides ground on E lead to originate M = Registered equipment provides battery on M lead to originate |

## Jacks

Note: Jacks for terminating the PBX end of a Tie line must be compatible with the Facility Interface Arrangement.

| FIC | Jack USOC RJ2EX | Jack USOC RJ2FX | Jack USOC RJ2GX | Jack USOC RJ2HX |
| --- | --- | --- | --- | --- |
| TL11M TL11E | X | X | X | X |
| TL12M TL12E |  | X |  | X |
| TL31M TL31E TC31M TC31E |  |  | X | X |
| TL32M TL32E TC32M TC32E |  |  |  | X |
| Jack Capacity | 12 | 8 | 8 | 6 |

## Due Dates

Refer to Resale Due Date matrix for standard due date intervals.  Note: All due dates are dependent upon installation technician availability.

Effective March 20, 2002, an Expedite Order Charge (EOC) will be assessed on all expedited (installation) intervals.  An expedited interval is when a customer requests an installation due date less than the standard interval and that request is met.  The service is installed in fewer days than the standard interval.  If a requested expedited interval cannot be met by SBC, then a standard interval will be provided an no EOC assessed.

## USOCs

### Illinois

#### Type 2001

| SAME SERVICE AREA (SA) CHANNELS SERIES 2001 |
| --- |
| TYPE | USOC |
| 2 POINT BETWEEN POINTS WITHOUT CONFERENCE PER PT. 2-Wire - STF NOT APPLICABLE - STF APPLICABLE - C.O. TERMINATION - C.O. MUX TERMINATION WITH CONFERENCE PER PT. – 4 Wire - STF NOT APPLICABLE - C.O. TERMINATION | WWBA+ OWBA+ CTG AS32X WWB5+ CTG |
| WITH CONCENTRATOR ID. PER CKT - STF NOT APPLICABLE | WWBB+ |

Note: + Local Channel Suffix Codes

Access Area A = A

Access Area B = B

Access Area C = C

| INTER-SA 2 POINT CHANNELS SERIES 2001 |
| --- |
| TYPE | USOC |
| MILEAGE SHORT HAUL BETWEEN SAs - 1ST ¼ MILE - EACH ADDITIONAL ¼ MILE LONG HAUL BETWEEN SAs - 1ST MILE - EACH ADDITIONAL MILE | JZNAJ JZNAC JZNAX JZNAB |
| LOCAL CHANNELS 1 PER PT Short Haul WITHOUT CONFERENCE – 2 Wire - STF APPLICABLE -STF NOT APPLICABLE -CTG Termination WITH CONFERENCE – 4 Wire - STF NOT APPLICABLE - C.O. TERMINATION WITH CONCENTRATOR ID LONG HAUL WITHOUT CONFERENCE – 2 Wire - STF APPLICABLE - STF NOT APPLICABLE - C.O. TERMINATION WITH CONFERENCE – 4 Wire - STF APPLICABLE - C.O. TERMINATION WITHOUT CONCENTRATOR ONCE PER CKT - STF NOT APPLICABLE | WWGA+ OWGA+ CTG WWG5+ CTG WWGB+ WWGR+ OWGR+ CTG WWG6+ CTG WWGS+ |

Note: + Local Channel Suffix Codes

Access Area A = A

Access Area B = B

Access Area C = C

Note: Time and Materials (T&M) MAY BE APPLICABLE

| SAME SERVICE AREA (SA) CHANNELS SERIES 2001 – MULTI-POINT |
| --- |
| TYPE | USOC |
| WITHOUT CONFERENCE PER PT. – 2 WIRE – SAME CO ONLY - STF NOT APPLICABLE STF APPLICABLE CO TERMINATION WITH CONFERENCE PER PT – 4 WIRE - STF NOT APPLICABLE | WWJA+ OWJA+ WWJB+ |
| WITH CONCENTRATOR ID PER CKT - STF NOT APPLICABLE | WWBB+ |

| INTER-SA MULTI-POINT CHANNELS SERIES 2001 |
| --- |
| TYPE | USOC |
| MILEAGE SHORT HAUL BETWEEN SAs WITHOUT CONFERENCE - 1ST ¼ MILE - EACH ADDITIONAL ¼ MILE WITH CONFERENCE - 1ST ¼ MILE -EACH ADDITIONAL 1/4 MILE LONG HAUL BETWEEN SAs – WITHOUT CONFERENCE -1st ¼ MILE -EACH ADDITIONAL MILE WITH CONFERENCE -1st ¼ MILE -EACH ADDITIONAL ¼ MILE | JZNWJ JZNWC JZNVJ JZNVC JZNWX JZNWB JZNVX JZNVB |
| LOCAL CHANNELS 1 PER PT WITHOUT CONFERENCE – 2 WIRE - STF APPLICABLE WITH CONFERENCE – 4 Wire - STF NOT APPLICABLE | WWN5+ WWNB+ |

Note:  + Local Channel Suffix Codes

Access Area A = A

Access Area B = B

Access Area C = C

Note: Time and Materials (T&M) may be applicable

#### Miscellaneous USOCs

| Automatic Signaling | USOC |
| --- | --- |
| Two-Point Intra-SA, without conference, 1 per circuit | 41G |
| Two-Point Inter-SA, without conference, 1 per circuit | 41G1X |
| Multi-point Intra-SA, without conference, 1 per circuit | YY8 |
| Multi-point Intra-SA with Conference or, Multi-Point Inter-SA with conference, 1 per station | 41H |
| Talk Battery |  |
| Applicable to end user provided paging when no battery at end user premise, Touch-tone page required, automatic signal not required per circuit | BA2 |
| Interface Conversion |  |
| 4-Wire to 2-Wire Interface Conversion Unit, 1 per point | UOE |

#### Type 2001A

| INTRA-SA CHANNELS SERIES 2001 |
| --- |
| TYPE | USOC |
| INTRA-DISTRICT |  |
| SAME CO (INTRA SA) (Including SA 105, Champaign-Urbana), LOCAL CHANNEL -STF NOT APPLICABLE -STF APPLICALBE | WWBC+ OWBC+ |
| INTER-DISTRICT |  |
| DIFFERENT CO (INTER SA), LOCAL CHANNEL, SHORT HAUL - STF NOT APPLICABLE - STF APPLICABLE | WWGC+ OWGC+ |
| SHORT HAUL MILEAGE -1st ¼ MILE -ADDITIONAL ¼ MILES | JZNOJ JZNOC |
| DIFFERENT CO (INTER SA), LOCAL CHANNEL, LONG HAUL - STF NOT APPLICABLE - STF APPLICABLE | WWGT+ OWGT+ |
| LONG HAUL MILEAGE -FIRST MILE -EACH ADDITIONAL MILE | JZNOX JZNOB |

Note: + Local Channel Suffix Codes

Access Area A = A

Access Area B = B

Access Area C = C

#### Type 2001B

| INTRA-SA CHANNELS SERIES 2001B |
| --- |
| TYPE | USOC |
| LOCAL CHANNELS PBX TO PBX, PER POINT - STF NOT APPLICABLE - STF APPLICABLE - C.O. TERMINATION PBX TO CENTREX, 1 PER TIE LINE -STF NOT APPLICABLE -STF APPLICABLE -CO TERMINANTION CENTREX TO CENTREX, 1 PER TIE LINE - STF NOT APPLICABLE - SECOND CENTREX TERMINATION | WWBD+ OWBD+ CTG WWBE+ OWBE+ CTG WWBF+ CTG |

Note: + Local Channel Suffix Codes

Access Area A = A

Access Area B = B

Access Area C = C

| INTER-SA CHANNELS SERIES 2001B |
| --- |
| TYPE | USOC |
| SHORT HAUL -FIRST ¼ MILE -EACH ADDITIONAL ¼ MILE LOCAL CHANNELS, PBX TO PBX, EACH POINT - STF NOT APPLICABLE - STF APPLICABLE - C.O. TERMINATION PBX TO CENTREX, 1 PER TIE LINE -STF NOT APPLICABLE -STF APPLICABLE -CO TERMINATION CENTREX TO CENTREX, 1 PER TIE LINE - STF NOT APPLICABLE -SECOND CENTREX TERMINATION LONG HAUL BETWEEN SAs -FIRST ¼ MILE -EACH ADDITIONAL ¼ MILE LOCAL CHANNELS, PBX TO PBX, EACH POINT -STF NOT APPLICABLE -STF APPLICABLE -CO TERMINATION LOCAL CHANNELS, PBX TO CTX, EACH POINT -STF NOT APPLICABLE -STF APPLICABLE -CO TERMINATION CTX TO CTX, 1 PER TIE LINE -STF NOT APPLICABLE -SECOND CENTREX TERMINATION SIGNALING ARRANGEMENTS E&M SIGNALING ARRANGEMENTS - ALL NEW PBX TIE LINES BEQUIRE AN E&M SIGNALING ARRANGEMENT. THIS ARRANGEMENT APPLIES AS FOLLOWS AND IS BILLED THE CONTROL END. -PBX TO PBX E&M AT EACH END -PBX TO CTX AT THE PBX, ONLY -CTX TO CTX NOT APPLICABLE | JZNPJ JZNPC WWGD+ OWGD+ CTG WWGE+ OWGE+ CTG WWGF+ CTG JZNPX JZNPB WWGU+ OWGU+ CTG WWGV+ WWGV+ CTG WWGW+ CTG SLM |
| Centrex Terminations |  |
| Common Equipment, per access code | 479 |
| Each Basic Cut-Through Private Line Termination (BPLT). Includes OCC & EPSCS without ACSI | BP1 |
| Each Basic Senderized Private Line Termination (BSPLT). Includes CCSA & OCC | BP2 |
| Each Advanced Senderized Private Line Termination (ASPLT). Includes ETS and Intertandem TLs. | ETX |
| Direct Connect Terminating Feature | TCD |
| Centrex Screening Number | SXMAA |

Note: + Local Channel Suffix Codes

Access Area A = A

Access Area B = B

Access Area C = C

#### Type 2001C

| SAME SA CHANNELS SERIES 2001C |
| --- |
| TYPE | USOC |
| LOCAL CHANNELS/1 PER POINT PBX - STF NOT APPLICABLE - STF APPLICABLE - C.O. TERMINATION | WWBG+ OWBG+ CTG |
| Local Channels / 1 per Point (Centrex) |  |
| STF Applicable | OTVV+ |

| INTRA-SA CHANNELS SERIES 2001C |
| --- |
| TYPE | USOC |
| - TYPE A SIGNALING - TYPE B SIGNALING - TYPE C SIGNALING | X6W1+ X6Y1+ X6Z1+ |

Note: + Local Channel Suffix Codes

Access Area A = A

Access Area B = B

Access Area C = C

| INTER-SA CHANNELS SERIES 2001C |
| --- |
| TYPE | USOC |
| SHORT HAUL MILEAGE -FIRST ¼ MILE -EACH ADDITIONAL ¼ MILE LOCAL CHANNELS – 1 PER POINT -STF NOT APPLICABLE -STF APPLICABLE -CO TERMINATION LONG HAUL MILEAGE -FIRST MILE -EACH ADDITIONAL MILE LOCAL CHANNELS – 1 PER POINT -STF NOT APPLICABLE -STF APPLICABLE -CO TERMINATION | JZNQJ JZNQC WWGG+ OWGG+ CTG JZNQX JZNQB WWGX+ OWGX+ CTG |
| -TYPE A SIGNALING -TYPE B SIGNALING -TYPE C SIGNALING | X6W2+ X6Y2+ X6Z2+ |

Note: + Local Channel Suffix Codes

Access Area A = A

Access Area B = B

Access Area C = C

#### Type 2001D

See Centrex-Off Premise Extensions for USOCs.

| SERIES 2001 MILEAGES |
| --- |
|  | PER MO. |
| SHORT HAUL MILEAGE | FIRST ¼ MILE USOC | ADDITIONAL ¼ MILES USOC |
| TYPE 2001A | JZNOJ | JZNOC |
| TYPE 2001B | JZNPJ | JZNPC |
| TYPE 2001C | JZNQJ | JZNQC |
| TYPE 2001D | JZNRJ | JZNRC |

| SERIES 2001 MILEAGES |
| --- |
|  | PER MO. |
| LONG HAUL MILEAGE | FIRST ¼ MILE USOC | ADDITIONAL ¼ MILES USOC |
| TYPE 2001A | JZNOX | JZNOB |
| TYPE 2001B | JZNPX | JZNPB |
| TYPE 2001C | JZNQX | JZNQB |
| TYPE 2001D | JZNRX | JZNRB |

#### Type 2002

| SAME SERVICE AREA (SA) CHANNELS SERIES 2002 |
| --- |
| TYPE | USOC |
| LOCAL CHANNELS , 2 point, 2 wire each point - STF NOT APPLICABLE - STF Applicable - C.O. TERMINATION 4 WIRE EACH PT - STF NOT APPLICABLE | WWBO+ OWBO+ CTG WWBP+ |
| LOCAL CHANNELS, MULTI-POINT, 2 Wire each point STF NOT APPLICABLE C.O. TERMINATION 4 WIRE EACH POINT - STF NOT APPLICABLE | WWJO+ CTG WWJP+ |

Note: + Local Channel Suffix Codes

Access Area A = A

Access Area B = B

Access Area C = C

| INTER-SA CHANNELS SERIES 2002 |
| --- |
| TYPE | USOC |
| 2 POINT MILEAGE - 2 WIRE SHORT HAUL BETWEEN SAs - 1ST ¼ MILE - EACH ADDITIONAL ¼ MILE 2 WIRE - LONG HAUL BETWEEN SAs - 1ST ¼ MILE - EACH ADDITIONAL ¼ MILE 4 WIRE - SHORT HAUL BETWEEN SAs - 1ST ¼ MILE - EACH ADDITIONAL ¼ MILE 4 WIRE - LONG HAUL BETWEEN SAs - 1ST MILE - EACH ADDITIONAL MILE 2 POINT - LOCAL CHANNELS, 1 TO EACH PT. 2 WIRE EACH PT SHORT HAUL - STF NOT APPLICABLE - C.O. TERMINATION LONG HAUL - STF NOT APPLICABLE - C.O. TERMINATION 4 WIRE EACH PT SHORT HAUL - STF NOT APPLICABLE - C.O. TERMINATION LONG HAUL - STF NOT APPLICABLE - STF APPLICABLE - C.O. TERMINATION MULTI POINT MILEAGE POINT - 1ST ¼ MILE - EACH ADDITIONAL ¼ MILE LONG HAUL BETWEEN SAs - 1ST MILE - EACH ADDITIONAL MILE LOCAL CHANNELS 2 WIRE - STF NOT APPLICABLE 4 WIRE - STF NOT APPLICABLE | JZNEJ JZNEC JZNEX JZNEB JZNSJ JZNSC JZNSX JZNSB WWGO+ CTG WWG3+ CTG WWGP+ CTG WWG4+ OWG4+ CTG JZNXJ JZNXC JZNXX JZNXB WWNO+ WWNP+ |

Note: + Local Channel Suffix Codes

Access Area A = A

Access Area B = B

Access Area C = C

#### Type 2301

| SAME SA CHANNELS SERIES 2301 |
| --- |
| TYPE | USOC |
| LOCAL CHANNELS 2 POINT 2 WIRE INTERFACE EACH PT - STF NOT APPLICABLE - STF APPLICABLE - C.O. TERMINATION 4 WIRE INTERFACE EACH PT - STF NOT APPLICABLE - C.O. TERMINATION | WWEA+ OWEA+ CTG WWEB+ CTG |

Note: + Local Channel Suffix Codes

Access Area A = A

Access Area B = B

Access Area C = C

| INTER-SA - 2 POINT SERIES 2301 |
| --- |
| TYPE | USOC |
| MILEAGE MILEAGE, 2 WIRE SHORT HAUL BETWEEN SAs - 1ST ¼ MILE - EACH ADDITIONAL ¼ MILE LONG HAUL BETWEEN SAs - 1ST ¼ MILE - EACH ADDITIONAL ¼ MILE | JZNMJ JZNMC JZNMX JZNMB |
| MILEAGE, 4 WIRE SHORT HAUL BETWEEN SAs - 1ST ¼ MILE - EACH ADDITIONAL ¼ MILE LONG HAUL BETWEEN SAs - 1ST MILE - EACH ADDITIONAL MILE 2 WIRE SHORT HAUL - STF NOT APPLICABLE - STF APPLICABLE C.O. TERMINATION 2 WIRE LONG HAUL -STF NOT APPLICABLE -STF APPLICABLE -CO TERMINATION 4 WIRE SHORT HAUL -STF NOT APPLICABLE -CO TERMINATION 4 WIRE LONG HAUL -STF NOT APPLICABLE -CO TERMINATION | JZNTJ JZNTC JZNTX JZNTB WWHA+ OWHA+ CTG WWHC+ OWHC+ CTG WWHB+ CTG WWHD+ CTG |
| JOINT USER ARRANGEMENT | JNP |

Note: + Local Channel Suffix Codes

Access Area A = A

Access Area B = B

Access Area C = C

Note: Expedite charges do not apply to Type 2301 channels.

#### Type 2335 – Common Equipment

| Description | USOC |
| --- | --- |
| Primary Bridging Loc – Per Bridging Loc – Common Bridging | BRM |
| Per Port / Master Station Without Filters With Filters | BPE BPG |
| Per Port / Remote Station 2-Wire Interface 4-Wire Interface | BPH2X BPH4X |
| Secondary Bridging Loc – Per Bridging Loc – Common Bridging | BRN |
| Per Port / Remote Station 2-Wire Interface 4-Wire Interface | BPY2X BPY4X |
| Filters – Per Bridging Location Primary and Secondary | FIE |

##### Type 2335 – Same SA – Local Channels

| Description | USOC |
| --- | --- |
| 2-Wire Remote Sta / Same CO as Bridge - STF N/A - STF | WWSO+ OWSO+ |
| 2-Wire Remote Sta / Diff CO than Bridge - STF N/A - STF | WWSD+ OWSD+ |
| Master Sta / 4-Wire Remote Sta / Same CO as Bridge - STF N/A - STF | WWSP+ OWSP+ |
| Master Sta / 4-Wire Remote Sta / Diff CO than Bridge STF N/A STF | WWSF+ OWSF+ |

Local Channel Suffix Codes:

| Access Area A | A |
| --- | --- |
| Access Area B | B |
| Access Area C | C |

##### Type 2335 – Inter SA – Local Channels and Mileage

| Description | USOC |
| --- | --- |
| 2-Wire Remote Sta / Short Haul Mileage - STF N/A - STF Applies | WWTO+ OWTO+ |
| 2-Wire Remote Sta / Long Haul Mileage - STF N/A - STF | WWT3+ OWT3+ |
| Master Sta / 4-Wire Remote Sta / Short Haul Mileage STF N/A STF | WWTP+ OWTP+ |
| Master Sta / 4-wire Remote Sta / Long Haul Mileage STF N/A STF | WWT4+ OWT4+ |
| Mileage |
| 2-wire Interface / Short Haul - 1st ¼ Mile - Ea Add’l ¼ Mile | JZN4J JZN4C |
| 2-wire Interface / Long Haul - 1st ¼ Mile - Ea Add’l ¼ Mile | JZN4X JZN4B |
| 4-wire Interface / Short Haul - 1st ¼ Mile - Ea Add’l ¼ Mile | JZN5J JZN5C |
| 4-wire Interface / Long Haul - 1st ¼ Mile - Ea Add’l ¼ Mile | JZN5X JZN5B |

Local Channel Suffix Codes:

| Access Area A | A |
| --- | --- |
| Access Area B | B |
| Access Area C | C |

#### Type 2336 – Common Equipment Charges

| Description | USOC |
| --- | --- |
| Primary Bridging Loc – Per Port / Per Remote Station 2336 Channel Connected | JM6PX |
| Secondary Bridging Loc – Per Port / Per Remote Station 2336 Channel Connected | JM6SX |

##### Type 2336 – Same SA – Local Channels

Different Bridging Locations Within a Service Area

| Description | USOC |
| --- | --- |
| STF N/A | WWMA+ |

##### Type 2336 – Inter SA – Local Channels and Mileage

| Description | USOC |
| --- | --- |
| Short Haul Mileage / STF Applicable | WWPA+ |
| Long Haul Mileage / STF N/A | WWPB+ |
| Mileage |  |
| Short Haul Mileage - 1st ¼ Mile - Ea Add’l ¼ Mile | JZN6J JZN6C |
| Long Haul - 1st ¼ Mile - Ea Add’l ¼ Mile | JZN6X JZN6B |

Local Channel Suffix Codes:

| Access Area A | A |
| --- | --- |
| Access Area B | B |
| Access Area C | C |

### Indiana

#### Type 2001

Continuous Property Terminations:

| INTRA-EXCHANGE SERIES 2001 CS - PLYVL (PL, PG, OI, VM, PM) |
| --- |
| TYPE | USOC |
| SAME BUILDING BUILDING CHANNEL TERMINATION (ONE AT EACH POINT) | 2SESZ |
| DIFFERENT BUILDING BUILDING CHANNEL TERMINATION (ONE AT EACH POINT) | 2SESZ |
| CONTINUOUS PROPERTY CHANNEL 10,000 FEET OR LESS OVER 10,000 FEET | 1LPA1 1LPA2 |
| GRANDFATHERED ITEM: MULTI-STATION (ON PREMISE BRIDGE) | MPGSX |

Non-Continuous Property Terminations:

| SERIES 2001 CS - PLYVL (PL, PG, OI, VM, PM) |
| --- |
| TYPE | USOC |
| SAME C.O. LOCAL CHANNEL (ONE PER PREMISES) | 1SESZ |
| CENTRAL OFFICE TERMINAL (FOR CENTREX END) | TTM |
| FOR ADDITIONAL TERMS AT SAME LOCATION AS A LOCAL CHANNEL SAME BUILDING EXTENSION (PER ADDITIONAL POINT) | 4SESZ |
| DIFFERENT BUILDING EXTENSION (PER ADDITIONAL POINT) | 4SESZ |
| CONTINUOUS PROPERTY CHANNEL (BETWEEN BUILDINGS) 10,000 FEET OR LESS OVER 10,000 FEET | 1LPB1 1LPB2 |
| MULTI-STATION (GRANDFATHERED) | MPGSX |
| DIFFERENT C.O. LOCAL CHANNEL (ONE PER PREMISES) INTEROFFICE CHANNEL (PER MILE)* INTEROFFICE CHANNEL TERMINATION (1 AT EACH END OF IO CHANNEL) | 1SESZ 1LPBS 2LH |
| OTHER MULTI-POINT (EQUAL TO NUMBER OF LOCAL CHANNELS WHEN 3 OR MORE) AUTOMATIC SIGNALING (ONLY FOR PL, PG, OI PER LOCAL CHANNEL 2-POINT CIRCUIT ONLY) | MPA 27M |

Note: *Plus T&M

##### Non-Continuous Property:

| INTER-EXCHANGE SERIES 2001 - CS FPSVS (PL, PG, OI, VM, PM) |
| --- |
| TYPE | USOC |
| IX MILEAGE 1-40 MILES (PER MILE) 41+ MILES (PER MILE) | 1LPA4 1LPA4 |
| IX CHANNEL TERMINATION 1-40 MILES 41+ MILES | P1N P3N |
| LOCAL CHANNEL (1 AT EACH CUSTOMER PREMISE) | 1SESZ |
| CUSTOMER NOT IN RATE CENTER, ADD: INTEROFFICE CHANNEL (PER MILE) INTEROFFICE CHANNEL TERMINATION (ON AT EACH END) | 1LPAS P2J |
| FOR ADDITIONAL TERMS AT SAME LOCATION CHANNEL EXTENSION (EACH ADDITIONAL TERMINATION) CONTINUOUS PROPERTY CHANNEL (BETWEEN BUILDINGS) 10,000 FEET OR LESS OVER 10,000 FEET MULTI-STATION (GRANDFATHERED) | 4SESZ 1LPA1 1LPA2 MPGSX |
| OTHER MULTI-POINT (EQUAL TO NUMBER OF LOCAL CHANNELS WHEN 3 OR MORE) AUTOMATIC SIGNALING (PER LOCAL CHANNEL) 2-POINT CIRCUIT ONLY | MPA 27M |

| INTRA-EXCHANGE SERIES 2001 OFF PREMISES EXTENSIONS (OP) |
| --- |
| Type | USOC |
| Same CO, same or different building NCP | EXF |
| Same CO, Local Channel, per line | LCASZ |
| Same CO, Grandfathered Extensions* | NW3 |
| Different CO, Local Channel, per line | LCASZ |
| Interoffice Channel Mileage, each mile or fraction | 1LLBS |
| Interoffice Channel Mileage Termination, one at each end of IO Channel | 2LK |

Note:  *Effective 1/15/91, extensions served by separate facilities are considered non-continuous property.  Extensions installed before 1/15/91 are grandfathered.

#### Type 2002

| INTRA-EXCHANGE SERIES 2002 CS: OMRVL (RT) |
| --- |
| Type | USOC |
| Local Distribution Channel (1 at each premise) | 1SESZ |
| Interoffice Channel Mileage (per mile) | 1L1MS |
| Interoffice Channel Mileage Termination (1 at each end of IO Channel) | P2J |
| Extension | 4SESZ |
| Building Channel Termination | 2SESZ |
| Continuous Property Channel 1 to 10,000 ft Over 10,000 ft | 1L1M1 1L1M2 |
| Multi-Point Charge | MPA |
| Multi-Station Charge (Grandfathered) | MSV++ |

| INTER-EXCHANGE SERIES 2002 CS: OMRVS (RT) |
| --- |
| Type | USOC |
| Local Distribution Channel | 1SESZ |
| InterExchange Channel Mileage 1 to 40 miles 41 + miles | 1L314 1L314 |
| InterExchange Channel Mileage Termination - 1 to 40 miles - 41 + miles | P1N P3N |
| Customers not in Rate Center (except for Contiguous exchanges), add: - Interoffice Channel Mileage 1L31S(per mile) | 1L31S |
| Interoffice Channel Mileage Termination (1 at each end of IO Mileage) | 2LH |
| Extension | 4SESZ |
| Continuous Property Channel 1 to 10,000 ft Over 10,000 ft | 1L1M1 1L1M2 |
| Multi-Point Charge | MPA |
| Multi-Station Charge (Grandfathered) | MSV++ |

#### Type 2014

| INTRA-EXCHANGE SERIES 2014 CS: PVLLL (OS) |
| --- |
| Type | USOC |
| Same CO – Local Channel (1 at each premise) | LCQSZ |
| Different CO – Local Channel (per line) (one at each premise) | LCQSZ |
| Different CO – Interoffice Channel Mileage each mile or fraction | 1LVBS |
| Different CO – Interoffice Channel Mileage Termination (one at each end of IO Channel) | 2LK |

| INTER-EXCHANGE SERIES 2014 CS: PVLLS (OS) |
| --- |
| Type | USOC |
| IX Mileage - 0 to 40 miles (per mile or fractions) - 41 + miles | 1LVA4 1LVA4 |
| IX Channel Mileage Termination (one at each end of IX) 0 to 40 miles 41 + miles | P1N P3N |
| Local Distribution Channel (one at each premises) | 1SESZ |
| Customer not in Rate Center add Interoffice Channel (per mile) | 1LVAS |
| Customer not in Rate Center add Interoffice Channel Termination (one at each end of IO channel) | P2J |
| For additional terminations at same location as a local channel, continuous property channel (between buildings) 10,000 feet or less over 10,000 feet | 1LVA1 1LVA2 |

| INTRA & INTER-EXCHANGE SERIES 2014 SIGNALING ARRANGEMENTS |
| --- |
| Type | USOC |
| Type A (OL13A) 0 to 199 Ohms | SAL |
| Type B (OL13B) 200 to 899 Ohms | SAU |
| Type C (OL13C) 900 and higher Ohms | SAY |

#### Type 2021

##### PBX to PBX

| RATES INTRA-EXCHANGE SERIES 2021 CS - PTBVL (TL, TA, IT, SA) |
| --- |
| TYPE | USOC |
| CONTINUOUS PROPERTY SAME BUILDING BUILDING CHANNEL TERMINATION (ONE AT EACH POINT) DIFFERENT BUILDING BUILDING CHANNEL TERMINATION (ONE AT EACH POINT) CONTINUOUS PROPERTY CHANNEL (BETWEEN BUILDINGS) 10,000 FEET OR LESS OVER 10,000 FEET | 2SES** 2SES** 1LTB1 1LTB2 |
| NON-CONTINUOUS PROPERTY*** SAME C.O. LOCAL CHANNEL (ONE AT EACH POINT) DIFFERENT C.O. LOCAL CHANNEL (PER LOCATION) INTEROFFICE CHANNEL (PER MILE) - SEE MILEAGE SECTION INTEROFFICE CHANNEL TERMINATION (1 AT EACH END OF IO CHANNEL) E&M SIGNALING | 1SESZ 1SESZ 1LTBS 2LK SLM |

Note: ** Q - CPE equipment. Use on all orders

*** E&M Signaling required per termination on all non-continuous property connections.

| INTEREXCHANGE PBX CONNECTED TO PBX SERIES 2021 CS - PTBVS (TL, TA, IT, SA) |
| --- |
| TYPE | USOC |
| IX MILEAGE FIRST 40 MILES (PER MILE) 41+ MILES (PER MILE) IX CHANNEL TERMINATION (1 AT EACH END OF IX) 1-40 MILES 41+ MILES LOCAL CHANNEL (1 AT EACH CUSTOMER PREMISE) CUSTOMER NOT LOCATED IN RATE CENTER, ADD: INTEROFFICE CHANNEL (PER MILE - SEE MILEAGE SECTION) INTEROFFICE CHANNEL TERMINATION (1 AT EACH END OF IO CHANNEL) | 1LTE4 1LTE4 P1N P3N 1SESZ 1LTAS 2LK SLM |

#### Type 2026

| CENTREX CO CONNECTED TO CENTREX CO SERIES 2026 CS - PTBCL (TL, TA, IT, SA) |
| --- |
| TYPE | USOC |
| NON-CONTINUOUS PROPERTY SAME C.O. C.O. TERMINATION (ONE PER CENTREX, PER TIE LINE) DIFFERENT C.O. INTEROFFICE CHANNEL (PER MILE - SEE MILEAGE SECTION) INTEROFFICE CHANNEL TERMINATION (1 AT EACH END OF IO CHANNEL) C.O. TERMINATION* (1 PER CENTREX, PER TIE LINE) Centrex Screening Number | PMN 1LTFS 2LK PMN SXMAA |

Note: * Information relating to additional charges for the Centrex Tie Line Terminations and order issuance will be found in the Centrex M&P.

| CENTREX CO CONNECTED TO CPE PBX SERIES 2021, 2026 CS - PTBVL (TL, TA, IT, SA) |
| --- |
| TYPE | USOC |
| NON-CONTINUOUS PROPERTY SAME C.O. PBX LOCATION - LOCAL CHANNEL E&M SIGNALING CENTREX C.O. - C.O. TERMINATION DIFFERENT C.O. PBX LOCATION - LOCAL CHANNEL INTEROFFICE CHANNEL (PER MILE - SEE MILEAGE SECTION) INTEROFFICE CHANNEL TERMINATION (1 AT EACH END OF IO CHANNEL) E&M SIGNALING CENTREX C.O.** TERMINATION Centrex Screening Number | 1SESZ SLM PMN 1SESZ 1LTBS 2LK SLM PMN SXMAA |

Note: ** Information relating to additional charges and order issuance for the Centrex Tie Line Terminations will be found in the Centrex M&P.

Non-Continuous Property:

| CENTREX CO TO CENTREX CO, CENTREX CO TO PBX SERIES 2021, 2026 CS - PTBCS (TL, TA, IT, SA) |
| --- |
| TYPE | USOC |
| IX MILEAGE FIRST 40 MILES (PER MILE) 41+ MILES (PER MILE) IX CHANNEL TERMINATION (1 AT EACH END OF IX) 1-40 MILES 41+ MILES CO TERMINATION (PER CTX-CO) LOCAL CHANNEL (APPLIES PER PBX END) E&M SIGNALING REQUIRED AT PBX END CUSTOMER NOT LOCATED IN RATE CENTER, ADD: INTEROFFICE CHANNEL (PER MILE) INTEROFFICE CHANNEL TERMINATION (1 AT EACH END) Centrex Screening Number | 1LTE4 1LTE4 P1N P3N PMN 1SESZ SLM 1LTES P2J SXMAA |

### Michigan

#### Direct Analog – VG32

| Burglar & Fire Alarm (Non-Morse) – 2 Way Radio Traffic Signal, Telemetering, Wired Music and Electrowriter CS: XZV2+ |
| --- |
| Description | USOC |
| 2 Wire Local Channel (half duplex) | T6E2X |
| 4 Wire Local Channel (full duplex) and 6 Wire | T6E4X |
| Inter Wire Center Mileage | 1L5XX |
| 2 Wire Bridging | BCNV2 |
| 4 Wire Bridging | BCNV4 |
| Channel Termination | CM6 |

| Mobile Radio Telephone – 2 Way Radio – Additional Terminal CS: XZV2+ |
| --- |
| Description | USOC |
| 2 Wire Local Channel (half duplex) | T6E2X |
| Inter Wire Center Mileage | 1L5XX |
| Channel Termination | CM6 |
| Signaling Per LDC | XSS++ |
| Route Direct | CPD |

Note:  ++ 4th and 5th Character – Signaling USOC variable derived from 3rd and 4th character of NCI code.  See NC/NCI.

| Mobile Radio Telephone Channel – Dispatch Service – Private Line CS: XZV2+ |
| --- |
| Description | USOC |
| 2 Wire Local Channel (half duplex) | T6E2X |
| 4 Wire Local Channel (full duplex) and 6 Wire | T6E4X |
| Inter Wire Center Mileage | 1L5XX |
| 2 Wire Bridging | BCNV2 |
| 4 Wire Bridging | BCNV4 |
| Channel Termination | CM6 |
| Signaling Per LDC Private Line only | XSS++ |

Note:  ++4th & 5th Character – Signaling USOC derived from 3rd and 4th character of NCI code.  See NC/NCI.

| Voice, Dry Pair, Hoot & Holler CS: XZV2+ |
| --- |
| Description | USOC |
| 2 Wire Local Channel (half duplex) | T6E2X |
| 4 Wire Local Channel (full duplex) | T6E4X |
| Channel Mileage per mile | 1L5XX |
| 2 Wire Bridging | BCNV2 |
| 4 Wire Bridging | BCNV4 |
| Channel Termination | CM6 |
| Route Direct | CPD |

| Toll Terminals CS: XZV2+ |
| --- |
| Description | USOC |
| 2 Wire Local Channel (half duplex) | T6E2X |
| 2 Wire Local Channel (nonbilled)** | FCKSA |
| Channel Mileage per mile | 1L5XX |
| Channel Mileage (nonbilled)** | 1LWV9 |
| Channel Termination | CM6 |
| Signaling Per LDC | XSS++ |

Note:  ++ 4th & 5th Character Signaling USOC variable derived from 3rd and 4th character of NCI code.  See NC/NCI.

Note:  ** When service cannot be provided from the end user’s LSO, apply non-billed USOCs.  When end user requests service from an FSO, then all billable rate elements apply.

| Break Hunt |
| --- |
| Description | USOC |
| Break Hunt* | BRR |
| Make Busy* | P89 |
| Local Distribution Channel % | T6E2X |

Note:  * Not available with statewide 800 service

% All new service must use this channel

| Continuous Property Extensions |
| --- |
| Description | USOC |
| Less Than 528 Feet | None* |
| More than 528 Feet, Non-Continuous Property, Same CO: |
| Off Premises Extension | EXF |
| 2-Wire Local Distribution Channel (LDC) | T6E2X |
| Surcharge -Exemption** | S25 S25EX |

Note:  *Handle as deregulated inside wire and jack.

** OPX end user is exempt from surcharge because of direct interconnection to local exchange network via main telephone number.  Surcharge Exemption Letter is required.

| Non-Continuous Property to Different CO/Different Exchange (Inter-Wire Center) |
| --- |
| Description | USOC |
| Off Premises Extension | None |
| 2 Wire Local Distribution Channel (2 required if different exchanges) | T6E2X |
| Channel Mileage per mile | 1L5XX |
| Channel Mileage Termination | CM6 |
| Signaling Per LDC | XSSLS |
| Surcharge, per Circuit -Exemption | S25 S25EX |

| Tie Line (VG – 32) CS: XZV3+ |
| --- |
| Description | USOC |
| 4 wire LDC | T6E4X |
| Channel Mileage, per mile | 1L5XX |
| Channel Mileage Termination | CM6 |
| E&M Signaling, per LDC | XSS+ |
| Route Direct | CPD |
| Centrex Screening Number | SXMAA |
| Centralized Automatic Reporting on Trunks (CAROT) | PKT # |
| Surcharge, per Circuit -Exemption | S25 S25EX |

Note:  # Centrex station line that requires a LCC, PIC, ZPIC, etc.

| PBX Off Premises Stations CS: XZV2+ |
| --- |
| Description | USOC |
| 2 Wire Local Distribution Channel (LDC) | T6E2X |
| Channel Mileage per mile | 1L5XX |
| Channel Mileage Termination | CM6 |
| Signaling Per LDC | XSS++* |
| Route Direct | CPD |

Note:  *Determine USOC as follows:

| If /NCI at /CKL 1 is: | Then Signaling USOC is: |
| --- | --- |
| 02LA2 | XSSLA |
| 02LB2 | XSSLB |
| 02LC2 | XSSLC |

### Ohio

#### Type 2001

| INTRA-EXCHANGE SERIES 2001 - CS FPSVL |
| --- |
| TYPE | USOC 2-WIRE | USOC 4-WIRE |
| SAME CO LOCAL CHANNEL SAF, per local channel | 1LPJJ OPMPS | 1LPNJ OPMPS |
| DIFFERENT CO LOCAL CHANNEL SAF, per local channel INTEROFFICE CHANNEL MLG | 1LPJJ OPMPD 1LPJS | 1LPNJ OPMPD 1LPNS |
| SIGNALING AUTOMATIC RING EQUIPMENT | 47R | 47R |
| Same Continuous Property* | UA7NA | UA7NA |

Note:  *Deregulated inside wire

| INTER-EXCHANGE SERIES 2001 - CS FPSVS |
| --- |
| TYPE | USOC 2-WIRE | USOC 4-WIRE |
| INTEREXCHANGE CHANNEL MILEAGE | 1LPJ4 | 1LPNJ4 |
| INTEROFFICE CHANNEL MILEAGE | 1LPJS | 1LPNS |
| SERVICE TERMINAL | P3N | P3N |
| DIFFERENT EXCHANGE - LOCAL CHANNEL - SAF | 1LPJJ OPMPX | 1LPNJ OPMPX |
| Same Continuous Property* | UA7NA | UA7NA |

Note:  *Deregulated inside wire

##### Signaling and Switching Arrangements:

| INTRA & INTER-EXCHANGE SERIES 2001 - CS FPSVL & FPSVS |
| --- |
| TYPE | USOC |
| AUTOMATIC RINGING ONE-WAY OR-TWO-WAY SINGLE RING ARRANGEMENT WHERE TWO-POINT SERVICE TERMINATES | 27M |
| AUTOMATIC SIGNALING PER LOCAL SERVICE AREA CHANNEL | 47R |
| AUTOMATIC INTERMITTENT SIGNAL ONE WAY AUTO/KEY SIGNALING TWO WAY AUTO SIGNALING | TL5 27L |

#### Type 2002

| INTRA-EXCHANGE SERIES 2002 - CS OMRVL |
| --- |
| TYPE | USOC 2-WIRE | USOC 4-WIRE |
| SAME CO LOCAL CHANNEL SAF | 1L1MJ OPMAW | 1L1FJ OPMAW |
| DIFFERENT CO LOCAL CHANNEL SAF INTEROFFICE CHANNEL MLG | 1L1MJ OPMAX 1L1MS | 1L1FJ OPMAX 1L1MS |
| Same Continuous Property* | UA7NA | UA7NA |

Note:  *Deregulated inside wire

#### Type 2013

| INTRA/INTEREXCHANGE SERIES 2013 - CS PYCL+ |
| --- |
| TYPE | USOC 2-WIRE |
| SAME CO LOCAL CHANNEL SAF* | 1LVJJ OPMBA |
| DIFFERENT CO LOCAL CHANNEL SAF* MILEAGE TERMINATION, 2 APPLY @ | 1LVJJ OPMBB CM6 |
| DIFFERENT EXCHANGE LOCAL CHANNEL SAF* | 1LVJJ OPMBC |
| INTEROFFICE CHANNEL PER MILE | 1LVJS |
| INTEROFFICE CHANNELS, PER MILE @ | 1L5XX |
| INTEREXCHANGE CHANNEL PER MILE | 1LVJ4 |
| INTER-EXCHANGE SERVICE TERMINAL (BETWEEN 2 DIFFERENT RATE CENTERS), 2 APPLY | P3N |

Note:  *One per channel

@Optinet Base Rate Only

#### Type 2014

| INTRA/INTEREXCHANGE SERIES 2014 – CS PYCL+ |
| --- |
| TYPE | USOC 2-WIRE |
| SAME CO LOCAL CHANNEL SAF* | 1LVJJ OPMBD |
| DIFFERENT CO LOCAL CHANNEL SAF* MILEAGE TERMINATION, 2 APPLY @ | 1LVJJ OPMBE CM6 |
| DIFFERENT EXCHANGE LOCAL CHANNEL SAF* | 1LVJJ OPMBF |
| INTEROFFICE CHANNEL PER MILE | 1LVJS |
| INTEROFFICE CHANNELS, PER MILE @ | 1L5XX |
| INTEREXCHANGE CHANNEL PER MILE | 1LVJ4 |
| INTEREXCHANGE SERVICE TERMINAL (BETWEEN 2 DIFFERENT RATE CENTERS), 2 APPLY | P3N |

Note:  *One per channel

@ Optinet Base Rate Only

Signaling and Switching Arrangements:

| INTRA/INTEREXCHANGE SERIES 2014 - CS PYCL+ |
| --- |
| TYPE | USOC |
| TYPE A WITH CLASS A PBX STATION PORTS IN RANGE OF 0-189 OHMS | SAL |
| TYPE B WITH CLASS A PBX STATION PORTS IN RANGE OF 220-889 OHMS | SAU |
| TYPE C WITH CLASS A PBX STATION PORTS IN RANGE OF 900+ OHMS | SAY |

#### Type 2020, 2021, 2024, 2025 and 2026

| INTRA/INTEREXCHANGE SERIES 2020, 2021, 2024, 2025 |
| --- |
| TYPE | USOC |
| Local Channels, one for each end -PBX -Centrex | 1LTBJ 1LTF8 |
| SAF -Same CO -Different Co -Different Exchange | No Signaling OPOBN OPOBO OPOBP | With Signaling OPOBQ OPOBR OPOBS |
| Signal Arrangements -E&M -Dial Signaling on InterExchange Service | SLM * 27E++ ** |
| InterOffice Channel Mileage -No Signaling -With Signaling | 1LTBS 1LTBS |
| InterExchange Channel Mileage (per mile) -No Signaling -With Signaling | 1LTB4 1LTB4 |
| Service Terminal (IXC) | P3N |

Note:  * Need one per each PBX end of the Tie Line

**For IXC Service, need one for each end of the PBX and Centrex

#### Miscellaneous Tie Line USOCs

| Description | USOC | Requirements |
| --- | --- | --- |
| Advanced Private Line | PLS | With Centrex 100 only |
| Centrex Switching Equipment – Facilities used with Tie Lines connecting Centrex switching equipment of primary location and switching equipment of secondary location. | RXNA | None |
| Intercom of Centrex system with Centrex Stations – Automatic Dial | RXN | With Centrex 100 only –RXN |
| Intercom of CTX system with CTX stations plus facilities terminating in CTX switch equipment or attendant positions. – Automatic for College Dorms | RXND | With Centrex 100 only – TLS |
| Intercom of CTX system with CTX stations plus facilities terminating in CTX switch equipment or attendant positions. – Automatic for All Others | TLS | With Centrex 100 only - TSY |
| Intercom of CTX system with CTX stations plus facilities terminating in CTX switch equipment or attendant positions. – Automatic/dial | TSY | With Centrex 100 only - TLSFP |
| Intercom of CTX system with CTX stations plus facilities terminating in CTX switch equipment or attendant positions. – Automatic Unrestricted Station Terminal | TCV | With Centrex 100 only - TCVFB |
| Station terminal in use: in conjunction with CTX Interexchange Tie Line | RFN | None |
| PBX Manual – Cord Switchboard Attendant Position (grandfathered) | YDM | N/A |
| PBX Dial Attendant Control – Console | EJN | N/A |
| PBX Dial Attendant Control – Cord Switchboard (Grandfathered) | YDM | N/A |
| PBX Dial Attendant Control – Incoming | EJS | N/A |
| PBX Dial Attendant Control – Outgoing | EJL | N/A |
| PBX Dial Attendant Control – Incoming & Outgoing | EJT | N/A |
| ETS type line with Centrex and PBX | EXT | N/A |

#### Off Premises Extension

| Non-Continuous and Continuous Property |
| --- |
| Type | USOC |
| Non-Continuous Property, Same CO Local Channel SAF, one per end | 1LLBJ OPEXX |
| Non-Continuous Property, Different CO Local Channel SAF, one per end Interoffice Channel Mileage, per mile | 1LLBJ OPUYY 1LLBS |
| Continuous Property – handled as deregulated jack and wire |

### Wisconsin

#### Type 2001

| INTRA OR INTER-EXCHANGE SERIES 2001 - CS PLYV+ |
| --- |
| TYPE | USOC |
| SAME WIRE CENTER (WWC) - INITIAL ¼ MILE - SUBSEQUENT ¼ MILE | 1L9X6 1L9X6 |
| DIFFERENT WIRE CENTER (IWCC) - INITIAL MILE - SUBSEQUENT MILE | 1LN2X 1LN2X |
| LOCAL DISTRIBUTION CHANNEL (PER CHANNEL) - INITIAL ¼ MILE SUBSEQUENT ¼ MILE PROVISIONING ONLY – SAME CO, CKL 2 2 WIRE, 2 POINT 4 WIRE, 2 POINT | 1LD2J 1LD2J AS32X AS34X |
| MULTI-POINT OPTION 1 | MPY1X |

+ = L, INTRAEXCHANGE S = INTEREXCHANGE

| SERIES 2001 - LINE POWER |
| --- |
| CHANNEL TYPE | CHANNEL ELEMENT | USOC |
| 2001 | SAME WC DIFFERENT WC | PWG1X PWG2X |

##### Signaling

| SERIES 2001 - Signaling |
| --- |
| Type | USOC |
| Manual ring-down, per channel | SL31X |
| Automatic ring-down, per channel | YY81X |

#### Type 2002

| INTRA OR INTER-EXCHANGE SERIES 2002 - CS PLYV+ |
| --- |
| TYPE | USOC |
| SAME WIRE CENTER (WWC) - INITIAL ¼ MILE - SUBSEQUENT ¼ MILE | 1L9X7 1L9X7 |
| DIFFERENT WIRE CENTER (IWCC) - INITIAL MILE - SUBSEQUENT MILE | 1LN4X 1LN4X |
| LOCAL DISTRIBUTION CHANNEL (PER CHANNEL) - INITIAL ¼ MILE SUBSEQUENT ¼ MILE Provisioning Only, Same CO, CKL 2 -2 Wire, 2 Point -4 Wire, 2 Point | 1LD4J 1LD4J AS32X AS34X |
| MULTI-POINT OPTION 1 PER LDC | MPY2X |

+ = L, INTRAEXCHANGE S = INTEREXCHANGE

#### Type 2003

| INTRA OR INTER-EXCHANGE SERIES 2003 - CS OMRV+ |
| --- |
| TYPE | USOC |
| SAME WIRE CENTER (WWC) - INITIAL ¼ MILE - SUBSEQUENT ¼ MILE | 1L9X6 1L9X6 |
| DIFFERENT WIRE CENTER (IWCC) - INITIAL MILE - SUBSEQUENT MILE | 1LN2X 1LN2X |
| LOCAL DISTRIBUTION CHANNEL (PER CHANNEL) - INITIAL ¼ MILE SUBSEQUENT ¼ MILE Provisioning Only, Same CO, CKL 2 -2 Wire, 2 Point -4 Wire, 2 Point | 1LD2J 1LD2J AS32X AS34X |
| MULTI-POINT OPTION 1 PER LDC | MPY1X |

+ = L, INTRAEXCHANGE S = INTEREXCHANGE

#### Type 2004

| INTRA OR INTER-EXCHANGE SERIES 2004 - CS OMRV+ |
| --- |
| TYPE | USOC |
| SAME WIRE CENTER (WWC) - INITIAL ¼ MILE - SUBSEQUENT ¼ MILE | 1L9X7 1L9X7 |
| DIFFERENT WIRE CENTER (IWCC) - INITIAL MILE - SUBSEQUENT MILE | 1LN4X 1LN4X |
| LOCAL DISTRIBUTION CHANNEL (PER CHANNEL) - INITIAL ¼ MILE SUBSEQUENT ¼ MILE Provisioning Only, Same CO, CKL 2 -2 Wire, 2 Point -4 Wire, 2 Point | 1LD4J 1LD4J AS32X AS34X |
| MULTI-POINT OPTION 1 (IWCC) PER LDC | MPY2X |

+ = L, INTRAEXCHANGE S = INTEREXCHANGE

#### Type 2005

| TYPE | USOC |
| --- | --- |
| SAME WIRE CENTER (WWC) - INITIAL ¼ MILE - SUBSEQUENT ¼ MILE | 1L9X6 1L9X6 |
| DIFFERENT WIRE CENTER (IWCC) - INITIAL MILE - SUBSEQUENT MILE | 1LN2X 1LN2X |
| LOCAL DISTRIBUTION CHANNEL (PER CHANNEL) - INITIAL ¼ MILE - SUBSEQUENT ¼ MILE | 1LD2J 1LD2J |

+ = L, INTRAEXCHANGE S = INTEREXCHANGE

##### Signaling

| SERIES 2001 - SIGNALING |
| --- |
| Type | USOC |
| Loop Type A, per channel | SAL1X |
| Loop Type B, per channel | SAU1X |
| Loop Type C, per channel | SAY1X |

#### Type 2006

| Type | USOC |
| --- | --- |
| Continuous Property Extension Routed via the Central Office: 1/10 mile or less 1/10 mile or more | 1LDVD 1LDVE |
| Non-Continuous Property Inter-Wire Center Channel (IWCC): First Mile Each additional mile | 1LNVX 1LNVX |
| Non-Continuous Property Local Distribution Channel (LDC) First ¼ Mile Each additional ¼ mile | 1LDVJ 1LDVJ |
| Station Bridging | EHA |

#### Type 2010

| TYPE | USOC |
| --- | --- |
| DIFFERENT WIRE CENTER (IWCC) - INITIAL MILE - SUBSEQUENT MILE | 1LN4X 1LN4X |
| LOCAL DISTRIBUTION CHANNEL (PER CHANNEL) - INITIAL ¼ MILE - SUBSEQUENT ¼ MILE | 1LD4J 1LD4J |
| E&M Signaling | SLM1X |
| Centrex Screening Number | SXMAA |

* CO - PREM PTBC+

CO - CO PTBT+

PREM - PREM PTBV+

+ = L, INTRAEXCHANGE S = INTEREXCHANGE

## FIDs

| FID | Description |
| --- | --- |
| CKL | Circuit Location Example: CKL 1-1234 Any Av, My Town, AA Order Placement: Not Required |
| CLS | Common Language Circuit Identification – Serial Number Format Example: .AAAA.#####..AA Order Placement: ECCKT Field |
| CLT | Common Language Circuit Identification – Telephone Number Format Example: .FXNA.NPA.NXX.XXXX..A Order Placement: ECCKT Field |
| DPA | Different Premises Address – Indicates that the line terminates at another address as well as the main location and provides that address information. Example: DPA 1-1234 Any Av, My Town, AA Order Placement: FEATURE DETAIL field following the line assignable USOC in the FEATURE field. |
| FIC | Facility Interface Code – Indicates the translation to the network channel interface for CPE. Example: /FIC OL13C Order Placement: Resale Private Line Form in feature detail field. |
| FSO | Foreign Serving Office – Identifies that service is provided from a Central Office that does not normally serve the street address. Example: NPA NXX Order Placement: FSO Field on Resale Private Line Form. |
| LOC | Location (Floor/Room Number, etc) – Indicates the location within the building where the line terminates. Example: /LOC Suite 1234 Order Placement: FEATURE DETAIL Field following the line assignable USOC in the Feature field. |
| LSO | Local Serving Office Example: NPA NXX Order Placement: LSO Field on Resale Private Line form |
| NC | Network Channel – Required on Michigan orders only. Example: .UGPA.######..MB/NC UG- Order Placement: NC Field on Resale Private Line form |
| NCI | Network Channel Interface Code – Required on Michigan orders only. Example: CKL 1-225 N Randolph, Grand Rapids, MI/NCI 02DA2 Order Placement: NCI and SECNCI Fields on Resale Private Line Form. |
| SCS and ZSCS | Secondary Class of Service – Indicates a Class of Service different from the main class of service. Example: SCS LDCDL Order Placement: STOS Field on Resale Private Line Form. |
| SGN | Segment Number – Indicates the segments in a multipoint circuit which carries a Common Language Circuit Identification (CLCI). Example: USOC/CKL 3-609 N Grand, Indpls, IN/SGN C Order Placement: Not required |

## NC/NCI

Important: NC and NCI codes are required on orders in the state of Michigan.

### VG32 – Formerly Type 1

| Circuit Description | NC Code |
| --- | --- |
| Standard 2 point | UC-- |
| Bridging (Multipoint) | UC-B |

### VG32 – Formerly Voice Dry Pair, Hoot & Holler

| Circuit Description | NC Code |
| --- | --- |
| Standard 2 point | UC-- |
| Bridging (Multipoint) | UC-B |

### VG32 – Voice Burglar & Fire Alarm (non-Morse), Two-Way Radio, Traffic Signal, Telemetering, Wired Music, Electrowriter

| Circuit Description | NC Code |
| --- | --- |
| Standard 2 point | UC-- |
| Bridging (Multipoint) | UC-B |
| Data Capability | UCD- |

### VG32 – Toll Terminal and Mobile Radio Telephone, Two-Way Radio – Additional Terminal

| Circuit Description | NC Code |
| --- | --- |
| Standard 2 point | UC-- |
| Data Capability | UCD- |

### VG32 – PBX Off Premises Station

| Circuit Description | NC Code |
| --- | --- |
| Standard | UC-- |
| Data Capability | UDC- |

### VG32 – Off Premises Extension

| Circuit Description | NC Code |
| --- | --- |
| Standard 2 point | UC-- |
| Data Capability | UDC- |

### VG – Tie Lines

| Circuit Description | NC Code |
| --- | --- |
| Standard | UD-- |
| Data Capability | UDD- |

## NCI Codes

### VG32 – Formerly Type 1 – (PL)

| Circuit Description | NC Code for CKL 1,2 & 3 |
| --- | --- |
| Auto Ringdown | 02LR2 |
| Manual Ringdown 2 Wire | 02AC2 |
| Manual Ringdown 4 Wire | 04AC2 |
| Code Select 2W Multipoint | 02AC2.R |
| Code Select 4W Multipoint | 04AC2.R |
| No Signaling – 2W | 02NO2 |
| No Signaling – 4W | 04NO2 |

### VG32 – Formerly Type 1 – (RT)

| Circuit Description | NC Code for CKL 1, 2 & 3 |
| --- | --- |
| 2W Interface | 02NO2 |
| 4W Interface | 02NO2 |

### VG32 – Formerly Type 1 – (PL & RT) Bridging

| Circuit Description | NC Code for CKL 1, 2 & 3 |
| --- | --- |
| Conference | 04BR2.CF |
| Non Conference 1 way or 2 way Transmission | 04BR2.SP |
| Auto Ringdown when multipoint | 02BT2 |

### VG32 – Formerly Voice Dry Pair, Hoot & Holler

| Circuit Description | NC Code for CKL 1, 2 & 3 |
| --- | --- |
| 2W Interface | 02NO2 |
| 4W Interface | 04NO2 |

### VG32 – Formerly Voice Dry Pair, Hoot & Holler-Bridging

| Circuit Description | NC Code for CKL 1, 2 & 3 |
| --- | --- |
| Conference | 04BR2.CF |
| Non Conference 1 way or 2 way Transmission | 04BR2.SP |

### VG32 – Voice Burglar & Fire Alarm (non-Morse), Two Way Radio, Traffic Signal, Telemetering, Wired Music, Electrowriter

| Circuit Description | NC Code for CKL 1, 2 & 3 |
| --- | --- |
| 2W Interface – One Way – CKL 1 to CKL 2 | 02NO2..0- 02NO2..-0 |
| 2W Interface – One Way – CKL 2 to CKL 1 | 02NO2..-0 02NO2..0- |
| 2W Interface – Two Way – All circuits | 02NO2 |
| 4W Interface – All Circuits | 04NO2 |
| 6W Interface – All Circuits | 06NO2 |

### VG32 – Voice Burglar & Fire Alarm (non-Morse), Two Way Radio, Traffic Signal, Telemetering, Wired Music, Electrowriter – Bridging

| Circuit Description | NC Code for CKL 1, 2 & 3 |
| --- | --- |
| Conference | 04BR2.CF |
| Split Path 1 way or 2 Way Transmission | 04BR2.SP |

### VG32 – Toll Terminal and Mobile Radio Telephone, Two-Way Radio – Additional Terminal

| Circuit Description | NC Code - CKL 1 | CKL 2 |
| --- | --- | --- |
| 2W Interface | 02LO3 | 02LS2 |
| Data Capability | 02LO3.DB | 02LS2.DB |

### VG32 – PBX Off Premises Station

| Circuit Description | If FIC Code is | Then NCI @ CKL 1 is | Then NCI @ CKL 2 is |
| --- | --- | --- | --- |
| 2 wire Interface | OL13A | 02LA2 | 02LS2 |
| 2 wire Interface | OL13B | 02LB2 | 02LS2 |
| 2 wire Interface | OL13C | 02LC2 | 02LS2 |
| 2 wire Interface w/Data Capability | OL13A | 02LA2.DB | 02LS2.DB |
| 2 wire Interface w/ Data Capability | OL13B | 02LB2.DB | 02LS2.DB |
| 2 wire Interface w/ Data Capability | OL13C | 02LC2.DB | 02LS2.DB |

### VG32 – Off Premises Extension

| Circuit Description | NCI Code |
| --- | --- |
| Two Wire Interface | 02LS2 |
| Data Capability | 02LS2.DB |

### VG32 – Tie Lines

| If FIC is | Then NCI Code is | NCI Code for Data Capability is |
| --- | --- | --- |
| TL11M | 04EA3.MQQ | 04EA2.MDD.QQ |
| TL11E | 04EA2.E.QQ | 04EA2.EDD.QQ |
| VCA (CDQ2X) | 04EA2.M.ZA | 04EA2.MOD.ZA |
| TL31M, 31TLMB | 06EA2.M.QQ | 06EA2.MDD.QQ |
| TL31E, 31TLEG | 06EA2.E.QQ | 06EA2.EDD.QQ |
| TC31M | 06EA2.M.UL | 06EA2.MDD.UL |
| TC31E | 06EA2.E.UL | 06EA2.EDD.UL |
| VAC (CDQ4X) 1TTMB | 06EA2.M.ZA | 03EA2.MDD.ZA |
| TL12M, 12TTMB | 06EB2.M.QQ | 06EB2.MDD.QQ |
| TL12E | 06EB2.E.QQ | 06EB2.EDD.QQ |
| VAC (CDQ2W) | 06EB2.M.ZA | 06EB2.MDD.ZA |
| TL32M, 32TTMB | 08EB2.M.QQ | 08EB2.MDD.QQ |
| TL32E | 08EB2.E.QQ | 08EB2.EDD.QQ |
| TC32M | 08EB2.M.UL | 08EB2.MDD.UL |
| TC32E | 08EB2.E.UL | 08EB2.EDD.UL |
| VCA (CDQ4W), 2TTMB | 08EB2.M.ZA | 08EB2.MDD.ZA |
| Analog Centrex* | 02CT3 | 02CT3.DD |
| Digital Centrex* | 04CT2 | 04CT2.DD |

Note: *Requires Centrex Tie Line

## Miscellaneous Ordering Procedures

- Channel Services in the 2000 Series are ordered on a REQ TYP 'K'.

- Channel mileage USOCs should be shown first in the FEATURE field.

- NC and NCI codes are required on order for end users in the state of Michigan.

- FIC codes are required on all Tie Line Orders and Off Premise PBX station orders.

- Tie Lines terminating in a Centrex require additional information so that the Central Office switch can be programmed correctly. This information should be entered in the Remarks section of the order request.

# Billing

Minimum period of service is one month.