Centrex

Description	3

Aliases	3

Availability	3

Restrictions/Limitations	4

All States	4

Illinois & Michigan	4

Ohio and Wisconsin	4

Sunsetted Centrex	4

Required Companion Products	5

Features	5

Standard	6

Illinois	6

Michigan	8

Ohio	10

Wisconsin	12

Optional Line Features	14

Illinois	14

Michigan	15

Ohio	17

Wisconsin	18

Optional System Features	19

Illinois	19

Michigan	21

Ohio	23

Wisconsin	25

Simultaneous Ring One Number	27

Restrictions/Limitations	27

Console Arrangements - Standard Features	28

All States	28

Console Arrangement - Optional Features	29

Illinois	29

Michigan	30

Ohio	30

Wisconsin	30

Premium Feature Package	30

Illinois, Ohio and Wisconsin	30

Michigan	31

Advanced Custom Calling Features Offered in CTX (CLASS)	31

Illinois	32

Michigan	32

Ohio	32

Wisconsin	33

Standard Electronic Key Features	33

Optional System Electronic Key Features	35

Centrex Lines Terminated at Another Customer Location	36

Centrex Mileage Extensions	36

Intercept of Calls to Unassigned Station Line Numbers	36

Voice Grade Channels - Centrex Service to Other Systems	36

CPE Involvement	36

Resale/Sharing	37

Ordering	37

End User Negotiations	37

Listings	38

Due Dates	38

USOCs	38

Class of Service	38

Illinois	38

Michigan	39

Ohio	39

Wisconsin	39

Centrex Line USOCs	40

Illinois, Ohio & Wisconsin	40

Michigan	41

Centrex Intercom USOCs	41

Long Term Number Portability Surcharge USOC – NSR	42

PIC	42

FIDs	42

Line Class Codes (LCCs)	46

TGS (5ESS only)	50

All States	50

Miscellaneous Ordering Procedures	51

Master Agency Billing	51

Billing	51

Exchange Names by Access Area	51

Access Area A	51

Access Area B	51

Access Area C	52

Ohio	53

Network Access Area (CPXHX) Quantity Discounts	53

Contracts	53

# Description

Important: Packet switching has been Grandfathered effective as follows:

- Illinois and Michigan - July 5th, 2005

- Indiana and Ohio - July 16, 2005

- Wisconsin - July 31, 2005

This document encompasses Centrex Service for Illinois, Michigan, Ohio and Wisconsin. Centrex Service is not available in Indiana. See  Advanced Centrex Service-Indiana.

- Centrex is a competitive local exchange telecommunications service in which the equipment controlling the switching is located in a telephone company's Central Office. Centrex Service provides for the transmission and switching of digital and analog signals, where technology and facilities permit.

- Central office line selection provides direct inward dialing (DID) to Centrex lines, direct outward dialing (DOD) with individual line identification in the central office for those inter-exchange carriers for which AT&T renders billing services, and intercom dialing within the Centrex system.

- A wide range of line features and system enhancements are available with to allow the CLEC to tailor the service to meet the specific needs of the end user.

- Centrex Electronic Key line service provides the capability for an Electronic Key Line (EKL) set with preprogrammed push button features to be utilized on a specially provisioned line (C-line card, two-wire, non-loaded subscriber loop).

- Integrated Services Digital Network (ISDN) provides an integrated voice/data communications capability for the transmission of circuit switched voice, and circuit switched data. ISDN offers two 64K 'B' (Bearer) channels for a high speed simultaneous data and voice transportation service. ISDN Centrex National offers features and capabilities that are standardized with all types of central office switches. ISDN Centrex-Custom offers features that require the use of proprietary Customer Premises Equipment (CPE). Feature operations between ISDN Custom and ISDN-National may not be the same for all features.

- ISDN features and charges are not covered in this document. See the ISDN Centrex document for specific information relating to ISDN Centrex.

## Aliases

- CTX

- Centrex 2000

# Availability

- Centrex Service is available in Illinois, Ohio, Michigan and Wisconsin.

- Centrex is provided from switching equipment, located in telephone company premises, and is offered for two or more lines subject to availability of facilities. It can be serviced from 1A, 5ESS, DMS, and EWSD switches.

- The exchange of the serving wire center determines the local service area for all station lines.

## Restrictions/Limitations

### All States

- Cannot have POTS as secondary class of service at an SLA address.

- Suspension of service is not offered.

- Local Usage Saver is the only optional calling plan available.

- Centrex is limited to a minimum of two lines.

- Centrex is provided at option of AT&T and furnished subject to Central office switching capacity and availability of outside plant facilities.

- The availability, functionality and capabilities of Centrex features may vary by central office.

  - Variations in the switching and control equipment used may cause differences in the operation or availability of certain features.

The following are not available on Centrex

- Privacy Manager

- Dual Service

- Pay-per-use features

- Suspension of service

### Illinois & Michigan

- Last number redial is not available in 1AESS offices in Michigan.

- Centrex intercom calling is only allowed between station users internal to the CLEC’s end-user or station users of an affiliate company to the Carrier’s end-user.

- Direct interconnection of unaffiliated end users' Centrex systems is prohibited

- The end user shall not assign or otherwise transfer rights or obligations under any Centrex arrangement without prior written consent of AT&T.

- Intercom prices for each Centrex system are based on one and one-half or less Centum Call Seconds load.

### Ohio and Wisconsin

- CTX cannot be used to provide Centrex Dormitory Service in Ohio.

## Sunsetted Centrex

Sunsetted services means that the tariff has been withdrawn and any end users currently on that tariff must be moved on to the most current tariff, if they want to retain the service.   Sunsetted Centrex services are no longer available in the tariff. Only accounts with an existing contract can have these types of services.

| IF | THEN |
| --- | --- |
| Contract is expired | Account CANNOT be resold and must be converted to Centrex Service. The LSR will be rejected. Note: If the Centrex Account is Sunsetted, it must be changed to the current Retail Centrex offering prior to Resale conversion /migration. |
| Contract is NOT expired | It can be resold. The LSC will an issue order to assume account as Resold. Note: On a conversion/migration request, a positive entry must be stated on the Remarks section of the LSR, "Contract NOT expired on Sunsetted Centrex - convert to Resale Centrex. |

## Required Companion Products

In Illinois, Service Transport Facilities (STF) is required with Pair-At-A-Time rates. STF is an arrangement for connecting CLECs' premises to AT&T central office facilities (local loop).

# Features

General Centrex features are broken down into the following categories:

| Feature Set | Description |
| --- | --- |
| Standard Features | Features that are provided to the CLEC at no additional charge. |
| Optional Line Features | Features that are provided on the Centrex line; End User pays an additional amount for the features. |
| Optional System Features | Features that are provided on the end user’s Centrex system; end user pays an additional amount for the features. |
| Premium Feature Package | Optional line features that are packaged; one monthly rate is charged for all features in the package whether one or all features are used. |
| Advanced Custom Calling (CLASS) Features Offered in Centrex | Class custom calling features that are available to Centrex as well as other types of service. |
| Standard Electronic Key Only Features | Features that are provided to electronic key end users at no additional charge. These features are normally not available on a Centrex voice line. |
| Optional Electronic Key Only Features | Features that are provided to electronic key end users at an additional charge. These features are normally not available on a Centrex voice line. |

## Standard

### Illinois

| Standard Feature | ZUSOC | Modifying FID |
| --- | --- | --- |
| Servicemate | See Servicemate | N/A |
| Call Diverting | No ZUSOC required | N/A |
| Call Forwarding Variable - All Calls to Inside and Outside Centrex | ZCFV1 | N/A |
| Call Forwarding Variable - DID to Inside Centrex only | ZCF1V | N/A |
| Call Forwarding - Busy All Calls | ZCFBA | /ZTN |
| Call Forwarding - Busy Internal/External Split | ZB5ES | /CFBE XXXX /CFBI XXXX |
| Call Forwarding - Don't Answer | ZCFDA | /ZTN/RCYC X |
| Call Forwarding - Don't Answer Internal/External Split | ZD1ES | /CFDE XXXX/RCYC /CFDI XXXX/RCYC |
| Call Forwarding of Call Waiting | No ZUSOC required | N/A |
| Call Hold | ZCVLD | N/A |
| Call Pick-Up (1AESS, DMS, EWSD only) | ZXAPU | /CPG* |
| Call Pick-Up (5ESS only) | ZTAS1 ZTAS2 | /CPG* /CPG* |
| Call Transfer (All-Calls) Deluxe | ZCSAC | N/A |
| Call Transfer (Intra-System) Deluxe | ZCSTH | N/A |
| Call Waiting - Call Waiting Terminating All Calls - Call Waiting Terminating DID Only - Call Waiting Terminating Internal - Call Waiting-Dial | ZCWTG ZCW1O ZCKT1 ZCWTD | N/A N/A N/A N/A |
| Cancel Call Waiting (Call Waiting Terminating) | No ZUSOC required | N/A |
| Conference Calling, 3-Way | No ZUSOC required | N/A |
| Consultation Hold | No ZUSOC required | N/A |
| Cutoff on Disconnect (DMS only) | ZCODT | N/A |
| Deny Incoming (from outside CTX) | ZD1NP (DMS only) | /DIN$ |
| Deny Originating | ZDRG9 (DMS/EWSD only) | N/A |
| Deny Terminating (all calls) | ZDTMC (DMS/EWSD only) | N/A |
| Direct Inward Dialing | No ZUSOC required | N/A |
| Direct Outward Dialing | No ZUSOC required | N/A |
| Distinctive Ring & Call Waiting Tone | ZDR1C | N/A |
| End to End Signaling | No ZUSOC required | N/A |
| Equal Access for InterLATA Calling | No ZUSOC required | N/A |
| Hunting Arrangements | No ZUSOC required | N/A |
| Intercom Calling | No ZUSOC required | N/A |
| Message Waiting Indicator - Audible (Use w/Vendor Provided Voice Mail) Message Waiting Indicator - Audible - (Use w/AT&T Voice Mail) | ZMYAD ZMYAM | /ZGRP ISVMGRP (5ESS) /CAR N/CRX N (DMS) EWSD & 1AESS- None required /ZGRP ISVMGRP (5ESS) /CAR N/CRX N (DMS) EWSD & 1AESS- None required |
| Trunk Answer Any Station Night Service (Used for CPU in 5ESS) | ZTAS1 ZTAS2 | /CPG* /CPG* |
| Remote Access to Call Forwarding WILL BE GRANDFATHERED ON 3/31/01. NO NEW ORDERS WILL BE TAKEN FOR THIS PRODUCT AND NO UPGRADE OR DOWNGRADE REQUESTS WILL BE MADE. REMOVED GRANDFATHERED PACKAGES CANNOT BE ADDED BACK TO AN ACCOUNT AT A LATER DATE. | --- | --- |
| Speed Calling - Short | ZSCSL | N/A |
| Touch-Tone | No ZUSOC required | N/A |
| Transfer Calls To Restricted Station | No ZUSOC required | N/A |
| Usage Billing by Line Number | No ZUSOC required | N/A |

Note: ***/ZTN requires telephone number, which should be entered exactly as end user would dial.

- CPG (Call Pick Up Group) requires Call Pick Up Group number to be entered (3-7 numeric characters).

- When establishing a new CPG, the CLEC is required to do one of the following, depending on switch type:

- 1AESS/5ESS - Preorder through the LSC.

- EWSD - Assign an unassigned CPG number, which is a three-digit number, starting with 001 (eg. /CPG 001)

- DMS100 - Assign the seven-digit number of one of the numbers or master number, in the Call Pick Up Group.  Do not use a three-digit Group number (eg. /CPG 2344444).

- When adding a telephone number to an existing CPG, the existing CPG from the CSR should be used.

- When adding a telephone number to existing CPG, and end user has Servicemate service, the CLEC must list the CPG the line is being added to.

Remote Access to Call Forwarding not available on new CTX systems installed after September 1994.

### Michigan

| Standard Feature | ZUSOC | Modifying FID |
| --- | --- | --- |
| Servicemate | See Servicemate | N/A |
| Call Diverting | No ZUSOC required | N/A |
| Call Forwarding Variable - External Only - Internal Only - All Calls/Universal - Denied | ZCF1V ZCJDE ZCFV1 ZXDCF | N/A N/A N/A N/A |
| Call Forwarding Busy - External Only - Internal Only - All Calls - Inhibit Busy - Station Activation - All Calls Outside Centrex | ZCFB1 ZCJDE ZCFBA ZCF1B ZCLFC ZCFBU | /ZTN* /ZTN* /ZTN* N/A /ZTN* /ZTN* |
| Call Forwarding - Don't Answer - External Only - Internal Only - All Calls - Station Activation - All Calls Outside Centrex | ZCFD1 ZCKDE ZCFDA ZCAFB ZCFDU | /ZTN*/RCYC X /ZTN*/RCYC X /ZTN*/RCYC X /ZTN*/RCYC X /ZTN*/RCYC X |
| Call Forward BY/DA, Internal / External Split | ZBTSS | /ZTN plus Busy: /CFBE, /CFBI DA: /CFDE, /CFDI |
| Call Forwarding of Call Waiting | No ZUSOC required | N/A |
| Call Hold | ZCVLD | N/A |
| Call Pick-Up | ZXAPU | /CPG** |
| Call Transfer - All Calls - Outside - Intra - To Restricted Station | ZCSAC ZCATO ZCATN ZD1RT | N/A N/A N/A /DIN |
| Call Waiting - Terminating - Originating - Dial - Exempt - Intragroup | ZCWTG ZCWRG ZCWTD ZCWXT ZCW1O | N/A N/A N/A N/A N/A |
| Cancel Call Waiting (Call Waiting Terminating) | ZCWAC | N/A |
| Conference Calling, 3-Way Calling and Consultation Hold | No ZUSOC required | N/A |
| Deny Incoming (from outside CTX) | ZD1NP | /DIN$ |
| Deny Originating | ZDRG9 | N/A |
| Deny Terminating | ZDTMC | N/A |
| Direct Inward Dialing | No ZUSOC required | N/A |
| Direct Outward Dialing | No ZUSOC required | N/A |
| Distinctive Ring & Call Waiting Tone | ZDR1C (ringing) ZRCWO (call wtg) | N/A |
| End to End Signaling | No ZUSOC required | N/A |
| Equal Access for InterLATA Calling | No ZUSOC required | N/A |
| Hunting Arrangements | No ZUSOC required | N/A |
| Intercom Calling | No ZUSOC required | N/A |
| Message Waiting Indicator - Audible (Use w/Vendor Provided Voice Mail) Message Waiting Indicator - Audible - (Use w/AT&T Voice Mail) | ZMYAD ZMYAM | /ZGRP ISVMGRP (5ESS) /CAR N/CRX N (DMS) EWSD & 1AESS- None required /ZGRP ISVMGRP (5ESS) /CAR N/CRX N (DMS) EWSD & 1AESS- None required |
| Ring Reminder On/Off | Z1CFR | N/A |
| Speed Calling - Short | ZSCSL | N/A |
| Touch-Tone | TTV | N/A |
| Transfer Calls to Restricted Station | ZD1RT | /DIN |
| Usage Billing by Line Number | No ZUSOC required | N/A |

Note: ***/ZTN requires telephone number, which should be entered exactly as end user would dial.

- CPG (Call Pick Up Group) requires Call Pick Up Group number to be entered (3-7 numeric characters).

- When establishing a new CPG, the CLEC is required to do one of the following, depending on switch type:

- 1AESS/5ESS - Preorder through the LSC.

- EWSD - Assign an unassigned CPG number, which is a three-digit number, starting with 001 (eg. /CPG 001)

- DMS100 - Assign the seven-digit number of one of the numbers or master number, in the Call Pick Up Group.  Do not use a three-digit Group number (eg. /CPG 2344444).

- When adding a telephone number to an existing CPG, the existing CPG from the CSR should be used.

- When adding a telephone number to existing CPG, and end user has Servicemate service, the CLEC must list the CPG the line is being added to.

### Ohio

| Standard Feature | ZUSOC | Modifying FID |
| --- | --- | --- |
| Servicemate | See Servicemate | N/A |
| Billing Usage by line number (formerly known as 9FF) | No ZUSOC required - provided to all customers | N/A |
| Call Diverting | No ZUSOC required | N/A |
| Call Forwarding Variable - All Calls to Inside and Outside Centrex | ZCFV1 | N/A |
| Call Forwarding Variable - DID to Inside Centrex only | ZCF1V | N/A |
| Call Forwarding - Busy All Calls | ZCFBA | /ZTN |
| Call Forwarding - Busy Internal/External Split | ZB5ES | /CFBE XXXX /CFBI XXXX |
| Call Forwarding - Don't Answer | ZCFDA | /ZTN/RCYC X |
| Call Forwarding - Don't Answer Internal/External Split | ZD1ES | /CFDE XXXX/RCYC /CFDI XXXX/RCYC |
| Call Forwarding of Call Waiting | No ZUSOC required | N/A |
| Call Hold | ZCVLD | N/A |
| Call Pick-Up/All switch types | ZXAPU | /CPG* |
| Call Transfer (All-Calls) Deluxe | ZCSAC | N/A |
| Call Transfer (Intra-System) Deluxe | ZCSTH | N/A |
| Call Waiting - Call Waiting Terminating All Calls - Call Waiting Terminating DID Only - Call Waiting Terminating Internal - Call Waiting-Dial | ZCWTG ZCW1O ZCKT1 ZCWTD | N/A N/A N/A N/A |
| Cancel Call Waiting (Call Waiting Terminating) | No ZUSOC required | N/A |
| Conference Calling, 3-Way | No ZUSOC required | N/A |
| Consultation Hold | No ZUSOC required | N/A |
| Deny Incoming (from outside CTX) | ZD1NP | /DIN$ ($ equals all calls/enter after SXP++ USOC) |
| Deny Originating | ZDRG9 | N/A |
| Deny Terminating (all calls) | ZDTMC | N/A |
| Direct Inward Dialing | No ZUSOC required | N/A |
| Direct Outward Dialing | No ZUSOC required | N/A |
| Distinctive Ring & Call Waiting Tone | ZDR1C | N/A |
| End to End Signaling | No ZUSOC required | N/A |
| Equal Access for InterLATA Calling | No ZUSOC required | N/A |
| Hunting Arrangements | No ZUSOC required | N/A |
| Intercom Calling | No ZUSOC required | N/A |
| Message Waiting Indicator – Audible/Vendor (Stutter Dial Tone) | ZMYAD | /ZGRP 1SVMGRP (5ESS) /CAR N/CRX N (DMS) EWSD & 1AESS - None Required |
| Message Waiting Indicator – Audible/AT&T (Stutter Dial Tone) | ZMYAM | /ZGRP ISVMGRP (5ESS) /CAR N/CRX N (DMS100) EWSD & 1AESS- None required |
| Private Facilities Access (5ESS only) | ZPRFA | /ZGRP (CTX NAME) |
| Remote Access to Call Forwarding WILL BE GRANDFATHERED ON 3/31/01. NO NEW ORDERS WILL BE TAKEN FOR THIS PRODUCT AND NO UPGRADE OR DOWNGRADE REQUESTS WILL BE MADE. REMOVED GRANDFATHERED PACKAGES CANNOT BE ADDED BACK TO AN ACCOUNT AT A LATER DATE. | --- | --- |
| Speed Calling - Short | ZSCSL | N/A |
| Touch-Tone | TTB required in OH and WI | N/A |
| Transfer Calls To Restricted Station | No ZUSOC required | N/A |
| Trunk station (ZTAS1) and Trunk station picked up (ZTAS2) (Used with night service after hours call pick up in 5ESS. This feature can be on end user’s account in addition to standard call pick up.) | ZTAS1 ZTAS2 | /CPG* /CPG* |
| Usage Billing by Line Number (formerly known as 9FF) | No ZUSOC required | N/A |

Note: ***/ZTN requires telephone number, which should be entered exactly as end user would dial.

- CPG (Call Pick Up Group) requires Call Pick Up Group number to be entered (3-7 numeric characters).

- When establishing a new CPG, the CLEC is required to do one of the following, depending on switch type:

- 1AESS/5ESS - Preorder through the LSC.

- EWSD - Assign an unassigned CPG number, which is a three-digit number, starting with 001 (eg. /CPG 001)

- DMS100 - Assign the seven-digit number of one of the numbers or master number, in the Call Pick Up Group.  Do not use a three-digit Group number (eg. /CPG 2344444).

- When adding a telephone number to an existing CPG, the existing CPG from the CSR should be used.

- When adding a telephone number to existing CPG, and end user has Servicemate service, the CLEC must list the CPG the line is being added to.

Remote Access to Call Forwarding not available on new CTX systems installed after September 1994.

### Wisconsin

| Standard Feature | ZUSOC | Modifying FID |
| --- | --- | --- |
| Servicemate | See Servicemate | N/A |
| Call Diverting | No ZUSOC required | N/A |
| Call Forwarding Variable - All Calls to Inside and Outside Centrex | ZCFV1 | N/A |
| Call Forwarding Variable - DID to Inside Centrex only | ZCF1V | N/A |
| Call Forwarding - Busy All Calls | ZCFBA | /ZTN |
| Call Forwarding - Busy Internal/External Split | ZB5ES | /CFBE XXXX /CFBI XXXX |
| Call Forwarding - Don't Answer | ZCFDA | /ZTN/RCYC X |
| Call Forwarding - Don't Answer Internal/External Split | ZD1ES | /CFDE XXXX/RCYC /CFDI XXXX/RCYC |
| Call Forwarding of Call Waiting | No ZUSOC required | N/A |
| Call Hold | ZCVLD | N/A |
| Call Pick-Up | ZXAPU | /CPG* |
| Call Transfer (All-Calls) Deluxe | ZCSAC | N/A |
| Call Transfer (Intra-System) Deluxe | ZCSTH | N/A |
| Call Waiting - Call Waiting Terminating All Calls - Call Waiting Terminating DID Only - Call Waiting Terminating Internal - Call Waiting-Dial | ZCWTG ZCW1O ZCKT1 ZCWTD | N/A N/A N/A N/A |
| Cancel Call Waiting (Call Waiting Terminating) | No ZUSOC required | N/A |
| Conference Calling, 3-Way | No ZUSOC required | N/A |
| Consultation Hold | No ZUSOC required | N/A |
| Deny Incoming (from outside CTX) | ZD1NP | /DIN$ |
| Deny Originating | ZDRG9 | N/A |
| Deny Terminating (all calls) | ZDTMC | N/A |
| Direct Inward Dialing | No ZUSOC required | N/A |
| Direct Outward Dialing | No ZUSOC required | N/A |
| Distinctive Ring & Call Waiting Tone | ZDR1C | N/A |
| End to End Signaling | No ZUSOC required | N/A |
| Equal Access for InterLATA Calling | No ZUSOC required | N/A |
| Hunting Arrangements | No ZUSOC required | N/A |
| Intercom Calling | No ZUSOC required | N/A |
| Message Waiting Indicator - Audible (Use with Vendor Provided Voice Mail) Message Waiting Indicator - Audible (Use with AT&T Voice Mail) | ZMYAD ZMYAM | /ZGRP ISVMGRP(5ESS) /CAR N/CRX N (DMS100) EWSD & 1AESS None required /ZGRP ISVMGRP(5ESS) /CAR N/CRX N (DMS100) EWSD & 1AESS None required |
| Private Facilities Access (5ESS only) | ZPRFA | /ZGRP (CTX NAME) |
| Remote Access to Call Forwarding WILL BE GRANDFATHERED ON 3/31/01. NO NEW ORDERS WILL BE TAKEN FOR THIS PRODUCT AND NO UPGRADE OR DOWNGRADE REQUESTS WILL BE MADE. REMOVED GRANDFATHERED PACKAGES CANNOT BE ADDED BACK TO AN ACCOUNT AT A LATER DATE. | --- | --- |
| Speed Calling - Short | ZSCSL | N/A |
| Touch-Tone | TTB required in OH and WI | N/A |
| Transfer Calls To Restricted Station | No ZUSOC required | N/A |
| Usage Billing by Line Number | No ZUSOC required | N/A |

Note: ***/ZTN requires telephone number, which should be entered exactly as end user would dial.

- CPG (Call Pick Up Group) requires Call Pick Up Group number to be entered (3-7 numeric characters)

- When establishing a new CPG, the CLEC is required to do one of the following, depending on switch type:

- 1AESS/5ESS - Preorder through the LSC.

- EWSD - Assign an unassigned CPG number, which is a three-digit number, starting with 001 (eg. /CPG 001)

- DMS100 - Assign the seven-digit number of one of the numbers or master number, in the Call Pick Up Group.  Do not use a three-digit Group number (eg. /CPG 2344444).

- When adding a telephone number to an existing CPG, the existing CPG from the CSR should be used.

- When adding a telephone number to existing CPG, and end user has Servicemate service, the CLEC must list the CPG the line is being added to.

Remote Access to Call Forwarding not available on new CTX systems installed after September 1994.

## Optional Line Features

### Illinois

| Optional Line Features | ZUSOC or USOC | Modifying FID |
| --- | --- | --- |
| Automatic Route Selection (ARS)/Flexible Route Selection (FRS) (5ESS Only) | ZARSC | ZGRP XXX(CTX GRP) |
| Call Forwarding Over Private Facilities | ZCFVP | N/A |
| Call Request with Queue (DMS100) | ZMWCR | /CAR X/CAR X |
| Centrex Station Identification - Per System - Per Tie Trunk | STNPG STN | N/A N/A |
| Conference Services 6 port – add to all lines that require access to conference bridge | ZCQF6 | N/A |
| Direct Connect Originating | ZAULN | /ZTN* |
| Direct Connect with Delay | ZXAWL | /WLN XXX-XXXX /WLT X |
| Ground Start Use SXPAB (DMS100 only) Use FID /GST(all other switches) | GSTXB (Access Area B) GSTXC (Access Area C) | --- --- |
| Make Busy Arrangements- - Make Busy Key (DMS100 Only) | ZXMBK | N/A |
| Message Waiting Indication – Visual - As CLASS Feature - As NON-CLASS Feature Note: For DMS100 only use SXPAE | ZMYAW ZMYAV | ZMWVW/ZGRPISVMGRP (5ESS) ZMWVW/CAR N/CRX N (DMS100) ZMYAV/ZGRP ISVMGRP (5ESS) ZMYAV/CAR N/CRX N (DMS100) |
| Private Facilities Access (5ESS only) | ZPRFA | /ZGRP (CTX NAME) |
| Speed Calling - Expanded Number Group, Controller Per List (N/A Siemens Switch (EWSD) - 50 Number List - 70 Number List - 80 Number List | ZSCC5 ZSCC7 ZSCC8 | /SCG XX (speed call group number) |
| Speed Calling Expanded Number Group: User (N/A in EWSD) - 50 Number List - 70 Number List - 80 Number List | ZSC5O ZSC7O ZSC8O | /SCG XX (speed call group number) |
| Speed Calling - Long (30 List) Per List -Controller -User | ZSCC3 (1) ZSC3O | /SCG XX (speed call group number) |
| Stop Hunt - Key/Access Code | 2URSH | N/A |
| UCD | See UCD |  |

Note: * ZTN represents the number that calls are forwarding to. This number should be formatted exactly as dialed.

†ZGSP represents the call forwarding paths.

‡For specifics regarding UCD see the Uniform Call Distribution (UCD) document.

(1) Note:  1 required per speed call group

### Michigan

| Optional Line Features | ZUSOC or USOC | Modifying FID |
| --- | --- | --- |
| Call Forwarding Over Private Facilities | ZCFVP | N/A |
| Centrex Calling Line ID | ZC1ND | (See Caller ID) |
| Centrex Open Interface | HPD1X, 3X |  |
| Centrex Station ID - Per Tie Trunk | STNPG STN | N/A |
| Conference Services -6 Port -30 Port | ZCQF6 ZCQF3 | N/A N/A |
| Direct Connect Originating | ZAULN | /ZTN* |
| Direct Connect with Delay | ZXAWL | /WLN XXX-XXXX /WLT X |
| Do Not Disturb | ZDMDB | /DND XX (DMS100 only) |
| Group Intercom (EBS) | ZG1CM | /GIC |
| Ground Start | SXPAB (DMS100 only) Use SXP++/GST all other switch types | /GST |
| High Speed Data (Datapath) -Critical Path Restoration | DP9 ZCFPR | /ZTN* |
| Message Waiting Indication – Visual -As CLASS Feature -As NON CLASS Feature Note: For DMS100 only, use SXPAE | ZMWVW ZMYAV | ZMWVW/ZGRP ISVMGRP (5ESS) ZMWVW/CAR N/CRX N (DMS100) ZMYAV/ZGRP ISVMGRP (5ESS) ZMYAV/CAR N/CRX N (DMS100) |
| Private Facility Access(5ESS only) | ZPRFA | /ZGRP(CTX. Name) |
| Private Facility Access(EWSD only) | ZXGRL | /FRL |
| Station Call Thru Test (SCTT) | SAT | N/A |
| Speed Calling - Expanded Number Group, Controller Per List (50/70 Number List) | ZSCC5 ZSCC7 | /SCG XX (speed call group number) |
| Speed Calling Expanded Number Group: User (50/70 Number List) | ZSC5O ZSC7O | /SCG# |
| Speed Calling - Long, Per List -Controller -User | ZSCC3 (1) ZSC3O | /SCG# |
| Speed Call Pause Insertion | P1SPG | N/A |
| Stop Hunt - Key/Access Code | 2URSH | N/A |
| 800 Call Transfer, per 800 # term | C8EPN | N/A |
| UCD -Per UCD Group -Per Station -Per EKL Line -Per UCD Software # | UQZPG A82 UGP SXMAA | N/A N/A N/A /DES UCD |

Note: * ZTN represents the number that calls are forwarding to. This number should be formatted exactly as dialed.

(1) Note:  1 required per speed call group

### Ohio

| Optional Line Features | ZUSOC or USOC | Modifying FID |
| --- | --- | --- |
| Call Forwarding Over Private Facilities | ZCFVP | N/A |
| Call Request with Queue | ZMWCR | /CAR X/CRX X |
| Centrex Station Identification- Per Tie Trunk | STNPG STN | N/A |
| Conference Services 6 Port – add to each line that requires access to the conference bridge | ZCQF6 | N/A |
| Direct Connect Originating | ZAULN | /ZTN* |
| Direct Connect with Delay | ZXAWL | /WLN XXX-XXXX /WLT X |
| Do Not Disturb | ZDMDB | /DND XX (DMS100 only) |
| Ground Start -Use SXPAB for DMS100 only -Use SXP++/GST for all other switch types | GST |  |
| Make Busy and Access Arrangement- Key Arrangement | ZXMBK | N/A |
| Message Waiting Indication – Visual As CLASS Feature As NON-CLASS Feature Note: Use SXPAE for DMS100 only | ZMWVW ZMYAV | ZMWVW/ZGRP ISVMGRP (5ESS) ZMWVW/CAR N/CRX N (DMS100 only) ZMYAV/ZGRP ISVMGRP (5ESS) ZMYAV/CAR N/CRX N (DMS100) |
| Private Facility Access | ZPRFA | /AGRP (CTX Name or private facility group name) |
| Speed Calling - Expanded Number Group, Controller Per List -50 Number List -70 Number List | ZSCC5 ZSCC7 | /SCG XX (speed call group number) |
| Speed Calling Expanded Number Group: User -50 Number List -70 Number List | ZSC5O ZSC7O | /SCG# |
| Speed Calling - Long, Per List -Controller -User | ZSCC3 (1) ZSC3O | /SCG# |
| Stop Hunt - Key/Access Code | 2URSH | N/A |
| UCD -Per UCD Group -Per Station -Per EKL Line | UQZPG A82 UGP | N/A |

Note: *ZTN represents the number that calls are forwarding to. This number should be formatted exactly as dialed.

(1) Note:  1 required per speed call group

### Wisconsin

| Optional Line Features | ZUSOC or USOC | Modifying FID |
| --- | --- | --- |
| Call Forwarding Over Private Facilities | ZCFVP | N/A |
| Call Request with Queue | ZMWCR | /CAR X/CRX X |
| Conference Services 6 Port – add to each line that requires access to the conference bridge | ZCQF6 | N/A |
| Direct Connect Originating | ZAULN | /ZTN |
| Direct Connect Originating with Delay | ZXAWL | /WLN XXX-XXXX /WLT X |
| Ground Start -Use SXPAB for DMS100 only -Use SXP++/GST for all other switch types | GST | N/A |
| Last Number Redial | ZLNRB |  |
| Make Busy Key | ZXMBK | N/A |
| Message Waiting Indication – Visual As CLASS Feature As NON-CLASS Feature Note: Use SXPAE for DMS100 only | ZMWVW ZMYAV | ZMWVW/ZGRP ISVMGRP (5ESS) ZMWVW/CAR N/CRX N (DMS100 only) ZMYAV/ZGRP ISVMGRP (5ESS) ZMYAV/CAR N/CRX N (DMS100) |
| Speed Calling-Expanded Number Group; User Per List - 50 Number List - 70 Number List | ZSCC5 ZSCC7 | /SCG XX# |
| Speed Calling-Expanded Number Group; User Per List - 50 Number List - 70 Number List | ZSC50 ZSC70 | /SCG# |
| Speed Calling-Long, Per List - Controller - User | ZSCC3 (1) ZSC3O | /SCG# |
| Stop Hunt Key | 2URSH | N/A |
| Telephone Number Reprogramming Service | NR9CR | N/A |

Note: *ZTN represents the number that calls are forwarding to. This number should be formatted exactly as dialed.

(1) Note:  1 required per speed call group

## Optional System Features

### Illinois

| Optional System Features | USOC (Billing only) |
| --- | --- |
| Call Detail Recording Service -Per Account (includes 5,000 call records) -Additional 5,000 call records (or fraction of) -Additional 25,000 call records (or fraction of) -Additional 50,000 call records (or fraction of) -Subsequent Rearrangement Charge -Retrieval of Duplicate Call Detail, per occasion | RSD RS51X RS52X RS53X READK REH1X |
| Servicemate (standard for 7 line or more guarantee) -Per System (for less than 7 line guarantee) -Per Line (for less than 7 line guarantee) | MLBPS MLB |
| Centrex Message Signal Interface | SMQPS |
| Announcement Services -Per C.O. Announcement (24 sec max) -Interface to customer premise for announcement or music | RKQ N5A |
| Area Wide Networking (AWN) - See Billing section at end of document. | --- |
| Assume Dial 9 | A9D |
| Authorization Codes -Initial 100 -Each Additional 25 -Station-Specific Per Line Arranged | AKG1X AKG AJN |
| Automatic Route Selection (ARS) - Basic -Initial Pattern of Three Routes -Additional Patterns, each -Change Existing Pattern | AR9 ARH RCHAZ |
| Automatic Route Selection (ARS) - Deluxe -Additional Patterns, each -7-10 Digit Screening -IDDD Dialing -Time of Day Routing -Change Existing Pattern | AQPVS ARH AHAPS A1GPS TMQ RCHAZ |
| Call Forwarding MultiPath – per system/per type -Per station/Call Forwarding Variable -Per station/Call Forwarding Busy -Per station/Call Forwarding Don’t Answer | ESD ZCFMV ZCFMB ZCFMD |
| Conferencing Services -Station Controlled Conference (add to all lines that require access to conference bridge) -6 Port Conference Circuit -Conference Linking (per each additional 6 port) -Privacy Release Conf Control (EKL only) | ZCQF6 EQ6 EQ6PA PE8 |
| Console Arrangement | --- |
| Customized Call Diverting (Line Class Code) | RSHPS |
| Direct Inward System Access (DISA) | DJMPS |
| Do Not Disturb -Per Line -Per Group of Lines | DJD DJDPG |
| Line Side Access Termination | QPV |
| Music on Hold (Note: Only one music source is allowed) | MOH |
| Network Speed Calling | NWSPS |
| Outgoing Deluxe Trunk Queuing | QOCPG |
| Personal Call Screening | EV3 |
| Queue Slots | AQA |
| Remote Access -Initial Access Arrangement -Additional Access Arrangement | RUMPG RUMAX |
| Special Intercept | LA2 |
| Split Service | EBSPG |
| Station Message Detail Recording - CO -Per Account -Per FX, FCO or FD -Per Tie Line -Per Other Carrier Switching Access Line -Per Message | CMM CMQ CMT CMZ --- |
| Station Message Detail Recording - Premise † -Per System -Per Termination (FX, WATS, or Tie Trunk) | MDR SMDPT |
| Supplemental Three-Digit Dialing -Per System -Per Termination | T3NPX T38 |
| Trunk Side Access Connections (Private Fac.) -2 Wire Analog -4 Wire Analog -DS1 Termination -PRI Connection -PRI Connection "D" Data Channel Backup -Network Ring Again -Network Name Display | 2PV 4PV D1E1X DUG1X ZPBXD ZRA ZNN |
| Trunk Verification Designation Station | BVSPS |

Note: *Effective August 31, 1996, DISA is no longer available to new or existing Centrex end users.

†Station Message Detail Recording (SMDR) to Premise requires a 3002 channel from the Central Office to the carrier’s customer’s equipment.

### Michigan

| Optional System Features | USOC (Billing only) |
| --- | --- |
| Call Detail Recording Service -Per Account (includes 5,000 call records) -Additional 5,000 call records (or fraction of) -Additional 25, 000 call records (or fraction of) -Additional 50,000 call records (or fraction of) -Subsequent Rearrangement Charge -Retrieval of Duplicate Call Detail, per occasion -Feature Group A (FGA) and/or Tie Line Call Detail | RSD RS51X RS52X RS53X READK REH1X C6FFA |
| Servicemate (Note: These USOCs apply to less than 7 lines only as 7 lines are standard) -Per System -Per Line | MLBPS MLB |
| Centrex Message Signal Interface | SMQPS |
| Announcement Services -Per C.O. Announcement (24 sec max) -Interface to customer premise for announcement or music | RKQ N5A |
| Area Wide Networking (AWN) - See Billing section at end of document. | --- |
| ACD | AQDPS |
| Assume Dial 9 (requires SPS order to add to system) | A9D |
| Authorization Codes -Initial 100 -Each Additional 25 | AKG1X AKG |
| Automatic Route Selection (ARS) - Basic -Initial Pattern of Three Routes -Additional Patterns, each -Change Existing Pattern -Per Station (5E only) | AR9 ARH RCHAZ ZARAD/ZGRP |
| Automatic Route Selection (ARS) - Deluxe -Additional Patterns, each -7-10 Digit Screening -Permissive Home Numbering Plan Area (NPA) Code Dialing, per ARS Deluxe Group - 900/976 Special Access -Change Existing Pattern | AQPVS ARH AHAPS PHNPG No Charge RCHAZ |
| Call Forwarding MultiPath – per system/per type -Per station/Call Forwarding Variable -Per station/Call Forwarding Busy -Per station/Call Forwarding Don’t Answer | ESD ZCFMV ZCFMB ZCFMD |
| Customer Dialed Account Recording (CDAR) | OF5CU |
| Conferencing Services -Station Controlled Conference (6 Port) -Station Controlled Conference (30 Port) -6 Port Conference Circuit -Conference Linking -Privacy Release Conf Control (EKL only) | EAAPS C3RPS EQ6 EQ6PA PE8 |
| Console Arrangement See Standard and Optional Features below. | --- |
| Customized Call Diverting (Line Class Code) | RSHPS |
| Do Not Disturb -Per Line -Per Group of Lines | ZDMDB DJDPG |
| Music on Hold (Note: Only one source is allowed with Music On Hold) | MOH |
| Network Speed Calling | NWSPS |
| Personal Call Screening | EV3 |
| Queue Slots | AQA |
| Special Intercept | LA2 |
| Split Service (grandfathered as of 7-24-96) | EBSPG |
| Station Message Detail Recording - CO -Per System -Per Termination (FX, WATS, Tie Trunk) | CSH SMDPT |
| Station Message Detail Recording - Premise * -Per System -Per Termination (FX, WATS, Tie Trunk) | MDR SMDPT |
| Trunk Side Access Connections (Private Fac.) -2 Wire Analog -4 Wire Analog -DS1 Termination -PRI Connection -PRI Connection "D" Cannel Backup -Network Ring Again -Network Name Display | 2PV 4PV D1E1X DUG1X ZPBXD ZRA ZNN |
| Trunk Verification Designated Station | BVSPS |

Note: * SMDR to Premise requires a 3002 channel from the Central Office to the carrier’s customer’s premise equipment.

### Ohio

| Optional System Features | USOC (Billing only) |
| --- | --- |
| Call Detail Recording Service -Per Account (includes 5,000 call records) -Additional 5,000 call records (or fraction of) -Additional 25,000 call records (or fraction of) -Additional 50,000 call records (or fraction of) -Subsequent Rearrangement Charge -Retrieval of Duplicate Call Detail, per occasion | RSD RS51X RS52X RS53X READK REH1X |
| Servicemate (standard for 7 lines or more) -Per System -Per Line | MLBPS MLB |
| Centrex Message Signal Interface | SMQPS |
| Announcement Services -Per C.O. Announcement (24 sec max) -Interface to customer premise for announcement or music | RKQ N5A |
| Area Wide Networking (AWN) - See Billing section at end of document. | --- |
| Assume Dial 9 | A9D |
| Authorization Codes -Initial 100 -Each Additional 25 -Station-Specific Per Line Arranged | AKG1X AKG AJN |
| Automatic Route Selection (ARS) - Basic -Initial Pattern of Three Routes -Additional Patterns, each -Change Existing Pattern | AR9 ARH RCHAZ |
| Automatic Route Selection (ARS) - Deluxe -Additional Patterns, each -7-10 Digit Screening -IDDD Dialing -Time of Day Routing -Change Existing Pattern | AQPVS ARH AHAPS A1GPS TMQ RCHAZ |
| Call Forwarding MultiPath – per system/per type -Per station/Call Forwarding Variable -Per station/Call Forwarding Busy -Per station/Call Forwarding Don’t Answer | ESD ZCFMV ZCFMB ZCFMD |
| Conferencing Services -Station Controlled Conference (6 Port) (Add to all lines that require access to conference bridge) -6 Port Conference Circuit -Conference Linking (30 Port) -Privacy Release Conf Control (EKL only) | ZCQF6 EQ6 EQ6PA PE8 |
| Console Arrangement See Standard and Optional Features below. | --- |
| Customized Call Diverting (Line Class Code) | RSHPS |
| Direct Inward System Access (DISA) | DJMPS |
| Do Not Disturb -Per Line -Per Group of Lines | DJD DJDPG |
| Line Side Access Termination | QPV |
| Music on Hold (Note: Only one music source is allowed) | MOH |
| Network Speed Calling | NWSPS |
| Personal Call Screening | EV3 |
| Queue Slots | AQA |
| Remote Access -Initial Access Arrangement -Additional Access Arrangement | RUMPG RUMAX |
| Special Intercept | LA2 |
| Split Service | EBSPG |
| Station Message Detail Recording - CO -Per Account -Per FX, FCO or FD -Per Tie Line -Per Other Carrier Switching Access Line -Per Message | CMM CMQ CMT CMZ --- |
| Station Message Detail Recording - Premise * -Per System -Per Termination (FX, WATS, Tie Trunk) | MDR SMDPT |
| Supplemental Three-Digit Dialing -Per System -Per Termination | T3NPX T38 |
| Trunk Side Access Connections (Private Fac.) -2 Wire Analog -4 Wire Analog -DS1 Termination -PRI Connection -PRI Connection Data (D) Channel Backup -Network Ring Again -Network Name Display | 2PV 4PV D1E1X DUG1X ZPBXD ZRA ZNN |
| Trunk Verification Designation Station | BVSPS |

Note: * SMDR to Premise requires a 3002 channel from the Central Office to the carrier’s customer’s premise equipment.

### Wisconsin

| Optional System Features | USOC (Billing Only) |
| --- | --- |
| Call Detail Recording Service (ACDRS) File Transfer Arrangement -per End user -per Wire Center Per Line, per end user when the total number ACDRS equipped lines are: - 1 to 99 lines, each - 100 to 999 lines, each - Over 1,000 lines, each Per FX trunk group terminated in ACDRS arrangement per occasion - Per Wire Center - Per FX Trunk Per Tie Trunk Group terminated in ACDRS arrangement per occasion -per wire centers -per tie trunk Per WATS group terminated in ACDRS arrangement per occasion -per wire center -per WATS lines | BTA CRW CRW1X CRW1X CRW3X CRNGX CMQES CRNHX CMTES CRNJX CWTES |
| Servicemate (standard for 7 lines or more) -per system -per line | MLBPS MLB |
| Centrex Message Signal Interface | See CMSI |
| Virtual Network |  |
| Announcement Services -Per C.O. Announcement (24 sec max) -Interface to customer premise for announcement or music | RKQ N5A |
| Assume Dial 9 (requires SPS order to add to system) | A9D |
| Authorization Codes | AKG |
| Automatic Route Selection (ARS)-Basic -Initial Pattern of Three Routes -Additional Patterns, each -Change Existing Pattern | AR9 ARH RCHAZ |
| Automatic Route Selection (ARS) - Deluxe -Additional Patterns, each -7-10 Digit Screening -IDDD Dialing -Time of Day Routing -Change Existing Pattern | AQPVS ARH AHAPS A1GPS TMQ RCHAZ |
| Call Detail Account Recording -Per Wire Center -Per Centrex Line | CYDPW CYD |
| Call Forwarding MultiPath – per system/per type -Per station/Call Forwarding Variable -Per station/Call Forwarding Busy -Per station/Call Forwarding Don’t Answer | ESD ZCFMV ZCFMB ZCFMD |
| Call Waiting Lamp Interface | SUGPL |
| Centrex Station Identification (CSI) -Per Tie Trunk | STNPG STN |
| Conference Services -Station Controlled Conference (6 Port) -Station Controlled Conference (30 Port) -6 Port Conference Circuit -Conference Linking -Privacy Release Conf Control (EKL only) | ZCQF6 ZCQF3 EQ6 EQ6PA PE8 |
| Customized Call Diverting (Line Class Code) | RSHPS |
| Do Not Disturb -Per Line -Per Group of lines | DJD DJDPG |
| Music on Hold (Note: Only one music source is allowed) | MOH |
| Network Speed Calling | NWSPS |
| Outgoing Deluxe Trunk Queuing | QOCPG |
| Personal Call Screening | EV3 |
| Private Facility Terminations -Line Side Access terminations -Analog 4 Wire Termination per arrangement -DS1 Connection each arrangement -Analog Tie Trunk DS1/DS3 Interface -Centrex Line Side DS1 Interface -Trunk Side Access -PRI Connection each arrangement -"D" Channel Backup, each -Network Ring Again per arrangement -Network Name Display per arrangement | 2PV 4PV D1E1X NR9CW NR9CW DUG1X CPBXD ZRA ZNN |
| Queue Slots | AQA |
| Special Intercept Service | LA2 |
| Split Service | EBSPG |
| Station Message Detail Recording - CO (SMDR-CO) -Per System -Per Termination -Per Record -CDAR Per Message | CSH SMDPT CMA MD |
| Station Message Detail Recording - Premises (SMDR-P)* -Per System -Per Termination | MDR SMDPT |
| Supplemental Three-Digit Dialing -Per System -Per Termination | T3NPX T38 |
| Trunk Verification from Designation Station | BVSPS |
| Uniform Call Distribution (UCD) -Per UCD Group -Per Line Equipped -Per EKL | UQZPG A82 4GP |
| Virtual Routing-each group of 24 access paths | VF1 |

Note: *SMDR to Premises requires a 3002 channel from the Central Office to the Carrier’s customer’s premise equipment.

## Simultaneous Ring One Number

Centrex Simultaneous Ring One Number (CSR-ON) is an optional feature available in DMS100 only effective June 30, 2004.  It enables a Centrex number and an additional telephone number, within the same DMS100 switch, to ring simultaneously.  CSR-ON rings a Centrex station and one other number when the Centrex number is dialed.

- The numbers that ring simultaneously can be any valid telephone number within the same DMS100 switch that the end user selects.

- CSR-ON works with Nortel MCS5100 but is not required.

- Valid telephone numbers include:

  - Centrex lines, including ISDN and EKL

  - POTS (business or residential)

  - DID/PBX

- The two components of CSR-ON are Pilot Directory Number (PDN) and non-Pilot Member Directory Numbers (NPMDN).

### Restrictions/Limitations

- CSR-ON is not compatible with ServiceMate

- NPMDNs must be a working number in the same switch as the PDN.

- If the PDN and NPMDN has voice mail, the call will be answered by whichever voice mail answers first.

- When Call forwarding Variable is activated, CSR-ON does not ring the member number.

- When Call Forwarding Busy or Don’t Answer is activated, CSR-ON does not ring the member number.

- Three-Way calling in an intra-switch transfer only rings the PDN; in an inter-switch transfer, both PDN and NPMDNs ring.

- Activating Call Forwarding variable on the PDN overrides/cancels out CSR-ON.

- If PDN and NPMDN are located in the same switch and the NPMDN is a ported number, it may not ring.

- PDN lines cannot be:

  - 5E, 1A, EWSD, DMS10 Centrex lines

  - Centex IP

  - ISDN Centrex

  - Centrex EKL with Multiple Call Appearance or Multiple Appearance Directory Numbers

  - ACD/UCD

  - Hunting lines

- NPMDNs are not compatible with CSR-ON:

  - International DNs

  - Numbers with special service codes or speed dial codes (ie “*” or “#”)

  - DNs that contain less than 4 or more than 30 digits

  - DNs that are NPMDNs of another CSR-ON PDN in the same DMS100

  - Meet-me conference DNs

  - Multiple Appearance Directory Number (MADN)

  - Members of a multi-line hunting, ACD or UCD

## Console Arrangements - Standard Features

### All States

Note: USOCs not required for provisioning standard console features.

| Standard Console Features | Standard Console Features, contd. |
| --- | --- |
| Access to Paging/Code Calling | Flexible Console Alerting |
| Attendant Call Park | Incoming Call Identification |
| Attendant Camp-On | Information Display Calls in Queue |
| Attendant Conference Capability | Interposition Calling |
| Attendant Console Screen Mgmt | Locked Loop Operation |
| Attendant Control of Call Forward Busy Line & Don't Answer | Lockout |
| Attendant Position Busy | Message Waiting Control |
| Attendant Recall from Satellite | Multiple Console Operation |
| Attendant Recorded Announcement | Multiple Listed Directory Numbers |
| Attendant to UCD Transfer | Night Service (Fixed or Flexible) |
| Attendant Transfer | Power Failure Transfer |
| AutoDial | Queuing with Call Waiting Indication |
| Automatic Recall | Release Upon Completion of Dialing |
| Busy Verification of Station Trunk | Secrecy |
| Call Hold | Serial Calling |
| Call Hold with Recall | Speed Calling |
| Call Park Recall Timer | Straight Forward Outward Completion |
| Call Selection | Supervisory Control |
| Call Splitting | Switched Loop Operation |
| Call Through Tests | Through Dialing |
| Console Display Capabilities | Time of Day & Date |
| Console Test | Timed Reminder |
| Control of Trunk Group Access | Toll Diversion to Attendant |
| Control of Virtual Facilities Group | Trunk Busy Identification |
| Delayed Operations | Trunk Group Busy/Access Control Key |
| Direct Trunk Group Selection | Trunk Group Identification/Indicators |
| DTMF End to End Signaling | UCD from Queue |
| Emergency Access to Attendant | Verification of Authorization Codes |
| Emergency Override | Wild Card Key |
| Extended Calls to Busy/No Answer | 800 Termination |
| Foreign Exchange Termination | --- |

## Console Arrangement - Optional Features

### Illinois

| Optional Features | USOC |
| --- | --- |
| Per DMS Console | NG9PC |
| Per 5ESS Console | MD9PC |
| Attendant Call Detail Entry | AE3PB |
| Attendant Conference (30 Port) | C3P |
| Direct Station Selection & Busy Lamp Field | BUDPC |
| Name Display for Attendant Console | NDFPC |
| Multi-Position Hunt -Per Group -Per Position | AHBPG A6V |
| Operational Measurement | AOKPC |

### Michigan

| Optional Features | USOC |
| --- | --- |
| Per 5ESS Console | MD9PC |
| Per Attendant Position, DMS 100 -Per Console (provisioning) -Per Lead Directory Software Number | NG9PC FZD1X SXMAA/DES T4S |
| Attendant Conference (30 Port) | C3P |
| Direct Station Selection & Busy Lamp Field w/Camp On | BUY |
| Multi-Position Hunt -Per Position | A6V |

### Ohio

| Optional Features | USOC |
| --- | --- |
| Per DMS Console | NG9PC |
| Per 5ESS Console | MD9PC |
| Attendant Call Detail Entry | AE3PB |
| Attendant Conference (30 Port) | C3P |
| Direct Station Selection & Busy Lamp Field | BUDPC |
| Name Display for Attendant Console | NDFPC |
| Operational Measurement | AOKPC |

### Wisconsin

| Optional Features | USOC |
| --- | --- |
| Per DMS Console | NG9PC |
| Per 5ESS Console | MD9PC |
| Attendant Call Detail Entry | AE3PB |
| Attendant Conference (30 Port) | C3P |
| Direct Station Selection & Busy Lamp Field | BUDPC |
| Name Display for Attendant Console | NDFPC |
| Operational Measurement | AOKPC |

## Premium Feature Package

### Illinois, Ohio and Wisconsin

| Premium Features | USOC* | ZUSOC | Modifying FID |
| --- | --- | --- | --- |
| Automatic Callback | ESY79 | ZACBK | /RIE |
| Call Waiting Originating (A.K.A. Call Camp On) | ESY79 | ZCWRG | /RIE |
| Dial Call Waiting (A.K.A. Call Camp On Selective) | ESY79 | ZCWTD | /RIE |
| Call Park | ESY79 | ZPDRK | /RIE |
| Directed Call Park | ESY79 | ZDCPK | /RIE |
| Directed Call Pick-Up -Non Barge-In -Barge-In | ESY79 ESY79 | ZDCPU ZDCPU ZDCB1 | /RIE /RIE |
| Last Number Redial (SLS) | ESY79 | ZXKNR | /RIE |

Note: Last Number Redial is not available in 1AESS switch.

*Only one USOC ESY79 per line should be entered. When more than one feature is provisioned per line the other ZUSOCs should float /RIE (Rate Included Elsewhere).

### Michigan

| Premium Features | USOC* | ZUSOC | Modifying FID |
| --- | --- | --- | --- |
| Automatic Callback | ESY79 | ZACBK | /RIE |
| Call Waiting Originating (A.K.A. Call Camp On) | ESY79 | ZCWRG | /RIE |
| Dial Call Waiting (A.K.A. Call Camp On Selective) | ESY79 | ZCWTD | /RIE |
| Call Park | ESY79 | ZPDRK | /RIE |
| Directed Call Park | ESY79 | ZDCPK | /RIE |
| Directed Call Pick-Up Non Barge-In -Originating -Terminating Exempt Barge-In -Originating -Terminating Exempt | ESY79 | ZDCPU ZDCPT ZDCB1 ZDCBT | /RIE /RIE /RIE /RIE |
| Last Number Redial (SLS) | ESY79 | ZXKNR | /RIE |

Note:  Last Number Redial is not available in a 1AESS switch.

*Only one USOC ESY79 per line should be entered. When more than one feature is provisioned per line the other ZUSOCs should float /RIE (Rate Included Elsewhere).

## Advanced Custom Calling Features Offered in CTX (CLASS)

Note:  These features are not part of the Premium Feature Package.

### Illinois

| Advanced Custom Calling Feature | USOC | Modifying FID |
| --- | --- | --- |
| Automatic Callback | ZCLAR | N/A |
| Call Screening | ZACSR | N/A |
| Call Trace | No ZUSOC needed | N/A |
| Caller ID - Network -Intercom -with Name | ZC1ND ZCL1D | N/A |
| Repeat Dialing | ZACRD | N/A |
| Selective Distinctive Ringing Call Waiting | ZACDC | N/A |
| Visual Message Waiting Indication -use with AT&T Voice Mail -use with Vendor-provided Voice Mail | ZMWVW ZMWVC | /ZGRP ISVMGRP (5E) /CAR N/CRX N (DMS100) |

### Michigan

| Advanced Custom Calling Feature | USOC | Modifying FID |
| --- | --- | --- |
| Automatic Callback | ZCLAR | N/A |
| Call Screening | ZACSR | N/A |
| Calling Line ID | ZC1ND | N/A |
| Repeat Dialing | ZACRD | N/A |
| Selective Distinctive Ringing Call Waiting | ZACDC | N/A |
| Visual Message Waiting Indication | ZMWVW | /ZGRP ISVMGRP (5E) * /CAR N/CRX N (DMS100) * |

Note: * Not required for Integrated Voice Mail.

### Ohio

| Advanced Custom Calling Feature | USOC | Modifying FID |
| --- | --- | --- |
| Automatic Callback | ZCLAR | N/A |
| Call Screening | ZACSR | N/A |
| Call Trace | No ZUSOC required | N/A |
| Caller ID | ZC1ND | N/A |
| Caller ID with Name | NMP | N/A |
| Repeat Dialing | ZACRD | N/A |
| Selective Distinctive Ringing Call Waiting | ZACDC | N/A |
| Visual Message Waiting Indication | ZMWVW | /ZGRP ISVMGRP (5E) /CAR N/CRX N (DMS100) |

### Wisconsin

| Advanced Custom Calling Feature | USOC | Modifying FID |
| --- | --- | --- |
| Automatic Callback | ZCLAR | N/A |
| Call Screening | ZASCR | N/A |
| Caller ID | ZC1ND | N/A |
| Caller ID w/Name | NMP | N/A |
| Repeat Dialing | ZACRD | N/A |
| Distinctive Ringing Call Waiting | ZACDC | N/A |
| Visual Message Waiting Indication | ZMWVW | /ZGRP ISVMGRP (SE) /CAR N/CRX N (DMS100) |

## Standard Electronic Key Features

Note:  See Electronic Key Line Features document for more information.

Analog Line Pickups

Automatic Dial

Automatic Line Pre-select

Blind Transfer with Recall Identification

Call Diverting

Call Forward of Call Waiting Calls

Call Forwarding Busy

Call Forwarding Don’t Answer

Call Forwarding Variable

Call Forwarding Per Key

Call Hold

Call Pickup

Call Request

Call Request with Queue

Call Transfer

Call Waiting/Cancel Call Waiting

Called Number Display

Caller ID Intercom

Calling Reason Display

Conference Calling – 3 Way

Consultation Hold

Direct Inward Dialing

Direct Outward Dialing

Directory Number Hunt with Call Waiting and Preferential Hunt

Display Capability

Distinctive Ringing and Call Waiting Tone

End to End Signaling

Equal Access

Executive Busy Override

Executive Busy Override - Exempt

Executive Message Waiting

Feature Buttons

Group Intercom

Hunting Arrangements

Intercom Calling

Last Number Redial

Leave Message Activation

Listen on Hold

Make Set Busy

Make Set Busy Except in Group Intercom

Message Retrieval Display

Message Waiting Activation Control

Message Waiting Indication - Visual

Message Waiting Indication – Lamp

Message Waiting Indication - Audible

Multiple Appearance Directory Number (MADN) Single Call Arrangement (SCA)

Night Answer

On Hook Dialing

Repeat Alert

Ring Again Idle Set

Ringing Options for MADN

Secondary MADN Call Forwarding

Set Inspect

Short Hunt

Speed Calling - Short

Stop Hunt Access Code

Time and Date Display

Touch Tone

Transfer Call to Restricted Station

Usage Billing By Line Number

## Optional System Electronic Key Features

Add-on Modules

Automatic Callback

Call Camp-On

Call Camp-On Selective

Call Forward Reason Display (MI only)

Call Forwarding Over Private Facilities

Call Park

Caller ID

Caller ID with Name

Calling Name Display on Intercom

Custom Calling Name on Centrex

CLASS Features

Datapath Critical Path Restoration (MI only)

Direct Connect Originating

Direct Connect Originating with Delay

Direct Station Selection/Busy Lamp Field with Fast Transfer

Directed Call Park

Directed Call Pickup

Distance Extension

Executive Display Communications

Make busy

Multiple Appearance Directory Number (MADN) Multiple Call Arrangement (MCA)

Network Number Display (MI Only)

Premium Feature Package

Query Busy Station

Secondary Directory Telephone Number

Special Billing Code

Speed Calling-Expanded Number Group

Speed Calling – Long

Speed Call Pause Insertion (MI Only)

Station Call Through Test (MI only)

Station Controlled Conference

Telephone Number Reprogramming Service (WI only)

800 Call Transfer Single Line Set (MI Only)

## Centrex Lines Terminated at Another Customer Location

Centrex end user may terminate one or more lines at another business end user’s location when the lines are used exclusively for the Centrex end user’s own communication needs. The following regulations apply to Centrex lines terminated at another business end user’s location:

- The Centrex lines must be restricted from placing calls outside the Centrex system.

- The Centrex end user is responsible for all nonrecurring charges and recurring rates for the Centrex service lines.

- The Centrex end user is responsible for all the services associated with the Centrex lines including, but not limited to directory listings and incoming MTS toll charges.

## Centrex Mileage Extensions

- End user may extend Centrex lines outside of the central office providing the Centrex service. Monthly mileage rates apply for channel charges as defined in the appropriate tariffs.

## Intercept of Calls to Unassigned Station Line Numbers

- Incoming and intragroup calls to unassigned numbers may be directed to one of the end user working station numbers or attendant console.  See Extended Intercept Service for additional information.

- Customized-recorded intercept messages may be provided where facilities permit at additional rates and charges.  See Special Intercept document for specific information.

## Voice Grade Channels - Centrex Service to Other Systems

Voice Grade Channels are provided between Centrex Service and the following:

- Customer Premises Equipment (CPE)

- Private Branch Exchange (PBX) Systems

- Other Centrex Systems between affiliated end users only.

## CPE Involvement

AT&T will assume no responsibility for the removal, storage, replacement, or restoral of CPE and wiring. It is the end user’s responsibility to retain and restore CPE and its associated wiring if the option to return to the prior service is selected.

## Resale/Sharing

- A CLEC may resell Centrex Services to or arrange for the sharing of Centrex Service among unaffiliated end user clients consistent with the restrictions contained within the CTX tariff. A CLEC may establish as many Centrex systems as desired.

- Intercom calling between unaffiliated end user clients of a Centrex-based resale or sharing system(s) is prohibited.

- AT&T and the CLEC will work together to resolve any instance of prohibited intercom calling by end user clients. In instances of persistent or blatant violation, Ameritech may request the CLEC to disconnect the offending end user clients from the resale or sharing system.

- Each Centrex-based resale or sharing system may be established by a CLEC only within a single CO serving exchange area switching unit.

- Centrex Service shall be available for resale or sharing in COs wherever Centrex Service is available, subject to the availability of existing facilities within such offices.

- For service provided to residential customers connected to Centrex-based resale or sharing systems, the CLEC shall be charged, by AT&T, at tariffed business Centrex rates.

# Ordering

Complete the appropriate Centrex Order Forms and forward to the LSC (Local Service Center). Blank forms can be found in LSC Manual Forms.

## End User Negotiations

- Obtain listing information

- Interview end user to determine what features would be needed.

- Explain features that are inherent to every line:

- Conference Calling/Three Way Calling

- Call Transfer

- Consultation Hold

- Intercom Calling

- Touch-Tone

- Direct Inward Dialing

- Direct Outward Dialing

- Other features are available and should be ordered at the same time to avoid delays and additional charges.

- There is no local call allowance. Note: Intercom calls do not count as local messages.

- The end user will usually dial 9 to make an outgoing call (Example: 9+911)

Important: Centrex Station Numbers cannot be reserved through the pre-order system. Refer to the Pre-Ordering Section, Manual Process Guidelines.

- Determine line restrictions per line:

| If | Then |
| --- | --- |
| Unrestricted | Can dial intercom, local, toll information and 900/976. |
| Toll Restricted | Can dial intercom and local |
| Semi Restricted | Deny 900/976 – Can dial intercom, local and information |
| Fully Restricted | Can dial intercom only |
| Others | Contact your Account or Service Manager |

- Will need to reprogram fax machines, modems, etc with outside access codes.

## Listings

AT&T will furnish the following, without charge, for each Centrex system:

- One main directory listing

- One Yellow Page directory listing

Note: If the account is unlisted or has a miscellaneous number for a main BTN, then no free Yellow Page listing is available.

- Individual business listings of telephone numbers, by department, title or individual name, may be indented under the main listing or listed separately. Additional charges apply.

## Due Dates

Refer to Resale Due Date Matrix.

## USOCs

### Class of Service

#### Illinois

- The Class of Service USOC for Centrex is E6++X.

- The third character is determined by the local calling area rate as follows:

| Calling Area | Third Character |
| --- | --- |
| Flat | E |
| Measured | J |
| Message | K |

- The fourth character is determined by serving switch type as follows:

| CO Type | Fourth Character |
| --- | --- |
| 1/AESS | 2 |
| 5ESS | U |
| DMS 10 | D |
| DMS100 | J |
| EWSD | S |

- The fifth character is always X.

- Centrex Service can only be a secondary class of service to another Centrex Service.

#### Michigan

- The Class of Service Code for Centrex is E6K++ (3rd character always K for Message Service).

- The fourth character is determined by serving switch type as follows:

| CO Type | Fourth Character |
| --- | --- |
| 1/AESS | 2 |
| 5ESS | U |
| DMS 10 | D |
| DMS100 | J |
| EWSD | S |

- The fifth character is X except for resellers when it is then T.

#### Ohio

- The Class of Service USOC for Centrex Measured is AOM+X.

- The Class of Service USOC for Centrex Message is AON+X.

- The fourth character is determined by serving switch type as follows:

| CO Type | Fourth Character |
| --- | --- |
| 1/AESS | 2 |
| 5ESS | U |
| DMS 10 | D |
| DMS100 | J |
| EWSD | S |

- The fifth character is always X.

- An Account may have both Classes of Services:

- The Main Class of Service should reflect the majority of stations on the account.

- The Secondary Class of Service should reflect the lesser number of stations on the account.

#### Wisconsin

- The Class of Service USOC for Centrex is E6K+X

- The fourth character is determined by serving switch type as follows:

| CO Type | Fourth Character |
| --- | --- |
| 1/AESS | 2 |
| 5ESS | U |
| DMS 10 | D |
| DMS100 | J |
| EWSD | S |

- The fifth character is always X.

Exception: The CTX 1CB Class of Service is XCZ+X.

### Centrex Line USOCs

#### Illinois, Ohio & Wisconsin

| Description | Centrex System USOC |
| --- | --- |
| Single Line Centrex Line: -Unrestricted -Toll Restricted -Unrestricted, Deny 900/976 -Fully Restricted -Ground Start (DMS100 only) ** -Message Waiting Lamp (Non-class, DMS100 only) | SXPAA SXPBA SXPBA SXPCA SXP*B SXP*E |
| Business Set-EKL -Unrestricted -Toll Restricted -Fully Restricted | SXPAC SXPBC SXPCC |
| Bridged Station Extension -Same Premises, Same Building -Same Premises, Different Building -Different Premises | SXBAA=IL, WI SXFAA=OH SXBBA=IL; WI SXFBA=OH SXBCA=IL; WI SXFCA=OH |
| Secondary Directory Number | SOT |
| CO Test Line (For AT&T Use Only) | SXMGA |
| Screening Directory Number | SXMSA |
| Reference (Billing only) Number | SXMAA |
| OmniPresence Centrex Line | SXPRA |
| OPTI Centrex Line | SXPWA |

Note: A PIC entry is not allowed on a fully restricted line and a CO directory number.

** See PBX Trunks regarding Ground start/Loop start specifications

#### Michigan

| Description | Centrex System USOC |
| --- | --- |
| Exchange Access -Primary -Bridged -Software Number | SXP++ SXB++ SXM++ |
| Secondary Directory Number | SOT |
| OmniPresence Centrex Line | SXPRA |
| OPTI Centrex Line | SXPWA |

- The 4th character is determined as follows:

| IF the Line Restriction is | THEN the 4th Character is |
| --- | --- |
| - Unrestricted (Primary) - Partially Restricted (Primary) - Fully Restricted (Primary) - Unrestricted (Bridged) - Partially Restricted (Bridged) - Fully Restricted (Bridged) | A B C C H G |

- The 5th character is determined as follows:

| IF the Centrex Line is | THEN the 5th Character is |
| --- | --- |
| - Regular - Ground Start - Electronic Bus Set - Data - Message Waiting | - A - B * - C * - D * - E * |

Note: * DMS 100 Only.

### Centrex Intercom USOCs

- Centrex analog Intercom Line Rate includes standard Centrex features.

- Centrex Electronic Key Intercom Line Rate includes Standard Centrex and Standard Electronic Key features.

| Description | Illinois | Michigan | Ohio | Wisconsin |
| --- | --- | --- | --- | --- |
| Basic Centrex Analog Intercom | NUM | NUM | NDC | NUM |
| Electronic Key Line (EKL) Intercom | NUE | NUE | NDU | NUE |

Centrex Simultaneous Ring One Number

USOC:  S3S1X

### Long Term Number Portability Surcharge USOC – NSR

The Long Term Number Portability Surcharge USOC, NSR, is automatically generated.

- NSR is a retained USOC on the CSR.

- NSR is associated with the access line USOC such as SXP++.

- Some station USOCs are blocked from the charge such as SXM++.

### PIC

The USOCs are REB8A and REB8B and are automatically populated. REB8C is also applicable in Michigan only.

## FIDs

| FID | Description |
| --- | --- |
| BG | Bill Group – Method of grouping Centrex station for the application of trunk equivalency. For CTX, the BG number is always 1. Order Placement: Not required. |
| CAR | Call Send – DMS 100 only. Indicates whether the station line identified can send Message Waiting signals to another station with the Centrex group. Order Placement: FEATURE Detail field following the feature USOC in the Feature Field. Example: ZMYAD/CAR N |
| CAT | Customer Access Treatment Code - Identifies the station's ability to access certain calling areas or facilities. The CAT content is common block specific or assigned on a per- Carrier’s customer basis. Order Placement: FEATURE Detail Field following the line assignable USOC. Example: SXP++/CAT X |
| CFBE | Call Forward Busy External – Indicates the telephone number that calls originating from outside the Centrex should be forward to when the Call Forward Busy split feature is ordered. Order Placement: FEATURE Detail Field following the feature USOC in the Feature Field. Example: ZB5ES/CFBE 91NPANXXXXXX (if out of Centrex and Long Distance). |
| CFBI | Call Forward Busy Internal – Indicates the telephone number that calls originating from within the Centrex should be forwarded to when the Call Forward busy split feature is ordered. Order Placement: FEATURE Detail field following the feature USOC in the Feature field. Example: ZB5ES/CFBI XXXX (forward within the Centrex) |
| CFDE | Indicates the telephone number that call originating from outside the Centrex should be forwarded to when the Call Forward No Answer split is ordered. Order Placement: FEATURE Detail Field following the feature USOC in the Feature field. Example: ZD1ES/CFBE 91NPANXXXXXX (if out of Centrex and long Distance. |
| CFDI | Indicates the telephone number that call originating from within the Centrex should be forwarded to when the Call Forward No Answer split feature is ordered. Order Placement: FEATURE Detail field following the feature USOC in the Feature field. Example: ZD1ES/CFDI XXXX (forward within the Centrex) |
| CPG | Call Pick Up Group – Indicates the Call Pick Up Group this station belongs to. Order Placement: FEATURE Detail Field following the feature USOC in the Feature field. Example: ZXAPU/CPG ## |
| CRX | Call Request Exempt – DMS100 only Indicates whether the station line designated is or is not exempt from receiving Message Waiting signals from another station within the Centrex group. Order Placement: FEATURE Detail Field following the feature USOC in the Feature field. Example: ZMYAD/CAR N/CRX N |
| CSR | Customer (End User) Station Rearrangement – indicates that Service Mate is present on the account. It is floated behind the SXP++ and any feature that has to be retained on the Service Record. Order Placement: FEATURE Detail Field following the line assignable USOC. Example: SXP++/CSR |
| CTX | CLEC’s Customer Group Identifier - The Centrex common block, which identifies the system parameters such as station number ranges, Call Pick-Up range, and access codes selected. All new CTX should be 4 digits (plus: subgroup number for the DMS100, i.e. 0004:0 ). Order Placement: CB Field |
| DIN | Deny Incoming (DMS 100 only) – Indicates to deny incoming calls from outside of the Centrex group. Order Placement: Not required. Example: ZD1NP/DIN$ |
| DPA | Different Premises Address - Identifies the address of a centrex off premise extension to another location. Floated behind SXP++ (line USOC). Order Placement: FEATURE Detail Field following the line assignable USOC. Example: SXP++/DPA # |
| DPI | Different Premise Information Supplemental information concerning Different Premise Address (DPA) installation. Can only be used with “DPA” and not on “SLA” locations. Does not reflect in 911 Database. Order Placement: SADLO on Centrex Order Form Example: SXP++/DPA 1/DPI Term on 701E PBX. |
| DPS | Different Premises Subscriber - Identifies a different end user, other than the listed end user, at a different location (SLA) than the main listed address. Floated behind SLA information. This field is prohibited with the FID DPA. Allows E911 and Caller ID to pick up the correct end user name. Order Placement: FEATURE Detail Field following the line assignable USOC. Example: SXP++/DPS Any Company |
| GST *** | Ground Start - Floated behind the SXP++ in all switch types except DMS100. In DMS100 switches, provide correct USOC. Order Placement: SSIG Field Example: SXP++/GST (1A & 5ESS and EWSD) Example: SXPAB (DMS100) |
| IDP | Individual Dialing Plan - Required on the 5ESS only. Identifies the intercom dialing for the customer’s common block (3-4 or 5 digit dialing). Order Placement: FEATURE Detail Field following the line assignable USOC. Example: SXP++/IDP # |
| LASS | Local Area Signaling Service |
| LCC | Line Class Code - Defines the station's ability to access or be accessed by the switch exchange network. The LCCs are normally standard per switch and are not customer specific. Order Placement: FEATURE Detail field following the line assignable USOC. Example: SXP++/LCC AAA |
| NOL F | Number of Lines (Michigan Only)* |
|  | If # of Lines Guaranteed is | Then NOL G* is | And NOL F* is |
|  | 2 – 6 stations | 02 | 02 |
|  | 7 – 24 stations | 07 | 06 |
|  | 25 – 49 stations | 25 | 20 |
|  | 50–99 stations | 50 | 40 |
|  | 100-199 stations | 100 | 80 |
|  | 200-499 stations | 200 | 160 |
|  | 500+ stations | 500 | 400 |
| NOL G | Number of Lines Guaranteed - Indicates the number of lines the customer is required to keep in service. Order Placement: VTA Field on the LSR, fourth segment. Example: VTA 36/VT7/02292001/7 |
| PILN | Pilot Directory Number (CSR-ON) |
| RCYC | Ring Cycle – Indicates after how many rings the call should forward to the pre-selected number. The default is 3 ring cycles. Order Placement: FEATURE Detail field following the feature in the Feature field. Example: ACFDA/ZTN XXXX/RCYC 5 |
| SCG | Speed Call Group Number - Indicates to which speed call group this Centrex station has access. Order Placement: FEATURE Detail field following the feature in the Feature field. Example: ZSC50/SCG ## |
| SLA | Secondary Location Address - Identifies the address of each Centrex location. Floated behind SXP++ (line USOC). Order Placement: FEATURE Detail field following the line assignable USOC. Example: SXP++/SLA# |
| TGID | Terminal Group ID (Name) – Identifies the terminal group name used to provision Centrex lines in a 5ESS office only. Usually followed by the Centrex group number. Order Placement: Not required. |
| TGS | Terminal Group Station Restriction - Required on 5ESS only. Identifies the originating and termination line restrictions, as well as the intercept treatment (T; Tone vs A; Announcement) and optional features attributes. Order Placement: Not required - Ameritech will program as TGUUT unless otherwise specified. If other than TGUUT should be programmed then show the information in the FEATURE Detail following the line assignable USOC. Example: SXP++/TGS TGUUT |
| WLN | Warm Line Service Number – Indicates the telephone number, which is automatically called by the DMS100 switch at the expiration of a predetermined time interval, when the originating end user goes off hook. Order Placement: FEATURE Detail field following the feature USOC in the Feature field. Example: ZXAWL/WLN NXX-XXXX |
| WLT | Warm Line Transfer – Indicates the number of seconds that must elapse before the DMS100 switch sets up the connection for a warm line service number. Order Placement: FEATURE Detail field following the feature USOC in the Feature field. Example: ZXAWL/WLN NXX-XXXX/WLT XX |
| ZGRP | Private Facility Group Name 5ESS only – Required when message waiting indicator-audible is ordered. Indicates to which voice mail provider this line has a mailbox on. Also required when a Centrex station in a 5ESS switch has access to a private facility group. Order Placement: FEATURE Detail field following the message waiting USOC in the feature field. Example: ZMYAD/ZGRP ISVMGRP Example: ZPRFA/ZGRP (facility group name) |
| ZTN | Feature Related Telephone Number - Identifies the station's dialing pattern when associated with Call Forwarding features: Forwarding Inside The Centrex When call forwarding station - station within a Centrex, the forward to number must be written to reflect the intercom dialing patter, i.e. 3, 4 or 5 digits. Exception: 1AESS, all 7 digits of the forward to number must be provided. Forwarding Outside The Centrex When call forwarding outside the Centrex, the forward to number would include the Dial Access Code (DAC, Dial 1, NPA (if applicable) and the seven digit telephone number. Exception: 1AESS, do not show the DAC of 9, 8, etc. However the 1 is required when forwarding outside the NPA. Order Placement: FEATURE Detail field following the Feature USOC in the Feature Field. Example: ZCFBA/ZTN #### (Within the Centrex) Example: ZCFBA/ZTN 91NPANXXXXXX (Outside of the Centrex) |

*** See PBX Trunks regarding groundstart/loopstart specifications

Note:  *Michigan only: Termination liability is based on 80% of the number of liens guaranteed (NOLG) as well as the 80% number (NOL F)

## Line Class Codes (LCCs)

Defines the station's ability to access or be accessed by the switch exchange network.

- LCCs are normally standard per switch and are not customer specific.

- Non-standard LCCs will continue to be assigned by the LSC based on the customer's description in the REMARKS section of the service order form.

| State: Illinois |
| --- |
| Switch Type: 1AESS |
| Type of Restriction | Chicago | Suburban | State |
| Unrestricted | C4N | C8N | C4N |
| Block 900/976 | B4N | B8N | A8N * |
| Toll Restricted | CND | CND | CND |
| Fully Restricted | CFN | CFN | CFN |
| Blocks IDDD and 900/976 Only | B6N | B1N | A1N |
| * Downstate LATAs do not allow 976 blocking. |
| Switch Type: 5ESS |
| Type of Restriction | Chicago NonMLH/MLH* | Suburban NonMLH/MLH* | State NonMLH/MLH* |
| Unrestricted | C4N/C4M | C8N/C8M | C4N/C4M |
| Block 900/976 | B4N/B4M | B8N/B8M | A8N/A8M |
| Toll Restricted | CND/CMD | CND/CMD | CND/CMD |
| Fully Restricted | KZY/KZZ | KZY/KZZ | KZY/KZZ |
| Blocks IDDD and 900/976 Only | B6N/B6M | B1N/B1M | A5N/A5M |
| Also requires TGS FID in 5ESS Switch * Multi-line Hunt LCCs are not compatible with series completion hunt. |
| Switch Type: EWSD |
| Type of Restriction | Chicago | Suburban | State |
| Unrestricted | C4N | C8N | C4N |
| Block 900/976 | B4N | B8N | A8N |
| Toll Restricted | CND | CND | CND |
| Fully Restricted | CND | CND | CND |
| Blocks IDDD and 900/976 Only | B6N | B1N | A1N |
| Switch Type: DMS 100 |
| The Line Class Code of IBN is used on all DMS 100 orders. Standard types of restrictions are: Unrestricted Block 900/976 Toll Restricted Fully Restricted Block IDD and 900/976 Only The DMS switch also requires a Network Class of Service (NCOS/CAT) code together with the 1BN LCC which determines line restrictions. |
| Switch Type: DMS10 |
| The DMS switch requires a Network Class of Service code to determine line restrictions instead of Line Class Codes. |

Details in the areas covered in the Illinois table are:

| Chicago | All addresses with a City of Chicago listing address |
| --- | --- |
| Suburban | Area codes 773, 708, 847, 630, 815, 242 that does not have a City of Chicago listing address |
| State | Area codes 217, 309, 618 |

| State: Michigan |
| --- |
| Switch Type: 1AESS and 5ESS and EWSD |
| Type of Restriction | All Areas |
| Unrestricted | RM1 |
| Block 900/976 | RMA |
| Toll Restricted | R2M |
| Fully Restricted | R90 |
| Blocks IDDD and 900/976 Only | B36 |
| Switch Type: DMS100 |
| The Line Class Code of IBN is used on all DMS 100 orders. Standard types of restrictions are: Unrestricted Block 900/976 Toll Restricted Fully Restricted Block IDDD and 900/976 only The DMS switch also requires a Network Class of Service (NCOS) code which determines line restrictions. The standard NCOS codes are: NCOS 1 – unrestricted NCOS 2 – fully restricted |
| Switch Type: DMS10 |
| The DMS switch also requires a Network Class of Service (NCOS) code to determine line restrictions instead of LCCs. |

| State: Ohio |
| --- |
| Switch Type: 5ESS |
| Type of Restriction | All Areas |
| Unrestricted | RXR |
| Block 900/976 | 9BX |
| Toll Restricted | MTI |
| Fully Restricted | MTI |
| Blocks IDDD and 900/976 Only | 9BF |
| Switch Type: EWSD |
| Type of Restriction | All Areas |
| Unrestricted | MRI |
| Block 900/976 | 9BC |
| Toll Restricted | MTI |
| Fully Restricted | MTI |
| Blocks IDDD and 900/976 Only | 9BF |
| Switch Type: DMS100 |
| The Line Class Code of IBN is used on all DMS 100 orders. The DMS switch also requires a Network Class of Service (NCOS) code which determines line restrictions. Standard NCOS codes are: NCOS 1 – Unrestricted NCOS 2 – Semi restricted NCOS 3 – Fully restricted NCOS 4 – Toll Deny NCOS 9 – 900/976 Blocking |
| Switch Type: DMS10 |
| The DMS switch requires a Network Class of Service code to determine line restrictions instead of LCCs. |

| State: Wisconsin |
| --- |
| Switch Type: 5ESS and EWSD |
| Type of Restriction | Non-HML | HML |
| Unrestricted | RXR | RMR |
| Block 900/976 | RX6 | RM6 |
| Toll Restricted Toll & DA restricted (allows 800, 911 and local) | RXD | Not available |
| Toll Restricted Allows DA, 800, 911 and local | RXM | RMM |
| Fully Restricted # (5ESS) (Allows Intercom and incoming calls. if need is to restrict to Intercom only, must restrict via the TGS TG++T FID) | RX5 | RM5 |
| Fully Restricted (EWSD) | RX5 | RM5 |
| Switch Type: DMS 100 |
| The Line Class Code of IBN is used on all DMS 100 orders. The DMS switch also requires a Network Class of Service (NCOS) code which determines line restrictions. Standard NCOS codes are: NCOS 1 – Unrestricted NCOS 2 – Semi restricted NCOS 3 – Fully restricted NCOS 4 – 900/976 Blocking |
| Switch Type: DSM 100 |
| The DMS switch requires a Network Class of Service code to determine line restrictions instead of LCCs. |

Customer Access Treatment Codes (CAT)

- CAT Codes for the 1AESS, 5ESS, DMS10 and EWSD switch types are generally as follows:

| CAT Code | Network Access Allowed |
| --- | --- |
| 0 | No |
| 1 | Yes |

Note: Not all Centrex's have been built with this configuration; some may have more CAT Codes established or the CAT Codes could be different. Therefore, it is suggested that the CLEC contact their Service Manager for a complete listing of the CAT Codes built for the end user's Centrex.

### TGS (5ESS only)

#### All States

TGS = Terminal Group/Station Restriction. Also known as Deny Originating/Deny Terminating.

- The TGS FID is used to assign different calling restrictions to individual stations by modifying the TG++T (terminal group) data. It is used to allow/disallow incoming/outgoing calls to/from a station line.  Level of restrictions available are:

  - Unrestricted (U):

    - Originating lines have no restrictions on outgoing calls.

    - Terminating lines have no restrictions on incoming calls.

  - Semi Restricted (S):

    - Originating lines can make calls to lines within the same terminal group, including the attendant console, and can place calls over private facilities that are within the same terminal group.

    - Terminating lines can receive calls from these originating points.  All others are restricted.

  - Fully Restricted (F):

    - Originating and Terminating lines are the same as Semi restricted lines except that attendant calls are prohibited.

- The third and fourth characters of the FID determine the restriction on the line.

- The fifth character can be either T for Tone or A for Announcement.

## Miscellaneous Ordering Procedures

### Master Agency Billing

Master Agency Billing is NOT available in Resale or UNE-P/CPO. However, there are situations when a CLEC absorbs a Centrex contract or takes over some of the stations from an existing Centrex (Primary or Secondary account) that contain Master Agency Billing. Billing USOCs will be removed when these accounts are converted. Below are procedures the CLEC should utilize when converting such an account:

If the CLEC is taking over the entire Centrex, then:

- They must send one PON on an ACT V

- They must include a DL form if there are listings on the secondary accounts

- They must include the Hunting information

If the CLEC is taking over the Primary account, then:

- They must send one PON on an ACT V

- They must convert to a New Centrex or different class of service, i.e. POTS

If the CLEC is taking over the Secondary account only, then:

- They must send one PON on an ACT V

- The must convert to a New Centrex or different class of service, i.e. POTS

# Billing

Refer to state tariff for additional information regarding recurring and non recurring charges.

### Exchange Names by Access Area

#### Access Area A

- Detroit (Areas 1-6)

- Royal Oak

- Southfield

#### Access Area B

| Ann Arbor | Auburn Heights | Birmingham | Center Line |
| --- | --- | --- | --- |
| Commerce | Drayton Plains | Farmington | Flint |
| Grand Rapids | Lansing | Livonia | Mayfair |
| Mt. Clemens | Northville | Plymouth | Pontiac |
| Rochester | Romulus | Roseville | Trenton |
| Troy | Utica | Walled Lake | Warren |
| Wayne | West Bloomfield | Wyandotte | Ypsilanti |

#### Access Area C

| Ada | Algonac | Akron | Albion | Alto |
| --- | --- | --- | --- | --- |
| Amasa | Applegate | Armada | Athens | Auburn |
| Bad Axe | Baldwin | Bark River | Battle Creek | Bay City |
| Bay Port | Beaverton | Belding | Belleville | Benton Harbor |
| Bergland | Bessemer | Berrien Spring | Beulah | Big Bay |
| Big Rapids | Birch Run | Boyne City | Brevort | Brighton |
| Buchanan | Byron | Byron Center | Cadillac | Caldeonia |
| Calumet | Carleton | Carsonville | Casnovia | Cedar Springs |
| Champion | Channing | Charlevoix | Charlotte | Cheboygan |
| Chelsea | Clare | Clark Lake | Clarkston | Clarksville |
| Clio-Mt. Morris | Coleman | Coloma | Coral | Cornell |
| Croswell | Crystal Falls | Curtis | Dansville | Dexter |
| Dimondale | Dorr | Dutton | East Jordan | East Tawas |
| Eaton Rapids | Eau Claire | Elk Rapids | Engadine | Escanaba |
| Evart | Fairgrove | Farwell | Fenton | Fife Lake |
| Flat Rock | Flushing | Fountain | Fowlerville | Frankenmuth |
| Frankfort | Freeland | Freeport | Freesoil | Fremont |
| Fulton | Gagetown | Galesburg | Galien | Gladstone |
| Gladwin | Grand Blanc | Grand Haven | Grant | Grattan |
| Greenville | Gwinn | Harbor Springs | Harrietta | Harrison |
| Hartland | Hastings | Hermansville | Hillsdale | Holland |
| Holly | Holt | Hopkins | Houghton | Howell |
| Hudsonville | Indian River | Interlochen | Ionia | Iron Mountain |
| Iron River | Irons | Ironwood | Ishpeming | Jackson |
| Jamestown | Jonesville | Kalamazoo | Kalkaska | Kent City |
| Keweenau | Lake Leelanlau | Lake Linden | Lake Odessa | Lake Orion |
| Lapeer | LeRoy | Leslie | Lexington | Linwood |
| Lowell | Luther | Mackinaw City | Mackinac Island | Mancelona |
| Manchester | Manistee | Manton | Marine City | Marion |
| Marne | Marquette | Marshall | Martin | Mason |
| Mayville | McBain | Menominee | Michigamme | Middleville |
| Midland | Milan | Moline | Monroe | Morley |
| Mulliken | Napoleon | Nashville | Negaunee | New Baltimore |
| New Boston | New Buffalo | Newaygo | Newberry | New Haven |
| Niles | Northport | Norway | Olivet | Onekama |
| Oscoda | Otsego | Owendale | Oxford | Peck |
| Pellston | Perkins | Petoskey | Pinckney | Plainwell |
| Port Huron | Port Sanilac | Portland | Potterville | Powers |
| Rapid River | Reed City | Reese | Republic | Richland |
| Rock | Rockford | Rockwood | Romeo | Rosebush |
| Saginaw | St. Charles | St. Clair | St. Helen | St. Ignace |
| St. Joseph | Sand Lake | Sandusky | Saranac | Sault St. Marie |
| Scotts | Scottville | Sebawaing | Snover | South Lyon |
| Sparta | Standish | Stephenson | Three Oaks | Traverse City |
| Trout Lake | Trufant | Tustin | Ubly | Unionville |
| Vassar | Vermontville | Vicksburg | Wakefield | Walloon Lake |
| Washington | Watersmeet | Watervliet | Wayland | West Branch |
| Williamsburg | White cloud | Whitmore lake | Willis | Wolvervine |
| Zeeland |  |  |  |  |

#### Ohio

Access Areas are designated as B, C and D.  See tariff for additional information.

- The Network Access Line is a rate element that equates to the local loop of the Centrex Line, i.e., the part of the line from the customer’s premises to the serving Central Office.

- The end user's serving Central Office determines the applicable Access Area for the main location rate.

- When a Centrex Station is in FX or Independent Territory, Access Area D is appropriate.

- CPXHX/TN XXX-XXXX/SPP VT3 is the entry that is placed on the Service Order unless Quantity Discounts apply.

- The quantity is based upon Trunk Equivalents.

##### Network Access Area (CPXHX) Quantity Discounts

- With a minimum commitment of 36 months, quantity discounts are available based upon the volume of Network Access Lines required by an end user's customer at a single location.

- The end user's needs a minimum of 495 Centrex stations at one location to equate to 48 Trunk Equivalent or 48 Network Access Lines.

- Monthly Rate per Network Access Line appears in Resale Tariff; same USOCS used regardless of system size (CPXHX).

## Contracts

Contract options offered are:  month-to-month, 36, 60 or 84-month term.  Effective March 5, 2007, a 12 and 24-month term is available.

- Additional lines and/or features may be added to existing Centrex service anytime during the contract period.

- Prior to the completion of a contact, an end user may enter into a new contract for a period equal to or greater than the life of the original contract with the same or larger Line Category for a term equal to or greater than the term remaining on the original contract.

- Effective January 3, 2006, during the last twelve months of a term contract, end users presently under a  36, 60 or 84-month term payment plan are eligible to extend their contract with the same Line Category for either an additional 12 or 24 month period.

  - At the end of the end user’s first extension term, the end user may exercise the option to extend the contract again up to two additional times provided that at the time of expiration, extension terms are still offered.

  - Standard termination charges apply for premature, total or partial discontinuance of the service.

  - Month-to-Month and ICB contract Centrex end users are not eligible for the option.

  - End users that exercise this option are not entitled to a different rate based on the overall term of the contract as extended.

- Upon expiration of the contract if the end user does not elect to subscribe to a new contract and does not request discontinuance of service, service is continued on a month-to-month basis.

- Discontinuance of service prior to contract expiration will result in termination charges.

- An end user shall not assign or otherwise transfer their rights or obligations under any Centrex arrangement without prior written consent of AT&T.

- End users who sign a 12 or 24 month Centrex contract will receive a discount on the monthly recurring Centrex Basic and Electronic Key Line rates.

- Should customer decide to terminate service prior to the expiration of the contract period, customer will be required to pay an early termination fee.

# Footnotes

CLECAM05-295, CLECAM05-297, CLECAM07-022