Automatic Route Selection/Flexible Route Selection (ARS/FRS)

Description	3

Aliases	3

How to Use the Feature	3

Dial Access Codes - Basic and Deluxe, All Switch Types	3

User Operation	4

Interdigital Timing Delay - Basic and Deluxe, All Switch Types	4

Features	4

General	4

Call Diverting / Blocking	5

900/976 - All Switch Types	5

Repair TNs & Directory Assistance - All Switch Types	5

Call Routing	5

Digit 1 Delivery (Insertion)	6

Facilities	6

Routes/Patterns	6

ARS/FRS Deluxe	7

7- to 10-Digit Screening / Blocking	8

Expensive Route Warning Tone	8

Customer Access Treatment	8

International Direct Distance Dialing (IDDD)	8

Time-of-Day Routing	9

Availability	9

Illinois	9

Indiana	10

Basic	10

Deluxe	10

Michigan	10

Basic	10

Deluxe	11

Ohio	11

Wisconsin	12

Restrictions/Limitations	12

Basic and Deluxe	12

Interactions	13

Call Forwarding - Basic and Deluxe, All Switch Types	13

Variable Over Private Facilities	13

Variable	13

Direct Connect - Basic and Deluxe, All Switch Types	13

Speed Calling - Basic and Deluxe, All Switch Types	13

Customer Access Treatment (CAT) Codes - Basic and Deluxe	13

Outgoing Deluxe Trunk Queuing, All Switch Types	14

CentrexMate Compatibility	14

Ordering	14

Procedures	14

End User Negotiations - Basic and Deluxe	14

ISDN Provisioning	15

Due Dates	15

USOCs/FIDs	15

Illinois	15

Centrex Service (CS) & Centrex ISDN	15

All Grandfathered Centrex Services	16

Indiana	17

Advanced Centrex Service	17

All Grandfathered Centrex Services	17

Michigan	18

Centrex Service (CS)	18

IIN Grandfathered Centrex Services	19

Ohio	19

Centrex Service (CS)/CSCSO	19

All Grandfathered Centrex Services	20

Wisconsin	21

Centrex Service (CS)	21

All Grandfathered Centrex Services	22

FIDs	23

Miscellaneous Ordering Procedures	23

Billing	24

Usage Billing	24

# Description

ARS/FRS provides a Centrex end user with automatic routing of outgoing calls over private facilities i.e. Foreign Exchange (FX), tie lines, or Wide Area Telephone Service (WATS).  The Centrex station user dials the ARS access code (usually a 9) followed by the telephone number.

ARS/FRS allows for the completion of calls to a public network telephone number by:

- Automatically scanning the dialed digits and selecting a first choice route for completion, or

- Selecting a subsequent route if the first choice route is not available.

The ARS/FRS feature is available as two offerings:

- ARS/FRS Basic

- ARS/FRS Deluxe (ARS/FRS Deluxe includes all features from ARS/FRS Basic)

Note:  This feature is compatible with a Centrex line, EKL/Meridian Business Set and ISDN.

## Aliases

- ARS

- FRS

# How to Use the Feature

## Dial Access Codes - Basic and Deluxe, All Switch Types

- One access code is assigned for each ARS/FRS established.

- 'Dial 9' should be used as the ARS/FRS access code only if the ARS/FRS final route is the Direct Distance Dialing (DDD) network.

- When the ARS/FRS final route is blocking, any code with one to three digits, other than '9', can be assigned as the access code, as long as it does not conflict with any of the following:

  - Centrex feature activation codes

  - Centrex intercom dialing plan

  - Other trunk group access codes

- To access a separate group of patterns, establish a separate ARS/FRS with its own access code using a separate group of trunk facilities.

- You may assign an individual non-ARS/FRS trunk access code to an ARS/FRS trunk group to enable station users without access to use trunk groups that are built into the ARS/FRS.

## User Operation

### Interdigital Timing Delay - Basic and Deluxe, All Switch Types

Note:  Interdigital Timing Delay is inherent in the switch and does not require a USOC for provisioning.

- Used by Centrex systems to verify that all digits have been dialed.

- Involves a delay of approximately 7-12 seconds.

- May be cancelled by dialing # (pound sign) on a touch-tone station immediately after dialing the number.

Signaling delay:

- Touch-tone pulsing takes 3-5 seconds.

- Dial pulsing takes 2-4 seconds longer than touch-tone.

1AESS/EWSD:

- Dial tone is heard immediately as the user goes off-hook.

- Dial ARS/FRS access code and 7- or 10-digit number desired.

- Dial # (pound sign) to cancel interdigital timing feature.

5ESS/DMS 100:

- Dial tone is heard in about one second after user goes off-hook.

- Dial ARS/FRS access code. Second dial tone is heard in about 4 seconds.

- Dial 7- to 10-digit number desired.

- Dial # (pound sign) to cancel interdigital timing feature.

## Features

### General

The following components apply to both Basic and Deluxe:

- ARS/FRS Basic allows for the completion of calls to a public network telephone number by

  - Automatically scanning the dialed digits and selecting a first choice route for completion, or

  - Selecting a subsequent route if the first choice route is not available.

- Routes may include:

  - Foreign Exchange lines (FX)

  - WATS

  - Carrier Access lines

  - Direct Distance Dialing (DDD) Network

  - Other compatible arrangements

- The final completing route is the toll network.

- ARS/FRS is composed of Facilities, Routes/Patterns and Codes.

- ARS/FRS is reached by use of an access code. See Dial Access Codes-Basic and Deluxe-All Switch Types.

#### Call Diverting / Blocking

- ARS/FRS is used for call routing, and should not be used specifically for call blocking.

- Call Diverting service may not be applied to lines accessing ARS/FRS patterns that have a final route to the Direct Distance Dialing (DDD) network.

#### 900/976 - All Switch Types

- End users who choose to block, via their ARS/FRS, can block 900 and/or 976 calls via their ARS/FRS at no charge.

- If all lines in the ARS/FRS are to be blocked, the appropriate code must be shown on the service order (this is also necessary if the end user has Centrex Mate):

  - 976 only

  - 900 only

  - 900/976

  - It is not necessary to line identify these USOC codes.

#### Repair TNs & Directory Assistance - All Switch Types

- Blocking repair TNs and calls to Directory Assistance numbers (e.g., 411 and 555) is prohibited via the ARS/FRS.

- Each Centrex line with ARS/FRS access requires a line class code (LCC) that gives the user an allowed calling area equal to or greater than the calling area of the facilities in the ARS/FRS.

- When the Centrex user places a call over the ARS/FRS that is outside its allowed calling area, the call will either:

  - Complete if it routes to a facility that can access that particular calling area, or

  - Block if it routes to a Direct Distance Dialing (DDD) based on the line class code and switch type.

#### Call Routing

- ARS/FRS automatically routes outgoing seven- and ten-digit calls to an idle facility in the end user’s dedicated trunk groups.

- The ARS/FRS checks for an available facility in the order that the end user has preprogrammed based on the first three or six digits of the number dialed. (NPA, NNX, NPA/NNX).

- Routing is selected based on the Direct Distance Dialing (DDD) numbering plan. Both three- and six-digit screening are available in the same ARS/FRS pattern group.

- If the end user’s original choices are not available, then the call will route to the Direct Distance Dialing (DDD) network or it can be blocked with an overflow tone/recorded announcement.

- If an NPA or NNX is not programmed to route to an ARS/FRS pattern, then it will default to Direct Distance Dialing (DDD) even when all patterns are blocked.  Lines with Dial 1 Plus service will overflow to the predesignated long-distance carrier.

The following types of calls will default to the Direct Distance Dialing (DDD) network because they are ineligible for routing over the ARS/FRS:

- 0+ calls

- Calls with less then seven to ten digits (e.g., 411, 611, 911)

- Intra-central office calls:

  - Each CO processes intra-CO calls utilizing dedicated intra-office trunks. Therefore, Centrex end users cannot route prefixes in their own CO over Foreign Exchange or Foreign District lines from another central office area.

- IDDD calls beginning with 011:

  - Some Other Common Carriers have WATS services that allow IDDD (International Direct Distant Dialing) calls. IDDD automatically routes to the final pattern if circuits are in the ARS/FRS pattern.

  - IDDD is an optional feature of ARS Deluxe. IF the customer wants IDDD over ARS/FRS, THEN the ARS/FRS system is billed as ARS-D.

#### Digit 1 Delivery (Insertion)

An enhancement has been added to the ARS to allow the delivery of the digit '1' ONLY to an interexchange carrier.  Example:  1+700 is not allowed

#### Facilities

Denote a particular type of trunk or circuit in the ARS/FRS. The following trunk groups can be utilized in an ARS/FRS:

- Foreign Exchange/Foreign District

- Outward WATS

- Tie Lines:

  - Senderized operation

  - Compartible dialing with the DDD network

- Announcement Trunks (final route only)

Other Common Carrier Switching System access lines, requiring the following:

- Same bill name as ARS/FRS

- Senderized operation

- Compatible dialing with the Direct Distance Dialing (DDD) network

- Calls that terminate solely via dedicated public communication service channels not usable for any private line service

- A recorded announcement for calls that are not completed due to dialing errors

- A grade of service equivalent to two calls blocked per 100 attempts or better must be provided by the OCCSS in completing calls offered over the Other Common Carrier Switching System access lines

#### Routes/Patterns

- Patterns are a unique sequence of routes arranged by end user choice and used to reach specific calling areas in the most economical manner.

- Each pattern consists of a series of facility groups called routes. The end user arranges these routes and chooses them in order of least to most expensive facility group for the particular number dialed.

- Routes denote a group of like facilities [WATS (simulated) or Tie Lines (physical)] used to complete seven- to ten-digit outgoing calls.

- Any facility group can be used as a route in multiple patterns.

- One individual facility group equals one route in a pattern.

- Each pattern can have up to four routes before the final route is seized.

- The final routes must be the same in all patterns of the ARS/FRS. Final routes that can be used:

  - Direct Distance Dialing (DDD) Network: The call will be routed as a directly dialed call, and it will be billed to the Centrex line making the call.

  - Blocked with overflow tone: The overflow tone supplies a fast busy tone indicating all trunks are busy and the caller should hang up and try again.

  - Blocked with recorded announcement: The recorded announcement advises the caller that the call cannot be placed at this time.

## ARS/FRS Deluxe

ARS/FRS Deluxe contains all of the components listed in ARS/FRS Basic plus the following:

- ARS/FRS Deluxe allows for the completion of calls to a public network telephone number by:

  - Automatically scanning the dialed digits and selecting a first choice route for completion, or

  - Selecting a subsequent route if the first choice route is not available.

- Routes may include:

  - Foreign Exchange lines

  - WATS

  - Carrier Access lines

  - Direct Distance Dialing (DDD) Network

  - Other compatible arrangements

- The final completion route may be the Direct Distance Dialing (DDD) network.

IF the Customer Access Treatment (CAT)/Line Class Code (LCC) is insufficient to complete the call, the end user may direct call attempts to be routed to an overflow tone.

- Expensive Route Warning Tone provides a warning tone to indicate the selection of an expensive route (as defined by the end user).

- CAT/LCCs are required with ARS/FRS Deluxe and on each Centrex line and incoming tie line to determine the types of calls and facilities within the privileges of the associated user. These are included in the system charge for ARS/FRS Deluxe.

- Authorization Codes used with ARS/FRS Deluxe will allow a station user to dial a code to override the LCC associated with the dialing Centrex line or tie line.

- Further enhancement of the ARS/FRS Deluxe feature may also be achieved with the options of Time of Day Routing, IDDD and 7 to 10 Digit Screening/Blocking.

### 7- to 10-Digit Screening / Blocking

ARS provides screening of 7 to 10 specific digits in the 5ESS and DMS switches (EWSD under development). This allows an end user to block calls to particular telephone numbers without blocking the entire NPA or prefix.  Contact your Service Manager to coordinate due dates.

### Expensive Route Warning Tone

Expensive Route Warning Tone (ERWT) is a standard feature with ARS/FRS Deluxe. This feature provides a warning tone to indicate the selection of an expensive route.    ERWT is given under the following conditions:

- A route marked as expensive is selected by ARS/FRS for a call.

- The call being processed has not been queued.  Note:  A call that has been off-hook queued or callback queued is not given ERWT.

- The NCOS is selected to receive ERWT.

ERWT is not given to the following:

- Three-way calls

- Transferred calls

- Calls with overlap outpulsing

- Calls that are forwarded

- Attendant consoles

- Automatic lines

After receiving ERWT, the caller may:

- Refuse to use the expensive route and hang up.

- Activate call back queuing.

- Wait for the predetermined time-out period and allow the call to terminate on the most expensive route.

### Customer Access Treatment

- Customer Access Treatment (CAT) defines the calling privileges associated with a line.

- Each outgoing route within a routing pattern is also assigned an LCC that identifies the minimum level of privilege needed to access the facility.

- The originating line must have an LCC equal to or greater than that of the facility to be used.

### International Direct Distance Dialing (IDDD)

- IDDD allows end users to access international points through their ARS/FRS for the fastest and most economical connections.

- The user activates the feature by dialing the following:

  - Network access code

  - IDDD access code (011)

  - Country code

  - National number

### Time-of-Day Routing

- Time-of-Day Routing enables cost-effective use of facilities by allowing or denying route choices based on the time of day.

- The time can be set according to the rate schedules for the carriers (e.g., public network, common carriers).

- The route choices can also be based on the day of the week to account for weekends and holidays.

- Up to 16 distinct routing patterns can be employed by a single time-of-day Routing scheme.

# Availability

## Illinois

| Centrex System | 1AESS | 5ESS | DMS 100 | EWSD |
| --- | --- | --- | --- | --- |
| Centrex Service (CS) * | All | All | All | All |
| Basic 2+ (grandfathered) | All | All | All | All |
| Basic 3 (grandfathered) | All | All | All | All |
| CSS (grandfathered) | All | All | All | All |
| IIN100 (grandfathered) | All | All | All | All |
| IIN Plus (grandfathered) | All | All | All | All |
| Business Solutions (BS) | No | No | No | No |
| Centrex ISDN | All | All | All | All |

Note:  If the Centrex system is not shown, then the feature is not available.

*Some options are currently available only to end users served in digital offices or are not available.  Check with your Service Manager.

## Indiana

### Basic

| Centrex System | 1AESS | 5ESS | DMS 100 | EWSD |
| --- | --- | --- | --- | --- |
| Centrex Service | All | All | All | All |
| Centrex Communication System (CSS) (grandfathered) | All | All | All | All |
| Centrex I (grandfathered) | All | All | All | All |
| Centrex II (grandfathered) | All | All | All | All |
| Advanced Ctx Service ISDN | All | All | All | All |

### Deluxe

| Centrex System | 1AESS | 5ESS | DMS 100 | EWSD |
| --- | --- | --- | --- | --- |
| Advanced Centrex Service | N/A | N/A | N/A | N/A |
| Centrex Communication System (CSS) (grandfathered) | N/A | N/A | N/A | N/A |
| Centrex I (grandfathered) | N/A | N/A | N/A | N/A |
| Centrex II (grandfathered) | N/A | N/A | N/A | N/A |
| Advanced Ctx Service ISDN | N/A | N/A | N/A | N/A |

Note:  If the Centrex system is not shown, then the feature is not available.

## Michigan

### Basic

| Centrex System | 1AESS | 5ESS | DMS 100 | EWSD |
| --- | --- | --- | --- | --- |
| Centrex Service (CS) | All | All | All | All |
| Centrex IV (grandfathered) | All | All | All | All |
| Centrex V (grandfathered) | All | All | All | All |
| Centrex DS (grandfathered) | All | All | All | All |
| IIN Centrex (grandfathered) | All | All | All | All |
| Business Solutions (BS) | No | No | No | No |
| Centrex ISDN | All | All | All | All |

### Deluxe

| Centrex System | 1AESS | 5ESS | DMS 100 | EWSD |
| --- | --- | --- | --- | --- |
| Centrex Service (ACS) | All | All | All | All |
| Centrex IV (grandfathered) | N/A | N/A | N/A | N/A |
| Centrex V (grandfathered) | N/A | N/A | N/A | N/A |
| Centrex DS (grandfathered) | All | All | All | All |
| IIN Centrex (grandfathered) | All | All | All | All |
| Centrex ISDN | All | All | All | All |

Note:  If the Centrex system is not shown, then the feature is not available.

## Ohio

| Centrex System | 1AESS | 5ESS | DMS 100 | EWSD |
| --- | --- | --- | --- | --- |
| Centrex Service (CS)/CSCSO | All | All | All | All |
| Centrex 100 (grandfathered) | All | All | All | All |
| Centrex Zone Type I (grandfathered) | All | All | All | All |
| Centrex Zone Type II (grandfathered) | All | All | All | All |
| Centrex Large Non Zone (grandfathered) | All | All | All | All |
| LSI (grandfathered) | All | All | All | All |
| Business Solutions (BS) | No | No | No | No |
| Centrex ISDN | All | All | All | All |

Note:  If the Centrex system is not shown, then the feature is not available.

## Wisconsin

| Centrex System | 1AESS | 5ESS | DMS 100 | EWSD |
| --- | --- | --- | --- | --- |
| Centrex Service (CS) | All | All | All | All |
| Centrex III (grandfathered) | All | All | All | All |
| Custom Centrex I (grandfathered) | All | All | All | All |
| Custom Centrex II (grandfathered) | All | All | All | All |
| System 20 (grandfathered) | All | All | All | All |
| Centrex ISDN | All | All | All | All |

Note:  If the Centrex system is not shown, then the feature is not available.

## Restrictions/Limitations

### Basic and Deluxe

- All ARS/FRS patterns must have the Direct Distance Dialing (DDD) network, overflow tone, or a recorded announcement as the final route. No combination is allowed within the same group of patterns accessed by one access code.

- It is the responsibility of the CLEC to notify SBC regarding updates to the end user’s ARS patterns, whether caused by changes in the end user’s private network or the public switched network.

- Tie lines must be senderized with a dialing pattern that is consistent with the Direct Distance Dialing (DDD) network.

- Fixed WATS route advances from WATS facilities accessed via ARS/FRS do not count as additional routes.

- Patterns without final route to the Direct Distance Dialing (DDD) network may be offered only if an end user subscribes to a sufficient number of facilities. These facilities must provide an adequate level of service to avoid interrupting or interfering with the service of others.

The following types of calls are ineligible for routing over facilities within an ARS/FRS and will default to the Direct Distance Dialing (DDD) network when dialed:

- 0+ calls

- Calls with less than seven to ten digits (e.g., 411, 611, 911)

- Intra-central office calls

- IDDD calls starting with 011

Exception:  If an end user has ARS Deluxe, then IDDD calls can be routed over private facilities.

### Interactions

#### Call Forwarding - Basic and Deluxe, All Switch Types

##### Variable Over Private Facilities

- Call Forwarding Over Private Facilities is an optional Centrex line feature.

- Centrex line users may establish routing of incoming calls to specific private facilities. Examples are Common Control Switching Arrangement (CCSA), WATS, Foreign Exchange/District, Tie Lines arranged for senderized operation, and the Message Toll Service Network.

##### Variable

- Call Forwarding Variable cannot be activated over ARS/FRS.

- Station users who will use Call Forwarding Variable features to forward calls out of the Centrex must be given a separate Direct Distance Dialing (DDD) access code to use with this feature.

#### Direct Connect - Basic and Deluxe, All Switch Types

- Direct Connect to ARS/FRS is available on Centrex lines with the Direct Connect feature programmed to an ARS/FRS access code.

- May be used in lieu of PBX trunks in a PBX system that does not have Automatic Routing.

#### Speed Calling - Basic and Deluxe, All Switch Types

- Lines with Speed Calling using ARS/FRS to call out of the Centrex must be programmed with the speed call lists showing the telephone numbers dialed. These must include the ARS/FRS access code as the first digit(s) dialed (e.g., 9+1+). Without this programming, the call will not route over the ARS/FRS.

#### Customer Access Treatment (CAT) Codes - Basic and Deluxe

- The CAT codes give the Centrex station user the capability to access ARS/FRS.

#### Outgoing Deluxe Trunk Queuing, All Switch Types

- Outgoing Deluxe Trunk Queuing can be used with ARS/FRS Deluxe, permitting station users to be placed in a queue whenever all facilities in the first choice route in a pattern are in use.

## CentrexMate Compatibility

| Centrex Feature | 1AESS | 5ESS | DMS 100 | EWSD |
| --- | --- | --- | --- | --- |
| ARS/FRS | X | X | X | X |

Note:  The ARS/FRS feature cannot be changed or added via Centrex Mate. Only the Centrex lines (SXP++) with ARS/FRS can be changed to allow access to the ARS/FRS.

# Ordering

## Procedures

### End User Negotiations - Basic and Deluxe

- Make a list of the facilities the end user has chosen to utilize.

- Determine the most economical routes for facilities being used on IntraLATA and state area calls and the facilities the end user will use to make these calls. Apply the same method for InterLATA calls.

- Provide an analysis based on usage studies and end user calling patterns of existing end user facilities in order to assist the end user in determining routes and patterns.

- Design the ARS/FRS with the end user’s preferences and the most economical calling patterns in mind. Use the following criteria in the ARS/FRS design:

- First Route - Must be most cost effective route for the area called.

- Second, Third, Fourth Routes:

    - Should be arranged in the order of most economical to least economical facility for the area called.

    - Must have a calling area greater than or equal to the first route.

- Final Route:

    - Must be the same for all patterns.

    - Must be selected by the end user from two options: Direct Distance Dialing (DDD) or blocking with tone or announcement.

Note:  Blocking with tone or announcement is used only when the end user subscribers to an adequate number of facilities so that a minimum number of calls will actually be blocked.

Tone does not require any additional facilities; however, a recorded announcement requires billable announcement trunk(s) and a recording arrangement similar to those used with UCD.

- Obtain approval of the ARS/FRS design from the end user.

- Contact the LSC (Local Service Center) regarding provisioning forms for the ARS/FRS service.

- Submit all forms to the LSC.  If sending order requests electronically, fax ARS forms using same PON so that the LSC can correlate both parts of the order.

## ISDN Provisioning

- ISDN provisioning requires switch specific provisioning forms as well as a service request.

- Contact your Service Manager regarding completing the provisioning forms.

## Due Dates

- Due Dates must be negotiated with your SBC Account and/or Service Manager.

- The average interval is 10 business days or the date of the facilities associated with the ARS, whichever is longer.

## USOCs/FIDs

Note:  If the Centrex system is not listed, then the feature is not available.

### Illinois

#### Centrex Service (CS) & Centrex ISDN

Basic

| Centrex Feature | Billing USOC |
| --- | --- |
| Initial pattern | AR9 |
| Each additional pattern | ARH |

Exception:

In the 5ESS, a ZUSOC code ZARSC with a modifying FID of ZGRP is required for each line (SXP++) accessing the ARS/FRS.

Deluxe

| Centrex Feature | Billing USOC |
| --- | --- |
| Per system | AQVPS* |
| Each additional pattern | ARH |
| IDDD Dialing, per system | A1GPS |
| 10-Digit Screening, per translation | AHAPS* |
| Time-of-Day Routing, per schedule | TMQ |
| Digit 1 Delivery | DTN1X |

Note:  *Includes the initial pattern (3 or 6 digit screening), Expensive Route Warning Tone and Facility Restriction Level.

#### All Grandfathered Centrex Services

Basic

| Centrex Feature | USOC |
| --- | --- |
| ARS/FRS Basic, common equipment per system /per access code | ART |
| 3 Digit Screening, per arrangement | AR9 |
| 6 Digit Screening, per NPA Code | ARH |
| Route Selection Pattern, Final Route to Direct Distance Dialing (DDD), each | AXR |
| Route Selection Pattern, Final Route to Overflow Tone or Announcement Trunk, each | ARK |
| Route Selection Pattern, per Facility Terminated in Pattern, per Line or Trunk | AR5 |

Exception:

In the 5ESS, a ZUSOC code ZARSC with a modifying FID of ZGRP is required for each line (SXP++) accessing the ARS/FRS.

Deluxe

| Centrex Feature | Billing USOC |
| --- | --- |
| Common Equipment per ARS/FRS Access Code | ASH |
| Route Selection Pattern, per facility terminated in patterns, per line or trunk | ASJ |
| Route Selection Pattern, by NPA code only (3 digit translation, per pattern) | ASK |
| Route Selection Pattern, by NPA and Central Office Code (6 digit translation, per pattern, per NPA) | ASO |
| Additions of Patterns, per pattern | ASK |

### Indiana

#### Advanced Centrex Service

Basic

| Centrex Feature | Billing USOC |
| --- | --- |
| Common Equipment per ARS/FRS access code | ART |
| Routing Arrangements, based on first 3 digits dialed with final route to Direct Distance Dialing (DDD) network, or final route to overflow tone or announcement trunk, per pattern, each | ARG |
| Routing Arrangements, based on first 6 digits dialed with final route to Direct Distance Dialing (DDD) network, or final route to overflow tone or announcement trunk, per pattern, each | ARK |
| Route Selection Patterns, per facility terminated in patterns, per line or trunk | AR5 |

Exception:

In the 5ESS, a ZUSOC code ZARSC with a modifying FID of ZGRP is required for each line (SXP++) accessing the ARS/FRS.

#### All Grandfathered Centrex Services

Basic

| Centrex Feature | Billing USOC |
| --- | --- |
| Common Equipment per ARS/FRS access code | ART |
| Routing Arrangements, based on first 3 digits dialed, per arrangement | AR9 |
| Routing Arrangements, based on first 6 digits dialed, per NPA selected* | ARH |
| Route Selection Patterns, final route to overflow tone or announcement trunk, each | ARK |
| Route Selection Patterns, per facility terminated in patterns, per line or trunk | AR5 |
| Termination Arrangements, common Equipment, per group of FX/district, or tie trunks (determined by access code), each group | 479 |
| Termination Arrangements, termination for each FCO or FX/district line | AA1 |

### Michigan

#### Centrex Service (CS)

Basic

| Centrex Feature | Billing USOC |
| --- | --- |
| Initial pattern | AR9 |
| Each Additional Pattern | ARH |
| Permissive home NPA dialing, per ARS | PHNPG |

Exception:

In the 5ESS, a ZUSOC code ZARSC with a modifying FID of ZGRP is required for each line (SXP++) accessing the ARS/FRS.

Deluxe

| Centrex Feature | Billing USOC |
| --- | --- |
| Per System | AQVPS |
| Additional Pattern, per pattern | ARH |
| Permissive home NPA dialing, per ARS | PHNPG |
| 7 - 10 Digit Screening, per translation | AHAPS |

#### IIN Grandfathered Centrex Services

Basic

| Centrex Feature | Billing USOC |
| --- | --- |
| Per System | AB8 |
| Per ARS Group (per access code) | F5GPG |
| Routing Arrangements, based on first 3 digits dialed, per arrangement | A3A |
| Routing Arrangements, based on first 6 digits dialed, per NPA selected* | ABM |
| Routing Arrangements, 10 Digit Screening, per translation | FROPN |
| Routing Arrangements, permissive home NPA dialing, per ARS | PHNPG |
| Routing Arrangements, blocking of 7 digit telephone number, per ARS location | FROPA |

Exception:

In the 5ESS, a ZUSOC code ZARSC with a modifying FID of ZGRP is required for each line (SXP++) accessing the ARS/FRS.

### Ohio

#### Centrex Service (CS)/CSCSO

Basic

| Centrex Feature | Billing USOC |
| --- | --- |
| Initial pattern | AR9 |
| Each Additional pattern | ARH |

Exception:

In the 5ESS, a ZUSOC code ZARSC with a modifying FID of ZGRP is required for each line (SXP++) accessing the ARS/FRS.

Deluxe

| Centrex Feature | Billing USOC |
| --- | --- |
| Per System | AQVPS |
| Each Additional pattern | ARH |
| IDDD Dialing, per system | A1GPS |
| 7 - 10 Digit Screening, per translation | AHAPS |
| Time of Day Routing, per Schedule | TMQ |
| Digit 1 delivery | DTN1X |

#### All Grandfathered Centrex Services

Basic

| Centrex Feature | Billing USOC |
| --- | --- |
| Common Equipment per ARS/FRS access code | ART |
| Routing Arrangements, based on first 3 digits dialed, per arrangement | AR9 |
| Routing Arrangements, based on first 6 digits dialed, per NPA selected | ARH |
| Route Selection Patterns, final route to Direct Distance Dialing (DDD) network, each | AS5 |
| Route Selection Patterns, final route to overflow tone or announcement trunk, each | ARK |
| Route Selection Patterns, per facility terminated in patterns, per line or trunk | AR5 |
| Termination Arrangements, common Equipment, per group of FX/district, or tie trunks (determined by access code), each group | 479 |
| Termination Arrangements, termination for each FCO or FX/district line | AA1 |

Exception:

In the 5ESS, a ZUSOC code ZARSC with a modifying FID of ZGRP is required for each line (SXP++) accessing the ARS/FRS.

Deluxe

| Centrex Feature | Billing USOC |
| --- | --- |
| Common Equipment per ARS/FRS access code | ASH |
| Route Selection Patterns, per facility terminated in patterns, per line or trunk | ASJ |
| Route Selection Patterns, by NPA code only (3 digit translation, per pattern) | ASK |
| Route Selection Patterns, by NPA and Central Office Code (6 digit translation, per pattern, per NPA) | ASO |
| Route Selection Patterns, addition of Patterns, per pattern | ASK |
| Rearrangements for Additional Pattern groups for Time of Day routing, each arrangement | ASZ |

### Wisconsin

#### Centrex Service (CS)

Basic

| Centrex Feature | Billing USOC |
| --- | --- |
| Initial pattern | AR9 |
| Each additional pattern | ARH |

Exception:

In the 5ESS, a ZUSOC code ZARSC with a modifying FID of ZGRP is required for each line (SXP++) accessing the ARS/FRS.

Deluxe

| Centrex Feature | Billing USOC |
| --- | --- |
| Per System | AQVPS |
| Each additional pattern | ARH |
| IDDD Dialing, per system | A1GPS |
| 7 - 10 Digit Screening, per translation | AHAPS |
| Time of Day Routing, per Schedule | TMQ |
| Digit 1 delivery | DTN1X |

#### All Grandfathered Centrex Services

Basic

| Centrex Feature | Billing USOC |
| --- | --- |
| Common Equipment per ARS/FRS access code | ART |
| Routing Arrangements, based on first 3 digits dialed, per arrangement | AR9 |
| Routing Arrangements, based on first 6 digits dialed, per NPA selected* | ARH |
| Route Selection Patterns, final route to Direct Distance Dialing (DDD) network, each | AS5 |
| Route Selection Patterns, final route to overflow tone or announcement trunk, each | ARK |
| Route Selection Patterns, per facility terminated in patterns, per line or trunk | AR5 |
| Termination Arrangements, common Equipment, per group of FX/district, or tie trunks (determined by access code), each group | 479 |
| Termination Arrangements, termination for each FCO or FX/district line | AA1 |

Exception:

In the 5ESS, a ZUSOC code ZARSC with a modifying FID of ZGRP is required for each line (SXP++) accessing the ARS/FRS.

Deluxe

| Centrex Feature | Billing USOC |
| --- | --- |
| Common Equipment per ARS/FRS access code | ASH |
| Route Selection Patterns: per facility terminated in patterns, per line or trunk | ASJ |
| Route Selection Patterns: by NPA code only (3 digit translation, per pattern) | ASK |
| Route Selection Patterns: by NPA and Central Office Code (6 digit translation, per pattern, per NPA) | ASO |
| Route Selection Patterns: Addition of Patterns, per pattern | ASK |
| Rearrangements - Arrangements for Additional Pattern groups for Time of Day routing, each arrangement | ASZ |

## FIDs

| FID | Switch Type | Description | Use |
| --- | --- | --- | --- |
| ZGRP | 5ESS | Private Facility Group Name | Indicates that the Centrex station has access to a private facility group and which one. Order placement: FEATURE DETAIL Field following the ARS Feature in the Feature field. Example: ZARSC/SGRP NAME |

## Miscellaneous Ordering Procedures

New Centrex Service Orders:

- New Centrex Service can only be ordered manually at this time.

- The forms to build a new Centrex Common Block can be obtained by calling the LSC.

- The forms to build an ARS/FRS are also obtained from the LSC at this time.

Subsequent Centrex Orders:

- Centrex class of service must be shown on the LSR form in the 'TOS' field.

- Centrex service features are ordered on a REQ TYPE 'P'.

- USOCs that are common equipment to the ACS Centrex or Grandfathered Centrex are shown on the LSR in the Account Feature field.

- USOCs that are applicable to the Centrex station are shown on the Centrex Service Request Form in the Feature Field. (This application varies by switch type)

# Billing

Refer to state tariff for more information regarding recurring and non-recurring charges.

Note:  Contact your Account Manager for customer-specific contracts for ordering and billing information.

- Charges for the ARS/FRS are billed to the Centrex main account.

- Charges for associated facilities or terminating arrangements are billed per the normal billing procedure for those services.

- One service order charge business (SOBC) is applicable to establish an ARS/FRS. (N/A in MI.)

- If ARS/FRS is established at the time the Centrex system is installed, the Centrex account is billed (SOCB) to establish the account. No additional SOBC applies for the ARS/FRS.

- Rearrangement charges are billed for additions, rearrangements, deletions, or modifications of patterns. The exact charges applicable depend on the actual work being done on the ARS/FRS.

Programming charges and installation intervals for ARS/FRS changes involving Other Common Carrier Special Services (OCCSS) facilities must be coordinated by your Service Manager.

## Usage Billing

- Calls completed over the ARS/FRS to a particular facility will be billed against that facility. The Centrex line originating the call will not be identified unless the end user subscribes to a call detail product such as Call Detail Reporting Service (CDRS) or Station Message Detail Recording (SMDR).

- IntraLATA calls that complete over the Direct Distance Dialing (DDD) network will be billed to the Centrex line originating the call.

- InterLATA calls that complete over the Direct Distance Dialing (DDD) network will be billed by the InterLATA carrier subscribed to by that Centrex line.