Advanced Centrex Service - Indiana

Description	2

Aliases	3

Features	3

General	3

Basic	4

Optional	5

Availability	7

Sunsetted Centrex	7

Restrictions/Limitations	8

General	8

Feature Limitations	8

Automatic Callback	8

Call Forwarding Over Private Facilities	9

Call Park	9

Caller ID	9

Conference Services	9

Direct Connect	9

Directed Call Park	10

Distinctive Ringing and Call Waiting Tone	10

Intercom	10

Last Number Redial	10

FX termination for Centrex	10

How to Use the Product	10

End user Premises Equipment (CPE) Involvement	11

Pre-Ordering	11

Ordering	11

End User Negotiations	11

Establish Centrex Service/Cuts	11

Listed Directory and Billing Number	12

Disconnecting Stations	13

Move Service	13

Add Stations	14

PBX/MFE on Centrex	15

Joint Tenant Service	15

Storage Stations	16

Automatic Intercept	16

Listings	16

Due Dates	17

Standard Service Order Intervals	17

USOCs	17

Classes of Service	17

Intercom USOCs	18

Station USOC	18

Feature USOCs	20

Optional Features USOCs	21

Other Station USOCs	24

E911 USOCs	24

PICC (Primary InterExchange Carrier Charge)	24

Long Term Number Portability Surcharge (NSR)	24

Zone USOCs	24

Centrex Group Number	24

FIDs	25

Customer Access Treatment Codes (CAT)	30

Line Class Code (LCC)	31

5ESS Non-Hospital	32

5ESS Hospital	35

5ESS Joint Tenant	36

TGS (5ESS only)	38

DMS100 LCC	38

EWSD/1AESS	38

Joint Tenant	39

DMS10	39

Miscellaneous Ordering Procedures	39

Master Agency Billing	39

Billing	40

Basic System Equipment USOCs	40

Suburban Zone USOCs	40

Station Feature USOCs	41

Station Service USOCs	41

Non-Centrex to Centrex Change Charge USOCs	42

System Feature USOCs	42

Conference Arrangement	42

Music On Hold	43

Other Common Carrier (OCC Access)	43

Switched Services Network Access Terminals	43

Terminating Equipment	43

Foreign Exchange Service	43

Joint Tenant Service Billing	44

Off Premises Extensions USOCs	44

Bridged Station (DPA)	44

Primary/Secondary Premises (SLA)	44

Intercept Services	45

End User Common Line Charge (EUCL)	45

Handicap Surcharge/Dual Party Relay Service (DPRS)	46

Implied Elements	46

Channel Equivalency	46

Trunk Equivalency	47

Minimum Billing/Termination	49

Centrex Termination Charges	49

Payment Options/Contracts	49

# Description

Important: Packet switching has been Grandfathered effective as follows:

- Illinois and Michigan - July 5th, 2005

- Indiana and Ohio - July 16, 2005

- Wisconsin - July 31, 2005

Advanced Centrex Service (ACS) is an electronic system utilizing stored program control in the central office.

- Centrex is a central office based service, which is an alternative to premises-based PBX, Multifunction and Key systems.

- Advanced Centrex Service requires a minimum of 11 primary stations at the main location for the same end user.

- Centrex is a complete communication system that is individually designed for each end user.   A wide range of line features and system enhancements are available with Advanced Centrex to allow the end user to tailor the service to meet the specific needs of the business.

- Centrex Electronic Key line service provides the capability for an EKL set with preprogrammed push button features to be utilized on a specially provisioned line. EKL/Business Set service is not covered in this document.

- Integrated Services Digital Network (ISDN) provides an integrated voice/data communications capability for the transmission of circuit switched voice, circuit switched data and packet switched data. ISDN Centrex-National offers feature and capabilities that are standardized with all types of central office switches. ISDN-Centrex Custom offers features, which require the use of proprietary CPE. ISDN features and charges are not covered in this document.

## Aliases

ACS

# Features

## General

- Centrex includes the use of CO switching equipment and facilities necessary for the following:

  - Station-to-Station Dialing

  - Station Hunting

  - Direct Inward/Outward Dialing

  - Automatic Identification of Outward Dialing

  - Call Transfer-All Calls/Three-Way Calling

  - Consultation Hold for incoming and outgoing calls

  - Night Service

  - Touch-Tone

- These stations and features are included in the basic service offering. Additional stations and optional features that provide other services are also available.

- The features are activated, deactivated, and changed by preparing a service order and by interpreting and entering the 'feature' information into the CO switch.

## Basic

Centrex includes certain features in the basic monthly rate for service. Those features (and USOCs where applicable) are as follows:

| Feature | USOC or ZUSOC | Modifying FID |
| --- | --- | --- |
| Call Forwarding Variable§ | ZCFV1 | --- |
| Call Forwarding - Busy§ | ZCFBA | ZTN |
| Call Forwarding - Don't Answer§ | ZCFDA | ZTN, RCYC |
| Call Hold*§ | ZCVLD |  |
| Call Pick-Up§ | ZXAPU | CPG$ |
| Call Waiting - All Calls, Terminating§ | ZCWTG | --- |
| Call Diverting |  |  |
| Call Transfer |  |  |
| Conference Calling – Three Way |  |  |
| Consultation Hold |  |  |
| Deny Terminating |  |  |
| DID (Direct Inward Dial)* | --- | --- |
| DOD (Direct Outward Dial)* | --- | --- |
| Distinctive Ringing/Call Waiting Tone |  |  |
| Intercom Calling |  |  |
| Night Service | See Consoles | --- |
| Speed Calling - Long§ - Controller - Shared user | ZSCC3 ZSC3O | SCG# SCG# |
| Speed Calling - Short - controller§ | ZSCSL | SCG# |
| Station Hunting | --- | --- |
| Station-to-Station Dialing | --- | --- |
| Touch-Tone Service | TTB | --- |
| Transfer Call to Restricted Station |  |  |
| Message Waiting Indicator-Audible |  |  |

*Feature not available with intercom-only stations.
§Optional feature.

- If a USOC or modifying FID is not indicated, then one is not required.
Note:***/ZTN requires the number to which calls are forwarding. The ZTN should be formatted exactly as it would be dialed( e.g. 9,1,312-555-5555)

- #SCG represents the Speed Call Group

- CPG (Call Pick Up Group) requires Call Pick Up Group Number to be entered (1-4 numeric characters):

  - When establishing a new CPG, the CLEC is required to use placeholders (AA) for all members of the new CPG.

  - When adding a telephone number to an existing CPG, the existing CPG from the CSR should be used.

  - When adding a telephone number to existing CPG, and the end user has ServiceMate service, the CLEC must list the CPG the line is being added to.

## Optional

Centrex does not include the following Centrex features in the basic monthly rate for service. The activation of these features is optional and additional charges apply.

| Feature | USOC | Modifying FID * |
| --- | --- | --- |
| Centrex Message Signal Interface | See CMSI document | --- |
| Centrex Virtual Network | See Virtual Network document |  |
| Attendant Console Feature Package Attendant Camp-On Attendant Control of Trunk Group Access |  |  |
| Automatic Call Back Per system Per station |  |  |
| Automatic Route Selection-Basic (ARS-B) Automatic Route Selection – Deluxe Authorization Codes Deluxe Queuing Facilities Restrictions Level Time of Day Routing |  | --- |
| Authorization Codes |  |  |
| Call Forwarding Over Private Facilities Per system Per station |  |  |
| Call Detail Recording System |  | --- |
| Call Forwarding Busy-Don't Answer Internal/External Split - Busy per station - Don't Answer per station | - ZB5ES - ZD1ES | CFBE, CFBI / ZTN CFDE, CFDI § |
| Caller ID |  |  |
| Caller ID with Name |  |  |
| Custom Calling Name on Centrex |  |  |
| Call Park/Directed Call Park/Directed Call Park with Barge-in |  |  |
| Conference Arrangement – Attendant and/or Station Dial Control |  |  |
| Conference Arrangement Large |  |  |
| Customer Station Rearrangement | See ServiceMate |  |
| Datapath line |  |  |
| Direct Connect | ZAULN | ZTN § |
| Distinctive Ringing and Call Waiting Tone |  |  |
| End user Dialed Account Recording |  | --- |
| End user Station Rearrangement | See ServiceMate | --- |
| Music On Hold | MOHPS | --- |
| Directed Call Pick-Up Non-Barge In§ | ZDCPU | --- |
| Extended Intercept Service |  |  |
| Music On Hold (Note: Only one music source allowed) |  |  |
| Open Interface - See Open Interface DS1 Term | OP3, OP6 | --- |
| Other Common Carrier Access | OAL | --- |
| Station Message Detail Recording |  | --- |
| Station Restriction |  |  |
| Toll Restricted Station | ZDGNY | --- |
| Switched Services Network Access | 9O1 | --- |
| Terminating Equipment | RXN | --- |
| Uniform Call Distribution | See UCD | --- |

* If there is no modifying FID indicated, then one is not required.
§ ZTN, CFBE, CFBI, CFDE and CFDI represent the number to which calls are forwarding. They should be formatted to reflect the forwarded to number exactly as it would be dialed (e.g. 9,1,312 555-5555).

Electronic Key Line - See Electronic Key Line (EKL) or Business Set.

# Availability

Centrex is provided in COs served by the following switch types:

- 1/1AESS

- 5ESS

- DMS 100

- DMS 10

- Siemens

- ACS is provided subject to facility availability.

## Sunsetted Centrex

Sunsetted services means that the tariff has been withdrawn and any end users currently on that tariff must be moved on to the most current tariff, if they want to retain the service.   Sunsetted Centrex services are no longer available in the tariff. Only accounts with an existing contract can have these types of services.

| IF | THEN |
| --- | --- |
| Contract is expired | Account CANNOT be resold and must be converted to Centrex Service. The LSR will be rejected. Note: If the Centrex Account is Sunsetted, it must be changed to the current Retail Centrex offering prior to Resale conversion /migration. |
| Contract is NOT expired | It can be resold. The LSC will an issue order to assume account as Resold. Note: On a conversion/migration request, a positive entry must be stated on the Remarks section of the LSR, "Contract NOT expired on Sunsetted Centrex - convert to Resale Centrex. |

## Restrictions/Limitations

## General

- Centrex is offered only as a complete service. The exchange access or intercommunication portions of the Centrex Station charges are not offered separately.

- Centrex requires a minimum of 11 primary stations at the main location for the same end user.

- Centrex is provided at the option of AT&T and is furnished subject to CO switching capability and the availability of outside plant facilities.

- Variations in the switching and control equipment used may cause differences in the operation or availability of certain features.

- Suspension of service, (vacation service), is not permitted.

- Advanced Centrex is available in Indiana only.

- Dual Service is not available with ACS.

## Feature Limitations

### Automatic Callback

- Automatic Callback is available as a system feature but allowed or denied on a per Centrex line basis.

- Use of Automatic Callback is restricted to Centrex intragroup (intercom) calls.

- Cannot be used for Operator “0” calls

- Conditions that inhibit Automatic Callback activation and cause the caller to receive a fast busy after dialing the activation code are:

  - Calling line dials the activation code when it already has a callback request active.  Each Centrex line can have one callback request active.

  - An automatic callback request is already active to the called line.

  - A called line is not in the same Centrex group as the calling line.

  - A make busy key has been activated to busy out the idle called line.

  - Time-out occurred prior to the user dialing the automatic callback activation code after receiving a busy signal.

  - The called line is in a multi-line hunt group.

  - The called line is an attendant position that is in a multi-line hunt group.

- The number of simultaneous automatic callback activations allowed depends on the CO facilities.

- Automatic Callback overrides Call Forwarding Busy and camp-on to the busy line.

- Call Pickup cannot be activated on an automatic callback request.

### Call Forwarding Over Private Facilities

- The Call Forwarding Over Private Facilities features provides the call forward all calls capability but the user may supply account and authorization codes that apply to the forwarded calls.  The user can forward over private facilities via either Private Facility Access or Automatic Route Selection.

- The originating calling party receives reorder when trunks are not available for routing.

- Call Forwarding All Calls and Call Forwarding Over Private Facilities are not assigned to the same line.

- Call Forwarding Over Private Facilities is not assigned to a feature button.

- A user cannot activate the Call Forward Private Facilities feature remotely by using the Remote Access to Call Forwarding feature; however, the feature can be deactivated via this method.

### Call Park

- Call Transfer (with Three-way calling) must be assigned for Call Park to function.

- While in “call park held” or “recall” status, the parked party cannot activate any features.

- Call Park attempts are denied by the following types of calls:

  - Calls involving the attendant console

  - Conference calls

- Recall to the Call Park Originating only occurs if it is idle and if it has not activated Call Forwarding or Do Not Disturb.

### Caller ID

- Both parties must be in the same central office for SS7 to provide identification.

- Other limitations are:

  - Automatic Callback – ringback causes calling number to be displayed.

  - Call Forwarding – Number being forwarded is displayed.

  - Distinctive Ringing – Incoming call is displayed

  - Three-Way Calling – displays the number that originated the three-way call.

### Conference Services

Large Conference Services (30 members) is available in DMS100 only.

### Direct Connect

- Feature is not changeable via ServiceMate.

- Speed Call is incompatible.

### Directed Call Park

- In order for feature to function without a dedicated key, station must either be assigned three-way calling or belong to a customer group having the option call transfer (all calls).

- Only one parked call per directory number is allowed.

- The following types of calls are incompatible:

  - Calls involving an operator position or an attendant console

  - Conference calls and calls in which other features are in effect

- While in held or recall status, parked party cannot activate any features.

- When a call primed for parking involves two DMS stations, an attempt by either party to activate three-way calling or call transfer (via switch-hook flash) cancels the Directed Call Park feature and initiates the requested feature.

### Distinctive Ringing and Call Waiting Tone

- Distinctive Ringing is incompatible with a foreign exchange Centrex line.

- Dial Call Waiting tone is applied only once to a line.

### Intercom

- Intercom Calling is only allowed between station users.

- Toll Restricted is not available with intercom only stations.

### Last Number Redial

- A maximum of 24 digits can be stored.

- Feature codes, authorization codes or partially dialed numbers are not stored.

- With Three-way calling, the called number dialed for the second leg of the call is stored.

### FX termination for Centrex

- Because the FX line terminating in a Centrex uses the facilities of two central offices, both facilities must be available simultaneously for a call to complete.

- If the Centrex Hot line station is in use and the FX facilities are idle, an incoming call will ring open.  The caller receives a ring from the FX facilities but call does not complete to the Hot Line station.  Therefore, Hot line station should be solely dedicated to FX service.

# How to Use the Product

Refer to individual Centrex feature dialing documents for operation of Centrex features.

## End user Premises Equipment (CPE) Involvement

Ameritech assumes no responsibility for the removal, storage, replacement or restoration of CPE and wiring. It is the end user’s responsibility to retain and restore CPE and its associated wiring.

# Pre-Ordering

- Complete the AT&T Centrex Reduced Input Form AT&T Centrex Reduced Input Form and forward to the LSC (Local Service Center).

- When an end user adds Centrex Lines to their Indiana Centrex Service, these lines are coterminous.  This means that these lines are added to the contract and will incur 'Termination Charges' if removed before the expiration of the contract.

# Ordering

## End User Negotiations

### Establish Centrex Service/Cuts

Centrex service may be established on single line or key line equipment.  If the end user is establishing Centrex on PBX or MFE equipment, see PBX/MFE on Centrex.

- Obtain Listing information.

- Interview end user to determine what features would be needed.

- Explain features that are inherent to every line.

  - Conference Calling / Three Way Calling

  - Consultation Hold

  - Intercom Calling

  - Touch Tone

  - Direct Inward Dialing

  - Direct Outward Dialing

- Other features are available and should be ordered at the same time to avoid delays and additional charges.

- Negotiate the dial access code to make an outgoing call (usually 9).

- Determine the intercom calling digit dial plan (usually 4).  Ensure that the digit dial plan does not conflict with any of the dial access codes.

- Negotiate telephone numbers.  See Listed Directory and Account Telephone Number.

- Determine line restrictions per line:

  - Unrestricted - can dial intercom, local, toll, information and 900/976

  - Semi-restricted - some dial patterns restricted (See Line Class Code (LSCC)).

  - Fully restricted - can dial intercom only

- Explain operation:

  - The switch-hook and access codes are used to operate features

  - The 'flash', 'recall' or 'link' button is used instead of the switchhook on some types of telephones

  - May need to program fax machines, modem, etc. with outside access codes

- Explain, if necessary, possible feature interactions with CPE equipment.

  - Single line vs. multi-line

  - CLASS vs. Non-CLASS

  - Display vs. non-display

### Listed Directory and Billing Number

The Listed Directory Number (LDN) and Billing Number (BN) are used in the following ways:

- The LDN identifies the end user for directory appearance

- The BN identifies the file location for the end user record

- The BN and the LDN do not have to be the same telephone number

- The BN can be any telephone number in the Centrex range

The end user LDN and the BN, when associated with Direct Inward Dialing (DID) Centrex service, are usually the same.

Existing end users applying for new Centrex service usually want to retain the existing LDN.  Where service is in the same CO, and if available, the LDN is included in the new range of station numbers assigned to the DID service.

| IF | THEN |
| --- | --- |
| Service is in the same CO | The existing BN on the POTS account can be used as the BN on the Centrex account even if the LDNs change. |
| Station range within the same prefix as the LDN is not available. | Encourage the end user to change to new LDNs that are within the range of station numbers to obtain the following advantage: The end user will receive better utilization of the DID service. This is especially important when trying to reduce traffic from the main answering point. Note: The end user cannot retain the LDNs if the Centrex service is going to be served out of a different CO switch. |

The prefix of the LDN or BN can be different.  This may cause future complications if, for example, re-homing occurs.  Therefore, it is recommend keeping the LDN, BN and station numbers within the same prefix.

| IF | AND | THEN |
| --- | --- | --- |
| The BN is not established as a working station on the initial cut | The end user wants to make it a working station | Issue an order to add, disconnect or change the BN as a working station. |
| The BN is established as working station | The end user wants to change or remove that number |  |

When the LDN and the DID numbers are different, a decision must be made as to how the answering point will receive internally generated calls.  The end user must choose either to:

- Activate the attendant access feature (level 0) Or,

- Include the LDN in the station dialing plan

There are cases where end users insist on keeping their LDN and the LDN is in conflict with the Centrex Dialing Plan.  For instance, the end user's current LDN is 288-9000 and the Centrex station range is 282-7420 through 282-7449.  The dialing plan calls for three digit dialing (ie., 420, 421, etc).  The 288-9000 LDN has all four digits in conflict.  The 9 is reserved for dial access to outgoing calls from the Centrex and cannot be used as the first number for station-to-station dialing.  The end user must be advised that the LDN will be part of the Centrex but all seven digits must be dialed when calling the LDN within the Centrex.

- All TNs that are to be retained must be listed.

Important:  Centrex Station Numbers cannot be reserved through the pre-order system.  To pre-order Centrex Station Numbers, fax the AT&T Address Validation/TN Reservation Form to the LSC.

### Disconnecting Stations

If an end user requests to have part of the service disconnected, eg remove one or more stations, but leave the Centrex intact, THEN the appropriate action would be to Issue a C order to remove the station numbers.

Note:  Eleven stations must stay active; all the rest can be disconnected.  If the number of stations drops below 11, it is recommended that the Centrex service be terminated.

- Determine if the end user needs a referral of calls.

### Move Service

Within Same Central Office:

Important:  Termination Charges DO NOT apply if the end user moves all stations under contract.

- An end user may move a maximum of 25 primary stations without signing a new VTPP.

- When moving 26 or more stations, the end user must sign a new VTPP unless AT&T determined that existing facilities are available.

  - Confirm all listing information (name, address, YPH, etc)

  - Validate new address in SAG (Street Address Guide)

  - Negotiate due date for service at the new location.  NOTE:  Dual service is not available on Centrex service.

To Different Central Office:

- A new VTPP is required.

- Termination liability may apply to the service at the old location

- Negotiate the dial access code to make an outgoing call (usually 9)

- Determine the intercom calling digit dial plan (usually 4).  Ensure that the digit dial plan does not conflict with any of the dial access codes.

- Negotiate telephone numbers.

- Determine line restrictions per line:

  - Unrestricted - can dial intercom, local, toll, information and 900/976.

  - Semi-restricted - some dial patterns restricted.

  - Fully restricted - can dial intercom only.

- Explain operation:

  - The switch-hook and access codes are used to operate features.

  - The 'flash', 'recall' or 'link' button is used instead of the switch-hook on some types of telephones.

  - May need to program fax machines, modems, etc., with outside access codes.

### Add Stations

- Determine service address for new station(s).

| IF | THEN |
| --- | --- |
| At same address as existing service | Go to next bullet |
| At new address | Determine facility availability, then go to next bullet. |

- Advise end user of next available station number(s) in the range.  Negotiate listing if desired.

- Negotiate line restrictions

- Determine features on the new station(s)

- Negotiate due date.

- Determine if month to month or coterminous

Important:  If the end user adds Primary or Intercom Only Stations that result in a different cell size, then in order to be eligible for the new price for that cell size, the end user must enter into a new contract equal to or greater than the existing contract.

## PBX/MFE on Centrex

- Centrex end users may have communications needs that require the use of end user Premises Equipment (CPE) classified as PBX or MFE (Multifunctional system). These end users will be provided Centrex stations at the appropriate exchange service rate for business lines or PBX trunks.

- End User access charges (EUCL) will be calculated at the Exchange service rate per business line. Trunk equivalency rating procedures do not apply.

- Stations used to provide exchange access for a PBX or MFE system are not counted as stations for cell size or minimum station requirements.

- Ground start or loop start must be shown for trunks.

- The intercom portion of the recurring rate does not apply to 'PBX' stations. However, the nonrecurring charge for the intercom portion does apply.

- Many key systems carry dual registration and the appropriate charges will be applied.

| IF | Rate Applied Is: |
| --- | --- |
| A single-line set behind a Key Service Unit (KSU) has pooled access and is hard-wired to 'pickup' or 'answer only' one CO line | Centrex rates |
| A KSU is used to select a CO line via a dialing code or the depression of a pool selection button | Exchange rate |
| Incoming pooled access occurs when an incoming call can be received by one station/line unit and transferred via the KSU to another station/line | Exchange rate |
| There is a one-to-one relationship on incoming and outgoing lines/ports, AND The system behind/in front of the automated attendant is classified with NMFE as part of the identification number, AND Transfers from one CO line to another take place by depressing the Centrex switch-hook | Centrex rates |

## Joint Tenant Service

This service is grandfathered as of November 14, 2004.

## Storage Stations

- If a station is being temporarily removed, the end user can place the contractible USOC in storage to avoid termination charges. The end user will continue to pay for the contractible USOC as if it were still in service.

Note:  End user must keep 11 stations active. All others can go into storage.

- Once a NRSX1 is placed in storage, it can be removed and reused at any new or existing location.  If stored from the primary location, it can be reused at any SLA.

- The storage NRSX+ can be converted to the required locations' cell size.  For example, a NRSX3 stored form the primary location can be removed and reused as a NRSX1 at SLA3.  This allows the end user to avoid paying for both a stored NRSX3 and a new NRSX1.

- The eligible storage USOCs are installed without TN or GB identification.

- /DES STORAGE is shown for identification.

- The storage USOCs are found in the common equipment of the CSR.  They will be stored there until a new station is installed.  At that time, the USOCs can be removed from storage and associated with the new TN being installed.

- All USOCs associated with the station TN are removed.

## Automatic Intercept

Requests for intercept are received from the CLEC at the time a disconnect, move of service or change of telephone number order is placed.

- Determine number(s) to be intercepted

- The TC OPT Field is populated with either 01 or 21 and telephone number will route to a disconnect recording

| IF | THEN |
| --- | --- |
| The telephone number to be intercepted is a listed number | No charge applies to the referral of calls. |
| The telephone number to be intercepted is not listed | A charge applies. |

## Listings

Follow standard procedures for listings. See Directory section.

## Due Dates

Effective 10/1/98, standard due date intervals have been established for all Centrex services.

### Standard Service Order Intervals

Refer to Resale Due Date Matrix for standard due date intervals.  Important: The Standard Due Date Intervals are in addition to contract or negotiations service center processing intervals.

Centrex Standard Due Date intervals are based on Complex vs. Non-Complex services and can involve central office translations and/or line provisioning.

All standard due date intervals assume:

- Central office hardware and/or software is in place.

- Local facilities (cable pairs) are available.

- Force and load date is available if a premise visit is required, based on number of lines being installed.

## USOCs

### Classes of Service

- Unique class of service codes are assigned for Centrex. They are as follows:

  - CYR+X - used for 1AESS, 5ESS and DMS100.

  - 3ZQSX - used for EWSD (Siemens).

  - 3ZQDX - used for DMS10.

- The class of service identifies the type of service for a Centrex end user. The class of service USOC contains the following three parts:

  - The first three characters identify the type of Centrex sold to the end user.

  - The fourth character identifies the type of switch providing the Centrex service to the end user.

  - The fifth character is always an X.

| Code | Switch Type |
| --- | --- |
| 2 | 1AESS |
| U | 5ESS |
| J | DMS 100 |

### Intercom USOCs

- Intercommunication allows internal communication between stations within the end user's Centrex system. Intercommunication recurring and nonrecurring rates are applied per station.

- The service order USOC for intercommunication is NRSX+. The + suffix is normally a numeric character based on the number of stations in the bill group.

| BG Size (in stations) | Numeric + USOC | Alpha + USOC |
| --- | --- | --- |
| 1-20 | NRSX1 | NRSXA |
| 21-100 | NRSX2 | NRSXB |
| 101-250 | NRSX3 | NRSXC |
| 251-1000 | NRSX4 | NRSXD |
| 1001+ | NRSX5 | NRSXE |

- The following stations do not require intercom USOCs:

  - WTK

  - SXMAA

  - SXMDD

  - SXMF+

  - SXML+

  - SXMM+

  - SOT

### Station USOC

The station is represented by a 3-5 alphanumeric character code. The code of USOC contains three parts:

- The first three characters of the station USOC identify the station type and the application

| Description | Code |
| --- | --- |
| Primary Station | SXP++ |
| Bridge Station | SXB++ |
| Miscellaneous Station | SXM++ |

- The fourth character of the station USOC identifies the type of station restriction:

| Description of Station Restriction | Code |
| --- | --- |
| Primary Station (SXP++) -Unrestricted -Semi-Restricted -Fully Restricted | A B C |
| Bridged Station (SXB++) Same Premises -Unrestricted -Partially Restricted -Fully Restricted Off Premises -Unrestricted -Partially Restricted -Fully Restricted | N O P C H G |
| Bridged Station (SXB++) Electronic Key Line Single Line Extension | Q |
| Bridged Station (SXB++) Electronic Business Set Single Line Extension (Grandfathered) | R |
| Miscellaneous Station (SXM++) -Datapath -Datapath at SLA address -Square Key Station -Hunting Access -Non-hunting Access -Station in Use, Billing -Station in Use, No Billing -Test Station -Trunk on Centrex | D Q K L M P A G F |

- The fifth character of the station USOC identifies the circuit card assignment:

| Description | Code |
| --- | --- |
| Regular station | A |
| Ground start station | B* |
| 'P' Phone (Business set) | C* |
| Datapath station | D* |
| Message Waiting Station | E* |

Note:*Only available with a DMS100 switch and does not apply to Miscellaneous station (SXM++).

### Feature USOCs

Centrex includes certain features in the basic monthly rate for service.  Those features, and USOCs where applicable, are as follows:

Note:  If there is no USOC or modifying FID indicated, then one is not required.

| Feature | USOC or ZUSOC | Modifying FID |
| --- | --- | --- |
| AIOD (Automatic Identification of Outward Dialing) with billing of toll by individual station numbers | N/A | N/A |
| Call Forwarding Variable | ZCFV1 | N/A |
| Call Forwarding – Busy Within Centrex Outside Centrex | ZCFBA ZCFVA | ZTN |
| Call Forwarding - Don't Answer Within Centrex Outside Centrex | ZCFDA ZCFVD | ZTN, RCYC |
| Call Hold | ZCVLD | N/A |
| Call Pick Up | ZXAPU | CPG |
| Call Waiting - All Calls, Terminating | ZCWTG | N/A |
| Consultation Hold, Call Transfer, Three-Way Calling | ZCSAC | N/A |
| Cutoff on Disconnect (DMS100) | ZCODT | N/A |
| DID (Direct Inward Dial) | N/A | N/A |
| Denied Incoming Calls | ZD1NP | /DIN $ |
| Denied - Terminating | ZDTMC | N/A |
| DOD (Direct Outward Dialing) | N/A | N/A |
| Night Service | See Consoles | N/A |
| Speed Calling – Long Controller Shared User | ZSCC3 ZSC3O | SCG |
| Speed Calling - Short - Controller | ZSCSL | N/A |
| Station Hunting | N/A | N/A |
| Station to Station Dialing | N/A | N/A |
| Touch Tone Service | TTB | N/A |

### Optional Features USOCs

Centrex does not include the following Centrex features in the basic monthly rate for service.  The activation of these features is optional and additional charges apply.

Note:  If there is no modifying FID indicated, then one is not required.

| Feature | USOC | Modifying FID |
| --- | --- | --- |
| Message Signal Interface | See Central Message Signal Interface | N/A |
| Alternate Answer | ZCFVD | ZTN |
| Attendant and/or Station Dial Controlled Conference (0-6 members) | ZCQF6 |  |
| Attendant Console Feature Package Camp-On Control of Trunk Access Group | See Consoles | N/A |
| Automatic Callback Per System Per station | ACY ZACBK | N/A |
| Automatic Route Selection | See ARS/FRS | N/A |
| Busy Line Transfer | ZCFVA | ZTN |
| Call Detail Recording System | See CDRS | N/A |
| Call Forwarding Over Private Facilities Per system Per station | EAY ZCFVP | N/A |
| Call Forwarding Busy - Don't Answer Internal/External Split Busy per station Don't answer per station | ZB5ES ZD1ES | CFBE, CFBI CFDE, CFDI Example: Call Forwarding Busy / CFBE XXX-XXXX/CFBI XXXX Example: Call Forwarding Don't Answer /CFDE XXX-XXXX/CFDI XXXX/RCYC X Requires both FIDs for External and Internal |
| Call Park Directed Call Park | ZPDRK ZDCPK | N/A |
| Call Waiting Originating | ZCWRG | N/A |
| Caller ID | ZC1ND See Centrex Caller ID | N/A |
| Caller ID - Per Line Blocking | See Centrex Caller ID | N/A |
| Caller ID with Name | NMP or N8D if AIN converted. See Caller ID with Name-Centrex | N/A |
| Conference Services Attendant and/or Station Dial Controlled, per system up to 6 | EAN (system) ZCQF6 (line) | N/A |
| Conference Services Large Conference Arrangement (30 members) | EQ6PS (system) ZCQF3 (line) | N/A |
| Custom Calling Name on Centrex | See Custom Calling Name on Centrex |  |
| Customer Dialed Account Recording | CRV per station | N/A |
| Customer Station Rearrangement | See ServiceMate | N/A |
| End User Station Rearrangement | See ServiceMate | N/A |
| Datapath | SXMDD |  |
| Directed Call Pick-Up Non Barge In Barge In | ZDCPU ZDCB1 | N/A |
| Direct Connect | ZAULN | ZTN |
| Distinctive Ringing and Call Waiting Tone Per system Per station | DRR ZDR1C | N/A |
| Last Number Redial | ZXKNR |  |
| Message Service Attendant Message Waiting Business Set Message Waiting | See Consoles See EKL/Business Sets |  |
| Message Waiting (used with Alternate Answer and Busy Line Transfer) Stutter Dial tone Visual | ZMYAD ZMYAV | For both ZMYAD and ZMYAV CAR N, CRX N (DMS100 only) MSGN (5ESS only) |
| Music On Hold | MOHPS | N/A |
| Directed Call Pick-Up Non-Barge In | ZDCPU | N/A |
| Open Interface | OP3, OP6 | N/A |
| Other Common Carrier Access | OAL | N/A |
| Ring Again Enhanced | ZACAC | N/A |
| Speed Calling Enhanced 50 code list (per list-controller) per station-shared user 70 code list (per list-controller) per station-shared user | ZSCC5 ZSS50 ZSCC7 ZSC70 | SCG |
| Station Message Detail Recording | See SMDR | N/A |
| Toll Restricted Station | ZDGNY | N/A |
| Switched Services Network Access | 9O1 | N/A |
| Terminating Equipment | RXN | N/A |
| Uniform Call Distribution | See UCD | N/A |

### Other Station USOCs

| Description | Code |
| --- | --- |
| 800 Service station | WTK |
| Console ESS & DMS | EAR |
| Console Loop (assoc with 50 ACPS) | CX4 |
| Secondary Directory number | SOT |

### E911 USOCs

- The E911 USOC does not apply to the following stations:

  - SXMDD

  - SXMF+

  - MG8

  - SXMAA

  - WTK

  - SOT

  - SXML+

  - SXPDA

  - LTQ6X

  - SXMM+

  - MGA

### PICC (Primary InterExchange Carrier Charge)

If an end user orders a new line and does not select a PIC or is undecided, then a PICC charge will be assessed.  The USOC is REB8A for interstate/interlata; REB8B for intrastate/interlata.

### Long Term Number Portability Surcharge (NSR)

End users in select areas will be billed for a Long Term Number Portability Surcharge effective February 1, 1999.  The USOC is NSR.

### Zone USOCs

Zone Service, USOC ZNA or ZNB if applicable, is a required service order entry based upon an indicator in the SAG.

## Centrex Group Number

The Centrex Group number (also referred to as the common block) houses all of the features and parameters of operation for each individual Centrex. The Common Block Request that is built using the service provisioning system (SPS) defines all of the features that are to operate for the Centrex. It also includes items such as:

- Station number range

- Centrex Access Treatment

- Facilities

- Access, etc.

Each common block within the CO is assigned a number to identify it and the end users served. The common block identification is entered on the service request in the CB Field.

| Switch Type | Standard | Appearance |
| --- | --- | --- |
| 1AESS, EWSD, 5ESS, DMS10 | 4 digits | /CTX 1234 |
| DMS 100 | 4 digits + subgroup | /CTX 1234:0 |

## FIDs

| FID | Description |
| --- | --- |
| BG | A Bill Group (BG) entry is required whenever a Centrex station is present The BG is a method of grouping Centrex stations for the application of a sliding scale and/or trunk equivalent. A separate BG is used for each address on the end user's account with the following exceptions: Some end users have different street addresses within their contiguous property. These stations are counted as one Bill Group even though some stations may be shown at different addresses. ICB (Individual Case Basis) accounts If BG is not used for sliding scale or trunk equivalency computations, one BG can be used for the entire account. Order placement: Not required |
| CAR | Call Send - DMS100 ONLY Indicates whether the station line identified can send Message Waiting signals to another station with the Centrex group. Order placement: FEATURE DETAIL field following the feature USOC in the FEATURE field. Example: ZMYAD/CAR N |
| CFBE | Call Forward Busy External Indicates the telephone number that calls originating from outside the Centrex should be forwarded to when the Call Forward Busy split feature is ordered. Order Placement: FEATURE DETAIL field following the feature USOC in the FEATURE field. Example: ZB5ES/CFBE 91NPANXXXXXX (if out of Centrex and Long Distance) |
| CFBI | Call Forward Busy Internal Indicates the telephone number that calls originating from within the Centrex should be forwarded to when the Call Forward Busy split feature is ordered. Order Placement: FEATURE DETAIL Field following the feature USOC in the FEATURE field. Example: ZB5ES/CFBI XXXX (Forward within the Centrex) |
| CFDE | Indicates the telephone number that calls originating from outside the Centrex should be forwarded to when the Call Forward No Answer split feature is ordered. Order Placement: FEATURE DETAIL Field following the feature USOC in the FEATURE field. Example: ZD1ES/CFBE 91NPANXXXXXX (if out of Centrex and Long Distance) |
| CFDI | Indicates the telephone number that calls originating from within the Centrex should be forwarded to when the Call Forward No Answer split feature is ordered. Order Placement: FEATURE DETAIL Field following the feature USOC in the FEATURE field. Example: ZD1ES/CFDI XXXX (forward within the Centrex) |
| CPG | Call Pick Up Group Indicates the Call Pick Up Group this station belongs to. Order Placement: FEATURE DETAIL field following the feature USOC in the FEATURE field. Example: ZXAPU/CPG ## |
| CRX | Call Request Exempt - DMS100 ONLY Indicates whether the station line designated is or is not exempt from receiving Message Waiting signals from another station within the Centrex group. Order Placement: FEATURE DETAIL field following the feature USOC in the FEATURE field. Example: ZMYAD/CAR N/CRX N |
| CSR | Customer (End User) Station Rearrangement Indicates that Service Mate is present on the account. It is floated behind the SXP++ and any feature that has to be retained on the Service Record. Order Placement: FEATURE DETAIL field following the feature USOC in the FEATURE field. Example: ZMYAD/CAR N/CRX N |
| SLA | Secondary Location Address Identifies the address of each Centrex location other than the main address Floated behind line USOC (ie., SXP++) Multiple Centrex stations that terminate at addresses other than the main can be shown on the same service request provided they are all for the same end user. See Miscellaneous Ordering Procedures for details. The BG FID appears on the CSR ahead of the Centrex station details. Order Placement: Under Secondary Location, use the Address Fields as applicable. |
| DPA | Different Premises Address Identifies the address of a Centrex off premises extension to another location. Floated behind line USOC (ie., SXP++) Order Placement: Under Secondary Location, use the Address Fields as applicable |
| DPS | Different Premises Subscriber Identifies a different end user other than the listed end user at a different location (SLA or DPA) than the main listed address. Floated behind SLA or DPA information. Allows E911 and Caller ID to pick up the correct end user name. Order placement: Under Secondary Location, use the Name Field. |
| SPP | There are three common FIDs that are used on service orders with pricing plans. They are: SPP - Special Pricing Plan TA - Term Agreement SED - Service Established Date General SPP information is shown on the service request in the VTA field on the LSR. If applicable, SPP information must be shown on a migration order in the VTA field. If the end user has an existing SPP on the CSR and it is not shown on the migration order, termination charges may apply. Entered Left-Hand in the S&E Section The SPP FID followed by plan option data provides information to properly rate the payment plan. The left hand appearance of the SPP FID is found at the beginning of the S&E section of a CSR. Order placement: VTA Field on the LSR Form Entered Floating in the S&E Section To identify the end user's choice of month-to-month contract on the CSR, the identifier VT3 follows the SPP FID. FT7 should be used for all contracts. Order Placement: VTA Field, Segment 2, on the LSR Form. Example: VTA XX/VT7 TA - Term Agreement TA is entered floating in the S&E section following the left hand SPP FID and data entries. The TA FID followed by two numerics indicate the contract length followed by the date billing should begin. The system will generate the completion date of the order if a date is not provided. Order placement: VTA Field, Segment 1, on the LSR Form Example: VTA XX SED - Service Established Date SED is found floating in the S&E section following the TA FID and data entries The SED FID is followed by the date the CLEC signed the contract and is required to establish rating. This entry guarantees the CLEC will be billed the rate in effect on the date the contract was signed. Order Placement: VTA Field, Segment 3, on the LSR Form. Example: VTA XX/VT7/MMDDCCYY |
| ZTN | Feature Related Telephone Number Identifies the station's dialing pattern when associated with Call Forwarding Features. The ZTN should be shown exactly as it should be dialed (eg 9, 1, 312 555-5555). Order Placement: FEATURE DETAIL Field following the Feature USOC in the Feature Field. Example: ZCFVA/ZTN 91NPANXXXXXX |
| TN | Telephone Number - Identifies the seven digit station number. Order placement: TNS Field |
| CTX | End User Group Identifier - identifies the parameters by cross-referencing the service order to the common block. Order placement: CT Field |
| LCC | Line Class Code defines the ability to access or be accessed by the switched exchange network. The LCCs are established individually when the common block is built. Order Placement: FEATURE DETAIL following the line assignable USOC. Example: SXP++/LCC XXXX |
| CAT | End user Access Treatment - identifies the ability of the station to use certain routes (eg. Foreign Exchange Service) and special facilities. Specific CAT codes permit or restrict access to different combinations of routes and special facilities. The CAT codes are established individually when the common block is built. Order Placement: FEATURE DETAIL following the line assignable USOC. Example: SXP++/CAT X. See CAT Codes for additional information |
| DIN | Deny Incoming (DMS100) only. Indicates to deny incoming calls from outside of the Centrex group. Order Placement: Not required Example: ZD1NP/DIN$ |
| DPI | Different Premise Information Supplement information concerning Different Premise Address (DPA) installation Can only be used with 'DPA' and not on 'SLA' locations. Does not reflect in 911 Database. Order Placement: SADLO on Centrex Order Form Example: SXP++/DPA 1/DPI Term on 701E PBX |
| TGID | Terminal Group and Station Restriction - identifies additional station restriction to the switch*. Order Placement: Not required |
| IDP | Individual Dialing Plan - provides the ability to interpret dialed digits according to a customized plan rather than the CO's dialing plan*. Order Placement: Not required |
| LPIC | Pre-designated IntraExchange Carrier Name - Identifies the end user - selected IntraExchange carrier. Order Placement: LPIC Field. |
| ZPIC | Pre-designated IntraExchange Carrier Code - Identifies the end user - selected IntraExchange carrier. Order Placement: Not required. |
| LPCA | Presubscription Carrier Arrangement - identifies how an IntraExchange carrier was selected for the end user. Order Placement: Not required. |
| PIC | Pre-designated InterExchange Carrier Name - identifies the end user - selected interExchange carrier. Order Placement: PIC Field |
| PICX | Predesignated InterExchange Carrier Code - identifies the end user - selected interExchange carrier. Order Placement: Not required. |
| PCA | Presubscription Carrier Arrangement - identifies how an interExchange carrier was selected for the end user. Order Placement: Not required. |
| RIE | Rate Included Elsewhere - Indicates that the normal monthly charge should not be billed. Order Placement: FEATURE DETAIL Field following the feature in the FEATURE field. Example: ZDCPK/RIE |
| RCYC | Ring Cycle - Indicates after how many rings the call should be forwarded to the pre-selected number. The default is 3 ring cycles. Order Placement: FEATURE DETAIL Field following the feature in the FEATURE field. Example: ZCFDA/ZTN XXXX/RCYC 5 |
| SCG | Speed Call Group Number - Indicates to which speed call group this Centrex station has access. Order Placement: FEATURE DETAIL Field following the feature in the FEATURE field. Example: ZSC50/SCG ## |
| TGS TGUU+ | Terminal Group Station Restriction - Required on 5ESS only. Identifies the originating and terminating line restrictions as well as the intercept treatment (T-Tone vs A-Announcement) and optional features attributes. Order Placement: Not required - Ameritech will program as TGUUT unless otherwise specified. If other than TGUUT should be programmed, then show the information in the FEATURE DETAIL following the line assignable USOC. Example: SXP++/TGS TGUUT |
| WLN | Warm Line Service Number - Identifies the telephone number, which is automatically called by the DMS100 switch at the expiration of a predetermined time interval, when the originating end user goes off hook. Order Placement: FEATURE DETAIL Field following the feature USOC in the FEATURE field. Example: ZXAWL/WLN NXX-XXXX |

Note:  *Applicable to the 5ESS switch only.

## Customer Access Treatment Codes (CAT)

- CAT Codes for the 5ESS, 1AESS, DMS10 and EWSD switch types are generally as follows:

| CAT Code | Network Access Allowed |
| --- | --- |
| 0 | No |
| 1 | Yes |

Note:  Not all Centrex's have been built with this configuration; some may have more CAT Codes established or the CAT Codes could be different.  Therefore, it is suggested that the CLEC contact their Service Manager for a complete listing of the CAT Codes built for the end user's Centrex.

- CAT Codes are called NCOS or Network Class of Service Codes in the DMS100 switch.  Generally, when a Centrex is built, four basic restriction levels are built.  Most of them look like the following:

| NCOS Code | Network Access Allowed |
| --- | --- |
| 1 | Unrestricted - can place and receive intercom calls, local calls, long distance calls, 900/976 calls, 800 calls, International Calls, 911 calls and can call Directory Assistance |
| 2 | Semi Restricted - can place and receive intercom calls, local calls, 800 calls, 911 calls and can call Directory Assistance |
| 3 | Fully Restricted - can place and receive intercom calls and 911 calls |
| 4 | Semi-Restricted - can place and receive intercom calls, local calls, long distance calls, 800 calls, International calls, 911 calls and can call Directory Assistance. |

## Line Class Code (LCC)

The Line Class Code describes the station's ability to access Level 9 for local dialing, long distance, or other stations.

| DMS10 Switch Type |
| --- |
| Type of Restriction | State | LCC |
| Unrestricted | Indiana | DY1 |

### 5ESS Non-Hospital

| USOC Code | LCC | Class of Service | Incoming DID | Outgoing Local | Outgoing Toll | Access Attendant | Stations |
| --- | --- | --- | --- | --- | --- | --- | --- |
| SXP++ SXB++ SXM++ | RXR R9R | Nonrestricted Station (900/976) Blocking | Yes | Yes | Yes | Yes | Yes |
| SXP++ SXB++ SXM++ | RWR | Denies Access 9+1 (includes 900/976 Blocking) | Yes | Yes | Yes (9+0) (9+1+800) | Yes | Yes |
| SXP++ SXB++ SXM++ | 8RX | Semi-Restricted Station | No | Yes | No (1+411) (1+800) | Yes & can receive DID transferred call | Yes & can receive DID transferred call |
| SXP++ SXB++ SXM++ | 2RX 5RX | Semi-Restricted Station -Semi-Restricted Station | Yes No | No No | No No | Yes Yes & can receive DID transferred call | Yes Yes & can receive DID transferred call |
| SXP++ SXB++ SXM++ | 7RX | Toll Restricted Station | Yes | Yes | No Toll No 800 No 1-411 | Yes | Yes |
| SXP++ SXB++ SXM++ | 6RX | Manual Station | No | No | No | Yes | No |
| SXP++ SXB++ SXM++ | 1RX | Full Restricted Station (Isolated) | No | No | No | No | Yes |
| SXP++ SXB++ SXM++ | DO3 | One Way In, Semi-Restricted Station | Yes | No | No | Only incoming | Only incoming |
| SXP++ SXB++ SSM++ | DO5 | One Way In, Fully Restricted Station (Isolated) | No | No | No | No | Only incoming |
| SXP++ SXB++ SSM++ | DY1 D91 | One Way Out, Non-Restricted Station (900/976 Blocking) | No | Yes | Yes | Outgoing to attendant | Only outgoing |
| SXP++ SXB++ SSM++ | SR1 | One Way Out, Semi-Restricted Station | No | No | No | Outgoing to attendant | Only outgoing |
| SXP++ SXB++ SXM++ | FR1 | One Way Out, Fully Restricted Station (Isolated) | No | No | No | No | Only outgoing |
| SXP++ SXB++ SXM++ | DY4 | One Way Out, Toll Restricted Station | No | Yes | No | Outgoing to attendant | Only outgoing |
| SXP++ SXB++ SSM++ | DY6 | Semi-Restricted Station | No | Yes | No | Yes | Yes |
| WTK | WRX DYX | -InWATS -Station (800) | Yes Yes | No Yes | No No | Yes Yes | Yes Yes |
| SXP++ SXB++ SSM++ | R8R | Toll Restricted Station | Yes | Yes | No Toll No 1-411 Yes 800 | Yes | Yes |
| SXP++ SXB++ SSM++ | 4RX | Attendant Level '0' & through DIAL using key set | Yes | Yes | Yes | Yes | Yes |
| EAR | 3RX | Attendant Level '0' DIAL using console | Yes | Yes | Yes | Yes | Yes |
| SXP++ SXB++ SSM++ | 4NX | Semi-Restricted Station | Yes | Yes | No Toll Yes 1-411 Yes 800 | Yes | Yes |
| SXP++ SXB++ SSM++ | 2NX 2R9 | No DID Allow Toll (900/976 Blocking) | No | Yes | Yes | Yes | Yes & can receive transferred call |
| SXP++ SXB++ SSM++ | RDC | Direct Connect 1 Way Out | No | Yes | Yes | Yes | Yes |
| SXP++ SXB++ SSM++ | DC2 | Direct Connect 1 Way Out | No | Yes | Yes | Yes | Yes |

### 5ESS Hospital

| USOC Code | LCC | Class of Service | Incoming (DID) | Outgoing Local | Outgoing Toll | Access Attendant | Stations |
| --- | --- | --- | --- | --- | --- | --- | --- |
| SXP++ SXB++ SSM++ | HF1 | CTX Attendant | Yes | Yes | Yes | Yes | Yes |
| SXP++ SXB++ SSM++ | HF4 | Semi-Restricted | Yes | No | No | Yes | Yes |
| SXP++ SXB++ SSM++ | HF5 | Semi-Restricted, One Way In | Yes | No | No | No | Yes |
| SXP++ SXB++ SSM++ | HF6 | Toll Restricted | Yes | Yes | No | Yes | Yes |
| SXP++ SXB++ SSM++ | HF7 | Semi-Restricted Station | No | No | No | Yes | Yes |
| SXP++ SXB++ SSM++ | HFN R9R | Non-Restricted (900/976 Blocking) | Yes | Yes | Yes | Yes | Yes |
| SXP++ SXB++ SSM++ | HO6 | Fully Restricted (Isolated) | No | No | No | No | Yes |
| SXP++ SXB++ SSM++ | HO3 | One Way In, Semi-Restricted Station | Yes | No | No | Only In | Only In |
| SXP++ SXB++ SSM++ | HO5 | One Way In, Fully Restricted Station (Isolated) | No | No | No | No | Only Incoming |
| SXP++ SXB++ SSM++ | HF8 | One Way In, Fully Restricted Station (Isolated) | No | No | No | No | Only Incoming |

### 5ESS Joint Tenant

| USOC Code | LCC | Class of Service | Incoming (DID) | Outgoing Local | Outgoing Toll | Access Attendant | Stations |
| --- | --- | --- | --- | --- | --- | --- | --- |
| SXP++ SXB++ SSM++ | R8V | Toll Restricted | Yes | Yes | No Toll, No 1-411; Yes 800 | Yes | Yes |
| EAR | RVA | Attendant Level '0' and through Dial using console | Yes | Yes | Yes | Yes | Yes |
| SXP++ SXB++ SSM++ | RVX RVW (Ofc networking only) | Joint Tenant Service | Yes | Yes | 0+; Yes 1-411; Yes 800 | Yes | Yes |
| SXP++ SXB++ SSM++ | RV4 | Semi-Restricted | Yes | Yes | No Toll; Yes 1-411; Yes 800 | Yes | Yes |

#### TGS (5ESS only)

- TGS = Terminal Group/Station Restriction.  Also known as Deny Originating/Deny Terminating.

- The TGS FID is used to assign different calling restrictions to individual stations by modifying the TG++T (terminal group) data.  It is used to allow/disallow incoming/outgoing calls to/from a station line.

- The TGS is higher in the hierarchy for restrictions than the LCC.

- The TGS is not changeable through ServiceMate

- The third and fourth characters of the FID determine the restriction on the line:

Unrestricted (U).

  - Originating lines have no restrictions on outgoing calls

  - Terminating lines have no restrictions on incoming calls

Semi Restricted (S):

  - Originating lines can make calls to lines within the same terminal group, including the attendant console, and can place calls over private facilities that are within the same terminal group.

  - Terminating lines can receive calls from these originating points.  All others are restricted.

Fully Restricted (F):

  - Originating and terminating lines are the same as Semi-Restricted lines except that attendant calls are prohibited.

- The fifth character can be either T for Tone or A for Announcement

- The TGS Code always assigned is TGUUT.

### DMS100 LCC

The Line Class Code in  the DMS100 switch is always IBN for regular telephone sets.  IF the end user has NorTel proprietary sets, also known as P-Phones, Business Sets or Electronic Key Line Telephone Sets, THEN the LCC is the model number of the set.

### EWSD/1AESS

- Unrestricted - RXR

- Toll Restricted - R8R

- Block 900/976 - R9R

- Block 900/976/IDDD - R9C

- Fully Restricted – 1RX

Note:  1RX is not built into all switches.

#### Joint Tenant

- Unrestricted – RXR

- Toll Restricted – RV7

- Block 900/976 – RV9

### DMS10

Unrestricted LCC of RXR is used on all DMS10 orders.

## Miscellaneous Ordering Procedures

New Centrex Service Orders:

- Information for a new Common Block (ie., Line Class Codes, Treatment Codes) should be placed in the 'Remarks' section of the LSR form.

- New Centrex Service can only be ordered manually at this time.

Subsequent Centrex Orders:

The following details how to show items that do not have specific fields on the new manual LSR

- To indicate a Transfer of Calls option, in the Remarks field put /TC OPT.

- To indicate a Jack Request, in the Feature Detail Field following the Line Assignable USOC, enter /JR.

- Centrex class of service must be shown on the LSR form in the 'TOS' field.

- If a telephone number has not been pre-assigned, a placeholder can be used in field 'TNS' when establishing new service.

- 'PIC' and 'LPIC' are required on all orders.

- Centrex service is ordered on a REQ TYP 'P'

- The 'line assignable USOC should be shown first in the FEATURE field on the product form.

- Centrex station numbers cannot be reserved through the pre-order system.

CB - Common Block Field #7

At this time, per LSOR 5.00, this is a required field and the valid entry is a 5 to 11 alpha/numeric/special characters.  If a Centrex Common Block Name/Number is less than five (5) characters, you must populate using zero(s) preceding the CTX Name/Number in order to reach the minimum character field requirement (ie. 00123).

## Master Agency Billing

Master Agency Billing is NOT available in Resale or UNE-P/CPO.  However, there are situations when a CLEC absorbs a Centrex contract or takes over some of the stations from an existing Centrex (Primary or Secondary account) that contain Master Agency Billing.  Billing USOCs will be removed when these accounts are converted.  Below are procedures the CLEC should utilize when converting such an account:

If the CLEC is taking over the entire Centrex, then:

- They must send one PON on an ACT V

- They must include a DL form if there are listings on the secondary accounts

- They must include the Hunting information

If the CLEC is taking over the Primary account, then:

- They must send one PON on an ACT V

- They must convert to a New Centrex or different class of service, i.e. POTS

If the CLEC is taking over the Secondary account only, then:

- They must send one PON on an ACT V

- The must convert to a New Centrex or different class of service, i.e. POTS

# Billing

## Basic System Equipment USOCs

| Basic System Equipment | USOC |
| --- | --- |
| Common Equipment - Service Establishment -25 primary or intercom only stations and under -26 primary or intercom only stations and over | CKC -SEPB1 -SEPB2 |
| Primary Station | SXPA+ |
| Intercom Only Station | SXPC+ |
| Cell Size -1-20 stations -21-100 stations -101-250 stations -251-1000 stations -1001+ stations | NRSX1 NRSX2 NRSX3 NRSX4 NRSX5 |

## Suburban Zone USOCs

- In some areas, zone charges apply. Application is determined by an indicator in the SAG. They are represented by either the USOC ZNA (Zone A) or ZNB (Zone B).

- If zone charges apply, an entry is required only on the first station of the order.

- The zone charges will be summarized on the Station Element Summary (SES) of the CSR.

- Centrex applies on a channel equivalency basis.

- Common equipment recurring and nonrecurring charges are determined by the type of Centrex service.

| Suburban Zone Service | USOC |
| --- | --- |
| Locations with stations Per Equivalent channel | ZNA ZNB |

## Station Feature USOCs

| Station Features | USOC |
| --- | --- |
| Automatic Callback -Per primary station equipped -Common equipment per system | ZACBK ACY |
| Alternate Answer & Busy Line Transfer -Per primary station equipped | ZCFVD ZCFVA |
| Call Forwarding Busy/Don't Answer Internal/External Split -Per station - Busy -Per station - Don't Answer | ZB5ES ZD1ES |
| Direct Connect -Per primary station equipped | ZAULN |
| Distinctive Ringing and Call Waiting Tone -Class B ringing/ tone, per primary station -Common Equipment - Class B ringing/tone per system | ZDR1C DRR |

## Station Service USOCs

Note: If the station is removed along with the feature, waive the SS charge.

| Station Service Charges | USOC | IC |
| --- | --- | --- |
| Activation or Deactivation of Feature (Single feature charge, per feature, per station) -Call Forwarding - Don't Answer -Call Forwarding - Variable -Call Hold -Call Pickup Call Waiting - All Calls -Call Waiting - Originating -Call Waiting - Terminating -Directed Call Pickup Non-Barge In -Speed Calling - Long 30 number (ZSCC3 is controller and ZSC3O is shared user) -Speed Calling - short (ZSCSL is used for controller of short list - each person controls their own list. ZSCUR (user) no longer used.) | ZCFDA ZCFV1 ZCVLD ZXAPU ZCW10 ZCWRG ZCWTG ZDCPU ZSC3O, ZSCC3* ZSCSL* ZSCSL | Refer to tariff |
| Multiple feature charge, per station |  | Refer to tariff |
| Memory Change per Station Changed Note: Only bill one REAF9 or PT3T1 per station -Add or remove change hunting -Add or remove Call Forward Busy -Change forward to number Call Forward-Busy -Change forward to number and/or ringing cycle on Call Forward Don't Answer -Change Call Pickup group -Change level access (CAT) -Change Direct Connection station number -Change Night Service number -Change Station Restriction (LCC) | REAF9 REAF9 PT3T1 PT3T1 PT3T1 PT3T1 PT3T1 PT3T1 PT3T1 | Refer to tariff |

Note: *No charge for ZSCC3 if installed at the same time on same TN. To waive charge, enter /NRI NI on every ZSCC3 where ZSC3O is being added on same TN at same time.

## Non-Centrex to Centrex Change Charge USOCs

Use the following charts for activating new lines into an existing Centrex or if converting existing lines into an existing Centrex common block as a working number.

## System Feature USOCs

### Conference Arrangement

|  | USOC |
| --- | --- |
| Attendant and/or Station Dial Controlled, per system up to 6 members | EAN (system) ZCQF6 (line) |
| Large conference arrangement (30 members) | EQ6PS (system) ZCQF3 (line) |

### Music On Hold

|  | USOC |
| --- | --- |
| Per system (requires appl. 6011 channel service) | MOHPS |

### Other Common Carrier (OCC Access)

|  | USOC |
| --- | --- |
| Access Line Terminal | OAL |

### Switched Services Network Access Terminals

|  | USOC |
| --- | --- |
| Access Line Terminal | 901 |

### Terminating Equipment

|  | USOC |
| --- | --- |
| For each dial termination of tie line or Type A Enhanced Private Switched Communication Service Line | RXN |

### Foreign Exchange Service

| Description | USOC |
| --- | --- |
| Same CO Local Distribution (Type 2006A) Channel, each (+ = B for trunk, A for Line) | 1LHBJ |
| Different CO (Type 2006B) Channel, each Centrex | SV6SX |
| Contiguous Interexchange Channel, each mile or fraction -0 to 40 miles -41+ miles Interexchange Channel Termination, each mile or fraction -0 to 40 miles -41+ miles | ILHB4 P1N P7K |
| Non-Contiguous In addition to contiguous above -Interoffice Channel mileage, each mile or fraction -Interoffice Channel terminal, each | ILHBS 2LH |

## Joint Tenant Service Billing

Joint Tenant Service is grandfathered effective November 15, 2004.

## Off Premises Extensions USOCs

### Bridged Station (DPA)

| Description | USOC |
| --- | --- |
| Same CO Local Distribution Channel (Type 2011) | LCUSZ |
| Different CO -Local Distribution (Type 2011) -Interoffice Channel Mileage, each mile or fraction thereof -Interoffice Channel Mileage Termination, each | LCUSZ ILVFS 2LK |
| Service Charges -Premises work charge applies -Service order charge applies for initial termination -Service order charge does not apply for add’l termination when ordered at same time and same premises as initial termination | --- |

### Primary/Secondary Premises (SLA)

| Description | USOC |
| --- | --- |
| Same CO | --- |
| Different CO -Foreign CO terminal per line -Interoffice Channel Mileage, each mile or fraction thereof -Interoffice Channel Mileage Termination, each | FCMS2 ILVFS 2LK |
| Service Charges -Premises Work Charge applies -Service Order Charge applies for initial termination -Service Order Charge does not apply for add’l termination when ordered at same time and at same premise as initial termination. | --- |

## Intercept Services

| Description | USOC |
| --- | --- |
| -First station | A1WTX |

## End User Common Line Charge (EUCL)

- End users having access to the facilities must pay for a portion of the cost of providing and maintaining telephone service for local and long distance calls. End users are billed an End User Common Line charge (EUCL) each month on a line/station or Trunk Equivalency basis.

- EUCL is not a required service order entry, since it is an implied element.

- The Station Element Summary Screen of the online CSR contains the following:

  - Quantity

  - Recurring rate

  - Total amount charged for EUCL (the charge is calculated by ACIS)

- Centrex end users are billed monthly for intrastate and interstate EUCL using a Trunk Equivalency method. The charge is applied on a per-BG basis. Fully restricted stations are excluded from the count.

- The EUCL charge PBX/Trunk Equivalency is billed on the following station USOCs:

| Description | Code |
| --- | --- |
| Console Attendant access line | EAR |
| Unrestricted | SXPA+ |
| Semi-restricted | SXPB+ |
| Station number in use | SXMPA |

## Handicap Surcharge/Dual Party Relay Service (DPRS)

- A surcharge is imposed to cover the cost of providing telecommunications service to those with hearing or speech impairments.  Also known as Dual Part Relay Service. The USOC is NBVDP.

## Implied Elements

- Implied Elements are billing elements of a Centrex station that the end user does not order but receives as a part of the service. The USOCs will not be shown on the service order or on the CSR.

- Special behind-the-scenes processing, triggered by the station USOC, will generate the following rate elements associated with a Centrex station.

  - EUCL - Intrastate

  - EUCL - Interstate

  - Handicap Surcharge - DPRS

  - Extended Area Service

  - EUCL Offset

- The rate element application can vary by:

  - State

  - Class of service

  - Station USOC code

  - Exchange

  - Contract

- The Station Element Summary (SES) screen will contain the following:

  - Quantity

  - Recurring rate

  - Total amount of charges

## Channel Equivalency

- The following components of Centrex Service are billed on a Channel Equivalency basis.

  - Dual Party Relay (Handicapped Surcharge)

  - Extended Area Service

  - Suburban Zone Charges

  - Exchange Access

- The following table is used to convert the number of stations on a per location basis to the equivalent number of channels.

| Channel Equivalency Table |
| --- |
| Station Cell Size | Equivalent Channel |
| 1 - 54 | Applies per primary stations |
| 55 - 64 | 9 |
| 65 - 75 | 10 |
| 76 - 86 | 11 |
| 87 - 98 | 12 |
| 99 - 111 | 13 |
| 112 - 125 | 14 |
| 126 - 139 | 15 |
| 140 - 155 | 16 |
| 156 - 171 | 17 |
| 172 - 189 | 18 |
| 190 - 207 | 19 |
| 208 - 225 | 20 |
| 226 - 243 | 21 |
| 244 - 262 | 22 |
| 263 - 281 | 23 |
| 282 - 300 | 24 |
| For each additional 15 stations over 300 or fraction thereof | 1 additional |

## Trunk Equivalency

- Trunk Equivalency is a method used to reduce the quantity of services the end user pays for to approximate a PBX Trunk. Eligible services usually include EUCL and/or E911 charges.

- On Centrex systems, the EUCL charge and E911 charge are applied using the Trunk Equivalency table.

- The following table is used to compare the number of stations on a per location basis. The equivalent trunk count is then used to bill the EUCL charge and the E911 charge.

| Number of Stations | Number of PBX Equivalent Channels |
| --- | --- |
| 1 | 1 |
| 2 - 6 | 2 |
| 7 - 15 | 3 |
| 16 - 21 | 4 |
| 22 - 28 | 5 |
| 29 - 36 | 6 |
| 37 - 45 | 7 |
| 46 - 54 | 8 |
| 55 - 64 | 9 |
| 65 - 75 | 10 |
| 76 - 86 | 11 |
| 87 - 98 | 12 |
| 99 - 111 | 13 |
| 112 - 125 | 14 |
| 126 - 139 | 15 |
| 140 - 155 | 16 |
| 156 - 171 | 17 |
| 172 - 189 | 18 |
| 190 - 207 | 19 |
| 208 - 225 | 20 |
| 226 - 243 | 21 |
| 244 - 262 | 22 |
| 263 - 281 | 23 |
| 282 - 300 | 24 |
| Each additional 15 lines over 300 | 1 |

## Minimum Billing/Termination

### Centrex Termination Charges

- The end user is billed termination charges for each line disconnected that is billed under contract.

## Payment Options/Contracts

Effective January 3, 2006, Centrex end users presently under a 36, 60 or 84-month term payment plan may extend their contract an additional 12 or 24 months.  Effective March 5, 2007, a 12 and 24-month term is available.

- End user must commit to the highest line category possible given the number of contracted Centrex lines.

- Eligible end users must have 12 months or less remaining on an existing tariff term payment plan.

- Standard termination charges apply for premature, total or partial discontinuance of the service.

- End users that exercise the option to extend the term of the contract are not entitled to a different rate based on the overall term of the contract extended.

- End users on a Month-to-Month or ICB contract are not eligible for this option.

- Subject to AT&T’s right to seek to discontinue this option or to otherwise change the terms and conditions of this option, the end user may exercise this option up to three separate times.

- End users who sign a 12 or 24 month Centrex contract will receive a discount on the monthly recurring Centrex Basic and Electronic Key Line rates.

- Should customer decide to terminate service prior to the expiration of the contract period, customer will be required to pay an early termination fee.

# Footnotes

Note:  1 required per speed call group

CLECAM05-295, CLECAM05-297, CLECM07-022