Electronic Key Line Service

Description

Electronic Key Line Service (EKL) provides voice communication using M5000 Meridian Business Sets. Business sets use out-of-band signaling to communicate with the switch and enable the operation of feature-access keys and display features.

- Each Business Set requires its own directory number (DN) which is assigned to button 1 of the set. The DN assigned to button 1 of the business set is called the 'Primary Directory Number.'

- The remaining buttons of the business set are assigned as a directory number and/or Feature buttons, or may remain unassigned.

- The depression of the button assigned to a DN automatically ties the business set to the associated DN and its features.

- Each DN appearance on a set is assigned an NCOS. Each can have a different NCOS or the same DN can have different NCOS's on its different appearances on different sets.

Aliases

- P-phones

- Psets

- Business Sets

- Electronic Telephone Set (ETS)

- Meridian Business Sets (MBS)

- EKL

Features

Standard

- Analog Line Pickups

- Automatic Dial

- Automatic Line Pre-select

- Blind Transfer with Recall Identification

- Call Diverting

- Call Forwarding per Key

- Call Hold

- Call Pickup

- Call Request

- Call Request with Queue

- Call Transfer

- Call Waiting/Cancel Call Waiting

- Called Number Display

- Caller ID Intercom

- Calling Reason Display

- Conference Calling – 3 Way

- Consultation Hold

- Direct Inward Dialing

- Direct Outward Dialing

- Directory Number hunt with Call Waiting and Preferential Hunt

- Display Capability

- Distinctive Ringing and Call Waiting Tone

- End to End Signaling

- Equal Access

- Executive Busy Override / Exempt

- Executive Message Waiting

- Feature Buttons

- Group Intercom

- Hunting Arrangement

- Intercom Calling

- Last Number Redial

- Leave Message Activation

- Listen on Hold

- Make Set Busy

- Make Set Busy except on Group Intercom

- Message Retrieval Display

- Message Waiting Activation Control

- Message Waiting Indication Lamp / Visual

- Multiple Appearance Directory Number (MADN) Single Call Arrangement (SCA)

- Night Answer

- Repeat Alert

- Ring Again Idle Set

- Ringing Options for MADN

- Secondary MADN Call Forwarding

- Set Inspect

- Short Hunt

- Speed Calling Short

- Stop Hunt Access Code

- Time and Date Display

- Touch Tone

- Transfer Call to Restricted Station

- Usage Billing by Line Number

Optional

- Add On Modules

- Automatic Callback

- Call Camp-On

- Call Camp-On Selective

- Call Forward Reason Display (Michigan only)

- Call Forwarding Over Private Facilities

- Call Park

- Call Screening

- Caller ID

- Caller ID with Name

- Calling Name Display on Intercom

- Custom Calling Name on Centrex

- CLASS Features

- Datapath Critical Path Restoration (Michigan only)

- Direct Connect Originating

- Direct Connect Originating with Delay

- Direct Station Selection/Busy Lamp Field with Fast Transfer

- Directed Call Park

- Directed Call Pickup

- Distance Extension

- Executive Display Communications

- Make Busy

- Multiple Appearance Directory Number (MADN) Multiple Call Arrangement (MCA)

- Network Number Display (Michigan only)

- Premium Feature Package

- Query Busy Station

- Secondary Directory Telephone Number

- Special Billing Code

- Speed Calling-Expanded Number Group

- Speed Calling-Long

- Speed Call Pause Insertion (Michigan only)

- Station Call Through Test (Michigan only)

- Station Controlled Conference

- Telephone Number Reprogramming Service (Michigan only)

- 800 Call Transfer Single Line Set (Michigan only)

Availability

Electronic Key Line Service is available to all Centrex Service and Advanced Centrex Service customers. It can also be offered to most grandfathered and/or customer specific Centrex contract customers in DMS100 central offices only.

Restrictions/Limitations

- Meridian business Sets are available on in DMS100 offices

- The Direct Station Select/Busy Lamp Field can only appear on a maximum of 8 BLF keys associated with a directory number.

- Feature capability is limited by switch availability and state specific tariff offering.

- Ground start is not available on EKL.

- Reuse of Facilities are not allowed.

- MADNs are not allowed on ACD sets.

- Dual Service is not available.

- A telephone number can have only one Key 1 appearance on an EKL set.

- Cannot have EKL set as foreign exchange service.

- Secondary Directory Number cannot be the main BTN.

- Call Screening is not available in Indiana.

- Message Waiting Stutter does not work on EKL sets.

- EKL end users must subscribe to Centrex Service or Advanced Centrex Service.  Note:  EKL is available to some applicable grandfathered Centrex service.

Interactions

The following indicate incompatible interactions with the stated featured.

Automatic Answer Back (AAB)

- (MADN) Multiple Appearance Directory Number

- MADN release

Automatic Line (AUL)

- Automatic Callback

- Automatic Call Distribution

- Automatic Recall

- Call Forwarding Busy

- Call Forwarding Don't Answer

- Call Forward Group Don't Answer

- Call Forwarding

- Calling Number Deliver Blocking

- Customer Oriented Trace

- Dial Call Waiting

- Directed Call Pickup with Barge-In

- Directed Call Pickup, Non-Barge-In

- Denied Origination

- Last Number Redial

- Speed Calling

Bridge Night Number (BNN)

- Automatic Callback

- Automatic Call Distribution

- Call Forwarding Busy

- Call Forwarding Don't Answer

- Call Forwarding Universal, per key

- Call Pickup

- Denied Incoming

- Speed Calling

Call Forward Busy Internal Calls Only (CBE)

- Bridged Night Number

- Distributed Line Hunt

- Directory Number Hunting

- Multi-line Hunting

- Primary Hunt Group

Call Forward Busy External Calls Only (CBI)

- Bridged Night Number

- Distributed Line Hunt

- Directory Number Hunting

- Multi-line Hunting

- Primary Hunt Group

Common Control Switching Arrangement (CSSA)

- Automatic Callback

- Calling Number Delivery

- Local Call Detail Recording

- Operator Number Identification

- Selective Call Forwarding

Call Forwarding Don't Answer Internal Calls Only (CDE)

- Bridged Night Number

- Distributed Line Hunt

- Denied Termination

- Multi-line Hunting

Call Forward Don't Answer External Calls Only (CDI)

- Bridged Night Number

- Distributed Line Hunt

- Denied Termination

- Multi-line Hunting

Call Forward Busy (CFB)

- Bridged Night Number

- Distributed Line Hunt

- Directory Number Hunt

- Multi-line Hunt

- Multiple-Position Hunt with Queue

Call Forward Don't Answer (CFD)

- Bridged Night Number

- Distributed Line Hunt

- Multi-line Hunting

- Denied Termination

Call Forwarding Don't Answer Variable Timer (CFDVT)

- Bridged Night Number

- Distributed Line Hunt

- Multi-line Hunting

Call Forward IntraGroup (CFI)

- Bridged Night Number

- Call Forward Universal

- Denied Origination

- Denied Termination

Call Forward Universal (CFU)

- Bridged Night Number

- Denied Origination

- Denied Termination

Call Forward (CFW)

- Automatic Line

- Bridged Night Number

Call Hold (CHD)

- Denied Origination

- Denied Termination

Calling Line Identification Through Flash (CLF)

- Essential Service Line

Calling Line Identification (CLI)

- Private Business Line

Call Park (PRK)

- Denied Origination

- Denied Termination

Call Pickup (CPU)

- Bridged Night Number

- Denied Origination

- Denied Termination

Call Waiting, Dial (CWD)

- Automatic Line

- Call Waiting Originating

- Denied Origination

Call Waiting IntraGroup (CWI)

- Call Waiting Exempt

- Distributed Line Hunt

- Denied Termination

- Multiple-Position Hunt with Queue

Call Waiting Originating (CWO)

- Dial Call Waiting

- Denied Origination

Call Waiting Terminating (CWT)

- Distributed Line Hunt

- Denied Termination

- Repeat Alert

Call Waiting Exempt (CWX)

- Bridged Night Number

- Circular Hunting

- Call Waiting, Intergroup

- Distributed Line Hunt

- Directory Number Hunting

- Denied Termination

- Line Overflow to a Directory Number

- Multi-line Hunting

- Multiple-Position Hunt with Queue

- Random Make Busy

- Stop Hunt

Circular Hunting (CIR)

- Call Waiting Exempt

- Distributed Line Hunt

- Multi-line Hunting

- Call Waiting, Intergroup

- Series Completion

- Secondary Directory Number

Conference Line Option (CNF)

- Denied Origination

Custom Calling Name on Centrex (CCNAM)

- Caller ID with Name

- Calling Name Display on Intercom

Directed Call Pickup Barge-In (DCBI)

- Automatic Line

- Directed Call Pickup, Non Barge-In

- Denied Origination

Directed Call Pickup Barge-In Exempt (DCBX)

- Directed Call Pickup Exempt

- Denied Termination

Directed Call Park (DCPK)

- Denied Origination

- Denied Termination

Directed Call Pickup Non-Barge-In (DCPU)

- Automatic Line

- Directed Call Pickup with Barge-In

- Denied Origination

Directed Call Pickup Non-Barge-In Exempt (DCPX)

- Directed Call Pickup Barge-In Exempt

- Denied Termination

Denied Incoming (DIN)

- Bridged Night Number

- Denied Termination

- Private Business Line

- Single Call Arrangement

- Selective Call Forwarding

Distributed Line Hunt (DLH)

- Automatic Call Distribution

- Call Forwarding Busy

- Call Forwarding Don’t Answer

- Circular Hunting

- Call Waiting, Intergroup

- Call Waiting

- Call Waiting Terminating

- Call Waiting Exempt

- Directory Number Hunting

- MADN

- Multi-line Hunting

- Ring Again

- Series Completion

- Secondary Directory Number

- Stop Hunt

- Uniform Call Distribution

Do Not Disturb (DND)

- Denied Termination

- Private Business Line

- MADN

Directory number Hunting (DNH)

- Automatic Call Distribution

- Call Forwarding Busy

- Call Waiting Exempt

- Distributed Line Hunt

- MADN

- Multi-line hunting

- Series Completion

- Secondary Directory Number

- Uniform Call Distribution

Denied Originating (DOR)

- Automatic Callback

- Automatic Call Distribution

- Automatic Recall

- Call Forwarding Busy

- Call Forwarding Don’t Answer

- Call Forward, intragroup

- Call Forward Universal per Key

- Call Pickup

- Dial Call Waiting

- Call Waiting Originating

- Directed Call Pickup with Barge-in

- Directed Call Pickup Non Barge-in

- Directed Call Park

- Last Number Redial

- Make Set Busy

- Message Waiting Indication

- Message Waiting

- Call Park

- Ring Again

- Speed Calling

- Station Message Detail Recording

Denied Terminating (DTM)

- Automatic Callback

- Automatic Call Distribution

- Automatic Recall

- Call Forwarding Busy

- Call Forwarding Don’t Answer

- Call Forward Universal per Key

- Permanent Hold

- Calling Number Delivery

- Customer Oriented Trace

- Call Pickup

- Call Waiting, intergroup

- Call Waiting

- Call Waiting Terminating

- Call Waiting Exempt

- Directed Call Pickup Barge-In Exempt

- Directed Call Pickup Exempt

- Directed Call Park

- Denied Incoming

- Distinctive Ring Call Waiting

- Executive Busy Override Exempt

- Make Set Busy

- Message Waiting

- Call Park

- Ring Again

- Single Call Arrangement

- Selective Call Forwarding

- Secondary Directory Number

- Simplified Message Desk Interface

- Uniform Call Distribution

Executive Busy Override Exempt (EBX)

- Denied Termination

Essential Service Line (ESL)

- Calling Line Identification through Flash

- Feature Group A

- Series Completion

Group Intercom (GIC)

- Automatic Call Distribution

- MADN

Permanent Hold (HLD)

- Denied Origination

- Denied Termination

Last Number Redial (LNR)

- Automatic Line

- Denied Origination

- Last Number Redial Associated with set

Line Hunt Overflow to a Directory Number (LOD)

- Call Waiting Exempt

- Line Overflow to Route

- Series Completion

- Secondary Directory Number

Line Overflow to a Route (LOR)

- Call Waiting Exempt

- Line Hunt Overflow to a Directory number

- Series Completion

- Secondary Directory Number

Multiple Appearance Directory number (MADN)

- Automatic Answer Back

- Automatic Call Distribution

- Bridged Night Number

- Distributed Line Hunt

- Do Not Disturb

- Directory Number Hunting

- Group Intercom

- Multi-line Hunting

- Private Business Line

- Random Make Busy

- Secondary Directory Number

- Stop Hunt

- Simplified Message Desk interface

- Uniform Call Distribution

Multi-line Hunting (MLH)

- Automatic Call Distribution

- Call Forwarding Busy

- Call Forwarding Don’t Answer

- Distributed Line Hunt

- Directory Number Hunting

- MADN

- Ring Again

- Series Completion

- Secondary Directory Number

- Uniform Call Distribution

Make Set Busy (MSB)

- Denied Origination

- Denied Termination

- Make Set Busy, intragroup

Make Set Busy, intragroup ( MSBI)

- Denied Origination

- Denied Termination

- Make Set Busy

Message Waiting (MWT)

- Denied Origination

- Denied Termination

Private Business Line (PBL)

- Automatic line

- Bridged Night Number

- Calling Line identification

- Denied Incoming

- Do Not Disturb

- MADN

- Random Make Busy

- Stop Hunt

Ring Again (RAG)

- Automatic Callback

- Automatic Recall

- Bridged Night Number

- Distributed Line Hunt

- Denied Origination

- Denied Termination

- Multi-line Hunting

- Multiple Position Hunt with Queue

Random Make Busy (RMB)

- Automatic Call Distribution

- Call Waiting Exempt

- Feature Group A

- Make Set Busy Key

- MADN

- Secondary Directory Number

- Private Business Line

- Simplified Message Desk Interface

- Uniform Call Distribution

Speed Call Long (SCL)

- Automatic Line

- Bridged Night Number

- Denied Origination

- Speed Call User

Speed Call Short (SCS)

- Automatic Line

- Bridged Night Number

- Denied Origination

Speed Call User (SCU)

- Automatic Line

- Bridged Night Number

- Denied Origination

- Speed Calling Group, long list

Stop Hunt

- Automatic Call Distribution

- Call Waiting Exempt

- Distributed Line Hunt

- MADN

- Private Business Line

- Secondary Directory Number

- Simplified Message Desk Interface

- Uniform Call Distribution

Subscriber Line Usage (SLU)

- Private Business Line

Station Message Detail Recording (SMDR)

- Denied Origination

Special Billing Code (SPB)

- Bridged Night Number

- Private Business Line

Toll Denial (TDN)

- Automatic Line

- Toll Diversion

Toll Diversion (TDV)

- Automatic Line

- Toll Diversion

Uniform Call Distribution (UCD)

- Automatic Call Distribution

- Automatic Line

- Bridged Night Number

- Calling Number Delivery Blocking

- Distributed Line Hunt

- Directory Number Hunting

- Denied Termination

- Key Short Hunt

- MADN

- Multi-line Hunting

- Random Make Busy

- Series Completion

- Secondary Directory Number

- Stop Hunt

CPE Involvement

EKL requires the use of (non-ISDN) Meridian Business Sets which use a Type-C line card at the Central office.  This CPE uses an out-of-band signaling channel to communicate with the switch and enable the operation of feature-access keys and display features.

Meridian Business Sets

Every M5000 Meridian Business Set offers these standard features:

- Fixed Buttons

- Line/Features Keys

- Liquid Crystal Display (LCD) Indicators

- Primary Line Select

- On Hook Dialing

- Listen on Hold

- Ringing Tones

- Auto Hold

- DTMF End-to-End Signaling

M5008 Business Set

The M5008 offers a choice of selected key and system features and is equipped with the following:

  - Three fixed keys

  - A dial pad consisting of 12 fixed keys

  - Eight programmable feature and/or directory keys with LCD indicators

Meridian M5009 Business Set

The M5009 Business Set features:

- Three fixed keys:

  - Hold

  - Release

  - Speaker Volume Adjustment

- Eight programmable feature/directory number keys with LCD indicators (lamps)

- One programmable feature key without an LCD indicator (Key 9)

- Speaker for alerting tones, on-hook dialing, intercom

Meridian M5112 Business Set

The M5112 Business Set features:

- Five fixed keys:

  - Hold

  - Release

  - Mute

  - Hands-free

  - Speaker Volume Adjustment

- Ten programmable feature/directory number keys with LCD indicators (lamps)

- Microphone and speaker for hands-free operation

- The M5112 requires external power for operating the LCD key indicators for all keys beyond Key 8.

M5208 Business Set

The M5208 is equipped with the following choice of selected key and system features:

- Three fixed keys

- A dial pad consisting of 12 fixed keys

- Eight programmable feature and/or directory number keys with LCD indicators

- A speaker for alerting tones, on hook dialing and intercom

- The alphanumeric display module is mounted at the rear top edge of the telephone and is hinges so that the viewing angle can be adjusted physically to reduce glare and maximize the contrast. The maximum display capacity of the display screen is two rows of 24 characters each.

Meridian M5209 Display Set

The M5209 Business Set features:

- Three fixed keys:

  - Hold

  - Release

  - Speaker Volume Adjustment

- Nine programmable feature/directory number keys with LCD indicators (lamps)

- Speaker for alerting tones, on-hook dialing, and intercom

- Built-in display consisting of two lines of 24 characters each. The lower line displays dialed digits, and the upper line displays incoming DN and other call information.

M5216 Business Set

The M5216 ACD telephone set with alphanumeric display and a headset port has been designed specifically for use with ACD applications:

- 14 buttons with associated liquid crystal display (LCD) indicators that may be assigned to features or line appearance

- One button with associated LCD indicator for Handset Mute off/on

- One button with associated LCD indicator for Programming local features

- Hold, Release and Volume Control Keys

- 2X24 alphanumeric display

- 12 key dial pad

- Modular port for headset support

- The alphanumeric display module is mounted at the rear top edge of the telephone and is hinged so the viewing angle can be adjusted physically to reduce glare and maximize the contrast.

- The M5216 may be equipped with one or two M522, 22 button add-on modules.

Meridian M5312 Display Set

The M5312 Business Set features:

- Five fixed keys:

  - Hold

  - Release

  - Mute

  - Hands-free

  - Speaker Volume Adjustment

- Ten programmable feature/directory number keys with LCD indicators (lamps)

- Microphone and speaker for hands-free operation

- Built-in display consisting of two lines of 24 characters each. The lower line displays dialed digits, and the upper line displays incoming DN and other call information.

- The M5312 requires external power for operating the LCD key indicators for all keys beyond Key 8.

M5316 Business Set

The M5316 telephone set with alphanumeric display is a loudspeaker business phone set designed specifically for use in office environment.

- 13 buttons with associated liquid crystal display (LCD) indicators that may be assigned to features or line appearances

- One button with associated LCD indicator for Hands-free off/on

- One button with associated LCD indicator for Mute off/on

- One button with associated LCD indicator for Programming local features

- Hold, Release, and Volume Control Keys

- 2 X 24 alphanumeric display

- 12 key dial pad

- The alphanumeric display module is mounted at the rear top edge of the telephone and is hinged so the viewing angle can be adjusted physically to reduce glare and maximize the contrast.

- The M5316 may be equipped with one or two M522 22-button add-on modules.

Meridian M518 Add-On Module

- The M518 Add-On Module has 18 keys, all of which have an associated LCD indicator and can be programmed for a feature or directory number.

- The M518 can be used with any M5 business set. It is positioned to the right of the set and provided with auxiliary power supplies that accommodate both the add-on and the business set.

- Each M5000 business set can have up to three M518 add-ons or one M518 plus one Meridian M536 Add-On Module. The second M518 on the same set will start with Key 30; the third M518 will start with Key 48.

Meridian M522 Add-On Module

- M522, 22 button Add-On Module can be attached to the M5216 or M5316 Meridian Business Set to provide extra features/line keys.

- The 22 feature keys available on the M522 Add-On-Module are assigned key numbers to enable the switch to identify individual key functions.

Meridian M536 Add-On Module

- The M536 Add-On Module has 36 keys, all of which have an associated LCD indicator and can be programmed for a feature or directory number.

- The M536 can be used with any M5000 business set. It is positioned to the right of the set and provided with auxiliary power supplies that accommodate both the add-on and the business set.

- Each M5 business set can have up to one M536 plus one Meridian M518 Add-On Module. Only one M536 can be associated with a set.

CPE Feature Assignment Requirements for Analog and Business Sets

Feature - A

| Feature | Analog | Business Set |
| --- | --- | --- |
| AAB - Automatic Answerback*+ | No | Yes |
| AUD - Automatic Dial | No | Yes |
| AUL - Automatic Line | Yes | Yes |
| AUTODISP - Automatic Display+ | No | Yes |

Note:  *This feature requires a hands-free business set

+ This feature must be assigned to Key 1

Feature - C

| Feature | Analog | Business Set |
| --- | --- | --- |
| CCV - Call Coverage* | No | Yes |
| CFB (N1) - Call Forward Busy | Yes | Yes |
| CB1 (N5) - Call Forward Busy External Calls Only | Yes | Yes |
| CBE (N5) - Call Forward Busy Internal Calls Only | Yes | Yes |
| CBU (N5) - Call Forward Busy Unrestricted | Yes | Yes |
| IECFB (N5) - Call Forward Busy Internal/External | Yes | Yes |
| CFD (N1) - Call Forward Don't Answer | Yes | Yes |
| CDI (N9) - Call Forward Don't Answer External Calls Only | Yes | Yes |
| CDE (N9) - Call Forward Don't Answer Internal Calls Only | Yes | Yes |
| IECFD (N9) - Call Forward Don't Answer Internal/External | Yes | Yes |
| CDU (N9) - Call Forward Don't Answer Unrestricted | Yes | Yes |
| CFDVT - Call Forward Don't Answer Variable Timer | Yes | Yes |
| CFF - Call Forward Fixed† | Yes | Yes |
| CFGD - Call Forward Don't Answer For Hunt Group‡ | Yes | Yes |
| CFI (N1) - Call Forward IntraGroup | Yes | Yes |
| CFK (N1) - Call Forward On PCA/LPCA Per Key Basis | No | Yes |
| CFRA (N11) - Call Forward Remote Access | No | Yes |
| CFS (N10) - Call Forward Simultaneous | Yes | Yes |
| CFU (N1) - Call Forward Universal | Yes | Yes |
| CHD - Call Hold | Yes | No** |
| PRK - Call Park | Yes | Yes |
| CPU - Call Pick-Up | Yes | Yes |
| CXR - Call Transfer | Yes | Yes |
| CWD - Call Waiting Dial | Yes | Yes |
| CWT - Call Waiting, Basic | Yes | Yes |
| CWO - Call Waiting Originating | Yes | Yes |
| CWI - Call Waiting IntraGroup | Yes | Yes |
| CWR - Call Waiting Distinctive Ringing | No | Yes |
| CWX - Call Waiting Exempt | Yes | Yes |
| CLI - Calling Line Identification | Yes | Yes |
| CLF - Calling Line Identification with Flash | Yes | No |
| NAME - Calling Name Display | Yes | Yes |
| CTW - Call Transfer Warning Tone | Yes | Yes |
| CNF - Conference (Station Controlled) | Yes | Yes |
| CTD - Carrier Toll Denied | Yes | Yes |
| CDC - Customer Data Change | Yes | Yes |
| CCNAM – Custom Calling Name on Centrex | Yes | Yes |

Note:  * Can only be assigned to the secondary MADN appearance

†  This feature must be assigned to Key 1.

‡  CFGD must be assigned to the Pilot DN of a Hunt Group (DNH, MLH, DLH).

** Hold is accessed on the Business set by using the HOLD key.

Call Forward Notes

| Note | Description |
| --- | --- |
| N1 | All types of Call Forwarding must be assigned to the same key. |
| N5 | This feature customizes CFB. It must be assigned to the same key as CFB. All DNs in the CFB key list will be associated with this option. |
| N9 | This feature customizes CFD. It must be assigned to the same key as CFD. All DNs in the CFD key list will be associated with this option. |
| N10 | This feature is assigned to the Call Forwarding Key. All DNs in the keylist are associated with the option. |
| N11 | CFRA must be assigned to a line that already has a flavor of CFX assigned. |

Feature - D

| Feature | Analog | Business Set |
| --- | --- | --- |
| DIN - Denied Incoming | Yes | Yes |
| DOR - Denied Originating | Yes | Yes |
| DTM - Denied Terminating | Yes | Yes |
| DCPK - Directed Call Park | Yes | Yes |
| DCPU - Directed Call Pick-Up Non-Barge-In | Yes | Yes |
| DCBI - Directed Call Pick-Up Barge-In | Yes | Yes |
| DCBX - Directed Call Pick-Up Barge-In Exempt | Yes | Yes |
| DCPX - Directed Call Non-Barge-In Exempt | Yes | Yes |
| DND - Do Not Disturb | Yes | Yes |
| DRING - Distinctive Ringing | Yes | Yes |

Feature - E

| Feature | Analog | Business Set |
| --- | --- | --- |
| EBX - Executive Busy Override Exempt | Yes | Yes |
| EMW - Executive Message Waiting | Yes* | Yes |

Note:  *Only assigned to single line sets when using screening.

Feature - G

| Feature | Analog | Business Set |
| --- | --- | --- |
| GIC - Group Intercom | Yes | Yes |

Feature - I

| Feature | Analog | Business Set |
| --- | --- | --- |
| IMB - Inhibit Line Busy* | Yes | Yes |
| ILB - Inhibit Line Busy* | -- | -- |
| INSPECT - Inspect Key | No | Yes |

Note:  *This feature must be assigned to a line with CFB already assigned.

Feature - K

| Feature | Analog | Business Set |
| --- | --- | --- |
| KSH - Key Short Hunt* | No | Yes |
| KSMOH - Keyset Music On Hold | No | Yes |

Note:  *This feature must be assigned to Key 1.

Feature - L

| Feature | Analog | Business Set |
| --- | --- | --- |
| LNRA - Last Number Redial Associated with Set | No | Yes |
| LVM - Leave Message | No | Yes |

Feature - M

| Feature | Analog | Business Set |
| --- | --- | --- |
| MRFM - MADN Ring Forward Manual | No | Yes |
| MEMDISP - MADN Member Display* | No | Yes |
| MBK - Make Busy Key† | -- | -- |
| MSB - Make Set Busy | Yes | Yes |
| MSB1 - Make Set Busy IntraGroup | Yes | Yes |
| MCH - Malicious Call Hold | No | Yes |
| MWQRY - Message Waiting Query | No | Yes |
| MWT - Message Waiting Tone (Stutter) | Yes | No |
| MDN - Multiple Appearance Directory Number | Yes | Yes |
| MWIDC - Message Waiting Indicator (Lamp) | No | Yes |
| MDN-NAME - Multiple Appearance Directory Number Name | Yes | Yes |

Note:  * Must be assigned to a secondary member of a MADN group.
† This feature must be assigned to a line that already has CFB assigned

Feature - P

| Feature | Analog | Business Set |
| --- | --- | --- |
| HLD - Permanent Hold | Yes | No* |
| PIC - Primary InterLATA Carrier | Yes | Yes |
| PRV - Privacy | No | Yes |
| PRL - Privacy Release | No | Yes |

Note:  *Message Waiting is available on analog sets by Stutter dial tone.  The “link” set makes a message waiting lamp available.  Business sets utilize the HOLD key.

Feature - Q

| Feature | Analog | Business Set |
| --- | --- | --- |
| QTD - Query Time And Date | No | Yes |

Feature - R

| Feature | Analog | Business Set |
| --- | --- | --- |
| RAG - Ring Again | Yes | Yes |
| IRR - Ring Reminder Off/On | Yes | Yes |

Feature - S

| Feature | Analog | Business Set |
| --- | --- | --- |
| CFMDN - Secondary MADN Call Forwarding | Yes | Yes |
| SCMP - Series Completion | Yes | Yes |
| SPB - Special Billing Code | Yes | Yes |
| SCL - Speed Call Long | Yes | Yes |
| SCS - Speed Call Short | Yes | Yes |
| SCU - Speed Call User | Yes | Yes |
| SMD1 - Simplified Message Desk Interface | Yes | Yes |
| MBSCAMP - Station Camp-on | No | Yes |
| SMDR - Station Message Detail Recording | Yes | Yes |
| SSAC - Station Specific Authorization Code | Yes | Yes |
| SOR - Station Origination Restrictions | Yes | Yes |
| SORC - Station Origination Restrictions Controller | Yes | Yes |
| SLU - Subscriber Line Usage | Yes | Yes |

Feature - T

| Feature | Analog | Business Set |
| --- | --- | --- |
| 3WC - Three-Way Call | Yes | Yes |

Feature - U

| Feature | Analog | Business Set |
| --- | --- | --- |
| UCDLG - Uniform Call Distribution Login | No | Yes |
| UCDSD - Uniform Call Distribution Signal Distributor Point | No | Yes |

Ordering

Procedures

- Contact your Service Manager regarding a 'loop' qualification for the end user's address or addresses where the EKL equipment will be located.

- Conduct station review with end user and verify EKL equipment the end user will purchase and its availability.

- Submit Centrex Service Request and Resale Electronic Key Line Order Form to LSC (Local Service Center).

Loop Qualifications

- AT&T verifies that the local loop is qualified to handle a particular service like Electronic Key Lines prior to the service being ordered.

- Loop qualifications are done for the following products and services:

  - Electronic Key line

  - ISDN Direct

  - ISDN Centrex

  - ISDN Intra Service Area (MSA105)

- When the CLEC contacts their Service Manager, the Loop Qualification process begins.

Feature Order Information

The following alphabetical tables provide the feature names and appropriate switch codes.   In addition, the matrix provides an easy reference for feature categories (e.g., set feature, button, or code access).

| Feature Category | Characteristics |
| --- | --- |
| Set Features | If button activated, features in this category are assigned to a vacant key on the set. If access code activated, features must be assigned to Key 1 of the set. These features are associated with all the directory number appearances on the set. |
| Keylist Features | These features are associated with only the keys that are specified in the keylist area. |
| Key Features | These features have the same scope as Set Features, but they can have more than one key appearance on the set. |
| Directory Number (DN) Features | These features are assigned to the l directory number appearance to which the features are to be used. |
| MADN Features | These features must be assigned to the PRIMARY MADN appearance of a directory number. |
| Dedicated Key Features | These features may be assigned to a vacant key on the set. |
| Lamp Features | These features, when assigned to a dedicated key, must have a functioning lamp. |
| Code Access | These features may be accessed by dialing an access code. Must be assigned to key 1 if a dedicated key is not used. |
| Display Features | These features require a set with display capabilities. |

Feature - A

| Feature | Set | Subset | Key | DN |
| --- | --- | --- | --- | --- |
| AAB - Automatic Answerback* | Yes | -- | -- | -- |
| AUD - Automatic Dial | -- | -- | Yes | -- |
| AUL - Automatic Line | -- | -- | -- | Yes |
| AUTODISP - Automatic Display† | -- | Yes | -- | -- |

Note:  *This feature requires a hands-free business set.

† This feature must be assigned to Key 1.

Feature - C

| Feature | Set | Subset | Key | DN |
| --- | --- | --- | --- | --- |
| CCV - Call Coverage* | -- | -- | Yes | -- |
| CFB (N1) - Call Forward Busy | -- | Yes | -- | -- |
| CB1 (N5) - Call Forward Busy External Calls Only | -- | -- | -- | -- |
| CBE (N5) - Call Forward Busy Internal Calls Only | -- | -- | -- | -- |
| CBU (N5) - Call Forward Busy Unrestricted | -- | -- | -- | -- |
| IECFB (N5) - Call Forward Busy Internal/External | -- | -- | -- | -- |
| CFD (N1) - Call Forward Don't Answer | -- | Yes | -- | -- |
| CDI (N9) - Call Forward Don't Answer External Calls Only | -- | -- | -- | -- |
| CDE (N9) - Call Forward Don't Answer Internal Calls Only | -- | -- | -- | -- |
| IECFD (N9) - Call Forward Don't Answer Internal/External | -- | -- | -- | -- |
| CDU (N9) - Call Forward Don't Answer Unrestricted | -- | -- | -- | -- |
| CFDVT - Call Forward Don't Answer Variable Timer | -- | -- | -- | Yes |
| CFF - Call Forward Fixed† | -- | Yes | -- | -- |
| CFGD - Call Forward Don't Answer For Hunt Group‡ | -- | -- | -- | Yes |
| CFI (N1) - Call Forward IntraGroup | -- | Yes | -- | -- |
| CFK (N1) - Call Forward On PCA/LPCA Per Key Basis | -- | -- | -- | -- |
| CFRA (N11) - Call Forward Remote Access | -- | -- | -- | -- |
| CFS (N10) - Call Forward Simultaneous | -- | -- | -- | -- |
| CFU (N1) - Call Forward Universal | -- | Yes | -- | -- |
| CHD - Call Hold | -- | -- | -- | -- |
| PRK - Call Park | Yes | -- | -- | -- |
| CPU - Call Pick-Up | -- | Yes | -- | -- |
| CXR - Call Transfer | Yes | -- | -- | -- |
| CWD - Call Waiting Dial | -- | -- | -- | Yes |
| CWT - Call Waiting Basic | -- | Yes | -- | -- |
| CWO - Call Waiting Originating | -- | -- | -- | Yes |
| CWI - Call Waiting IntraGroup | -- | -- | -- | Yes |
| CWR - Call Waiting Distinctive Ringing | -- | -- | -- | Yes |
| CWX - Call Waiting Exempt | -- | Yes | -- | - |
| CLI - Calling Line Identification | -- | -- | -- | Yes |
| CLF - Calling Line Identification with Flash | -- | -- | -- | -- |
| NAME - Calling Name Display | -- | -- | -- | Yes |
| CTW - Call Transfer Warning Tone | -- | -- | -- | Yes |
| CNF - Conference (Station Controlled) | Yes | -- | -- | -- |
| CTD - Carrier Toll Denied | -- | -- | -- | Yes |
| CDC - Customer Data Change | Yes | -- | -- | -- |
| CCNAM – Custom Calling Name on Centrex | -- | -- | -- | Yes |

| Note: | * Can only be assigned to the secondary MADN appearance. † This feature must be assigned to Key 1. ‡ CFGD must be assigned to the Pilot DN of a Hunt Group (DNH, MLH, DLH). |
| --- | --- |

Call Forward Notes

| Note | Description |
| --- | --- |
| N1 | All types of Call Forwarding must be assigned to the same key. |
| N5 | This feature customizes CFB. It must be assigned to the same key as CFB. All DNs in the CFB key list will be associated with this option. |
| N9 | This feature customizes CFD. It must be assigned to the same key as CFD. All DNs in the CFD key list will be associated with this option. |
| N10 | This feature is assigned to the Call Forwarding Key. All DNs in the keylist are associated with the option. |
| N11 | CFRA must be assigned to a line that already has a flavor of CFX assigned. |

Feature - D

| Feature | Set | Subset | Key | DN |
| --- | --- | --- | --- | --- |
| DIN - Denied Incoming | -- | -- | -- | Yes |
| DOR - Denied Originating | -- | -- | -- | Yes |
| DTM - Denied Terminating | -- | -- | -- | Yes |
| DCPK - Directed Call Park | Yes | -- | -- | -- |
| DCPU - Directed Call Pick-Up Non-Barge-In | -- | -- | -- | Yes |
| DCBI - Directed Call Pick-Up Barge-In | -- | -- | -- | Yes |
| DCBX - Directed Call Pick-Up Barge-In Exempt | -- | -- | -- | Yes |
| DCPX - Directed Call Non-Barge-In Exempt | -- | -- | -- | Yes |
| DND - Do Not Disturb | -- | -- | -- | Yes |
| DRING - Distinctive Ringing | Yes | -- | -- | -- |

Feature - E

| Feature | Set | Subset | Key | DN |
| --- | --- | --- | --- | --- |
| EBX - Executive Busy Override Exempt | Yes | -- | -- | -- |
| EMW - Executive Message Waiting | -- | -- | Yes | -- |

Feature - G

| Feature | Set | Subset | Key | DN |
| --- | --- | --- | --- | --- |
| GIC - Group Intercom | -- | -- | Yes | -- |

Feature - I

| Feature | Set | Subset | Key | DN |
| --- | --- | --- | --- | --- |
| IMB - Inhibit Line Busy* | -- | -- | -- | -- |
| ILB - Inhibit Line Busy* | Yes | -- | -- | -- |
| INSPECT - Inspect Key | Yes | -- | -- | -- |

| Note: | * This feature must be assigned to a line with CFB already assigned. |
| --- | --- |

Feature - K

| Feature | Set | Subset | Key | DN |
| --- | --- | --- | --- | --- |
| KSH - Key Short Hunt* | -- | Yes | -- | -- |
| KSMOH - Keyset Music On Hold | Yes | -- | -- | -- |

| Note: | * This feature must be assigned to Key 1. |
| --- | --- |

Feature - L

| Feature | Set | Subset | Key | DN |
| --- | --- | --- | --- | --- |
| LNRA - Last Number Redial Associated with Set | Yes | -- | -- | -- |
| LVM - Leave Message | Yes | -- | -- | -- |

Feature - M

| Feature | Set | Subset | Key | DN |
| --- | --- | --- | --- | --- |
| MRFM - MADN Ring Forward Manual | -- | Yes | Yes | -- |
| MEMDISP - MADN Member Display* | -- | -- | -- | Yes |
| MBK - Make Busy Key† | -- | -- | -- | -- |
| MSB - Make Set Busy | -- | Yes | -- | -- |
| MSB1 - Make Set Busy IntraGroup | -- | Yes | -- | -- |
| MCH - Malicious Call Hold | Yes | -- | -- | -- |
| MWQRY - Message Waiting Query | Yes | -- | -- | -- |
| MWT-LMP - Message Waiting Lamp/Visual | -- | -- | -- | Yes |
| MWT-STD – Message Waiting Stutter Dial Tone/Audible | -- | -- | -- | -- |
| MDN - Multiple Appearance Directory Number | -- | -- | -- | Yes |
| MWIDC - Message Waiting Indicator | Yes | -- | -- | -- |
| PF - Name Programming Power Feature | Yes | -- | -- | -- |
| MDN-NAME - Multiple Appearance Directory Number Name | -- | -- | -- | Yes |

| Note: | * This feature must be assigned to Key 1. † This feature must be assigned to a line that already has CFB assigned. |
| --- | --- |

Feature - P

| Feature | Set | Subset | Key | DN |
| --- | --- | --- | --- | --- |
| HLD - Permanent Hold | -- | -- | -- | -- |
| PIC - Primary InterLATA Carrier | -- | -- | -- | Yes |
| PRV - Privacy | Yes | -- | -- | -- |
| PRL - Privacy Release | Yes | -- | -- | -- |

Feature - Q

| Feature | Set | Subset | Key | DN |
| --- | --- | --- | --- | --- |
| QTD - Query Time And Date | Yes | -- | -- | -- |

Feature - R

| Feature | Set | Subset | Key | DN |
| --- | --- | --- | --- | --- |
| RAG - Ring Again | Yes | -- | -- | -- |
| IRR - Ring Reminder Off/On | -- | -- | -- | Yes |

Feature - S

| Feature | Set | Subset | Key | DN |
| --- | --- | --- | --- | --- |
| CFMDN - Secondary MADN Call Forwarding | -- | -- | -- | Yes |
| SCMP - Series Completion | -- | -- | -- | Yes |
| SPB - Special Billing Code | -- | -- | Yes | -- |
| SCL - Speed Call Long | Yes | -- | -- | -- |
| SCS - Speed Call Short | Yes | -- | -- | -- |
| SCU - Speed Call User | Yes | -- | -- | -- |
| SMD1 - Simplified Message Desk Interface | -- | -- | -- | Yes |
| MBSCAMP - Station Camp-on | -- | -- | Yes | -- |
| SMDR - Station Message Detail Recording | -- | -- | -- | Yes |
| SSAC - Station Specific Authorization Code | -- | -- | -- | Yes |
| SOR - Station Origination Restrictions | -- | -- | -- | Yes |
| SORC - Station Origination Restrictions Controller | -- | -- | -- | Yes |
| SLU - Subscriber Line Usage | -- | -- | -- | Yes |

Feature - T

| Feature | Set | Subset | Key | DN |
| --- | --- | --- | --- | --- |
| 3WC - Three-Way Call | Yes | -- | -- | -- |

Feature - U

| Feature | Set | Subset | Key | DN |
| --- | --- | --- | --- | --- |
| UCDLG - Uniform Call Distribution Login | -- | -- | Yes | -- |
| UCDSD - Uniform Call Distribution Signal Distributor Point | -- | -- | -- | Yes |

Additional Order Information for EKLs

The following alphabetical feature tables serve as a reference to Business Set feature assignment requirements to aid in correctly provisioning the EKL set.

| Legend for Additional Information Columns |
| --- |
| MADN Features | These features, like DN features, are associated with a specific directory number appearance. - When these features are associated with Multiple Appearance Directory Number (MADN), they must be assigned to the primary appearance of the MADN. - When a MADN feature is assigned to the primary appearance, it is associated with every MADN group number. |
| Dedicated Key | Features in this category show the features that require a lamp (LCD Indicators) when assigned to a key on the set. |
| Code Access Features | Features in this category may either be set or subset features. These are the features that may be accessed by dialing a special code specified and therefore do not necessarily have to be assigned to a vacant key. However, they must be assigned to the PDN key of the set, Key 1. |
| Display | Features in this category require sets with display. |
| Lamp Features | The Lamp category shows the features that require a lamp (LCD Indicator) when assigned to a key on the Business Set. The M5009 is the only Meridian Business Set that does not have a lamp associated with all feature/DN keys. It does not have a lamp associated with Key 9; therefore, a feature that does not require a lamp would be a candidate for this key. |

Feature - A

| Feature | MADN | Dedicated Key | Lamp | Code | Display |
| --- | --- | --- | --- | --- | --- |
| AAB - Automatic Answerback* | -- | Yes | Yes | -- | -- |
| AUD - Automatic Dial | -- | Yes | Yes | -- | -- |
| AUL - Automatic Line | -- | -- | -- | -- | -- |
| AUTODISP - Automatic Display† | -- | -- | -- | -- | Yes |

| Note: | * This feature requires a hands-free Business Set. † This feature must be assigned to Key 1. |
| --- | --- |

Feature - B

| Feature | MADN | Dedicated Key | Lamp | Code | Display |
| --- | --- | --- | --- | --- | --- |
| BLF - Busy Lamp Field | -- | Yes | Yes | -- | -- |

Feature - C

| Feature | MADN | Dedicated Key | Lamp | Code | Display |
| --- | --- | --- | --- | --- | --- |
| CCV - Call Coverage* | -- | Yes | Yes | -- | -- |
| CFB (N1) - Call Forward Busy · No Control · Fixed · Programmable | Yes | -- | -- | -- N2 N3 N4 | -- |
| CB1 (N5) - Call Forward Busy External Calls Only | Yes | -- | -- | -- | -- |
| CBE (N5) - Call Forward Busy Internal Calls Only | Yes | -- | -- | -- | -- |
| CBU (N5) - Call Forward Busy Unrestricted | Yes | -- | -- | -- | -- |
| IECFB (N5) - Call Forward Busy Internal/External | Yes | -- | -- | -- | -- |
| CFD (N1) - Call Forward Don't Answer · No Control · Fixed · Programmable | Yes | -- | -- | -- | -- N6 N7 N8 |
| CDI (N9) - Call Forward Don't Answer External Calls Only | Yes | -- | -- | -- | -- |
| CDE (N9) - Call Forward Don't Answer Internal Calls Only | Yes | -- | -- | -- | -- |
| IECFD (N9) - Call Forward Don't Answer Internal/External | Yes | -- | -- | -- | -- |
| CDU (N9) - Call Forward Don't Answer Unrestricted | Yes | -- | -- | -- | -- |
| CFDVT - Call Forward Don't Answer Variable Timer | -- | -- | -- | -- | -- |
| CFF - Call Forward Fixed† | Yes | Yes | Yes | Yes | -- |
| CFGD - Call Forward Don't Answer For Hunt Group‡ | Yes | Yes | Yes | Yes | -- |
| CFI (N1) - Call Forward IntraGroup | Yes | Yes | Yes | Yes | -- |
| CFK (N1) - Call Forward On PCA/LPCA Per Key Basis | Yes | Yes | Yes | Yes | -- |
| CFRA (N11) - Call Forward Remote Access | Yes | Yes | Yes | Yes | -- |
| CFS (N10) - Call Forward Simultaneous | Yes | -- | -- | -- | -- |
| CFU (N1) - Call Forward Universal | Yes | Yes | Yes | Yes | -- |
| CHD - Call Hold | -- | -- | -- | -- | -- |
| PRK - Call Park | -- | Yes | Yes | Yes | -- |
| CPU - Call Pick-Up | -- | Yes | -- | Yes | -- |
| CXR - Call Transfer | -- | Yes | Yes | -- | -- |
| CWD - Call Waiting Dial | -- | -- | -- | Yes | -- |
| CWT - Call Waiting, Basic | -- | Yes | Yes | -- | -- |
| CWO - Call Waiting Originating | -- | -- | -- | -- | -- |
| CWI - Call Waiting IntraGroup | -- | -- | -- | -- | -- |
| CWR - Call Waiting Distinctive Ringing | -- | -- | -- | -- | -- |
| CWX - Call Waiting Exempt | -- | -- | -- | -- | -- |
| CLI - Calling Line Identification | -- | -- | -- | -- | -- |
| CLF - Calling Line Identification with Flash | -- | -- | -- | -- | -- |
| NAME - Calling Name Display | -- | -- | -- | -- | Yes |
| CTW - Call Transfer Warning Tone | -- | -- | -- | -- | -- |
| CNF - Conference (Station Controlled) | -- | Yes | Yes | Yes | -- |
| CTD - Carrier Toll Denied | -- | -- | -- | -- | -- |
| CDC - Customer Data Change | -- | -- | -- | -- | -- |

| Note: | * Can only be assigned to the secondary MADN appearance. † This feature must be assigned to Key 1. ‡ CFGD must be assigned to the Pilot DN of a Hunt Group (DNH, MLH, DLH). |
| --- | --- |

Call Forward Notes

| Note | Description |
| --- | --- |
| N1 | All types of Call Forwarding must be assigned to the same key. |
| N2 | CFBDN is fixed in Service Order. CFB occurs automatically. |
| N3 | CFBDN is fixed in Service Order. Access codes are needed to activate and deactivate CFB. |
| N4 | The end-user programs the CFBDN. Access codes are needed to program/activate and deactivate CFB. |
| N5 | This feature customizes CFB. It must be assigned to the same key as CFB. All DNs in the CFB key list will be associated with this option. |
| N6 | CFDDN is fixed in Service Order. CFD occurs automatically. |
| N7 | CFDDN is fixed in Service Order. Access codes are needed to activate and deactivate CFD. |
| N8 | The end-user programs the CFDDN. Access codes are needed to program/activate and deactivate CFD. |
| N9 | This feature customizes CFD. It must be assigned to the same key as CFD. All DNs in the CFD key list will be associated with this option. |
| N10 | This feature is assigned to the Call Forwarding key. All DNs in the key list are associated with the option. |
| N11 | CFRA must be assigned to a line that already has a flavor of CFX assigned. |

Feature - D

| Feature | MADN | Dedicated Key | Lamp | Code | Display |
| --- | --- | --- | --- | --- | --- |
| DCF - Denied Call Forward | Yes | -- | -- | -- | -- |
| DIN - Denied Incoming | -- | Yes | -- | Yes | -- |
| DOR - Denied Originating | -- | -- | -- | -- | -- |
| DTM - Denied Terminating | -- | -- | -- | -- | -- |
| DCPK - Directed Call Park | -- | Yes | Yes | Yes | Yes |
| DCPU - Directed Call Pick-Up Non-Barge-In | Yes | -- | -- | Yes | -- |
| DCBI - Directed Call Pick-Up Barge-In | Yes | -- | -- | Yes | -- |
| DCBX - Directed Call Pick-Up Barge-In Exempt | Yes | -- | -- | -- | -- |
| DCPX - Directed Call Non-Barge-In Exempt | Yes | -- | -- | -- | -- |
| DND - Do Not Disturb | Yes | -- | -- | -- | -- |
| DRING - Distinctive Ringing | -- | -- | -- | -- | -- |

Feature - E

| Feature | MADN | Dedicated Key | Lamp | Code | Display |
| --- | --- | --- | --- | --- | --- |
| EBO - Executive Busy Override | -- | Yes | -- | Yes | -- |
| EBX - Executive Busy Override Exempt | -- | -- | -- | -- | -- |
| EMW - Executive Message Waiting | -- | Yes | Yes | -- | -- |

Feature - G

| Feature | MADN | Dedicated Key | Lamp | Code | Display |
| --- | --- | --- | --- | --- | --- |
| GIAC - Group Intercom All Calls | -- | Yes | Yes | -- | -- |
| GIC - Group Intercom | -- | Yes | Yes | -- | -- |

Feature - I

| Feature | MADN | Dedicated Key | Lamp | Code | Display |
| --- | --- | --- | --- | --- | --- |
| ICM - Intercom | -- | Yes | Yes | -- | -- |
| IMB - Inhibit Line Busy* | -- | -- | -- | -- | -- |
| ILB - Inhibit Line Busy† | -- | -- | -- | -- | -- |
| INSPECT - Inspect Key | -- | Yes | Yes | -- | Yes |

| Note: | * Only assign to Single Line Sets when using screening. † This feature must be assigned to a line with CFB already assigned. |
| --- | --- |

Feature - K

| Feature | MADN | Dedicated Key | Lamp | Code | Display |
| --- | --- | --- | --- | --- | --- |
| KSH - Key Short Hunt* | Yes | -- | -- | -- | -- |
| KSMOH - Keyset Music On Hold | -- | -- | -- | -- | -- |

| Note: | * This feature must be assigned to Key 1. |
| --- | --- |

Feature - L

| Feature | MADN | Dedicated Key | Lamp | Code | Display |
| --- | --- | --- | --- | --- | --- |
| LNR - Last Number Redial | -- | -- | -- | Yes | -- |
| LNRA - Last Number Redial Associated with Set | -- | -- | -- | Yes | -- |
| LVM - Leave Message | -- | Yes | Yes | -- | -- |

Feature - M

| Feature | MADN | Dedicated Key | Lamp | Code | Display |
| --- | --- | --- | --- | --- | --- |
| MRF - MADN Ring Forward | -- | -- | -- | -- | -- |
| MRFM - MADN Ring Forward Manual | -- | Yes | Yes | -- | -- |
| MEMDISP - MADN Member Display* | -- | -- | -- | -- | -- |
| MBK - Make Busy Key† | -- | -- | -- | -- | -- |
| MSB - Make Set Busy | -- | Yes | Yes | Yes | -- |
| MSB1 - Make Set Busy IntraGroup | -- | Yes | -- | Yes | -- |
| MCH - Malicious Call Hold | -- | Yes | -- | Yes | -- |
| MWQRY - Message Waiting Query | -- | Yes | Yes | -- | -- |
| MWT - Message Waiting | Yes | Yes | Yes | Yes | -- |
| MDN - Multiple Appearance Directory Number | -- | -- | -- | -- | -- |
| MWIDC - Message Waiting Indicator | -- | Yes | Yes | -- | -- |
| PF - Name Programming Power Feature | -- | Yes | Yes | Yes | Yes |
| MDN-NAME - Multiple Appearance Directory Number Name | -- | -- | -- | -- | Yes |

| Note: | * Must be assigned to a secondary member of a MADN group. † This feature must be assigned to a line that already has CFB assigned. |
| --- | --- |

Feature - O

| Feature | MADN | Dedicated Key | Lamp | Code | Display |
| --- | --- | --- | --- | --- | --- |
| OLS - Originating Line Selection | -- | -- | -- | -- | -- |

Feature - P

| Feature | MADN | Dedicated Key | Lamp | Code | Display |
| --- | --- | --- | --- | --- | --- |
| HLD - Permanent Hold | -- | -- | -- | -- | -- |
| PIC - Primary InterLATA Carrier | -- | -- | -- | -- | -- |
| PRV - Privacy | -- | Yes | -- | Yes | -- |
| PRL - Privacy Release | -- | Yes | -- | Yes | -- |

Feature - Q

| Feature | MADN | Dedicated Key | Lamp | Code | Display |
| --- | --- | --- | --- | --- | --- |
| QBS - Query Busy Station | -- | Yes | Yes | -- | -- |
| QTD - Query Time And Date | -- | Yes | -- | -- | Yes |

Feature - R

| Feature | MADN | Dedicated Key | Lamp | Code | Display |
| --- | --- | --- | --- | --- | --- |
| RMB - Random Make Busy | -- | -- | -- | -- | -- |
| RAG - Ring Again | -- | Yes | Yes | -- | -- |
| IRR - Ring Reminder Off/On | -- | -- | -- | -- | -- |

Feature - S

| Feature | MADN | Dedicated Key | Lamp | Code | Display |
| --- | --- | --- | --- | --- | --- |
| SEC - Security | -- | -- | -- | -- | -- |
| CFMDN - Secondary MADN Call Forwarding | -- | -- | -- | Yes | -- |
| SCMP - Series Completion | -- | -- | -- | -- | -- |
| SPB - Special Billing Code | -- | -- | -- | -- | -- |
| SCL - Speed Call Long | -- | Yes | Yes | Yes | -- |
| SCRJ – Call Screening | Yes | Yes | -- | Yes | -- |
| SCS - Speed Call Short | -- | Yes | Yes | Yes | -- |
| SCU - Speed Call User | -- | Yes | Yes | Yes | -- |
| SMD1 - Simplified Message Desk Interface | Yes | -- | -- | -- | -- |
| MBSCAMP - Station Camp-on | -- | Yes | Yes | -- | Yes |
| SMDR - Station Message Detail Recording | -- | -- | -- | -- | -- |
| SSAC - Station Specific Authorization Code | -- | -- | -- | Yes | -- |
| SOR - Station Origination Restrictions | -- | -- | -- | -- | -- |
| SORC - Station Origination Restrictions Controller | -- | -- | -- | -- | -- |
| SLU - Subscriber Line Usage | Yes | -- | -- | -- | -- |

Feature - T

| Feature | MADN | Dedicated Key | Lamp | Code | Display |
| --- | --- | --- | --- | --- | --- |
| TLS - Terminating Line Select | -- | -- | -- | -- | -- |
| 3WC - Three-Way Call | -- | Yes | Yes | -- | -- |

Feature - U

| Feature | MADN | Dedicated Key | Lamp | Code | Display |
| --- | --- | --- | --- | --- | --- |
| UCD - Uniform Call Distribution | -- | -- | -- | -- | -- |
| UCDLG - Uniform Call Distribution Login | -- | Yes | Yes | -- | -- |
| UCDSD - Uniform Call Distribution Signal Distributor Point | -- | -- | Yes | -- | -- |

Due Dates

Refer to the Resale Due Date matrix for standard due date intervals.

Class of Service

See applicable Centrex document.

USOCs

EKL Station USOCs

| USOC | Description |
| --- | --- |
| SXPAC | - This USOC is used to indicate a Centrex electronic key line (EKL). - SXPAC is always associated with the line appearing on the first key of an electronic key telephone set. - There should be one SXPAC for every EKL in the system. |
| SXMKC | Note: This type of arrangement is no longer offered and cannot be used. This USOC was used to indicate a square key arrangement, that being an SXPAC (key one on an EKL) being extended as the primary number to the key one of another EKL. |
| SOT | - This USOC is used to indicate an software appearance of a number on an EKL set. - A SOT can never appear on Key 1 of an EKL. The same SOT can have up to 16 appearances but becomes a MADN after the second appearance. - Cable/pairs are not assigned to a SOT. This number appears as a button on a EKL and uses the cable/pair assigned to the primary number on the set. |
| SXBQA (IL) SXBRA (IN only) SXFQA (OH only) | - The SXBQA/SXBRA/SXFQA USOC is used to indicate that the primary number of a EKL (SXPAC) is extended to a single line telephone set. |
| NUE NDU | Intercom USOC IL, MI & WI Intercom USOC OH |

Optional Electronic Key Features USOCs

These ACS Optional EKL features are available for an additional cost. See Billing.

Illinois

| Optional Electronic Key Features | USOC |
| --- | --- |
| Add on Modules EKL: 10 or 18 button 20, 22 or 36 button | PT3CA PT3CB |
| Calling Name Display on Intercom | ZCQMD |
| Call Forward over private facilities | ZCFVP |
| Direct Connect Originating | ZAULN |
| Direct Connect Originating with Delay | ZXAWL |
| Direct Station Select/Busy Lamp Field with Fast Connect and Camp-On | BUY |
| Distance Extension | LOV |
| Executive Display Communications | EMV |
| Make Busy Key | ZXMBK |
| Message Waiting Visual | ZMWVW* |
| Multiple Appearance Directory Numbers in a Multiple Call Arrangement (MCA) | MA8 |
| Query Busy Station | QB2 |
| Repeat Alert | ZDCRB |
| Speed Calling Expanded Number Group: Controller 50# Controller 70# Controller 80# | ZSCC5 ZSCC7 ZSCC8 |
| Speed Calling Expanded Number Group: User 50# User 70# User 80# | ZSC50 ZSC70 ZSC80 |

Note:  *If the end user’s lamping is associated with a number which resides on a key other than 1, they need Executive Message Waiting.

Indiana

| Optional Electronic Key Features | USOC |
| --- | --- |
| Calling Name Display on Intercom | NDFPK |
| Camp-On | CPKPK |
| Direct Connect Originating | ZAULN |
| Direct Station Select/Busy Lamp Field | BUDPK |
| Executive Message Waiting | EMVPK |
| Extended Loop Facility | LOV |
| Inspect | NP6PK |
| Multiple Call Appearance | MGA |
| Message Waiting Visual | ZMWVW* |
| Repeat Alert | ZDCRB |
| Single Line Extension | 25S |

Note:  *If the end user’s lamping is associated with a number which resides on a key other than 1, they need Executive Message Waiting.

Michigan

| Optional Electronic Key Features | USOC |
| --- | --- |
| Add on Modules EKL: 10 or 18 button 20, 22 or 36 button | PT3CA PT3CB |
| Call Forward Reason Display | ZFRD1 |
| Calling Name Display on Intercom | ZCQMD |
| Direct Station Selection/Busy Lamp Field with Camp-On (per set) | BUY |
| Distance Extension for EKL | LOV |
| Executive Display Communications | EMVPS |
| Executive Message Waiting | EMVPK |
| Multiple Appearance Directory Numbers (MADN) | MA8 |
| Message Waiting Visual | ZMWVW* |
| Network Name Display | NKUPS |
| Network Number Display | NKVPS |
| Privacy Release Conference Control | PE8PS |
| Query Busy Station | ZQBST |
| Repeat Alert | ZDCRB |

Note:  *If the end user’s lamping is associated with a number which resides on a key other than 1, they need Executive Message Waiting.

Ohio

| Optional Electronic Key Features | USOC |
| --- | --- |
| Add on Modules EKL: 10 or 18 button 20, 22 or 36 button | N/A |
| Calling Name Display on Intercom | ZCQMD |
| Direct Station Select/Busy Lamp Field with Fast Connect and Camp-On | BUY |
| Electronic Key Range Extender | LOV |
| Executive Message Waiting | EMVPK |
| Fast Transfer for Business Sets | FTU |
| Message Desk Attendant Arrangement | ANZPC |
| Message Waiting Visual | ZMWVW* |
| Multiple Appearance Directory Numbers in a Multiple Call Arrangement (MCA): · MADN Bridging Capability · MADN Bridging 3WC · MADN Cut-off on Disconnect (COD) · MADN Ring Forward (MRF) · Privacy Release (PRL) · Secondary MADN Call Forwarding (CFMDN) | MA8 |
| Station Camp-on for Business Sets | CPK |
| Query Busy Station | QB2 |
| Repeat Alert | ZDCRB |

Note:  *If the end user’s lamping is associated with a number which resides on a key other than 1, they need Executive Message Waiting.

Wisconsin

| Optional Electronic Key Features | USOC |
| --- | --- |
| Add on Modules: 10 or 18 button 20, 22 or 36 button | PT3CA PT3CB |
| Calling Name Display on Intercom | ZCQMD |
| Distance Extension-per EKL | LOV |
| Executive Display Communications | EMV |
| Executive Message Waiting | EMVPK |
| Make Busy Access Code | DKV |
| Make Busy Key | DKV |
| Message Waiting Visual | ZMWVW* |
| Multiple Appearance Directory Number (MADN) in a Multiple Call Arrangement (MCA) | MA8 |
| Repeat Alert | ZDCRB |
| Telephone Number Reprogramming Service | NR9CR |

Note:  *If the end user’s lamping is associated with a number which resides on a key other than 1, they need Executive Message Waiting.

FIDs

| FID | Description |
| --- | --- |
| BG | Bill Group - Is a method of grouping Centrex station for the application of trunk equivalency. For ACS, the BG number is always 1. Order Placement: Not required |
| CAR | Call Send - DMS100 Only Indicates whether the station line identified can send Message Waiting signals to another station with the Centrex group. Order Placement: FEATURE DETAIL Field following the USOC in the FEATURE field. Example: ZMYAD/CAR N |
| CAT/NCOS | Customer Access Treatment Code - Identifies the station's ability to access certain calling areas or facilities. The CAT content is common block specific or assigned on a per-Carrier's customer basis. Order Placement: FEATURE DETAIL Field following the line assignable USOC. Example: SXP++/CAT X |
| CFBE | Call Forward Busy External - Indicates the telephone number tha6t calls originating from outside the Centrex should be forwarded to when the Call Forward Busy split feature is ordered. Order Placement: FEATURE DETAIL field following the feature USOC in the FEATURE field. Example: ZB5ES/CFBE 91NPANXXXXXX (if out of Centrex and long distance) |
| CFBI | Call Forward Busy Internal - Indicates the telephone number that calls originating from within the Centrex should be forwarded to when the Call forward Busy split feature is ordered. Order Placement: FEATURE DETAIL field following the feature USOC in the FEATURE field. |
| CFDE | Indicates the telephone number that call originating from outside the Centrex should be forwarded to when the Call Forward No Answer split feature is ordered. Order Placement: FEATURE DETAIL Field following the feature USOC in the FEATURE field. Example: ZD1ES/CFBE 91NPANXXXXXX (if out of Centrex and long distance |
| CFDI | Indicates the telephone number that call originating from within the Centrex should be forwarded to when the Call Forward no Answer split feature is ordered. Order Placement: FEATURE DETAIL field following the feature USOC in the FEATURE field. Example: ZD1ES/CFDI XXXX (forward within the Centrex) |
| CPG | Call Pick Up Group - indicates the Call Pick Up Group this station belongs to. Order Placement: FEATURE DETAIL Field following the feature USOC in the FEATURE field. Example: ZXAPU/CPG## |
| CRX | Call Request Exempt - DMS100 only Indicates whether the station line designated is or is not exempt from receiving Message Waiting signals from another station within the Centrex group. Order Placement: FEATURE DETAIL field following the Feature USOC in the FEATURE Field. Example: ZMYAD/CAR N/CRX N |
| CSR | Customer (End User) Station Rearrangement - Indicates that ServiceMate is present on the account. it is floated behind the SXP++ and any feature that has to be retained on the Service Record. Order Placement: FEATURE DETAIL Field following the line assignable USOC. Example: SXP++/CSR |
| CTX | Telecommunication Carrier's Customer Group Identifier - The Centrex common block identifies the system parameters such as station number ranges, Call Pick Up range and access codes selected. All new CTS should be 4 digits (plus subgroup number for the DMS100 ie., 0004:0). Order Placement: CB Field |
| DIN | Deny Incoming (DMS100) only - Indicates to deny incoming calls from outside of the Centrex group. Order Placement: Not required. Example: ZDINP/DIN$ |
| DPA | Different Premises Address - Identifies the address of a Centrex off premise extension to another location. Floated behind SXP++ line USOC. Order Placement: FEATURE DETAIL field following the line assignable USOC. Example: SXP++/DPA # |
| DPI | Different Premise Information -Supplemental information concerning Different Premise Address (DPA) installation. - Can only be used with 'DPA' and not on 'SLA' locations. -Does not reflect in 911 database. Order Placement: SADLO on Centrex Order Form Example: SXP++/DPA 1/DPI Term on 701E PBX. |
| DPS | Different Premise Subscriber - Identifies a different end user other than the listed end user at a different location (SLA) than the main listed address. Floated behind SLA information. This field is prohibited with the FID DPA. Allows 911 and Caller ID to pick up the correct end user name. Order Placement: FEATURE DETAIL Field following the line assignable USOC, Example: SXP++/DPS Any Company |
| DSA | Distribution and Supplemental Assignment - Indiana Only M identifies a primary circuit Order Placement: FEATURE DETAIL field following the line assignable USOC in the FEATURE field. Example: SXPAC/TN XXX-XXXX/DSA M |
| KEY | Key Designation - Associated with an electronic set that the feature or telephone number appears on. A button or key number follows Key. Order Placement: FEATURE DETAIL following either the line assignable USOC or features USOC in the FEATURE Field. Example: SXPAC/TN XXX-XXXX/KEY 1 or ZCFV1/KEY 6 |
| LCC | Line Class Code - Defines the station's ability to access or be accessed by the switch exchange network. The LCCs are normally standard per switch and are not customer specific. See Line Class Codes for particular codes to be used. |
| MADN | Multiple Appearance Directory Number - The MADN FID has three elements that indicate the call arrangement associated with a DMS100 Multiple Appearance Directory Number feature. Data following this FID consists of three elements which are separated by spaces. MADN Call Arrangement Indicator: S - Single Call Arrangement M - Multiple Call Arrangement MADN Primary/Secondary Appearance Indicator: P - Primary Appearance N – Non-Primary Appearance Ringing Indicator: R - Ring NR - No Ring Order Placement: FEATURE DETAIL field following the line assignable USOC in the FEATURE field. Example: SXPAC/TN XXX-XXXX/MADN S P R. Note: The primary MADN location or primary MADN member must be replaced when the existing primary MADN number is removed. When all secondary MADN members are removed from the group, the status of the primary member must also be removed. |
| NOL F | Number of Lines (Michigan only)* |
|  | If # of lines Guaranteed is | Then NOL G* is | And NOL F* is |
|  | 2-6 stations | 02 | 02 |
|  | 7-24 stations | 07 | 06 |
|  | 25-49 stations | 25 | 20 |
|  | 50-99 stations | 50 | 40 |
|  | 100-199 stations | 100 | 80 |
|  | 200-499 stations | 200 | 160 |
|  | 500+ stations | 500 | 400 |
| NOL G | Number of Lines Guaranteed - Indicates the number of lines the customer is required to keep in service. Order Placement: VTA Field on the LSR, Fourth segment. Example: VTA 36/VT7/02292001/7 |
| PN | Primary Number - Indicates the primary indicator or number of a multiple directory number arrangement. Order Placement: FEATURE DETAIL Field following the line assignable USOC in the FEATURE field. Example: SCPAC/TN XXX-XXXX/PN XXX-XXXX |
| PN + SET | Set is required with PN when a primary number on one set is repeated as “ON’ on one or more additional telephone sets. A number follows SET. Order Placement: FEATURE DETAIL FIELD following the line assignable USOC in the FEATURE field. Example: SXPAC/TN XXX-XXXX/PN XXX-XXXX/SET 2 |
| RIE | Rate Included Elsewhere - Indicates that the normal monthly charge should not be billed. Order Placement: FEATURE DETAIL field following the FEATURE Field. Example: ZDCPK/RIE |
| RCYC | Ring Cycle - Indicates after how many rings the call should be forward to the pre-selected number. The default is 3 ring cycles. Order Placement: FEATURE DETAIL field following the feature in the FEATURE field Example: ZCFDA/ZTN XXXX/RCYC 5 |
| SCG | Speed Call Group /number - Indicates to which speed call group this Centrex station has access. Order Placement: FEATURE DETAIL Field following the feature in the FEATURE field. Example: ASC50/SCG## |
| SLA | Secondary Location Address - Identifies the address of each Centrex location. Floated behind SXP++ (line USOC). Order Placement: FEATURE DETAIL Field following the line assignable USOC. Example: SXP++/SLA # |
| WLN | Warm Line Service Number - Indicates the telephone number which is automatically called by the DMS100 switch at the expiration of a predetermined time interval when the originating end user goes off hook. Order Placement: FEATURE DETAIL Field following the feature USOC in the FEATURE Field. Example: ZXAWL/WLN NXX-XXXX |
| WLT | Warm Line Transfer - Indicates the number of seconds that must elapse before the DMS100 switch sets up the connection for a warm line service number. Order Placement: FEATURE DETAIL following the feature USOC in the FEATURE field. Example: ZXAWL/WLN NXX-XXXX/WLT XX |
| ZTN | Feature Related Telephone Number - Identifies the station's dialing pattern when associated with Call Forwarding features: Forwarding Inside the Centrex - When call forwarding station, station within a Centrex, the forward to number must be written to reflect the intercom dialing pattern (ie., 3, 4 or 5 digits) Exception: 1AESS, all 7 digits of the forward to number must be provided. Forwarding Outside the Centrex - When call forwarding outside the Centrex, the forward to number would include the Dial Access Code (DAC, Dial 1, NPA (if applicable) and the seven digit telephone number). Exception: 1AESS, do not show the DAC of 9, 8, etc. However, the 1 is required when forwarding outside the NPA. Order Placement: FEATURE DETAIL Field following the Feature USOC in the FEATURE field. Example: (Within the Centrex) ZCFBA/ZTN #### Example: (Outside of the Centrex) ZCFBA/ZTN 91NPANXXXXXX |

Line Class Codes (LCC)

The Line Class Code is based on the type of EKL set being as follows:

| Business Set | LCC |
| --- | --- |
| M5008 | M5008 |
| M5009 | M5009 |
| M5112 Handsfree Unit | M5112 |
| M5208 Display | M5208 |
| M5209 Display | M5209 |
| M5216 Display and Handsfree Capability | M5216 |
| M5312 Display and Handsfree Unit | M5312 |
| M5316 Display and Handsfree Unit | M5316 |
| PSET | PSET |

Note:  A NCOS must be provided in addition to LCC.

Listings

See applicable Centrex document.

Miscellaneous Ordering Procedures

New Centrex Service Orders

- New Centrex Service can only be ordered manually at this time.

- The forms to build a new Centrex Common Block can be obtained by calling the LSC.

Subsequent Centrex Orders

The following details how to show items that do not have specific fields on the new manual LSR.

- To indicate a Transfer of Calls Option, field TC OPT in the Remarks field put /TC OPT _

- To indicate a Jack Request - in the Feature Detail Field following the line assignable USOC enter /JR.

- Centrex class of service must be shown on the LSR form in the 'TOS' field.

- Centrex service requires that the main class of service be a Centrex class of service.

- If a telephone number has not been pre-assigned, a placeholder can be used in the 'TNS' when establishing new service.

- 'PIC' and 'LPIC' are required on all orders.

- Centrex service is ordered on a REQ TYP 'P'.

- The 'line assignable' USOC should be shown first in the FEATURE field on the product form.

- Centrex station numbers cannot be reserved through the pre-order system.

- In addition to the Centrex Service Request Form, the Electronic Key Line Order Form is also required when ordering this product.

- If the Centrex order is being submitted electronically, either through EDI or LEX, then fax the Electronic key line Order form to the LSC using the same PON.

The Electronic Key Line Order form can be found in Forms & Exhibits-Complex/POTS Administrative Forms.

Minimum Billing/Termination

Minimum billing and termination charges are based on the Centrex contract.