Fractional DS1 Service

Description	3

Wisconsin Tariff Rate Re-Structure	3

Indiana Tariff Rate Re-Structure	3

Illinois Tariff Rate Re-Structure	4

Aliases	4

Features	4

Local Distribution Channel	5

Channel Mileage and Channel Mileage Termination	5

Availability	5

Illinois	6

Michigan	6

Ohio	7

Indiana	7

Wisconsin	7

Restrictions/Limitations	7

Interactions	8

Required Common Products	8

Pre-Ordering	8

Ordering	8

Service Order Requirements –All States	8

Due Dates	9

Class of Service	9

Illinois, Indiana and Ohio	9

Michigan	9

Wisconsin	9

USOCs	10

Illinois	10

Rate Application Rules	10

Determining the Access Area	10

Same Access Area	10

Different Access Area	11

Indiana	11

Rate Zones	11

Determining the Rate Zone	11

Michigan, Ohio and Wisconsin	11

Determining the Rate Zone	12

Rate Zones for Michigan	12

Rate Zones for Ohio	13

Rate Zones for Wisconsin	13

FIDs	13

CFA	13

CLCI	14

NC/NCI	14

Network Channel (NC) Codes	14

Network Channel Interface (NCI) Codes	14

Premises-to Premises/Riding DS1	15

Miscellaneous Ordering Procedures	15

Billing	15

Illinois - As of 7/19/99	15

Recurring Charges	15

Nonrecurring Charges	15

Indiana	16

Recurring Charges	16

Nonrecurring Charges	16

Michigan	17

Recurring Charges	17

Nonrecurring Charges	17

Ohio	17

Recurring Charges	17

Nonrecurring Charges	17

Wisconsin	17

Recurring Charges	17

Nonrecurring Charges	18

Payment Options/Contracts	18

Michigan Only	18

All States	18

Conversion of Services to New VTPP or Higher Speed	18

Moves	19

Minimum Billing/Termination	19

Single Bill/Multiple Tariffs in Ohio	19

# Description

- Two-point private line services that provide bulk transport facilities at transmission speeds of 128, 256, and 384 Kbps.

- These services provide full duplex (simultaneous two-way) transmission of serial, asynchronous digital signals.

- Fractional DS1 service is always provisioned with clear channel capability.

Wisconsin Tariff Rate Re-Structure

Effective March 13, 2000, Wisconsin DS1 and Fractional DS1 rate structure will become standardized under the same structure used in Michigan and Ohio. This will impact not only DS1 and Fractional DS1 but ISDN Prime, ISDN Centrex, ADTS-E and ADTS.

The changes include the following:

- Establish 'Co-Mingling' for Fractional DS1 on a DS1.

- Establish Shared Network Arrangement

- Establish three geographic rate zones for all USOC's

- Establish a new DS1 Class of Service

- Eliminate Volume discounts.

- Eliminate plug-in rate elements and USOC's.

Indiana Tariff Rate Re-Structure

Effective November 15,1999, the Indiana Tariff standardization of DS1, Fractional DS1 and C.O. Multiplexing will Grandfather existing end users and put a new structure in place. This change also impacts ISDN Prime and ADTS-E on the DS1 portion of these services.

This will apply to all existing DS1 customers both Month-to-Month and Term Payment Plan.

- All circuits can convert to the new structure.

- Circuits under an existing TPP must sign a new TPP with the same or greater number of months remaining on the old TPP.

  - Grandfathered circuits with an 84 or 120 month TPP with 60 months or more remaining can convert to the new structure with a 60 month TPP as 84 and 120 month contract lengths have been eliminated.

  - When a Grandfathered TPP expires, the circuit will automatically convert to the Grandfathered Month-to-Month rate.

- Physical changes, moves or rearrangements will not be allowed on the Grandfathered service. End users will be required to convert to the new structure before making any physical changes on the existing service.

- New orders under the Grandfathered structure will not be allowed.

- A 'sunset date' which has yet to be determined, will be appointed. At that time any remaining circuits under the Grandfathered structure will have to be converted to the new structure and the Grandfathered structure will be removed from the tariff and billing systems by this date.

## Illinois Tariff Rate Re-Structure

- The Illinois tariff rate re-structure was effective 7/19/99.

- There will be a direct affect on several products as they relate to DS1 service:

  - Base Rate

  - Enhanced ADTS-E

  - ISDN Prime

  - OPTI-Centrex

  - Fiber Hub Cross-Connect (DS1 & DS3)

  - Multiplexer Cross-Connect (DS1 & DS3)

  - Hub Rearrangement (DS1 & DS3)

- The Illinois DS1 changes will establish Access Area pricing for Channel Mileage, Channel Mileage Termination, Central Office Multiplexing, Fiber Hub Cross-Connect and Non-Recurring charges. The Central Office Multiplexer Plug-In USOCs of PUG1X and PUG3X will be eliminated, as well as, the MX6 charge for Common Equipment. The only rate change will be the Central Office Multiplexing rate which will increase due to the elimination of the plug-in charges.

- Multiplexer Cross-Connect and Hub Rearrangement (for DS1 and DS3) will become available in Illinois for the first time.

## Aliases

- Fractional T1

- 128, 256, and 384 Transport Service(s)

## Features

- Fractional DS1 Service is a dedicated digital service that can be ordered as a two-point, non-channelized service between two end user designated premises, or that rides an DS1 with multiplexing in Michigan and Ohio.

- Fractional DS1 may be ordered to ride a channelized or multiplexed DS3. (No monthly rate or NRC applies to clear channel capability when provided with Fractional DS1 Service.

- Fractional DS1 Service can only ride a DS1 that is multiplexed in an office that is DCS 1/0 equipped, and must be assigned to consecutive channels of the DS1.

- Local Distribution Channel (LDC) rate element applies to each end of the circuit terminated at a customer-designated premise.

- The interoffice transport portion consists of the Channel Mileage and Channel Mileage Termination rate elements, which are priced at a lower rate than DS1.

- Clear Channel Capability (CLR) using the Binary Eight Zero Substitution (B8ZS) line code protocol, is required. Framing options include Superframe (SF) or Extended Superframe (ESF). Clear Channel is provided at no extra charge.

- Special Facilities Routing is available on Fractional DS1 circuits. The following types are available:

  - Local Channel Diversity

  - Inter-Wire Center Diversity (IWC)

  - Serving Wire Center (SWC) Avoidance

### Local Distribution Channel

The Local Distribution Channel (LDC) provides for the communication path between a customer's designated premises and the serving wire center for that premises.

### Channel Mileage and Channel Mileage Termination

- Channel Mileage (CM) provides the transmission facilities between:

  - The Serving Wire Center (SWC) associated with two customer premises.

  - A SWC associated with a customer's designated premises and a fiber hub.

  - A SWC associated with a customer's designated premises and a multiplexing serving office.

- Channel Mileage is calculated using Vertical and Horizontal (V&H) coordinates based on the airline distance between the two locations involved.

- The Channel Mileage Termination (CMT) provides for the termination of Channel Mileage (CM).

- There are two (2) Channel Mileage Terminations for each mileage calculation (one at each end).

- There is no CMT if there is no mileage.

# Availability

Fractional DS1 is available in a two-point configuration between:

- Two end user premises

- An end user premises and a central office for cross-connection or hubbing (co-mingling).

- End users premises and a central office for termination in an DS3 to DS1/128, 256, or 384 Central Office (C.O.) multiplexer, Automatic Route Selection (ARS) system, or for connection to Optical Interconnection Service.

- Two COs when connecting two ARS systems via Channel Mileage and Channel Mileage terminations to interconnect channels included in the end user's database for the ARS.

- Fractional DS1 can only be provided from COs equipped for appropriate digital transmission. (Since not all COs are presently equipped to furnish Fractional DS1 services, a service inquiry must be made to determine availability of service.

In order to furnish new Fractional DS1 service, the CO switch must have 1/0 Digital Cross Connect Capability.

## Illinois

Central Offices Equipped Digital Cross-Connect Equipment*

| AURRILARK18 | BLVLILADK01 | CHCGILIDK74 | CHCGILWBK53 |
| --- | --- | --- | --- |
| CHHGILCHK36 | CHMPILCPK48 | CHMPILCPK60 | COVLILCQK50 |
| DAVLILDAK65 | DAVLILDAK66 | DCTRILDCK01 | DCTRILDNK67 |
| DCTRILDNK68 | DRFDILDFK54 | DRFDILDFK55 | ELGNILELK56 |
| ELGNILELK57 | EWVLILERK69 | EWVLILERK70 | JOLTILJWK01 |
| KNKKILKKK24 | LVVLILLIK25 | MRRSILMSK27 | PEORILPBK71 |
| PEORILPBK72 | PEORILPJK51 | QNCYILQYK01 | RCFRILRTK01 |
| RCISILRIK02 | RMVLILRMK01 | RVDLILRDK58 | RVDLILRDK59 |
| SPFDILSWK61 | SFDILSWK62 | STNGILSIK01 | WDSTILWSK31 |

* This list is subject to change.

## Michigan

In order for a 128, 256, or 384 Kbps circuit to 'ride' a channelized DS1, the DS1 must be multiplexed in one of the following appropriately equipped COs:

DCS 1/0 Offices*

| BNHRMIMNK01 | BTCKMIMNK01 | BYCYMIWSK01 | CDLCMIMNK01 |
| --- | --- | --- | --- |
| DRBRMIDBK01 | DRBRMIOR01 | DTRTMIMDK01 | DTRTMIPGK01 |
| DTRTMIRFK01 | DTRTMIRVK01 | ESCNMIMNK01 | GDRPMIBLK03 |
| GDRPMIESK01 | GRHVMIMNK01 | HLLDMIMNK01 | HNCCMIMNK01 |
| IRMTMIMNK01 | JCSNMIMNK01 | JCSNMIMNK02 | KLMZMIFAK02 |
| LIVNMIMNK01 | LNNGMIMNK02 | MDLDMIMNK01 | MDLDMIMNK02 |
| MONRMIMNK01 | MRQTMIMNK01 | MTCLMIMNK01 | MTCLMINRK01 |
| NHRVLMIMNK01 | PNTCMIMNK01 | PNTCMINEK01 | PTHRMIMNK01 |
| PTSKMIMNK01 | RMLSMIMNK01 | ROMOMIMNK01 | RYLOMIMNK01 |
| SFLDMIOKK01 | SGNWMIFAK02 | SSMRMIMNK01 | TAYLMIWKK01 |
| TRENMIMNK01 | TROYMIMNK01 | TROYMISMK01 | UTICMIMNK01 |
| WAYNMIMNHK02 | WRRNMIMNK01 | YPSLMIMNK01 | ZELDMIZLK01 |

* This list is subject to change.

## Ohio

In order for a 128, 256, or 384 Kbps circuit to 'ride' a channelized DS1, the DS1 must be multiplexed in one of the following appropriately equipped COs:

DCS 1/0 Offices*

| AKRNOH25K01 | AKRNOH78K01 | AKRNOH78K02 | BCWDOH46K03 |
| --- | --- | --- | --- |
| BKPKOH26K02 | CLEVOH62K03 | CLEVOH64K03 | CLMBOH11K07 |
| CNTNOH45K01 | DYTNOH22K04 | DYTNOH23K01 | DYTNOH23K02 |
| FNDYOH42K01 | INDPOH52K02 | LNCSOH65K02 | MDTWOH42K01 |
| SCVIOH69K01 | TOLDOH21K04 | TOLDOH38K01 | TOLDOH38K02 |
| WOTNOH88K01 | WOTNOH88K04 | XENIOH37K01 | YNTWOH74K01 |
| YNTWOH74K02 | YNTWOH78K01 | WNTWOH78K02 | ZNVLOH45K01 |

* This list is subject to change.

## Indiana

| ARSNIN01K01 | AUBNIN01K01 | BLTNIN01K02 | BLTNIN01K03 |
| --- | --- | --- | --- |
| CFVLIN01K01 | CLMBIN01K01 | CLMBIN01K02 | CRMLIN01K01 |
| CRPNINCXK01 | EVVLIN03K02 | EVVLIN03K03 | FSHRIN01K01 |
| FSHRIN01K02 | FSHRIN01K03 | GARYING0K02 | GNWDIN01K01 |
| HNTNIN01K01 | IPLSIN04K02 | IPLSIN07K01 | IPLSIN08K02 |
| IPLSIN08K03 | IPLSIN10K01 | IPLSIN21K01 | KOKMIN01K02 |
| MARNIN03K01 | MCCTIN01K01 | MCCTIN01K02 | MUNCIN01K01 |
| NWALIN01K01 | SBNDIN04K01 | SBNDIN04K02 | VINCIN01K01 |

## Wisconsin

| APPLI01K02 | EUCLWI01K02 | GNBYWI01K02 | GNBYWI11K01 |
| --- | --- | --- | --- |
| JNVLWI01K01 | MDSNWI11K02 | MDSNWI4K01 | MDSNWI14K02 |
| MILWWI16K01 | MILWWI45K01 | MILWWI45K02 | MILWWI48K02 |
| MNMNWI11K01 | MNMNWI11K02 | RACNWI01K02 | STPTWI01K01 |

## Restrictions/Limitations

- Temporary suspension of service is not provided for Fractional DS1.

- Current technology restricts the usable bandwidth the end user receives by blocking an appropriate number of the 24 DS1 channels available on a DS1 (see list below)

- The network interface is a standard 1.544 Mbps DS1 interface, but the usable portion of the bandwidth is limited according to the speed requested by the customer. (Accomplished through a transceiver card in the repeater bay.)

- Bandwidth is limited on an existing DS1, thus the customer is not allowed to channelize the service to a DS0 (voice grade) level.

  - 128 Kbps occupies two channels (2 X 64 - 128); 22 channels blocked

  - 256 Kbps occupies four channels (4 X 64 = 256); 20 channels blocked

  - 384 Kbps occupies six channels (6 X 64 = 384); 18 channels blocked

The following offerings are not available with Fractional DS1:

| State | Offering |
| --- | --- |
| All States | Fiber Hub Cross-Connection Multiplexer Cross-Connection Line Power CSUs |
| Michigan | Term Payment Plan (TPP) on Channel Mileage and Channel Mileage Termination Charges |
| Ohio | Variable Term Payment (VTPP) on Channel Mileage or Channel Mileage Termination Charges |

### Interactions

Fractional DS1 circuits can ride a regular multiplexed DS1 circuits in some offices. This is called co-mingling. A digital cross-connect machine must be available in the central office and a spare DS1 port within the equipment must be available. Both the DS1 and the Fractional DS1 must terminate in the same digital cross-connect machine. It is necessary for the DS1 to be provisioned with Clear Channel but the timing does not necessarily have to match.

### Required Common Products

Clear Channel Capability

# Pre-Ordering

SBC mechanized pre-ordering Operational Support System (OSS) is available to assist the CLECs on obtaining pre-ordering information. However, certain orders require a manual pre-ordering transaction before an LSR can be submitted successfully. The manual pre-ordering process is described in detail under the Pre-Ordering section of this handbook.

When performing a manual pre-ordering transaction, fill in the LSR request as completely as possible using EDI/WebLEX. When the needed manual pre-ordering information is filled out, save the LSR request. Print a copy of the request and fax it to SBC along with the Manual Pre-Ordering Information Cover Sheet. SBC will fax back the needed pre-ordering information so the CLEC can successfully submit a firm LSR.

# Ordering

## Service Order Requirements –All States

The following information is required on Fractional DS1 Service Orders:

- Carrier Facility Assignment (CFA) if riding a DS1

- Common Language Location Codes (CLLI)

- NC/NCI Codes

- Secondary Class of Service (STOS)

- Payment Plan information - see Payment Options/Contracts and Forms.

- Format is required for Fractional DS1 circuits

Note: Fractional DS1 circuits are always provisioned with Clear Channel

## Due Dates

Refer to the Resale Due Date matrix for standard due date intervals.

## Class of Service

### Illinois, Indiana and Ohio

| Secondary Class of Service Code | Description |
| --- | --- |
| XDHSN | 128 Kbps |
| XDHRN | 256 Kbps |
| XDHEN | 384 Kbps |

### Michigan

| Secondary Class of Service Code | Description |
| --- | --- |
| XDHS+ | 128 Kbps |
| XDHR+ | 256 Kbps |
| XDHE+ | 384 Kbps |

Note: + L= Intraexchange/Intra Wire Center, S=Interexchange/Inter Wire Center;

1 = Intraexchange/Inter Wire Center; X = Interstate

### Wisconsin

| Secondary Class of Service Code | Description |
| --- | --- |
| XDHS+ | 128 Kbps |
| XDHR+ | 256 Kbps |
| XDHE+ | 384 Kbps |

Note: + L= Intraexchange/Intra Wire Center, S=Interexchange/Inter Wire Center

## USOCs

### Illinois

The following USOCs must be used when provisioning Fractional DS1 in Illinois, beginning 7/19/99:

| Description | USOC |
| --- | --- |
| Channel Mileage, per mile, Access Area A, B, or C | 1YZX+ |
| Channel Mileage Termination, per end, Access Area A, B, or C | CZ4X+ |
| Local Distribution Channel, per point of termination, Access Area A, B or C | FQA1+ |
| (+) equals A, B or C depending on Access Area |

#### Rate Application Rules

The following chart may be used to assist in determining the correct Access Area or all USOCs associated with DS1 circuits when there is more than one Access Area involved:

| USOC | Rate Element | Access Area |
| --- | --- | --- |
| FQA1+ | Local Distribution Channel | Per CKL LSO |
| 1YZX+ | Channel Mileage | Per CKL in highest Access Area |
| CZ4X+ | Channel Mileage Termination | Per CKL in highest Access Area |
| CLYYX+ | Clear Channel | Per CKL in highest Access Area |
| NRBA+* | Administrative Charge | Per CKL in highest Access Area |
| NRBB+* | Customer Connection Charge | Per CKL LSO |
| NRBD+* | Design and CO Connection Charge | Per CKL in highest Access Area |

* is 1, 2 or 3 depending on the Access Area.

#### Determining the Access Area

##### Same Access Area

If a circuit terminates in the same Access Area, the entire circuit is rated per that Access Area.

Example: A Premise to Premise T-1 with both CKLs in Access Area A is rated as follows:

| USOC | Description | Access Area |
| --- | --- | --- |
| FQA1A | CKL 1 LDC | A |
| CZ4XA | Channel Mileage Termination | A |
| 1YZXA | Channel Mileage | A |
| FQA1A | CKL 2 LDC | A |

##### Different Access Area

If a circuit has two LDC's, each in a different Access Area, the appropriate LDC USOC will be used to indicate the different Access Areas. The Channel Mileage and Channel Mileage Terminations will take on the higher of the two Access Areas.

Example: A premise to premise DS1 with CKL 1 in Access Area A and CKL 2 in Access Area B would be rated as follows:

| USOC | Description | Access Area |
| --- | --- | --- |
| FQA1A | CKL 1 LDC | A |
| CZ4XB | Channel Mileage Termination | B |
| 1YZXB | Channel Mileage | B |
| FQA1B | CKL 2 LDC | B |

### Indiana

| Description | USOC |
| --- | --- |
| Local Distribution Channel, per end, Rate Zone 1 or 3 | TZ4X+ |
| Channel Mileage, per circuit, Rate Zone 1 or 3 | 1YZX+ |
| Channel Mileage Termination, per circuit, Rate Zone 1 or 3 | CZ4X+ |
| (+) will be 1 or 3 depending on the Rate Zone. There is NO Rate Zone 2 in Indiana. |

#### Rate Zones

| Rate Zone 1 | Rate Zone 2 | Rate Zone 3 |
| --- | --- | --- |
| IPLSIN01 | N/A | All other COs that are not listed under Rate Zone 1 or 2 and all independent telephone companies |

##### Determining the Rate Zone

| Same Rate Zone | Multiple Rate Zones |
| --- | --- |
| If a circuit terminates within a single rate zone, the entire circuit is rated per that zone. | If a circuit has two LDCs, each in a different rate zone, the appropriate LDC USOC will be used to indicate the different rate zones. The channel mileage and channel mileage terminations will take on the higher of the two rate zones. |

### Michigan, Ohio and Wisconsin

| Description | USOC |
| --- | --- |
| DS1/128, 256, and 384 Local Distribution Channel (LDC) | TZ4X+ |
| Channel Mileage Termination | CZ4X+ |
| Channel Mileage | 1YZX+ |

Note: + =

1 = Zone 1
2 = Zone 2
3 = Zone 3

#### Determining the Rate Zone

| Same Rate Zone | Multiple Rate Zones |
| --- | --- |
| If a circuit terminates within a single rate zone, the entire circuit is rated per that zone. | If a circuit has two LDCs, each in a different rate zone, the appropriate LDC USOC will be used to indicate the different rate zones. The channel mileage and channel mileage terminations will take on the higher of the two rate zones. |

##### Rate Zones for Michigan

| Rate Zone 1 | Rate Zone 2 | Rate Zone 3 |
| --- | --- | --- |
| DTRTMIBL DTRTNIRV | ABHLMIBH BLVLMINE BRHMMIMN DRBRMIDB DRBRMIFB DRBRMIOR DTRTMICL DTRTMILX DTRTMIMD DTRTMIPE DTRTMIPG DTRTMIRF DTRTMITE DTRTMITW STRTMIUV DTRTMIVT DTRTMIVW FMHLMIFH GDRPMIBL HGPKMITS LNNGMIMN PNTCMIMN RYLOMIMN SFLDMIMN SFLDMIOK TROYMIMN TROYMISM WBFDMIMN WRRNMITL | All other central offices that are not listed under Zones 1 or 2 and all independent telephone company offices |

##### Rate Zones for Ohio

| Rate Zone 1 | Rate Zone 2 | Rate Zone 3 |
| --- | --- | --- |
| AKRNOH25 CLEVOH62 CLMB0H11 DYTNOH22 | BCWDOH46 BKPKOH26 BKPKOH97 CLEVOH25 CLEVOH42 CLEVOH43 CLEVOH45 CLEVOH53 CLEVOH63 CLEVOH64 CLEVOH74 CLHGOH32 CLMBOH27 CLMBOH29 DYTNOH25 LKWDOH52 MPHGOH66 SHHGOH92 TOLDOH21 WOTNOH88 | All other central offices that are not listed under Zones 1 or 2 and all independent telephone company offices |

##### Rate Zones for Wisconsin

| Rate Zone 1 | Rate Zone 2 | Rate Zone 3 |
| --- | --- | --- |
| MILWWI13 | MMILWWI17 MMILWWI22 MMILWWI23 MMILWWI27 MMILWWI34 MMILWWI38 MMILWWI42 MMILWWI48 MDSNWI11 MDSNWI15 | All other COs that are not listed under Zones 1 or 2 and all independent telephone companies. |

## FIDs

### CFA

- Fractional DS1 circuits riding a DS1 must have a Connecting Facility Assignment (CFA) equaling the number of channels required for that circuit:

  - 128 Kbps requires two channels of a DS1

  - 256 Kbps requires four channels of a DS1

  - 384 Kbps requires six channels of a DS1

- Channels assigned may be any of the 24 available DS1 channels, but must be consecutive.

For example: 128 circuit riding channels four and five of a DS1 would have CFA shown on the order as follows:
/CFA 101 T1Z 4-5 CLLI CODE A, CLLI CODE Z

- Other services may also ride the DS1 if available channels exist.

### CLCI

All States:  Fractional DS1 Service is identified with the following CLCI (Common Language Circuit Identification) format.

| Svc Code | Modifiers No. | Serial ID | Company |
| --- | --- | --- | --- |
| .XX | XX. | ######. | .XX |
| .FL | ZC. | ######. | LB = Illinois NB = Indiana MB = Michigan OB = Ohio WT = Wisconsin |

## NC/NCI

### Network Channel (NC) Codes

NC Codes specify the characteristics of the basic channel and their options. A unique code is designated for each of the Fractional DS1 Services.

| Network Channel Code | Description |
| --- | --- |
| HXZB | 128 Kbps |
| HXZD | 256 Kbps |
| HXZF | 384 Kbps |

- HX represents all Fractional DS1 services.

- Z represents Clear Channel Capability (CCC). Since CCC is the standard format on Fractional DS1 Service, it is not considered an additional feature and is provided at no additional cost to the customer.

- B, D, and F represent the bandwidth:

  - B, if two channels for 128 transport

  - D, if four channels for 256 transport

  - F, if six channels for 383 transport

### Network Channel Interface (NCI) Codes

NCI codes define the electrical parameters of the interface or connection of a circuit  between SBC facilities and the circuit's terminating equipment.

#### Premises-to Premises/Riding DS1

| Circuit Type | Signaling | NCI for CKL1 | NCI for CKL2 |
| --- | --- | --- | --- |
| Premises to Premises | SF & CCC* | 04DU9.DN | 04DU9.DN |
| Premises to Premises | ESF (ANSI) & CCC* | 04DU9.1SN | 04DU9.1SN |
| Premises to Premises | ESF (Non ANSI) & CCC* | 04DU9.SN | 04DU9.SN |
| Riding a DS1 | ESF (NON-ANSI) & CCC* | 04DU9.SN | 04DU9.SN |

Note: * Clear Channel is required on all fractional DS1 circuits

## Miscellaneous Ordering Procedures

- All mileage USOCs should be shown in the FA, FEATURE and FEATURE DETAIL fields for the primary location.

- LDC (Local Distribution Channel) USOCs should be shown under the appropriate circuit leg in the FA, FEATURE and FEATURE DETAIL fields.

# Billing

Fractional DS1 circuits may be billed on either a miscellaneous bill or an end user's telephone number account.. Charges will be assessed if order is placed by Carrier non-electronically.

## Illinois - As of 7/19/99

### Recurring Charges

| Description | USOC |
| --- | --- |
| Channel Mileage, per mile, Access Area A | 1YZXA |
| Channel Mileage, per mile, Access Area B | 1YZXB |
| Channel Mileage, per mile, Access Area C | 1YZXC |
| Channel Mileage Termination, per end, Access Area A | CZ4XA |
| Channel Mileage Termination, per end, Access Area B | CZ4XB |
| Channel Mileage Termination, per end, Access Area C | CZ4XC |
| Local Distribution Channel, per point of termination, Access Area A | FQA1A |
| Local Distribution Channel, per point of termination, Access Area B | FQA1B |
| Local Distribution Channel, per point of termination, Access Area C | FQA1C |

### Nonrecurring Charges

The following are the nonrecurring charges that must be used when provisioning Fractional DS1 in Illinois as of 7/19/99:

| Description | USOC |
| --- | --- |
| Establish a Premises-to-Premises Circuit or a Premises-to-CO Circuit, bill the following: |  |
| Administrative Charge - per request, Access Area A | NRBA1 |
| Administrative Charge - per request, Access Area B | NRBA2 |
| Administrative Charge - per request, Access Area C | NRBA3 |
| Design CO Connection Charge - per circuit, Access Area A | NRBDA |
| Design CO Connection Charge - per circuit, Access Area B | NRBDB |
| Design CO Connection Charge - per circuit, Access Area C | NRBDC |
| Customer Connection Charge - per customer termination, Access Area A | NRBBA |
| Customer Connection Charge - per customer termination, Access Area B | NRBBB |
| Customer Connection Charge - per customer termination, Access Area C | NRBBC |
| Shared Network Arrangement, Access Area A | SNRXA |
| Shared Network Arrangement, Access Area B | SNRXB |
| Shared Network Arrangement, Access Area C | SNRXC |

Change location charges are not applicable. If either end changes, new installation charges apply.

## Indiana

### Recurring Charges

| Description | USOC |
| --- | --- |
| Channel Mileage, per mile | 1YZX+ |
| Channel Mileage Termination, per point of termination | CZ4X+ |
| Local Distribution Channel, per point of termination | TZ4X+ |
| (+) will be either a 1 or 3 depending on the Rate Zone. |

### Nonrecurring Charges

| Description | USOC |
| --- | --- |
| Administrative Charge, per order | NRBA+ |
| Design & Central Office Connection Charge, per circuit | NRBD+ |
| End User Connection Charge, per termination | NRBB+ |
| Shared Network Arrangement, per service order | SRNX+ |
| (+) will be either a 1 or 3 depending on the Rate Zone |

## Michigan

### Recurring Charges

| Description | USOC |
| --- | --- |
| Local Distribution Channel | TZ4X+ |
| Mileage | 1YZX+ |
| Mileage Termination | CZ4X+ |
| (+) will be either a 1, 2 or 3 depending on the Rate Zone |

### Nonrecurring Charges

| Description | USOC |
| --- | --- |
| Administrative Charge, per order | NRBA+ |
| Design & Central Office Connection Charge, per circuit | NRBD+ |
| End User Connection Charge, per termination | NRBB+ |
| (+) will be either a 1 or 3 depending on the Rate Zone |

## Ohio

### Recurring Charges

| Description | USOC |
| --- | --- |
| LDC | TZ4X+ |
| Mileage | 1YZX+ |
| Mileage Termination | CZ4X+ |
| (+) will be either a 1, 2 or 3 depending on the Rate Zone |

### Nonrecurring Charges

| Description | USOC |
| --- | --- |
| Administrative Charge, per order | NRBA+ |
| Design & Central Office Connection Charge, per circuit | NRBD+ |
| End User Connection Charge, per termination | NRBB+ |
| (+) will be either a 1 or 3 depending on the Rate Zone |

## Wisconsin

### Recurring Charges

| Description | USOC |
| --- | --- |
| Local Distribution Channel, Rate Zone 1, 2 or 3 | TZ4X+ |
| Channel Mileage, Rate Zone 1, 2 or 3 | 1YZX+ |
| Channel Mileage Termination, per end, Rate Zone 1, 2 or 3 | CZ4X+ |
| (+) will be either a 1, 2 or 3 depending on the Rate Zone |

### Nonrecurring Charges

| Description | USOC |
| --- | --- |
| Administrative Charge, per order, Rate Zone 1, 2 or 3 | NRBA+ |
| Design and CO Connection Charge, per end, Rate Zone 1, 2 or 3 | NRBD+ |
| End User Connection Charge, per end, Rate Zone 1, 2 or 3 | NRBB+ |
| Shared Network Arrangement processing charge, per order, Rate Zone 1, 2 or 3 | SRNX+ |
| (+) will be either a 1, 2 or 3 depending on the Rate Zone |

## Payment Options/Contracts

### Michigan Only

The Discount Commitment Plan was grandfathered as of 10/21/96.

### All States

- Fractional DS1 is offered under the VTPP. This plan offers fixed rate contracts of 12, 36 and 60 months, as well as month-to-month rates.

- All conditions and regulations pertaining to the VTPP are addressed in Section Two of the Exchange and Network Services Tariff (ENST). Exceptions, as they apply to Fractional DS1 Service, are included in the Private Line Services Tariff (PLST).

- Normal order entries for VTPP apply. Choices are:

  - SPP VT3: Month-to-Month Contract

  - SPP VT1: 12, 36, 60 Month Contract

  - SPP VT1: Single Payment Option

## Conversion of Services to New VTPP or Higher Speed

- During an end user’s VTPP term, conversion may be made to a new VTPP term of the same or different length or to a higher speed service.

- If the expiration date for the new service or VTPP term is beyond the end of the original VTPP term, the remaining VTPP charges for the original term will apply.

- If no physical changes are made to the service, the Administrative Charge, the design and C.O. Connection Charge, and the Customer Connection Charge will not apply.

### Moves

During a VTPP term, an end user may move one LDC to another location in the same LATA, while keeping the VTPP in force, provided no lapse in service occurs.

## Minimum Billing/Termination

See Term Payment Plan

## Single Bill/Multiple Tariffs in Ohio

When issuing orders for Fractional DS1 Service involved with an Independent Telephone Company, keep the following in mind:

- The SBC contract, if there is one, does not involve the Independent Telephone Company’s rates.

- There is no guarantee on the future rates of the Independent Telephone Company end of the circuit. The Independent Company involved can raise their rates or have tariff changes that will be passed on to the CLEC regardless of an SBC contract.

- A note, in the Remarks of the service order request, that a particular leg of the circuit is terminating in an Independent Telephone Company’s territory will facilitate in the provisioning of the order.