OPT-E-MAN

Description	1

Service Configuration	1

Basic	1

Basic Plus	1

Grades of Service	2

Features	2

Standard	2

Optional	2

Availability	2

Restrictions/Limitations	3

Ordering	3

Special Ordering Instructions	3

Billing	3

# Description

OPT-E-MAN service is an optically switched data service which allows businesses to interconnect two or more locations within a Metropolitan Area Network (MAN)

As if they were segments on the same LAN using packet-based switching technologies.  OPT-E-MAN service provides dedicated bandwidth from 5 Mbps up to 1 Gbps.

## Service Configuration

### Basic

Basic service provides the end user a switched, logical point-to-point or point-to-multi-point connection between end user locations using a physical connection to the network and virtual connections through the OPT-E-MAN network.

- A total of 8 EVCs may be configured per 10/100 Base T connection

- A total of 64 EVCs may be configured per 1 Gbps connection

### Basic Plus

Basic Plus provides the end user a switched, logical point-to-point, point-to-multi-point or multi-point to multi-point connection between end user locations using a physical connection to the network and virtual connections through the OPT-E-MAN network.

- A total of 7 EVCs may be configured per 10/100 Base T connection

- A total of 63 EVCs may be configured per 1 Gbps connection

## Grades of Service

Service configurations include a choice of one or two underlying grades of services which offers different level of service performance.

Bronze application is appropriate for general data traffic since it tolerates bursty and time-varying traffic.  Parameters included are Packet Delivery Rate and Latency.

Silver application supports applications that require minimal loss and low latency variation.  Data is provisioned in a priority queue indicating that it is delay sensitive.  Parameters included are Packet Delivery Rate, Latency and Jitter.

## Features

### Standard

- Connection

- Committed Information Rate (CIR)

### Optional

- Repeater

- Ethernet Virtual Connections (EVCs)

- Additional MAC addresses

# Availability

Available in Illinois, Indiana, Michigan, Ohio and Wisconsin in those LATAs served by and within the service territories of SBC only.

- Chicago (LATA 358)

- Indianapolis (LATA 336)

- Detroit (LATA 340)

- Cleveland (LATA 320)

Effective August 25, 2006, service is available in:

Ohio – Akron, Canton, Columbus, Cuyahoga Falls, Dayton, Toledo, Youngstown

Illinois – Champaign, Rockford, Springfield and Urbana

Indiana – South Bend

Michigan – Grand Rapids

## Restrictions/Limitations

- New service installed after November 29, 2006, allows end users to connect any two or more locations together when utilizing a point-to-point or point-to-multipoint configuration,  and a minimum of three or more locations when utilizing a multipoint-to-multipoint configuration as long as they are in the same LATA or MAN and the service is available.

  - The aggregate assigned CIR across all Ethernet Virtual Connections between any two connections cannot exceed 600 mbps per Basic or Basic Plus connection.

  - For point-to-point and point-to-mulitpoint connections, EVCs can be set in 1 Mbps increments from 5 Mbps to 600 Mbps

- Service is provisioned at the option of AT&T where equipment and facilities permit and is available only within the same LATA.

- Customer-provided equipment (CPE) must deliver the data signal for OPT-E-MAN transport within the industry specification for the subscribed data service.

- Service requiring a cross connect in a CO is only available with a 1 Gbps connection.

- OPT-E-MAN does not allow for oversubscription.

- Connection using a bridge or switch for Layer 2 connectivity is limited to only 50 MAC addresses per Layer 2 device per port.

- The CIR selected must be committed to for a 30-day period before an increase can be requested.

- The selected CIR bandwidth usage may not exceed the physical bandwidth/speed of that port.

- Not available in meet-point billing arrangements.

# Ordering

CLEC should contact their account manager before ordering.

Refer to USOC Search Tool for USOC/FID information.

## Special Ordering Instructions

Due to service order processing issues, the CLEC will:
1.  Populate the SVC CD field on the Resale Private Line Form with LX

2.  Populate the correct Service Code Modifier in the Remarks section of the LSR.

Example: L1 or L2

# Billing

Service Level Agreements (SLAs) are available.  Refer to tariff for additional information regarding SLAs, recurring and non-recurring charges.

Term Pricing Plans are available for 1, 2, 3 or 5-year agreements.

- OPT-E-MAN TPP is not available for renewal.

- An existing TPP may be terminated and renegotiated, prior to the existing agreement expiring, only when the new TPP period is longer than the remaining period currently in effect.

- End user must provide AT&T with a written notice of intent to renew TPP no later than 90 days prior to its expiration.

- Agreements cancelled prior to the expiration date will incur termination charges.

- End user may upgrade their CIR to a higher speed without incurring termination charges.

- End user may move their existing service to a new location without incurring termination charges provided certain conditions are met.  Refer to tariff for additional information.

# Footnotes

CLECAM06-162, CLECAM06-168, CLECAM06-290