# Dial 1 Plus

Dial 1 Plus	1

Description	2

Aliases	2

Features	2

Dialing Instructions	2

Calls Originating from Non-Coin Stations	2

1010XXXX+	2

Service Access Codes	2

Cut –Through	3

Directory Assistance	3

Vacant Codes	3

Calls originating from Coin stations	3

1010XXXX+	4

Service Access codes	4

Cut Through	4

Types of Calls	5

Alternate Billed Calls	5

Calling Cards	5

Automated Collect and Third Number Calling (ACTC)	5

Direct Distance Dialing (DDD)	5

Collect Calls	5

Person-to-Person	6

Station-to-Station	6

Sent-Paid	6

Third Number Billing	6

Restrictions/Limitations	6

Ordering	6

# Description

Dial 1 Plus permits end users to dial the digit '1' plus the desired telephone number when they are placing calls through their Interexchange Carrier's (IXC) network, hence the name 'Dial 1 Plus.'

## Aliases

- Equal Access

- PIC

- 1+

## Features

- Dial 1 Plus allows end users to place directly dialed calls through their Predesignated Interexchange Carrier (PIC) by dialing a '1' plus the telephone number.

- Dial 1 Plus also permits end users to place calls through an alternate IXC by using a '101XXXX' carrier access code. The code consists of the number '101' followed by a four-digit numeric code for the desired IXC.

- CLECs may designate a Dial 1 Plus IXC by submitting an order to the Local Service Center.

## Dialing Instructions

### Calls Originating from Non-Coin Stations

| If the End User Dials | Then the Call Will reach the |
| --- | --- |
| 1+10 digits (intraLATA) | ZPIC |
| 1+10 digits (interLATA) | PIC |
| 0+10 digits (intraLATA | SBC Midwest Operator |
| 0+10 digits (interLATA) | PIC |
| 0- | SBC Midwest operator |
| 00- | PIC |

#### 1010XXXX+

| If the End User Dials | Then the Call Will reach the |
| --- | --- |
| 1010XXXX + (1+) 7/10 digits (intraLATA) | 1010XXXX IC |
| 1010XXXX + (1+) 7/10 digits (interLATA) | 1010XXXX IC |
| 1010XXXX + 0+ 7/10 digits | 1010XXXX IC |
| 1010XXXX + 0- | 1010XXXX IC |

#### Service Access Codes

| If the End User Dials | Then the Call Will reach the |
| --- | --- |
| 1 + 700 + 7 digits | PIC |
| 101XXXX + 1 + 700 + 7 digits | 101XXXX IXC |
| 0 + 700 + 7 digits | PIC |
| 101XXXX + 0 + 700 + 7 digits | 101XXXX IXC |
| 1 + 800 + 7 digits | IXC or SBC, depending on NXX. |
| 101XXXX + 1 + 800 + 7 digits | an announcement |
| 0 + 800 + 7 digits | an announcement |
| 101XXXX + 0 + 800 + 7 digits | an announcement |
| 1 + 900 + 7 digits | IXC or SBC based on NXX |
| 0 + 900 + 7 digits | Reach an announcement. Note: If a carrier has ordered the 0+900 option, the call will be routed to the IXC based on the NXX. |
| 101XXXX + 1 + 900 + 7 digits | an announcement |
| 101XXXX + 0 + 900 + 7 digits | an announcement |

#### Cut –Through

| If the End User Dials | Then the Call Will reach the |
| --- | --- |
| 101XXXX + # | Reach the 101XXXX IXC if cut through requested. Announcement if cut through not requested. Note: Cut through is a term used when referring to the dialing pattern which, when used, routes the call directly to the IXC switch prior to dialing the NPA, NXX-line number, the call is |

#### Directory Assistance

| If the End User Dials | Then the Call Will reach the |
| --- | --- |
| 1 + 411 | Reach SBC Directory Assistance (if 411 is a valid code) |
| 1 + 555 + 1212 | Reach SBC Directory Assistance |
| 1 + NPA + 555 + 1212 | PIC |
| 101XXXX + 1 + NPA + 555-1212 | 101XXXX IXC |
| 0 + 411 | SBC operator (if 411 is a valid code) |
| 0 + 555-1212 | SBC operator |
| 0 + NPA + 555-1212 | PIC |
| 101XXXX + 0 + NPA + 555-1212 | 101XXXX IXC |

#### Vacant Codes

| If the End User Dials | Then the Call Will reach the |
| --- | --- |
| 1 + Vacant Code | Vacant Code Announcement |
| 101XXXX + 1 + Vacant Code | Vacant Code Announcement |
| 0 + Vacant Code | Vacant Code Announcement |
| 101XXXX + 0 + Vacant Code | Vacant Code Announcement |

### Calls originating from Coin stations

Coin stations include all coin classes of service except customer-owned coin.

| If the End User Dials | Then the Call Will reach the |
| --- | --- |
| 1 + 7/10 digits (intraLATA) | SBC Midwest |
| 1+ 7/10 digits (interLATA) | AT&T |
| 0+ 7/10 digits (intraLATA) | SBC Midwest operator |
| 0+ 7/10 digits (interLATA) | PIC |
| 0- | SBC Midwest operator |
| 00- | PIC |

#### 1010XXXX+

| If the End User Dials | Then the Call Will reach the |
| --- | --- |
| 1010XXXX+1+7/10 digits (intraLATA) | AT&T |
| 1010XXXX+1+7/10 digits (interLATA) | AT&T |
| 1010XXXX+0+7/10 digits (intraLATA) | 1010XXXX IXC |
| 1010XXXX+0+7/10 digits | 1010XXXX IXC |
| 1010XXXX+0- | 1010XXXX IXC |
| 01+CC+NN | PIC |
| 011+CC+NN | AT&T |

#### Service Access codes

| If the End User Dials | Then the Call Will reach the |
| --- | --- |
| 1+700+7 digits | AT&T |
| 1010XXXX+1+700+7 digits | AT&T |
| 0+700+7 digits | PIC |
| 1010XXXX+0+7/10 digits | 1010XXXX IXC |
| 1+800+7 digits | IXC or SBC Midwest based on NXX |
| 1010XXXX+1+800+7 digits | Announcement |
| 0+800+7 digits | Announcement |
| 1010XXXX+0+800+7 digits | Announcement |
| 1+900+7 digits | Announcement |
| 0+900+7 digits | Announcement |
| 1010XXXX+1+900+7 digits | Announcement |
| 1010XXXX+0+900+7 digits | Announcement |

#### Cut Through

| If the End User Dials | Then the Call Will reach the |
| --- | --- |
| 1010XXXX+ # | 1010XXXX IXC |
| 1+411 | SBC Midwest DA |
| 1+555+1212 | SBC Midwest DA |
| 1+NPA+555-1212 | AT&T |
| 1010XXXX+1+NPA+555-1212 | AT&T |
| 0+411 | SBC Midwest operator |
| 0+555-1212 | SBC Midwest operator |
| 0+NPA+555-1212 | PIC |
| 1010XXXX+0+NPA+555-1212 | 1010XXXX IXC |
| 1+Vacant code | Vacant code announcement |
| 0+Vacant code | Vacant code announcement |
| 1010XXXX+0+vacant code | Vacant code announcement |

## Types of Calls

### Alternate Billed Calls

- Calls not placed DDD or sentpaid

- Alternate billing arrangements include calling card, third number billing and collect calling.

- Callas are placed as:

  - 0+

  - Carrier access code

  - 1010XXXX+0

### Calling Cards

- Can be customer or operator-dialed in which calling card number is validated prior to completion of call.

- For Customer dialed calling card calls end user dials 0+ area code + telephone number and then enters calling card number when they hear mechanized tone.

- For Operator dialed calls, end user dials 0 and the call defaults to an operator who will then request calling card information to complete the call.

### Automated Collect and Third Number Calling (ACTC)

- Uses voice recognition to automate processing of collect the third number calls.

- Only applies to intralata toll calls handled by SBC Midwest operator services.

- In order to qualify for ACTC handling, it must meet the requirements of:

  - Be dialed from a touch-tone telephone

  - Be a 0+ call to a 7 or 10 digit number

  - Pass the LIDB check which checks for Toll Billing Exception

- Automated voice announces the end user’s call to the party being billed and they either accept or decline charge.

  - If declined, caller is notified their call cannot be completed.

### Direct Distance Dialing (DDD)

- Calls are placed by dialing 1+ area code + telephone number from the end user’s telephone.

- Billing begins when the called number is answered.

### Collect Calls

- Collect Calls are calls where billing is accepted at the called number.

- Collect calls are normally validated through LIDB to determine if called number has Toll Billing Exception.

### Person-to-Person

- Person-to-person calls are placed through an operator with the caller providing the name or extension they wish to reach.

- End users are billed once the requested party is reached.

- All types of operator assisted calls can be placed as person-to-person calls.

### Station-to-Station

- Calls are placed as station-to-station if the caller is willing to speak with anyone who answers.

- Billing begins when the called number answers.

- All DDD calls are station-to-station

- Operator-assisted calls can be station-to-station

### Sent-Paid

- Sent paid calls are calls billed to the originating number.

- Can be DDD or operator-assisted

- All DDD calls are sent-paid

### Third Number Billing

- Third number Billing is a call billed to a number other than the originating or called number.

- Third number billing normally is validated through LIDB to determine if billed to  number has Toll Billing Exception.

# Restrictions/Limitations

- An IXC must establish Equal Access (Feature Group D) with SBC before offering Dial 1 Plus Service to their customers.

# Ordering

- The end user's IXC will be able to request removal of PICC billing due to non-payment, thereby changing the PIC to 'NONE', even if the CLEC has made an agreement with the LSC that PIC changes can only be initiated by the CLEC.

- If the CLEC would like to be notified when PIC/LPIC is changed for their end users, please contact your account manager to request an 836 PIC/LPIC electronic notification.

Use the following codes for end users who do not select a PIC:

| Code | Description |
| --- | --- |
| UNDC | End user is undecided on a primary IXC selection (1+ dialing blocked). |
| NONE | End user chooses not to select a primary IXC (1+ dialing blocked). |