Dark Fiber

Overview	2

Service Description	2

Unbundled Dark Fiber (UDF) Transport	2

Availability	2

Spare Fiber Inventory Availability	2

Limitations	3

Maintenance Spares	3

Revocations	3

Ordering Requirements	4

Dark Fiber Inquiry Requirements	4

Due Date Intervals for Dark Fiber Inquiries (per ASR)	4

Dark Fiber Ordering Requirements	4

Common Language Circuit ID (CLCI), Network Channel (NC), Network Channel Interface (NCI), and SPEC codes	5

Dark Fiber Interoffice	5

Dark Fiber USOC Codes	5

# Overview

AT&T is no longer obligated to provide Unbundled Dark Fiber Local Loop.

Unbundled Dark Fiber (UDF) Transport is offered as a point-to-point arrangement between AT&T Wire Centers.  UDF Transport is spare optical fiber and is offered without optical signal regeneration to compensate for signal losses.  This arrangement consists of four optical fibers and fiber terminating equipment.

# Service Description

UDF Transport is spare fiber that has not been activated through connection to the electronics that 'light it', and thereby rendering it capable of carrying communications services (FCC UNE Remand Paragraph 174).

UDF Transport is a segment between two Central Offices. Spare fibers do not include maintenance spares, fibers set aside and documented for forecasted growth by AT&T, defective fibers, nor fibers subscribed to by other carriers.

AT&T will calculate maintenance spares by segment. No CLEC can obtain any more than 25% of the spare Dark Fiber contained in the segment. Before fibers are ordered, AT&T must have an executed Interconnection Agreement with the CLEC providing for UDF Transport and must be physically collocated prior to obtaining UDF Transport.  AT&T is not required to place the fiber for UDF if none is available.

# Unbundled Dark Fiber (UDF) Transport

AT&T will allow CLECs to order and interconnect single-mode UDF Transport between originating and terminating serving wire centers, which may include multiple interoffice segments if the fibers are spliced through in all segments and terminated in approved fiber cross connect or optical splitter hardware. All fiber terminating panels and splitters may be, but are not required to be, located in the same Fiber Distribution Frame (FDF).

## Availability

For UDF Transport availability, please refer to the Unbundled Dedicated Transport Availability - Wire Center Tiers.

https://clec.att.com/clec/hb/shell.cfm?section=2410&hb=1151

## Spare Fiber Inventory Availability

All available spare Dark Fiber will be offered 'as is' (without conditioning). Spare Dark Fiber is fiber that is spliced in all segments, point-to-point but not assigned. Spare fibers do not include maintenance spares, fibers set aside and documented for 12 month forecasted growth by AT&T, defective fibers, or fibers subscribed to by other carriers. No CLEC can request more than 25% of the spare Dark Fiber contained in the segment.

# Limitations

## Maintenance Spares

- Defective fibers will be subtracted from inventory of spare fibers.

- AT&T growth fibers are fibers documented as reserved by AT&T for utilization for growth within 12 months of the carrier's request.

- Maintenance spare fibers are considered unavailable for assignment and are determined based on the number of fibers in a cable sheath as follows:

| Fiber Cable Size | No. of Maintenance Spares |
| --- | --- |
| 24 Fiber and Less | 2 |
| 36 & 48 Fiber | 4 |
| 72 & 96 Fiber | 8 |
| 144 Fiber | 12 |
| 216 Fiber | 18 |
| 288 Fiber | 24 |
| 432 Fiber | 36 |
| 864 Fiber | 72 |

## Revocations

Should CLECs not use the leased fiber strands within the 12-month period from date of lease, AT&T reserves the right to regain those fiber facilities in AT&T inventory. AT&T reserves the right upon demonstration to revoke the lease of UDF Transport facility after the 12-month interval if fiber is not being used.

AT&T can also revoke CLECs' right to use the UDF Transport upon twelve (12) months' written notice. To exercise this right of revocation, AT&T must demonstrate that the UDF Transport is needed to meet it’s bandwidth requirements within the next 12 months.

# Ordering Requirements

## Dark Fiber Inquiry Requirements

CLECs order UDF Transport on a strand-by-strand basis and may request a single strand or multiple strands for each point-to-point arrangement.  Therefore, the appropriate CFA must accompany each dark fiber circuit

CLECs will submit Dark Fiber facility inquiry, giving their specific point to point (A to Z) Dark Fiber requirements. If the Dark Fiber is available, CLECs may place Access Service Request (ASR) for ordering. In order to secure Dark Fiber, CLECs must place ASR request for available Dark Fiber. Dark Fiber will be assigned to CLECs when an ASR is processed. Inquiry facility checks do not reserve Dark Fiber.  In order to secure UDF Transport, CLECs must place a firm order.

When CLECs submit a Dark Fiber inquiry, appropriate rates for the inquiry will be charged.  CLEC inquiries will be billed one non-recurring charge per CLEC request (ASR), not per service order and not per strand.  The inquiry process only determines fiber availability at that time.

Important: The CLEC must have an effective interconnection agreement which includes terms, conditions and rates prior to ordering UDF Transport. Prior to ordering UDF Transport, CLECs must establish Collocation (using the collocation process).

## Due Date Intervals for Dark Fiber Inquiries (per ASR)

| Dark Fiber | 1-10 ASRs | 11-20 ASRs | 21+ASRs |
| --- | --- | --- | --- |
| Dark Fiber Inquiry per ASR | 5 days | 10 days | ICB |

Intervals specified are business days and are applicable UDF Transport. Each ASR should only address a single segment (A to Z), but may include multiple strands.

Note: Due Date Intervals for Firm Orders are 20 business days.

AT&T will evaluate the requests based on existing plant location records and internal tracking systems. The Local Service Center (LSC) will provide the results to the CLEC including the approved number of fiber strands. Inquiry facility checks do not reserve UDF Transport. Results from the inquiry process reflect a snap-shot in time.

## Dark Fiber Ordering Requirements

CLECs must issue a complete and accurate ASR requesting a firm order for UDF Transport.

## Common Language Circuit ID (CLCI), Network Channel (NC), Network Channel Interface (NCI), and SPEC codes

### Dark Fiber Interoffice

| CLCI | TXXU |
| --- | --- |
| NC | LX-- |
| CO NCI | 01QBF.LLX |
| CO NCI | 01QBF.LLX |
| SPEC | UNBDT |

Order example for Dark Fiber inquiry:

## Dark Fiber USOC Codes

| USOC | Description |
| --- | --- |
| UBNTX | Interoffice, Class of Service |
| ULYCX | Interoffice, per strand |
| ULNCF | Interoffice, per foot |
| UKCJX | Interoffice, Cross Connect |
| NR9D6 | Interoffice, Inquiry |
| ULNCH | Interoffice (IOF), per 1,000 ft. |

Important: The CLEC must have the above USOCs codes in their interconnection agreement pricing schedule prior to ordering UDF Transport.