| STEP | ORDER PROCESS DESCRIPTION: |
| --- | --- |
| 1 | CLEC submits order following valid subscription completion (see subscription process). Qualifying orders consist of CHC and FDT LNP with Loop Reuse (LSNP) and a valid “DFDT” entry. |
| 2 | AIT LSC issues AIT internal service order(s). |
| 3 | AIT system auto-validates order information against systems tables and populates order with DD-2 DT/ANI Test USOC. In order for positive validation to occur: Order ACNA must match ACNA for a subscribed CLEC Order must be for CHC or FDT LNP with Loop Reuse (LSNP) Order must have “DFDT” entry |
| 4 | Ameritech provisioning systems assign work step for the central office technician to perform DD-2 test |
| 5 | On DD-2, the central office technician completes the DD-2 test confirming DT/ANI information available. DT/ANI testing will always be performed at the CLEC CFA prior to connection to Ameritech’s jumper. Whenever possible, DT/ANI testing will also be performed through to the Ameritech advanced jumper. |
| 6 | DD-2 test results are posted on the LOC provisioning web site throughout the day on DD-2 and no later than 10 am, CST, DD-1. The three possible test results are: Tested OK Incorrect ANI No Dial Tone |
| 7 | CLEC may check for updates throughout DD-2 and until 10 am CST, DD-1. If test results are not posted by 10 am, CST, DD-1, CLEC should follow step 7.1 to obtain results. |
| 7.1 | No – CLEC contacts LOC for resolution. CLEC is responsible for comparing responses on orders from their cut sheet, to orders displayed on the web. If an “LSC” notation is indicated on the Cut Sheet, DT/ANI results may be posted as late as Due Date. |
| 8 | YES – Were the test results successful (i.e. DT and correct ANI validated)? |
| 8.1 | NO – Either NDT (No Dial Tone) or Wrong ANI were found. CLEC should check translation provisioning & CFA Assignment/wiring. If CLEC finds a problem with their translations or CFA, corrective action should be taken. |
| 8.2 | Upon completion of corrective action or If CLEC does not find a problem they may: request an optional DT/ANI test request an escort ticket wait until the DT/ANI test on DD (step 9) |
| 9 | End – Dial Tone ANI Test will be performed as normal for FDT or CHC orders on Due Date and order will follow applicable FDT or CHC process for completion. |