###### SBC

Ameritech

Nevada Bell

Pacific Bell

Southern New England Telecommunications

Southwestern Bell Telephone (Excluding Texas)

Technical Publication

## TP 76841

Unbundled Dedicated Transport (OC-n)

Performance and Interface Specifications

# Issue 2

November 2000

TECHNICAL REFERENCE NOTICE

This document does not apply to the State of Texas.  For Texas, see document “TP 76841 TX”.  References to documents herein are to documents current as of the date this TP is approved.

In this document SBC means the SBC Local Exchange Carriers; Ameritech, Nevada Bell, Pacific Bell, Southern New England Telephone, and Southwestern Bell Telephone (excluding the State of Texas).

This technical document is published by SBC to provide Competitive Local Exchange Carriers (CLECs) with technical specifications for interconnecting to the SBC network.  SBC reserves the right to revise this document, subject to the approval of the Public Utilities Commission (PUC), for any reason including, but not limited to, conformity with standards promulgated by various regulatory or other agencies, use of advances in the state of the technical arts, or the reflection of changes in the design of any equipment, techniques or procedures described or referred to herein.

SBC makeS no representation or warranty, expressd or implied, with respect to the sufficiency, accuracy, or utility of any information or opinion contained herein.  SBC expressly advise that any use or reliance upon this technical reference is at the risk of the user and that neither SBC or their affiliates, directors, officers, employees, or other authorized representatives SHALL BE liable for any damage or injury incurred by any person arising out of the sufficiency, accuracy, or utility of any information or opinion contained herein.

This document is not to be construed as a suggestion to any equipment manufacturer to modify or change any of its products, nor does this document represent any offer or commitment by SBC or any affiliate thereof to purchase any product, whether or not it provides or meets the described characteristics.

SBC does not recommend products or services, and nothing contained herein is intended or should be construed as a recommendation or an endorsement of any product, service, vendor, or manufacturer to anyone.

Nothing contained herein shall be construed as conferring by implication, estoppel, or otherwise any license or right under any patent, whether or not the use of any information herein necessarily employs an invention of any existing or later issued patent.

SBC reserves the right not to offer any or all of these services and to withdraw any or all of them at any future time, subject to Federal and State orders, regulations and approval.

With respect to services offered pursuant to tariff, however, the terms and conditions of the service offering are determined by the tariff itself, applicable laws and regulations, and contractual agreements.

To the extent that any provision of this technical publication is inconsistent with the Interconnection Agreement between SBC and a Competitive Local Exchange Carrier, the terms of the Interconnection Agreement shall control.

#### SBC CONTACTS

To obtain additional copies of this document, contact; SBC at 210-886-1192, or log onto https://clec.sbc.com.

For questions concerning this document, contact;

Mel Smith

Area Manager – Network Planning & Engineering

214-858-0810

Revision History

Issue 2, November 2000:

- Added the following to page 6; “With UDT OC-n, the CLEC will get an OC-3  mapped as

3 STS-1s, or an OC-12 mapped as 12 STS-1s.   OC-3 service must be assigned to three

contiguous channels starting at channels - 1, 4, 7, 10 on OC-12 transport systems,  and channels

1, 4, 7, 10, 13, etc. on OC-48 transport systems. OC-12  must be assigned to 12 contiguous

channels starting at channels - 1 or 13, on OC-48 transport systems”.

2.   Added the following to page 6;“When UDT OC-12 is ordered without the multiplexing

option, OC-3c transport over the UDT OC-12 is not supported”.

- Removed  the following from page 6; “In addition, multiplexing options will be offered allowing CLECs  to combine lower speed electrical and optical services onto UDT OC-n transport.  Multiplexing will not be offered as a separate unbundled network element, however multiplexing may be obtained using the BFR process”.

Table of Contents

Page

1.0	General Description							6

2.0	Technical Parameters							9

1.0	General Description:

Unbundled Dedicated Transport (UDT) at SONET Optical Carrier Rates (OC-n) provides unbundled optical fiber-based full duplex point-to-point transmission capabilities to CLECs based on Synchronous Optical Network (SONET) standards approved by the International Telecommunication Union - Telecommunication Standardization Sector (ITU-TSS, formerly CCITT) and the American National Standards Institute (ANSI).

SBC will provide UDT OC-n on an interoffice transport basis between two SBC serving wire centers, or as an entrance facility between the CLEC's point of presence (POP) and the SBC serving wire center.   With entrance facility UDT OC-n, SBC will install and own the SONET ADM, DSX, optical cross-connect device, and 90/10 splitter at the CLEC’s POP.

All UDT OC-n transport interconnections between SBC and the CLEC will be 2 fibers (transmit and receive).  Additional protection required by the CLEC must be ordered as a separate UDT OC-n.

UDT OC-n will be offered as a UNE in the following optical line rates.

OC-3/OC-3c	  	(155.52 Mb/s)
	OC-12/OC12c		 (622.08 Mb/s)

With UDT OC-n, the CLEC will get an OC-3  mapped as 3 STS-1s, or an OC-12 mapped as 12 STS-1s.

OC-3 UDT must be assigned to three contiguous channels starting at channels - 1, 4, 7, 10 on OC-12 transport systems,  and channels 1, 4, 7, 10, 13, etc. on OC-48 transport systems.  OC-12 UDT must be assigned to 12 contiguous channels starting at channels - 1 or 13,  etc. on OC-48 transport systems.

Multiplexing options will be provided as follows:

| High-Speed UDT OC-n | Low-Speed Drop (Multiplexing Options) | Order Quantity |
| --- | --- | --- |
| OC-3 | DS1 | 1-84 DS1s in groups of 28 DS1s |
| OC-3 | DS3 | 1-3 DS3 |
| OC-12 | DS3 | 1-12 DS3 |
| OC-12 | OC-3 | 1-4 OC-3 |
| OC-12 | OC-3c | 1-4 OC-3c |

When UDT OC-12 is ordered without the multiplexing option, OC-3c transport over the UDT  OC-12 is not supported.

FDF:  Fiber Distribution Frame or equivalent optical cross-connect device

FDF:  Fiber Distribution Frame or equivalent optical cross-connect device

The SONET ADM, FDF (or equivalent device), DSX, and 90/10 splitter at the CLEC’s POP are SBC owned.

2.0	Technical Parameters:

This section provides technical parameters and references associated with UDT OC-n SONET transport.

| UDT OC-n Technical Parameter | Specification |
| --- | --- |
| Optical Interface Type 90/10 Optical Splitter | SC or ST Optical Connector |
| Optical Wavelength | 1310 or 1550 nanometers |
| Performance Objectives: DS3 % Availability per year Errored Seconds Per Day One Hour Test Limit | 99.950 % 432 (mean value over 30 or more days) <= 5 Errored Seconds, 0 Severely Errored Seconds Telcordia GR-342-CORE |
| Performance Objectives: DS1 % Availability Per Year Errored Seconds Per Day 15 Minute Test | 99.925 % 216 (mean value over 30 days or more) 0 Errored Seconds, 0 Severely Errored Seconds Telcordia GR-342-CORE |
| Performance Objectives: SONET OC-3 (End-To-End) % Availability Per Year 1 Hour Test | 99.83 % Errored Seconds <= 12 Severely Errored Seconds = 0 ANSI T1.514 |
| Performance Objectives: SONET OC-12 (End-To-End) % Availability Per Year 1 Hour Test | 99.83 % Severely Errored Seconds = 0 ANSI T1.514 |

# Text boxes

FDF

FDF

SONET ADM

DSX

DSX

SONET ADM

Collocation Arrangement

90/10 Splitter

SBC Wire Center

SONET ADM

Collocation Arrangement

CLEC’s POP

DSX

90/10 Splitter

SBC Wire Center

SBC Wire Center

Cross-Connect Element

Cross-Connect Element

Interoffice

SONET

Transport

Figure 1

UDT OC-n Interoffice

SONET ADM

DSX

Collocation Arrangement

FDF

FDF

90/10 Splitter

90/10 Splitter

Entrance  Facility

SONET

Transport

Cross-Connect Element

CLEC Owned Interconnect Cable

Figure 2

UDT OC-n Entrance Facility