TIKI REPORT FIELD DESCRIPTIONS AND DEFINITIONS

The heading of the report identifies the date it was pulled, the ACNA of the CLEC and the study period covered by the report.

Study Date

Date the monthly data was pulled from.

RESP

AT&T Trunk Servicer/Forecaster responsibility code.

ACNA

The ACNA the CLEC uses when ordering local interconnection trunking.

AC TANDEM

Access homing tandem.

LOC_A

The location "A" end of the trunk group.  This is the originating end of the trunk group

for a one-way trunk group and the lowest alphabetical office for a two-way group.

State_loc_a

State where Loc_A resides.

PLSG

Pulsing is a 2-character field located between the "A" location and the "Z"

location.  It describes the signals used to direct a call to its destinations.

Supervisory, trunk conditioning and automatic number identification

signals are excluded.  The first character represents the type of signal

outgoing from A to Z location.  The second character represents the type

of signal outgoing from the Z to A location.

Typical entries are:

M- or 7-   	This means this is a one-way trunk group.  It uses

multi-frequency or SS7 Signaling trunks from the "A" end to

the "Z" end and is not arranged for two-way operation.

MM or 77	Means the trunk group is, or has the capability to be,

arranged for two-way operation.  It uses multi-frequency or

SS7 Signaling trunks.

LOC_Z

The location Z end of the trunk group.  This is the terminating end of the

trunk group for a one-way trunk group and the highest alphabetical office

for a two-way group.

State_loc_z

State where Loc_Z resides.

TTD	TRAFFIC TYPE DESCRIPTION

This 13-character field is composed of Traffic Class, Office Class, Traffic

Use, and Modifier that are described below.

TRAFFIC CLASS

Commonly used entries are:

AF - DF - IF

These codes identify the trunk groups as "Final" trunk 				                       groups.  When all circuits are busy in a final trunk group,

a call offered to the trunk group will be blocked.  These calls

will receive an overflow tone from an end-office (120 IPM)

or an announcement from a tandem.

PH - IH

These codes identify the trunk groups as "High

Usage" trunk groups.  When all circuits are busy in a

high usage trunk group, a call offered to the trunk

group will be "overflowed" (alternate-routed) to

another trunk group, usually a final, through which

they can reach their destination.

OFFICE CLASS

This consists of a two-character code.  The first character is the "A"

location's office class, and the second character is the "Z" location's  office class.

TRAFFIC USE

This field is a two-character code identifying the type of traffic offered to a trunk group.  Listed below are some commonly used traffic use codes. (See the ASOG (Access Service Ordering Guidelines) for the complete list of industry standard traffic use codes.)

DD	Tandem Access - LAMA

DT	Tandem Connecting - LAMA

MD	Tandem Access - mixed Feature Group D

TC	Tandem Completing - Toll

TE	Interend Office - Toll

MODIFIER

The modifier is an optional variable length from 1-7 character alphanumeric code.

Positions 1-3 of the modifier are used to provide supplementary information in the

identification of message trunk groups.  Position 4 of the modifier will always reflect a

"J" to identify a CLEC interconnection trunk group.  Position 5-7 of the modifier contains

the ACNA of the company that has ASR issuance control for the trunk group.

TGSN

This is the Trunk Group Serial Number associated with this trunk group for data collection, forecasting and servicing.

CKT ID

This column is intentionally left black on the report.  It is provided as a place for the

CLEC to identify their trunk group name that is reflected in their databases.

DSN BLKG

Designed Blocking: AT&T uses Design Blocking to evaluate the number of trunks

required for a Final trunk group.  An average blocking ratio is used to engineer and

service the trunk groups.

BSY HR   BUSY HOUR

This is the time consistent hour during the study period that experienced the highest load.  It is in 24-hout time.  For example:

10 = 10:00 AM to 11:00 AM

19 = 7:00 PM to 8:00 PM

BLKG_pct

This is the percent overflow (percent of alternate-routed calls) for high usage trunk

groups, and the percent blocking on final trunk groups for this study period.

TRKS IN SVC

This is the number of Trunks In Service (in-effect) in each trunk group for the study

period.

TRKS REQD

This is the number of trunks required to satisfy the grade of service indicated by the

probability of blocking or the ECCS on the trunk group.  It is based on the traffic load

during the study period and the design criteria as calculated by the AT&T servicing

system.

NO DATA THIS STDY

An asterisk (*) will appear in this column if a trunk which is "in service" receives no data

through the servicing system.  When this happens, the following fields contain blanks or

zeros:

ECCS/DSN BLKG

%OFL OR %BLKG

TRKS REQD

The appearance of the asterisk (*) indicates that no data was collected during the data

collection period.  The level of blocking or overflow, and the number of trunks required

are unknown because of the condition.  AT&T will investigate the cause of a no data

condition.  A "no data" condition can be caused by the following:

Data not processed in downstream systems due to mechanical failure.

Data collection not available for specific trunk groups.

Data collection process not initiated by AT&T.