# Wireless Local Number Portability (WLNP)

## Content of this document was originally in the LOH Section 3 Ordering, General Local Service Ordering Information

Description:

Wireless Local Number Portability allows functionality and service whereby working telephone numbers may be ported; (i.e.: Wireless carrier to wire-line carrier (w – wl)) Wire-line carrier to wireless carrier (wl – w), Wireless carrier to wireless carrier (w – w). AT&T Southeast Region will port to and from wireless carriers per industry defined porting processes currently used for wireline to wireline porting.

Definitions:

Wire-Line - Any service connected to a LAN Line apparatus

Wireless - Any service connected to a wireless CMRS, Paging arrangement or wireless

apparatus.

CMRS-Commercial Mobile Radio Service (“CMRS”):  A mobile service that is: (a) (1) provided for profit, i.e., with the intent of receiving compensation or monetary gain; (2) an interconnected service; and (3) available to the public, or to such classes of eligible users as to be effectively available to a substantial portion of the public.

- PSTN = Public Switching Telephone Network

- LERG = Local Exchange Routing Guide

- AT&T-SE = AT&T Southeast Region

- NPAC = Number Portability Administration Center

- WSP = Wireless Service Provider

- WAM = Wireless Account Manager

- LSM = Local Service Manager

- TMRC = Toll Message Rate Center

- Network Service Provider = Provider where service is physically provisioned

Wireless Porting Service Arrangements:

AT&T Southeast Region allows wireless number porting for the following wireless interconnection service type arrangements.

Type 2 Interconnection

Type 1 Interconnection

Shared Type 1

Dedicated Type 1

Type 2 Interconnection: A trunk connection between the wireless carrier switch and a AT&T-SE access tandem switch (Type 2A) or AT&T-SE end office switch (Type 2B) that supports traffic between the wireless carrier switch and the PSTN. In theory type 2 interconnection is similar to facility base services where the telephone number resides in a switch other than AT&T Southeast Region.

Type 2 wireless numbers reside in the wireless carrier switch. All traffic associated with Type 2 wireless numbers routes to/from wireless carrier switch via either type 2 A or type 2 B trunk groups.

NPA NXXs associated with type 2 interconnection are assigned to the wireless carrier.  The wireless carrier is shown as the code holder in the LERG.

Porting of type 2 wireless numbers will occur in a manner similar to wireline CLEC ports. AT&T Southeast Region involvement in type 2 porting occurs only when AT&T-SE receives an LSR to port a AT&T-SE or CLEC Resale WLP wireline number to a wireless Type 2 carrier or when a customer request is received to port in a wireless telephone number as a Resale WLP wireline service (i.e.: REQTYP E Resale or REQTYP M WLP).

Port In from a wireless Type 2 to AT&T Southeast Region for (Resale or WLP)- If AT&T-SE submits an LSR to a wireless provider for WLNP to Resale/WLP (wireless provider is a Type 2 provider)-- [TN Ownership shows number belonging to the wireless provider], where we send an LSR to the losing wireless provider, an NPDI may be requested by the wireless provider. If that occurs, an NPDI of B should be used.

Type 1 Interconnection-A trunk connection between the wireless carrier switch and a AT&T Southeast Region end office switch which supports traffic between the wireless carrier switch and the PSTN. In theory type 1 interconnection is similar to resale service where the telephone number resides in a AT&T-SE switch.

Type 1 wireless numbers reside in the AT&T-SE end office and are assigned to the Type 1 trunk group 1. All traffic terminating to Type 1 wireless numbers routes to the AT&T-SE Type 1 trunk group in a fashion similar to DID calls.

Type 1 numbers are assigned to the wireless carrier via AT&T-SE tariff guidelines at the number block level (e.g., 20s 100s or 1000s)

NPA NXXs associated with type 1 interconnection are assigned to AT&T-SE and shown as the code holder in the LERG

A request to port a type 1 wireless number from one wireless carrier to another will trigger an LSR from the recipient wireless carrier to AT&T-SE requesting a port out of the type 1 wireless number

WLNP Type 1 porting activity is porting out of AT&T-SE’s network into another carrier’s network.

Shared Type 1- A code of numbers owned by AT&T Southeast Region E in the LERG, which AT&T-SE allows TN assignment to AT&T-SE customers and Resale WLP or wireless providers.

AT&T-SE is listed as the code owner in the LERG for shared type 1 numbers.

Dedicated Type 1- A code of numbers owned by AT&T Southeast Region in the NPAC.    However, the WSP is shown as owner in the LERG.

AT&T-SE is responsible for the porting activity even though not listed as the code owner in the LERG.

The CLEC/Wireless provider must perform TN ownership validation in NPAC to determine which provider should receive the LSR request.

AT&T Southeast Region offers a Preorder CSR query that will identify when a telephone number (TN) is entered, the query will identify that the TN is a part of a Wireless Type 1 account where AT&T-SE is the Network Service Provider. Other useful information found in the query will assist a Provider in populating some fields on the LSR: wireless main account number (to populate the EATN field, billing name and address (to populate the EU [end user] fields).

A port out of a Type 1 number to a Facility Based CLEC should be processed as a normal Type 1 port out without an NPDI being populated.

Port In to a Wireless Type 1 Provider

When a Wireless Type 1 Provider is requesting a Port In of a telephone number from a Wireless Type 2 provider or a Facility Based CLEC, they must submit a a 22-state AT&T Manual LSR forms (by Email) to the LSC-Local Service Center.

The ATN field must be populated with the Wireless Type 1 Providers 10 digit account number where the Port In number will migrate to. The ATN is a dialable telephone number

The NPDI field must reflect an A (if a wireless to wireless port) or C (if CLEC to Wireless Port)

The PORTED NBR field must be populated with the number(s) to be ported

EATN must not be populated

All other required fields must be populated. If these conditions are not met, the LSR will be returned to the provider.

Type 1 Wireless Ports and Project Management:

Because Type 1 Wireless service does not carry a 10 digit trigger (prepares TN to port), once the number ports, the disconnect service order must be coordinated by project management to remove the TN from the AT&T Southeast Region central office switch, therefore below procedures will be needed to accommodate this process:

All Service Providers must do Pre-Order CSR query to determine if porting Type 1

Wireless service.

If Porting 50 numbers or less, the Service Provider should assign:

A 7 business day interval (see SE Standard Interval Guide - Number Portability section) for Due Date Intervals

A Project ID will be assigned by AT&T Southeast Region and project management will be provided

If Porting over 50 numbers, the Service Provider will:

Contact the Local Project Management upfront, to negotiate a Project ID and Due Date prior to submitting the LSR to the LSC.

If NO Project ID is populated the LSR will be Clarified.

Project Manager will monitor all Type 1Wireless DID Ports (BAU for DID Ports).

Pre-Order:

The AT&T Southeast Region requires accurate information to process the LSR and produce an error free service order. The CLEC/WSP should always obtain a copy of a parsed/unparsed CSR for Type 1 request prior to submitting an LSR to AT&T-SE the CSR provides the following information:

TN

Service Address (SA)

Listed Name (LN)

Current Billing Name information

LOC (Returned when on existing CSR)

DZIP (Returned when on existing CSR)

Message=Type 1 account (when the existing account is a Type 1)

Note 1:  The WSP should contact their appropriate WAM for questions regarding how the CSR information translates to fields on LSR.

Note 2:  The CLEC should contact their appropriate LSM for questions regarding how the CSR information translates fields on the LSR.

E911 and Wireless LNP

When a wireline telephone number transfers to a wireless service, the E911 parser shall delete the record instead of unlocking, this will cause the E911 TN database to reflect that the TN is no longer a wireline service.

E911 wireless dynamic update logic must accommodate a 911 call from a wireless handset using the same telephone number as the old wireline account until the old service provider record is removed from the E911 database.

Product Restrictions and Limitations:

Directory Delivery is not applicable for WLNP

If the WSP is ordering/requesting Foreign Listings associated with WLNP, they must submit a manual LSR for processing

A wireless directory number may be ported to a wireline service provider as long as the resulting wireline serving address is geographically located within the wireline rate center (TMRC) associated with the wireless directory number (NPA NXX)

Porting from a wireless carrier to AT&T Southeast Region is limited to ports within existing TMRC as defined in the LERG (EXCEPTION: When porting from wireline to wireless Type 2 the TMRC will not be validated).

Wireless screening account TNs or Guide Numbers are not eligible to be ported.

Wireless Service Request (WSR) forms are not valid when submitting a request to the LSC. (WSR’s should be submitted to the AT&T-SE Wireless Service Center)

Existing LNP TN disconnect and TN reclaim industry procedures are applicable to WLNP and are found in the NPAC website (http://npac.com/)

Wireline to Wireless-An LSR request from a wireless service provider to port out a AT&T-SE wireline number authorizes AT&T-SE to disconnect a wireline number (BST, Reseller or WLP)

Wireless to Wireline- a request from a wireless end user customer to port into AT&T-SE as a wireline number authorizes AT&T-SE to disconnect the port-in number from the donor wireless carriers account

Wireless to wireline Port in-A request from a wireless end user customer to port into AT&T-SE as a wireline number authorizes AT&T-SE to establish a wireline account for the port in number (AT&T-SE, Reseller or WLP)

Service Order Restrictions:

None

Tariff Reference:

None

USOC / FID References:

None

Situations / Exhibits:

None

Related Topics / Information:

None